## Slide 1
Module 1
BJT AC Models and Voltage Amplifiers
9 teaching hours
• Base biased amplifier
• Emitter biased amplifier
• Small signal operation
• AC beta
• AC resistance of the emitter diode
• Two-transistor models
• Analyzing amplifier
• Voltage amplifiers
VCC
RC
BJT
RE
Vin
Vout
Bias sets Q point; AC signal rides on it
VTU 1BEC304 • Module 1 • 01/50
Notes: [Animation]
Use this slide as a section reset. Reveal syllabus cluster first, then the big visual.
[Sources]
- Official VTU 2025 scheme syllabus PDF for 1BEC304.
- Local syllabus images supplied in public/Analog Electronics and Linear Integrated Circuits/.
- Local textbook PDFs supplied in public/Analog Electronics and Linear Integrated Circuits/.

## Slide 2
COVERED / MISSING = 0
Module 1 syllabus audit
VTU syllabus topic
Coverage
Status
1. Base biased amplifier
Syllabus + textbook support
COVERED
2. Emitter biased amplifier
Syllabus + textbook support
COVERED
3. Small signal operation
Syllabus + textbook support
COVERED
4. AC beta
Syllabus + textbook support
COVERED
5. AC resistance of the emitter diode
Syllabus + textbook support
COVERED
6. Two-transistor models
Syllabus + textbook support
COVERED
7. Analyzing amplifier
Syllabus + textbook support
COVERED
8. Voltage amplifiers
Syllabus + textbook support
COVERED
9. Voltage gain
Syllabus + textbook support
COVERED
10. Multistage amplifiers
Syllabus + textbook support
COVERED
11. CC amplifier
Syllabus + textbook support
COVERED
12. Output impedance
Syllabus + textbook support
COVERED
13. Cascading CE and CC
Syllabus + textbook support
COVERED
14. Darlington connections
Syllabus + textbook support
COVERED
15. Voltage regulation
Syllabus + textbook support
COVERED
16. Common-base amplifier
Syllabus + textbook support
COVERED
Final status: no missing topics
VTU 1BEC304 • Module 1 • 02/50
Notes: [Animation]
This is the internal cross-check slide. Reveal final status only after all rows are discussed.
[Sources]
- Official VTU 2025 scheme syllabus PDF for 1BEC304.
- Local syllabus images supplied in public/Analog Electronics and Linear Integrated Circuits/.
- Local textbook PDFs supplied in public/Analog Electronics and Linear Integrated Circuits/.

## Slide 3
Teaching sequence
Roadmap for Module 1
1. Base biased amplifier
2. Emitter biased amplifier
3. Small signal operation
4. AC beta and emitter diode resistance
5. Two-transistor models
6. Voltage amplifiers
7. Multistage amplifiers
8. CC amplifier and output impedance
9. Darlington and voltage regulation
10. Common-base amplifier
Each topic becomes: concept -> circuit -> analysis -> example
VTU 1BEC304 • Module 1 • 03/50
Notes: [Animation]
Reveal the roadmap row by row. Use it to set expectations for problem-solving and diagrams.
[Sources]
- Official VTU 2025 scheme syllabus PDF for 1BEC304.
- Local syllabus images supplied in public/Analog Electronics and Linear Integrated Circuits/.
- Local textbook PDFs supplied in public/Analog Electronics and Linear Integrated Circuits/.

## Slide 4
Exam quick reference
Module 1 formula and design checkpoints
1
Av roughly -RC / re prime
core
2
Zin depends on bias network and beta re
core
3
Overall gain = product of loaded stage gains
check
4
Emitter follower Av nearly 1
check
VTU 1BEC304 • Module 1 • 04/50
Notes: [Animation]
Reveal formulas one at a time. Ask students to name the assumptions behind each checkpoint.
[Sources]
- Official VTU 2025 scheme syllabus PDF for 1BEC304.
- Local syllabus images supplied in public/Analog Electronics and Linear Integrated Circuits/.
- Local textbook PDFs supplied in public/Analog Electronics and Linear Integrated Circuits/.

## Slide 5
Module 1 / BJT AC Models and Voltage Amplifiers
Base biased amplifier: core idea
Base bias fixes operating point so the BJT can amplify small AC variations.
• bias path
• Q point
• AC signal
• coupling capacitor
Takeaway
Bias must keep the transistor in active region.
VCC
RC
BJT
RE
Vin
Vout
Bias sets Q point; AC signal rides on it
VTU 1BEC304 • Module 1 • 05/50
Notes: [Animation]
Start from the names: each term tells what the circuit controls.
[Sources]
- Official VTU 2025 scheme syllabus PDF for 1BEC304.
- Local syllabus images supplied in public/Analog Electronics and Linear Integrated Circuits/.
- Local textbook PDFs supplied in public/Analog Electronics and Linear Integrated Circuits/.

## Slide 6
Module 1 / BJT AC Models and Voltage Amplifiers
Base biased amplifier: circuit working
Follow the signal path and ask what each device or network contributes.
• Identify input and output nodes
• Mark DC bias and AC signal path
• Track phase, gain, impedance, or threshold
• Connect the result to the application
Takeaway
Bias must keep the transistor in active region.
VCC
RC
BJT
RE
Vin
Vout
Bias sets Q point; AC signal rides on it
VTU 1BEC304 • Module 1 • 06/50
Notes: [Animation]
Reveal the circuit blocks left to right.
[Sources]
- Official VTU 2025 scheme syllabus PDF for 1BEC304.
- Local syllabus images supplied in public/Analog Electronics and Linear Integrated Circuits/.
- Local textbook PDFs supplied in public/Analog Electronics and Linear Integrated Circuits/.

## Slide 7
Module 1 / BJT AC Models and Voltage Amplifiers
Base biased amplifier: analysis method
Use a small set of equations and assumptions to solve base biased amplifier problems.
• Draw the equivalent model
• Write known circuit relations
• Substitute device parameters
• State the result: Bias must keep the transistor in active region.
Takeaway
Bias must keep the transistor in active region.
VCC
RC
BJT
RE
Vin
Vout
Bias sets Q point; AC signal rides on it
VTU 1BEC304 • Module 1 • 07/50
Notes: [Animation]
Reveal model, equations, and result separately.
[Sources]
- Official VTU 2025 scheme syllabus PDF for 1BEC304.
- Local syllabus images supplied in public/Analog Electronics and Linear Integrated Circuits/.
- Local textbook PDFs supplied in public/Analog Electronics and Linear Integrated Circuits/.

## Slide 8
Module 1 / BJT AC Models and Voltage Amplifiers
Base biased amplifier: classroom example
A small numerical or waveform example makes base biased amplifier exam-ready.
• Given: bias path and Q point
• Find the target quantity
• Check units and region of operation
• Explain the physical meaning
Takeaway
Bias must keep the transistor in active region.
VCC
RC
BJT
RE
Vin
Vout
Bias sets Q point; AC signal rides on it
VTU 1BEC304 • Module 1 • 08/50
Notes: [Animation]
Animate the givens first, then the solution path.
[Sources]
- Official VTU 2025 scheme syllabus PDF for 1BEC304.
- Local syllabus images supplied in public/Analog Electronics and Linear Integrated Circuits/.
- Local textbook PDFs supplied in public/Analog Electronics and Linear Integrated Circuits/.

## Slide 9
Module 1 / BJT AC Models and Voltage Amplifiers
Emitter biased amplifier: core idea
Emitter bias improves stability by adding negative feedback in DC operation.
• emitter resistor
• thermal stability
• bypass capacitor
• gain
Takeaway
Stability and gain are traded through emitter resistance.
VCC
RC
BJT
RE
Vin
Vout
Bias sets Q point; AC signal rides on it
VTU 1BEC304 • Module 1 • 09/50
Notes: [Animation]
Start from the names: each term tells what the circuit controls.
[Sources]
- Official VTU 2025 scheme syllabus PDF for 1BEC304.
- Local syllabus images supplied in public/Analog Electronics and Linear Integrated Circuits/.
- Local textbook PDFs supplied in public/Analog Electronics and Linear Integrated Circuits/.

## Slide 10
Module 1 / BJT AC Models and Voltage Amplifiers
Emitter biased amplifier: circuit working
Follow the signal path and ask what each device or network contributes.
• Identify input and output nodes
• Mark DC bias and AC signal path
• Track phase, gain, impedance, or threshold
• Connect the result to the application
Takeaway
Stability and gain are traded through emitter resistance.
VCC
RC
BJT
RE
Vin
Vout
Bias sets Q point; AC signal rides on it
VTU 1BEC304 • Module 1 • 10/50
Notes: [Animation]
Reveal the circuit blocks left to right.
[Sources]
- Official VTU 2025 scheme syllabus PDF for 1BEC304.
- Local syllabus images supplied in public/Analog Electronics and Linear Integrated Circuits/.
- Local textbook PDFs supplied in public/Analog Electronics and Linear Integrated Circuits/.

## Slide 11
Module 1 / BJT AC Models and Voltage Amplifiers
Emitter biased amplifier: analysis method
Use a small set of equations and assumptions to solve emitter biased amplifier problems.
• Draw the equivalent model
• Write known circuit relations
• Substitute device parameters
• State the result: Stability and gain are traded through emitter resistance.
Takeaway
Stability and gain are traded through emitter resistance.
VCC
RC
BJT
RE
Vin
Vout
Bias sets Q point; AC signal rides on it
VTU 1BEC304 • Module 1 • 11/50
Notes: [Animation]
Reveal model, equations, and result separately.
[Sources]
- Official VTU 2025 scheme syllabus PDF for 1BEC304.
- Local syllabus images supplied in public/Analog Electronics and Linear Integrated Circuits/.
- Local textbook PDFs supplied in public/Analog Electronics and Linear Integrated Circuits/.

## Slide 12
Module 1 / BJT AC Models and Voltage Amplifiers
Emitter biased amplifier: classroom example
A small numerical or waveform example makes emitter biased amplifier exam-ready.
• Given: emitter resistor and thermal stability
• Find the target quantity
• Check units and region of operation
• Explain the physical meaning
Takeaway
Stability and gain are traded through emitter resistance.
VCC
RC
BJT
RE
Vin
Vout
Bias sets Q point; AC signal rides on it
VTU 1BEC304 • Module 1 • 12/50
Notes: [Animation]
Animate the givens first, then the solution path.
[Sources]
- Official VTU 2025 scheme syllabus PDF for 1BEC304.
- Local syllabus images supplied in public/Analog Electronics and Linear Integrated Circuits/.
- Local textbook PDFs supplied in public/Analog Electronics and Linear Integrated Circuits/.

## Slide 13
Module 1 / BJT AC Models and Voltage Amplifiers
Small signal operation: core idea
Small-signal analysis replaces nonlinear curves with local linear models.
• incremental signal
• active region
• linearization
• Q point
Takeaway
Amplifier math is built around the operating point.
VCC
RC
BJT
RE
Vin
Vout
Bias sets Q point; AC signal rides on it
VTU 1BEC304 • Module 1 • 13/50
Notes: [Animation]
Start from the names: each term tells what the circuit controls.
[Sources]
- Official VTU 2025 scheme syllabus PDF for 1BEC304.
- Local syllabus images supplied in public/Analog Electronics and Linear Integrated Circuits/.
- Local textbook PDFs supplied in public/Analog Electronics and Linear Integrated Circuits/.

## Slide 14
Module 1 / BJT AC Models and Voltage Amplifiers
Small signal operation: circuit working
Follow the signal path and ask what each device or network contributes.
• Identify input and output nodes
• Mark DC bias and AC signal path
• Track phase, gain, impedance, or threshold
• Connect the result to the application
Takeaway
Amplifier math is built around the operating point.
VCC
RC
BJT
RE
Vin
Vout
Bias sets Q point; AC signal rides on it
VTU 1BEC304 • Module 1 • 14/50
Notes: [Animation]
Reveal the circuit blocks left to right.
[Sources]
- Official VTU 2025 scheme syllabus PDF for 1BEC304.
- Local syllabus images supplied in public/Analog Electronics and Linear Integrated Circuits/.
- Local textbook PDFs supplied in public/Analog Electronics and Linear Integrated Circuits/.

## Slide 15
Module 1 / BJT AC Models and Voltage Amplifiers
Small signal operation: analysis method
Use a small set of equations and assumptions to solve small signal operation problems.
• Draw the equivalent model
• Write known circuit relations
• Substitute device parameters
• State the result: Amplifier math is built around the operating point.
Takeaway
Amplifier math is built around the operating point.
VCC
RC
BJT
RE
Vin
Vout
Bias sets Q point; AC signal rides on it
VTU 1BEC304 • Module 1 • 15/50
Notes: [Animation]
Reveal model, equations, and result separately.
[Sources]
- Official VTU 2025 scheme syllabus PDF for 1BEC304.
- Local syllabus images supplied in public/Analog Electronics and Linear Integrated Circuits/.
- Local textbook PDFs supplied in public/Analog Electronics and Linear Integrated Circuits/.

## Slide 16
Module 1 / BJT AC Models and Voltage Amplifiers
Small signal operation: classroom example
A small numerical or waveform example makes small signal operation exam-ready.
• Given: incremental signal and active region
• Find the target quantity
• Check units and region of operation
• Explain the physical meaning
Takeaway
Amplifier math is built around the operating point.
VCC
RC
BJT
RE
Vin
Vout
Bias sets Q point; AC signal rides on it
VTU 1BEC304 • Module 1 • 16/50
Notes: [Animation]
Animate the givens first, then the solution path.
[Sources]
- Official VTU 2025 scheme syllabus PDF for 1BEC304.
- Local syllabus images supplied in public/Analog Electronics and Linear Integrated Circuits/.
- Local textbook PDFs supplied in public/Analog Electronics and Linear Integrated Circuits/.

## Slide 17
Module 1 / BJT AC Models and Voltage Amplifiers
AC beta and emitter diode resistance: core idea
AC beta relates collector signal current to base signal current; emitter resistance sets gain scale.
• beta_ac
• re prime
• thermal voltage
• emitter current
Takeaway
re prime falls as emitter current rises.
VCC
RC
BJT
RE
Vin
Vout
Bias sets Q point; AC signal rides on it
VTU 1BEC304 • Module 1 • 17/50
Notes: [Animation]
Start from the names: each term tells what the circuit controls.
[Sources]
- Official VTU 2025 scheme syllabus PDF for 1BEC304.
- Local syllabus images supplied in public/Analog Electronics and Linear Integrated Circuits/.
- Local textbook PDFs supplied in public/Analog Electronics and Linear Integrated Circuits/.

## Slide 18
Module 1 / BJT AC Models and Voltage Amplifiers
AC beta and emitter diode resistance: circuit working
Follow the signal path and ask what each device or network contributes.
• Identify input and output nodes
• Mark DC bias and AC signal path
• Track phase, gain, impedance, or threshold
• Connect the result to the application
Takeaway
re prime falls as emitter current rises.
VCC
RC
BJT
RE
Vin
Vout
Bias sets Q point; AC signal rides on it
VTU 1BEC304 • Module 1 • 18/50
Notes: [Animation]
Reveal the circuit blocks left to right.
[Sources]
- Official VTU 2025 scheme syllabus PDF for 1BEC304.
- Local syllabus images supplied in public/Analog Electronics and Linear Integrated Circuits/.
- Local textbook PDFs supplied in public/Analog Electronics and Linear Integrated Circuits/.

## Slide 19
Module 1 / BJT AC Models and Voltage Amplifiers
AC beta and emitter diode resistance: analysis method
Use a small set of equations and assumptions to solve ac beta and emitter diode resistance problems.
• Draw the equivalent model
• Write known circuit relations
• Substitute device parameters
• State the result: re prime falls as emitter current rises.
Takeaway
re prime falls as emitter current rises.
VCC
RC
BJT
RE
Vin
Vout
Bias sets Q point; AC signal rides on it
VTU 1BEC304 • Module 1 • 19/50
Notes: [Animation]
Reveal model, equations, and result separately.
[Sources]
- Official VTU 2025 scheme syllabus PDF for 1BEC304.
- Local syllabus images supplied in public/Analog Electronics and Linear Integrated Circuits/.
- Local textbook PDFs supplied in public/Analog Electronics and Linear Integrated Circuits/.

## Slide 20
Module 1 / BJT AC Models and Voltage Amplifiers
AC beta and emitter diode resistance: classroom example
A small numerical or waveform example makes ac beta and emitter diode resistance exam-ready.
• Given: beta_ac and re prime
• Find the target quantity
• Check units and region of operation
• Explain the physical meaning
Takeaway
re prime falls as emitter current rises.
VCC
RC
BJT
RE
Vin
Vout
Bias sets Q point; AC signal rides on it
VTU 1BEC304 • Module 1 • 20/50
Notes: [Animation]
Animate the givens first, then the solution path.
[Sources]
- Official VTU 2025 scheme syllabus PDF for 1BEC304.
- Local syllabus images supplied in public/Analog Electronics and Linear Integrated Circuits/.
- Local textbook PDFs supplied in public/Analog Electronics and Linear Integrated Circuits/.

## Slide 21
Module 1 / BJT AC Models and Voltage Amplifiers
Two-transistor models: core idea
Models simplify the BJT into resistances and controlled sources.
• r model
• hybrid model
• input resistance
• current gain
Takeaway
Choose the model that makes the circuit easiest to analyze.
VCC
RC
BJT
RE
Vin
Vout
Bias sets Q point; AC signal rides on it
VTU 1BEC304 • Module 1 • 21/50
Notes: [Animation]
Start from the names: each term tells what the circuit controls.
[Sources]
- Official VTU 2025 scheme syllabus PDF for 1BEC304.
- Local syllabus images supplied in public/Analog Electronics and Linear Integrated Circuits/.
- Local textbook PDFs supplied in public/Analog Electronics and Linear Integrated Circuits/.

## Slide 22
Module 1 / BJT AC Models and Voltage Amplifiers
Two-transistor models: circuit working
Follow the signal path and ask what each device or network contributes.
• Identify input and output nodes
• Mark DC bias and AC signal path
• Track phase, gain, impedance, or threshold
• Connect the result to the application
Takeaway
Choose the model that makes the circuit easiest to analyze.
VCC
RC
BJT
RE
Vin
Vout
Bias sets Q point; AC signal rides on it
VTU 1BEC304 • Module 1 • 22/50
Notes: [Animation]
Reveal the circuit blocks left to right.
[Sources]
- Official VTU 2025 scheme syllabus PDF for 1BEC304.
- Local syllabus images supplied in public/Analog Electronics and Linear Integrated Circuits/.
- Local textbook PDFs supplied in public/Analog Electronics and Linear Integrated Circuits/.

## Slide 23
Module 1 / BJT AC Models and Voltage Amplifiers
Two-transistor models: analysis method
Use a small set of equations and assumptions to solve two-transistor models problems.
• Draw the equivalent model
• Write known circuit relations
• Substitute device parameters
• State the result: Choose the model that makes the circuit easiest to analyze.
Takeaway
Choose the model that makes the circuit easiest to analyze.
VCC
RC
BJT
RE
Vin
Vout
Bias sets Q point; AC signal rides on it
VTU 1BEC304 • Module 1 • 23/50
Notes: [Animation]
Reveal model, equations, and result separately.
[Sources]
- Official VTU 2025 scheme syllabus PDF for 1BEC304.
- Local syllabus images supplied in public/Analog Electronics and Linear Integrated Circuits/.
- Local textbook PDFs supplied in public/Analog Electronics and Linear Integrated Circuits/.

## Slide 24
Module 1 / BJT AC Models and Voltage Amplifiers
Two-transistor models: classroom example
A small numerical or waveform example makes two-transistor models exam-ready.
• Given: r model and hybrid model
• Find the target quantity
• Check units and region of operation
• Explain the physical meaning
Takeaway
Choose the model that makes the circuit easiest to analyze.
VCC
RC
BJT
RE
Vin
Vout
Bias sets Q point; AC signal rides on it
VTU 1BEC304 • Module 1 • 24/50
Notes: [Animation]
Animate the givens first, then the solution path.
[Sources]
- Official VTU 2025 scheme syllabus PDF for 1BEC304.
- Local syllabus images supplied in public/Analog Electronics and Linear Integrated Circuits/.
- Local textbook PDFs supplied in public/Analog Electronics and Linear Integrated Circuits/.

## Slide 25
Module 1 / BJT AC Models and Voltage Amplifiers
Voltage amplifiers: core idea
A voltage amplifier converts small input voltage changes into larger output voltage changes.
• input
• output
• phase inversion
• loading
Takeaway
Common-emitter stages give voltage gain and phase inversion.
VCC
RC
BJT
RE
Vin
Vout
Bias sets Q point; AC signal rides on it
VTU 1BEC304 • Module 1 • 25/50
Notes: [Animation]
Start from the names: each term tells what the circuit controls.
[Sources]
- Official VTU 2025 scheme syllabus PDF for 1BEC304.
- Local syllabus images supplied in public/Analog Electronics and Linear Integrated Circuits/.
- Local textbook PDFs supplied in public/Analog Electronics and Linear Integrated Circuits/.

## Slide 26
Module 1 / BJT AC Models and Voltage Amplifiers
Voltage amplifiers: circuit working
Follow the signal path and ask what each device or network contributes.
• Identify input and output nodes
• Mark DC bias and AC signal path
• Track phase, gain, impedance, or threshold
• Connect the result to the application
Takeaway
Common-emitter stages give voltage gain and phase inversion.
VCC
RC
BJT
RE
Vin
Vout
Bias sets Q point; AC signal rides on it
VTU 1BEC304 • Module 1 • 26/50
Notes: [Animation]
Reveal the circuit blocks left to right.
[Sources]
- Official VTU 2025 scheme syllabus PDF for 1BEC304.
- Local syllabus images supplied in public/Analog Electronics and Linear Integrated Circuits/.
- Local textbook PDFs supplied in public/Analog Electronics and Linear Integrated Circuits/.

## Slide 27
Module 1 / BJT AC Models and Voltage Amplifiers
Voltage amplifiers: analysis method
Use a small set of equations and assumptions to solve voltage amplifiers problems.
• Draw the equivalent model
• Write known circuit relations
• Substitute device parameters
• State the result: Common-emitter stages give voltage gain and phase inversion.
Takeaway
Common-emitter stages give voltage gain and phase inversion.
VCC
RC
BJT
RE
Vin
Vout
Bias sets Q point; AC signal rides on it
VTU 1BEC304 • Module 1 • 27/50
Notes: [Animation]
Reveal model, equations, and result separately.
[Sources]
- Official VTU 2025 scheme syllabus PDF for 1BEC304.
- Local syllabus images supplied in public/Analog Electronics and Linear Integrated Circuits/.
- Local textbook PDFs supplied in public/Analog Electronics and Linear Integrated Circuits/.

## Slide 28
Module 1 / BJT AC Models and Voltage Amplifiers
Voltage amplifiers: classroom example
A small numerical or waveform example makes voltage amplifiers exam-ready.
• Given: input and output
• Find the target quantity
• Check units and region of operation
• Explain the physical meaning
Takeaway
Common-emitter stages give voltage gain and phase inversion.
VCC
RC
BJT
RE
Vin
Vout
Bias sets Q point; AC signal rides on it
VTU 1BEC304 • Module 1 • 28/50
Notes: [Animation]
Animate the givens first, then the solution path.
[Sources]
- Official VTU 2025 scheme syllabus PDF for 1BEC304.
- Local syllabus images supplied in public/Analog Electronics and Linear Integrated Circuits/.
- Local textbook PDFs supplied in public/Analog Electronics and Linear Integrated Circuits/.

## Slide 29
Module 1 / BJT AC Models and Voltage Amplifiers
Multistage amplifiers: core idea
Cascaded stages multiply gain but interact through impedances.
• stage gain
• loading
• coupling
• overall gain
Takeaway
Overall gain must include loading between stages.
VCC
RC
BJT
RE
Vin
Vout
Bias sets Q point; AC signal rides on it
VTU 1BEC304 • Module 1 • 29/50
Notes: [Animation]
Start from the names: each term tells what the circuit controls.
[Sources]
- Official VTU 2025 scheme syllabus PDF for 1BEC304.
- Local syllabus images supplied in public/Analog Electronics and Linear Integrated Circuits/.
- Local textbook PDFs supplied in public/Analog Electronics and Linear Integrated Circuits/.

## Slide 30
Module 1 / BJT AC Models and Voltage Amplifiers
Multistage amplifiers: circuit working
Follow the signal path and ask what each device or network contributes.
• Identify input and output nodes
• Mark DC bias and AC signal path
• Track phase, gain, impedance, or threshold
• Connect the result to the application
Takeaway
Overall gain must include loading between stages.
VCC
RC
BJT
RE
Vin
Vout
Bias sets Q point; AC signal rides on it
VTU 1BEC304 • Module 1 • 30/50
Notes: [Animation]
Reveal the circuit blocks left to right.
[Sources]
- Official VTU 2025 scheme syllabus PDF for 1BEC304.
- Local syllabus images supplied in public/Analog Electronics and Linear Integrated Circuits/.
- Local textbook PDFs supplied in public/Analog Electronics and Linear Integrated Circuits/.

## Slide 31
Module 1 / BJT AC Models and Voltage Amplifiers
Multistage amplifiers: analysis method
Use a small set of equations and assumptions to solve multistage amplifiers problems.
• Draw the equivalent model
• Write known circuit relations
• Substitute device parameters
• State the result: Overall gain must include loading between stages.
Takeaway
Overall gain must include loading between stages.
VCC
RC
BJT
RE
Vin
Vout
Bias sets Q point; AC signal rides on it
VTU 1BEC304 • Module 1 • 31/50
Notes: [Animation]
Reveal model, equations, and result separately.
[Sources]
- Official VTU 2025 scheme syllabus PDF for 1BEC304.
- Local syllabus images supplied in public/Analog Electronics and Linear Integrated Circuits/.
- Local textbook PDFs supplied in public/Analog Electronics and Linear Integrated Circuits/.

## Slide 32
Module 1 / BJT AC Models and Voltage Amplifiers
Multistage amplifiers: classroom example
A small numerical or waveform example makes multistage amplifiers exam-ready.
• Given: stage gain and loading
• Find the target quantity
• Check units and region of operation
• Explain the physical meaning
Takeaway
Overall gain must include loading between stages.
VCC
RC
BJT
RE
Vin
Vout
Bias sets Q point; AC signal rides on it
VTU 1BEC304 • Module 1 • 32/50
Notes: [Animation]
Animate the givens first, then the solution path.
[Sources]
- Official VTU 2025 scheme syllabus PDF for 1BEC304.
- Local syllabus images supplied in public/Analog Electronics and Linear Integrated Circuits/.
- Local textbook PDFs supplied in public/Analog Electronics and Linear Integrated Circuits/.

## Slide 33
Module 1 / BJT AC Models and Voltage Amplifiers
CC amplifier and output impedance: core idea
The CC stage buffers signals with near-unity voltage gain.
• emitter follower
• high input impedance
• low output impedance
• buffer
Takeaway
Emitter followers are impedance transformers.
VCC
RC
BJT
RE
Vin
Vout
Bias sets Q point; AC signal rides on it
VTU 1BEC304 • Module 1 • 33/50
Notes: [Animation]
Start from the names: each term tells what the circuit controls.
[Sources]
- Official VTU 2025 scheme syllabus PDF for 1BEC304.
- Local syllabus images supplied in public/Analog Electronics and Linear Integrated Circuits/.
- Local textbook PDFs supplied in public/Analog Electronics and Linear Integrated Circuits/.

## Slide 34
Module 1 / BJT AC Models and Voltage Amplifiers
CC amplifier and output impedance: circuit working
Follow the signal path and ask what each device or network contributes.
• Identify input and output nodes
• Mark DC bias and AC signal path
• Track phase, gain, impedance, or threshold
• Connect the result to the application
Takeaway
Emitter followers are impedance transformers.
VCC
RC
BJT
RE
Vin
Vout
Bias sets Q point; AC signal rides on it
VTU 1BEC304 • Module 1 • 34/50
Notes: [Animation]
Reveal the circuit blocks left to right.
[Sources]
- Official VTU 2025 scheme syllabus PDF for 1BEC304.
- Local syllabus images supplied in public/Analog Electronics and Linear Integrated Circuits/.
- Local textbook PDFs supplied in public/Analog Electronics and Linear Integrated Circuits/.

## Slide 35
Module 1 / BJT AC Models and Voltage Amplifiers
CC amplifier and output impedance: analysis method
Use a small set of equations and assumptions to solve cc amplifier and output impedance problems.
• Draw the equivalent model
• Write known circuit relations
• Substitute device parameters
• State the result: Emitter followers are impedance transformers.
Takeaway
Emitter followers are impedance transformers.
VCC
RC
BJT
RE
Vin
Vout
Bias sets Q point; AC signal rides on it
VTU 1BEC304 • Module 1 • 35/50
Notes: [Animation]
Reveal model, equations, and result separately.
[Sources]
- Official VTU 2025 scheme syllabus PDF for 1BEC304.
- Local syllabus images supplied in public/Analog Electronics and Linear Integrated Circuits/.
- Local textbook PDFs supplied in public/Analog Electronics and Linear Integrated Circuits/.

## Slide 36
Module 1 / BJT AC Models and Voltage Amplifiers
CC amplifier and output impedance: classroom example
A small numerical or waveform example makes cc amplifier and output impedance exam-ready.
• Given: emitter follower and high input impedance
• Find the target quantity
• Check units and region of operation
• Explain the physical meaning
Takeaway
Emitter followers are impedance transformers.
VCC
RC
BJT
RE
Vin
Vout
Bias sets Q point; AC signal rides on it
VTU 1BEC304 • Module 1 • 36/50
Notes: [Animation]
Animate the givens first, then the solution path.
[Sources]
- Official VTU 2025 scheme syllabus PDF for 1BEC304.
- Local syllabus images supplied in public/Analog Electronics and Linear Integrated Circuits/.
- Local textbook PDFs supplied in public/Analog Electronics and Linear Integrated Circuits/.

## Slide 37
Module 1 / BJT AC Models and Voltage Amplifiers
Darlington and voltage regulation: core idea
Darlington connections increase current gain; regulators hold output against load changes.
• compound beta
• high input resistance
• regulator
• load change
Takeaway
Current gain helps drive loads without heavy source loading.
VCC
RC
BJT
RE
Vin
Vout
Bias sets Q point; AC signal rides on it
VTU 1BEC304 • Module 1 • 37/50
Notes: [Animation]
Start from the names: each term tells what the circuit controls.
[Sources]
- Official VTU 2025 scheme syllabus PDF for 1BEC304.
- Local syllabus images supplied in public/Analog Electronics and Linear Integrated Circuits/.
- Local textbook PDFs supplied in public/Analog Electronics and Linear Integrated Circuits/.

## Slide 38
Module 1 / BJT AC Models and Voltage Amplifiers
Darlington and voltage regulation: circuit working
Follow the signal path and ask what each device or network contributes.
• Identify input and output nodes
• Mark DC bias and AC signal path
• Track phase, gain, impedance, or threshold
• Connect the result to the application
Takeaway
Current gain helps drive loads without heavy source loading.
VCC
RC
BJT
RE
Vin
Vout
Bias sets Q point; AC signal rides on it
VTU 1BEC304 • Module 1 • 38/50
Notes: [Animation]
Reveal the circuit blocks left to right.
[Sources]
- Official VTU 2025 scheme syllabus PDF for 1BEC304.
- Local syllabus images supplied in public/Analog Electronics and Linear Integrated Circuits/.
- Local textbook PDFs supplied in public/Analog Electronics and Linear Integrated Circuits/.

## Slide 39
Module 1 / BJT AC Models and Voltage Amplifiers
Darlington and voltage regulation: analysis method
Use a small set of equations and assumptions to solve darlington and voltage regulation problems.
• Draw the equivalent model
• Write known circuit relations
• Substitute device parameters
• State the result: Current gain helps drive loads without heavy source loading.
Takeaway
Current gain helps drive loads without heavy source loading.
VCC
RC
BJT
RE
Vin
Vout
Bias sets Q point; AC signal rides on it
VTU 1BEC304 • Module 1 • 39/50
Notes: [Animation]
Reveal model, equations, and result separately.
[Sources]
- Official VTU 2025 scheme syllabus PDF for 1BEC304.
- Local syllabus images supplied in public/Analog Electronics and Linear Integrated Circuits/.
- Local textbook PDFs supplied in public/Analog Electronics and Linear Integrated Circuits/.

## Slide 40
Module 1 / BJT AC Models and Voltage Amplifiers
Darlington and voltage regulation: classroom example
A small numerical or waveform example makes darlington and voltage regulation exam-ready.
• Given: compound beta and high input resistance
• Find the target quantity
• Check units and region of operation
• Explain the physical meaning
Takeaway
Current gain helps drive loads without heavy source loading.
VCC
RC
BJT
RE
Vin
Vout
Bias sets Q point; AC signal rides on it
VTU 1BEC304 • Module 1 • 40/50
Notes: [Animation]
Animate the givens first, then the solution path.
[Sources]
- Official VTU 2025 scheme syllabus PDF for 1BEC304.
- Local syllabus images supplied in public/Analog Electronics and Linear Integrated Circuits/.
- Local textbook PDFs supplied in public/Analog Electronics and Linear Integrated Circuits/.

## Slide 41
Module 1 / BJT AC Models and Voltage Amplifiers
Common-base amplifier: core idea
The CB stage is useful when low input impedance or high-frequency response is needed.
• low input impedance
• high frequency
• current buffer
• no phase inversion
Takeaway
Not every amplifier is optimized for voltage gain.
VCC
RC
BJT
RE
Vin
Vout
Bias sets Q point; AC signal rides on it
VTU 1BEC304 • Module 1 • 41/50
Notes: [Animation]
Start from the names: each term tells what the circuit controls.
[Sources]
- Official VTU 2025 scheme syllabus PDF for 1BEC304.
- Local syllabus images supplied in public/Analog Electronics and Linear Integrated Circuits/.
- Local textbook PDFs supplied in public/Analog Electronics and Linear Integrated Circuits/.

## Slide 42
Module 1 / BJT AC Models and Voltage Amplifiers
Common-base amplifier: circuit working
Follow the signal path and ask what each device or network contributes.
• Identify input and output nodes
• Mark DC bias and AC signal path
• Track phase, gain, impedance, or threshold
• Connect the result to the application
Takeaway
Not every amplifier is optimized for voltage gain.
VCC
RC
BJT
RE
Vin
Vout
Bias sets Q point; AC signal rides on it
VTU 1BEC304 • Module 1 • 42/50
Notes: [Animation]
Reveal the circuit blocks left to right.
[Sources]
- Official VTU 2025 scheme syllabus PDF for 1BEC304.
- Local syllabus images supplied in public/Analog Electronics and Linear Integrated Circuits/.
- Local textbook PDFs supplied in public/Analog Electronics and Linear Integrated Circuits/.

## Slide 43
Module 1 / BJT AC Models and Voltage Amplifiers
Common-base amplifier: analysis method
Use a small set of equations and assumptions to solve common-base amplifier problems.
• Draw the equivalent model
• Write known circuit relations
• Substitute device parameters
• State the result: Not every amplifier is optimized for voltage gain.
Takeaway
Not every amplifier is optimized for voltage gain.
VCC
RC
BJT
RE
Vin
Vout
Bias sets Q point; AC signal rides on it
VTU 1BEC304 • Module 1 • 43/50
Notes: [Animation]
Reveal model, equations, and result separately.
[Sources]
- Official VTU 2025 scheme syllabus PDF for 1BEC304.
- Local syllabus images supplied in public/Analog Electronics and Linear Integrated Circuits/.
- Local textbook PDFs supplied in public/Analog Electronics and Linear Integrated Circuits/.

## Slide 44
Module 1 / BJT AC Models and Voltage Amplifiers
Common-base amplifier: classroom example
A small numerical or waveform example makes common-base amplifier exam-ready.
• Given: low input impedance and high frequency
• Find the target quantity
• Check units and region of operation
• Explain the physical meaning
Takeaway
Not every amplifier is optimized for voltage gain.
VCC
RC
BJT
RE
Vin
Vout
Bias sets Q point; AC signal rides on it
VTU 1BEC304 • Module 1 • 44/50
Notes: [Animation]
Animate the givens first, then the solution path.
[Sources]
- Official VTU 2025 scheme syllabus PDF for 1BEC304.
- Local syllabus images supplied in public/Analog Electronics and Linear Integrated Circuits/.
- Local textbook PDFs supplied in public/Analog Electronics and Linear Integrated Circuits/.

## Slide 45
Review
Module 1 summary map
BJT AC Models and Voltage Amplifiers
Base biased amplifier
Emitter biased amplifier
Small signal operation
AC beta and emitter diode resistance
Two-transistor models
Voltage amplifiers
Multistage amplifiers
CC amplifier and output impedance
If students can redraw this map, they can revise the module quickly.
VTU 1BEC304 • Module 1 • 45/50
Notes: [Animation]
Use this as a recall activity. Reveal outer topics and ask for one formula or circuit use for each.
[Sources]
- Official VTU 2025 scheme syllabus PDF for 1BEC304.
- Local syllabus images supplied in public/Analog Electronics and Linear Integrated Circuits/.
- Local textbook PDFs supplied in public/Analog Electronics and Linear Integrated Circuits/.

## Slide 46
Practice
Module 1 exam-focused questions
1
Explain base biased amplifier with a neat circuit diagram.
10 marks
2
Derive or outline the analysis method for emitter biased amplifier.
10 marks
3
Compare small signal operation and ac beta and emitter diode resistance.
10 marks
4
Solve a numerical design problem based on two-transistor models.
short note
5
Draw the waveform/response for voltage amplifiers and explain.
short note
6
Write short notes on multistage amplifiers and applications.
short note
VTU 1BEC304 • Module 1 • 46/50
Notes: [Animation]
Reveal questions one by one. For each question, ask students to first sketch the circuit or response.
[Sources]
- Official VTU 2025 scheme syllabus PDF for 1BEC304.
- Local syllabus images supplied in public/Analog Electronics and Linear Integrated Circuits/.
- Local textbook PDFs supplied in public/Analog Electronics and Linear Integrated Circuits/.

## Slide 47
Exam quick reference
Module 1 formula and design checkpoints
1
Av roughly -RC / re prime
core
2
Zin depends on bias network and beta re
core
3
Overall gain = product of loaded stage gains
check
4
Emitter follower Av nearly 1
check
VTU 1BEC304 • Module 1 • 47/50
Notes: [Animation]
Reveal formulas one at a time. Ask students to name the assumptions behind each checkpoint.
[Sources]
- Official VTU 2025 scheme syllabus PDF for 1BEC304.
- Local syllabus images supplied in public/Analog Electronics and Linear Integrated Circuits/.
- Local textbook PDFs supplied in public/Analog Electronics and Linear Integrated Circuits/.

## Slide 48
Review
Module 1 summary map
BJT AC Models and Voltage Amplifiers
Base biased amplifier
Emitter biased amplifier
Small signal operation
AC beta and emitter diode resistance
Two-transistor models
Voltage amplifiers
Multistage amplifiers
CC amplifier and output impedance
If students can redraw this map, they can revise the module quickly.
VTU 1BEC304 • Module 1 • 48/50
Notes: [Animation]
Use this as a recall activity. Reveal outer topics and ask for one formula or circuit use for each.
[Sources]
- Official VTU 2025 scheme syllabus PDF for 1BEC304.
- Local syllabus images supplied in public/Analog Electronics and Linear Integrated Circuits/.
- Local textbook PDFs supplied in public/Analog Electronics and Linear Integrated Circuits/.

## Slide 49
Practice
Module 1 exam-focused questions
1
Explain base biased amplifier with a neat circuit diagram.
10 marks
2
Derive or outline the analysis method for emitter biased amplifier.
10 marks
3
Compare small signal operation and ac beta and emitter diode resistance.
10 marks
4
Solve a numerical design problem based on two-transistor models.
short note
5
Draw the waveform/response for voltage amplifiers and explain.
short note
6
Write short notes on multistage amplifiers and applications.
short note
VTU 1BEC304 • Module 1 • 49/50
Notes: [Animation]
Reveal questions one by one. For each question, ask students to first sketch the circuit or response.
[Sources]
- Official VTU 2025 scheme syllabus PDF for 1BEC304.
- Local syllabus images supplied in public/Analog Electronics and Linear Integrated Circuits/.
- Local textbook PDFs supplied in public/Analog Electronics and Linear Integrated Circuits/.

## Slide 50
Module 1 / BJT AC Models and Voltage Amplifiers
Small signal operation: classroom example
A small numerical or waveform example makes small signal operation exam-ready.
• Given: incremental signal and active region
• Find the target quantity
• Check units and region of operation
• Explain the physical meaning
Takeaway
Amplifier math is built around the operating point.
VCC
RC
BJT
RE
Vin
Vout
Bias sets Q point; AC signal rides on it
VTU 1BEC304 • Module 1 • 50/50
Notes: [Animation]
Animate the givens first, then the solution path.
[Sources]
- Official VTU 2025 scheme syllabus PDF for 1BEC304.
- Local syllabus images supplied in public/Analog Electronics and Linear Integrated Circuits/.
- Local textbook PDFs supplied in public/Analog Electronics and Linear Integrated Circuits/.