## Slide 1
Green Materials and E-Waste Management
Module 5 explains sustainable materials, smart-system biomaterials and responsible electronics recovery.
VTU 1BCHES102/202 | Module 5
Opening
01
Applied Chemistry
Module 5
Green solvents • glycerol trioleate • ZnO nanoparticles • PLA • PEG • alginate hydrogel • e-waste • AI management • bioleaching
GREEN
SYSTEMS
Notes: What to say: Open by saying smart systems should be designed for performance and end-of-life responsibility.
Pause cue: pause after each process diagram and ask students what makes the method greener or more sustainable.
Pointing cue: point from source material to synthesis/property, then to application or waste-management outcome.
Question to ask students: Ask students to connect material property with smart-system use and environmental impact.
Animation instructions: Fade title; appear cards one by one; wipe process arrows in order; highlight keywords such as green solvent, glycerol trioleate, ZnO nanoparticles, RFID, IONT, PLA, PEG, alginate hydrogel, BCI, e-waste, AI and bioleaching word by word.
Transition style: Fade.
[Sources] VTU syllabus PDF 1BCHES102/202 Applied Chemistry for Smart Systems, Module 5 checklist, downloaded from https://vtu.ac.in/pdf/UG2024/1BCHES102.pdf; syllabus-listed textbooks: Engineering Chemistry, Suba Ramesh, Vairam, Ananda Murthy, Wiley India, 2011; A Textbook of Engineering Chemistry, R.V. Gadag and Nityananda Shetty, I.K. International, 2nd ed., 2016; Engineering Chemistry, Jain & Jain, Dhanpat Rai; Wiley Engineering Chemistry, Wiley India, 2013; syllabus-listed references for green/biomaterial/e-waste background include Green Chemistry and Engineering: A Practical Design Approach, Concepción Jiménez-González and David J.C. Constable, Wiley, 2011; E-Waste: Implications, Regulations, and Management in India and Current Global Best Practices, Rakesh Johri, TERI, 2008.

## Slide 2
Module 5 learning path
Use the VTU syllabus as the complete checklist.
VTU 1BCHES102/202 | Module 5
Opening
02
1
Explain green chemistry and green solvents for server heat management
2
Explain glycerol trioleate ester synthesis, properties and IT infrastructure uses
3
Explain green synthesis of ZnO nanoparticles and RFID/IONT applications
4
Explain PLA, PEG and touch-screen applications
5
Explain alginate hydrogel synthesis, properties and BCI applications
6
Explain e-waste sources, composition, effects, AI management and gold bioleaching
Notes: What to say: Show students that the module spans design, materials and waste recovery.
Pause cue: pause after each process diagram and ask students what makes the method greener or more sustainable.
Pointing cue: point from source material to synthesis/property, then to application or waste-management outcome.
Question to ask students: Ask students to connect material property with smart-system use and environmental impact.
Animation instructions: Fade title; appear cards one by one; wipe process arrows in order; highlight keywords such as green solvent, glycerol trioleate, ZnO nanoparticles, RFID, IONT, PLA, PEG, alginate hydrogel, BCI, e-waste, AI and bioleaching word by word.
Transition style: Fade.
[Sources] VTU syllabus PDF 1BCHES102/202 Applied Chemistry for Smart Systems, Module 5 checklist, downloaded from https://vtu.ac.in/pdf/UG2024/1BCHES102.pdf; syllabus-listed textbooks: Engineering Chemistry, Suba Ramesh, Vairam, Ananda Murthy, Wiley India, 2011; A Textbook of Engineering Chemistry, R.V. Gadag and Nityananda Shetty, I.K. International, 2nd ed., 2016; Engineering Chemistry, Jain & Jain, Dhanpat Rai; Wiley Engineering Chemistry, Wiley India, 2013; syllabus-listed references for green/biomaterial/e-waste background include Green Chemistry and Engineering: A Practical Design Approach, Concepción Jiménez-González and David J.C. Constable, Wiley, 2011; E-Waste: Implications, Regulations, and Management in India and Current Global Best Practices, Rakesh Johri, TERI, 2008.

## Slide 3
The Module 5 story
Show the sustainability logic.
VTU 1BCHES102/202 | Module 5
Opening
03
Choose safer chemistry
Make useful green materials
Use them in smart systems
Collect end-of-life electronics
Recover value responsibly
Notes: What to say: Use this as the throughline.
Pause cue: pause after each process diagram and ask students what makes the method greener or more sustainable.
Pointing cue: point from source material to synthesis/property, then to application or waste-management outcome.
Question to ask students: Ask students to connect material property with smart-system use and environmental impact.
Animation instructions: Fade title; appear cards one by one; wipe process arrows in order; highlight keywords such as green solvent, glycerol trioleate, ZnO nanoparticles, RFID, IONT, PLA, PEG, alginate hydrogel, BCI, e-waste, AI and bioleaching word by word.
Transition style: Fade.
[Sources] VTU syllabus PDF 1BCHES102/202 Applied Chemistry for Smart Systems, Module 5 checklist, downloaded from https://vtu.ac.in/pdf/UG2024/1BCHES102.pdf; syllabus-listed textbooks: Engineering Chemistry, Suba Ramesh, Vairam, Ananda Murthy, Wiley India, 2011; A Textbook of Engineering Chemistry, R.V. Gadag and Nityananda Shetty, I.K. International, 2nd ed., 2016; Engineering Chemistry, Jain & Jain, Dhanpat Rai; Wiley Engineering Chemistry, Wiley India, 2013; syllabus-listed references for green/biomaterial/e-waste background include Green Chemistry and Engineering: A Practical Design Approach, Concepción Jiménez-González and David J.C. Constable, Wiley, 2011; E-Waste: Implications, Regulations, and Management in India and Current Global Best Practices, Rakesh Johri, TERI, 2008.

## Slide 4
Why green materials matter
Start with real-world need.
VTU 1BCHES102/202 | Module 5
Opening
04
Data centers
Need safer and efficient thermal-management fluids.
Smart devices
Need light, transparent and biocompatible materials.
Nano systems
Need functional particles with greener synthesis routes.
E-waste growth
Electronics must be recovered without harming people or ecosystems.
Notes: What to say: Ask students which device they replace most often.
Pause cue: pause after each process diagram and ask students what makes the method greener or more sustainable.
Pointing cue: point from source material to synthesis/property, then to application or waste-management outcome.
Question to ask students: Ask students to connect material property with smart-system use and environmental impact.
Animation instructions: Fade title; appear cards one by one; wipe process arrows in order; highlight keywords such as green solvent, glycerol trioleate, ZnO nanoparticles, RFID, IONT, PLA, PEG, alginate hydrogel, BCI, e-waste, AI and bioleaching word by word.
Transition style: Fade.
[Sources] VTU syllabus PDF 1BCHES102/202 Applied Chemistry for Smart Systems, Module 5 checklist, downloaded from https://vtu.ac.in/pdf/UG2024/1BCHES102.pdf; syllabus-listed textbooks: Engineering Chemistry, Suba Ramesh, Vairam, Ananda Murthy, Wiley India, 2011; A Textbook of Engineering Chemistry, R.V. Gadag and Nityananda Shetty, I.K. International, 2nd ed., 2016; Engineering Chemistry, Jain & Jain, Dhanpat Rai; Wiley Engineering Chemistry, Wiley India, 2013; syllabus-listed references for green/biomaterial/e-waste background include Green Chemistry and Engineering: A Practical Design Approach, Concepción Jiménez-González and David J.C. Constable, Wiley, 2011; E-Waste: Implications, Regulations, and Management in India and Current Global Best Practices, Rakesh Johri, TERI, 2008.

## Slide 5
What is green chemistry?
Define green chemistry.
VTU 1BCHES102/202 | Module 5
Green Chemistry
05
Green chemistry
Green chemistry designs chemical products and processes that reduce or eliminate hazardous substances across their life cycle.
Safer design
Less waste
Low toxicity
Energy efficiency
Life cycle
Notes: What to say: Keep definition broad and link to every later topic.
Pause cue: pause after each process diagram and ask students what makes the method greener or more sustainable.
Pointing cue: point from source material to synthesis/property, then to application or waste-management outcome.
Question to ask students: Ask students to connect material property with smart-system use and environmental impact.
Animation instructions: Fade title; appear cards one by one; wipe process arrows in order; highlight keywords such as green solvent, glycerol trioleate, ZnO nanoparticles, RFID, IONT, PLA, PEG, alginate hydrogel, BCI, e-waste, AI and bioleaching word by word.
Transition style: Fade.
[Sources] VTU syllabus PDF 1BCHES102/202 Applied Chemistry for Smart Systems, Module 5 checklist, downloaded from https://vtu.ac.in/pdf/UG2024/1BCHES102.pdf; syllabus-listed textbooks: Engineering Chemistry, Suba Ramesh, Vairam, Ananda Murthy, Wiley India, 2011; A Textbook of Engineering Chemistry, R.V. Gadag and Nityananda Shetty, I.K. International, 2nd ed., 2016; Engineering Chemistry, Jain & Jain, Dhanpat Rai; Wiley Engineering Chemistry, Wiley India, 2013; syllabus-listed references for green/biomaterial/e-waste background include Green Chemistry and Engineering: A Practical Design Approach, Concepción Jiménez-González and David J.C. Constable, Wiley, 2011; E-Waste: Implications, Regulations, and Management in India and Current Global Best Practices, Rakesh Johri, TERI, 2008.

## Slide 6
Green chemistry design goals
Explain the purpose.
VTU 1BCHES102/202 | Module 5
Green Chemistry
06
Prevent waste
Avoid waste generation instead of treating waste later.
Safer materials
Choose less toxic solvents, reagents and products.
Energy efficiency
Prefer processes that use lower energy and mild conditions.
Renewable feedstocks
Use bio-based or recyclable sources where possible.
Notes: What to say: Make this an exam-ready point list.
Pause cue: pause after each process diagram and ask students what makes the method greener or more sustainable.
Pointing cue: point from source material to synthesis/property, then to application or waste-management outcome.
Question to ask students: Ask students to connect material property with smart-system use and environmental impact.
Animation instructions: Fade title; appear cards one by one; wipe process arrows in order; highlight keywords such as green solvent, glycerol trioleate, ZnO nanoparticles, RFID, IONT, PLA, PEG, alginate hydrogel, BCI, e-waste, AI and bioleaching word by word.
Transition style: Fade.
[Sources] VTU syllabus PDF 1BCHES102/202 Applied Chemistry for Smart Systems, Module 5 checklist, downloaded from https://vtu.ac.in/pdf/UG2024/1BCHES102.pdf; syllabus-listed textbooks: Engineering Chemistry, Suba Ramesh, Vairam, Ananda Murthy, Wiley India, 2011; A Textbook of Engineering Chemistry, R.V. Gadag and Nityananda Shetty, I.K. International, 2nd ed., 2016; Engineering Chemistry, Jain & Jain, Dhanpat Rai; Wiley Engineering Chemistry, Wiley India, 2013; syllabus-listed references for green/biomaterial/e-waste background include Green Chemistry and Engineering: A Practical Design Approach, Concepción Jiménez-González and David J.C. Constable, Wiley, 2011; E-Waste: Implications, Regulations, and Management in India and Current Global Best Practices, Rakesh Johri, TERI, 2008.

## Slide 7
What is a green solvent?
Define green solvents.
VTU 1BCHES102/202 | Module 5
Green Solvents
07
Green solvent
A green solvent performs the solvent function with lower toxicity, lower environmental persistence and improved safety compared with conventional hazardous solvents.
Low toxicity
Low volatility
Recyclable
Biodegradable
Safer handling
Notes: What to say: Explain that no solvent is automatically green; context matters.
Pause cue: pause after each process diagram and ask students what makes the method greener or more sustainable.
Pointing cue: point from source material to synthesis/property, then to application or waste-management outcome.
Question to ask students: Ask students to connect material property with smart-system use and environmental impact.
Animation instructions: Fade title; appear cards one by one; wipe process arrows in order; highlight keywords such as green solvent, glycerol trioleate, ZnO nanoparticles, RFID, IONT, PLA, PEG, alginate hydrogel, BCI, e-waste, AI and bioleaching word by word.
Transition style: Fade.
[Sources] VTU syllabus PDF 1BCHES102/202 Applied Chemistry for Smart Systems, Module 5 checklist, downloaded from https://vtu.ac.in/pdf/UG2024/1BCHES102.pdf; syllabus-listed textbooks: Engineering Chemistry, Suba Ramesh, Vairam, Ananda Murthy, Wiley India, 2011; A Textbook of Engineering Chemistry, R.V. Gadag and Nityananda Shetty, I.K. International, 2nd ed., 2016; Engineering Chemistry, Jain & Jain, Dhanpat Rai; Wiley Engineering Chemistry, Wiley India, 2013; syllabus-listed references for green/biomaterial/e-waste background include Green Chemistry and Engineering: A Practical Design Approach, Concepción Jiménez-González and David J.C. Constable, Wiley, 2011; E-Waste: Implications, Regulations, and Management in India and Current Global Best Practices, Rakesh Johri, TERI, 2008.

## Slide 8
Properties of green solvents
List required properties.
VTU 1BCHES102/202 | Module 5
Green Solvents
08
Low toxicity
Reduces risk to workers and environment.
Thermal stability
Important for heat-transfer applications.
Low volatility
Reduces vapor emissions and fire risk.
Reusability
Supports recycling and lower operating waste.
Notes: What to say: Connect properties to server heat management.
Pause cue: pause after each process diagram and ask students what makes the method greener or more sustainable.
Pointing cue: point from source material to synthesis/property, then to application or waste-management outcome.
Question to ask students: Ask students to connect material property with smart-system use and environmental impact.
Animation instructions: Fade title; appear cards one by one; wipe process arrows in order; highlight keywords such as green solvent, glycerol trioleate, ZnO nanoparticles, RFID, IONT, PLA, PEG, alginate hydrogel, BCI, e-waste, AI and bioleaching word by word.
Transition style: Fade.
[Sources] VTU syllabus PDF 1BCHES102/202 Applied Chemistry for Smart Systems, Module 5 checklist, downloaded from https://vtu.ac.in/pdf/UG2024/1BCHES102.pdf; syllabus-listed textbooks: Engineering Chemistry, Suba Ramesh, Vairam, Ananda Murthy, Wiley India, 2011; A Textbook of Engineering Chemistry, R.V. Gadag and Nityananda Shetty, I.K. International, 2nd ed., 2016; Engineering Chemistry, Jain & Jain, Dhanpat Rai; Wiley Engineering Chemistry, Wiley India, 2013; syllabus-listed references for green/biomaterial/e-waste background include Green Chemistry and Engineering: A Practical Design Approach, Concepción Jiménez-González and David J.C. Constable, Wiley, 2011; E-Waste: Implications, Regulations, and Management in India and Current Global Best Practices, Rakesh Johri, TERI, 2008.

## Slide 9
Green solvents for server heat management
Explain the application.
VTU 1BCHES102/202 | Module 5
Green Solvents
09
Server heat management
Green solvents or cooling fluids can absorb and transfer heat in electronics or data-center cooling systems while reducing hazard, flammability and environmental burden.
Heat generated
Green coolant absorbs heat
Heat is transported
Heat is rejected safely
Coolant is reused
Notes: What to say: Relate to data centers and high-performance computing.
Pause cue: pause after each process diagram and ask students what makes the method greener or more sustainable.
Pointing cue: point from source material to synthesis/property, then to application or waste-management outcome.
Question to ask students: Ask students to connect material property with smart-system use and environmental impact.
Animation instructions: Fade title; appear cards one by one; wipe process arrows in order; highlight keywords such as green solvent, glycerol trioleate, ZnO nanoparticles, RFID, IONT, PLA, PEG, alginate hydrogel, BCI, e-waste, AI and bioleaching word by word.
Transition style: Fade.
[Sources] VTU syllabus PDF 1BCHES102/202 Applied Chemistry for Smart Systems, Module 5 checklist, downloaded from https://vtu.ac.in/pdf/UG2024/1BCHES102.pdf; syllabus-listed textbooks: Engineering Chemistry, Suba Ramesh, Vairam, Ananda Murthy, Wiley India, 2011; A Textbook of Engineering Chemistry, R.V. Gadag and Nityananda Shetty, I.K. International, 2nd ed., 2016; Engineering Chemistry, Jain & Jain, Dhanpat Rai; Wiley Engineering Chemistry, Wiley India, 2013; syllabus-listed references for green/biomaterial/e-waste background include Green Chemistry and Engineering: A Practical Design Approach, Concepción Jiménez-González and David J.C. Constable, Wiley, 2011; E-Waste: Implications, Regulations, and Management in India and Current Global Best Practices, Rakesh Johri, TERI, 2008.

## Slide 10
Why server coolants need careful chemistry
Explain engineering constraints.
VTU 1BCHES102/202 | Module 5
Green Solvents
10
High heat capacity
Fluid should remove heat efficiently.
Chemical compatibility
Should not damage metals, polymers or seals.
Electrical safety
Coolants near electronics need low conductivity or proper isolation.
Environmental safety
Leaks, disposal and worker exposure must be manageable.
Notes: What to say: Ask students why water is not always enough near electronics.
Pause cue: pause after each process diagram and ask students what makes the method greener or more sustainable.
Pointing cue: point from source material to synthesis/property, then to application or waste-management outcome.
Question to ask students: Ask students to connect material property with smart-system use and environmental impact.
Animation instructions: Fade title; appear cards one by one; wipe process arrows in order; highlight keywords such as green solvent, glycerol trioleate, ZnO nanoparticles, RFID, IONT, PLA, PEG, alginate hydrogel, BCI, e-waste, AI and bioleaching word by word.
Transition style: Fade.
[Sources] VTU syllabus PDF 1BCHES102/202 Applied Chemistry for Smart Systems, Module 5 checklist, downloaded from https://vtu.ac.in/pdf/UG2024/1BCHES102.pdf; syllabus-listed textbooks: Engineering Chemistry, Suba Ramesh, Vairam, Ananda Murthy, Wiley India, 2011; A Textbook of Engineering Chemistry, R.V. Gadag and Nityananda Shetty, I.K. International, 2nd ed., 2016; Engineering Chemistry, Jain & Jain, Dhanpat Rai; Wiley Engineering Chemistry, Wiley India, 2013; syllabus-listed references for green/biomaterial/e-waste background include Green Chemistry and Engineering: A Practical Design Approach, Concepción Jiménez-González and David J.C. Constable, Wiley, 2011; E-Waste: Implications, Regulations, and Management in India and Current Global Best Practices, Rakesh Johri, TERI, 2008.

## Slide 11
What is glycerol trioleate ester?
Define the ester.
VTU 1BCHES102/202 | Module 5
Glycerol Trioleate
11
Glycerol trioleate
Glycerol trioleate is a triglyceride ester formed from glycerol and oleic acid; it is useful as a bio-based lubricant or heat-transfer material.
Glycerol
Oleic acid
Ester linkage
Bio-based
Lubricity
Notes: What to say: Introduce it as a green material from renewable-type chemistry.
Pause cue: pause after each process diagram and ask students what makes the method greener or more sustainable.
Pointing cue: point from source material to synthesis/property, then to application or waste-management outcome.
Question to ask students: Ask students to connect material property with smart-system use and environmental impact.
Animation instructions: Fade title; appear cards one by one; wipe process arrows in order; highlight keywords such as green solvent, glycerol trioleate, ZnO nanoparticles, RFID, IONT, PLA, PEG, alginate hydrogel, BCI, e-waste, AI and bioleaching word by word.
Transition style: Fade.
[Sources] VTU syllabus PDF 1BCHES102/202 Applied Chemistry for Smart Systems, Module 5 checklist, downloaded from https://vtu.ac.in/pdf/UG2024/1BCHES102.pdf; syllabus-listed textbooks: Engineering Chemistry, Suba Ramesh, Vairam, Ananda Murthy, Wiley India, 2011; A Textbook of Engineering Chemistry, R.V. Gadag and Nityananda Shetty, I.K. International, 2nd ed., 2016; Engineering Chemistry, Jain & Jain, Dhanpat Rai; Wiley Engineering Chemistry, Wiley India, 2013; syllabus-listed references for green/biomaterial/e-waste background include Green Chemistry and Engineering: A Practical Design Approach, Concepción Jiménez-González and David J.C. Constable, Wiley, 2011; E-Waste: Implications, Regulations, and Management in India and Current Global Best Practices, Rakesh Johri, TERI, 2008.

## Slide 12
Synthesis of glycerol trioleate
Show esterification route.
VTU 1BCHES102/202 | Module 5
Glycerol Trioleate
12
Ester synthesis
Glycerol reacts with oleic acid through esterification to form glycerol trioleate and water, usually with a catalyst and controlled heating.
Glycerol
Oleic acid
Esterification
Remove water
Glycerol trioleate
Notes: What to say: Point out three hydroxyl groups form three ester linkages.
Pause cue: pause after each process diagram and ask students what makes the method greener or more sustainable.
Pointing cue: point from source material to synthesis/property, then to application or waste-management outcome.
Question to ask students: Ask students to connect material property with smart-system use and environmental impact.
Animation instructions: Fade title; appear cards one by one; wipe process arrows in order; highlight keywords such as green solvent, glycerol trioleate, ZnO nanoparticles, RFID, IONT, PLA, PEG, alginate hydrogel, BCI, e-waste, AI and bioleaching word by word.
Transition style: Fade.
[Sources] VTU syllabus PDF 1BCHES102/202 Applied Chemistry for Smart Systems, Module 5 checklist, downloaded from https://vtu.ac.in/pdf/UG2024/1BCHES102.pdf; syllabus-listed textbooks: Engineering Chemistry, Suba Ramesh, Vairam, Ananda Murthy, Wiley India, 2011; A Textbook of Engineering Chemistry, R.V. Gadag and Nityananda Shetty, I.K. International, 2nd ed., 2016; Engineering Chemistry, Jain & Jain, Dhanpat Rai; Wiley Engineering Chemistry, Wiley India, 2013; syllabus-listed references for green/biomaterial/e-waste background include Green Chemistry and Engineering: A Practical Design Approach, Concepción Jiménez-González and David J.C. Constable, Wiley, 2011; E-Waste: Implications, Regulations, and Management in India and Current Global Best Practices, Rakesh Johri, TERI, 2008.

## Slide 13
Properties of glycerol trioleate
Explain why it is useful.
VTU 1BCHES102/202 | Module 5
Glycerol Trioleate
13
Biodegradability potential
Ester-based materials can be more environmentally acceptable.
Lubricating behavior
Long hydrocarbon chains reduce friction.
Thermal usefulness
Can help in heat-transfer or coolant-type roles.
Low volatility tendency
Large ester molecules generally evaporate less easily than light solvents.
Notes: What to say: Tie each property to infrastructure use.
Pause cue: pause after each process diagram and ask students what makes the method greener or more sustainable.
Pointing cue: point from source material to synthesis/property, then to application or waste-management outcome.
Question to ask students: Ask students to connect material property with smart-system use and environmental impact.
Animation instructions: Fade title; appear cards one by one; wipe process arrows in order; highlight keywords such as green solvent, glycerol trioleate, ZnO nanoparticles, RFID, IONT, PLA, PEG, alginate hydrogel, BCI, e-waste, AI and bioleaching word by word.
Transition style: Fade.
[Sources] VTU syllabus PDF 1BCHES102/202 Applied Chemistry for Smart Systems, Module 5 checklist, downloaded from https://vtu.ac.in/pdf/UG2024/1BCHES102.pdf; syllabus-listed textbooks: Engineering Chemistry, Suba Ramesh, Vairam, Ananda Murthy, Wiley India, 2011; A Textbook of Engineering Chemistry, R.V. Gadag and Nityananda Shetty, I.K. International, 2nd ed., 2016; Engineering Chemistry, Jain & Jain, Dhanpat Rai; Wiley Engineering Chemistry, Wiley India, 2013; syllabus-listed references for green/biomaterial/e-waste background include Green Chemistry and Engineering: A Practical Design Approach, Concepción Jiménez-González and David J.C. Constable, Wiley, 2011; E-Waste: Implications, Regulations, and Management in India and Current Global Best Practices, Rakesh Johri, TERI, 2008.

## Slide 14
Uses in IT infrastructure
Explain applications.
VTU 1BCHES102/202 | Module 5
Glycerol Trioleate
14
Cooling fluids
Can be considered in thermal-management fluid design.
Lubrication
Useful for moving parts in support equipment.
Insulation support
Non-aqueous fluids may help where water is unsuitable.
Sustainable operations
Bio-based materials can reduce dependence on petroleum-derived fluids.
Notes: What to say: Keep the language careful and application-oriented.
Pause cue: pause after each process diagram and ask students what makes the method greener or more sustainable.
Pointing cue: point from source material to synthesis/property, then to application or waste-management outcome.
Question to ask students: Ask students to connect material property with smart-system use and environmental impact.
Animation instructions: Fade title; appear cards one by one; wipe process arrows in order; highlight keywords such as green solvent, glycerol trioleate, ZnO nanoparticles, RFID, IONT, PLA, PEG, alginate hydrogel, BCI, e-waste, AI and bioleaching word by word.
Transition style: Fade.
[Sources] VTU syllabus PDF 1BCHES102/202 Applied Chemistry for Smart Systems, Module 5 checklist, downloaded from https://vtu.ac.in/pdf/UG2024/1BCHES102.pdf; syllabus-listed textbooks: Engineering Chemistry, Suba Ramesh, Vairam, Ananda Murthy, Wiley India, 2011; A Textbook of Engineering Chemistry, R.V. Gadag and Nityananda Shetty, I.K. International, 2nd ed., 2016; Engineering Chemistry, Jain & Jain, Dhanpat Rai; Wiley Engineering Chemistry, Wiley India, 2013; syllabus-listed references for green/biomaterial/e-waste background include Green Chemistry and Engineering: A Practical Design Approach, Concepción Jiménez-González and David J.C. Constable, Wiley, 2011; E-Waste: Implications, Regulations, and Management in India and Current Global Best Practices, Rakesh Johri, TERI, 2008.

## Slide 15
What are ZnO nanoparticles?
Define ZnO nanoparticles.
VTU 1BCHES102/202 | Module 5
ZnO Nanoparticles
15
ZnO nanoparticles
Zinc oxide nanoparticles are nanoscale ZnO particles with semiconductor, optical and surface properties useful in sensing and smart-device applications.
ZnO
Nanoparticle
Semiconductor
Surface activity
Smart systems
Notes: What to say: Connect to RFID and Internet of Nano Things.
Pause cue: pause after each process diagram and ask students what makes the method greener or more sustainable.
Pointing cue: point from source material to synthesis/property, then to application or waste-management outcome.
Question to ask students: Ask students to connect material property with smart-system use and environmental impact.
Animation instructions: Fade title; appear cards one by one; wipe process arrows in order; highlight keywords such as green solvent, glycerol trioleate, ZnO nanoparticles, RFID, IONT, PLA, PEG, alginate hydrogel, BCI, e-waste, AI and bioleaching word by word.
Transition style: Fade.
[Sources] VTU syllabus PDF 1BCHES102/202 Applied Chemistry for Smart Systems, Module 5 checklist, downloaded from https://vtu.ac.in/pdf/UG2024/1BCHES102.pdf; syllabus-listed textbooks: Engineering Chemistry, Suba Ramesh, Vairam, Ananda Murthy, Wiley India, 2011; A Textbook of Engineering Chemistry, R.V. Gadag and Nityananda Shetty, I.K. International, 2nd ed., 2016; Engineering Chemistry, Jain & Jain, Dhanpat Rai; Wiley Engineering Chemistry, Wiley India, 2013; syllabus-listed references for green/biomaterial/e-waste background include Green Chemistry and Engineering: A Practical Design Approach, Concepción Jiménez-González and David J.C. Constable, Wiley, 2011; E-Waste: Implications, Regulations, and Management in India and Current Global Best Practices, Rakesh Johri, TERI, 2008.

## Slide 16
Why green synthesis of ZnO is preferred
Explain the greener route need.
VTU 1BCHES102/202 | Module 5
ZnO Nanoparticles
16
Lower hazard
Avoids harsh reducing and stabilizing chemicals where possible.
Biological resources
Plant extracts or biomolecules can act as reducing/capping agents.
Mild conditions
Often aims for simpler temperature and solvent conditions.
Sustainable scaling
Reduces solvent and reagent burden in nanoparticle preparation.
Notes: What to say: Tell students green synthesis is about reducing process hazard.
Pause cue: pause after each process diagram and ask students what makes the method greener or more sustainable.
Pointing cue: point from source material to synthesis/property, then to application or waste-management outcome.
Question to ask students: Ask students to connect material property with smart-system use and environmental impact.
Animation instructions: Fade title; appear cards one by one; wipe process arrows in order; highlight keywords such as green solvent, glycerol trioleate, ZnO nanoparticles, RFID, IONT, PLA, PEG, alginate hydrogel, BCI, e-waste, AI and bioleaching word by word.
Transition style: Fade.
[Sources] VTU syllabus PDF 1BCHES102/202 Applied Chemistry for Smart Systems, Module 5 checklist, downloaded from https://vtu.ac.in/pdf/UG2024/1BCHES102.pdf; syllabus-listed textbooks: Engineering Chemistry, Suba Ramesh, Vairam, Ananda Murthy, Wiley India, 2011; A Textbook of Engineering Chemistry, R.V. Gadag and Nityananda Shetty, I.K. International, 2nd ed., 2016; Engineering Chemistry, Jain & Jain, Dhanpat Rai; Wiley Engineering Chemistry, Wiley India, 2013; syllabus-listed references for green/biomaterial/e-waste background include Green Chemistry and Engineering: A Practical Design Approach, Concepción Jiménez-González and David J.C. Constable, Wiley, 2011; E-Waste: Implications, Regulations, and Management in India and Current Global Best Practices, Rakesh Johri, TERI, 2008.

## Slide 17
Green synthesis of ZnO nanoparticles
Show process.
VTU 1BCHES102/202 | Module 5
ZnO Nanoparticles
17
Green ZnO synthesis
A zinc precursor is combined with a green reducing/capping medium such as plant extract, then precipitated, dried and calcined to obtain ZnO nanoparticles.
Zinc precursor
Plant extract / green medium
Precipitation
Drying / calcination
ZnO nanoparticles
Notes: What to say: Use this as the synthesis answer framework.
Pause cue: pause after each process diagram and ask students what makes the method greener or more sustainable.
Pointing cue: point from source material to synthesis/property, then to application or waste-management outcome.
Question to ask students: Ask students to connect material property with smart-system use and environmental impact.
Animation instructions: Fade title; appear cards one by one; wipe process arrows in order; highlight keywords such as green solvent, glycerol trioleate, ZnO nanoparticles, RFID, IONT, PLA, PEG, alginate hydrogel, BCI, e-waste, AI and bioleaching word by word.
Transition style: Fade.
[Sources] VTU syllabus PDF 1BCHES102/202 Applied Chemistry for Smart Systems, Module 5 checklist, downloaded from https://vtu.ac.in/pdf/UG2024/1BCHES102.pdf; syllabus-listed textbooks: Engineering Chemistry, Suba Ramesh, Vairam, Ananda Murthy, Wiley India, 2011; A Textbook of Engineering Chemistry, R.V. Gadag and Nityananda Shetty, I.K. International, 2nd ed., 2016; Engineering Chemistry, Jain & Jain, Dhanpat Rai; Wiley Engineering Chemistry, Wiley India, 2013; syllabus-listed references for green/biomaterial/e-waste background include Green Chemistry and Engineering: A Practical Design Approach, Concepción Jiménez-González and David J.C. Constable, Wiley, 2011; E-Waste: Implications, Regulations, and Management in India and Current Global Best Practices, Rakesh Johri, TERI, 2008.

## Slide 18
Properties of ZnO nanoparticles
Explain useful properties.
VTU 1BCHES102/202 | Module 5
ZnO Nanoparticles
18
Semiconducting nature
Useful in electronic and sensing devices.
Optical response
ZnO can interact with UV/visible light.
High surface area
Improves interaction with analytes or environments.
Chemical stability
Useful for device and coating applications.
Notes: What to say: Relate nanoscale size to surface area.
Pause cue: pause after each process diagram and ask students what makes the method greener or more sustainable.
Pointing cue: point from source material to synthesis/property, then to application or waste-management outcome.
Question to ask students: Ask students to connect material property with smart-system use and environmental impact.
Animation instructions: Fade title; appear cards one by one; wipe process arrows in order; highlight keywords such as green solvent, glycerol trioleate, ZnO nanoparticles, RFID, IONT, PLA, PEG, alginate hydrogel, BCI, e-waste, AI and bioleaching word by word.
Transition style: Fade.
[Sources] VTU syllabus PDF 1BCHES102/202 Applied Chemistry for Smart Systems, Module 5 checklist, downloaded from https://vtu.ac.in/pdf/UG2024/1BCHES102.pdf; syllabus-listed textbooks: Engineering Chemistry, Suba Ramesh, Vairam, Ananda Murthy, Wiley India, 2011; A Textbook of Engineering Chemistry, R.V. Gadag and Nityananda Shetty, I.K. International, 2nd ed., 2016; Engineering Chemistry, Jain & Jain, Dhanpat Rai; Wiley Engineering Chemistry, Wiley India, 2013; syllabus-listed references for green/biomaterial/e-waste background include Green Chemistry and Engineering: A Practical Design Approach, Concepción Jiménez-González and David J.C. Constable, Wiley, 2011; E-Waste: Implications, Regulations, and Management in India and Current Global Best Practices, Rakesh Johri, TERI, 2008.

## Slide 19
ZnO in magnetic RFID applications
Explain RFID link.
VTU 1BCHES102/202 | Module 5
ZnO Nanoparticles
19
RFID application
ZnO nanoparticles can support functional coatings, sensing layers or nanocomposite materials used around RFID tags and smart identification systems.
RFID tag
Functional ZnO layer
Signal / sensing response
Data identification
Smart tracking
Notes: What to say: Keep RFID connection at syllabus level without overclaiming magnetism details.
Pause cue: pause after each process diagram and ask students what makes the method greener or more sustainable.
Pointing cue: point from source material to synthesis/property, then to application or waste-management outcome.
Question to ask students: Ask students to connect material property with smart-system use and environmental impact.
Animation instructions: Fade title; appear cards one by one; wipe process arrows in order; highlight keywords such as green solvent, glycerol trioleate, ZnO nanoparticles, RFID, IONT, PLA, PEG, alginate hydrogel, BCI, e-waste, AI and bioleaching word by word.
Transition style: Fade.
[Sources] VTU syllabus PDF 1BCHES102/202 Applied Chemistry for Smart Systems, Module 5 checklist, downloaded from https://vtu.ac.in/pdf/UG2024/1BCHES102.pdf; syllabus-listed textbooks: Engineering Chemistry, Suba Ramesh, Vairam, Ananda Murthy, Wiley India, 2011; A Textbook of Engineering Chemistry, R.V. Gadag and Nityananda Shetty, I.K. International, 2nd ed., 2016; Engineering Chemistry, Jain & Jain, Dhanpat Rai; Wiley Engineering Chemistry, Wiley India, 2013; syllabus-listed references for green/biomaterial/e-waste background include Green Chemistry and Engineering: A Practical Design Approach, Concepción Jiménez-González and David J.C. Constable, Wiley, 2011; E-Waste: Implications, Regulations, and Management in India and Current Global Best Practices, Rakesh Johri, TERI, 2008.

## Slide 20
ZnO in Internet of Nano Things
Explain IONT application.
VTU 1BCHES102/202 | Module 5
ZnO Nanoparticles
20
Nano-sensing nodes
ZnO surfaces can help detect chemical or environmental changes.
Miniaturized systems
Nanoparticles fit small-scale device architectures.
Smart communication
Sensor output can feed connected nano/IoT networks.
Environmental monitoring
Useful for distributed sensing concepts.
Notes: What to say: Define IONT as connected nanoscale sensing/actuating systems.
Pause cue: pause after each process diagram and ask students what makes the method greener or more sustainable.
Pointing cue: point from source material to synthesis/property, then to application or waste-management outcome.
Question to ask students: Ask students to connect material property with smart-system use and environmental impact.
Animation instructions: Fade title; appear cards one by one; wipe process arrows in order; highlight keywords such as green solvent, glycerol trioleate, ZnO nanoparticles, RFID, IONT, PLA, PEG, alginate hydrogel, BCI, e-waste, AI and bioleaching word by word.
Transition style: Fade.
[Sources] VTU syllabus PDF 1BCHES102/202 Applied Chemistry for Smart Systems, Module 5 checklist, downloaded from https://vtu.ac.in/pdf/UG2024/1BCHES102.pdf; syllabus-listed textbooks: Engineering Chemistry, Suba Ramesh, Vairam, Ananda Murthy, Wiley India, 2011; A Textbook of Engineering Chemistry, R.V. Gadag and Nityananda Shetty, I.K. International, 2nd ed., 2016; Engineering Chemistry, Jain & Jain, Dhanpat Rai; Wiley Engineering Chemistry, Wiley India, 2013; syllabus-listed references for green/biomaterial/e-waste background include Green Chemistry and Engineering: A Practical Design Approach, Concepción Jiménez-González and David J.C. Constable, Wiley, 2011; E-Waste: Implications, Regulations, and Management in India and Current Global Best Practices, Rakesh Johri, TERI, 2008.

## Slide 21
Green materials comparison
Separate the three green-chemistry materials.
VTU 1BCHES102/202 | Module 5
Green Materials
21
Material
Key property
Smart-system use
Green solvents
Safer cooling/processing medium
Server heat management
Glycerol trioleate
Bio-based ester, lubrication/thermal role
IT infrastructure fluids
ZnO nanoparticles
Semiconductor nanosurface properties
RFID and IONT systems
Notes: What to say: Use this as checkpoint revision before biomaterials.
Pause cue: pause after each process diagram and ask students what makes the method greener or more sustainable.
Pointing cue: point from source material to synthesis/property, then to application or waste-management outcome.
Question to ask students: Ask students to connect material property with smart-system use and environmental impact.
Animation instructions: Fade title; appear cards one by one; wipe process arrows in order; highlight keywords such as green solvent, glycerol trioleate, ZnO nanoparticles, RFID, IONT, PLA, PEG, alginate hydrogel, BCI, e-waste, AI and bioleaching word by word.
Transition style: Fade.
[Sources] VTU syllabus PDF 1BCHES102/202 Applied Chemistry for Smart Systems, Module 5 checklist, downloaded from https://vtu.ac.in/pdf/UG2024/1BCHES102.pdf; syllabus-listed textbooks: Engineering Chemistry, Suba Ramesh, Vairam, Ananda Murthy, Wiley India, 2011; A Textbook of Engineering Chemistry, R.V. Gadag and Nityananda Shetty, I.K. International, 2nd ed., 2016; Engineering Chemistry, Jain & Jain, Dhanpat Rai; Wiley Engineering Chemistry, Wiley India, 2013; syllabus-listed references for green/biomaterial/e-waste background include Green Chemistry and Engineering: A Practical Design Approach, Concepción Jiménez-González and David J.C. Constable, Wiley, 2011; E-Waste: Implications, Regulations, and Management in India and Current Global Best Practices, Rakesh Johri, TERI, 2008.

## Slide 22
What is a biomaterial?
Define biomaterial.
VTU 1BCHES102/202 | Module 5
Biomaterials
22
Biomaterial
A biomaterial is a material designed to interact with biological systems for a medical, sensing, interface or device-related purpose.
Biocompatibility
Biological interaction
Device use
Polymer
Interface
Notes: What to say: Introduce PLA, PEG and alginate hydrogel.
Pause cue: pause after each process diagram and ask students what makes the method greener or more sustainable.
Pointing cue: point from source material to synthesis/property, then to application or waste-management outcome.
Question to ask students: Ask students to connect material property with smart-system use and environmental impact.
Animation instructions: Fade title; appear cards one by one; wipe process arrows in order; highlight keywords such as green solvent, glycerol trioleate, ZnO nanoparticles, RFID, IONT, PLA, PEG, alginate hydrogel, BCI, e-waste, AI and bioleaching word by word.
Transition style: Fade.
[Sources] VTU syllabus PDF 1BCHES102/202 Applied Chemistry for Smart Systems, Module 5 checklist, downloaded from https://vtu.ac.in/pdf/UG2024/1BCHES102.pdf; syllabus-listed textbooks: Engineering Chemistry, Suba Ramesh, Vairam, Ananda Murthy, Wiley India, 2011; A Textbook of Engineering Chemistry, R.V. Gadag and Nityananda Shetty, I.K. International, 2nd ed., 2016; Engineering Chemistry, Jain & Jain, Dhanpat Rai; Wiley Engineering Chemistry, Wiley India, 2013; syllabus-listed references for green/biomaterial/e-waste background include Green Chemistry and Engineering: A Practical Design Approach, Concepción Jiménez-González and David J.C. Constable, Wiley, 2011; E-Waste: Implications, Regulations, and Management in India and Current Global Best Practices, Rakesh Johri, TERI, 2008.

## Slide 23
Why biomaterials matter in smart systems
Explain application need.
VTU 1BCHES102/202 | Module 5
Biomaterials
23
Touch screens
Need transparent, flexible and surface-compatible materials.
Wearables
Need skin-contact materials with low irritation.
Medical interfaces
Need materials that work safely near tissues or biofluids.
BCIs
Need soft, hydrated and interface-friendly materials.
Notes: What to say: Relate biomaterials to human-device interaction.
Pause cue: pause after each process diagram and ask students what makes the method greener or more sustainable.
Pointing cue: point from source material to synthesis/property, then to application or waste-management outcome.
Question to ask students: Ask students to connect material property with smart-system use and environmental impact.
Animation instructions: Fade title; appear cards one by one; wipe process arrows in order; highlight keywords such as green solvent, glycerol trioleate, ZnO nanoparticles, RFID, IONT, PLA, PEG, alginate hydrogel, BCI, e-waste, AI and bioleaching word by word.
Transition style: Fade.
[Sources] VTU syllabus PDF 1BCHES102/202 Applied Chemistry for Smart Systems, Module 5 checklist, downloaded from https://vtu.ac.in/pdf/UG2024/1BCHES102.pdf; syllabus-listed textbooks: Engineering Chemistry, Suba Ramesh, Vairam, Ananda Murthy, Wiley India, 2011; A Textbook of Engineering Chemistry, R.V. Gadag and Nityananda Shetty, I.K. International, 2nd ed., 2016; Engineering Chemistry, Jain & Jain, Dhanpat Rai; Wiley Engineering Chemistry, Wiley India, 2013; syllabus-listed references for green/biomaterial/e-waste background include Green Chemistry and Engineering: A Practical Design Approach, Concepción Jiménez-González and David J.C. Constable, Wiley, 2011; E-Waste: Implications, Regulations, and Management in India and Current Global Best Practices, Rakesh Johri, TERI, 2008.

## Slide 24
What is polylactic acid?
Define PLA.
VTU 1BCHES102/202 | Module 5
PLA
24
PLA
Polylactic acid is a biodegradable aliphatic polyester made from lactic acid or lactide, often obtained from renewable resources.
Lactic acid
Polyester
Biodegradable
Renewable source
Thermoplastic
Notes: What to say: Use packaging and biomedical polymers as familiar contexts.
Pause cue: pause after each process diagram and ask students what makes the method greener or more sustainable.
Pointing cue: point from source material to synthesis/property, then to application or waste-management outcome.
Question to ask students: Ask students to connect material property with smart-system use and environmental impact.
Animation instructions: Fade title; appear cards one by one; wipe process arrows in order; highlight keywords such as green solvent, glycerol trioleate, ZnO nanoparticles, RFID, IONT, PLA, PEG, alginate hydrogel, BCI, e-waste, AI and bioleaching word by word.
Transition style: Fade.
[Sources] VTU syllabus PDF 1BCHES102/202 Applied Chemistry for Smart Systems, Module 5 checklist, downloaded from https://vtu.ac.in/pdf/UG2024/1BCHES102.pdf; syllabus-listed textbooks: Engineering Chemistry, Suba Ramesh, Vairam, Ananda Murthy, Wiley India, 2011; A Textbook of Engineering Chemistry, R.V. Gadag and Nityananda Shetty, I.K. International, 2nd ed., 2016; Engineering Chemistry, Jain & Jain, Dhanpat Rai; Wiley Engineering Chemistry, Wiley India, 2013; syllabus-listed references for green/biomaterial/e-waste background include Green Chemistry and Engineering: A Practical Design Approach, Concepción Jiménez-González and David J.C. Constable, Wiley, 2011; E-Waste: Implications, Regulations, and Management in India and Current Global Best Practices, Rakesh Johri, TERI, 2008.

## Slide 25
Synthesis of PLA
Show synthesis route.
VTU 1BCHES102/202 | Module 5
PLA
25
PLA synthesis
PLA can be produced from lactic acid by condensation polymerization or through lactide formation followed by ring-opening polymerization.
Lactic acid
Lactide / oligomer
Polymerization
PLA chain
Processing into film
Notes: What to say: Mention ring-opening route gives better controlled polymer.
Pause cue: pause after each process diagram and ask students what makes the method greener or more sustainable.
Pointing cue: point from source material to synthesis/property, then to application or waste-management outcome.
Question to ask students: Ask students to connect material property with smart-system use and environmental impact.
Animation instructions: Fade title; appear cards one by one; wipe process arrows in order; highlight keywords such as green solvent, glycerol trioleate, ZnO nanoparticles, RFID, IONT, PLA, PEG, alginate hydrogel, BCI, e-waste, AI and bioleaching word by word.
Transition style: Fade.
[Sources] VTU syllabus PDF 1BCHES102/202 Applied Chemistry for Smart Systems, Module 5 checklist, downloaded from https://vtu.ac.in/pdf/UG2024/1BCHES102.pdf; syllabus-listed textbooks: Engineering Chemistry, Suba Ramesh, Vairam, Ananda Murthy, Wiley India, 2011; A Textbook of Engineering Chemistry, R.V. Gadag and Nityananda Shetty, I.K. International, 2nd ed., 2016; Engineering Chemistry, Jain & Jain, Dhanpat Rai; Wiley Engineering Chemistry, Wiley India, 2013; syllabus-listed references for green/biomaterial/e-waste background include Green Chemistry and Engineering: A Practical Design Approach, Concepción Jiménez-González and David J.C. Constable, Wiley, 2011; E-Waste: Implications, Regulations, and Management in India and Current Global Best Practices, Rakesh Johri, TERI, 2008.

## Slide 26
Properties of PLA
Explain properties.
VTU 1BCHES102/202 | Module 5
PLA
26
Biodegradable
Breaks down under suitable composting or biological conditions.
Transparent and glossy
Useful for films and display-related components.
Thermoplastic
Can be molded, extruded or printed.
Brittleness concern
Often blended or modified for toughness.
Notes: What to say: Connect property trade-offs to device design.
Pause cue: pause after each process diagram and ask students what makes the method greener or more sustainable.
Pointing cue: point from source material to synthesis/property, then to application or waste-management outcome.
Question to ask students: Ask students to connect material property with smart-system use and environmental impact.
Animation instructions: Fade title; appear cards one by one; wipe process arrows in order; highlight keywords such as green solvent, glycerol trioleate, ZnO nanoparticles, RFID, IONT, PLA, PEG, alginate hydrogel, BCI, e-waste, AI and bioleaching word by word.
Transition style: Fade.
[Sources] VTU syllabus PDF 1BCHES102/202 Applied Chemistry for Smart Systems, Module 5 checklist, downloaded from https://vtu.ac.in/pdf/UG2024/1BCHES102.pdf; syllabus-listed textbooks: Engineering Chemistry, Suba Ramesh, Vairam, Ananda Murthy, Wiley India, 2011; A Textbook of Engineering Chemistry, R.V. Gadag and Nityananda Shetty, I.K. International, 2nd ed., 2016; Engineering Chemistry, Jain & Jain, Dhanpat Rai; Wiley Engineering Chemistry, Wiley India, 2013; syllabus-listed references for green/biomaterial/e-waste background include Green Chemistry and Engineering: A Practical Design Approach, Concepción Jiménez-González and David J.C. Constable, Wiley, 2011; E-Waste: Implications, Regulations, and Management in India and Current Global Best Practices, Rakesh Johri, TERI, 2008.

## Slide 27
PLA uses in touch-screen applications
Explain application.
VTU 1BCHES102/202 | Module 5
PLA
27
Protective films
Transparent polymer films can protect display surfaces.
Flexible substrates
Light polymer sheets can support flexible device layers.
Biodegradable accessories
Potential for lower-impact screen-related components.
Design limitation
Thermal resistance and durability must match device conditions.
Notes: What to say: Keep it self-explanatory for students.
Pause cue: pause after each process diagram and ask students what makes the method greener or more sustainable.
Pointing cue: point from source material to synthesis/property, then to application or waste-management outcome.
Question to ask students: Ask students to connect material property with smart-system use and environmental impact.
Animation instructions: Fade title; appear cards one by one; wipe process arrows in order; highlight keywords such as green solvent, glycerol trioleate, ZnO nanoparticles, RFID, IONT, PLA, PEG, alginate hydrogel, BCI, e-waste, AI and bioleaching word by word.
Transition style: Fade.
[Sources] VTU syllabus PDF 1BCHES102/202 Applied Chemistry for Smart Systems, Module 5 checklist, downloaded from https://vtu.ac.in/pdf/UG2024/1BCHES102.pdf; syllabus-listed textbooks: Engineering Chemistry, Suba Ramesh, Vairam, Ananda Murthy, Wiley India, 2011; A Textbook of Engineering Chemistry, R.V. Gadag and Nityananda Shetty, I.K. International, 2nd ed., 2016; Engineering Chemistry, Jain & Jain, Dhanpat Rai; Wiley Engineering Chemistry, Wiley India, 2013; syllabus-listed references for green/biomaterial/e-waste background include Green Chemistry and Engineering: A Practical Design Approach, Concepción Jiménez-González and David J.C. Constable, Wiley, 2011; E-Waste: Implications, Regulations, and Management in India and Current Global Best Practices, Rakesh Johri, TERI, 2008.

## Slide 28
What is polyethylene glycol?
Define PEG.
VTU 1BCHES102/202 | Module 5
PEG
28
PEG
Polyethylene glycol is a water-soluble polyether available in different molecular weights, known for flexibility and biocompatibility.
Polyether
Water soluble
Flexible chain
Biocompatible
Molecular weight
Notes: What to say: Explain PEG properties change with chain length.
Pause cue: pause after each process diagram and ask students what makes the method greener or more sustainable.
Pointing cue: point from source material to synthesis/property, then to application or waste-management outcome.
Question to ask students: Ask students to connect material property with smart-system use and environmental impact.
Animation instructions: Fade title; appear cards one by one; wipe process arrows in order; highlight keywords such as green solvent, glycerol trioleate, ZnO nanoparticles, RFID, IONT, PLA, PEG, alginate hydrogel, BCI, e-waste, AI and bioleaching word by word.
Transition style: Fade.
[Sources] VTU syllabus PDF 1BCHES102/202 Applied Chemistry for Smart Systems, Module 5 checklist, downloaded from https://vtu.ac.in/pdf/UG2024/1BCHES102.pdf; syllabus-listed textbooks: Engineering Chemistry, Suba Ramesh, Vairam, Ananda Murthy, Wiley India, 2011; A Textbook of Engineering Chemistry, R.V. Gadag and Nityananda Shetty, I.K. International, 2nd ed., 2016; Engineering Chemistry, Jain & Jain, Dhanpat Rai; Wiley Engineering Chemistry, Wiley India, 2013; syllabus-listed references for green/biomaterial/e-waste background include Green Chemistry and Engineering: A Practical Design Approach, Concepción Jiménez-González and David J.C. Constable, Wiley, 2011; E-Waste: Implications, Regulations, and Management in India and Current Global Best Practices, Rakesh Johri, TERI, 2008.

## Slide 29
Synthesis of PEG
Show synthesis route.
VTU 1BCHES102/202 | Module 5
PEG
29
PEG synthesis
PEG is commonly prepared by polymerization of ethylene oxide under controlled conditions to obtain chains of required molecular weight.
Ethylene oxide
Initiator / catalyst
Chain growth
PEG polymer
Purification
Notes: What to say: Keep safety details out of scope, but mention controlled polymerization.
Pause cue: pause after each process diagram and ask students what makes the method greener or more sustainable.
Pointing cue: point from source material to synthesis/property, then to application or waste-management outcome.
Question to ask students: Ask students to connect material property with smart-system use and environmental impact.
Animation instructions: Fade title; appear cards one by one; wipe process arrows in order; highlight keywords such as green solvent, glycerol trioleate, ZnO nanoparticles, RFID, IONT, PLA, PEG, alginate hydrogel, BCI, e-waste, AI and bioleaching word by word.
Transition style: Fade.
[Sources] VTU syllabus PDF 1BCHES102/202 Applied Chemistry for Smart Systems, Module 5 checklist, downloaded from https://vtu.ac.in/pdf/UG2024/1BCHES102.pdf; syllabus-listed textbooks: Engineering Chemistry, Suba Ramesh, Vairam, Ananda Murthy, Wiley India, 2011; A Textbook of Engineering Chemistry, R.V. Gadag and Nityananda Shetty, I.K. International, 2nd ed., 2016; Engineering Chemistry, Jain & Jain, Dhanpat Rai; Wiley Engineering Chemistry, Wiley India, 2013; syllabus-listed references for green/biomaterial/e-waste background include Green Chemistry and Engineering: A Practical Design Approach, Concepción Jiménez-González and David J.C. Constable, Wiley, 2011; E-Waste: Implications, Regulations, and Management in India and Current Global Best Practices, Rakesh Johri, TERI, 2008.

## Slide 30
Properties of PEG
Explain useful properties.
VTU 1BCHES102/202 | Module 5
PEG
30
Hydrophilic
Attracts water and improves surface wetting.
Flexible
Soft polymer chains improve comfort and compatibility.
Biocompatible
Widely useful in biomedical and interface materials.
Tunable molecular weight
Liquid, waxy or solid behavior depends on chain length.
Notes: What to say: Ask students why water solubility matters for biointerfaces.
Pause cue: pause after each process diagram and ask students what makes the method greener or more sustainable.
Pointing cue: point from source material to synthesis/property, then to application or waste-management outcome.
Question to ask students: Ask students to connect material property with smart-system use and environmental impact.
Animation instructions: Fade title; appear cards one by one; wipe process arrows in order; highlight keywords such as green solvent, glycerol trioleate, ZnO nanoparticles, RFID, IONT, PLA, PEG, alginate hydrogel, BCI, e-waste, AI and bioleaching word by word.
Transition style: Fade.
[Sources] VTU syllabus PDF 1BCHES102/202 Applied Chemistry for Smart Systems, Module 5 checklist, downloaded from https://vtu.ac.in/pdf/UG2024/1BCHES102.pdf; syllabus-listed textbooks: Engineering Chemistry, Suba Ramesh, Vairam, Ananda Murthy, Wiley India, 2011; A Textbook of Engineering Chemistry, R.V. Gadag and Nityananda Shetty, I.K. International, 2nd ed., 2016; Engineering Chemistry, Jain & Jain, Dhanpat Rai; Wiley Engineering Chemistry, Wiley India, 2013; syllabus-listed references for green/biomaterial/e-waste background include Green Chemistry and Engineering: A Practical Design Approach, Concepción Jiménez-González and David J.C. Constable, Wiley, 2011; E-Waste: Implications, Regulations, and Management in India and Current Global Best Practices, Rakesh Johri, TERI, 2008.

## Slide 31
PEG uses in touch-screen applications
Explain touch-screen relevance.
VTU 1BCHES102/202 | Module 5
PEG
31
Surface coatings
Can improve wettability and user-interface feel.
Flexible films
Useful in soft or flexible polymer formulations.
Anti-fouling surfaces
Hydrophilic PEG-like layers can reduce unwanted adhesion.
Device compatibility
Useful where transparent, soft polymer interfaces are needed.
Notes: What to say: Frame as material role in smart screens.
Pause cue: pause after each process diagram and ask students what makes the method greener or more sustainable.
Pointing cue: point from source material to synthesis/property, then to application or waste-management outcome.
Question to ask students: Ask students to connect material property with smart-system use and environmental impact.
Animation instructions: Fade title; appear cards one by one; wipe process arrows in order; highlight keywords such as green solvent, glycerol trioleate, ZnO nanoparticles, RFID, IONT, PLA, PEG, alginate hydrogel, BCI, e-waste, AI and bioleaching word by word.
Transition style: Fade.
[Sources] VTU syllabus PDF 1BCHES102/202 Applied Chemistry for Smart Systems, Module 5 checklist, downloaded from https://vtu.ac.in/pdf/UG2024/1BCHES102.pdf; syllabus-listed textbooks: Engineering Chemistry, Suba Ramesh, Vairam, Ananda Murthy, Wiley India, 2011; A Textbook of Engineering Chemistry, R.V. Gadag and Nityananda Shetty, I.K. International, 2nd ed., 2016; Engineering Chemistry, Jain & Jain, Dhanpat Rai; Wiley Engineering Chemistry, Wiley India, 2013; syllabus-listed references for green/biomaterial/e-waste background include Green Chemistry and Engineering: A Practical Design Approach, Concepción Jiménez-González and David J.C. Constable, Wiley, 2011; E-Waste: Implications, Regulations, and Management in India and Current Global Best Practices, Rakesh Johri, TERI, 2008.

## Slide 32
PLA and PEG compared
Help students separate biomaterials.
VTU 1BCHES102/202 | Module 5
PLA and PEG
32
Point
PLA
PEG
Polymer type
Biodegradable polyester
Water-soluble polyether
Main strength
Rigid transparent thermoplastic
Flexible hydrophilic biocompatible polymer
Touch-screen link
Protective/film/substrate role
Coating/flexible interface role
Main limitation
Brittleness/heat sensitivity
Water sensitivity depending on design
Notes: What to say: Use this as a quick comparison.
Pause cue: pause after each process diagram and ask students what makes the method greener or more sustainable.
Pointing cue: point from source material to synthesis/property, then to application or waste-management outcome.
Question to ask students: Ask students to connect material property with smart-system use and environmental impact.
Animation instructions: Fade title; appear cards one by one; wipe process arrows in order; highlight keywords such as green solvent, glycerol trioleate, ZnO nanoparticles, RFID, IONT, PLA, PEG, alginate hydrogel, BCI, e-waste, AI and bioleaching word by word.
Transition style: Fade.
[Sources] VTU syllabus PDF 1BCHES102/202 Applied Chemistry for Smart Systems, Module 5 checklist, downloaded from https://vtu.ac.in/pdf/UG2024/1BCHES102.pdf; syllabus-listed textbooks: Engineering Chemistry, Suba Ramesh, Vairam, Ananda Murthy, Wiley India, 2011; A Textbook of Engineering Chemistry, R.V. Gadag and Nityananda Shetty, I.K. International, 2nd ed., 2016; Engineering Chemistry, Jain & Jain, Dhanpat Rai; Wiley Engineering Chemistry, Wiley India, 2013; syllabus-listed references for green/biomaterial/e-waste background include Green Chemistry and Engineering: A Practical Design Approach, Concepción Jiménez-González and David J.C. Constable, Wiley, 2011; E-Waste: Implications, Regulations, and Management in India and Current Global Best Practices, Rakesh Johri, TERI, 2008.

## Slide 33
What is alginate hydrogel?
Define alginate hydrogel.
VTU 1BCHES102/202 | Module 5
Alginate Hydrogel
33
Alginate hydrogel
Alginate hydrogel is a water-rich polymer network formed when alginate chains crosslink, commonly with calcium ions, to create a soft gel.
Alginate
Hydrogel
Crosslinking
Calcium ions
Water-rich network
Notes: What to say: Explain alginate comes from seaweed-derived polysaccharide.
Pause cue: pause after each process diagram and ask students what makes the method greener or more sustainable.
Pointing cue: point from source material to synthesis/property, then to application or waste-management outcome.
Question to ask students: Ask students to connect material property with smart-system use and environmental impact.
Animation instructions: Fade title; appear cards one by one; wipe process arrows in order; highlight keywords such as green solvent, glycerol trioleate, ZnO nanoparticles, RFID, IONT, PLA, PEG, alginate hydrogel, BCI, e-waste, AI and bioleaching word by word.
Transition style: Fade.
[Sources] VTU syllabus PDF 1BCHES102/202 Applied Chemistry for Smart Systems, Module 5 checklist, downloaded from https://vtu.ac.in/pdf/UG2024/1BCHES102.pdf; syllabus-listed textbooks: Engineering Chemistry, Suba Ramesh, Vairam, Ananda Murthy, Wiley India, 2011; A Textbook of Engineering Chemistry, R.V. Gadag and Nityananda Shetty, I.K. International, 2nd ed., 2016; Engineering Chemistry, Jain & Jain, Dhanpat Rai; Wiley Engineering Chemistry, Wiley India, 2013; syllabus-listed references for green/biomaterial/e-waste background include Green Chemistry and Engineering: A Practical Design Approach, Concepción Jiménez-González and David J.C. Constable, Wiley, 2011; E-Waste: Implications, Regulations, and Management in India and Current Global Best Practices, Rakesh Johri, TERI, 2008.

## Slide 34
Synthesis of alginate hydrogel
Show gelation route.
VTU 1BCHES102/202 | Module 5
Alginate Hydrogel
34
Alginate hydrogel synthesis
Sodium alginate solution is mixed with calcium ions, forming ionic crosslinks between alginate chains and producing a soft hydrogel network.
Sodium alginate solution
Add Ca2+ ions
Ionic crosslinks form
Gel network develops
Alginate hydrogel
Notes: What to say: Use egg-box model verbally if desired.
Pause cue: pause after each process diagram and ask students what makes the method greener or more sustainable.
Pointing cue: point from source material to synthesis/property, then to application or waste-management outcome.
Question to ask students: Ask students to connect material property with smart-system use and environmental impact.
Animation instructions: Fade title; appear cards one by one; wipe process arrows in order; highlight keywords such as green solvent, glycerol trioleate, ZnO nanoparticles, RFID, IONT, PLA, PEG, alginate hydrogel, BCI, e-waste, AI and bioleaching word by word.
Transition style: Fade.
[Sources] VTU syllabus PDF 1BCHES102/202 Applied Chemistry for Smart Systems, Module 5 checklist, downloaded from https://vtu.ac.in/pdf/UG2024/1BCHES102.pdf; syllabus-listed textbooks: Engineering Chemistry, Suba Ramesh, Vairam, Ananda Murthy, Wiley India, 2011; A Textbook of Engineering Chemistry, R.V. Gadag and Nityananda Shetty, I.K. International, 2nd ed., 2016; Engineering Chemistry, Jain & Jain, Dhanpat Rai; Wiley Engineering Chemistry, Wiley India, 2013; syllabus-listed references for green/biomaterial/e-waste background include Green Chemistry and Engineering: A Practical Design Approach, Concepción Jiménez-González and David J.C. Constable, Wiley, 2011; E-Waste: Implications, Regulations, and Management in India and Current Global Best Practices, Rakesh Johri, TERI, 2008.

## Slide 35
Properties of alginate hydrogel
Explain properties.
VTU 1BCHES102/202 | Module 5
Alginate Hydrogel
35
High water content
Mimics soft hydrated biological environments.
Biocompatibility
Useful near cells, tissues and biointerfaces.
Soft mechanics
Can match flexible biological surfaces better than hard plastics.
Ion-responsive gelation
Crosslinking can be controlled through calcium concentration.
Notes: What to say: Relate softness to brain-interface applications.
Pause cue: pause after each process diagram and ask students what makes the method greener or more sustainable.
Pointing cue: point from source material to synthesis/property, then to application or waste-management outcome.
Question to ask students: Ask students to connect material property with smart-system use and environmental impact.
Animation instructions: Fade title; appear cards one by one; wipe process arrows in order; highlight keywords such as green solvent, glycerol trioleate, ZnO nanoparticles, RFID, IONT, PLA, PEG, alginate hydrogel, BCI, e-waste, AI and bioleaching word by word.
Transition style: Fade.
[Sources] VTU syllabus PDF 1BCHES102/202 Applied Chemistry for Smart Systems, Module 5 checklist, downloaded from https://vtu.ac.in/pdf/UG2024/1BCHES102.pdf; syllabus-listed textbooks: Engineering Chemistry, Suba Ramesh, Vairam, Ananda Murthy, Wiley India, 2011; A Textbook of Engineering Chemistry, R.V. Gadag and Nityananda Shetty, I.K. International, 2nd ed., 2016; Engineering Chemistry, Jain & Jain, Dhanpat Rai; Wiley Engineering Chemistry, Wiley India, 2013; syllabus-listed references for green/biomaterial/e-waste background include Green Chemistry and Engineering: A Practical Design Approach, Concepción Jiménez-González and David J.C. Constable, Wiley, 2011; E-Waste: Implications, Regulations, and Management in India and Current Global Best Practices, Rakesh Johri, TERI, 2008.

## Slide 36
Alginate hydrogel in BCI applications
Explain BCI relevance.
VTU 1BCHES102/202 | Module 5
Alginate Hydrogel
36
BCI application
Soft hydrogels can act as interface materials between electronic components and biological tissue, improving contact, comfort and signal coupling concepts.
Brain / tissue interface
Soft hydrogel layer
Electrode contact
Signal coupling
BCI device function
Notes: What to say: Define BCI as brain-computer interface.
Pause cue: pause after each process diagram and ask students what makes the method greener or more sustainable.
Pointing cue: point from source material to synthesis/property, then to application or waste-management outcome.
Question to ask students: Ask students to connect material property with smart-system use and environmental impact.
Animation instructions: Fade title; appear cards one by one; wipe process arrows in order; highlight keywords such as green solvent, glycerol trioleate, ZnO nanoparticles, RFID, IONT, PLA, PEG, alginate hydrogel, BCI, e-waste, AI and bioleaching word by word.
Transition style: Fade.
[Sources] VTU syllabus PDF 1BCHES102/202 Applied Chemistry for Smart Systems, Module 5 checklist, downloaded from https://vtu.ac.in/pdf/UG2024/1BCHES102.pdf; syllabus-listed textbooks: Engineering Chemistry, Suba Ramesh, Vairam, Ananda Murthy, Wiley India, 2011; A Textbook of Engineering Chemistry, R.V. Gadag and Nityananda Shetty, I.K. International, 2nd ed., 2016; Engineering Chemistry, Jain & Jain, Dhanpat Rai; Wiley Engineering Chemistry, Wiley India, 2013; syllabus-listed references for green/biomaterial/e-waste background include Green Chemistry and Engineering: A Practical Design Approach, Concepción Jiménez-González and David J.C. Constable, Wiley, 2011; E-Waste: Implications, Regulations, and Management in India and Current Global Best Practices, Rakesh Johri, TERI, 2008.

## Slide 37
Biomaterials revision comparison
Connect PLA, PEG and alginate.
VTU 1BCHES102/202 | Module 5
Biomaterials
37
Biomaterial
Core property
Application in module
PLA
Biodegradable transparent thermoplastic
Touch-screen films/substrates
PEG
Hydrophilic flexible biocompatible polymer
Touch-screen coatings/interfaces
Alginate hydrogel
Soft water-rich crosslinked gel
BCI interface material
Notes: What to say: Use this before e-waste.
Pause cue: pause after each process diagram and ask students what makes the method greener or more sustainable.
Pointing cue: point from source material to synthesis/property, then to application or waste-management outcome.
Question to ask students: Ask students to connect material property with smart-system use and environmental impact.
Animation instructions: Fade title; appear cards one by one; wipe process arrows in order; highlight keywords such as green solvent, glycerol trioleate, ZnO nanoparticles, RFID, IONT, PLA, PEG, alginate hydrogel, BCI, e-waste, AI and bioleaching word by word.
Transition style: Fade.
[Sources] VTU syllabus PDF 1BCHES102/202 Applied Chemistry for Smart Systems, Module 5 checklist, downloaded from https://vtu.ac.in/pdf/UG2024/1BCHES102.pdf; syllabus-listed textbooks: Engineering Chemistry, Suba Ramesh, Vairam, Ananda Murthy, Wiley India, 2011; A Textbook of Engineering Chemistry, R.V. Gadag and Nityananda Shetty, I.K. International, 2nd ed., 2016; Engineering Chemistry, Jain & Jain, Dhanpat Rai; Wiley Engineering Chemistry, Wiley India, 2013; syllabus-listed references for green/biomaterial/e-waste background include Green Chemistry and Engineering: A Practical Design Approach, Concepción Jiménez-González and David J.C. Constable, Wiley, 2011; E-Waste: Implications, Regulations, and Management in India and Current Global Best Practices, Rakesh Johri, TERI, 2008.

## Slide 38
What is e-waste?
Define e-waste.
VTU 1BCHES102/202 | Module 5
E-Waste
38
E-waste
E-waste is discarded electrical and electronic equipment and its components, including devices, circuit boards, batteries, cables and peripherals.
Discarded electronics
Components
Metals
Plastics
Hazardous substances
Notes: What to say: Use phones, laptops and chargers as examples.
Pause cue: pause after each process diagram and ask students what makes the method greener or more sustainable.
Pointing cue: point from source material to synthesis/property, then to application or waste-management outcome.
Question to ask students: Ask students to connect material property with smart-system use and environmental impact.
Animation instructions: Fade title; appear cards one by one; wipe process arrows in order; highlight keywords such as green solvent, glycerol trioleate, ZnO nanoparticles, RFID, IONT, PLA, PEG, alginate hydrogel, BCI, e-waste, AI and bioleaching word by word.
Transition style: Fade.
[Sources] VTU syllabus PDF 1BCHES102/202 Applied Chemistry for Smart Systems, Module 5 checklist, downloaded from https://vtu.ac.in/pdf/UG2024/1BCHES102.pdf; syllabus-listed textbooks: Engineering Chemistry, Suba Ramesh, Vairam, Ananda Murthy, Wiley India, 2011; A Textbook of Engineering Chemistry, R.V. Gadag and Nityananda Shetty, I.K. International, 2nd ed., 2016; Engineering Chemistry, Jain & Jain, Dhanpat Rai; Wiley Engineering Chemistry, Wiley India, 2013; syllabus-listed references for green/biomaterial/e-waste background include Green Chemistry and Engineering: A Practical Design Approach, Concepción Jiménez-González and David J.C. Constable, Wiley, 2011; E-Waste: Implications, Regulations, and Management in India and Current Global Best Practices, Rakesh Johri, TERI, 2008.

## Slide 39
Sources of e-waste
List major sources.
VTU 1BCHES102/202 | Module 5
E-Waste
39
Consumer devices
Phones, laptops, tablets, TVs and chargers.
IT infrastructure
Servers, networking devices, storage drives and peripherals.
Industrial electronics
Control boards, sensors and automation equipment.
Household appliances
Refrigerators, washing machines and small electronics.
Notes: What to say: Ask students which source is fastest in their own life.
Pause cue: pause after each process diagram and ask students what makes the method greener or more sustainable.
Pointing cue: point from source material to synthesis/property, then to application or waste-management outcome.
Question to ask students: Ask students to connect material property with smart-system use and environmental impact.
Animation instructions: Fade title; appear cards one by one; wipe process arrows in order; highlight keywords such as green solvent, glycerol trioleate, ZnO nanoparticles, RFID, IONT, PLA, PEG, alginate hydrogel, BCI, e-waste, AI and bioleaching word by word.
Transition style: Fade.
[Sources] VTU syllabus PDF 1BCHES102/202 Applied Chemistry for Smart Systems, Module 5 checklist, downloaded from https://vtu.ac.in/pdf/UG2024/1BCHES102.pdf; syllabus-listed textbooks: Engineering Chemistry, Suba Ramesh, Vairam, Ananda Murthy, Wiley India, 2011; A Textbook of Engineering Chemistry, R.V. Gadag and Nityananda Shetty, I.K. International, 2nd ed., 2016; Engineering Chemistry, Jain & Jain, Dhanpat Rai; Wiley Engineering Chemistry, Wiley India, 2013; syllabus-listed references for green/biomaterial/e-waste background include Green Chemistry and Engineering: A Practical Design Approach, Concepción Jiménez-González and David J.C. Constable, Wiley, 2011; E-Waste: Implications, Regulations, and Management in India and Current Global Best Practices, Rakesh Johri, TERI, 2008.

## Slide 40
Composition of e-waste
Explain what e-waste contains.
VTU 1BCHES102/202 | Module 5
E-Waste
40
Valuable metals
Copper, aluminium, gold, silver and palladium.
Hazardous metals
Lead, cadmium, mercury and chromium compounds may be present.
Polymers and flame retardants
Plastic housings, cables and circuit-board resins.
Glass and ceramics
Displays, screens and insulating components.
Notes: What to say: Emphasize e-waste is both resource and hazard.
Pause cue: pause after each process diagram and ask students what makes the method greener or more sustainable.
Pointing cue: point from source material to synthesis/property, then to application or waste-management outcome.
Question to ask students: Ask students to connect material property with smart-system use and environmental impact.
Animation instructions: Fade title; appear cards one by one; wipe process arrows in order; highlight keywords such as green solvent, glycerol trioleate, ZnO nanoparticles, RFID, IONT, PLA, PEG, alginate hydrogel, BCI, e-waste, AI and bioleaching word by word.
Transition style: Fade.
[Sources] VTU syllabus PDF 1BCHES102/202 Applied Chemistry for Smart Systems, Module 5 checklist, downloaded from https://vtu.ac.in/pdf/UG2024/1BCHES102.pdf; syllabus-listed textbooks: Engineering Chemistry, Suba Ramesh, Vairam, Ananda Murthy, Wiley India, 2011; A Textbook of Engineering Chemistry, R.V. Gadag and Nityananda Shetty, I.K. International, 2nd ed., 2016; Engineering Chemistry, Jain & Jain, Dhanpat Rai; Wiley Engineering Chemistry, Wiley India, 2013; syllabus-listed references for green/biomaterial/e-waste background include Green Chemistry and Engineering: A Practical Design Approach, Concepción Jiménez-González and David J.C. Constable, Wiley, 2011; E-Waste: Implications, Regulations, and Management in India and Current Global Best Practices, Rakesh Johri, TERI, 2008.

## Slide 41
Why e-waste is difficult to manage
Explain complexity.
VTU 1BCHES102/202 | Module 5
E-Waste
41
Mixed product design
Many tiny components
Hazardous and valuable materials together
Manual separation is hard
Improper recycling causes harm
Notes: What to say: Tie design complexity to recycling difficulty.
Pause cue: pause after each process diagram and ask students what makes the method greener or more sustainable.
Pointing cue: point from source material to synthesis/property, then to application or waste-management outcome.
Question to ask students: Ask students to connect material property with smart-system use and environmental impact.
Animation instructions: Fade title; appear cards one by one; wipe process arrows in order; highlight keywords such as green solvent, glycerol trioleate, ZnO nanoparticles, RFID, IONT, PLA, PEG, alginate hydrogel, BCI, e-waste, AI and bioleaching word by word.
Transition style: Fade.
[Sources] VTU syllabus PDF 1BCHES102/202 Applied Chemistry for Smart Systems, Module 5 checklist, downloaded from https://vtu.ac.in/pdf/UG2024/1BCHES102.pdf; syllabus-listed textbooks: Engineering Chemistry, Suba Ramesh, Vairam, Ananda Murthy, Wiley India, 2011; A Textbook of Engineering Chemistry, R.V. Gadag and Nityananda Shetty, I.K. International, 2nd ed., 2016; Engineering Chemistry, Jain & Jain, Dhanpat Rai; Wiley Engineering Chemistry, Wiley India, 2013; syllabus-listed references for green/biomaterial/e-waste background include Green Chemistry and Engineering: A Practical Design Approach, Concepción Jiménez-González and David J.C. Constable, Wiley, 2011; E-Waste: Implications, Regulations, and Management in India and Current Global Best Practices, Rakesh Johri, TERI, 2008.

## Slide 42
Effects on environment
Explain environmental harm.
VTU 1BCHES102/202 | Module 5
E-Waste Impacts
42
Soil contamination
Heavy metals can enter soil from unsafe dumping.
Water pollution
Leachate can contaminate groundwater and surface water.
Air pollution
Open burning releases toxic fumes and particulates.
Resource loss
Valuable metals are wasted when devices are not recovered.
Notes: What to say: Keep this clear and grounded.
Pause cue: pause after each process diagram and ask students what makes the method greener or more sustainable.
Pointing cue: point from source material to synthesis/property, then to application or waste-management outcome.
Question to ask students: Ask students to connect material property with smart-system use and environmental impact.
Animation instructions: Fade title; appear cards one by one; wipe process arrows in order; highlight keywords such as green solvent, glycerol trioleate, ZnO nanoparticles, RFID, IONT, PLA, PEG, alginate hydrogel, BCI, e-waste, AI and bioleaching word by word.
Transition style: Fade.
[Sources] VTU syllabus PDF 1BCHES102/202 Applied Chemistry for Smart Systems, Module 5 checklist, downloaded from https://vtu.ac.in/pdf/UG2024/1BCHES102.pdf; syllabus-listed textbooks: Engineering Chemistry, Suba Ramesh, Vairam, Ananda Murthy, Wiley India, 2011; A Textbook of Engineering Chemistry, R.V. Gadag and Nityananda Shetty, I.K. International, 2nd ed., 2016; Engineering Chemistry, Jain & Jain, Dhanpat Rai; Wiley Engineering Chemistry, Wiley India, 2013; syllabus-listed references for green/biomaterial/e-waste background include Green Chemistry and Engineering: A Practical Design Approach, Concepción Jiménez-González and David J.C. Constable, Wiley, 2011; E-Waste: Implications, Regulations, and Management in India and Current Global Best Practices, Rakesh Johri, TERI, 2008.

## Slide 43
Effects on human health
Explain health risk.
VTU 1BCHES102/202 | Module 5
E-Waste Impacts
43
Respiratory problems
Burning and dust exposure affect lungs.
Neurological effects
Lead and mercury exposure can damage nervous systems.
Skin and eye irritation
Acids, solvents and dust can harm workers.
Long-term toxicity
Bioaccumulation and chronic exposure create serious risk.
Notes: What to say: Mention informal recycling worker risk.
Pause cue: pause after each process diagram and ask students what makes the method greener or more sustainable.
Pointing cue: point from source material to synthesis/property, then to application or waste-management outcome.
Question to ask students: Ask students to connect material property with smart-system use and environmental impact.
Animation instructions: Fade title; appear cards one by one; wipe process arrows in order; highlight keywords such as green solvent, glycerol trioleate, ZnO nanoparticles, RFID, IONT, PLA, PEG, alginate hydrogel, BCI, e-waste, AI and bioleaching word by word.
Transition style: Fade.
[Sources] VTU syllabus PDF 1BCHES102/202 Applied Chemistry for Smart Systems, Module 5 checklist, downloaded from https://vtu.ac.in/pdf/UG2024/1BCHES102.pdf; syllabus-listed textbooks: Engineering Chemistry, Suba Ramesh, Vairam, Ananda Murthy, Wiley India, 2011; A Textbook of Engineering Chemistry, R.V. Gadag and Nityananda Shetty, I.K. International, 2nd ed., 2016; Engineering Chemistry, Jain & Jain, Dhanpat Rai; Wiley Engineering Chemistry, Wiley India, 2013; syllabus-listed references for green/biomaterial/e-waste background include Green Chemistry and Engineering: A Practical Design Approach, Concepción Jiménez-González and David J.C. Constable, Wiley, 2011; E-Waste: Implications, Regulations, and Management in India and Current Global Best Practices, Rakesh Johri, TERI, 2008.

## Slide 44
Responsible e-waste management flow
Show management hierarchy.
VTU 1BCHES102/202 | Module 5
E-Waste Management
44
Reduce and repair
Collect separately
Sort and dismantle
Recover materials safely
Treat residues responsibly
Notes: What to say: This gives students a practical answer flow.
Pause cue: pause after each process diagram and ask students what makes the method greener or more sustainable.
Pointing cue: point from source material to synthesis/property, then to application or waste-management outcome.
Question to ask students: Ask students to connect material property with smart-system use and environmental impact.
Animation instructions: Fade title; appear cards one by one; wipe process arrows in order; highlight keywords such as green solvent, glycerol trioleate, ZnO nanoparticles, RFID, IONT, PLA, PEG, alginate hydrogel, BCI, e-waste, AI and bioleaching word by word.
Transition style: Fade.
[Sources] VTU syllabus PDF 1BCHES102/202 Applied Chemistry for Smart Systems, Module 5 checklist, downloaded from https://vtu.ac.in/pdf/UG2024/1BCHES102.pdf; syllabus-listed textbooks: Engineering Chemistry, Suba Ramesh, Vairam, Ananda Murthy, Wiley India, 2011; A Textbook of Engineering Chemistry, R.V. Gadag and Nityananda Shetty, I.K. International, 2nd ed., 2016; Engineering Chemistry, Jain & Jain, Dhanpat Rai; Wiley Engineering Chemistry, Wiley India, 2013; syllabus-listed references for green/biomaterial/e-waste background include Green Chemistry and Engineering: A Practical Design Approach, Concepción Jiménez-González and David J.C. Constable, Wiley, 2011; E-Waste: Implications, Regulations, and Management in India and Current Global Best Practices, Rakesh Johri, TERI, 2008.

## Slide 45
Why AI helps e-waste management
Introduce AI role.
VTU 1BCHES102/202 | Module 5
AI in E-Waste
45
Recognition
Computer vision can identify device types and components.
Sorting
AI-guided systems can separate materials faster and more accurately.
Tracking
Data systems can trace collection, transport and processing.
Prediction
Models can forecast e-waste volume and recycling demand.
Notes: What to say: Frame AI as a tool, not a magic solution.
Pause cue: pause after each process diagram and ask students what makes the method greener or more sustainable.
Pointing cue: point from source material to synthesis/property, then to application or waste-management outcome.
Question to ask students: Ask students to connect material property with smart-system use and environmental impact.
Animation instructions: Fade title; appear cards one by one; wipe process arrows in order; highlight keywords such as green solvent, glycerol trioleate, ZnO nanoparticles, RFID, IONT, PLA, PEG, alginate hydrogel, BCI, e-waste, AI and bioleaching word by word.
Transition style: Fade.
[Sources] VTU syllabus PDF 1BCHES102/202 Applied Chemistry for Smart Systems, Module 5 checklist, downloaded from https://vtu.ac.in/pdf/UG2024/1BCHES102.pdf; syllabus-listed textbooks: Engineering Chemistry, Suba Ramesh, Vairam, Ananda Murthy, Wiley India, 2011; A Textbook of Engineering Chemistry, R.V. Gadag and Nityananda Shetty, I.K. International, 2nd ed., 2016; Engineering Chemistry, Jain & Jain, Dhanpat Rai; Wiley Engineering Chemistry, Wiley India, 2013; syllabus-listed references for green/biomaterial/e-waste background include Green Chemistry and Engineering: A Practical Design Approach, Concepción Jiménez-González and David J.C. Constable, Wiley, 2011; E-Waste: Implications, Regulations, and Management in India and Current Global Best Practices, Rakesh Johri, TERI, 2008.

## Slide 46
AI-based e-waste management process
Show workflow.
VTU 1BCHES102/202 | Module 5
AI in E-Waste
46
AI management
AI systems can combine imaging, sensors and data analytics to classify e-waste, guide sorting, optimize recovery and monitor compliance.
Image / sensor data
AI classification
Robotic or guided sorting
Recovery route selection
Reporting and compliance
Notes: What to say: Ask students where sensors from Module 4 fit into this system.
Pause cue: pause after each process diagram and ask students what makes the method greener or more sustainable.
Pointing cue: point from source material to synthesis/property, then to application or waste-management outcome.
Question to ask students: Ask students to connect material property with smart-system use and environmental impact.
Animation instructions: Fade title; appear cards one by one; wipe process arrows in order; highlight keywords such as green solvent, glycerol trioleate, ZnO nanoparticles, RFID, IONT, PLA, PEG, alginate hydrogel, BCI, e-waste, AI and bioleaching word by word.
Transition style: Fade.
[Sources] VTU syllabus PDF 1BCHES102/202 Applied Chemistry for Smart Systems, Module 5 checklist, downloaded from https://vtu.ac.in/pdf/UG2024/1BCHES102.pdf; syllabus-listed textbooks: Engineering Chemistry, Suba Ramesh, Vairam, Ananda Murthy, Wiley India, 2011; A Textbook of Engineering Chemistry, R.V. Gadag and Nityananda Shetty, I.K. International, 2nd ed., 2016; Engineering Chemistry, Jain & Jain, Dhanpat Rai; Wiley Engineering Chemistry, Wiley India, 2013; syllabus-listed references for green/biomaterial/e-waste background include Green Chemistry and Engineering: A Practical Design Approach, Concepción Jiménez-González and David J.C. Constable, Wiley, 2011; E-Waste: Implications, Regulations, and Management in India and Current Global Best Practices, Rakesh Johri, TERI, 2008.

## Slide 47
AI advantages and limitations
Balance answer.
VTU 1BCHES102/202 | Module 5
AI in E-Waste
47
Advantages
Limitations
1
Faster identification
2
Improved sorting accuracy
3
Better inventory tracking
4
Reduced worker exposure
1
Needs quality data
2
High setup cost
3
Mixed waste remains challenging
4
Still needs safe chemical recovery
Notes: What to say: Keep it exam-ready.
Pause cue: pause after each process diagram and ask students what makes the method greener or more sustainable.
Pointing cue: point from source material to synthesis/property, then to application or waste-management outcome.
Question to ask students: Ask students to connect material property with smart-system use and environmental impact.
Animation instructions: Fade title; appear cards one by one; wipe process arrows in order; highlight keywords such as green solvent, glycerol trioleate, ZnO nanoparticles, RFID, IONT, PLA, PEG, alginate hydrogel, BCI, e-waste, AI and bioleaching word by word.
Transition style: Fade.
[Sources] VTU syllabus PDF 1BCHES102/202 Applied Chemistry for Smart Systems, Module 5 checklist, downloaded from https://vtu.ac.in/pdf/UG2024/1BCHES102.pdf; syllabus-listed textbooks: Engineering Chemistry, Suba Ramesh, Vairam, Ananda Murthy, Wiley India, 2011; A Textbook of Engineering Chemistry, R.V. Gadag and Nityananda Shetty, I.K. International, 2nd ed., 2016; Engineering Chemistry, Jain & Jain, Dhanpat Rai; Wiley Engineering Chemistry, Wiley India, 2013; syllabus-listed references for green/biomaterial/e-waste background include Green Chemistry and Engineering: A Practical Design Approach, Concepción Jiménez-González and David J.C. Constable, Wiley, 2011; E-Waste: Implications, Regulations, and Management in India and Current Global Best Practices, Rakesh Johri, TERI, 2008.

## Slide 48
What is bioleaching?
Define bioleaching.
VTU 1BCHES102/202 | Module 5
Bioleaching
48
Bioleaching
Bioleaching uses microorganisms or their metabolites to dissolve and recover metals from ores or waste materials under controlled conditions.
Microorganisms
Metal recovery
Leaching solution
Low-temperature process
E-waste
Notes: What to say: Explain it is a biological extraction method.
Pause cue: pause after each process diagram and ask students what makes the method greener or more sustainable.
Pointing cue: point from source material to synthesis/property, then to application or waste-management outcome.
Question to ask students: Ask students to connect material property with smart-system use and environmental impact.
Animation instructions: Fade title; appear cards one by one; wipe process arrows in order; highlight keywords such as green solvent, glycerol trioleate, ZnO nanoparticles, RFID, IONT, PLA, PEG, alginate hydrogel, BCI, e-waste, AI and bioleaching word by word.
Transition style: Fade.
[Sources] VTU syllabus PDF 1BCHES102/202 Applied Chemistry for Smart Systems, Module 5 checklist, downloaded from https://vtu.ac.in/pdf/UG2024/1BCHES102.pdf; syllabus-listed textbooks: Engineering Chemistry, Suba Ramesh, Vairam, Ananda Murthy, Wiley India, 2011; A Textbook of Engineering Chemistry, R.V. Gadag and Nityananda Shetty, I.K. International, 2nd ed., 2016; Engineering Chemistry, Jain & Jain, Dhanpat Rai; Wiley Engineering Chemistry, Wiley India, 2013; syllabus-listed references for green/biomaterial/e-waste background include Green Chemistry and Engineering: A Practical Design Approach, Concepción Jiménez-González and David J.C. Constable, Wiley, 2011; E-Waste: Implications, Regulations, and Management in India and Current Global Best Practices, Rakesh Johri, TERI, 2008.

## Slide 49
Why bioleaching is used for e-waste gold
Explain the need.
VTU 1BCHES102/202 | Module 5
Bioleaching
49
Gold is valuable
Small amounts in PCBs can justify recovery.
Conventional routes can be harsh
Strong chemicals and high energy can create risk.
Biological route
Microbes can generate leaching agents or conditions for metal dissolution.
Selective recovery goal
Process aims to dissolve and recover target metals efficiently.
Notes: What to say: Avoid naming microbes unless required by faculty notes.
Pause cue: pause after each process diagram and ask students what makes the method greener or more sustainable.
Pointing cue: point from source material to synthesis/property, then to application or waste-management outcome.
Question to ask students: Ask students to connect material property with smart-system use and environmental impact.
Animation instructions: Fade title; appear cards one by one; wipe process arrows in order; highlight keywords such as green solvent, glycerol trioleate, ZnO nanoparticles, RFID, IONT, PLA, PEG, alginate hydrogel, BCI, e-waste, AI and bioleaching word by word.
Transition style: Fade.
[Sources] VTU syllabus PDF 1BCHES102/202 Applied Chemistry for Smart Systems, Module 5 checklist, downloaded from https://vtu.ac.in/pdf/UG2024/1BCHES102.pdf; syllabus-listed textbooks: Engineering Chemistry, Suba Ramesh, Vairam, Ananda Murthy, Wiley India, 2011; A Textbook of Engineering Chemistry, R.V. Gadag and Nityananda Shetty, I.K. International, 2nd ed., 2016; Engineering Chemistry, Jain & Jain, Dhanpat Rai; Wiley Engineering Chemistry, Wiley India, 2013; syllabus-listed references for green/biomaterial/e-waste background include Green Chemistry and Engineering: A Practical Design Approach, Concepción Jiménez-González and David J.C. Constable, Wiley, 2011; E-Waste: Implications, Regulations, and Management in India and Current Global Best Practices, Rakesh Johri, TERI, 2008.

## Slide 50
Gold extraction by bioleaching
Show process.
VTU 1BCHES102/202 | Module 5
Bioleaching
50
Gold bioleaching
Pre-treated e-waste is exposed to suitable microorganisms or bio-generated lixiviants, dissolving gold into solution for later recovery.
Collect PCB/e-waste
Pre-treat and size reduce
Add microbes/leaching medium
Gold dissolves into solution
Recover purified gold
Notes: What to say: Point to pre-treatment and recovery as important steps.
Pause cue: pause after each process diagram and ask students what makes the method greener or more sustainable.
Pointing cue: point from source material to synthesis/property, then to application or waste-management outcome.
Question to ask students: Ask students to connect material property with smart-system use and environmental impact.
Animation instructions: Fade title; appear cards one by one; wipe process arrows in order; highlight keywords such as green solvent, glycerol trioleate, ZnO nanoparticles, RFID, IONT, PLA, PEG, alginate hydrogel, BCI, e-waste, AI and bioleaching word by word.
Transition style: Fade.
[Sources] VTU syllabus PDF 1BCHES102/202 Applied Chemistry for Smart Systems, Module 5 checklist, downloaded from https://vtu.ac.in/pdf/UG2024/1BCHES102.pdf; syllabus-listed textbooks: Engineering Chemistry, Suba Ramesh, Vairam, Ananda Murthy, Wiley India, 2011; A Textbook of Engineering Chemistry, R.V. Gadag and Nityananda Shetty, I.K. International, 2nd ed., 2016; Engineering Chemistry, Jain & Jain, Dhanpat Rai; Wiley Engineering Chemistry, Wiley India, 2013; syllabus-listed references for green/biomaterial/e-waste background include Green Chemistry and Engineering: A Practical Design Approach, Concepción Jiménez-González and David J.C. Constable, Wiley, 2011; E-Waste: Implications, Regulations, and Management in India and Current Global Best Practices, Rakesh Johri, TERI, 2008.

## Slide 51
Bioleaching advantages and limitations
Balance answer.
VTU 1BCHES102/202 | Module 5
Bioleaching
51
Advantages
Limitations
1
Lower energy than smelting
2
Potentially fewer harsh chemicals
3
Can recover valuable metals
4
Supports circular economy
1
Slower process
2
Needs controlled pH/temperature
3
Mixed waste can inhibit microbes
4
Final metal recovery still required
Notes: What to say: Use this as a five-mark answer.
Pause cue: pause after each process diagram and ask students what makes the method greener or more sustainable.
Pointing cue: point from source material to synthesis/property, then to application or waste-management outcome.
Question to ask students: Ask students to connect material property with smart-system use and environmental impact.
Animation instructions: Fade title; appear cards one by one; wipe process arrows in order; highlight keywords such as green solvent, glycerol trioleate, ZnO nanoparticles, RFID, IONT, PLA, PEG, alginate hydrogel, BCI, e-waste, AI and bioleaching word by word.
Transition style: Fade.
[Sources] VTU syllabus PDF 1BCHES102/202 Applied Chemistry for Smart Systems, Module 5 checklist, downloaded from https://vtu.ac.in/pdf/UG2024/1BCHES102.pdf; syllabus-listed textbooks: Engineering Chemistry, Suba Ramesh, Vairam, Ananda Murthy, Wiley India, 2011; A Textbook of Engineering Chemistry, R.V. Gadag and Nityananda Shetty, I.K. International, 2nd ed., 2016; Engineering Chemistry, Jain & Jain, Dhanpat Rai; Wiley Engineering Chemistry, Wiley India, 2013; syllabus-listed references for green/biomaterial/e-waste background include Green Chemistry and Engineering: A Practical Design Approach, Concepción Jiménez-González and David J.C. Constable, Wiley, 2011; E-Waste: Implications, Regulations, and Management in India and Current Global Best Practices, Rakesh Johri, TERI, 2008.

## Slide 52
Circular economy view of electronics
Connect all Module 5 topics.
VTU 1BCHES102/202 | Module 5
Circular Economy
52
Design greener materials
Use smart devices responsibly
Collect e-waste
Recover materials
Feed materials back into production
Notes: What to say: Show this is the final sustainability loop.
Pause cue: pause after each process diagram and ask students what makes the method greener or more sustainable.
Pointing cue: point from source material to synthesis/property, then to application or waste-management outcome.
Question to ask students: Ask students to connect material property with smart-system use and environmental impact.
Animation instructions: Fade title; appear cards one by one; wipe process arrows in order; highlight keywords such as green solvent, glycerol trioleate, ZnO nanoparticles, RFID, IONT, PLA, PEG, alginate hydrogel, BCI, e-waste, AI and bioleaching word by word.
Transition style: Fade.
[Sources] VTU syllabus PDF 1BCHES102/202 Applied Chemistry for Smart Systems, Module 5 checklist, downloaded from https://vtu.ac.in/pdf/UG2024/1BCHES102.pdf; syllabus-listed textbooks: Engineering Chemistry, Suba Ramesh, Vairam, Ananda Murthy, Wiley India, 2011; A Textbook of Engineering Chemistry, R.V. Gadag and Nityananda Shetty, I.K. International, 2nd ed., 2016; Engineering Chemistry, Jain & Jain, Dhanpat Rai; Wiley Engineering Chemistry, Wiley India, 2013; syllabus-listed references for green/biomaterial/e-waste background include Green Chemistry and Engineering: A Practical Design Approach, Concepción Jiménez-González and David J.C. Constable, Wiley, 2011; E-Waste: Implications, Regulations, and Management in India and Current Global Best Practices, Rakesh Johri, TERI, 2008.

## Slide 53
Common mistakes in Module 5
Clarify likely errors.
VTU 1BCHES102/202 | Module 5
Exam Prep
53
1
Calling any solvent green without discussing toxicity, volatility or recyclability
2
Writing glycerol trioleate use without ester synthesis or properties
3
Forgetting ZnO green synthesis steps and RFID/IONT applications
4
Mixing PLA, PEG and alginate hydrogel properties
5
Listing e-waste sources without composition and effects
6
Saying AI replaces recycling chemistry completely
7
Writing bioleaching without microorganisms and recovery step
Notes: What to say: Use this as pre-exam protection.
Pause cue: pause after each process diagram and ask students what makes the method greener or more sustainable.
Pointing cue: point from source material to synthesis/property, then to application or waste-management outcome.
Question to ask students: Ask students to connect material property with smart-system use and environmental impact.
Animation instructions: Fade title; appear cards one by one; wipe process arrows in order; highlight keywords such as green solvent, glycerol trioleate, ZnO nanoparticles, RFID, IONT, PLA, PEG, alginate hydrogel, BCI, e-waste, AI and bioleaching word by word.
Transition style: Fade.
[Sources] VTU syllabus PDF 1BCHES102/202 Applied Chemistry for Smart Systems, Module 5 checklist, downloaded from https://vtu.ac.in/pdf/UG2024/1BCHES102.pdf; syllabus-listed textbooks: Engineering Chemistry, Suba Ramesh, Vairam, Ananda Murthy, Wiley India, 2011; A Textbook of Engineering Chemistry, R.V. Gadag and Nityananda Shetty, I.K. International, 2nd ed., 2016; Engineering Chemistry, Jain & Jain, Dhanpat Rai; Wiley Engineering Chemistry, Wiley India, 2013; syllabus-listed references for green/biomaterial/e-waste background include Green Chemistry and Engineering: A Practical Design Approach, Concepción Jiménez-González and David J.C. Constable, Wiley, 2011; E-Waste: Implications, Regulations, and Management in India and Current Global Best Practices, Rakesh Johri, TERI, 2008.

## Slide 54
How to write a 10-mark green-material answer
Give a repeatable framework.
VTU 1BCHES102/202 | Module 5
Exam Prep
54
Definition
Synthesis / preparation
Properties
Smart-system application
Green advantage
Notes: What to say: Tell students this works for green solvents, glycerol trioleate, ZnO, PLA, PEG and alginate.
Pause cue: pause after each process diagram and ask students what makes the method greener or more sustainable.
Pointing cue: point from source material to synthesis/property, then to application or waste-management outcome.
Question to ask students: Ask students to connect material property with smart-system use and environmental impact.
Animation instructions: Fade title; appear cards one by one; wipe process arrows in order; highlight keywords such as green solvent, glycerol trioleate, ZnO nanoparticles, RFID, IONT, PLA, PEG, alginate hydrogel, BCI, e-waste, AI and bioleaching word by word.
Transition style: Fade.
[Sources] VTU syllabus PDF 1BCHES102/202 Applied Chemistry for Smart Systems, Module 5 checklist, downloaded from https://vtu.ac.in/pdf/UG2024/1BCHES102.pdf; syllabus-listed textbooks: Engineering Chemistry, Suba Ramesh, Vairam, Ananda Murthy, Wiley India, 2011; A Textbook of Engineering Chemistry, R.V. Gadag and Nityananda Shetty, I.K. International, 2nd ed., 2016; Engineering Chemistry, Jain & Jain, Dhanpat Rai; Wiley Engineering Chemistry, Wiley India, 2013; syllabus-listed references for green/biomaterial/e-waste background include Green Chemistry and Engineering: A Practical Design Approach, Concepción Jiménez-González and David J.C. Constable, Wiley, 2011; E-Waste: Implications, Regulations, and Management in India and Current Global Best Practices, Rakesh Johri, TERI, 2008.

## Slide 55
How to write a 10-mark e-waste answer
Give a repeatable framework.
VTU 1BCHES102/202 | Module 5
Exam Prep
55
Definition and sources
Composition
Environmental effects
Human-health effects
AI / bioleaching management
Notes: What to say: This provides a complete e-waste answer structure.
Pause cue: pause after each process diagram and ask students what makes the method greener or more sustainable.
Pointing cue: point from source material to synthesis/property, then to application or waste-management outcome.
Question to ask students: Ask students to connect material property with smart-system use and environmental impact.
Animation instructions: Fade title; appear cards one by one; wipe process arrows in order; highlight keywords such as green solvent, glycerol trioleate, ZnO nanoparticles, RFID, IONT, PLA, PEG, alginate hydrogel, BCI, e-waste, AI and bioleaching word by word.
Transition style: Fade.
[Sources] VTU syllabus PDF 1BCHES102/202 Applied Chemistry for Smart Systems, Module 5 checklist, downloaded from https://vtu.ac.in/pdf/UG2024/1BCHES102.pdf; syllabus-listed textbooks: Engineering Chemistry, Suba Ramesh, Vairam, Ananda Murthy, Wiley India, 2011; A Textbook of Engineering Chemistry, R.V. Gadag and Nityananda Shetty, I.K. International, 2nd ed., 2016; Engineering Chemistry, Jain & Jain, Dhanpat Rai; Wiley Engineering Chemistry, Wiley India, 2013; syllabus-listed references for green/biomaterial/e-waste background include Green Chemistry and Engineering: A Practical Design Approach, Concepción Jiménez-González and David J.C. Constable, Wiley, 2011; E-Waste: Implications, Regulations, and Management in India and Current Global Best Practices, Rakesh Johri, TERI, 2008.

## Slide 56
Module 5 mind map
Connect all syllabus headings.
VTU 1BCHES102/202 | Module 5
Summary
56
Module 5
Green chemistry
Safer design.
Green materials
Solvents, ester, ZnO.
Biomaterials
PLA, PEG, alginate.
Smart systems
Servers, RFID, IONT, BCI.
E-waste
Sources and effects.
Recovery
AI and bioleaching.
Notes: What to say: Use this as the end-of-teaching overview.
Pause cue: pause after each process diagram and ask students what makes the method greener or more sustainable.
Pointing cue: point from source material to synthesis/property, then to application or waste-management outcome.
Question to ask students: Ask students to connect material property with smart-system use and environmental impact.
Animation instructions: Fade title; appear cards one by one; wipe process arrows in order; highlight keywords such as green solvent, glycerol trioleate, ZnO nanoparticles, RFID, IONT, PLA, PEG, alginate hydrogel, BCI, e-waste, AI and bioleaching word by word.
Transition style: Fade.
[Sources] VTU syllabus PDF 1BCHES102/202 Applied Chemistry for Smart Systems, Module 5 checklist, downloaded from https://vtu.ac.in/pdf/UG2024/1BCHES102.pdf; syllabus-listed textbooks: Engineering Chemistry, Suba Ramesh, Vairam, Ananda Murthy, Wiley India, 2011; A Textbook of Engineering Chemistry, R.V. Gadag and Nityananda Shetty, I.K. International, 2nd ed., 2016; Engineering Chemistry, Jain & Jain, Dhanpat Rai; Wiley Engineering Chemistry, Wiley India, 2013; syllabus-listed references for green/biomaterial/e-waste background include Green Chemistry and Engineering: A Practical Design Approach, Concepción Jiménez-González and David J.C. Constable, Wiley, 2011; E-Waste: Implications, Regulations, and Management in India and Current Global Best Practices, Rakesh Johri, TERI, 2008.

## Slide 57
20 important viva questions
Rapid oral revision.
VTU 1BCHES102/202 | Module 5
Summary
57
1. What is green chemistry?
2. Define green solvent.
3. Properties of green solvents?
4. Server heat-management use?
5. What is glycerol trioleate?
6. How is glycerol trioleate synthesized?
7. What are ZnO nanoparticles?
8. Green synthesis of ZnO steps?
9. ZnO use in RFID?
10. What is IONT?
11. Define biomaterial.
12. What is PLA?
13. What is PEG?
14. What is alginate hydrogel?
15. BCI application of hydrogel?
16. Define e-waste.
17. Sources of e-waste?
18. Composition of e-waste?
19. How does AI help e-waste management?
20. What is bioleaching?
Notes: What to say: Run this as quick viva.
Pause cue: pause after each process diagram and ask students what makes the method greener or more sustainable.
Pointing cue: point from source material to synthesis/property, then to application or waste-management outcome.
Question to ask students: Ask students to connect material property with smart-system use and environmental impact.
Animation instructions: Fade title; appear cards one by one; wipe process arrows in order; highlight keywords such as green solvent, glycerol trioleate, ZnO nanoparticles, RFID, IONT, PLA, PEG, alginate hydrogel, BCI, e-waste, AI and bioleaching word by word.
Transition style: Fade.
[Sources] VTU syllabus PDF 1BCHES102/202 Applied Chemistry for Smart Systems, Module 5 checklist, downloaded from https://vtu.ac.in/pdf/UG2024/1BCHES102.pdf; syllabus-listed textbooks: Engineering Chemistry, Suba Ramesh, Vairam, Ananda Murthy, Wiley India, 2011; A Textbook of Engineering Chemistry, R.V. Gadag and Nityananda Shetty, I.K. International, 2nd ed., 2016; Engineering Chemistry, Jain & Jain, Dhanpat Rai; Wiley Engineering Chemistry, Wiley India, 2013; syllabus-listed references for green/biomaterial/e-waste background include Green Chemistry and Engineering: A Practical Design Approach, Concepción Jiménez-González and David J.C. Constable, Wiley, 2011; E-Waste: Implications, Regulations, and Management in India and Current Global Best Practices, Rakesh Johri, TERI, 2008.

## Slide 58
Important exam questions
Provide practice questions.
VTU 1BCHES102/202 | Module 5
Summary
58
1. 2M: Define green chemistry.
2. 2M: Define green solvent.
3. 2M: What is e-waste?
4. 2M: Define bioleaching.
5. 2M: What is PLA?
6. 5M: Explain properties and applications of green solvents.
7. 5M: Explain synthesis and uses of glycerol trioleate ester.
8. 5M: Explain green synthesis and applications of ZnO nanoparticles.
9. 5M: Explain synthesis and properties of PLA and PEG.
10. 5M: Explain alginate hydrogel for BCI applications.
11. 10M: Explain green chemistry materials in IT infrastructure applications.
12. 10M: Explain PLA, PEG and alginate hydrogel with synthesis and uses.
13. 10M: Explain sources, composition and effects of e-waste.
14. 10M: Explain AI in e-waste management.
15. 10M: Explain extraction of gold from e-waste by bioleaching.
Notes: What to say: Use this as the student study checklist.
Pause cue: pause after each process diagram and ask students what makes the method greener or more sustainable.
Pointing cue: point from source material to synthesis/property, then to application or waste-management outcome.
Question to ask students: Ask students to connect material property with smart-system use and environmental impact.
Animation instructions: Fade title; appear cards one by one; wipe process arrows in order; highlight keywords such as green solvent, glycerol trioleate, ZnO nanoparticles, RFID, IONT, PLA, PEG, alginate hydrogel, BCI, e-waste, AI and bioleaching word by word.
Transition style: Fade.
[Sources] VTU syllabus PDF 1BCHES102/202 Applied Chemistry for Smart Systems, Module 5 checklist, downloaded from https://vtu.ac.in/pdf/UG2024/1BCHES102.pdf; syllabus-listed textbooks: Engineering Chemistry, Suba Ramesh, Vairam, Ananda Murthy, Wiley India, 2011; A Textbook of Engineering Chemistry, R.V. Gadag and Nityananda Shetty, I.K. International, 2nd ed., 2016; Engineering Chemistry, Jain & Jain, Dhanpat Rai; Wiley Engineering Chemistry, Wiley India, 2013; syllabus-listed references for green/biomaterial/e-waste background include Green Chemistry and Engineering: A Practical Design Approach, Concepción Jiménez-González and David J.C. Constable, Wiley, 2011; E-Waste: Implications, Regulations, and Management in India and Current Global Best Practices, Rakesh Johri, TERI, 2008.

## Slide 59
One-page revision sheet
End with compact keywords and answer pattern.
VTU 1BCHES102/202 | Module 5
Summary
59
Keywords
Green chemistry; green solvent; low toxicity; low volatility; recyclability; biodegradability; server heat management; coolant; glycerol trioleate; glycerol; oleic acid; esterification; IT infrastructure; ZnO nanoparticles; green synthesis; plant extract; RFID; Internet of Nano Things; biomaterial; PLA; polylactic acid; lactic acid; lactide; biodegradable polyester; PEG; polyethylene glycol; hydrophilic polymer; touch screen; alginate hydrogel; sodium alginate; calcium crosslinking; BCI; e-waste; sources; composition; heavy metals; plastics; environment effects; human-health effects; AI sorting; computer vision; bioleaching; microorganisms; gold recovery.
Exam answer pattern
For green materials: definition, synthesis, properties, application, green advantage. For e-waste: definition, sources, composition, effects, AI management and bioleaching recovery.
Memory trick
Green materials reduce hazard at the design stage; e-waste management reduces harm after product life ends.
Notes: What to say: Close by asking students to explain how one material reduces impact before use and one method reduces impact after disposal.
Pause cue: pause after each process diagram and ask students what makes the method greener or more sustainable.
Pointing cue: point from source material to synthesis/property, then to application or waste-management outcome.
Question to ask students: Ask students to connect material property with smart-system use and environmental impact.
Animation instructions: Fade title; appear cards one by one; wipe process arrows in order; highlight keywords such as green solvent, glycerol trioleate, ZnO nanoparticles, RFID, IONT, PLA, PEG, alginate hydrogel, BCI, e-waste, AI and bioleaching word by word.
Transition style: Fade.
[Sources] VTU syllabus PDF 1BCHES102/202 Applied Chemistry for Smart Systems, Module 5 checklist, downloaded from https://vtu.ac.in/pdf/UG2024/1BCHES102.pdf; syllabus-listed textbooks: Engineering Chemistry, Suba Ramesh, Vairam, Ananda Murthy, Wiley India, 2011; A Textbook of Engineering Chemistry, R.V. Gadag and Nityananda Shetty, I.K. International, 2nd ed., 2016; Engineering Chemistry, Jain & Jain, Dhanpat Rai; Wiley Engineering Chemistry, Wiley India, 2013; syllabus-listed references for green/biomaterial/e-waste background include Green Chemistry and Engineering: A Practical Design Approach, Concepción Jiménez-González and David J.C. Constable, Wiley, 2011; E-Waste: Implications, Regulations, and Management in India and Current Global Best Practices, Rakesh Johri, TERI, 2008.