## Slide 1
Digital Communication
Module 1 asks: How do I turn a radio-frequency waveform into a handful of numbers, and what is the best possible receiver…
VTU BEC503 | Module 1
Opening
01
MODULE 1
Bandpass Signals to Equivalent Lowpass and Signalling over AWGN Channels
10 contact hours | 16 teaching units | 56 slides
PRESCRIBED TEXTBOOK
Digital Communication Systems
Simon Haykin
John Wiley & Sons, 1st edition, 2014
TB1 (Haykin 2014) Ch. 2.8-2.11 pp. 42-52 and Ch. 7.1-7.4 pp. 323-344
Signal Space & AWGN • Digital Modulation • Information Theory • Block & Cyclic Codes • Convolutional Codes
Carrier hides the information → Hilbert builds the analytic signal → Complex envelope drops the carrier → Gram-Schmidt makes signals vectors → Matched filter decides optimally
EC · Semester 5 · BEC503 · generated for Phase 2 conversion
Notes: What to say: Open by putting the whole module on one page. Tell them this is 10 contact hours and 16 teaching units, and that all of it exists to answer one question: How do I turn a radio-frequency waveform into a handful of numbers, and what is the best possible receiver once I have? Name the prescribed textbook out loud and say which chapters they will be living in, so nobody is reading the wrong book by week two. Pause cue: Pause after reading the driving question aloud, before naming the textbook. Pointing cue: Point at the module title block, then at the textbook panel, then run a finger along the five-beat arc. Question to ask students: Ask: before we start, what do you already expect the answer to "How do I turn a radio-frequency waveform into a handful of numbers, and what is the best…" to look like? Animation instructions: Module title block fades in first, then the textbook panel slides in from the right, then the five arc beats appear left to right one at a time. Transition style: Fade [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 1: Bandpass Signals to Equivalent Lowpass and Signalling over AWGN Channels, 10 hours, TB1 (Haykin 2014) Ch. 2.8-2.11 pp. 42-52 and Ch. 7.1-7.4 pp. 323-344. TB1: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 2
What this module is actually for
One question, five beats, and the scope it does not cover.
VTU BEC503 | Module 1
Overview
02
THE DRIVING QUESTION
How do I turn a radio-frequency waveform into a handful of numbers, and what is the best possible receiver once I have?
1
Carrier hides the information
2
Hilbert builds the analytic signal
3
Complex envelope drops the carrier
4
Gram-Schmidt makes signals vectors
5
Matched filter decides optimally
SCOPE AND PROVENANCE
Built from TB1 Sections 2.8-2.11 and 7.1-7.4, the sections the syllabus names. The organising idea is a single change of representation: a bandpass waveform carries no information in its carrier, so the carrier is removed analytically to leave a complex lowpass envelope, and that envelope is then projected onto an orthonormal basis so that a continuous waveform becomes a point in a finite-dimensional space. Once signals are points and noise is a Gaussian cloud, the optimum receiver is forced rather than invented: it is nearest-neighbour decision, and the correlation receiver and matched filter are two circuits computing the same projection.
Course outcomes exercised: CO1
Assessment: 20 MCQs + 13 descriptive questions + 11 assignment items
Notes: What to say: Give them the map before the territory. Read the driving question once more, then walk the five beats across the slide and say in one sentence what changes between each beat and the next. Finish on the scope paragraph, because knowing what a module does not cover saves more marks than anything else on this slide. Pause cue: Pause for four or five seconds after the five beats appear, before moving to scope. Pointing cue: Point at the driving question panel, then at each numbered beat in turn, then at the scope paragraph. Question to ask students: Ask: which of these five beats do you expect to find hardest, and why that one? Animation instructions: The driving question panel fades in, then the five numbered beats appear left to right one at a time, then the scope paragraph fades in beneath them. Transition style: Fade [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 1: Bandpass Signals to Equivalent Lowpass and Signalling over AWGN Channels, 10 hours, TB1 (Haykin 2014) Ch. 2.8-2.11 pp. 42-52 and Ch. 7.1-7.4 pp. 323-344. TB1: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 3
Every unit against its chapter and pages
Units 1-9 of 16, with the deck slides that teach each one.
VTU BEC503 | Module 1
Syllabus mapping
03
# — Teaching unit — Book chapter and pages — Deck slides — CO / Bloom
01 Why a bandpass signal needs a lowpass equivalent — Ch. 2, pp. 42-45 — slides 5, 6, 7 — CO1 / L2
02 The Hilbert transform as a wideband 90-degree phase shifter — Ch. 2, pp. 42-45 — slides 8, 9, 10 — CO1 / L2
03 Properties of the Hilbert transform and why they matter — Ch. 2, pp. 42-45 — slides 11, 12, 13 — CO1 / L3
04 The pre-envelope, or analytic signal — Ch. 2, pp. 45-47 — slides 14, 15, 16 — CO1 / L3
05 The complex envelope: removing the carrier — Ch. 2, pp. 47-49 — slides 17, 18, 19 — CO1 / L3
06 Canonical representation: in-phase and quadrature components — Ch. 2, pp. 49-52 — slides 20, 21, 22 — CO1 / L3
07 Polar form: natural envelope and phase — Ch. 2, pp. 49-52 — slides 23, 24, 25 — CO1 / L3
08 The AWGN channel model and what it assumes — Ch. 7, pp. 323-324 — slides 26, 27, 28 — CO1 / L2
09 Geometric representation: signals as points in a vector space — Ch. 7, pp. 324-332 — slides 29, 30, 31 — CO1 / L3
Notes: What to say: Tell them this is the slide to photograph. Every unit in the module is listed against a real chapter and a real page range, so there is no ambiguity about what to read. Point out the slide-number column and say plainly that if they miss a lecture, those are the slides covering that unit. Say that the page ranges come from the book's own table of contents rather than a guess. Pause cue: Pause for ten seconds and let them photograph the table before saying anything else. Pointing cue: Run a finger down the chapter-and-pages column, then across one complete row. Question to ask students: Ask: pick any row - which chapter would you open first, and what would you expect in the first paragraph? Animation instructions: Header row appears first, then the unit rows fade in one at a time from the top, then the chapter-and-pages column highlights. Transition style: Cut [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 1: Bandpass Signals to Equivalent Lowpass and Signalling over AWGN Channels, 10 hours, TB1 (Haykin 2014) Ch. 2.8-2.11 pp. 42-52 and Ch. 7.1-7.4 pp. 323-344. TB1: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014. Mapping covers all 16 teaching units. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 4
Syllabus mapping, continued
Units 10-16 of 16, with the deck slides that teach each one.
VTU BEC503 | Module 1
Syllabus mapping
04
# — Teaching unit — Book chapter and pages — Deck slides — CO / Bloom
10 The Gram-Schmidt orthogonalization procedure — Ch. 7, pp. 324-332 — slides 32, 33, 34 — CO1 / L4
11 Energy, distance and the constellation diagram — Ch. 7, pp. 324-332 — slides 35, 36, 37 — CO1 / L4
12 Converting the continuous AWGN channel into a vector channel — Ch. 7, pp. 332-337 — slides 38, 39, 40 — CO1 / L4
13 The theorem of irrelevance and sufficient statistics — Ch. 7, pp. 332-337 — slides 41, 42, 43 — CO1 / L4
14 Maximum likelihood decoding and decision regions — Ch. 7, pp. 337-344 — slides 44, 45, 46 — CO1 / L4
15 The correlation receiver — Ch. 7, pp. 337-344 — slides 47, 48, 49 — CO1 / L3
16 The matched filter receiver and its equivalence to the correlator — Ch. 7, pp. 337-344 — slides 50, 51, 52 — CO1 / L4
Notes: What to say: Tell them this is the slide to photograph. Every unit in the module is listed against a real chapter and a real page range, so there is no ambiguity about what to read. Point out the slide-number column and say plainly that if they miss a lecture, those are the slides covering that unit. Say that the page ranges come from the book's own table of contents rather than a guess. Pause cue: Pause for ten seconds and let them photograph the table before saying anything else. Pointing cue: Run a finger down the chapter-and-pages column, then across one complete row. Question to ask students: Ask: pick any row - which chapter would you open first, and what would you expect in the first paragraph? Animation instructions: Header row appears first, then the unit rows fade in one at a time from the top, then the chapter-and-pages column highlights. Transition style: Cut [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 1: Bandpass Signals to Equivalent Lowpass and Signalling over AWGN Channels, 10 hours, TB1 (Haykin 2014) Ch. 2.8-2.11 pp. 42-52 and Ch. 7.1-7.4 pp. 323-344. TB1: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014. Mapping covers all 16 teaching units. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 5
Why a bandpass signal needs a lowpass equivalent
What it is, why it works, and what it costs.
VTU BEC503 | Module 1
Why a bandpass signal needs a lowpass…
05
THE MECHANISM
A bandpass signal has all its significant frequency content confined to a band of width 2W centred on a carrier frequency fc, where fc is typically far larger than W. The carrier itself carries no information — it exists only to place the message where the antenna and the licence allow — so every operation that matters happens to the modulation riding on it. Working directly with the bandpass waveform forces a sampling rate set by fc rather than by W, which for a 2 GHz carrier and a 2 MHz message is three orders of magnitude of waste. The lowpass equivalent is a complex signal of bandwidth W that carries exactly the same information, so analysis and simulation cost is set by the message and not by where the message happens to sit.
KEY TERMS
• bandpass signal
• carrier frequency
• bandwidth
• lowpass equivalent
• sampling rate
TAKEAWAY
The carrier is packaging, not content; strip it analytically and the sampling cost drops by the ratio fc/W.
DIAGRAM FOR PHASE 2
A frequency axis running from -fc to +fc. Two shaded lobes of width 2W sit at -fc and +fc, labelled "negative-frequency image" and "positive-frequency band". Below, a second axis centred on zero shows one lobe…
Source: Digital Communication Systems, 1st ed., Ch. 2, pp. 42-45
CO1 | Bloom L2 | visual id: bandpass-to-lowpass-shift
Notes: What to say: Give them the idea before the formalism. Say it plainly first: A bandpass signal has all its significant frequency content confined to a band of width 2W centred on a carrier frequency fc, where fc is typically far la… Then add the part they are examined on - The carrier is packaging, not content; strip it analytically and the sampling cost drops by the ratio fc/W. Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "bandpass signal" constrain here, and what would break if it did not hold? Animation instructions: the frequency axis draws, then the two bandpass lobes fade in together, then the lower axis appears, then the translate arrow sweeps the positive lobe down to the origin, then the two sampling-rate lines land one after the other with the green one last. Transition style: Fade [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 1: Bandpass Signals to Equivalent Lowpass and Signalling over AWGN Channels. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 2, pp. 42-45. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 6
Why a bandpass signal needs a lowpass equivalent - how it works
The procedure in order, and what each pass costs you.
VTU BEC503 | Module 1
Why a bandpass signal needs a lowpass…
06
1. Confirm the signal is bandpass: content confined to fc - W < |f| < fc + W
2. Suppress the negative-frequency half to form the pre-envelope
3. Translate the remaining spectrum down by fc
4. Retain the resulting complex lowpass signal as the equivalent
5. Recover the bandpass signal when needed by re-modulating and taking the real part
COST AND BEHAVIOUR
Best: no information is lost — the mapping is exactly invertible
Typical: sampling rate falls from 2(fc + W) to 2W
Worst: the equivalent is complex, so two real sequences are stored instead of one
WHAT THAT MEANS
Two real sequences at 2W still beat one real sequence at 2(fc + W) whenever fc > W, which is always.
Source: Digital Communication Systems, 1st ed., Ch. 2, pp. 42-45 | CO1 | Bloom L2
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Confirm the signal is bandpass: content confined to fc - W < |f| < fc + W - and check everyone has written it before moving on. At the cost panel, translate it: Two real sequences at 2W still beat one real sequence at 2(fc + W) whenever fc > W, which is always. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 1: Bandpass Signals to Equivalent Lowpass and Signalling over AWGN Channels. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 2, pp. 42-45. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 7
Why a bandpass signal needs a lowpass equivalent - worked example
One concrete case, carried all the way to a stated number.
VTU BEC503 | Module 1
Why a bandpass signal needs a lowpass…
07
GIVEN
A signal occupying 2.400 GHz to 2.402 GHz, so fc = 2.401 GHz and W = 1 MHz.
1. Bandpass sampling would need fs > 2 x 2.402 GHz = 4.804 GHz
2. Form the pre-envelope, removing the negative-frequency lobe
3. Shift down by fc = 2.401 GHz; content now occupies -1 MHz to +1 MHz
4. Lowpass sampling needs fs > 2 MHz, complex
RESULT
4.804 GHz real samples become 2 MHz complex samples — a factor of about 1200 fewer numbers for exactly the same information.
s(t) = a(t) cos(2*pi*fc*t + phi(t))
= Re{ s_lowpass(t) * exp(j*2*pi*fc*t) }
s_lowpass(t) = a(t) * exp(j*phi(t)) complex, bandwidth W
s_pre(t) = s(t) + j*s_hat(t) analytic, one-sided spectrum
THE MISTAKE STUDENTS MAKE
Students treat the lowpass equivalent as an approximation and expect a loss of accuracy. It is an exact, invertible change of representation — the bandpass signal can be reconstructed from it perfectly, provided fc > W so the two spectral lobes do not overlap.
Source: Digital Communication Systems, 1st ed., Ch. 2, pp. 42-45 | CO1 | Bloom L2
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is A signal occupying 2.400 GHz to 2.402 GHz, so fc = 2.401 GHz and W = 1 MHz. Work at the pace of the slowest note-taker and land hard on the result: 4.804 GHz real samples become 2 MHz complex samples — a factor of about 1200 fewer numbers for exactly the same information. Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 1: Bandpass Signals to Equivalent Lowpass and Signalling over AWGN Channels. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 2, pp. 42-45. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 8
The Hilbert transform as a wideband 90-degree phase shifter
What it is, why it works, and what it costs.
VTU BEC503 | Module 1
The Hilbert transform as a wideband 9…
08
THE MECHANISM
The Hilbert transform of a signal g(t) is its convolution with the kernel 1/(pi*t), written g-hat(t). In the frequency domain this multiplies the spectrum by -j*sgn(f), which leaves every magnitude untouched and rotates every positive-frequency component by -90 degrees and every negative-frequency component by +90 degrees. It is therefore not a filter in the usual sense — nothing is attenuated — but a phase shifter that acts uniformly across all frequencies, which is exactly what a simple RC network cannot do. Its purpose in this course is single-sided spectra: adding j times the Hilbert transform to the original signal cancels the negative-frequency half.
KEY TERMS
• Hilbert transform
• quadrature filter
• signum function
• phase shift
• convolution kernel
TAKEAWAY
The Hilbert transform changes phase by 90 degrees at every frequency and magnitude at none, which is why it can cancel a whole spectral half.
DIAGRAM FOR PHASE 2
Two stacked plots against frequency f. The upper plot is |H(f)| = 1, a flat horizontal green line across all f, labelled "magnitude unchanged". The lower plot is the phase response: a step at -90 degrees for f…
Source: Digital Communication Systems, 1st ed., Ch. 2, pp. 42-45
CO1 | Bloom L2 | visual id: hilbert-phase-response
Notes: What to say: Give them the idea before the formalism. Say it plainly first: The Hilbert transform of a signal g(t) is its convolution with the kernel 1/(pi*t), written g-hat(t). Then add the part they are examined on - The Hilbert transform changes phase by 90 degrees at every frequency and magnitude at none, which is why it can cancel a who… Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "Hilbert transform" constrain here, and what would break if it did not hold? Animation instructions: the frequency axis draws, then the flat magnitude line sweeps in left to right and its label lands, then the two phase segments appear one at a time with the discontinuity circle last, then the time-domain inset fades in and the dashed shifted wave slides a quarter period to the right. Transition style: Fade [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 1: Bandpass Signals to Equivalent Lowpass and Signalling over AWGN Channels. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 2, pp. 42-45. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 9
The Hilbert transform as a wideband 90-degree phase shi… - how it works
The procedure in order, and what each pass costs you.
VTU BEC503 | Module 1
The Hilbert transform as a wideband 9…
09
1. Take the Fourier transform G(f) of the signal
2. Multiply by -j for all f > 0 and by +j for all f < 0
3. Leave the magnitude spectrum entirely alone
4. Inverse transform to obtain g-hat(t)
5. Equivalently, convolve g(t) with 1/(pi*t) in the time domain
COST AND BEHAVIOUR
Best: trivial for a single sinusoid — cos becomes sin
Typical: one FFT, one multiply, one inverse FFT
Worst: the ideal kernel is non-causal and infinitely long, so any real implementation truncates and delays
WHAT THAT MEANS
Practical Hilbert transformers are FIR approximations with a group delay of half the filter length.
Source: Digital Communication Systems, 1st ed., Ch. 2, pp. 42-45 | CO1 | Bloom L2
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Take the Fourier transform G(f) of the signal - and check everyone has written it before moving on. At the cost panel, translate it: Practical Hilbert transformers are FIR approximations with a group delay of half the filter length. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 1: Bandpass Signals to Equivalent Lowpass and Signalling over AWGN Channels. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 2, pp. 42-45. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 10
The Hilbert transform as a wideband 90-degree phase shi… - worked example
One concrete case, carried all the way to a stated number.
VTU BEC503 | Module 1
The Hilbert transform as a wideband 9…
10
GIVEN
g(t) = cos(2*pi*f0*t), a single tone.
1. G(f) consists of two impulses of weight 1/2 at +f0 and -f0
2. Multiply the +f0 impulse by -j and the -f0 impulse by +j
3. The result is the transform of sin(2*pi*f0*t)
4. Check the reverse: applying the transform again gives -cos(2*pi*f0*t)
RESULT
The Hilbert transform of cos is sin, and applying it twice returns the negative of the original — consistent with (-j*sgn(f))^2 = -1.
g_hat(t) = (1/pi) * integral_{-inf}^{inf} g(tau)/(t - tau) dtau
G_hat(f) = -j * sgn(f) * G(f)
sgn(f) = +1 for f > 0, -1 for f < 0
Hilbert{cos(2*pi*f0*t)} = sin(2*pi*f0*t)
Hilbert{sin(2*pi*f0*t)} = -cos(2*pi*f0*t)
THE MISTAKE STUDENTS MAKE
Students call the Hilbert transform a filter and expect it to remove something. It removes nothing: |H(f)| = 1 everywhere. Every bit of energy in the signal is still present in g-hat(t); only the phase relationships have changed.
Source: Digital Communication Systems, 1st ed., Ch. 2, pp. 42-45 | CO1 | Bloom L2
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is g(t) = cos(2*pi*f0*t), a single tone. Work at the pace of the slowest note-taker and land hard on the result: The Hilbert transform of cos is sin, and applying it twice returns the negative of the original — consistent with (-j*sgn(f))^2 =… Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 1: Bandpass Signals to Equivalent Lowpass and Signalling over AWGN Channels. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 2, pp. 42-45. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 11
Properties of the Hilbert transform and why they matter
What it is, why it works, and what it costs.
VTU BEC503 | Module 1
Properties of the Hilbert transform a…
11
THE MECHANISM
Three properties do all the work later. First, g(t) and g-hat(t) have the same amplitude spectrum, hence the same energy, because the transform touches only phase. Second, a signal and its Hilbert transform are orthogonal over all time, so their inner product is zero — this is what allows in-phase and quadrature channels to share a band without interfering. Third, applying the transform twice returns -g(t), because multiplying by -j*sgn(f) twice gives -1. The kernel 1/(pi*t) is non-zero for negative t, so the ideal transformer is non-causal and any implementation must accept delay.
KEY TERMS
• energy conservation
• orthogonality
• double transform
• even and odd symmetry
• non-causality
TAKEAWAY
Same energy, orthogonal to the original, and self-inverse up to a sign — these three properties are what make quadrature signalling possible.
DIAGRAM FOR PHASE 2
Three cards arranged left to right on a common baseline. Card one, headed "Energy", shows two identical spectral magnitude plots side by side with an equals sign between them and the caption "E{g} = E{g-hat}".…
Source: Digital Communication Systems, 1st ed., Ch. 2, pp. 42-45
CO1 | Bloom L3 | visual id: hilbert-properties-triad
Notes: What to say: Give them the idea before the formalism. Say it plainly first: Three properties do all the work later. Then add the part they are examined on - Same energy, orthogonal to the original, and self-inverse up to a sign — these three properties are what make quadrature sig… Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "energy conservation" constrain here, and what would break if it did not hold? Animation instructions: the three cards rise in sequence from the baseline, then inside card two the positive and negative shaded lobes fill and visibly cancel to zero, then inside card three the chain arrows draw one after the other and the final waveform flips vertically. Transition style: Fade [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 1: Bandpass Signals to Equivalent Lowpass and Signalling over AWGN Channels. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 2, pp. 42-45. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 12
Properties of the Hilbert transform and why they matter - how it works
The procedure in order, and what each pass costs you.
VTU BEC503 | Module 1
Properties of the Hilbert transform a…
12
1. Energy: |G-hat(f)| = |G(f)| for all f, so Parseval gives equal energies
2. Orthogonality: the product spectrum is odd, so its integral vanishes
3. Double transform: (-j*sgn(f))^2 = -1, hence Hilbert{Hilbert{g}} = -g
4. Symmetry: if g(t) is even then g-hat(t) is odd, and conversely
5. Causality: 1/(pi*t) extends to t < 0, so the ideal transformer cannot be realised in real time
COST AND BEHAVIOUR
Best: properties are exact for finite-energy signals
Typical: orthogonality holds over infinite time, approximately over a symbol
Worst: truncated FIR implementations break exact orthogonality at band edges
WHAT THAT MEANS
The orthogonality that quadrature modulation relies on degrades first at the edges of the band.
Source: Digital Communication Systems, 1st ed., Ch. 2, pp. 42-45 | CO1 | Bloom L3
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Energy: |G-hat(f)| = |G(f)| for all f, so Parseval gives equal energies - and check everyone has written it before moving on. At the cost panel, translate it: The orthogonality that quadrature modulation relies on degrades first at the edges of the band. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 1: Bandpass Signals to Equivalent Lowpass and Signalling over AWGN Channels. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 2, pp. 42-45. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 13
Properties of the Hilbert transform and why they matter - worked example
One concrete case, carried all the way to a stated number.
VTU BEC503 | Module 1
Properties of the Hilbert transform a…
13
GIVEN
g(t) = cos(2*pi*f0*t) over an integer number of periods, so g-hat(t) = sin(2*pi*f0*t).
1. Product g(t)*g-hat(t) = cos*sin = (1/2)sin(4*pi*f0*t)
2. Integrate over an integer number of periods of the doubled frequency
3. The positive and negative half-cycles cancel exactly
4. Energy check: mean square of cos and of sin are both 1/2
RESULT
Inner product is zero and energies are equal, confirming orthogonality and energy conservation on a concrete case.
Energy: integral |g(t)|^2 dt = integral |g_hat(t)|^2 dt
Orthogonality: integral g(t) * g_hat(t) dt = 0
Double: Hilbert{Hilbert{g(t)}} = -g(t)
Symmetry: g(t) even => g_hat(t) odd
g(t) odd => g_hat(t) even
THE MISTAKE STUDENTS MAKE
Students assume orthogonality of g and g-hat holds over any finite interval. It holds over all time, and over a symbol interval only when the interval contains a whole number of carrier cycles. Non-integer cycle counts leave a residue that shows up as I/Q crosstalk.
Source: Digital Communication Systems, 1st ed., Ch. 2, pp. 42-45 | CO1 | Bloom L3
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is g(t) = cos(2*pi*f0*t) over an integer number of periods, so g-hat(t) = sin(2*pi*f0*t). Work at the pace of the slowest note-taker and land hard on the result: Inner product is zero and energies are equal, confirming orthogonality and energy conservation on a concrete case. Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 1: Bandpass Signals to Equivalent Lowpass and Signalling over AWGN Channels. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 2, pp. 42-45. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 14
The pre-envelope, or analytic signal
What it is, why it works, and what it costs.
VTU BEC503 | Module 1
The pre-envelope, or analytic signal
14
THE MECHANISM
The pre-envelope of a real signal g(t) is g_plus(t) = g(t) + j*g-hat(t). Its Fourier transform is 2G(f) for f > 0 and exactly zero for f < 0, so the whole negative-frequency half of the spectrum has been annihilated and the positive half doubled. This is the payoff of the 90-degree phase shift: adding j times the shifted copy makes the two halves cancel on one side and reinforce on the other. The price is that g_plus(t) is complex even though g(t) was real, which is unavoidable — a signal with a one-sided spectrum cannot be real-valued, because real signals have conjugate-symmetric spectra.
KEY TERMS
• pre-envelope
• analytic signal
• one-sided spectrum
• positive-frequency content
• complex-valued signal
TAKEAWAY
Adding j times the Hilbert transform deletes the negative-frequency half of the spectrum; the cost of a one-sided spectrum is that the signal must go complex.
DIAGRAM FOR PHASE 2
Three frequency-domain rows stacked vertically, all sharing a vertical zero-frequency line. Row one shows G(f): two lobes of equal height at -fc and +fc, labelled "real signal, conjugate symmetric". Row two sh…
Source: Digital Communication Systems, 1st ed., Ch. 2, pp. 45-47
CO1 | Bloom L3 | visual id: pre-envelope-spectrum-cancellation
Notes: What to say: Give them the idea before the formalism. Say it plainly first: The pre-envelope of a real signal g(t) is g_plus(t) = g(t) + j*g-hat(t). Then add the part they are examined on - Adding j times the Hilbert transform deletes the negative-frequency half of the spectrum; the cost of a one-sided spectrum i… Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "pre-envelope" constrain here, and what would break if it did not hold? Animation instructions: row one fades in, then row two fades in beneath it, then the two negative-frequency lobes slide together and visibly annihilate to a flat line while the two positive lobes stack and double in height, then the row-three label lands. Transition style: Fade [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 1: Bandpass Signals to Equivalent Lowpass and Signalling over AWGN Channels. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 2, pp. 45-47. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 15
The pre-envelope, or analytic signal - how it works
The procedure in order, and what each pass costs you.
VTU BEC503 | Module 1
The pre-envelope, or analytic signal
15
1. Compute the Hilbert transform g-hat(t) of the real signal
2. Form g_plus(t) = g(t) + j*g-hat(t)
3. Verify in the frequency domain: G_plus(f) = 2G(f) for f > 0, 0 for f < 0
4. Note the signal is now complex-valued
5. Recover the original as g(t) = Re{g_plus(t)}
COST AND BEHAVIOUR
Best: exact and invertible: the real part recovers g(t) exactly
Typical: storage doubles, from one real sequence to one complex sequence
Worst: requires the Hilbert transform, which is non-causal in ideal form
WHAT THAT MEANS
The doubling in storage is repaid immediately at the next step, when the sampling rate drops.
Source: Digital Communication Systems, 1st ed., Ch. 2, pp. 45-47 | CO1 | Bloom L3
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Compute the Hilbert transform g-hat(t) of the real signal - and check everyone has written it before moving on. At the cost panel, translate it: The doubling in storage is repaid immediately at the next step, when the sampling rate drops. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 1: Bandpass Signals to Equivalent Lowpass and Signalling over AWGN Channels. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 2, pp. 45-47. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 16
The pre-envelope, or analytic signal - worked example
One concrete case, carried all the way to a stated number.
VTU BEC503 | Module 1
The pre-envelope, or analytic signal
16
GIVEN
g(t) = cos(2*pi*fc*t).
1. g-hat(t) = sin(2*pi*fc*t)
2. g_plus(t) = cos(2*pi*fc*t) + j*sin(2*pi*fc*t)
3. By Euler, this is exp(j*2*pi*fc*t)
4. Its spectrum is a single impulse at +fc, with nothing at -fc
RESULT
The pre-envelope of a cosine is a complex exponential — the textbook one-sided spectrum, and the cleanest possible demonstration of the construction.
g_plus(t) = g(t) + j * g_hat(t)
G_plus(f) = 2*G(f) for f > 0
= G(0) for f = 0
= 0 for f < 0
Example: g(t) = cos(2*pi*fc*t)
g_plus(t) = exp(j*2*pi*fc*t)
Recovery: g(t) = Re{ g_plus(t) }
THE MISTAKE STUDENTS MAKE
Students expect the pre-envelope to be the envelope. It is not: the pre-envelope still oscillates at the carrier frequency. The envelope only appears after the carrier is removed at the next step, and the magnitude |g_plus(t)| is what equals the envelope.
Source: Digital Communication Systems, 1st ed., Ch. 2, pp. 45-47 | CO1 | Bloom L3
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is g(t) = cos(2*pi*fc*t). Work at the pace of the slowest note-taker and land hard on the result: The pre-envelope of a cosine is a complex exponential — the textbook one-sided spectrum, and the cleanest possible demonstration… Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 1: Bandpass Signals to Equivalent Lowpass and Signalling over AWGN Channels. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 2, pp. 45-47. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 17
The complex envelope: removing the carrier
What it is, why it works, and what it costs.
VTU BEC503 | Module 1
The complex envelope: removing the ca…
17
THE MECHANISM
The complex envelope is g-tilde(t) = g_plus(t)*exp(-j*2*pi*fc*t), the pre-envelope translated down so that the carrier sits at zero frequency. Its spectrum occupies -W to +W, a genuine baseband signal, and it is complex because the pre-envelope was. All the information originally spread around fc is now packed into a slowly varying complex function whose magnitude is the amplitude modulation and whose argument is the phase modulation. Every simulation of a modem operates on this signal, because it is the smallest complete description of what the transmitter is actually saying.
KEY TERMS
• complex envelope
• frequency translation
• baseband
• modulating signal
• natural envelope
TAKEAWAY
Multiplying the pre-envelope by exp(-j*2*pi*fc*t) slides the spectrum to baseband and leaves the complex envelope — the smallest complete description of the modulation.
DIAGRAM FOR PHASE 2
Left half: a frequency axis with a single lobe of width 2W sitting at +fc, labelled "pre-envelope". A multiply block marked "x exp(-j 2 pi fc t)" sits between the halves. Right half: the same lobe now centred…
Source: Digital Communication Systems, 1st ed., Ch. 2, pp. 47-49
CO1 | Bloom L3 | visual id: complex-envelope-translation
Notes: What to say: Give them the idea before the formalism. Say it plainly first: The complex envelope is g-tilde(t) = g_plus(t)*exp(-j*2*pi*fc*t), the pre-envelope translated down so that the carrier sits at zero frequency. Then add the part they are examined on - Multiplying the pre-envelope by exp(-j*2*pi*fc*t) slides the spectrum to baseband and leaves the complex envelope — the smal… Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "complex envelope" constrain here, and what would break if it did not hold? Animation instructions: the left lobe appears, then the multiply block flashes, then the lobe slides horizontally left until it is centred on zero, then the time-domain strip fades in, then the fast oscillation dims to grey while the slow envelope outline brightens and detaches to the right. Transition style: Fade [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 1: Bandpass Signals to Equivalent Lowpass and Signalling over AWGN Channels. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 2, pp. 47-49. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 18
The complex envelope: removing the carrier - how it works
The procedure in order, and what each pass costs you.
VTU BEC503 | Module 1
The complex envelope: removing the ca…
18
1. Start from the pre-envelope g_plus(t)
2. Multiply by exp(-j*2*pi*fc*t) to translate the spectrum down by fc
3. The result g-tilde(t) is complex and band-limited to |f| < W
4. Its magnitude |g-tilde(t)| is the natural envelope of the bandpass signal
5. Its argument arg{g-tilde(t)} is the phase modulation
COST AND BEHAVIOUR
Best: one complex multiply per sample
Typical: sampling rate can now be reduced to just above 2W
Worst: a frequency error in the local oscillator rotates g-tilde(t) continuously
WHAT THAT MEANS
That rotation is exactly the carrier-frequency-offset problem every real receiver has to correct.
Source: Digital Communication Systems, 1st ed., Ch. 2, pp. 47-49 | CO1 | Bloom L3
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Start from the pre-envelope g_plus(t) - and check everyone has written it before moving on. At the cost panel, translate it: That rotation is exactly the carrier-frequency-offset problem every real receiver has to correct. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 1: Bandpass Signals to Equivalent Lowpass and Signalling over AWGN Channels. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 2, pp. 47-49. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 19
The complex envelope: removing the carrier - worked example
One concrete case, carried all the way to a stated number.
VTU BEC503 | Module 1
The complex envelope: removing the ca…
19
GIVEN
Bandpass signal s(t) = 3*cos(2*pi*fc*t + pi/4).
1. Pre-envelope: s_plus(t) = 3*exp(j*(2*pi*fc*t + pi/4))
2. Multiply by exp(-j*2*pi*fc*t)
3. s-tilde(t) = 3*exp(j*pi/4), a constant
4. Magnitude 3, argument 45 degrees
RESULT
An unmodulated carrier collapses to a single constant complex number — the clearest possible statement that the carrier carries nothing.
g_tilde(t) = g_plus(t) * exp(-j*2*pi*fc*t)
G_tilde(f) = G_plus(f + fc) band-limited to |f| < W
Envelope: a(t) = |g_tilde(t)|
Phase: phi(t) = arg{ g_tilde(t) }
Reconstruct: g(t) = Re{ g_tilde(t) * exp(j*2*pi*fc*t) }
THE MISTAKE STUDENTS MAKE
Students drop the "complex" and treat g-tilde(t) as the amplitude envelope alone. Discarding the imaginary part throws away all phase modulation, so PSK and QAM signals become indistinguishable from an unmodulated carrier.
Source: Digital Communication Systems, 1st ed., Ch. 2, pp. 47-49 | CO1 | Bloom L3
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is Bandpass signal s(t) = 3*cos(2*pi*fc*t + pi/4). Work at the pace of the slowest note-taker and land hard on the result: An unmodulated carrier collapses to a single constant complex number — the clearest possible statement that the carrier carries n… Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 1: Bandpass Signals to Equivalent Lowpass and Signalling over AWGN Channels. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 2, pp. 47-49. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 20
Canonical representation: in-phase and quadrature components
What it is, why it works, and what it costs.
VTU BEC503 | Module 1
Canonical representation: in-phase an…
20
THE MECHANISM
Writing the complex envelope in rectangular form, g-tilde(t) = gI(t) + j*gQ(t), gives the canonical representation of the bandpass signal: g(t) = gI(t)*cos(2*pi*fc*t) - gQ(t)*sin(2*pi*fc*t). The two real signals gI and gQ are the in-phase and quadrature components, both lowpass and both band-limited to W. Because cos and sin are orthogonal over a symbol, the two components ride the same carrier frequency without interfering, which doubles the data a given bandwidth can carry. This form is the direct blueprint for hardware: two baseband paths, two mixers driven 90 degrees apart, one summing junction.
KEY TERMS
• in-phase component
• quadrature component
• canonical form
• I/Q
• quadrature modulator
TAKEAWAY
Every bandpass signal is two real lowpass signals on orthogonal carriers — that is why one band can carry two independent streams.
DIAGRAM FOR PHASE 2
A left-to-right block diagram. Two input arrows at the left labelled "gI(t)" and "gQ(t)" feed two multiplier circles. A local oscillator box at the bottom centre feeds the upper multiplier directly, labelled "…
Source: Digital Communication Systems, 1st ed., Ch. 2, pp. 49-52
CO1 | Bloom L3 | visual id: iq-modulator-blockchain
Notes: What to say: Give them the idea before the formalism. Say it plainly first: Writing the complex envelope in rectangular form, g-tilde(t) = gI(t) + j*gQ(t), gives the canonical representation of the bandpass signal: g(t) = gI(t)*co… Then add the part they are examined on - Every bandpass signal is two real lowpass signals on orthogonal carriers — that is why one band can carry two independent st… Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "in-phase component" constrain here, and what would break if it did not hold? Animation instructions: the two input arrows draw, then the oscillator box and its two branches appear with the -90 degree box flashing, then the two multipliers light in turn, then the summing junction fills and the output arrow extends, then the phasor inset draws the I axis, the Q axis, and finally the resultant. Transition style: Fade [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 1: Bandpass Signals to Equivalent Lowpass and Signalling over AWGN Channels. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 2, pp. 49-52. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 21
Canonical representation: in-phase and quadrature compo… - how it works
The procedure in order, and what each pass costs you.
VTU BEC503 | Module 1
Canonical representation: in-phase an…
21
1. Split the complex envelope into real and imaginary parts: gI = Re{g-tilde}, gQ = Im{g-tilde}
2. Multiply gI(t) by cos(2*pi*fc*t)
3. Multiply gQ(t) by -sin(2*pi*fc*t)
4. Sum the two products to obtain the real bandpass signal
5. At the receiver, multiply by cos and by -sin and lowpass filter to recover gI and gQ
COST AND BEHAVIOUR
Best: two multipliers and one adder in hardware
Typical: doubles spectral efficiency relative to a single real carrier
Worst: gain or phase mismatch between the I and Q paths leaks one channel into the other
WHAT THAT MEANS
I/Q imbalance is the dominant impairment in cheap direct-conversion radios.
Source: Digital Communication Systems, 1st ed., Ch. 2, pp. 49-52 | CO1 | Bloom L3
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Split the complex envelope into real and imaginary parts: gI = Re{g-tilde}, gQ = Im{g-tilde} - and check everyone has written it before moving on. At the cost panel, translate it: I/Q imbalance is the dominant impairment in cheap direct-conversion radios. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 1: Bandpass Signals to Equivalent Lowpass and Signalling over AWGN Channels. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 2, pp. 49-52. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 22
Canonical representation: in-phase and quadrature compo… - worked example
One concrete case, carried all the way to a stated number.
VTU BEC503 | Module 1
Canonical representation: in-phase an…
22
GIVEN
gI(t) = 1, gQ(t) = 1, both constant over the symbol.
1. g(t) = 1*cos(2*pi*fc*t) - 1*sin(2*pi*fc*t)
2. Combine: g(t) = sqrt(2)*cos(2*pi*fc*t + pi/4)
3. Envelope is sqrt(2), phase is +45 degrees
4. This is one of the four QPSK constellation points
RESULT
Two unit baseband values produce a carrier of amplitude 1.414 at 45 degrees — the arithmetic behind every QPSK constellation diagram.
g_tilde(t) = gI(t) + j*gQ(t)
g(t) = gI(t)*cos(2*pi*fc*t) - gQ(t)*sin(2*pi*fc*t)
Recovery at the receiver:
gI(t) = LPF{ 2*g(t)*cos(2*pi*fc*t) }
gQ(t) = LPF{ -2*g(t)*sin(2*pi*fc*t) }
THE MISTAKE STUDENTS MAKE
Students write a plus sign in front of the quadrature term. The canonical form carries a minus, which follows from Re{(gI + j gQ)(cos + j sin)}. A sign error here rotates the whole constellation and inverts every quadrature decision.
Source: Digital Communication Systems, 1st ed., Ch. 2, pp. 49-52 | CO1 | Bloom L3
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is gI(t) = 1, gQ(t) = 1, both constant over the symbol. Work at the pace of the slowest note-taker and land hard on the result: Two unit baseband values produce a carrier of amplitude 1.414 at 45 degrees — the arithmetic behind every QPSK constellation diag… Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 1: Bandpass Signals to Equivalent Lowpass and Signalling over AWGN Channels. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 2, pp. 49-52. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 23
Polar form: natural envelope and phase
What it is, why it works, and what it costs.
VTU BEC503 | Module 1
Polar form: natural envelope and phase
23
THE MECHANISM
The same complex envelope written in polar form is g-tilde(t) = a(t)*exp(j*phi(t)), giving g(t) = a(t)*cos(2*pi*fc*t + phi(t)). Here a(t) = sqrt(gI^2 + gQ^2) is the natural envelope, always non-negative, and phi(t) = atan2(gQ, gI) is the instantaneous phase. The polar form is the right one when reasoning about amplitude modulation, envelope detection or the peak-to-average power ratio that decides how hard a power amplifier is driven; the rectangular form is the right one when reasoning about hardware and about decisions. They are the same object, and converting between them is the same operation as converting between Cartesian and polar coordinates.
KEY TERMS
• natural envelope
• instantaneous phase
• polar form
• envelope detector
• phase trajectory
TAKEAWAY
Rectangular form suits circuits and decisions; polar form suits amplifiers and envelope arguments — pick by the question, not by habit.
DIAGRAM FOR PHASE 2
A single complex plane with I on the horizontal axis and Q on the vertical. A point P sits in the first quadrant. Dashed grey lines drop from P to both axes and are labelled "gI" and "gQ". A solid arrow runs f…
Source: Digital Communication Systems, 1st ed., Ch. 2, pp. 49-52
CO1 | Bloom L3 | visual id: polar-rectangular-duality
Notes: What to say: Give them the idea before the formalism. Say it plainly first: The same complex envelope written in polar form is g-tilde(t) = a(t)*exp(j*phi(t)), giving g(t) = a(t)*cos(2*pi*fc*t + phi(t)). Then add the part they are examined on - Rectangular form suits circuits and decisions; polar form suits amplifiers and envelope arguments — pick by the question, no… Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "natural envelope" constrain here, and what would break if it did not hold? Animation instructions: the axes draw, then point P appears, then the two dashed projections drop to the axes with their labels, then the radius arrow sweeps out from the origin and the angle arc fills, then the two formula cards slide in from left and right, then the time strip fades up. Transition style: Fade [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 1: Bandpass Signals to Equivalent Lowpass and Signalling over AWGN Channels. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 2, pp. 49-52. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 24
Polar form: natural envelope and phase - how it works
The procedure in order, and what each pass costs you.
VTU BEC503 | Module 1
Polar form: natural envelope and phase
24
1. Compute a(t) = sqrt(gI(t)^2 + gQ(t)^2)
2. Compute phi(t) = atan2(gQ(t), gI(t)), using the four-quadrant form
3. Note a(t) >= 0 always; all sign information lives in phi(t)
4. Convert back with gI = a*cos(phi) and gQ = a*sin(phi)
5. For peak-to-average power ratio, work with max{a^2}/mean{a^2}
COST AND BEHAVIOUR
Best: exact conversion, no approximation involved
Typical: a square root and an arctangent per sample
Worst: phase is undefined when a(t) = 0, and unwrapping is needed across 2*pi boundaries
WHAT THAT MEANS
CORDIC hardware computes both without a multiplier, which is why it is standard in radios.
Source: Digital Communication Systems, 1st ed., Ch. 2, pp. 49-52 | CO1 | Bloom L3
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Compute a(t) = sqrt(gI(t)^2 + gQ(t)^2) - and check everyone has written it before moving on. At the cost panel, translate it: CORDIC hardware computes both without a multiplier, which is why it is standard in radios. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 1: Bandpass Signals to Equivalent Lowpass and Signalling over AWGN Channels. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 2, pp. 49-52. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 25
Polar form: natural envelope and phase - worked example
One concrete case, carried all the way to a stated number.
VTU BEC503 | Module 1
Polar form: natural envelope and phase
25
GIVEN
gI = -1, gQ = 1 over one symbol.
1. a = sqrt((-1)^2 + 1^2) = sqrt(2) = 1.414
2. atan2(1, -1) = 135 degrees, correctly placed in the second quadrant
3. A two-quadrant arctan would have returned -45 degrees, the wrong quadrant
4. Bandpass signal: 1.414*cos(2*pi*fc*t + 135 degrees)
RESULT
Envelope 1.414 at 135 degrees. The four-quadrant atan2 is what keeps the point out of the wrong half-plane.
g_tilde(t) = a(t) * exp(j*phi(t))
a(t) = sqrt( gI(t)^2 + gQ(t)^2 ) >= 0
phi(t) = atan2( gQ(t), gI(t) ) four-quadrant
g(t) = a(t) * cos(2*pi*fc*t + phi(t))
PAPR = max{a(t)^2} / mean{a(t)^2}
THE MISTAKE STUDENTS MAKE
Students use a two-argument-free arctan, atan(gQ/gI), and lose the quadrant. Points in the second and third quadrants are reported 180 degrees away from their true position, which silently inverts half the constellation.
Source: Digital Communication Systems, 1st ed., Ch. 2, pp. 49-52 | CO1 | Bloom L3
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is gI = -1, gQ = 1 over one symbol. Work at the pace of the slowest note-taker and land hard on the result: Envelope 1.414 at 135 degrees. The four-quadrant atan2 is what keeps the point out of the wrong half-plane. Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 1: Bandpass Signals to Equivalent Lowpass and Signalling over AWGN Channels. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 2, pp. 49-52. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 26
The AWGN channel model and what it assumes
What it is, why it works, and what it costs.
VTU BEC503 | Module 1
The AWGN channel model and what it as…
26
THE MECHANISM
The additive white Gaussian noise channel model says the received waveform is x(t) = s(t) + w(t), where w(t) is a sample function of a zero-mean Gaussian process with two-sided power spectral density N0/2 watts per hertz, constant over all frequencies. Three separate claims are packed in: additive, meaning the noise does not depend on the signal; white, meaning samples at distinct times are uncorrelated; and Gaussian, meaning the amplitude distribution is normal, which follows from the central limit theorem applied to enormous numbers of independent electron motions. It is the right model for thermal noise in a receiver front end and the wrong model for interference, impulsive noise or fading, all of which violate at least one of the three claims.
KEY TERMS
• AWGN
• white noise
• power spectral density N0/2
• additive channel
• thermal noise
TAKEAWAY
AWGN is three assumptions, not one; every result in this module inherits all three, and each fails in a different real channel.
DIAGRAM FOR PHASE 2
A central channel block with an input arrow "s(t)" on the left, a summing circle inside fed from below by an arrow labelled "w(t)", and an output arrow "x(t) = s(t) + w(t)" on the right. Three callout cards fa…
Source: Digital Communication Systems, 1st ed., Ch. 7, pp. 323-324
CO1 | Bloom L2 | visual id: awgn-three-assumptions
Notes: What to say: Give them the idea before the formalism. Say it plainly first: The additive white Gaussian noise channel model says the received waveform is x(t) = s(t) + w(t), where w(t) is a sample function of a zero-mean Gaussian… Then add the part they are examined on - AWGN is three assumptions, not one; every result in this module inherits all three, and each fails in a different real chann… Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "AWGN" constrain here, and what would break if it did not hold? Animation instructions: the channel block draws with its input arrow, then the noise arrow rises into the summing circle which flashes, then the output arrow extends, then the three cards fan out one at a time, then the three red failure footnotes appear together. Transition style: Fade [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 1: Bandpass Signals to Equivalent Lowpass and Signalling over AWGN Channels. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 7, pp. 323-324. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 27
The AWGN channel model and what it assumes - how it works
The procedure in order, and what each pass costs you.
VTU BEC503 | Module 1
The AWGN channel model and what it as…
27
1. Model the received waveform as x(t) = s(t) + w(t)
2. Take w(t) zero-mean Gaussian with PSD Sw(f) = N0/2 for all f
3. Note the autocorrelation is an impulse: Rw(tau) = (N0/2)*delta(tau)
4. Conclude that samples at distinct instants are uncorrelated, hence independent for a Gaussian process
5. Check the three assumptions against the real channel before using any result derived from them
COST AND BEHAVIOUR
Best: analytically tractable — closed-form error probabilities follow
Typical: good model for a thermal-noise-limited receiver
Worst: infinite total power, since a flat PSD over infinite bandwidth integrates to infinity
WHAT THAT MEANS
The infinity is harmless: only noise inside the receiver bandwidth ever reaches the decision.
Source: Digital Communication Systems, 1st ed., Ch. 7, pp. 323-324 | CO1 | Bloom L2
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Model the received waveform as x(t) = s(t) + w(t) - and check everyone has written it before moving on. At the cost panel, translate it: The infinity is harmless: only noise inside the receiver bandwidth ever reaches the decision. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 1: Bandpass Signals to Equivalent Lowpass and Signalling over AWGN Channels. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 7, pp. 323-324. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 28
The AWGN channel model and what it assumes - worked example
One concrete case, carried all the way to a stated number.
VTU BEC503 | Module 1
The AWGN channel model and what it as…
28
GIVEN
A receiver of bandwidth B = 1 MHz with N0 = 4 x 10^-21 W/Hz.
1. Noise power in the band: P = N0 * B for a real bandpass filter of width B
2. P = 4 x 10^-21 x 10^6 = 4 x 10^-15 W
3. In dBm: 10*log10(4 x 10^-15 / 10^-3) = -114 dBm
4. Widening the bandwidth to 10 MHz raises this by 10 dB
RESULT
A 1 MHz receiver sees about -114 dBm of thermal noise; every doubling of bandwidth costs 3 dB of noise floor.
x(t) = s(t) + w(t)
E[w(t)] = 0
Sw(f) = N0/2 for all f (two-sided)
Rw(tau) = (N0/2) * delta(tau)
Noise power in bandwidth B: P = N0 * B
Thermal: N0 = k*T, k = 1.38e-23 J/K
THE MISTAKE STUDENTS MAKE
Students read N0/2 as half the noise power. It is the two-sided power spectral density; the one-sided density is N0. Using N0/2 where N0 belongs produces error probabilities that are wrong by 3 dB.
Source: Digital Communication Systems, 1st ed., Ch. 7, pp. 323-324 | CO1 | Bloom L2
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is A receiver of bandwidth B = 1 MHz with N0 = 4 x 10^-21 W/Hz. Work at the pace of the slowest note-taker and land hard on the result: A 1 MHz receiver sees about -114 dBm of thermal noise; every doubling of bandwidth costs 3 dB of noise floor. Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 1: Bandpass Signals to Equivalent Lowpass and Signalling over AWGN Channels. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 7, pp. 323-324. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 29
Geometric representation: signals as points in a vector space
What it is, why it works, and what it costs.
VTU BEC503 | Module 1
Geometric representation: signals as…
29
THE MECHANISM
A set of M finite-energy waveforms can always be written as linear combinations of at most M orthonormal basis functions, so each waveform is completely described by its N coefficients and becomes a point in an N-dimensional Euclidean space. The inner product of two waveforms equals the dot product of their coefficient vectors, and the energy of a waveform equals the squared length of its vector — the Parseval relation in geometric dress. This is the central move of the module: an infinite-dimensional problem about continuous functions collapses to a finite-dimensional problem about points, and every question about detection becomes a question about distance.
KEY TERMS
• signal space
• orthonormal basis
• signal constellation
• dimension
• inner product
TAKEAWAY
Once signals are points and energy is squared length, detection is geometry — and the answer is always the nearest point.
DIAGRAM FOR PHASE 2
Left panel: three time-domain waveforms s1(t), s2(t), s3(t) drawn stacked. A wide arrow labelled "project onto basis" points right. Right panel: a two-dimensional plane with axes labelled "phi1" and "phi2", ca…
Source: Digital Communication Systems, 1st ed., Ch. 7, pp. 324-332
CO1 | Bloom L3 | visual id: signal-space-projection
Notes: What to say: Give them the idea before the formalism. Say it plainly first: A set of M finite-energy waveforms can always be written as linear combinations of at most M orthonormal basis functions, so each waveform is completely d… Then add the part they are examined on - Once signals are points and energy is squared length, detection is geometry — and the answer is always the nearest point. Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "signal space" constrain here, and what would break if it did not hold? Animation instructions: the three waveforms fade in on the left one at a time, then the projection arrow sweeps right, then the two axes draw, then each dot flies from its waveform to its position in the plane in turn, then the dashed coordinates appear on one dot, then the caption lands. Transition style: Fade [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 1: Bandpass Signals to Equivalent Lowpass and Signalling over AWGN Channels. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 7, pp. 324-332. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 30
Geometric representation: signals as points in a vector… - how it works
The procedure in order, and what each pass costs you.
VTU BEC503 | Module 1
Geometric representation: signals as…
30
1. Collect the M signal waveforms of the modulation scheme
2. Find an orthonormal basis phi1..phiN spanning them, with N <= M
3. Compute coefficients s_ij = integral of s_i(t)*phi_j(t) dt
4. Represent each waveform by its vector s_i = [s_i1, ..., s_iN]
5. Read energy as ||s_i||^2 and inter-signal distance as ||s_i - s_k||
COST AND BEHAVIOUR
Best: N = 1 for binary antipodal signalling
Typical: N <= M always, and usually far smaller than M
Worst: M orthogonal signals need N = M dimensions
WHAT THAT MEANS
The dimension N is the real cost driver: it sets both bandwidth and receiver complexity.
Source: Digital Communication Systems, 1st ed., Ch. 7, pp. 324-332 | CO1 | Bloom L3
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Collect the M signal waveforms of the modulation scheme - and check everyone has written it before moving on. At the cost panel, translate it: The dimension N is the real cost driver: it sets both bandwidth and receiver complexity. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 1: Bandpass Signals to Equivalent Lowpass and Signalling over AWGN Channels. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 7, pp. 324-332. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 31
Geometric representation: signals as points in a vector… - worked example
One concrete case, carried all the way to a stated number.
VTU BEC503 | Module 1
Geometric representation: signals as…
31
GIVEN
Binary antipodal signalling: s1(t) = +sqrt(Eb)*phi(t), s2(t) = -sqrt(Eb)*phi(t).
1. One basis function suffices, so N = 1
2. Vectors are the scalars s1 = +sqrt(Eb) and s2 = -sqrt(Eb)
3. Energy of each: (sqrt(Eb))^2 = Eb
4. Distance between them: |s1 - s2| = 2*sqrt(Eb)
RESULT
BPSK lives on a line, with the two points 2*sqrt(Eb) apart — the largest separation any two signals of energy Eb can achieve.
s_i(t) = sum_{j=1}^{N} s_ij * phi_j(t), i = 1..M
s_ij = integral_0^T s_i(t) * phi_j(t) dt
Orthonormality:
integral phi_i(t)*phi_j(t) dt = 1 if i = j, 0 otherwise
Energy: E_i = sum_j s_ij^2 = ||s_i||^2
Distance: d_ik = ||s_i - s_k||
THE MISTAKE STUDENTS MAKE
Students assume the number of basis functions equals the number of signals. N is the dimension of the space the signals span, and it is often far smaller than M — QPSK has M = 4 signals but N = 2 dimensions.
Source: Digital Communication Systems, 1st ed., Ch. 7, pp. 324-332 | CO1 | Bloom L3
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is Binary antipodal signalling: s1(t) = +sqrt(Eb)*phi(t), s2(t) = -sqrt(Eb)*phi(t). Work at the pace of the slowest note-taker and land hard on the result: BPSK lives on a line, with the two points 2*sqrt(Eb) apart — the largest separation any two signals of energy Eb can achieve. Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 1: Bandpass Signals to Equivalent Lowpass and Signalling over AWGN Channels. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 7, pp. 324-332. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 32
The Gram-Schmidt orthogonalization procedure
What it is, why it works, and what it costs.
VTU BEC503 | Module 1
The Gram-Schmidt orthogonalization pr…
32
THE MECHANISM
Gram-Schmidt is the constructive algorithm that turns any set of M waveforms into an orthonormal basis for the space they span. It processes the signals in order: the first basis function is the first signal normalised; each later basis function is formed by subtracting from the next signal its projections onto all basis functions already built, then normalising what remains. If the remainder is zero the signal was linearly dependent on its predecessors and contributes no new dimension, which is precisely how the algorithm discovers that N < M. The order of processing changes the basis obtained but never changes N or any distance between signal points.
KEY TERMS
• Gram-Schmidt
• orthonormalisation
• projection
• linear independence
• basis construction
TAKEAWAY
Subtract what is already represented, normalise what is left — and a zero remainder tells you the signal added no new dimension.
DIAGRAM FOR PHASE 2
A two-dimensional plane. Step one shows vector s1 drawn from the origin and, beside it, a shorter unit vector along the same direction labelled "phi1 = s1/||s1||". Step two shows s2 drawn, with a dashed projec…
Source: Digital Communication Systems, 1st ed., Ch. 7, pp. 324-332
CO1 | Bloom L4 | visual id: gram-schmidt-two-step
Notes: What to say: Give them the idea before the formalism. Say it plainly first: Gram-Schmidt is the constructive algorithm that turns any set of M waveforms into an orthonormal basis for the space they span. Then add the part they are examined on - Subtract what is already represented, normalise what is left — and a zero remainder tells you the signal added no new dimens… Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "Gram-Schmidt" constrain here, and what would break if it did not hold? Animation instructions: s1 draws from the origin, then shrinks-copies into phi1, then s2 draws, then the dashed projection drops from s2 onto phi1, then the residual arrow rises from the projection tip to s2, then it rotates to the origin and normalises into phi2 with the right-angle square snapping into place, then the caption appears. Transition style: Fade [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 1: Bandpass Signals to Equivalent Lowpass and Signalling over AWGN Channels. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 7, pp. 324-332. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 33
The Gram-Schmidt orthogonalization procedure - how it works
The procedure in order, and what each pass costs you.
VTU BEC503 | Module 1
The Gram-Schmidt orthogonalization pr…
33
1. Set phi1(t) = s1(t)/sqrt(E1), where E1 is the energy of s1
2. For each subsequent signal s_i, compute its projections s_ij onto every existing phi_j
3. Form the residual g_i(t) = s_i(t) - sum_j s_ij*phi_j(t)
4. If the residual has zero energy, skip it: s_i adds no new dimension
5. Otherwise normalise the residual to obtain the next basis function and continue
COST AND BEHAVIOUR
Best: signals already orthogonal — each normalisation is one division
Typical: O(M^2 N) inner products for M signals in N dimensions
Worst: numerically unstable for nearly parallel signals; modified Gram-Schmidt is preferred
WHAT THAT MEANS
Classical Gram-Schmidt loses orthogonality in floating point; the modified variant costs the same and does not.
Source: Digital Communication Systems, 1st ed., Ch. 7, pp. 324-332 | CO1 | Bloom L4
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Set phi1(t) = s1(t)/sqrt(E1), where E1 is the energy of s1 - and check everyone has written it before moving on. At the cost panel, translate it: Classical Gram-Schmidt loses orthogonality in floating point; the modified variant costs the same and does not. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 1: Bandpass Signals to Equivalent Lowpass and Signalling over AWGN Channels. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 7, pp. 324-332. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 34
The Gram-Schmidt orthogonalization procedure - worked example
One concrete case, carried all the way to a stated number.
VTU BEC503 | Module 1
The Gram-Schmidt orthogonalization pr…
34
GIVEN
s1(t) = 1 on [0,1]; s2(t) = 1 on [0,0.5] and 0 on [0.5,1].
1. E1 = 1, so phi1(t) = 1 on [0,1]
2. Projection of s2 on phi1: s21 = integral over [0,0.5] of 1 = 0.5
3. Residual g2(t) = s2(t) - 0.5*phi1(t): equals +0.5 on [0,0.5] and -0.5 on [0.5,1]
4. Energy of g2 = 0.25*0.5 + 0.25*0.5 = 0.25, so ||g2|| = 0.5 and phi2 = g2/0.5 = +1 then -1
RESULT
Two signals, two dimensions. s1 sits at [1, 0] and s2 at [0.5, 0.5], and the basis is the constant function and the square wave.
phi_1(t) = s_1(t) / sqrt(E_1)
for i = 2..M:
s_ij = integral s_i(t) * phi_j(t) dt for j < i
g_i(t) = s_i(t) - sum_{j<i} s_ij * phi_j(t)
if energy(g_i) == 0: skip s_i, no new dimension
else: phi_i(t) = g_i(t) / sqrt(energy(g_i))
THE MISTAKE STUDENTS MAKE
Students subtract the projection of the basis function onto the signal instead of the projection of the signal onto the basis function. The coefficient must be the inner product with the unit-norm basis function, otherwise the residual is not orthogonal to what came before.
Source: Digital Communication Systems, 1st ed., Ch. 7, pp. 324-332 | CO1 | Bloom L4
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is s1(t) = 1 on [0,1]; s2(t) = 1 on [0,0.5] and 0 on [0.5,1]. Work at the pace of the slowest note-taker and land hard on the result: Two signals, two dimensions. s1 sits at [1, 0] and s2 at [0.5, 0.5], and the basis is the constant function and the square wave. Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 1: Bandpass Signals to Equivalent Lowpass and Signalling over AWGN Channels. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 7, pp. 324-332. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 35
Energy, distance and the constellation diagram
What it is, why it works, and what it costs.
VTU BEC503 | Module 1
Energy, distance and the constellatio…
35
THE MECHANISM
Plotting the M signal vectors in the N-dimensional space produces the constellation diagram, and two numbers read off it determine performance. The average symbol energy is the mean of the squared distances from the origin, and it is what the power amplifier must supply. The minimum Euclidean distance d_min is the smallest separation between any two points, and it is what noise must overcome to cause an error. Every modulation comparison in the next module is a fight over the ratio d_min^2/E_avg, because raising d_min for a fixed energy budget is the only way to buy reliability without buying power.
KEY TERMS
• constellation
• Euclidean distance
• average energy
• minimum distance
• decision region
TAKEAWAY
A constellation is judged by one ratio: minimum distance squared over average energy. Everything else is detail.
DIAGRAM FOR PHASE 2
A two-dimensional constellation plane showing four points at the corners of a square, each with a thin vector from the origin. One vector is highlighted and labelled "sqrt(E)", and a caption reads "average ene…
Source: Digital Communication Systems, 1st ed., Ch. 7, pp. 324-332
CO1 | Bloom L4 | visual id: constellation-energy-distance
Notes: What to say: Give them the idea before the formalism. Say it plainly first: Plotting the M signal vectors in the N-dimensional space produces the constellation diagram, and two numbers read off it determine performance. Then add the part they are examined on - A constellation is judged by one ratio: minimum distance squared over average energy. Everything else is detail. Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "constellation" constrain here, and what would break if it did not hold? Animation instructions: the four points appear together, then the radius vectors draw outward from the origin and the energy label lands, then the d_min arrow snaps between the two nearest points and pulses once, then the dashed boundaries sweep out from the origin to partition the plane and the tints fill, then the side card slides in. Transition style: Fade [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 1: Bandpass Signals to Equivalent Lowpass and Signalling over AWGN Channels. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 7, pp. 324-332. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 36
Energy, distance and the constellation diagram - how it works
The procedure in order, and what each pass costs you.
VTU BEC503 | Module 1
Energy, distance and the constellatio…
36
1. Plot all M signal vectors in the N-dimensional space
2. Compute each energy as the squared distance from the origin
3. Average over the M points, weighted by their probabilities, to get E_avg
4. Compute all pairwise distances and take the smallest as d_min
5. Partition the plane by perpendicular bisectors to obtain the decision regions
COST AND BEHAVIOUR
Best: binary antipodal maximises d_min for a given energy
Typical: M(M-1)/2 pairwise distances to evaluate
Worst: as M grows at fixed E_avg, d_min shrinks and errors multiply
WHAT THAT MEANS
Doubling M at constant average energy typically costs about 3 dB in required SNR.
Source: Digital Communication Systems, 1st ed., Ch. 7, pp. 324-332 | CO1 | Bloom L4
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Plot all M signal vectors in the N-dimensional space - and check everyone has written it before moving on. At the cost panel, translate it: Doubling M at constant average energy typically costs about 3 dB in required SNR. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 1: Bandpass Signals to Equivalent Lowpass and Signalling over AWGN Channels. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 7, pp. 324-332. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 37
Energy, distance and the constellation diagram - worked example
One concrete case, carried all the way to a stated number.
VTU BEC503 | Module 1
Energy, distance and the constellatio…
37
GIVEN
QPSK with points at (+a, +a), (+a, -a), (-a, +a), (-a, -a).
1. Each energy: a^2 + a^2 = 2a^2, so E_avg = 2a^2 = E
2. Nearest neighbours differ in one coordinate only: distance = 2a
3. Express in terms of E: a = sqrt(E/2), so d_min = 2*sqrt(E/2) = sqrt(2E)
4. Compare BPSK at the same energy: d_min = 2*sqrt(E)
RESULT
QPSK has d_min = sqrt(2E) against BPSK d_min = 2*sqrt(E) — a factor sqrt(2) smaller per symbol, but each symbol carries two bits, so the energy per bit is identical.
E_i = ||s_i||^2
E_avg = (1/M) * sum_i ||s_i||^2
d_ik = ||s_i - s_k||
d_min = min over i != k of d_ik
Figure of merit: d_min^2 / E_avg
Decision region Z_i = { x : ||x - s_i|| < ||x - s_k|| for all k != i }
THE MISTAKE STUDENTS MAKE
Students compare constellations by minimum distance alone. A constellation can always be scaled up to enlarge d_min; the comparison is only meaningful at equal average energy, or equivalently by the ratio d_min^2/E_avg.
Source: Digital Communication Systems, 1st ed., Ch. 7, pp. 324-332 | CO1 | Bloom L4
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is QPSK with points at (+a, +a), (+a, -a), (-a, +a), (-a, -a). Work at the pace of the slowest note-taker and land hard on the result: QPSK has d_min = sqrt(2E) against BPSK d_min = 2*sqrt(E) — a factor sqrt(2) smaller per symbol, but each symbol carries two bits,… Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 1: Bandpass Signals to Equivalent Lowpass and Signalling over AWGN Channels. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 7, pp. 324-332. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 38
Converting the continuous AWGN channel into a vector channel
What it is, why it works, and what it costs.
VTU BEC503 | Module 1
Converting the continuous AWGN channe…
38
THE MECHANISM
Projecting the received waveform x(t) onto the N basis functions produces N numbers x_j, and each equals the corresponding signal coefficient plus a noise coefficient: x_j = s_ij + w_j. The noise projections w_j are jointly Gaussian, zero mean, mutually uncorrelated and each of variance N0/2 — uncorrelated because the basis functions are orthogonal and the noise is white, and independent because uncorrelated Gaussians are independent. The continuous channel has therefore become N parallel scalar Gaussian channels, which is the whole point: a detection problem over functions has become a detection problem over N real numbers with a known joint density.
KEY TERMS
• vector channel
• noise projection
• correlator bank
• independent components
• observation vector
TAKEAWAY
Project onto the basis and the channel becomes N independent Gaussian scalars, each of variance N0/2 — the same variance on every axis.
DIAGRAM FOR PHASE 2
Left: a waveform x(t) entering a vertical stack of N correlator blocks, each drawn as a multiplier fed by phi_j(t) followed by an integrator over [0,T]. Right: N output arrows carrying x_1 .. x_N into a vector…
Source: Digital Communication Systems, 1st ed., Ch. 7, pp. 332-337
CO1 | Bloom L4 | visual id: continuous-to-vector-channel
Notes: What to say: Give them the idea before the formalism. Say it plainly first: Projecting the received waveform x(t) onto the N basis functions produces N numbers x_j, and each equals the corresponding signal coefficient plus a noise… Then add the part they are examined on - Project onto the basis and the channel becomes N independent Gaussian scalars, each of variance N0/2 — the same variance on… Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "vector channel" constrain here, and what would break if it did not hold? Animation instructions: the waveform arrow enters and fans out to all N correlators simultaneously, then each correlator lights and emits its output in top-to-bottom sequence, then the vector box assembles, then the bell curves grow beneath each output together to emphasise they are identical, then the footnote card appears. Transition style: Fade [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 1: Bandpass Signals to Equivalent Lowpass and Signalling over AWGN Channels. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 7, pp. 332-337. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 39
Converting the continuous AWGN channel into a vector ch… - how it works
The procedure in order, and what each pass costs you.
VTU BEC503 | Module 1
Converting the continuous AWGN channe…
39
1. Correlate x(t) with each basis function phi_j over the symbol interval
2. Collect the N results as the observation vector x = [x_1, ..., x_N]
3. Recognise x_j = s_ij + w_j with w_j zero-mean Gaussian of variance N0/2
4. Confirm the w_j are uncorrelated because the phi_j are orthogonal and the noise is white
5. Discard the residual component of x(t) orthogonal to the basis: it is irrelevant to the decision
COST AND BEHAVIOUR
Best: N correlators, one per dimension
Typical: reduces an infinite-dimensional problem to N real numbers
Worst: requires exact symbol timing and carrier phase to be meaningful
WHAT THAT MEANS
Every practical loss in a coherent receiver traces back to imperfect timing or phase in exactly this step.
Source: Digital Communication Systems, 1st ed., Ch. 7, pp. 332-337 | CO1 | Bloom L4
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Correlate x(t) with each basis function phi_j over the symbol interval - and check everyone has written it before moving on. At the cost panel, translate it: Every practical loss in a coherent receiver traces back to imperfect timing or phase in exactly this step. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 1: Bandpass Signals to Equivalent Lowpass and Signalling over AWGN Channels. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 7, pp. 332-337. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 40
Converting the continuous AWGN channel into a vector ch… - worked example
One concrete case, carried all the way to a stated number.
VTU BEC503 | Module 1
Converting the continuous AWGN channe…
40
GIVEN
BPSK, N = 1, transmitted +sqrt(Eb), noise variance N0/2 = 0.1, one noise draw of -0.35.
1. Signal coefficient s = +sqrt(Eb); take Eb = 1 so s = +1
2. Observation x = 1 + (-0.35) = 0.65
3. Decision threshold sits at 0 by symmetry
4. 0.65 > 0, so the decision is +1
RESULT
Correct decision. An error would need a noise draw more negative than -1, which has probability Q(sqrt(2Eb/N0)).
x_j = integral_0^T x(t) * phi_j(t) dt j = 1..N
x_j = s_ij + w_j
E[w_j] = 0
E[w_j^2] = N0/2
E[w_j w_k] = 0 for j != k
x = s_i + w, w ~ N(0, (N0/2) I_N)
THE MISTAKE STUDENTS MAKE
Students worry that the part of x(t) not captured by the basis is being thrown away. The theorem of irrelevance shows that residual contains only noise, is independent of the signal and of the retained components, and therefore cannot improve any decision.
Source: Digital Communication Systems, 1st ed., Ch. 7, pp. 332-337 | CO1 | Bloom L4
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is BPSK, N = 1, transmitted +sqrt(Eb), noise variance N0/2 = 0.1, one noise draw of -0.35. Work at the pace of the slowest note-taker and land hard on the result: Correct decision. An error would need a noise draw more negative than -1, which has probability Q(sqrt(2Eb/N0)). Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 1: Bandpass Signals to Equivalent Lowpass and Signalling over AWGN Channels. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 7, pp. 332-337. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 41
The theorem of irrelevance and sufficient statistics
What it is, why it works, and what it costs.
VTU BEC503 | Module 1
The theorem of irrelevance and suffic…
41
THE MECHANISM
The theorem of irrelevance states that the component of the received waveform lying outside the span of the signal basis is statistically independent of both the transmitted signal and the observation vector, so conditioning on it changes no likelihood and it cannot improve any decision. This makes the observation vector x a sufficient statistic: it carries every scrap of information about which signal was sent that the entire received waveform carries. The practical consequence is decisive — a receiver may discard everything except N numbers per symbol with no loss of optimality whatsoever.
KEY TERMS
• theorem of irrelevance
• sufficient statistic
• residual noise
• likelihood
• data reduction
TAKEAWAY
N numbers per symbol are provably enough; the rest of the waveform is pure noise and discarding it costs nothing.
DIAGRAM FOR PHASE 2
A large rectangle labelled "received waveform x(t)" split by a vertical line into two unequal regions. The left region, coloured green and occupying about a third, is labelled "projection onto span{phi_1..phi_…
Source: Digital Communication Systems, 1st ed., Ch. 7, pp. 332-337
CO1 | Bloom L4 | visual id: sufficient-statistic-partition
Notes: What to say: Give them the idea before the formalism. Say it plainly first: The theorem of irrelevance states that the component of the received waveform lying outside the span of the signal basis is statistically independent of b… Then add the part they are examined on - N numbers per symbol are provably enough; the rest of the waveform is pure noise and discarding it costs nothing. Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "theorem of irrelevance" constrain here, and what would break if it did not hold? Animation instructions: the full rectangle draws, then the dividing line sweeps down to split it, then the green region fills and its label lands, then the grey region fills, then the green arrow extends to the decision box, then the grey arrow extends and its terminal circle is struck through, then the caption appears. Transition style: Fade [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 1: Bandpass Signals to Equivalent Lowpass and Signalling over AWGN Channels. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 7, pp. 332-337. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 42
The theorem of irrelevance and sufficient statistics - how it works
The procedure in order, and what each pass costs you.
VTU BEC503 | Module 1
The theorem of irrelevance and suffic…
42
1. Decompose the received waveform into its projection on the basis plus a residual
2. Show the residual is independent of the transmitted signal index
3. Show the residual is independent of the observation vector components
4. Conclude the conditional likelihood depends only on the observation vector
5. Discard the residual and base the decision entirely on x
COST AND BEHAVIOUR
Best: reduces the observation from a function to N numbers
Typical: no loss of optimality, ever, under the AWGN assumptions
Worst: the result depends on the noise being white; coloured noise makes the residual informative
WHAT THAT MEANS
With coloured noise the residual correlates with the retained components, and whitening must come first.
Source: Digital Communication Systems, 1st ed., Ch. 7, pp. 332-337 | CO1 | Bloom L4
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Decompose the received waveform into its projection on the basis plus a residual - and check everyone has written it before moving on. At the cost panel, translate it: With coloured noise the residual correlates with the retained components, and whitening must come first. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 1: Bandpass Signals to Equivalent Lowpass and Signalling over AWGN Channels. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 7, pp. 332-337. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 43
The theorem of irrelevance and sufficient statistics - worked example
One concrete case, carried all the way to a stated number.
VTU BEC503 | Module 1
The theorem of irrelevance and suffic…
43
GIVEN
BPSK, N = 1, basis phi(t). Received x(t) = s(t) + w(t).
1. Project: x_1 = integral x(t)*phi(t) dt = s + w_1
2. Residual: x_r(t) = x(t) - x_1*phi(t), which contains no s at all
3. x_r(t) is a function of the noise only, and is orthogonal to phi(t)
4. For white Gaussian noise, orthogonal implies independent
RESULT
A receiver that observes only x_1 makes exactly the same decisions as one that observes the whole waveform — the reduction is free.
x(t) = sum_j x_j * phi_j(t) + x_r(t)
x_r(t) = x(t) - sum_j x_j * phi_j(t) residual
x_r(t) independent of s_i and of x
=> p(x, x_r | s_i) = p(x | s_i) * p(x_r)
=> decision based on x alone is optimal
THE MISTAKE STUDENTS MAKE
Students carry this result across to coloured noise. Irrelevance depends on whiteness: with coloured noise the residual is correlated with the retained components and genuinely does carry usable information, so the received waveform must be whitened before projecting.
Source: Digital Communication Systems, 1st ed., Ch. 7, pp. 332-337 | CO1 | Bloom L4
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is BPSK, N = 1, basis phi(t). Received x(t) = s(t) + w(t). Work at the pace of the slowest note-taker and land hard on the result: A receiver that observes only x_1 makes exactly the same decisions as one that observes the whole waveform — the reduction is fre… Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 1: Bandpass Signals to Equivalent Lowpass and Signalling over AWGN Channels. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 7, pp. 332-337. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 44
Maximum likelihood decoding and decision regions
What it is, why it works, and what it costs.
VTU BEC503 | Module 1
Maximum likelihood decoding and decis…
44
THE MECHANISM
The receiver that minimises symbol error probability chooses the signal maximising the posterior probability given the observation; when all signals are equally likely this reduces to maximising the likelihood p(x | s_i). Because the noise is Gaussian with equal variance on every axis, the likelihood is a decreasing function of the squared Euclidean distance ||x - s_i||^2, so maximising the likelihood is exactly minimising that distance. The optimum receiver is therefore the nearest-neighbour rule, and the decision regions are the Voronoi cells bounded by the perpendicular bisectors between signal points. All of the geometry set up earlier exists to make this one sentence available.
KEY TERMS
• maximum likelihood
• MAP rule
• likelihood function
• decision region
• minimum distance rule
TAKEAWAY
Equal priors plus equal-variance Gaussian noise makes maximum likelihood identical to nearest neighbour — the optimum receiver is a distance comparison.
DIAGRAM FOR PHASE 2
A constellation plane with four points arranged in a square. Perpendicular bisectors between adjacent points are drawn as solid lines, partitioning the plane into four regions, each tinted a distinct pale colo…
Source: Digital Communication Systems, 1st ed., Ch. 7, pp. 337-344
CO1 | Bloom L4 | visual id: ml-decision-regions
Notes: What to say: Give them the idea before the formalism. Say it plainly first: The receiver that minimises symbol error probability chooses the signal maximising the posterior probability given the observation; when all signals are e… Then add the part they are examined on - Equal priors plus equal-variance Gaussian noise makes maximum likelihood identical to nearest neighbour — the optimum receiv… Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "maximum likelihood" constrain here, and what would break if it did not hold? Animation instructions: the four signal points appear, then the bisectors sweep out one at a time to partition the plane and the tints fill, then the received point x drops in, then the four dashed distance lines extend simultaneously, then the shortest thickens and brightens while the other three fade, then the side panel numbers count in with the minimum highlighted last. Transition style: Fade [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 1: Bandpass Signals to Equivalent Lowpass and Signalling over AWGN Channels. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 7, pp. 337-344. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 45
Maximum likelihood decoding and decision regions - how it works
The procedure in order, and what each pass costs you.
VTU BEC503 | Module 1
Maximum likelihood decoding and decis…
45
1. Receive the observation vector x
2. Compute the squared distance ||x - s_i||^2 to every candidate signal vector
3. Choose the index i minimising that distance
4. Equivalently, maximise the correlation term x . s_i - E_i/2
5. For unequal priors, add ln(p_i)*N0 to each correlation term to recover the MAP rule
COST AND BEHAVIOUR
Best: binary case is a single threshold comparison
Typical: M distance computations, each O(N)
Worst: M grows exponentially with bits per symbol, so exhaustive search becomes costly
WHAT THAT MEANS
Structured constellations such as QAM allow per-axis slicing instead of an M-way search.
Source: Digital Communication Systems, 1st ed., Ch. 7, pp. 337-344 | CO1 | Bloom L4
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Receive the observation vector x - and check everyone has written it before moving on. At the cost panel, translate it: Structured constellations such as QAM allow per-axis slicing instead of an M-way search. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 1: Bandpass Signals to Equivalent Lowpass and Signalling over AWGN Channels. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 7, pp. 337-344. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 46
Maximum likelihood decoding and decision regions - worked example
One concrete case, carried all the way to a stated number.
VTU BEC503 | Module 1
Maximum likelihood decoding and decis…
46
GIVEN
QPSK with points at (1,1), (1,-1), (-1,1), (-1,-1). Observation x = (0.3, 0.9).
1. To (1,1): (0.7)^2 + (0.1)^2 = 0.49 + 0.01 = 0.50
2. To (-1,1): (1.3)^2 + (0.1)^2 = 1.69 + 0.01 = 1.70
3. To (1,-1): (0.7)^2 + (1.9)^2 = 0.49 + 3.61 = 4.10
4. To (-1,-1): (1.3)^2 + (1.9)^2 = 1.69 + 3.61 = 5.30
RESULT
The decision is (1,1) at squared distance 0.50. Note the same answer follows from sign-slicing each coordinate separately, which is why QAM receivers do not search.
MAP: choose i maximising p(s_i) * p(x | s_i)
Equal priors => ML: choose i maximising p(x | s_i)
p(x | s_i) = (1/(pi*N0)^(N/2)) * exp( -||x - s_i||^2 / N0 )
=> choose i minimising ||x - s_i||^2
=> equivalently maximising x . s_i - E_i/2
THE MISTAKE STUDENTS MAKE
Students apply the nearest-neighbour rule when the signal energies differ and the priors are unequal. The correlation form needs the -E_i/2 bias term, and unequal priors need the ln(p_i) term; dropping either makes the receiver suboptimal without making it obviously wrong.
Source: Digital Communication Systems, 1st ed., Ch. 7, pp. 337-344 | CO1 | Bloom L4
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is QPSK with points at (1,1), (1,-1), (-1,1), (-1,-1). Observation x = (0.3, 0.9). Work at the pace of the slowest note-taker and land hard on the result: The decision is (1,1) at squared distance 0.50. Note the same answer follows from sign-slicing each coordinate separately, which… Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 1: Bandpass Signals to Equivalent Lowpass and Signalling over AWGN Channels. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 7, pp. 337-344. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 47
The correlation receiver
What it is, why it works, and what it costs.
VTU BEC503 | Module 1
The correlation receiver
47
THE MECHANISM
The correlation receiver implements the projection directly: it multiplies the received waveform by each basis function and integrates the product over the symbol interval, a structure usually built as a multiplier followed by an integrate-and-dump. N correlators in parallel produce the observation vector, which is then fed to the distance comparison. The structure is a literal circuit translation of the integral defining the inner product, which makes it easy to reason about and easy to get wrong in one specific way: the integrator must be reset at every symbol boundary, and the boundary must be known.
KEY TERMS
• correlator
• integrate-and-dump
• inner product
• bank of correlators
• symbol timing
TAKEAWAY
A correlator is the inner-product integral built in hardware — and it is only correct if the integrator is dumped exactly at the symbol boundary.
DIAGRAM FOR PHASE 2
A left-to-right diagram. Input arrow "x(t)" fans out to N parallel branches. Each branch has a multiplier circle fed from below by "phi_j(t)", then an integrator block marked with an integral sign over "0 to T…
Source: Digital Communication Systems, 1st ed., Ch. 7, pp. 337-344
CO1 | Bloom L3 | visual id: correlation-receiver-bank
Notes: What to say: Give them the idea before the formalism. Say it plainly first: The correlation receiver implements the projection directly: it multiplies the received waveform by each basis function and integrates the product over th… Then add the part they are examined on - A correlator is the inner-product integral built in hardware — and it is only correct if the integrator is dumped exactly at… Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "correlator" constrain here, and what would break if it did not hold? Animation instructions: the input arrow enters and fans to all branches, then a pulse travels along the top branch through multiplier, integrator and sampler in sequence, then the same pulse travels the remaining branches together, then the decision box fills and its output arrow extends, then the red reset callout snaps into view last. Transition style: Fade [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 1: Bandpass Signals to Equivalent Lowpass and Signalling over AWGN Channels. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 7, pp. 337-344. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 48
The correlation receiver - how it works
The procedure in order, and what each pass costs you.
VTU BEC503 | Module 1
The correlation receiver
48
1. Multiply the received waveform x(t) by basis function phi_j(t)
2. Integrate the product from 0 to T, the symbol duration
3. Sample the integrator output at exactly t = T
4. Dump — reset the integrator to zero before the next symbol
5. Repeat across all N branches and pass the vector to the distance comparison
COST AND BEHAVIOUR
Best: N multipliers and N integrators
Typical: one multiply-accumulate per sample per branch in a digital implementation
Worst: timing error of a fraction of a symbol degrades every branch simultaneously
WHAT THAT MEANS
A 10% timing error costs roughly 1 dB; a 50% error is catastrophic.
Source: Digital Communication Systems, 1st ed., Ch. 7, pp. 337-344 | CO1 | Bloom L3
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Multiply the received waveform x(t) by basis function phi_j(t) - and check everyone has written it before moving on. At the cost panel, translate it: A 10% timing error costs roughly 1 dB; a 50% error is catastrophic. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 1: Bandpass Signals to Equivalent Lowpass and Signalling over AWGN Channels. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 7, pp. 337-344. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 49
The correlation receiver - worked example
One concrete case, carried all the way to a stated number.
VTU BEC503 | Module 1
The correlation receiver
49
GIVEN
phi(t) = 1/sqrt(T) on [0,T]. Received x(t) = A on [0,T] plus noise integrating to +0.1.
1. Product x(t)*phi(t) = A/sqrt(T) on [0,T]
2. Integral over [0,T] = A*T/sqrt(T) = A*sqrt(T)
3. Add the noise contribution: x_1 = A*sqrt(T) + 0.1
4. For A = 2, T = 1: x_1 = 2.1
RESULT
The correlator output is 2.1 against a noiseless 2.0. The signal term scales as sqrt(T), which is why longer symbols are more robust.
x_j = integral_0^T x(t) * phi_j(t) dt
Hardware: multiply -> integrate over [0,T] -> sample at T -> dump
Digital: x_j = sum_{n=0}^{L-1} x[n] * phi_j[n]
Critical: integrator reset at every symbol boundary
THE MISTAKE STUDENTS MAKE
Students forget the dump. An integrator that is never reset accumulates across symbol boundaries, so each observation contains a contribution from every previous symbol and the constellation collapses into a drifting blur.
Source: Digital Communication Systems, 1st ed., Ch. 7, pp. 337-344 | CO1 | Bloom L3
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is phi(t) = 1/sqrt(T) on [0,T]. Received x(t) = A on [0,T] plus noise integrating to +0.1. Work at the pace of the slowest note-taker and land hard on the result: The correlator output is 2.1 against a noiseless 2.0. The signal term scales as sqrt(T), which is why longer symbols are more rob… Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 1: Bandpass Signals to Equivalent Lowpass and Signalling over AWGN Channels. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 7, pp. 337-344. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 50
The matched filter receiver and its equivalence to the correlator
What it is, why it works, and what it costs.
VTU BEC503 | Module 1
The matched filter receiver and its e…
50
THE MECHANISM
A matched filter for a basis function phi(t) has impulse response h(t) = phi(T - t), the time-reversed and shifted version of the signal it is matched to. Convolving the received waveform with this impulse response and sampling the output at t = T yields exactly the same number as the corresponding correlator produces, so the two structures are equivalent at the sampling instant and differ nowhere that matters. The matched filter is optimal in a stronger and independent sense: among all linear filters, it maximises the ratio of peak output signal power to average output noise power, and that maximum equals 2E/N0 regardless of the pulse shape.
KEY TERMS
• matched filter
• impulse response
• peak SNR
• time reversal
• convolution
TAKEAWAY
Matched filter and correlator give the same number at t = T; the matched filter also maximises peak SNR, and that maximum depends only on E/N0, never on the pulse shape.
DIAGRAM FOR PHASE 2
Two horizontal signal paths stacked with a large equals sign between them at the right. Upper path: "x(t)" into a multiplier fed by "phi(t)", into an integrator over [0,T], into a sampler at t = T, output "x_1…
Source: Digital Communication Systems, 1st ed., Ch. 7, pp. 337-344
CO1 | Bloom L4 | visual id: matched-filter-vs-correlator
Notes: What to say: Give them the idea before the formalism. Say it plainly first: A matched filter for a basis function phi(t) has impulse response h(t) = phi(T - t), the time-reversed and shifted version of the signal it is matched to. Then add the part they are examined on - Matched filter and correlator give the same number at t = T; the matched filter also maximises peak SNR, and that maximum de… Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "matched filter" constrain here, and what would break if it did not hold? Animation instructions: the upper path draws left to right, then the lower path draws left to right, then the equals sign appears and pulses, then the output plot draws its rising and falling edges, then the dashed sampling line drops onto the peak, then the time-reversal inset flips its waveform. Transition style: Fade [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 1: Bandpass Signals to Equivalent Lowpass and Signalling over AWGN Channels. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 7, pp. 337-344. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 51
The matched filter receiver and its equivalence to the… - how it works
The procedure in order, and what each pass costs you.
VTU BEC503 | Module 1
The matched filter receiver and its e…
51
1. Take the basis function phi(t) defined on [0,T]
2. Form the impulse response h(t) = phi(T - t)
3. Convolve the received waveform with h(t)
4. Sample the output at exactly t = T
5. Confirm the value equals the correlator output for the same branch
COST AND BEHAVIOUR
Best: a single filter replaces a multiplier and an integrator
Typical: peak output SNR is 2E/N0 for any pulse shape of energy E
Worst: output is only correct at t = T; sampling early or late loses SNR rapidly
WHAT THAT MEANS
Matched filtering maximises SNR at one instant only, which is why symbol synchronisation is inseparable from it.
Source: Digital Communication Systems, 1st ed., Ch. 7, pp. 337-344 | CO1 | Bloom L4
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Take the basis function phi(t) defined on [0,T] - and check everyone has written it before moving on. At the cost panel, translate it: Matched filtering maximises SNR at one instant only, which is why symbol synchronisation is inseparable from it. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 1: Bandpass Signals to Equivalent Lowpass and Signalling over AWGN Channels. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 7, pp. 337-344. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 52
The matched filter receiver and its equivalence to the… - worked example
One concrete case, carried all the way to a stated number.
VTU BEC503 | Module 1
The matched filter receiver and its e…
52
GIVEN
Rectangular pulse phi(t) = 1 on [0,T], T = 1.
1. h(t) = phi(T - t) = 1 on [0,1] — the rectangle is its own mirror image
2. Convolving a rectangle with a rectangle gives a triangle of width 2T
3. The triangle peaks at t = T = 1
4. Sampling anywhere else takes a value on the sloping sides, below the peak
RESULT
The output peaks exactly at the sampling instant. Sampling at t = 0.5T would collect only half the peak, costing 6 dB.
h(t) = phi(T - t) matched filter
y(t) = integral x(tau) * h(t - tau) dtau
y(T) = integral_0^T x(tau) * phi(tau) dtau = correlator output
Peak SNR at t = T: SNR_max = 2E/N0
Independent of pulse shape; depends only on energy E.
THE MISTAKE STUDENTS MAKE
Students write h(t) = phi(t) and skip the time reversal. Without reversing, the convolution does not compute a correlation, the output does not peak at t = T, and the SNR advantage is lost for any pulse that is not symmetric about T/2.
Source: Digital Communication Systems, 1st ed., Ch. 7, pp. 337-344 | CO1 | Bloom L4
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is Rectangular pulse phi(t) = 1 on [0,T], T = 1. Work at the pace of the slowest note-taker and land hard on the result: The output peaks exactly at the sampling instant. Sampling at t = 0.5T would collect only half the peak, costing 6 dB. Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 1: Bandpass Signals to Equivalent Lowpass and Signalling over AWGN Channels. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 7, pp. 337-344. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 53
One sentence per unit, six months from now
Units 1-7: what survives after the detail has gone.
VTU BEC503 | Module 1
Revision
53
01 The carrier is packaging, not content; strip it analytically and the sampling cost drops by the ratio fc/W.
02 The Hilbert transform changes phase by 90 degrees at every frequency and magnitude at none, which is why it can cancel a whole spectral half.
03 Same energy, orthogonal to the original, and self-inverse up to a sign — these three properties are what make quadrature signalling possible.
04 Adding j times the Hilbert transform deletes the negative-frequency half of the spectrum; the cost of a one-sided spectrum is that the signal must go complex.
05 Multiplying the pre-envelope by exp(-j*2*pi*fc*t) slides the spectrum to baseband and leaves the complex envelope — the smallest complete description of the modulation.
06 Every bandpass signal is two real lowpass signals on orthogonal carriers — that is why one band can carry two independent streams.
07 Rectangular form suits circuits and decisions; polar form suits amplifiers and envelope arguments — pick by the question, not by habit.
Notes: What to say: Slow right down here. Read each takeaway aloud and then stop talking for a beat, because these are the sentences that should still be in their heads when they sit the SEE. Tell them explicitly that if they can reconstruct the reasoning behind any one of these lines they understand that unit, and if they can only recite it they do not. Pause cue: Pause for three seconds after each takeaway before moving to the next. Pointing cue: Point at each numbered takeaway in turn as you read it. Question to ask students: Ask: choose the takeaway you trust least and tell me what you would have to check to believe it. Animation instructions: Takeaway rows reveal one at a time from the top, each row highlighting briefly as it appears. Transition style: Fade [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 1: Bandpass Signals to Equivalent Lowpass and Signalling over AWGN Channels, 10 hours, TB1 (Haykin 2014) Ch. 2.8-2.11 pp. 42-52 and Ch. 7.1-7.4 pp. 323-344. TB1: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014. Revision consolidates all 16 unit takeaways. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 54
Revision, continued
Units 8-14: what survives after the detail has gone.
VTU BEC503 | Module 1
Revision
54
08 AWGN is three assumptions, not one; every result in this module inherits all three, and each fails in a different real channel.
09 Once signals are points and energy is squared length, detection is geometry — and the answer is always the nearest point.
10 Subtract what is already represented, normalise what is left — and a zero remainder tells you the signal added no new dimension.
11 A constellation is judged by one ratio: minimum distance squared over average energy. Everything else is detail.
12 Project onto the basis and the channel becomes N independent Gaussian scalars, each of variance N0/2 — the same variance on every axis.
13 N numbers per symbol are provably enough; the rest of the waveform is pure noise and discarding it costs nothing.
14 Equal priors plus equal-variance Gaussian noise makes maximum likelihood identical to nearest neighbour — the optimum receiver is a distance comparison.
Notes: What to say: Slow right down here. Read each takeaway aloud and then stop talking for a beat, because these are the sentences that should still be in their heads when they sit the SEE. Tell them explicitly that if they can reconstruct the reasoning behind any one of these lines they understand that unit, and if they can only recite it they do not. Pause cue: Pause for three seconds after each takeaway before moving to the next. Pointing cue: Point at each numbered takeaway in turn as you read it. Question to ask students: Ask: choose the takeaway you trust least and tell me what you would have to check to believe it. Animation instructions: Takeaway rows reveal one at a time from the top, each row highlighting briefly as it appears. Transition style: Fade [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 1: Bandpass Signals to Equivalent Lowpass and Signalling over AWGN Channels, 10 hours, TB1 (Haykin 2014) Ch. 2.8-2.11 pp. 42-52 and Ch. 7.1-7.4 pp. 323-344. TB1: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014. Revision consolidates all 16 unit takeaways. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 55
Revision, continued
Units 15-16: what survives after the detail has gone.
VTU BEC503 | Module 1
Revision
55
15 A correlator is the inner-product integral built in hardware — and it is only correct if the integrator is dumped exactly at the symbol boundary.
16 Matched filter and correlator give the same number at t = T; the matched filter also maximises peak SNR, and that maximum depends only on E/N0, never on the pulse shape.
Notes: What to say: Slow right down here. Read each takeaway aloud and then stop talking for a beat, because these are the sentences that should still be in their heads when they sit the SEE. Tell them explicitly that if they can reconstruct the reasoning behind any one of these lines they understand that unit, and if they can only recite it they do not. Pause cue: Pause for three seconds after each takeaway before moving to the next. Pointing cue: Point at each numbered takeaway in turn as you read it. Question to ask students: Ask: choose the takeaway you trust least and tell me what you would have to check to believe it. Animation instructions: Takeaway rows reveal one at a time from the top, each row highlighting briefly as it appears. Transition style: Fade [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 1: Bandpass Signals to Equivalent Lowpass and Signalling over AWGN Channels, 10 hours, TB1 (Haykin 2014) Ch. 2.8-2.11 pp. 42-52 and Ch. 7.1-7.4 pp. 323-344. TB1: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014. Revision consolidates all 16 unit takeaways. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 56
How this module is assessed
Where the quiz and the assignment live, and what they test.
VTU BEC503 | Module 1
Assessment
56
MODULE 1 QUIZ
quizzes/Module_1_Quiz.pdf
quizzes/Module_1_Quiz.gift
45 minutes | 50 marks | pass 20 | 1 attempt
Part A: 20 MCQs, 1 mark each.
Part B: 13 descriptive questions, 30 marks.
Bloom spread: L1-L2 21%, L3-L4 79%, L5-L6 0%
Every question carries a CO tag, a Bloom level and a chapter reference; distractor feedback names the misconception.
MODULE 1 ASSIGNMENT
assignments/Module_1_Assignment.pdf
Assignment 1 — Signal space representation and optimum reception
20 marks | 10% of CIE | 8 problems + 3 theory items
Submit as PDF, single file, named <USN>_BEC503_Assignment1.pdf, via LMS upload. 10% per day, nothing after 5 days.
Rubric: Correctness of derivations (8); Numerical accuracy and units (5); Diagrams and signal space sketches (4); Interpretation and engineering judgement (3). Attainment: CO1 = 15, CO2 = 5.
Previous years' question papers for EC are indexed in pyq/PYQ_Index.pdf; the syllabus extract and the topic-to-slide mapping are in syllabus/Syllabus_Mapping.pdf.
Individual submission. Identical submissions score zero for both parties.
Notes: What to say: Close by telling them exactly where the assessment lives and what it tests. Name the two files, say the mark split out loud, and read the Bloom spread so they understand that roughly a quarter of the paper is not recall at all. Then read the integrity line word for word, because ambiguity there costs students more than any technical error in this module. Pause cue: Pause after the Bloom spread and before the integrity statement. Pointing cue: Point at the quiz panel, then the assignment panel, then the integrity line at the bottom. Question to ask students: Ask: which course outcome do you feel least ready on, and which unit would you reread tonight to fix it? Animation instructions: Quiz panel fades in from the left, then the assignment panel from the right, then the pointers strip appears, then the integrity line fades in last. Transition style: Fade [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 1: Bandpass Signals to Equivalent Lowpass and Signalling over AWGN Channels, 10 hours, TB1 (Haykin 2014) Ch. 2.8-2.11 pp. 42-52 and Ch. 7.1-7.4 pp. 323-344. TB1: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014. Assessment counts: 20 MCQs, 13 descriptive questions, 11 assignment items. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.