## Slide 1
Network Analysis
Module 5 asks: How do I describe a network I cannot open, using only measurements made at its two accessible ports — and t…
VTU BEC303 | Module 5
Opening
01
MODULE 5
Two-Port Networks
14 contact hours | 16 teaching units | 56 slides
PRESCRIBED TEXTBOOK
Engineering Circuit Analysis
W. H. Hayt, J. E. Kemmerly and S. M. Durbin
McGraw-Hill / Tata McGraw-Hill, 8th edition, 2012
Hayt 8e Ch. 17 (17.1–17.6), pp. 687–720
Mesh & Nodal Analysis • Network Theorems • Transient Response • Laplace / s-Domain • Two-Port Networks
One port gives driving-point impedance → Two ports need four numbers → Each parameter set has blind spots → Symmetry and reciprocity constrain them → Termination converts parameters to performance
EC · Semester 3 · BEC303 · generated for Phase 2 conversion
Notes: What to say: Open by putting the whole module on one page. Tell them this is 14 contact hours and 16 teaching units, and that all of it exists to answer one question: How do I describe a network I cannot open, using only measurements made at its two accessible ports — and then predict what it does with any source and any load? Name the prescribed textbook out loud and say which chapters they will be living in, so nobody is reading the wrong book by week two. Pause cue: Pause after reading the driving question aloud, before naming the textbook. Pointing cue: Point at the module title block, then at the textbook panel, then run a finger along the five-beat arc. Question to ask students: Ask: before we start, what do you already expect the answer to "How do I describe a network I cannot open, using only measurements made at its two access…" to look like? Animation instructions: Module title block fades in first, then the textbook panel slides in from the right, then the five arc beats appear left to right one at a time. Transition style: Fade [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 5: Two-Port Networks, 14 hours, Hayt 8e Ch. 17 (17.1–17.6), pp. 687–720. TB1: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 2
What this module is actually for
One question, five beats, and the scope it does not cover.
VTU BEC303 | Module 5
Overview
02
THE DRIVING QUESTION
How do I describe a network I cannot open, using only measurements made at its two accessible ports — and then predict what it does with any source and any load?
1
One port gives driving-point impedance
2
Two ports need four numbers
3
Each parameter set has blind spots
4
Symmetry and reciprocity constrain them
5
Termination converts parameters to performance
SCOPE AND PROVENANCE
Built from the syllabus-listed Hayt 8e Chapter 17 sections. The organising argument is that a two-port is a black box characterised by four numbers, and that the six possible parameter sets exist because each one is undefined for some perfectly ordinary network — which is why "why multiple representations are required" is treated as a unit in its own right rather than a remark. Reciprocity and symmetry are carried forward from Module 2 and shown here as matrix conditions. The module closes on terminated input and output impedance, which is the link back to the maximum power transfer results of Module 2.
Course outcomes exercised: CO5
Assessment: 20 MCQs + 13 descriptive questions + 13 assignment items
Notes: What to say: Give them the map before the territory. Read the driving question once more, then walk the five beats across the slide and say in one sentence what changes between each beat and the next. Finish on the scope paragraph, because knowing what a module does not cover saves more marks than anything else on this slide. Pause cue: Pause for four or five seconds after the five beats appear, before moving to scope. Pointing cue: Point at the driving question panel, then at each numbered beat in turn, then at the scope paragraph. Question to ask students: Ask: which of these five beats do you expect to find hardest, and why that one? Animation instructions: The driving question panel fades in, then the five numbered beats appear left to right one at a time, then the scope paragraph fades in beneath them. Transition style: Fade [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 5: Two-Port Networks, 14 hours, Hayt 8e Ch. 17 (17.1–17.6), pp. 687–720. TB1: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 3
Every unit against its chapter and pages
Units 1-9 of 16, with the deck slides that teach each one.
VTU BEC303 | Module 5
Syllabus mapping
03
# — Teaching unit — Book chapter and pages — Deck slides — CO / Bloom
01 One-port networks and driving-point impedance — Ch. 17, pp. 687-692 — slides 5, 6, 7 — CO5 / L2
02 What a two-port is and why four numbers suffice — Ch. 17, pp. 687-692 — slides 8, 9, 10 — CO5 / L2
03 Short-circuit admittance (y) parameters — Ch. 17, pp. 692-699 — slides 11, 12, 13 — CO5 / L3
04 Equivalent networks and the π model — Ch. 17, pp. 699-708 — slides 14, 15, 16 — CO5 / L4
05 Open-circuit impedance (z) parameters — Ch. 17, pp. 708-713 — slides 17, 18, 19 — CO5 / L3
06 The relationship between z and y, and when each fails — Ch. 17, pp. 692-713 — slides 20, 21, 22 — CO5 / L4
07 Hybrid (h) parameters — Ch. 17, pp. 713-716 — slides 23, 24, 25 — CO5 / L3
08 Why multiple representations are required — Ch. 17, pp. 713-716 — slides 26, 27, 28 — CO5 / L5
09 Transmission (ABCD) parameters — Ch. 17, pp. 716-720 — slides 29, 30, 31 — CO5 / L4
Notes: What to say: Tell them this is the slide to photograph. Every unit in the module is listed against a real chapter and a real page range, so there is no ambiguity about what to read. Point out the slide-number column and say plainly that if they miss a lecture, those are the slides covering that unit. Say that the page ranges come from the book's own table of contents rather than a guess. Pause cue: Pause for ten seconds and let them photograph the table before saying anything else. Pointing cue: Run a finger down the chapter-and-pages column, then across one complete row. Question to ask students: Ask: pick any row - which chapter would you open first, and what would you expect in the first paragraph? Animation instructions: Header row appears first, then the unit rows fade in one at a time from the top, then the chapter-and-pages column highlights. Transition style: Cut [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 5: Two-Port Networks, 14 hours, Hayt 8e Ch. 17 (17.1–17.6), pp. 687–720. TB1: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012. Mapping covers all 16 teaching units. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 4
Syllabus mapping, continued
Units 10-16 of 16, with the deck slides that teach each one.
VTU BEC303 | Module 5
Syllabus mapping
04
# — Teaching unit — Book chapter and pages — Deck slides — CO / Bloom
10 Cascading two-ports with ABCD — Ch. 17, pp. 716-720 — slides 32, 33, 34 — CO5 / L4
11 Two-port symmetry and reciprocity — Ch. 17, pp. 699-708 — slides 35, 36, 37 — CO5 / L4
12 Input impedance of a terminated two-port — Ch. 17, pp. 708-713 — slides 38, 39, 40 — CO5 / L4
13 Output impedance and the source-terminated two-port — Ch. 17, pp. 708-713 — slides 41, 42, 43 — CO5 / L4
14 Measuring two-port parameters in practice — Ch. 17, pp. 692-713 — slides 44, 45, 46 — CO5 / L5
15 Choosing and converting between parameter sets — Ch. 17, pp. 692-720 — slides 47, 48, 49 — CO5 / L5
16 Putting it together: a fully terminated two-port — Ch. 17, pp. 708-720 — slides 50, 51, 52 — CO5 / L5
Notes: What to say: Tell them this is the slide to photograph. Every unit in the module is listed against a real chapter and a real page range, so there is no ambiguity about what to read. Point out the slide-number column and say plainly that if they miss a lecture, those are the slides covering that unit. Say that the page ranges come from the book's own table of contents rather than a guess. Pause cue: Pause for ten seconds and let them photograph the table before saying anything else. Pointing cue: Run a finger down the chapter-and-pages column, then across one complete row. Question to ask students: Ask: pick any row - which chapter would you open first, and what would you expect in the first paragraph? Animation instructions: Header row appears first, then the unit rows fade in one at a time from the top, then the chapter-and-pages column highlights. Transition style: Cut [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 5: Two-Port Networks, 14 hours, Hayt 8e Ch. 17 (17.1–17.6), pp. 687–720. TB1: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012. Mapping covers all 16 teaching units. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 5
One-port networks and driving-point impedance
What it is, why it works, and what it costs.
VTU BEC303 | Module 5
One-port networks and driving-point i…
05
THE MECHANISM
A one-port is any network accessed through a single terminal pair, and it is described completely by one function — its driving-point impedance Z(s) = V(s)/I(s). This is the Thévenin idea of Module 2 generalised into the s-domain: whatever the internal complexity, the outside world sees only that one ratio. The defining requirement is the port condition: the current entering one terminal must equal the current leaving the other. If a stray path lets current return by another route, the terminal pair is not a port and no single impedance describes it. The driving-point impedance of a passive network is always a positive real function, which is the realisability constraint met at the end of Module 4.
KEY TERMS
• one-port
• driving-point impedance
• port condition
• Z(s)
TAKEAWAY
A one-port is one number as a function of s — and only if the port condition actually holds.
DIAGRAM FOR PHASE 2
Left: a cloud labelled "any linear network" with two terminals on its right edge, a current arrow I entering the upper terminal and an identical arrow I leaving the lower terminal, with V marked across them an…
Source: Engineering Circuit Analysis, 8th ed., Ch. 17, pp. 687-692
CO5 | Bloom L2 | visual id: one-port-condition
Notes: What to say: Give them the idea before the formalism. Say it plainly first: A one-port is any network accessed through a single terminal pair, and it is described completely by one function — its driving-point impedance Z(s) = V(s… Then add the part they are examined on - A one-port is one number as a function of s — and only if the port condition actually holds. Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "one-port" constrain here, and what would break if it did not hold? Animation instructions: left cloud and terminals draw, the two equal current arrows animate in and out together, the green tick lands; then the right cloud appears, the leakage wire draws in dotted red, the currents visibly mismatch, the red cross lands. Transition style: Fade [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 5: Two-Port Networks. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 17, pp. 687-692. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 6
One-port networks and driving-point impedance - how it works
The procedure in order, and what each pass costs you.
VTU BEC303 | Module 5
One-port networks and driving-point i…
06
1. Identify the terminal pair of interest
2. Verify that no other conducting path connects the network to the rest of the circuit
3. Apply a test source and compute the resulting terminal current, or the reverse
4. Form Z(s) = V(s)/I(s)
5. Confirm the result is a positive real function for a passive network
COST AND BEHAVIOUR
Best: O(n) series-parallel reduction
Typical: one symbolic network solve
Worst: a test-source solve when dependent sources are present
WHAT THAT MEANS
Identical in structure to finding Z_th in Module 2, now as a function of s.
Source: Engineering Circuit Analysis, 8th ed., Ch. 17, pp. 687-692 | CO5 | Bloom L2
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Identify the terminal pair of interest - and check everyone has written it before moving on. At the cost panel, translate it: Identical in structure to finding Z_th in Module 2, now as a function of s. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 5: Two-Port Networks. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 17, pp. 687-692. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 7
One-port networks and driving-point impedance - worked example
One concrete case, carried all the way to a stated number.
VTU BEC303 | Module 5
One-port networks and driving-point i…
07
GIVEN
A one-port consisting of R = 100 Ω in series with L = 50 mH.
1. Z(s) = R + sL = 100 + 0.05s
2. At s = jω with ω = 2000: Z = 100 + j100 Ω
3. Magnitude = 141.4 Ω at 45°
4. Positive real check: no poles, one zero at s = −2000, Re{Z} ≥ 0 for Re{s} ≥ 0 — passes
RESULT
Z(s) = 100 + 0.05s, reducing to the familiar 141.4∠45° Ω at 2000 rad/s and satisfying the passive realisability test.
Z(s) = R + sL = 100 + 0.05s
Z(j2000) = 100 + j100 = 141.4∠45° Ω
THE MISTAKE STUDENTS MAKE
Students apply one-port analysis to a terminal pair that shares a ground return with another part of the circuit. The two terminal currents then differ, the port condition fails, and the computed impedance does not predict what a load will actually see.
Source: Engineering Circuit Analysis, 8th ed., Ch. 17, pp. 687-692 | CO5 | Bloom L2
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is A one-port consisting of R = 100 Ω in series with L = 50 mH. Work at the pace of the slowest note-taker and land hard on the result: Z(s) = 100 + 0.05s, reducing to the familiar 141.4∠45° Ω at 2000 rad/s and satisfying the passive realisability test. Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 5: Two-Port Networks. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 17, pp. 687-692. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 8
What a two-port is and why four numbers suffice
What it is, why it works, and what it costs.
VTU BEC303 | Module 5
What a two-port is and why four numbe…
08
THE MECHANISM
A two-port has an input terminal pair and an output terminal pair, each satisfying the port condition, and it is described by relationships among four variables: V₁, I₁, V₂ and I₂. Because the network is linear, any two of these can be expressed as linear combinations of the other two, which takes exactly four coefficients — and that is why a two-port is a four-number object regardless of how many elements it contains internally. This is a genuine compression: a filter with thirty components and a filter with three are equally described by four numbers at a given frequency. The description is valid only for what happens at the ports, and says nothing about internal node voltages or internal dissipation.
KEY TERMS
• two-port
• port variables
• black box
• four parameters
• linearity
TAKEAWAY
Four numbers describe any linear two-port at a given frequency, no matter how many parts are inside.
DIAGRAM FOR PHASE 2
Centre: a rectangular black box with two terminals on the left labelled port 1 and two on the right labelled port 2. Arrows mark I₁ entering the upper-left terminal and leaving the lower-left, I₂ entering the…
Source: Engineering Circuit Analysis, 8th ed., Ch. 17, pp. 687-692
CO5 | Bloom L2 | visual id: two-port-black-box
Notes: What to say: Give them the idea before the formalism. Say it plainly first: A two-port has an input terminal pair and an output terminal pair, each satisfying the port condition, and it is described by relationships among four var… Then add the part they are examined on - Four numbers describe any linear two-port at a given frequency, no matter how many parts are inside. Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "two-port" constrain here, and what would break if it did not hold? Animation instructions: box and four terminals draw, the four port variables label in, then the three internal thumbnails appear above and their arrows sweep down into the box, then the matrix equation types in beneath. Transition style: Fade [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 5: Two-Port Networks. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 17, pp. 687-692. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 9
What a two-port is and why four numbers suffice - how it works
The procedure in order, and what each pass costs you.
VTU BEC303 | Module 5
What a two-port is and why four numbe…
09
1. Confirm both terminal pairs satisfy the port condition
2. Adopt the standard convention: both currents entering the upper terminal of their port
3. Choose which two variables will be independent
4. Express the remaining two as linear combinations of them
5. Record the four coefficients as the parameter set
6. Note the frequency at which they were determined
COST AND BEHAVIOUR
Best: four simple measurements or calculations
Typical: two network solves, each giving two parameters
Worst: a full symbolic solve per parameter for a complicated internal network
WHAT THAT MEANS
Parameters are frequency-dependent; a set quoted without its frequency is incomplete.
Source: Engineering Circuit Analysis, 8th ed., Ch. 17, pp. 687-692 | CO5 | Bloom L2
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Confirm both terminal pairs satisfy the port condition - and check everyone has written it before moving on. At the cost panel, translate it: Parameters are frequency-dependent; a set quoted without its frequency is incomplete. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 5: Two-Port Networks. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 17, pp. 687-692. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 10
What a two-port is and why four numbers suffice - worked example
One concrete case, carried all the way to a stated number.
VTU BEC303 | Module 5
What a two-port is and why four numbe…
10
GIVEN
A purely resistive T network with a 10 Ω series arm on each side and a 20 Ω shunt arm.
1. Port variables: V₁, I₁ at the input, V₂, I₂ at the output
2. Four coefficients are needed to relate any chosen pair to the other pair
3. The internal detail — three resistors — collapses into those four numbers
4. A different internal network giving the same four numbers is indistinguishable at the ports
RESULT
The three-element T is fully represented by four parameters, and any other network with the same four is externally identical to it.
[V₁] [a b] [V₂]
[I₁] = [c d] [−I₂] (four coefficients, any linear two-port)
THE MISTAKE STUDENTS MAKE
Students assume a two-port description captures internal behaviour, and try to compute internal power dissipation from it. The four parameters describe terminal behaviour only; two networks with identical parameters can dissipate different amounts internally.
Source: Engineering Circuit Analysis, 8th ed., Ch. 17, pp. 687-692 | CO5 | Bloom L2
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is A purely resistive T network with a 10 Ω series arm on each side and a 20 Ω shunt arm. Work at the pace of the slowest note-taker and land hard on the result: The three-element T is fully represented by four parameters, and any other network with the same four is externally identical to… Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 5: Two-Port Networks. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 17, pp. 687-692. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 11
Short-circuit admittance (y) parameters
What it is, why it works, and what it costs.
VTU BEC303 | Module 5
Short-circuit admittance (y) paramete…
11
THE MECHANISM
The y parameters express both currents in terms of both voltages: I₁ = y₁₁V₁ + y₁₂V₂ and I₂ = y₂₁V₁ + y₂₂V₂. Each is measured with one port short-circuited, because setting a port voltage to zero is what isolates a single coefficient. So y₁₁ = I₁/V₁ with port 2 shorted is the input admittance under output short; y₂₁ = I₂/V₁ with port 2 shorted is the forward transfer admittance; y₂₂ and y₁₂ follow by driving port 2 with port 1 shorted. The set is natural for networks whose elements sit in shunt, such as the π model, because shunt admittances simply add.
KEY TERMS
• y parameters
• short-circuit
• y₁₁ input admittance
• y₂₁ forward transfer admittance
TAKEAWAY
y parameters are the short-circuit set — and short-circuit tests are easy at low frequency and awkward at high frequency.
DIAGRAM FOR PHASE 2
A 2×2 arrangement of measurement setups. Top-left: a source V₁ on port 1 with port 2 shorted by a heavy bar, ammeters reading I₁ and I₂, annotated "y₁₁ = I₁/V₁, y₂₁ = I₂/V₁". Top-right: the defining equations…
Source: Engineering Circuit Analysis, 8th ed., Ch. 17, pp. 692-699
CO5 | Bloom L3 | visual id: y-parameter-measurement
Notes: What to say: Give them the idea before the formalism. Say it plainly first: The y parameters express both currents in terms of both voltages: I₁ = y₁₁V₁ + y₁₂V₂ and I₂ = y₂₁V₁ + y₂₂V₂. Then add the part they are examined on - y parameters are the short-circuit set — and short-circuit tests are easy at low frequency and awkward at high frequency. Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "y parameters" constrain here, and what would break if it did not hold? Animation instructions: top-left setup draws with the short bar slamming into place and the meters reading, then the equations appear with the vanishing terms fading to grey, then the mirrored setup builds, then the π thumbnail appears. Transition style: Fade [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 5: Two-Port Networks. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 17, pp. 692-699. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 12
Short-circuit admittance (y) parameters - how it works
The procedure in order, and what each pass costs you.
VTU BEC303 | Module 5
Short-circuit admittance (y) paramete…
12
1. Short-circuit port 2 and apply a known V₁
2. Measure or compute I₁ and I₂ to obtain y₁₁ and y₂₁
3. Short-circuit port 1 and apply a known V₂
4. Measure or compute I₂ and I₁ to obtain y₂₂ and y₁₂
5. Record all four with their units of siemens and the test frequency
6. Check y₁₂ = y₂₁ if the network is reciprocal
COST AND BEHAVIOUR
Best: two solves for four parameters
Typical: two network solves
Worst: two symbolic solves for a complicated internal network
WHAT THAT MEANS
Short-circuit tests can be difficult at high frequency where lead inductance prevents a true short.
Source: Engineering Circuit Analysis, 8th ed., Ch. 17, pp. 692-699 | CO5 | Bloom L3
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Short-circuit port 2 and apply a known V₁ - and check everyone has written it before moving on. At the cost panel, translate it: Short-circuit tests can be difficult at high frequency where lead inductance prevents a true short. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 5: Two-Port Networks. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 17, pp. 692-699. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 13
Short-circuit admittance (y) parameters - worked example
One concrete case, carried all the way to a stated number.
VTU BEC303 | Module 5
Short-circuit admittance (y) paramete…
13
GIVEN
A π network with 20 Ω shunt at each port and a 10 Ω series branch between them.
1. Short port 2: the input sees 20 Ω in parallel with 10 Ω, so y₁₁ = 1/20 + 1/10 = 0.15 S
2. Current into the short: I₂ = −V₁/10, so y₂₁ = −0.1 S
3. By symmetry of the network, y₂₂ = 0.15 S and y₁₂ = −0.1 S
4. Check: y₁₂ = y₂₁, confirming reciprocity
RESULT
y = [[0.15, −0.1], [−0.1, 0.15]] S — symmetric because the network is both reciprocal and geometrically symmetric.
I₁ = y₁₁V₁ + y₁₂V₂
I₂ = y₂₁V₁ + y₂₂V₂
π network: y = [[0.15, −0.1], [−0.1, 0.15]] S
THE MISTAKE STUDENTS MAKE
Students forget the sign of the transfer admittances. With both currents defined as entering their ports, y₁₂ and y₂₁ come out negative for a simple passive series branch; reporting them positive reverses the predicted direction of the output current.
Source: Engineering Circuit Analysis, 8th ed., Ch. 17, pp. 692-699 | CO5 | Bloom L3
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is A π network with 20 Ω shunt at each port and a 10 Ω series branch between them. Work at the pace of the slowest note-taker and land hard on the result: y = [[0.15, −0.1], [−0.1, 0.15]] S — symmetric because the network is both reciprocal and geometrically symmetric. Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 5: Two-Port Networks. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 17, pp. 692-699. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 14
Equivalent networks and the π model
What it is, why it works, and what it costs.
VTU BEC303 | Module 5
Equivalent networks and the π model
14
THE MECHANISM
Any reciprocal two-port can be represented by a π network of three admittances, and the mapping from y parameters is direct: the series branch is −y₁₂, the shunt branch at port 1 is y₁₁ + y₁₂, and the shunt branch at port 2 is y₂₂ + y₁₂. The equivalent is exact at the terminals, so a measurement cannot distinguish the real network from its π model. This is why the π appears everywhere in transmission-line and transistor modelling: it is the simplest structure that can reproduce an arbitrary reciprocal two-port. A non-reciprocal network needs a dependent source added to the π, since three passive branches always produce y₁₂ = y₂₁.
KEY TERMS
• π equivalent
• equivalent network
• terminal indistinguishability
• y-to-π mapping
TAKEAWAY
Three admittances reproduce any reciprocal two-port exactly — and a fourth element, a dependent source, is needed the moment it is not reciprocal.
DIAGRAM FOR PHASE 2
Left: a 2×2 y matrix with its four entries. Right: a π network drawn as two shunt branches to a common ground and one series branch between the top nodes. Three curved arrows map matrix entries onto branches:…
Source: Engineering Circuit Analysis, 8th ed., Ch. 17, pp. 699-708
CO5 | Bloom L4 | visual id: y-to-pi-mapping
Notes: What to say: Give them the idea before the formalism. Say it plainly first: Any reciprocal two-port can be represented by a π network of three admittances, and the mapping from y parameters is direct: the series branch is −y₁₂, th… Then add the part they are examined on - Three admittances reproduce any reciprocal two-port exactly — and a fourth element, a dependent source, is needed the moment… Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "π equivalent" constrain here, and what would break if it did not hold? Animation instructions: the matrix appears, then each curved arrow sweeps from its matrix entry to the corresponding branch which lights up as it is assigned, then the non-reciprocal variant fades in beneath with the diamond appearing last. Transition style: Fade [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 5: Two-Port Networks. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 17, pp. 699-708. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 15
Equivalent networks and the π model - how it works
The procedure in order, and what each pass costs you.
VTU BEC303 | Module 5
Equivalent networks and the π model
15
1. Obtain the four y parameters
2. Check whether y₁₂ equals y₂₁
3. If so, set the series admittance to −y₁₂
4. Set the port 1 shunt admittance to y₁₁ + y₁₂
5. Set the port 2 shunt admittance to y₂₂ + y₁₂
6. If not reciprocal, add a dependent source to account for the asymmetry
COST AND BEHAVIOUR
Best: O(1) — three subtractions
Typical: O(1) once y is known
Worst: O(1) plus a dependent-source term for non-reciprocal networks
WHAT THAT MEANS
The mapping is arithmetic; obtaining y is where the work lies.
Source: Engineering Circuit Analysis, 8th ed., Ch. 17, pp. 699-708 | CO5 | Bloom L4
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Obtain the four y parameters - and check everyone has written it before moving on. At the cost panel, translate it: The mapping is arithmetic; obtaining y is where the work lies. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 5: Two-Port Networks. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 17, pp. 699-708. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 16
Equivalent networks and the π model - worked example
One concrete case, carried all the way to a stated number.
VTU BEC303 | Module 5
Equivalent networks and the π model
16
GIVEN
y = [[0.15, −0.1], [−0.1, 0.15]] S.
1. Series admittance = −y₁₂ = 0.1 S, i.e. 10 Ω
2. Port 1 shunt = y₁₁ + y₁₂ = 0.15 − 0.1 = 0.05 S, i.e. 20 Ω
3. Port 2 shunt = y₂₂ + y₁₂ = 0.05 S, i.e. 20 Ω
4. Reciprocity confirmed since y₁₂ = y₂₁
RESULT
The π model is 20 Ω shunt, 10 Ω series, 20 Ω shunt — recovering exactly the network the parameters were computed from.
Y_series = −y₁₂ = 0.1 S (10 Ω)
Y_shunt1 = y₁₁ + y₁₂ = 0.05 S (20 Ω)
Y_shunt2 = y₂₂ + y₁₂ = 0.05 S (20 Ω)
THE MISTAKE STUDENTS MAKE
Students add y₁₂ when they mean to subtract, or vice versa, because the sign convention makes y₁₂ negative for a passive series branch. Working in admittances and checking that every resulting branch is physically realisable — a positive conductance — catches the slip immediately.
Source: Engineering Circuit Analysis, 8th ed., Ch. 17, pp. 699-708 | CO5 | Bloom L4
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is y = [[0.15, −0.1], [−0.1, 0.15]] S. Work at the pace of the slowest note-taker and land hard on the result: The π model is 20 Ω shunt, 10 Ω series, 20 Ω shunt — recovering exactly the network the parameters were computed from. Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 5: Two-Port Networks. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 17, pp. 699-708. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 17
Open-circuit impedance (z) parameters
What it is, why it works, and what it costs.
VTU BEC303 | Module 5
Open-circuit impedance (z) parameters
17
THE MECHANISM
The z parameters express both voltages in terms of both currents: V₁ = z₁₁I₁ + z₁₂I₂ and V₂ = z₂₁I₁ + z₂₂I₂. Each is measured with one port open-circuited, since setting a port current to zero isolates a single coefficient. So z₁₁ = V₁/I₁ with port 2 open is the input impedance under output open; z₂₁ = V₂/I₁ with port 2 open is the forward transfer impedance. The corresponding equivalent circuit is the T network, whose series arms are z₁₁ − z₁₂ and z₂₂ − z₁₂ with a shunt arm of z₁₂. The set is natural for networks whose elements sit in series, and open-circuit tests are generally easier at high frequency than short-circuit ones.
KEY TERMS
• z parameters
• open-circuit
• z₁₁ input impedance
• z₂₁ forward transfer impedance
• T model
TAKEAWAY
z parameters are the open-circuit set and map onto a T; y parameters are the short-circuit set and map onto a π.
DIAGRAM FOR PHASE 2
Left half: a measurement setup with a current source I₁ driving port 1 and port 2 left visibly open, with voltmeters reading V₁ and V₂, annotated "z₁₁ = V₁/I₁, z₂₁ = V₂/I₁ with I₂ = 0". Right half: a T network…
Source: Engineering Circuit Analysis, 8th ed., Ch. 17, pp. 708-713
CO5 | Bloom L3 | visual id: z-parameter-and-t-model
Notes: What to say: Give them the idea before the formalism. Say it plainly first: The z parameters express both voltages in terms of both currents: V₁ = z₁₁I₁ + z₁₂I₂ and V₂ = z₂₁I₁ + z₂₂I₂. Then add the part they are examined on - z parameters are the open-circuit set and map onto a T; y parameters are the short-circuit set and map onto a π. Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "z parameters" constrain here, and what would break if it did not hold? Animation instructions: the measurement setup draws with the open terminals flashing, the meters read, then the T model assembles arm by arm with each label appearing, then the dotted bracket links them, then the comparison strip slides up. Transition style: Fade [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 5: Two-Port Networks. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 17, pp. 708-713. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 18
Open-circuit impedance (z) parameters - how it works
The procedure in order, and what each pass costs you.
VTU BEC303 | Module 5
Open-circuit impedance (z) parameters
18
1. Open-circuit port 2 and drive port 1 with a known current
2. Measure V₁ and V₂ to obtain z₁₁ and z₂₁
3. Open-circuit port 1 and drive port 2
4. Measure V₂ and V₁ to obtain z₂₂ and z₁₂
5. Record all four in ohms with the test frequency
6. Map to a T model if an equivalent circuit is wanted
COST AND BEHAVIOUR
Best: two solves for four parameters
Typical: two network solves
Worst: two symbolic solves
WHAT THAT MEANS
Open-circuit tests are the practical choice at high frequency, where a true short is hard to realise.
Source: Engineering Circuit Analysis, 8th ed., Ch. 17, pp. 708-713 | CO5 | Bloom L3
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Open-circuit port 2 and drive port 1 with a known current - and check everyone has written it before moving on. At the cost panel, translate it: Open-circuit tests are the practical choice at high frequency, where a true short is hard to realise. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 5: Two-Port Networks. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 17, pp. 708-713. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 19
Open-circuit impedance (z) parameters - worked example
One concrete case, carried all the way to a stated number.
VTU BEC303 | Module 5
Open-circuit impedance (z) parameters
19
GIVEN
A T network with 10 Ω series arms on each side and a 20 Ω shunt arm.
1. Open port 2 and drive port 1: the current flows through 10 Ω then 20 Ω, so z₁₁ = 30 Ω
2. The voltage at port 2 is the drop across the shunt arm alone, so z₂₁ = 20 Ω
3. By symmetry z₂₂ = 30 Ω and z₁₂ = 20 Ω
4. Check: z₁₂ = z₂₁, confirming reciprocity
RESULT
z = [[30, 20], [20, 30]] Ω, and mapping back gives series arms of 10 Ω each with a 20 Ω shunt — the original network.
V₁ = z₁₁I₁ + z₁₂I₂
V₂ = z₂₁I₁ + z₂₂I₂
T network: z = [[30, 20], [20, 30]] Ω
THE MISTAKE STUDENTS MAKE
Students compute z₁₁ with port 2 short-circuited rather than open. That gives the input impedance under a short, which for the worked T is 10 + (20∥10) = 16.7 Ω rather than 30 Ω — a completely different number carrying a completely different meaning.
Source: Engineering Circuit Analysis, 8th ed., Ch. 17, pp. 708-713 | CO5 | Bloom L3
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is A T network with 10 Ω series arms on each side and a 20 Ω shunt arm. Work at the pace of the slowest note-taker and land hard on the result: z = [[30, 20], [20, 30]] Ω, and mapping back gives series arms of 10 Ω each with a 20 Ω shunt — the original network. Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 5: Two-Port Networks. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 17, pp. 708-713. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 20
The relationship between z and y, and when each fails
What it is, why it works, and what it costs.
VTU BEC303 | Module 5
The relationship between z and y, and…
20
THE MECHANISM
The z and y matrices are inverses of each other, z = y⁻¹, provided the inverse exists. It does not always: a network whose y matrix is singular has no z representation and vice versa. The classic example is an ideal series impedance with nothing in shunt — its z parameters are infinite because opening one port leaves no path at all, so the open-circuit test is meaningless. Conversely an ideal shunt element has no y representation in some configurations. This is not a mathematical curiosity; it is the concrete reason a single parameter set cannot serve every network, and it is what the next unit generalises.
KEY TERMS
• matrix inverse
• determinant
• singular matrix
• undefined parameter set
TAKEAWAY
z and y are matrix inverses, and when the inverse does not exist that parameter set simply does not describe the network.
DIAGRAM FOR PHASE 2
Left: the z matrix and the y matrix connected by a double-headed arrow labelled "z = y⁻¹" with the inversion formula shown beneath using the determinant Δ. Right: two failure cases side by side. Case A shows a…
Source: Engineering Circuit Analysis, 8th ed., Ch. 17, pp. 692-713
CO5 | Bloom L4 | visual id: z-y-inverse-with-failure
Notes: What to say: Give them the idea before the formalism. Say it plainly first: The z and y matrices are inverses of each other, z = y⁻¹, provided the inverse exists. Then add the part they are examined on - z and y are matrix inverses, and when the inverse does not exist that parameter set simply does not describe the network. Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "matrix inverse" constrain here, and what would break if it did not hold? Animation instructions: the two matrices appear with the inversion arrow animating between them, the determinant formula types in, then case A draws with its open port flashing red and its badge landing, then case B does the same, then the determinant caption appears. Transition style: Fade [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 5: Two-Port Networks. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 17, pp. 692-713. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 21
The relationship between z and y, and when each fails - how it works
The procedure in order, and what each pass costs you.
VTU BEC303 | Module 5
The relationship between z and y, and…
21
1. Compute the determinant of the matrix you hold
2. If it is non-zero, invert to obtain the other set
3. If it is zero, report that the other representation does not exist
4. Inspect the topology for a lone series or lone shunt element as the likely cause
5. Choose a different parameter set, such as h or ABCD, that does exist
COST AND BEHAVIOUR
Best: O(1) — a 2×2 inversion
Typical: O(1) plus a determinant check
Worst: O(1), but the failure case requires selecting an entirely different representation
WHAT THAT MEANS
The determinant check costs nothing and prevents dividing by zero unnoticed.
Source: Engineering Circuit Analysis, 8th ed., Ch. 17, pp. 692-713 | CO5 | Bloom L4
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Compute the determinant of the matrix you hold - and check everyone has written it before moving on. At the cost panel, translate it: The determinant check costs nothing and prevents dividing by zero unnoticed. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 5: Two-Port Networks. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 17, pp. 692-713. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 22
The relationship between z and y, and when each fails - worked example
One concrete case, carried all the way to a stated number.
VTU BEC303 | Module 5
The relationship between z and y, and…
22
GIVEN
z = [[30, 20], [20, 30]] Ω.
1. Determinant Δ = 30 × 30 − 20 × 20 = 900 − 400 = 500
2. y₁₁ = z₂₂/Δ = 30/500 = 0.06 S
3. y₁₂ = −z₁₂/Δ = −20/500 = −0.04 S
4. y₂₁ = −0.04 S and y₂₂ = 0.06 S
RESULT
y = [[0.06, −0.04], [−0.04, 0.06]] S — a valid inverse because the determinant was non-zero, and still reciprocal as expected.
Δ = z₁₁z₂₂ − z₁₂z₂₁ = 500
y = (1/Δ)[[z₂₂, −z₁₂], [−z₂₁, z₁₁]]
= [[0.06, −0.04], [−0.04, 0.06]] S
THE MISTAKE STUDENTS MAKE
Students invert element by element, writing y₁₁ = 1/z₁₁. Matrix inversion is not elementwise reciprocation; for the worked example that shortcut gives 0.0333 S against the correct 0.06 S, an 80 % error.
Source: Engineering Circuit Analysis, 8th ed., Ch. 17, pp. 692-713 | CO5 | Bloom L4
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is z = [[30, 20], [20, 30]] Ω. Work at the pace of the slowest note-taker and land hard on the result: y = [[0.06, −0.04], [−0.04, 0.06]] S — a valid inverse because the determinant was non-zero, and still reciprocal as expected. Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 5: Two-Port Networks. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 17, pp. 692-713. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 23
Hybrid (h) parameters
What it is, why it works, and what it costs.
VTU BEC303 | Module 5
Hybrid (h) parameters
23
THE MECHANISM
The h parameters mix the variable choice: V₁ = h₁₁I₁ + h₁₂V₂ and I₂ = h₂₁I₁ + h₂₂V₂. The four coefficients therefore have mixed units — h₁₁ in ohms, h₂₂ in siemens, and h₁₂ and h₂₁ dimensionless. This apparently awkward combination exists because it matches how a bipolar transistor is actually used and measured: h₁₁ is the input impedance with the output shorted, h₂₁ is the forward current gain with the output shorted, and both are exactly the quantities a transistor datasheet quotes as h_ie and h_fe. The set is also well defined for devices where z or y fail, which is the practical reason it survives in device modelling long after the others have been abandoned.
KEY TERMS
• h parameters
• mixed variables
• h_ie
• h_fe
• transistor model
TAKEAWAY
h parameters exist because transistors are current-in, voltage-out devices — the mixed units follow from the physics, not from taste.
DIAGRAM FOR PHASE 2
Left: the two h equations with each coefficient annotated with its unit — h₁₁ ohms, h₁₂ dimensionless, h₂₁ dimensionless, h₂₂ siemens. Centre: the h-parameter equivalent circuit, showing h₁₁ in series at the i…
Source: Engineering Circuit Analysis, 8th ed., Ch. 17, pp. 713-716
CO5 | Bloom L3 | visual id: h-parameter-transistor-link
Notes: What to say: Give them the idea before the formalism. Say it plainly first: The h parameters mix the variable choice: V₁ = h₁₁I₁ + h₁₂V₂ and I₂ = h₂₁I₁ + h₂₂V₂. Then add the part they are examined on - h parameters exist because transistors are current-in, voltage-out devices — the mixed units follow from the physics, not fr… Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "h parameters" constrain here, and what would break if it did not hold? Animation instructions: the equations type in with their unit annotations appearing one at a time, then the equivalent circuit builds left to right with the two dependent sources snapping in, then the transistor appears and the two mapping callouts sweep across from the circuit. Transition style: Fade [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 5: Two-Port Networks. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 17, pp. 713-716. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 24
Hybrid (h) parameters - how it works
The procedure in order, and what each pass costs you.
VTU BEC303 | Module 5
Hybrid (h) parameters
24
1. Short-circuit port 2 and drive port 1 with a known current
2. Measure V₁ for h₁₁ and I₂ for h₂₁
3. Open-circuit port 1 and drive port 2 with a known voltage
4. Measure V₁ for h₁₂ and I₂ for h₂₂
5. Record the mixed units explicitly
6. Cross-check h₂₁ against the device datasheet h_fe
COST AND BEHAVIOUR
Best: two measurements for four parameters
Typical: two network solves with mixed excitation types
Worst: two solves plus unit bookkeeping
WHAT THAT MEANS
Mixed units make dimensional checking unusually valuable here.
Source: Engineering Circuit Analysis, 8th ed., Ch. 17, pp. 713-716 | CO5 | Bloom L3
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Short-circuit port 2 and drive port 1 with a known current - and check everyone has written it before moving on. At the cost panel, translate it: Mixed units make dimensional checking unusually valuable here. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 5: Two-Port Networks. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 17, pp. 713-716. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 25
Hybrid (h) parameters - worked example
One concrete case, carried all the way to a stated number.
VTU BEC303 | Module 5
Hybrid (h) parameters
25
GIVEN
A transistor small-signal model with h₁₁ = 2 kΩ, h₁₂ ≈ 0, h₂₁ = 100, h₂₂ = 20 µS, driven by a 10 µA base current with a 5 kΩ load.
1. Input: V₁ = h₁₁I₁ = 2000 × 10e−6 = 20 mV
2. Output current source: h₂₁I₁ = 100 × 10e−6 = 1 mA
3. Output conductance h₂₂ = 20 µS is in parallel with the 5 kΩ load conductance of 200 µS
4. V₂ = −1 mA/(220 µS) = −4.55 V
RESULT
Voltage gain = −4.55/0.02 = −227, and the minus sign is the phase inversion of a common-emitter stage.
V₁ = h₁₁I₁ + h₁₂V₂ (h₁₁ in Ω)
I₂ = h₂₁I₁ + h₂₂V₂ (h₂₂ in S)
A_v = V₂/V₁ = −227 for the worked values
THE MISTAKE STUDENTS MAKE
Students treat all four h parameters as dimensionless because two of them are. Multiplying a current by a dimensionless h₁₁ produces a current where a voltage was needed, and the error survives to the end of the calculation looking like a gain.
Source: Engineering Circuit Analysis, 8th ed., Ch. 17, pp. 713-716 | CO5 | Bloom L3
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is A transistor small-signal model with h₁₁ = 2 kΩ, h₁₂ ≈ 0, h₂₁ = 100, h₂₂ = 20 µS, driven by a 10 µA base current with a 5 kΩ load. Work at the pace of the slowest note-taker and land hard on the result: Voltage gain = −4.55/0.02 = −227, and the minus sign is the phase inversion of a common-emitter stage. Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 5: Two-Port Networks. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 17, pp. 713-716. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 26
Why multiple representations are required
What it is, why it works, and what it costs.
VTU BEC303 | Module 5
Why multiple representations are requ…
26
THE MECHANISM
Six parameter sets exist for three distinct reasons. The first is existence: some networks simply have no z representation and others no y, because the corresponding matrix is singular — a lone series impedance is the standard counterexample for z. The second is measurement practicality: a true short circuit is hard to realise at high frequency because of lead inductance, so open-circuit z measurements are preferred there, while at low frequency the reverse is true. The third is algebraic convenience for a particular operation: ABCD parameters multiply under cascading while z and y do not, so a chain of stages is trivial in ABCD and painful in anything else. No single set is best; the correct one depends on whether you are asking about existence, measurement or composition.
KEY TERMS
• existence
• singular matrix
• measurement practicality
• cascade convenience
TAKEAWAY
Choose the parameter set by the question — existence, ease of measurement, or what operation you are about to perform.
DIAGRAM FOR PHASE 2
A central selector dial with six labelled positions — z, y, h, g, ABCD, inverse ABCD — and three input levers feeding into it from the left. Lever 1 "Does it exist?" points at z and y with a red X on each for…
Source: Engineering Circuit Analysis, 8th ed., Ch. 17, pp. 713-716
CO5 | Bloom L5 | visual id: parameter-set-selector
Notes: What to say: Give them the idea before the formalism. Say it plainly first: Six parameter sets exist for three distinct reasons. Then add the part they are examined on - Choose the parameter set by the question — existence, ease of measurement, or what operation you are about to perform. Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "existence" constrain here, and what would break if it did not hold? Animation instructions: the dial and its six positions draw, then lever 1 animates and the dial swings with the red X badges appearing, then lever 2 animates and the dial swings to z, then lever 3 animates and the dial swings to ABCD and holds. Transition style: Fade [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 5: Two-Port Networks. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 17, pp. 713-716. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 27
Why multiple representations are required - how it works
The procedure in order, and what each pass costs you.
VTU BEC303 | Module 5
Why multiple representations are requ…
27
1. Ask whether the required set exists for this topology by checking the relevant determinant
2. Ask which terminations are practical at the frequency of interest
3. Ask what operation follows — cascade, parallel, series
4. Choose ABCD for cascades, y for parallel connection, z for series connection
5. Choose h for active devices where the datasheet already uses it
6. Convert between sets only when necessary, and check the determinant before inverting
COST AND BEHAVIOUR
Best: O(1) selection from the question type
Typical: O(1) plus one determinant check
Worst: O(1) conversion between sets
WHAT THAT MEANS
Conversion is cheap; choosing the wrong set for a cascade is what costs real effort.
Source: Engineering Circuit Analysis, 8th ed., Ch. 17, pp. 713-716 | CO5 | Bloom L5
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Ask whether the required set exists for this topology by checking the relevant determinant - and check everyone has written it before moving on. At the cost panel, translate it: Conversion is cheap; choosing the wrong set for a cascade is what costs real effort. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 5: Two-Port Networks. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 17, pp. 713-716. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 28
Why multiple representations are required - worked example
One concrete case, carried all the way to a stated number.
VTU BEC303 | Module 5
Why multiple representations are requ…
28
GIVEN
A four-stage filter chain is to be analysed, and the stages are specified by their z parameters.
1. Cascading is the operation, so ABCD is the natural set
2. Convert each stage from z to ABCD using the standard relations
3. Multiply the four ABCD matrices in order
4. Convert the resulting overall ABCD back to z if the answer is wanted in that form
RESULT
Four conversions plus three matrix multiplications, against the alternative of repeatedly solving loaded networks stage by stage — the conversion overhead pays for itself immediately.
cascade ⇒ ABCD_total = A₁·A₂·A₃·A₄
parallel ⇒ y_total = y₁ + y₂
series ⇒ z_total = z₁ + z₂
THE MISTAKE STUDENTS MAKE
Students learn z parameters first and try to use them for everything, including cascades. z parameters do not multiply under cascading, so each stage has to be re-solved with its actual loading — which is exactly the work ABCD was invented to avoid.
Source: Engineering Circuit Analysis, 8th ed., Ch. 17, pp. 713-716 | CO5 | Bloom L5
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is A four-stage filter chain is to be analysed, and the stages are specified by their z parameters. Work at the pace of the slowest note-taker and land hard on the result: Four conversions plus three matrix multiplications, against the alternative of repeatedly solving loaded networks stage by stage… Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 5: Two-Port Networks. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 17, pp. 713-716. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 29
Transmission (ABCD) parameters
What it is, why it works, and what it costs.
VTU BEC303 | Module 5
Transmission (ABCD) parameters
29
THE MECHANISM
The transmission or ABCD parameters express the input variables in terms of the output ones: V₁ = A·V₂ − B·I₂ and I₁ = C·V₂ − D·I₂. The minus signs arise because the convention takes I₂ as flowing into the network while the transmission description treats it as flowing out toward the load; getting this sign wrong is the single most common ABCD error. The four coefficients have mixed units — A and D dimensionless, B in ohms, C in siemens. The set is defined precisely so that cascaded networks multiply, which makes it the standard description for transmission lines, filter chains and any signal path built from stages.
KEY TERMS
• ABCD parameters
• transmission matrix
• input in terms of output
• sign convention on I₂
TAKEAWAY
ABCD looks backwards — input written in terms of output — and that is exactly what makes cascading into matrix multiplication.
DIAGRAM FOR PHASE 2
Centre: a two-port box with V₁, I₁ on the left and V₂, I₂ on the right, with I₂ drawn as an arrow entering the box and a second faded arrow labelled "−I₂, toward the load" pointing out. A red highlight ring su…
Source: Engineering Circuit Analysis, 8th ed., Ch. 17, pp. 716-720
CO5 | Bloom L4 | visual id: abcd-definition-and-signs
Notes: What to say: Give them the idea before the formalism. Say it plainly first: The transmission or ABCD parameters express the input variables in terms of the output ones: V₁ = A·V₂ − B·I₂ and I₁ = C·V₂ − D·I₂. Then add the part they are examined on - ABCD looks backwards — input written in terms of output — and that is exactly what makes cascading into matrix multiplicatio… Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "ABCD parameters" constrain here, and what would break if it did not hold? Animation instructions: the box and port variables draw, the I₂ arrow animates inward and the faded outward arrow appears, the matrix equation types in and the red ring pulses twice on the minus signs, then the unit strip slides in from the left, then the cascade thumbnail appears on the right. Transition style: Fade [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 5: Two-Port Networks. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 17, pp. 716-720. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 30
Transmission (ABCD) parameters - how it works
The procedure in order, and what each pass costs you.
VTU BEC303 | Module 5
Transmission (ABCD) parameters
30
1. Open-circuit port 2 (I₂ = 0) and compute A = V₁/V₂ and C = I₁/V₂
2. Short-circuit port 2 (V₂ = 0) and compute B = −V₁/I₂ and D = −I₁/I₂
3. Record the mixed units
4. Check AD − BC = 1 for a reciprocal network
5. Check A = D for a symmetric network
6. Use the matrix directly for cascade calculations
COST AND BEHAVIOUR
Best: two solves for four parameters
Typical: two network solves
Worst: two symbolic solves
WHAT THAT MEANS
The AD − BC = 1 check catches most sign errors immediately.
Source: Engineering Circuit Analysis, 8th ed., Ch. 17, pp. 716-720 | CO5 | Bloom L4
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Open-circuit port 2 (I₂ = 0) and compute A = V₁/V₂ and C = I₁/V₂ - and check everyone has written it before moving on. At the cost panel, translate it: The AD − BC = 1 check catches most sign errors immediately. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 5: Two-Port Networks. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 17, pp. 716-720. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 31
Transmission (ABCD) parameters - worked example
One concrete case, carried all the way to a stated number.
VTU BEC303 | Module 5
Transmission (ABCD) parameters
31
GIVEN
A single series impedance Z between the ports, with nothing in shunt.
1. Open port 2: no current flows, so V₁ = V₂, giving A = 1, and I₁ = 0, giving C = 0
2. Short port 2: V₁ = −I₂·Z, giving B = Z; and I₁ = −I₂, giving D = 1
3. ABCD = [[1, Z], [0, 1]]
4. Check: AD − BC = 1 × 1 − Z × 0 = 1 ✓
RESULT
ABCD = [[1, Z], [0, 1]], the standard series-element matrix — and note this network has no z representation at all, which is why ABCD is useful here.
V₁ = A·V₂ − B·I₂
I₁ = C·V₂ − D·I₂
series Z: [[1, Z],[0, 1]], shunt Y: [[1, 0],[Y, 1]]
THE MISTAKE STUDENTS MAKE
Students drop the minus signs and write V₁ = AV₂ + BI₂. The resulting B and D come out with the wrong sign, the AD − BC = 1 check fails, and every cascaded result inherits the error.
Source: Engineering Circuit Analysis, 8th ed., Ch. 17, pp. 716-720 | CO5 | Bloom L4
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is A single series impedance Z between the ports, with nothing in shunt. Work at the pace of the slowest note-taker and land hard on the result: ABCD = [[1, Z], [0, 1]], the standard series-element matrix — and note this network has no z representation at all, which is why… Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 5: Two-Port Networks. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 17, pp. 716-720. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 32
Cascading two-ports with ABCD
What it is, why it works, and what it costs.
VTU BEC303 | Module 5
Cascading two-ports with ABCD
32
THE MECHANISM
When two-ports are cascaded, the output of one becomes the input of the next, and the overall ABCD matrix is the ordered product of the individual matrices, taken in the direction of signal flow. Matrix multiplication does not commute, so reversing the order generally gives a different network — which is correct, since a filter followed by an attenuator is not the same as an attenuator followed by a filter when either has non-trivial impedance. Crucially, the method automatically accounts for inter-stage loading, which is the effect that breaks the naive multiplication of transfer functions in Module 4. A ladder network can therefore be built by alternately multiplying series and shunt element matrices.
KEY TERMS
• cascade
• matrix multiplication
• order matters
• ladder synthesis
TAKEAWAY
ABCD multiplication handles inter-stage loading automatically — which is exactly what naive transfer-function cascading gets wrong.
DIAGRAM FOR PHASE 2
Top: three two-port boxes in a row, signal flowing left to right, each labelled with its own ABCD matrix. Curved brackets beneath group them into a single equivalent box labelled with the product A₁A₂A₃. A red…
Source: Engineering Circuit Analysis, 8th ed., Ch. 17, pp. 716-720
CO5 | Bloom L4 | visual id: abcd-cascade-chain
Notes: What to say: Give them the idea before the formalism. Say it plainly first: When two-ports are cascaded, the output of one becomes the input of the next, and the overall ABCD matrix is the ordered product of the individual matrice… Then add the part they are examined on - ABCD multiplication handles inter-stage loading automatically — which is exactly what naive transfer-function cascading gets… Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "cascade" constrain here, and what would break if it did not hold? Animation instructions: the three boxes draw left to right with their matrices, then the brackets sweep under and the equivalent box forms with the product expression, then the red naive panel appears and is struck through, then the ladder strip builds by alternating matrices sliding in. Transition style: Fade [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 5: Two-Port Networks. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 17, pp. 716-720. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 33
Cascading two-ports with ABCD - how it works
The procedure in order, and what each pass costs you.
VTU BEC303 | Module 5
Cascading two-ports with ABCD
33
1. Write the ABCD matrix of each stage in signal-flow order
2. Multiply them left to right in that order
3. Do not reorder the product
4. Convert the resulting matrix to whichever parameter set the answer requires
5. For a ladder, alternate series and shunt element matrices
6. Verify AD − BC = 1 on the product if every stage was reciprocal
COST AND BEHAVIOUR
Best: O(k) for k stages, each a 2×2 multiply
Typical: O(k) multiplications of 2×2 matrices
Worst: O(k) with symbolic entries, where expression growth dominates
WHAT THAT MEANS
Linear in the number of stages — compared with re-solving a loaded network per stage, this is the whole advantage.
Source: Engineering Circuit Analysis, 8th ed., Ch. 17, pp. 716-720 | CO5 | Bloom L4
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Write the ABCD matrix of each stage in signal-flow order - and check everyone has written it before moving on. At the cost panel, translate it: Linear in the number of stages — compared with re-solving a loaded network per stage, this is the whole advantage. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 5: Two-Port Networks. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 17, pp. 716-720. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 34
Cascading two-ports with ABCD - worked example
One concrete case, carried all the way to a stated number.
VTU BEC303 | Module 5
Cascading two-ports with ABCD
34
GIVEN
A series 10 Ω followed by a shunt 0.05 S, cascaded.
1. Series: [[1, 10], [0, 1]]
2. Shunt: [[1, 0], [0.05, 1]]
3. Product: [[1 + 10×0.05, 10], [0.05, 1]] = [[1.5, 10], [0.05, 1]]
4. Check: AD − BC = 1.5 × 1 − 10 × 0.05 = 1.5 − 0.5 = 1 ✓
RESULT
Overall ABCD = [[1.5, 10], [0.05, 1]], with the reciprocity check passing — and the loading of the shunt on the series element already accounted for.
[[1,10],[0,1]] · [[1,0],[0.05,1]] = [[1.5,10],[0.05,1]]
AD − BC = 1.5 − 0.5 = 1 ✓
THE MISTAKE STUDENTS MAKE
Students multiply the matrices in reverse order, treating matrix multiplication as commutative. The product order must follow signal flow; reversing it describes a physically different cascade, and the numbers are wrong in a way the AD − BC check will not catch.
Source: Engineering Circuit Analysis, 8th ed., Ch. 17, pp. 716-720 | CO5 | Bloom L4
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is A series 10 Ω followed by a shunt 0.05 S, cascaded. Work at the pace of the slowest note-taker and land hard on the result: Overall ABCD = [[1.5, 10], [0.05, 1]], with the reciprocity check passing — and the loading of the shunt on the series element al… Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 5: Two-Port Networks. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 17, pp. 716-720. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 35
Two-port symmetry and reciprocity
What it is, why it works, and what it costs.
VTU BEC303 | Module 5
Two-port symmetry and reciprocity
35
THE MECHANISM
Reciprocity and symmetry are distinct conditions that are often confused. Reciprocity means excitation and response may be interchanged, and it shows as z₁₂ = z₂₁, y₁₂ = y₂₁, h₁₂ = −h₂₁, or AD − BC = 1. Symmetry means the two ports are interchangeable — the network looks the same from either side — and it shows as z₁₁ = z₂₂, y₁₁ = y₂₂ or A = D. Every symmetric passive network is reciprocal, but the reverse does not hold: an unbalanced ladder is reciprocal and not symmetric. These conditions are worth checking on every computed parameter set, because they are free and they catch sign and arithmetic errors that would otherwise propagate.
KEY TERMS
• reciprocity condition
• symmetry condition
• z₁₂ = z₂₁
• z₁₁ = z₂₂
• AD − BC = 1
TAKEAWAY
Reciprocity is about swapping source and meter; symmetry is about swapping the ports themselves — and they are not the same claim.
DIAGRAM FOR PHASE 2
A 2×2 conceptual grid. Top-left cell "Reciprocal, symmetric": a balanced T network with equal arms, showing z₁₂ = z₂₁ and z₁₁ = z₂₂ both ticked green. Top-right "Reciprocal, not symmetric": an unbalanced ladde…
Source: Engineering Circuit Analysis, 8th ed., Ch. 17, pp. 699-708
CO5 | Bloom L4 | visual id: reciprocity-vs-symmetry-grid
Notes: What to say: Give them the idea before the formalism. Say it plainly first: Reciprocity and symmetry are distinct conditions that are often confused. Then add the part they are examined on - Reciprocity is about swapping source and meter; symmetry is about swapping the ports themselves — and they are not the same… Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "reciprocity condition" constrain here, and what would break if it did not hold? Animation instructions: the grid draws, each of the three circuit cells appears with its ticks and crosses landing one at a time, then the summary card fills in line by line. Transition style: Fade [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 5: Two-Port Networks. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 17, pp. 699-708. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 36
Two-port symmetry and reciprocity - how it works
The procedure in order, and what each pass costs you.
VTU BEC303 | Module 5
Two-port symmetry and reciprocity
36
1. Compute the full parameter set
2. Test reciprocity with the condition appropriate to that set
3. Test symmetry separately with its own condition
4. If reciprocity fails, confirm the network contains a dependent source or a directional element
5. If symmetry fails but reciprocity holds, the network is simply unbalanced
6. Use both tests as arithmetic checks on the computed parameters
COST AND BEHAVIOUR
Best: O(1) — two comparisons
Typical: O(1)
Worst: O(1) plus one determinant evaluation for the ABCD test
WHAT THAT MEANS
Free checks that catch a large fraction of sign errors.
Source: Engineering Circuit Analysis, 8th ed., Ch. 17, pp. 699-708 | CO5 | Bloom L4
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Compute the full parameter set - and check everyone has written it before moving on. At the cost panel, translate it: Free checks that catch a large fraction of sign errors. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 5: Two-Port Networks. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 17, pp. 699-708. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 37
Two-port symmetry and reciprocity - worked example
One concrete case, carried all the way to a stated number.
VTU BEC303 | Module 5
Two-port symmetry and reciprocity
37
GIVEN
A ladder with z = [[30, 20], [20, 45]] Ω.
1. Reciprocity test: z₁₂ = 20 and z₂₁ = 20, equal — reciprocal
2. Symmetry test: z₁₁ = 30 and z₂₂ = 45, unequal — not symmetric
3. Conclusion: a passive unbalanced ladder
4. Consequence: swapping source and meter gives the same reading, but swapping the ports does not give the same network
RESULT
Reciprocal but not symmetric — so reciprocity may be exploited to halve a two-configuration measurement, while port interchange may not.
reciprocal : z₁₂ = z₂₁ (also y₁₂=y₂₁, h₁₂=−h₂₁, AD−BC=1)
symmetric : z₁₁ = z₂₂ (also y₁₁=y₂₂, A=D)
THE MISTAKE STUDENTS MAKE
Students treat a symmetric-looking schematic as proof of reciprocity and stop checking. Symmetry of the drawing proves neither condition — a symmetric layout containing a dependent source is neither reciprocal nor symmetric in the parameter sense.
Source: Engineering Circuit Analysis, 8th ed., Ch. 17, pp. 699-708 | CO5 | Bloom L4
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is A ladder with z = [[30, 20], [20, 45]] Ω. Work at the pace of the slowest note-taker and land hard on the result: Reciprocal but not symmetric — so reciprocity may be exploited to halve a two-configuration measurement, while port interchange m… Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 5: Two-Port Networks. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 17, pp. 699-708. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 38
Input impedance of a terminated two-port
What it is, why it works, and what it costs.
VTU BEC303 | Module 5
Input impedance of a terminated two-p…
38
THE MECHANISM
The input impedance of a two-port is not a property of the network alone — it depends on what terminates the far port. In terms of z parameters, Z_in = z₁₁ − z₁₂z₂₁/(z₂₂ + Z_L). The first term is the open-circuit input impedance and the second is the correction reflected back through the network by the load. The correction vanishes when Z_L is infinite, recovering z₁₁, and is largest when Z_L is zero. This is the formal version of an everyday effect: changing a loudspeaker changes what an amplifier's output stage sees, and changing an antenna changes what a receiver's input sees.
KEY TERMS
• terminated two-port
• Z_in
• load dependence
• reflected impedance
TAKEAWAY
The load reflects back through the network and changes the input impedance — Z_in is never a property of the two-port alone.
DIAGRAM FOR PHASE 2
A two-port box with a source at port 1 and a load Z_L at port 2. A forward arrow runs from port 1 through the box to the load labelled "excitation", and a curved return arrow loops back from the load through t…
Source: Engineering Circuit Analysis, 8th ed., Ch. 17, pp. 708-713
CO5 | Bloom L4 | visual id: zin-reflection-path
Notes: What to say: Give them the idea before the formalism. Say it plainly first: The input impedance of a two-port is not a property of the network alone — it depends on what terminates the far port. Then add the part they are examined on - The load reflects back through the network and changes the input impedance — Z_in is never a property of the two-port alone. Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "terminated two-port" constrain here, and what would break if it did not hold? Animation instructions: box, source and load draw, the forward arrow sweeps right, the curved return arrow sweeps back, the formula types in with each term lighting as its arrow pulses, then the two limiting-case insets fade in side by side. Transition style: Fade [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 5: Two-Port Networks. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 17, pp. 708-713. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 39
Input impedance of a terminated two-port - how it works
The procedure in order, and what each pass costs you.
VTU BEC303 | Module 5
Input impedance of a terminated two-p…
39
1. Obtain the z parameters of the two-port
2. Identify the load impedance Z_L at port 2
3. Compute the reflected term z₁₂z₂₁/(z₂₂ + Z_L)
4. Subtract it from z₁₁ to get Z_in
5. Check the two limiting cases as a sanity test
6. Recompute whenever the load changes
COST AND BEHAVIOUR
Best: O(1) once z is known
Typical: O(1) per load value
Worst: recomputation per frequency point and per load
WHAT THAT MEANS
Cheap to evaluate repeatedly, which is why z parameters plus this formula beat re-solving the network for each load.
Source: Engineering Circuit Analysis, 8th ed., Ch. 17, pp. 708-713 | CO5 | Bloom L4
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Obtain the z parameters of the two-port - and check everyone has written it before moving on. At the cost panel, translate it: Cheap to evaluate repeatedly, which is why z parameters plus this formula beat re-solving the network for each load. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 5: Two-Port Networks. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 17, pp. 708-713. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 40
Input impedance of a terminated two-port - worked example
One concrete case, carried all the way to a stated number.
VTU BEC303 | Module 5
Input impedance of a terminated two-p…
40
GIVEN
z = [[30, 20], [20, 30]] Ω with a 50 Ω load at port 2.
1. Reflected term = 20 × 20/(30 + 50) = 400/80 = 5 Ω
2. Z_in = 30 − 5 = 25 Ω
3. Check Z_L → ∞: reflected term → 0, so Z_in → 30 Ω = z₁₁ ✓
4. Check Z_L = 0: reflected term = 400/30 = 13.3, so Z_in = 16.7 Ω, matching the direct short-circuit calculation
RESULT
Z_in = 25 Ω with the 50 Ω load, and both limiting cases confirm the formula — the input impedance ranges from 16.7 Ω to 30 Ω depending purely on the load.
Z_in = z₁₁ − z₁₂z₂₁/(z₂₂ + Z_L)
= 30 − 400/80 = 25 Ω
Z_L→∞ ⇒ 30 Ω; Z_L=0 ⇒ 16.7 Ω
THE MISTAKE STUDENTS MAKE
Students quote z₁₁ as the input impedance of a terminated network. z₁₁ is the open-circuit value only; in the worked example the actual input impedance under a 50 Ω load is 25 Ω, a 17 % difference that matters directly for any matching calculation.
Source: Engineering Circuit Analysis, 8th ed., Ch. 17, pp. 708-713 | CO5 | Bloom L4
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is z = [[30, 20], [20, 30]] Ω with a 50 Ω load at port 2. Work at the pace of the slowest note-taker and land hard on the result: Z_in = 25 Ω with the 50 Ω load, and both limiting cases confirm the formula — the input impedance ranges from 16.7 Ω to 30 Ω depe… Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 5: Two-Port Networks. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 17, pp. 708-713. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 41
Output impedance and the source-terminated two-port
What it is, why it works, and what it costs.
VTU BEC303 | Module 5
Output impedance and the source-termi…
41
THE MECHANISM
Output impedance is the mirror of input impedance: Z_out = z₂₂ − z₁₂z₂₁/(z₁₁ + Z_S), where Z_S is the impedance of the source driving port 1. It is exactly the Thévenin impedance looking back into port 2 with the source network attached, and it is what a load at port 2 actually sees. The symmetry of the two formulas is not a coincidence — it is reciprocity expressed in terminated form. Together the pair of formulas closes the loop with Module 2: given a two-port, a source and a load, Z_out determines the matched condition for maximum power transfer at the output, and Z_in determines it at the input.
KEY TERMS
• Z_out
• source impedance
• reverse reflection
• Thévenin at port 2
TAKEAWAY
Z_out is Z_in's mirror image with the source replacing the load — and it is the Thévenin impedance a real load will meet.
DIAGRAM FOR PHASE 2
A mirrored layout with a vertical centre line. Left half shows the input case: source Z_S, two-port, load Z_L, with Z_in marked at port 1 and the formula z₁₁ − z₁₂z₂₁/(z₂₂ + Z_L) beneath. Right half shows the…
Source: Engineering Circuit Analysis, 8th ed., Ch. 17, pp. 708-713
CO5 | Bloom L4 | visual id: zout-mirror-of-zin
Notes: What to say: Give them the idea before the formalism. Say it plainly first: Output impedance is the mirror of input impedance: Z_out = z₂₂ − z₁₂z₂₁/(z₁₁ + Z_S), where Z_S is the impedance of the source driving port 1. Then add the part they are examined on - Z_out is Z_in's mirror image with the source replacing the load — and it is the Thévenin impedance a real load will meet. Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "Z_out" constrain here, and what would break if it did not hold? Animation instructions: the left half builds with its formula, the centre line draws, the right half builds as an animated mirror of the left, the central swap badge appears, then the Module 2 link box slides up last. Transition style: Fade [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 5: Two-Port Networks. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 17, pp. 708-713. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 42
Output impedance and the source-terminated two-port - how it works
The procedure in order, and what each pass costs you.
VTU BEC303 | Module 5
Output impedance and the source-termi…
42
1. Obtain the z parameters of the two-port
2. Identify the source impedance Z_S at port 1
3. Compute the reflected term z₁₂z₂₁/(z₁₁ + Z_S)
4. Subtract from z₂₂ to obtain Z_out
5. Combine with the open-circuit output voltage to form a Thévenin equivalent at port 2
6. Apply the conjugate match if maximum output power is required
COST AND BEHAVIOUR
Best: O(1) once z is known
Typical: O(1) per source impedance
Worst: recomputation per frequency point
WHAT THAT MEANS
The Thévenin equivalent at port 2 makes any subsequent load sweep trivial.
Source: Engineering Circuit Analysis, 8th ed., Ch. 17, pp. 708-713 | CO5 | Bloom L4
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Obtain the z parameters of the two-port - and check everyone has written it before moving on. At the cost panel, translate it: The Thévenin equivalent at port 2 makes any subsequent load sweep trivial. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 5: Two-Port Networks. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 17, pp. 708-713. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 43
Output impedance and the source-terminated two-port - worked example
One concrete case, carried all the way to a stated number.
VTU BEC303 | Module 5
Output impedance and the source-termi…
43
GIVEN
z = [[30, 20], [20, 30]] Ω driven from a source with Z_S = 10 Ω.
1. Reflected term = 20 × 20/(30 + 10) = 400/40 = 10 Ω
2. Z_out = 30 − 10 = 20 Ω
3. For maximum power into a resistive load, choose Z_L = 20 Ω
4. Check with Z_S → ∞: reflected term → 0, so Z_out → z₂₂ = 30 Ω as expected
RESULT
Z_out = 20 Ω, so a 20 Ω load extracts maximum power — and the limiting case confirms the formula reduces to z₂₂ when the source is an ideal current source.
Z_out = z₂₂ − z₁₂z₂₁/(z₁₁ + Z_S)
= 30 − 400/40 = 20 Ω
⇒ matched load Z_L = 20 Ω
THE MISTAKE STUDENTS MAKE
Students use the load impedance in the output formula and the source impedance in the input formula, having memorised the shapes without the reasoning. Each formula uses the impedance at the far port from the one being computed, which is what "reflected through the network" means.
Source: Engineering Circuit Analysis, 8th ed., Ch. 17, pp. 708-713 | CO5 | Bloom L4
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is z = [[30, 20], [20, 30]] Ω driven from a source with Z_S = 10 Ω. Work at the pace of the slowest note-taker and land hard on the result: Z_out = 20 Ω, so a 20 Ω load extracts maximum power — and the limiting case confirms the formula reduces to z₂₂ when the source i… Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 5: Two-Port Networks. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 17, pp. 708-713. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 44
Measuring two-port parameters in practice
What it is, why it works, and what it costs.
VTU BEC303 | Module 5
Measuring two-port parameters in prac…
44
THE MECHANISM
Determining parameters experimentally exposes constraints the algebra hides. A short circuit is never ideal — lead inductance makes it an impedance that rises with frequency, so short-circuit sets like y become progressively less trustworthy above a few tens of megahertz. An open circuit is never ideal either, because stray capacitance provides a path, though this degrades more slowly. Both problems push high-frequency practice toward scattering parameters, which use matched terminations instead of shorts and opens. At low frequency, direct measurement is straightforward provided the source and meter impedances are accounted for and the parameters are recorded together with the frequency at which they were taken.
KEY TERMS
• measurement setup
• parasitic effects
• calibration
• frequency sweep
TAKEAWAY
Shorts and opens are idealisations; how badly they fail sets which parameter set you can actually measure at a given frequency.
DIAGRAM FOR PHASE 2
Left column "Ideal": a perfect short drawn as a zero-impedance bar and a perfect open drawn as a clean gap, each with a green tick. Right column "Real": the same short drawn with a small series inductor symbol…
Source: Engineering Circuit Analysis, 8th ed., Ch. 17, pp. 692-713
CO5 | Bloom L5 | visual id: measurement-reality-check
Notes: What to say: Give them the idea before the formalism. Say it plainly first: Determining parameters experimentally exposes constraints the algebra hides. Then add the part they are examined on - Shorts and opens are idealisations; how badly they fail sets which parameter set you can actually measure at a given frequen… Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "measurement setup" constrain here, and what would break if it did not hold? Animation instructions: the ideal column draws with its ticks, then the real column with the parasitic elements popping in and the amber warnings, then the two error curves trace across the frequency axis and the practical-limit marker drops, then the footer note appears. Transition style: Fade [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 5: Two-Port Networks. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 17, pp. 692-713. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 45
Measuring two-port parameters in practice - how it works
The procedure in order, and what each pass costs you.
VTU BEC303 | Module 5
Measuring two-port parameters in prac…
45
1. Choose the parameter set whose terminations are realisable at the test frequency
2. Characterise the test fixture and de-embed its parasitics
3. Apply a known excitation and record both port responses
4. Repeat with the excitation at the other port
5. Record every parameter with its frequency and its units
6. Verify reciprocity and symmetry conditions as a consistency check
COST AND BEHAVIOUR
Best: two measurements per frequency point
Typical: two measurements plus a calibration per frequency point
Worst: full de-embedding at every point in a wide sweep
WHAT THAT MEANS
Calibration usually dominates the measurement time, not the measurement itself.
Source: Engineering Circuit Analysis, 8th ed., Ch. 17, pp. 692-713 | CO5 | Bloom L5
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Choose the parameter set whose terminations are realisable at the test frequency - and check everyone has written it before moving on. At the cost panel, translate it: Calibration usually dominates the measurement time, not the measurement itself. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 5: Two-Port Networks. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 17, pp. 692-713. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 46
Measuring two-port parameters in practice - worked example
One concrete case, carried all the way to a stated number.
VTU BEC303 | Module 5
Measuring two-port parameters in prac…
46
GIVEN
A y-parameter measurement attempted at 100 MHz with a 5 nH lead inductance forming the short.
1. Ideal short impedance: 0 Ω
2. Actual: Z = j·2π·100e6·5e−9 = j3.14 Ω
3. If the network impedances are of order 50 Ω, that is a 6 % perturbation
4. The measured y₁₁ is correspondingly in error, and worse at higher frequencies
RESULT
A 5 nH lead produces 3.14 Ω at 100 MHz — enough to corrupt a y-parameter measurement by several percent, which is why scattering parameters replace them at these frequencies.
Z_short = jωL_lead = j·2π·10⁸·5e−9 = j3.14 Ω
vs 50 Ω reference ⇒ ≈6% perturbation
THE MISTAKE STUDENTS MAKE
Students report parameters without stating the frequency at which they were measured. Every parameter of a network containing reactance is frequency-dependent, so an unlabelled set is not a description of anything.
Source: Engineering Circuit Analysis, 8th ed., Ch. 17, pp. 692-713 | CO5 | Bloom L5
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is A y-parameter measurement attempted at 100 MHz with a 5 nH lead inductance forming the short. Work at the pace of the slowest note-taker and land hard on the result: A 5 nH lead produces 3.14 Ω at 100 MHz — enough to corrupt a y-parameter measurement by several percent, which is why scattering… Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 5: Two-Port Networks. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 17, pp. 692-713. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 47
Choosing and converting between parameter sets
What it is, why it works, and what it costs.
VTU BEC303 | Module 5
Choosing and converting between param…
47
THE MECHANISM
Conversions between sets are all algebraic and all hinge on a determinant. From z to y the relation is a matrix inverse using Δz = z₁₁z₂₂ − z₁₂z₂₁. From z to ABCD, A = z₁₁/z₂₁, B = Δz/z₂₁, C = 1/z₂₁ and D = z₂₂/z₂₁, which shows immediately that the conversion fails when z₂₁ is zero — a network with no forward transmission has no ABCD representation. Beyond cascading, the choice of set also follows the connection type: two-ports connected in parallel have y matrices that add, and two-ports connected in series have z matrices that add, provided the port conditions survive the interconnection.
KEY TERMS
• conversion formulas
• determinant
• parallel connection
• series connection
TAKEAWAY
Every conversion divides by something, so check what that something is before converting — a zero there means the target set does not exist.
DIAGRAM FOR PHASE 2
A hub-and-spoke diagram with four nodes arranged in a diamond: z at the top, y at the bottom, h on the left, ABCD on the right. Each connecting spoke is labelled with the quantity that must be non-zero for tha…
Source: Engineering Circuit Analysis, 8th ed., Ch. 17, pp. 692-720
CO5 | Bloom L5 | visual id: conversion-hub
Notes: What to say: Give them the idea before the formalism. Say it plainly first: Conversions between sets are all algebraic and all hinge on a determinant. Then add the part they are examined on - Every conversion divides by something, so check what that something is before converting — a zero there means the target set… Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "conversion formulas" constrain here, and what would break if it did not hold? Animation instructions: the four nodes appear, the spokes draw one at a time with their conditions labelling, then one spoke's red barrier closes to demonstrate a failed conversion, then the three outer connection badges drop into place. Transition style: Fade [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 5: Two-Port Networks. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 17, pp. 692-720. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 48
Choosing and converting between parameter sets - how it works
The procedure in order, and what each pass costs you.
VTU BEC303 | Module 5
Choosing and converting between param…
48
1. Identify the set you have and the set you need
2. Look up the conversion and identify its divisor
3. Verify the divisor is non-zero
4. Perform the conversion
5. Re-check reciprocity and symmetry in the new set
6. For interconnections, add y for parallel, add z for series, multiply ABCD for cascade
COST AND BEHAVIOUR
Best: O(1) — four arithmetic expressions
Typical: O(1) plus a determinant
Worst: O(1), but a zero divisor forces a different route entirely
WHAT THAT MEANS
The conversions are trivial; the divisor check is the part that carries the engineering content.
Source: Engineering Circuit Analysis, 8th ed., Ch. 17, pp. 692-720 | CO5 | Bloom L5
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Identify the set you have and the set you need - and check everyone has written it before moving on. At the cost panel, translate it: The conversions are trivial; the divisor check is the part that carries the engineering content. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 5: Two-Port Networks. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 17, pp. 692-720. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 49
Choosing and converting between parameter sets - worked example
One concrete case, carried all the way to a stated number.
VTU BEC303 | Module 5
Choosing and converting between param…
49
GIVEN
Convert z = [[30, 20], [20, 30]] Ω to ABCD.
1. Δz = 30 × 30 − 20 × 20 = 500
2. A = z₁₁/z₂₁ = 30/20 = 1.5
3. B = Δz/z₂₁ = 500/20 = 25 Ω
4. C = 1/z₂₁ = 0.05 S, D = z₂₂/z₂₁ = 1.5
RESULT
ABCD = [[1.5, 25], [0.05, 1.5]]; the check AD − BC = 2.25 − 1.25 = 1 confirms reciprocity, and A = D confirms symmetry.
Δz = 500
A = z₁₁/z₂₁ = 1.5, B = Δz/z₂₁ = 25 Ω
C = 1/z₂₁ = 0.05 S, D = z₂₂/z₂₁ = 1.5
AD − BC = 1 ✓, A = D ⇒ symmetric
THE MISTAKE STUDENTS MAKE
Students convert without checking the divisor and obtain infinities or silent nonsense. A network with z₂₁ = 0 transmits nothing forward, and asking for its ABCD matrix is asking for the transmission properties of something that does not transmit.
Source: Engineering Circuit Analysis, 8th ed., Ch. 17, pp. 692-720 | CO5 | Bloom L5
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is Convert z = [[30, 20], [20, 30]] Ω to ABCD. Work at the pace of the slowest note-taker and land hard on the result: ABCD = [[1.5, 25], [0.05, 1.5]]; the check AD − BC = 2.25 − 1.25 = 1 confirms reciprocity, and A = D confirms symmetry. Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 5: Two-Port Networks. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 17, pp. 692-720. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 50
Putting it together: a fully terminated two-port
What it is, why it works, and what it costs.
VTU BEC303 | Module 5
Putting it together: a fully terminat…
50
THE MECHANISM
With a source, a two-port and a load in place, every performance figure follows from the four parameters plus the two terminations. Input impedance uses the load, output impedance uses the source, and voltage gain follows from the z parameters and Z_L as V₂/V₁ = z₂₁Z_L/(z₁₁(z₂₂ + Z_L) − z₁₂z₂₁). Power gain then combines the voltage gain with the input and load impedances. This is where the module pays off: a black box characterised once by four measurements predicts its behaviour with any source and any load, without ever reopening it — and it links directly back to Module 2, since maximum output power requires the load to be the conjugate of Z_out.
KEY TERMS
• voltage gain
• current gain
• power gain
• terminated performance
• insertion loss
TAKEAWAY
Four parameters plus two terminations give every performance figure — that is the whole return on the two-port abstraction.
DIAGRAM FOR PHASE 2
Centre: a full chain — source with Z_S, two-port box labelled with its z matrix, load Z_L. Radiating outward, four dashboard cards each fed by a line from the relevant part of the chain: "Z_in" fed from port 1…
Source: Engineering Circuit Analysis, 8th ed., Ch. 17, pp. 708-720
CO5 | Bloom L5 | visual id: terminated-performance-dashboard
Notes: What to say: Give them the idea before the formalism. Say it plainly first: With a source, a two-port and a load in place, every performance figure follows from the four parameters plus the two terminations. Then add the part they are examined on - Four parameters plus two terminations give every performance figure — that is the whole return on the two-port abstraction. Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "voltage gain" constrain here, and what would break if it did not hold? Animation instructions: the chain draws left to right, then each dashboard card slides out in turn with its feeder line drawing first and its number filling in last, then the footer strip appears. Transition style: Fade [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 5: Two-Port Networks. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 17, pp. 708-720. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 51
Putting it together: a fully terminated two-port - how it works
The procedure in order, and what each pass costs you.
VTU BEC303 | Module 5
Putting it together: a fully terminat…
51
1. Measure or compute the four parameters at the frequency of interest
2. Compute Z_in using the load impedance
3. Compute Z_out using the source impedance
4. Compute the voltage gain from the parameters and the load
5. Combine into current and power gain as required
6. Apply the conjugate match at the output if maximum power is the goal
COST AND BEHAVIOUR
Best: O(1) per termination pair
Typical: O(1) per frequency point
Worst: full recomputation across a frequency sweep
WHAT THAT MEANS
One characterisation supports unlimited termination combinations, which is the entire economic argument for two-port modelling.
Source: Engineering Circuit Analysis, 8th ed., Ch. 17, pp. 708-720 | CO5 | Bloom L5
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Measure or compute the four parameters at the frequency of interest - and check everyone has written it before moving on. At the cost panel, translate it: One characterisation supports unlimited termination combinations, which is the entire economic argument for two-port modelling. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 5: Two-Port Networks. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 17, pp. 708-720. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 52
Putting it together: a fully terminated two-port - worked example
One concrete case, carried all the way to a stated number.
VTU BEC303 | Module 5
Putting it together: a fully terminat…
52
GIVEN
z = [[30, 20], [20, 30]] Ω, Z_S = 10 Ω, Z_L = 50 Ω, driven by 1 V.
1. Z_in = 30 − 400/80 = 25 Ω
2. Z_out = 30 − 400/40 = 20 Ω
3. A_v = z₂₁Z_L/(z₁₁(z₂₂+Z_L) − z₁₂z₂₁) = 20 × 50/(30 × 80 − 400) = 1000/2000 = 0.5
4. Matched output would require Z_L = 20 Ω rather than 50 Ω
RESULT
Z_in = 25 Ω, Z_out = 20 Ω and a voltage gain of 0.5 — and the 50 Ω load is mismatched, so output power is below the achievable maximum.
Z_in = z₁₁ − z₁₂z₂₁/(z₂₂+Z_L) = 25 Ω
Z_out = z₂₂ − z₁₂z₂₁/(z₁₁+Z_S) = 20 Ω
A_v = z₂₁Z_L/(z₁₁(z₂₂+Z_L) − z₁₂z₂₁) = 0.5
THE MISTAKE STUDENTS MAKE
Students compute a voltage gain from the parameters alone and quote it as the gain of the stage. Gain depends on the terminations; the same two-port shows a different gain into every different load, which is why a datasheet always specifies the test conditions.
Source: Engineering Circuit Analysis, 8th ed., Ch. 17, pp. 708-720 | CO5 | Bloom L5
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is z = [[30, 20], [20, 30]] Ω, Z_S = 10 Ω, Z_L = 50 Ω, driven by 1 V. Work at the pace of the slowest note-taker and land hard on the result: Z_in = 25 Ω, Z_out = 20 Ω and a voltage gain of 0.5 — and the 50 Ω load is mismatched, so output power is below the achievable ma… Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 5: Two-Port Networks. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 17, pp. 708-720. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 53
One sentence per unit, six months from now
Units 1-7: what survives after the detail has gone.
VTU BEC303 | Module 5
Revision
53
01 A one-port is one number as a function of s — and only if the port condition actually holds.
02 Four numbers describe any linear two-port at a given frequency, no matter how many parts are inside.
03 y parameters are the short-circuit set — and short-circuit tests are easy at low frequency and awkward at high frequency.
04 Three admittances reproduce any reciprocal two-port exactly — and a fourth element, a dependent source, is needed the moment it is not reciprocal.
05 z parameters are the open-circuit set and map onto a T; y parameters are the short-circuit set and map onto a π.
06 z and y are matrix inverses, and when the inverse does not exist that parameter set simply does not describe the network.
07 h parameters exist because transistors are current-in, voltage-out devices — the mixed units follow from the physics, not from taste.
Notes: What to say: Slow right down here. Read each takeaway aloud and then stop talking for a beat, because these are the sentences that should still be in their heads when they sit the SEE. Tell them explicitly that if they can reconstruct the reasoning behind any one of these lines they understand that unit, and if they can only recite it they do not. Pause cue: Pause for three seconds after each takeaway before moving to the next. Pointing cue: Point at each numbered takeaway in turn as you read it. Question to ask students: Ask: choose the takeaway you trust least and tell me what you would have to check to believe it. Animation instructions: Takeaway rows reveal one at a time from the top, each row highlighting briefly as it appears. Transition style: Fade [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 5: Two-Port Networks, 14 hours, Hayt 8e Ch. 17 (17.1–17.6), pp. 687–720. TB1: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012. Revision consolidates all 16 unit takeaways. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 54
Revision, continued
Units 8-14: what survives after the detail has gone.
VTU BEC303 | Module 5
Revision
54
08 Choose the parameter set by the question — existence, ease of measurement, or what operation you are about to perform.
09 ABCD looks backwards — input written in terms of output — and that is exactly what makes cascading into matrix multiplication.
10 ABCD multiplication handles inter-stage loading automatically — which is exactly what naive transfer-function cascading gets wrong.
11 Reciprocity is about swapping source and meter; symmetry is about swapping the ports themselves — and they are not the same claim.
12 The load reflects back through the network and changes the input impedance — Z_in is never a property of the two-port alone.
13 Z_out is Z_in's mirror image with the source replacing the load — and it is the Thévenin impedance a real load will meet.
14 Shorts and opens are idealisations; how badly they fail sets which parameter set you can actually measure at a given frequency.
Notes: What to say: Slow right down here. Read each takeaway aloud and then stop talking for a beat, because these are the sentences that should still be in their heads when they sit the SEE. Tell them explicitly that if they can reconstruct the reasoning behind any one of these lines they understand that unit, and if they can only recite it they do not. Pause cue: Pause for three seconds after each takeaway before moving to the next. Pointing cue: Point at each numbered takeaway in turn as you read it. Question to ask students: Ask: choose the takeaway you trust least and tell me what you would have to check to believe it. Animation instructions: Takeaway rows reveal one at a time from the top, each row highlighting briefly as it appears. Transition style: Fade [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 5: Two-Port Networks, 14 hours, Hayt 8e Ch. 17 (17.1–17.6), pp. 687–720. TB1: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012. Revision consolidates all 16 unit takeaways. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 55
Revision, continued
Units 15-16: what survives after the detail has gone.
VTU BEC303 | Module 5
Revision
55
15 Every conversion divides by something, so check what that something is before converting — a zero there means the target set does not exist.
16 Four parameters plus two terminations give every performance figure — that is the whole return on the two-port abstraction.
Notes: What to say: Slow right down here. Read each takeaway aloud and then stop talking for a beat, because these are the sentences that should still be in their heads when they sit the SEE. Tell them explicitly that if they can reconstruct the reasoning behind any one of these lines they understand that unit, and if they can only recite it they do not. Pause cue: Pause for three seconds after each takeaway before moving to the next. Pointing cue: Point at each numbered takeaway in turn as you read it. Question to ask students: Ask: choose the takeaway you trust least and tell me what you would have to check to believe it. Animation instructions: Takeaway rows reveal one at a time from the top, each row highlighting briefly as it appears. Transition style: Fade [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 5: Two-Port Networks, 14 hours, Hayt 8e Ch. 17 (17.1–17.6), pp. 687–720. TB1: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012. Revision consolidates all 16 unit takeaways. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 56
How this module is assessed
Where the quiz and the assignment live, and what they test.
VTU BEC303 | Module 5
Assessment
56
MODULE 5 QUIZ
quizzes/Module_5_Quiz.pdf
quizzes/Module_5_Quiz.gift
45 minutes | 50 marks | pass 20 | 1 attempt
Part A: 20 MCQs, 1 mark each.
Part B: 13 descriptive questions, 30 marks.
Bloom spread: L1-L2 18%, L3-L4 67%, L5-L6 15%
Every question carries a CO tag, a Bloom level and a chapter reference; distractor feedback names the misconception.
MODULE 5 ASSIGNMENT
assignments/Module_5_Assignment.pdf
Assignment 5 — Characterising and terminating two-port networks
20 marks | 10% of CIE | 10 problems + 3 theory items
Submit as PDF, single file, named <USN>_BEC303_Assignment5.pdf, via LMS upload. 10% per day, nothing after 5 days.
Rubric: Parameter determination and terminations (6); Conversion and existence reasoning (5); Cascading and equivalent circuits (4); Terminated performance and interpretation (5). Attainment: CO5 = 20.
Previous years' question papers for EC are indexed in pyq/PYQ_Index.pdf; the syllabus extract and the topic-to-slide mapping are in syllabus/Syllabus_Mapping.pdf.
Individual submission. Identical submissions score zero for both parties.
Notes: What to say: Close by telling them exactly where the assessment lives and what it tests. Name the two files, say the mark split out loud, and read the Bloom spread so they understand that roughly a quarter of the paper is not recall at all. Then read the integrity line word for word, because ambiguity there costs students more than any technical error in this module. Pause cue: Pause after the Bloom spread and before the integrity statement. Pointing cue: Point at the quiz panel, then the assignment panel, then the integrity line at the bottom. Question to ask students: Ask: which course outcome do you feel least ready on, and which unit would you reread tonight to fix it? Animation instructions: Quiz panel fades in from the left, then the assignment panel from the right, then the pointers strip appears, then the integrity line fades in last. Transition style: Fade [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 5: Two-Port Networks, 14 hours, Hayt 8e Ch. 17 (17.1–17.6), pp. 687–720. TB1: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012. Assessment counts: 20 MCQs, 13 descriptive questions, 13 assignment items. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.