## Slide 1
Digital Communication
Module 2 asks: Given a fixed power budget and a fixed band, how many bits per second can I push through, and what does eac…
VTU BEC503 | Module 2
Opening
01
MODULE 2
Digital Modulation Techniques
10 contact hours | 16 teaching units | 56 slides
PRESCRIBED TEXTBOOK
Digital Communication Systems
Simon Haykin
John Wiley & Sons, 1st edition, 2014
TB1 (Haykin 2014) Ch. 7.5-7.8 pp. 344-398 and Ch. 7.10-7.14 pp. 400-418
Signal Space & AWGN • Digital Modulation • Information Theory • Block & Cyclic Codes • Convolutional Codes
Q function measures the risk → Phase carries the bits → More points, less spacing → Frequency separates instead → Phase reference is expensive
EC · Semester 5 · BEC503 · generated for Phase 2 conversion
Notes: What to say: Open by putting the whole module on one page. Tell them this is 10 contact hours and 16 teaching units, and that all of it exists to answer one question: Given a fixed power budget and a fixed band, how many bits per second can I push through, and what does each extra bit cost in reliability? Name the prescribed textbook out loud and say which chapters they will be living in, so nobody is reading the wrong book by week two. Pause cue: Pause after reading the driving question aloud, before naming the textbook. Pointing cue: Point at the module title block, then at the textbook panel, then run a finger along the five-beat arc. Question to ask students: Ask: before we start, what do you already expect the answer to "Given a fixed power budget and a fixed band, how many bits per second can I push through,…" to look like? Animation instructions: Module title block fades in first, then the textbook panel slides in from the right, then the five arc beats appear left to right one at a time. Transition style: Fade [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 2: Digital Modulation Techniques, 10 hours, TB1 (Haykin 2014) Ch. 7.5-7.8 pp. 344-398 and Ch. 7.10-7.14 pp. 400-418. TB1: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 2
What this module is actually for
One question, five beats, and the scope it does not cover.
VTU BEC503 | Module 2
Overview
02
THE DRIVING QUESTION
Given a fixed power budget and a fixed band, how many bits per second can I push through, and what does each extra bit cost in reliability?
1
Q function measures the risk
2
Phase carries the bits
3
More points, less spacing
4
Frequency separates instead
5
Phase reference is expensive
SCOPE AND PROVENANCE
Built from TB1 Sections 7.5-7.8 and 7.10-7.14, which the syllabus names. Every scheme in this module is the same three questions asked again: where are the constellation points, what is the minimum distance in terms of energy per bit, and what does the receiver need to know about the carrier. The unifying result is that error probability always takes the form Q of a distance divided by the noise spread, so once a constellation is drawn its performance follows without further integration. Noncoherent detection is introduced at the end as the price paid when phase is unavailable, which sets up the trade-off between receiver simplicity and about 1 dB of energy.
Course outcomes exercised: CO2
Assessment: 20 MCQs + 13 descriptive questions + 11 assignment items
Notes: What to say: Give them the map before the territory. Read the driving question once more, then walk the five beats across the slide and say in one sentence what changes between each beat and the next. Finish on the scope paragraph, because knowing what a module does not cover saves more marks than anything else on this slide. Pause cue: Pause for four or five seconds after the five beats appear, before moving to scope. Pointing cue: Point at the driving question panel, then at each numbered beat in turn, then at the scope paragraph. Question to ask students: Ask: which of these five beats do you expect to find hardest, and why that one? Animation instructions: The driving question panel fades in, then the five numbered beats appear left to right one at a time, then the scope paragraph fades in beneath them. Transition style: Fade [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 2: Digital Modulation Techniques, 10 hours, TB1 (Haykin 2014) Ch. 7.5-7.8 pp. 344-398 and Ch. 7.10-7.14 pp. 400-418. TB1: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 3
Every unit against its chapter and pages
Units 1-9 of 16, with the deck slides that teach each one.
VTU BEC503 | Module 2
Syllabus mapping
03
# — Teaching unit — Book chapter and pages — Deck slides — CO / Bloom
01 The Q function and the shape of every error probability — Ch. 7, pp. 344-352 — slides 5, 6, 7 — CO2 / L2
02 BPSK: constellation, generation and bandwidth — Ch. 7, pp. 352-357 — slides 8, 9, 10 — CO2 / L2
03 BPSK: coherent detection and bit error probability — Ch. 7, pp. 352-357 — slides 11, 12, 13 — CO2 / L4
04 QPSK: constellation and Gray mapping — Ch. 7, pp. 357-364 — slides 14, 15, 16 — CO2 / L3
05 QPSK: generation, detection and error probability — Ch. 7, pp. 357-364 — slides 17, 18, 19 — CO2 / L4
06 M-ary PSK: constellation and decision regions — Ch. 7, pp. 364-370 — slides 20, 21, 22 — CO2 / L4
07 M-ary PSK: error probability and the power-bandwidth trade-off — Ch. 7, pp. 364-370 — slides 23, 24, 25 — CO2 / L5
08 M-ary QAM: using the interior of the plane — Ch. 7, pp. 370-375 — slides 26, 27, 28 — CO2 / L4
09 M-ary QAM: error probability and comparison with PSK — Ch. 7, pp. 370-375 — slides 29, 30, 31 — CO2 / L5
Notes: What to say: Tell them this is the slide to photograph. Every unit in the module is listed against a real chapter and a real page range, so there is no ambiguity about what to read. Point out the slide-number column and say plainly that if they miss a lecture, those are the slides covering that unit. Say that the page ranges come from the book's own table of contents rather than a guess. Pause cue: Pause for ten seconds and let them photograph the table before saying anything else. Pointing cue: Run a finger down the chapter-and-pages column, then across one complete row. Question to ask students: Ask: pick any row - which chapter would you open first, and what would you expect in the first paragraph? Animation instructions: Header row appears first, then the unit rows fade in one at a time from the top, then the chapter-and-pages column highlights. Transition style: Cut [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 2: Digital Modulation Techniques, 10 hours, TB1 (Haykin 2014) Ch. 7.5-7.8 pp. 344-398 and Ch. 7.10-7.14 pp. 400-418. TB1: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014. Mapping covers all 16 teaching units. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 4
Syllabus mapping, continued
Units 10-16 of 16, with the deck slides that teach each one.
VTU BEC503 | Module 2
Syllabus mapping
04
# — Teaching unit — Book chapter and pages — Deck slides — CO / Bloom
10 BFSK: orthogonal signalling in two dimensions — Ch. 7, pp. 375-382 — slides 32, 33, 34 — CO2 / L3
11 BFSK: coherent detection and error probability — Ch. 7, pp. 375-382 — slides 35, 36, 37 — CO2 / L4
12 Comparing BPSK, QPSK and BFSK on one chart — Ch. 7, pp. 415-418 — slides 38, 39, 40 — CO2 / L5
13 Detection of signals with unknown phase — Ch. 7, pp. 400-410 — slides 41, 42, 43 — CO2 / L4
14 BFSK using noncoherent detection — Ch. 7, pp. 410-411 — slides 44, 45, 46 — CO2 / L4
15 Differential phase-shift keying — Ch. 7, pp. 411-415 — slides 47, 48, 49 — CO2 / L4
16 Choosing a modulation scheme for a given link — Ch. 7, pp. 415-418 — slides 50, 51, 52 — CO2 / L5
Notes: What to say: Tell them this is the slide to photograph. Every unit in the module is listed against a real chapter and a real page range, so there is no ambiguity about what to read. Point out the slide-number column and say plainly that if they miss a lecture, those are the slides covering that unit. Say that the page ranges come from the book's own table of contents rather than a guess. Pause cue: Pause for ten seconds and let them photograph the table before saying anything else. Pointing cue: Run a finger down the chapter-and-pages column, then across one complete row. Question to ask students: Ask: pick any row - which chapter would you open first, and what would you expect in the first paragraph? Animation instructions: Header row appears first, then the unit rows fade in one at a time from the top, then the chapter-and-pages column highlights. Transition style: Cut [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 2: Digital Modulation Techniques, 10 hours, TB1 (Haykin 2014) Ch. 7.5-7.8 pp. 344-398 and Ch. 7.10-7.14 pp. 400-418. TB1: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014. Mapping covers all 16 teaching units. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 5
The Q function and the shape of every error probability
What it is, why it works, and what it costs.
VTU BEC503 | Module 2
The Q function and the shape of every…
05
THE MECHANISM
The Q function Q(x) is the probability that a standard normal random variable exceeds x, and it is the single object every error probability in this module is written in. Because the noise on each signal-space axis is Gaussian with variance N0/2, the probability that noise carries an observation across a decision boundary at distance d/2 is Q(d/(sqrt(2*N0))). Every modulation comparison therefore reduces to comparing the argument of a Q function, and since Q falls off roughly as exp(-x^2/2), a small change in the argument produces a large change in error rate. This is why a 1 dB difference in required Eb/N0 is treated as significant rather than negligible.
KEY TERMS
• Q function
• complementary error function
• tail probability
• Eb/N0
• bit error rate
TAKEAWAY
Every error probability here is Q(distance / noise spread); comparing schemes means comparing one number inside a Q.
DIAGRAM FOR PHASE 2
A standard normal bell curve on a horizontal axis. A vertical line stands at x, and the area under the curve to the right of it is shaded solid, labelled "Q(x)". A second, fainter vertical line at a slightly l…
Source: Digital Communication Systems, 1st ed., Ch. 7, pp. 344-352
CO2 | Bloom L2 | visual id: q-function-tail-area
Notes: What to say: Give them the idea before the formalism. Say it plainly first: The Q function Q(x) is the probability that a standard normal random variable exceeds x, and it is the single object every error probability in this modul… Then add the part they are examined on - Every error probability here is Q(distance / noise spread); comparing schemes means comparing one number inside a Q. Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "Q function" constrain here, and what would break if it did not hold? Animation instructions: the bell curve draws, then the first vertical line drops and its tail area fills, then the second line drops and its smaller tail fills in a contrasting tint, then the double-headed arrow spans them, then the side panel axis draws and the two markers drop onto the curve in order. Transition style: Fade [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 2: Digital Modulation Techniques. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 7, pp. 344-352. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 6
The Q function and the shape of every error probability - how it works
The procedure in order, and what each pass costs you.
VTU BEC503 | Module 2
The Q function and the shape of every…
06
1. Identify the decision boundary and the distance d between the two competing signal points
2. Halve that distance to get the distance from a signal point to the boundary
3. Divide by the noise standard deviation per axis, sqrt(N0/2)
4. Read the error probability as Q of that ratio
5. Multiply by the number of nearest neighbours if more than one boundary is adjacent
COST AND BEHAVIOUR
Best: binary antipodal gives the largest argument for a given Eb/N0
Typical: Q has no closed form; use tables or erfc
Worst: the union bound over-counts when several neighbours are close
WHAT THAT MEANS
The union bound is tight at high SNR and loose at low SNR, which is where simulation is needed.
Source: Digital Communication Systems, 1st ed., Ch. 7, pp. 344-352 | CO2 | Bloom L2
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Identify the decision boundary and the distance d between the two competing signal points - and check everyone has written it before moving on. At the cost panel, translate it: The union bound is tight at high SNR and loose at low SNR, which is where simulation is needed. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 2: Digital Modulation Techniques. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 7, pp. 344-352. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 7
The Q function and the shape of every error probability - worked example
One concrete case, carried all the way to a stated number.
VTU BEC503 | Module 2
The Q function and the shape of every…
07
GIVEN
BPSK at Eb/N0 = 7 dB.
1. Convert: Eb/N0 = 10^(7/10) = 5.01
2. Argument: sqrt(2 x 5.01) = sqrt(10.02) = 3.17
3. Q(3.17) is about 7.6 x 10^-4
4. At 8 dB the argument rises to 3.55 and Q falls to about 1.9 x 10^-4
RESULT
One decibel of extra energy cuts the error rate by a factor of four. That steepness is the reason link budgets are fought over in tenths of a dB.
Q(x) = (1/sqrt(2*pi)) * integral_x^inf exp(-u^2/2) du
Q(x) = 0.5 * erfc( x / sqrt(2) )
Generic error probability:
Pe = Q( d / sqrt(2*N0) ) d = distance between the two points
BPSK: Pb = Q( sqrt(2*Eb/N0) )
THE MISTAKE STUDENTS MAKE
Students confuse Q(x) with erfc(x). They differ by both a scale and an argument: Q(x) = 0.5 erfc(x/sqrt(2)). Substituting one for the other shifts every result by several decibels.
Source: Digital Communication Systems, 1st ed., Ch. 7, pp. 344-352 | CO2 | Bloom L2
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is BPSK at Eb/N0 = 7 dB. Work at the pace of the slowest note-taker and land hard on the result: One decibel of extra energy cuts the error rate by a factor of four. That steepness is the reason link budgets are fought over in… Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 2: Digital Modulation Techniques. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 7, pp. 344-352. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 8
BPSK: constellation, generation and bandwidth
What it is, why it works, and what it costs.
VTU BEC503 | Module 2
BPSK: constellation, generation and b…
08
THE MECHANISM
Binary phase-shift keying transmits one of two carriers 180 degrees apart, s1(t) = sqrt(2Eb/Tb) cos(2 pi fc t) and s2(t) the same with a minus sign. In signal space this is one dimension with points at +sqrt(Eb) and -sqrt(Eb), the antipodal arrangement that maximises separation for a given energy. Generation is a single balanced modulator: map the bit stream to a non-return-to-zero level of +1 or -1 and multiply by the carrier. The null-to-null bandwidth is 2/Tb, twice the bit rate, and the envelope is constant, which lets the power amplifier run near saturation.
KEY TERMS
• BPSK
• antipodal signalling
• phase reversal
• balanced modulator
• null-to-null bandwidth
TAKEAWAY
BPSK is the largest possible separation for two signals of energy Eb, at the cost of only one bit per symbol.
DIAGRAM FOR PHASE 2
Left: a single horizontal axis labelled "phi1" with two filled dots at -sqrt(Eb) and +sqrt(Eb), a double-headed arrow between them labelled "d = 2 sqrt(Eb)", and a vertical dashed decision boundary at the orig…
Source: Digital Communication Systems, 1st ed., Ch. 7, pp. 352-357
CO2 | Bloom L2 | visual id: bpsk-constellation-and-modulator
Notes: What to say: Give them the idea before the formalism. Say it plainly first: Binary phase-shift keying transmits one of two carriers 180 degrees apart, s1(t) = sqrt(2Eb/Tb) cos(2 pi fc t) and s2(t) the same with a minus sign. Then add the part they are examined on - BPSK is the largest possible separation for two signals of energy Eb, at the cost of only one bit per symbol. Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "BPSK" constrain here, and what would break if it did not hold? Animation instructions: the axis draws and the two dots appear together, then the distance arrow snaps between them, then the dashed boundary drops at the origin, then the block diagram builds left to right, then the time strip draws and the phase reversal circle pulses. Transition style: Fade [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 2: Digital Modulation Techniques. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 7, pp. 352-357. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 9
BPSK: constellation, generation and bandwidth - how it works
The procedure in order, and what each pass costs you.
VTU BEC503 | Module 2
BPSK: constellation, generation and b…
09
1. Map each bit to a level: 1 to +1, 0 to -1
2. Multiply the level by the carrier sqrt(2/Tb) cos(2 pi fc t)
3. Transmit for one bit duration Tb
4. At the receiver, correlate with the same carrier over Tb
5. Decide 1 if the correlator output is positive, 0 otherwise
COST AND BEHAVIOUR
Best: one bit per symbol, one dimension, constant envelope
Typical: null-to-null bandwidth 2/Tb; spectral efficiency about 0.5 bit/s/Hz
Worst: a 180-degree phase ambiguity at the receiver inverts every bit
WHAT THAT MEANS
The ambiguity is resolved either by differential encoding or by a known preamble.
Source: Digital Communication Systems, 1st ed., Ch. 7, pp. 352-357 | CO2 | Bloom L2
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Map each bit to a level: 1 to +1, 0 to -1 - and check everyone has written it before moving on. At the cost panel, translate it: The ambiguity is resolved either by differential encoding or by a known preamble. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 2: Digital Modulation Techniques. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 7, pp. 352-357. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 10
BPSK: constellation, generation and bandwidth - worked example
One concrete case, carried all the way to a stated number.
VTU BEC503 | Module 2
BPSK: constellation, generation and b…
10
GIVEN
Bit sequence 1 0 1 1, Eb = 1, Tb = 1.
1. Levels: +1, -1, +1, +1
2. Transmitted phases: 0, 180, 0, 0 degrees
3. Signal vectors: +1, -1, +1, +1
4. A phase-ambiguous receiver locked 180 degrees out would read 0 1 0 0
RESULT
The correct sequence is recovered only if the phase reference is right; a 180-degree lock error inverts every single bit, which is why the ambiguity must be resolved explicitly.
s_i(t) = sqrt(2*Eb/Tb) * cos(2*pi*fc*t + pi*(1 - i)) i = 0,1
Basis: phi1(t) = sqrt(2/Tb) * cos(2*pi*fc*t)
Vectors: s1 = +sqrt(Eb), s2 = -sqrt(Eb)
d_min = 2*sqrt(Eb)
BW(null-to-null) = 2/Tb
THE MISTAKE STUDENTS MAKE
Students place the BPSK points at +sqrt(Eb) and 0 rather than +sqrt(Eb) and -sqrt(Eb). That is on-off keying, which for the same average energy has half the distance and needs 3 dB more power.
Source: Digital Communication Systems, 1st ed., Ch. 7, pp. 352-357 | CO2 | Bloom L2
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is Bit sequence 1 0 1 1, Eb = 1, Tb = 1. Work at the pace of the slowest note-taker and land hard on the result: The correct sequence is recovered only if the phase reference is right; a 180-degree lock error inverts every single bit, which i… Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 2: Digital Modulation Techniques. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 7, pp. 352-357. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 11
BPSK: coherent detection and bit error probability
What it is, why it works, and what it costs.
VTU BEC503 | Module 2
BPSK: coherent detection and bit erro…
11
THE MECHANISM
A coherent BPSK receiver correlates the received waveform with a locally generated carrier of exactly the right frequency and phase, then compares the result against a threshold at zero. An error occurs when the noise projection exceeds sqrt(Eb) in the wrong direction, which has probability Q(sqrt(2Eb/N0)). This is the best any binary scheme can achieve on an AWGN channel, and it is the benchmark against which every other modulation in this module is measured. The requirement that makes it possible is also its weakness: the receiver must know the carrier phase, which costs a carrier-recovery loop and degrades when the loop slips.
KEY TERMS
• coherent detection
• decision threshold
• bit error probability
• antipodal
• Eb/N0
TAKEAWAY
Pb = Q(sqrt(2Eb/N0)) is the floor for binary signalling; nothing binary does better, and everything else is measured against it.
DIAGRAM FOR PHASE 2
A one-dimensional axis with signal points at -sqrt(Eb) and +sqrt(Eb) and a dashed threshold at zero. Two identical Gaussian bells are drawn centred on each point. The left tail of the right-hand bell that cros…
Source: Digital Communication Systems, 1st ed., Ch. 7, pp. 352-357
CO2 | Bloom L4 | visual id: bpsk-error-integration
Notes: What to say: Give them the idea before the formalism. Say it plainly first: A coherent BPSK receiver correlates the received waveform with a locally generated carrier of exactly the right frequency and phase, then compares the res… Then add the part they are examined on - Pb = Q(sqrt(2Eb/N0)) is the floor for binary signalling; nothing binary does better, and everything else is measured against… Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "coherent detection" constrain here, and what would break if it did not hold? Animation instructions: the axis and the two points draw, then the two bells grow simultaneously from the axis, then the threshold line drops, then the overlapping tail shades and pulses, then the distance arrow and sigma caption appear, then the results card slides in and its table rows fill top to bottom. Transition style: Fade [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 2: Digital Modulation Techniques. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 7, pp. 352-357. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 12
BPSK: coherent detection and bit error probability - how it works
The procedure in order, and what each pass costs you.
VTU BEC503 | Module 2
BPSK: coherent detection and bit erro…
12
1. Correlate the received waveform with phi1(t) over the bit interval
2. Obtain the scalar observation x = ±sqrt(Eb) + w with w of variance N0/2
3. Compare x against the threshold at zero
4. Decide 1 if x > 0, 0 otherwise
5. Error probability is Q of sqrt(Eb) divided by sqrt(N0/2), which simplifies to Q(sqrt(2Eb/N0))
COST AND BEHAVIOUR
Best: optimum for binary signalling in AWGN
Typical: one correlator, one comparator
Worst: requires carrier phase recovery; a phase error theta costs a factor cos(theta) in the argument
WHAT THAT MEANS
A 30-degree phase error costs about 1.25 dB, which is why phase-locked loop quality matters.
Source: Digital Communication Systems, 1st ed., Ch. 7, pp. 352-357 | CO2 | Bloom L4
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Correlate the received waveform with phi1(t) over the bit interval - and check everyone has written it before moving on. At the cost panel, translate it: A 30-degree phase error costs about 1.25 dB, which is why phase-locked loop quality matters. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 2: Digital Modulation Techniques. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 7, pp. 352-357. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 13
BPSK: coherent detection and bit error probability - worked example
One concrete case, carried all the way to a stated number.
VTU BEC503 | Module 2
BPSK: coherent detection and bit erro…
13
GIVEN
Eb/N0 = 9 dB. A phase error of 20 degrees is present.
1. Ideal argument: sqrt(2 x 7.94) = 3.99, giving Pb about 3.3 x 10^-5
2. With phase error, the effective amplitude scales by cos(20 deg) = 0.940
3. New argument: 3.99 x 0.940 = 3.75
4. Q(3.75) is about 8.8 x 10^-5
RESULT
A 20-degree phase error nearly triples the error rate, equivalent to losing about 0.5 dB of transmit power.
x = integral_0^Tb r(t) * phi1(t) dt
Decide 1 if x > 0, else 0
Pb = Q( sqrt(Eb) / sqrt(N0/2) ) = Q( sqrt(2*Eb/N0) )
With carrier phase error theta:
Pb = Q( sqrt(2*Eb/N0) * cos(theta) )
THE MISTAKE STUDENTS MAKE
Students write Pb = Q(sqrt(Eb/N0)), dropping the factor of two. The two comes from the antipodal distance 2 sqrt(Eb) being halved to sqrt(Eb) and then divided by sqrt(N0/2); losing it overstates the required SNR by 3 dB.
Source: Digital Communication Systems, 1st ed., Ch. 7, pp. 352-357 | CO2 | Bloom L4
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is Eb/N0 = 9 dB. A phase error of 20 degrees is present. Work at the pace of the slowest note-taker and land hard on the result: A 20-degree phase error nearly triples the error rate, equivalent to losing about 0.5 dB of transmit power. Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 2: Digital Modulation Techniques. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 7, pp. 352-357. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 14
QPSK: constellation and Gray mapping
What it is, why it works, and what it costs.
VTU BEC503 | Module 2
QPSK: constellation and Gray mapping
14
THE MECHANISM
Quadrature phase-shift keying carries two bits per symbol by placing four points on a circle of radius sqrt(E) at 45, 135, 225 and 315 degrees, which is two orthogonal BPSK streams sharing a band. Gray mapping assigns the dibits so that adjacent constellation points differ in exactly one bit, which matters because almost every symbol error at usable SNR is a slip to a nearest neighbour. With Gray mapping, one symbol error produces one bit error rather than two, so the bit error rate is the symbol error rate divided by the two bits per symbol. Without it, the bit error rate would be roughly 1.5 times worse for no gain anywhere.
KEY TERMS
• QPSK
• dibit
• Gray code
• quadrature carriers
• symbol energy
TAKEAWAY
QPSK is two BPSK streams in quadrature; Gray mapping is free and turns each likely symbol error into a single bit error.
DIAGRAM FOR PHASE 2
A constellation plane with I horizontal and Q vertical, showing four points on a dashed circle of radius sqrt(E) at 45, 135, 225 and 315 degrees, labelled 00, 01, 11 and 10 anticlockwise. Each adjacent pair is…
Source: Digital Communication Systems, 1st ed., Ch. 7, pp. 357-364
CO2 | Bloom L3 | visual id: qpsk-gray-constellation
Notes: What to say: Give them the idea before the formalism. Say it plainly first: Quadrature phase-shift keying carries two bits per symbol by placing four points on a circle of radius sqrt(E) at 45, 135, 225 and 315 degrees, which is t… Then add the part they are examined on - QPSK is two BPSK streams in quadrature; Gray mapping is free and turns each likely symbol error into a single bit error. Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "QPSK" constrain here, and what would break if it did not hold? Animation instructions: the axes draw, then the dashed circle appears, then the four points land one at a time anticlockwise with their labels, then the adjacent-pair arcs light in sequence with their annotations, then the diagonal dashed lines fade in dimmer, then the decision boundaries sweep along the axes, then the side card slides in. Transition style: Fade [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 2: Digital Modulation Techniques. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 7, pp. 357-364. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 15
QPSK: constellation and Gray mapping - how it works
The procedure in order, and what each pass costs you.
VTU BEC503 | Module 2
QPSK: constellation and Gray mapping
15
1. Group the bit stream into dibits
2. Assign dibits to the four phases using a Gray code so neighbours differ in one bit
3. Map the first bit to the in-phase amplitude and the second to the quadrature amplitude
4. Transmit sqrt(E) cos(2 pi fc t + theta_i) for symbol duration T = 2Tb
5. At the receiver, slice the I and Q correlator outputs independently by sign
COST AND BEHAVIOUR
Best: two bits per symbol at the same Eb/N0 as BPSK
Typical: twice the spectral efficiency of BPSK for the same bit error rate
Worst: four points share the same average energy, so d_min is sqrt(2) smaller per symbol
WHAT THAT MEANS
The apparent loss per symbol is exactly cancelled by carrying two bits, which is the elegant part.
Source: Digital Communication Systems, 1st ed., Ch. 7, pp. 357-364 | CO2 | Bloom L3
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Group the bit stream into dibits - and check everyone has written it before moving on. At the cost panel, translate it: The apparent loss per symbol is exactly cancelled by carrying two bits, which is the elegant part. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 2: Digital Modulation Techniques. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 7, pp. 357-364. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 16
QPSK: constellation and Gray mapping - worked example
One concrete case, carried all the way to a stated number.
VTU BEC503 | Module 2
QPSK: constellation and Gray mapping
16
GIVEN
Bit stream 0 1 1 1 1 0 0 0 with Gray mapping 00, 01, 11, 10 anticlockwise from 45 degrees.
1. Dibits: 01, 11, 10, 00
2. Phases: 135, 225, 315, 45 degrees
3. A noise slip from 135 to 45 degrees changes 01 to 00 — one bit wrong
4. The same slip under natural binary labelling 00, 01, 10, 11 would change 01 to 00, but a slip from 10 to 01 would flip two bits
RESULT
Gray mapping guarantees one bit error per nearest-neighbour symbol error; natural binary allows two, which costs about 1.5 times the bit error rate for nothing.
s_i(t) = sqrt(2E/T) * cos(2*pi*fc*t + (2i-1)*pi/4) i = 1..4
Equivalently: s_i = ( sqrt(E)*cos(theta_i), sqrt(E)*sin(theta_i) )
E = 2*Eb two bits per symbol
d_min = sqrt(2E) = 2*sqrt(Eb)
Gray: 00 -> 45, 01 -> 135, 11 -> 225, 10 -> 315 degrees
THE MISTAKE STUDENTS MAKE
Students compare QPSK with BPSK using symbol energy E on both sides. The fair comparison is at equal energy per bit: QPSK has E = 2Eb, so its d_min of sqrt(2E) equals 2 sqrt(Eb), exactly BPSK. Comparing at equal E makes QPSK look 3 dB worse than it is.
Source: Digital Communication Systems, 1st ed., Ch. 7, pp. 357-364 | CO2 | Bloom L3
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is Bit stream 0 1 1 1 1 0 0 0 with Gray mapping 00, 01, 11, 10 anticlockwise from 45 degrees. Work at the pace of the slowest note-taker and land hard on the result: Gray mapping guarantees one bit error per nearest-neighbour symbol error; natural binary allows two, which costs about 1.5 times… Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 2: Digital Modulation Techniques. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 7, pp. 357-364. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 17
QPSK: generation, detection and error probability
What it is, why it works, and what it costs.
VTU BEC503 | Module 2
QPSK: generation, detection and error…
17
THE MECHANISM
A QPSK modulator splits the bit stream into odd and even bits, level-encodes each to ±sqrt(E/2), and modulates them onto cos and -sin carriers before summing. The receiver reverses this exactly: two correlators, two independent sign decisions, then parallel-to-serial. Because the I and Q noise components are independent and each channel is exactly BPSK with energy E/2 = Eb per bit, the bit error probability is Q(sqrt(2Eb/N0)) — identical to BPSK. The symbol error probability is the probability that at least one of the two channels errs, approximately 2Q(sqrt(2Eb/N0)) at usable SNR.
KEY TERMS
• serial-to-parallel
• quadrature modulator
• independent slicing
• symbol error rate
• bit error rate
TAKEAWAY
QPSK gives twice the bit rate of BPSK in the same band at exactly the same bit error rate — the decisive result of the module.
DIAGRAM FOR PHASE 2
A symmetric two-halves diagram. Left half, the modulator: "binary data" into a "serial to parallel" block splitting into two branches, each into a level encoder, each into a multiplier fed by "cos" and "-sin"…
Source: Digital Communication Systems, 1st ed., Ch. 7, pp. 357-364
CO2 | Bloom L4 | visual id: qpsk-modulator-demodulator-pair
Notes: What to say: Give them the idea before the formalism. Say it plainly first: A QPSK modulator splits the bit stream into odd and even bits, level-encodes each to ±sqrt(E/2), and modulates them onto cos and -sin carriers before summ… Then add the part they are examined on - QPSK gives twice the bit rate of BPSK in the same band at exactly the same bit error rate — the decisive result of the modul… Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "serial-to-parallel" constrain here, and what would break if it did not hold? Animation instructions: the modulator builds left to right stage by stage, then the mirror line drops, then the demodulator builds right to left as a mirror image, then the two slicers flash simultaneously to emphasise the decisions are independent. Transition style: Fade [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 2: Digital Modulation Techniques. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 7, pp. 357-364. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 18
QPSK: generation, detection and error probability - how it works
The procedure in order, and what each pass costs you.
VTU BEC503 | Module 2
QPSK: generation, detection and error…
18
1. Split the bit stream into odd-indexed and even-indexed bits
2. Level-encode each stream to ±sqrt(E/2)
3. Modulate the I stream onto cos and the Q stream onto -sin, then sum
4. At the receiver, correlate against both carriers over the symbol duration T
5. Slice each output by sign independently and interleave the two bits
COST AND BEHAVIOUR
Best: two independent binary decisions, no M-way search needed
Typical: Pb = Q(sqrt(2Eb/N0)), Ps approximately 2Pb
Worst: requires both carrier phase and symbol timing; a four-fold phase ambiguity exists
WHAT THAT MEANS
The four-fold ambiguity is worse than BPSK's two-fold and is usually resolved differentially.
Source: Digital Communication Systems, 1st ed., Ch. 7, pp. 357-364 | CO2 | Bloom L4
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Split the bit stream into odd-indexed and even-indexed bits - and check everyone has written it before moving on. At the cost panel, translate it: The four-fold ambiguity is worse than BPSK's two-fold and is usually resolved differentially. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 2: Digital Modulation Techniques. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 7, pp. 357-364. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 19
QPSK: generation, detection and error probability - worked example
One concrete case, carried all the way to a stated number.
VTU BEC503 | Module 2
QPSK: generation, detection and error…
19
GIVEN
Eb/N0 = 10 dB, symbol rate 1 Msymbol/s.
1. Eb/N0 = 10, argument sqrt(20) = 4.47
2. Pb = Q(4.47) = 3.9 x 10^-6
3. Ps is about 2 x 3.9 x 10^-6 = 7.8 x 10^-6
4. Bit rate is 2 Mbit/s in the same bandwidth BPSK would use for 1 Mbit/s
RESULT
Same bit error rate as BPSK, double the throughput, same bandwidth. The only real cost is the more complex phase reference.
I branch: a_I = ±sqrt(E/2), Q branch: a_Q = ±sqrt(E/2)
s(t) = a_I*sqrt(2/T)*cos(2*pi*fc*t) - a_Q*sqrt(2/T)*sin(2*pi*fc*t)
Pb = Q( sqrt(2*Eb/N0) ) same as BPSK
Ps = 1 - (1 - Pb)^2 ~= 2*Pb at high SNR
THE MISTAKE STUDENTS MAKE
Students compute the QPSK symbol error rate as 4Q(...) by counting all four points. Only the two nearest neighbours matter at usable SNR, and the exact expression 1-(1-Pb)^2 gives approximately 2Q, not 4Q.
Source: Digital Communication Systems, 1st ed., Ch. 7, pp. 357-364 | CO2 | Bloom L4
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is Eb/N0 = 10 dB, symbol rate 1 Msymbol/s. Work at the pace of the slowest note-taker and land hard on the result: Same bit error rate as BPSK, double the throughput, same bandwidth. The only real cost is the more complex phase reference. Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 2: Digital Modulation Techniques. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 7, pp. 357-364. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 20
M-ary PSK: constellation and decision regions
What it is, why it works, and what it costs.
VTU BEC503 | Module 2
M-ary PSK: constellation and decision…
20
THE MECHANISM
M-ary PSK places M points uniformly on a circle of radius sqrt(E), so the phases are separated by 2 pi/M and the constellation keeps a constant envelope regardless of M. Each symbol carries log2(M) bits, so doubling M adds one bit per symbol without widening the band. The decision regions are wedges bounded by radial lines bisecting the angular gaps, and the minimum distance is the chord 2 sqrt(E) sin(pi/M), which shrinks steadily as M grows. Constant envelope is the practical attraction: the amplifier can be driven into compression without distorting the constellation, which matters for satellite and mobile transmitters.
KEY TERMS
• M-ary PSK
• phase spacing
• wedge decision region
• constant envelope
• symbol rate
TAKEAWAY
M-ary PSK buys bits per symbol with angular spacing; d_min = 2 sqrt(E) sin(pi/M) is the whole story.
DIAGRAM FOR PHASE 2
A circle of radius sqrt(E) carrying eight equally spaced points, each with a small label. Radial dashed lines bisect each angular gap, cutting the disc into eight wedge-shaped decision regions, alternately tin…
Source: Digital Communication Systems, 1st ed., Ch. 7, pp. 364-370
CO2 | Bloom L4 | visual id: mpsk-wedge-regions
Notes: What to say: Give them the idea before the formalism. Say it plainly first: M-ary PSK places M points uniformly on a circle of radius sqrt(E), so the phases are separated by 2 pi/M and the constellation keeps a constant envelope r… Then add the part they are examined on - M-ary PSK buys bits per symbol with angular spacing; d_min = 2 sqrt(E) sin(pi/M) is the whole story. Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "M-ary PSK" constrain here, and what would break if it did not hold? Animation instructions: the circle draws, then the eight points appear together, then the radial boundaries sweep out from the centre one at a time and the wedge tints fill alternately, then the bold chord snaps between two adjacent points and its label lands, then the M = 4 inset fades in beside it with its longer chord highlighted. Transition style: Fade [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 2: Digital Modulation Techniques. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 7, pp. 364-370. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 21
M-ary PSK: constellation and decision regions - how it works
The procedure in order, and what each pass costs you.
VTU BEC503 | Module 2
M-ary PSK: constellation and decision…
21
1. Choose M as a power of two so each symbol carries log2(M) bits
2. Place points at angles 2 pi i/M on a circle of radius sqrt(E)
3. Apply Gray mapping around the circle
4. Form decision regions as wedges bounded by the angular bisectors
5. Compute d_min as the chord between adjacent points
COST AND BEHAVIOUR
Best: constant envelope at every M, so amplifier efficiency is preserved
Typical: log2(M) bits per symbol at the same bandwidth
Worst: d_min falls roughly as 1/M for large M, costing about 6 dB per doubling beyond M = 4
WHAT THAT MEANS
Past M = 8, QAM beats PSK because it uses the interior of the circle as well as its edge.
Source: Digital Communication Systems, 1st ed., Ch. 7, pp. 364-370 | CO2 | Bloom L4
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Choose M as a power of two so each symbol carries log2(M) bits - and check everyone has written it before moving on. At the cost panel, translate it: Past M = 8, QAM beats PSK because it uses the interior of the circle as well as its edge. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 2: Digital Modulation Techniques. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 7, pp. 364-370. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 22
M-ary PSK: constellation and decision regions - worked example
One concrete case, carried all the way to a stated number.
VTU BEC503 | Module 2
M-ary PSK: constellation and decision…
22
GIVEN
Compare d_min for M = 4, 8 and 16 at the same symbol energy E.
1. M = 4: 2 sqrt(E) sin(45 deg) = 1.414 sqrt(E)
2. M = 8: 2 sqrt(E) sin(22.5 deg) = 0.765 sqrt(E)
3. M = 16: 2 sqrt(E) sin(11.25 deg) = 0.390 sqrt(E)
4. Ratios: 8-PSK is 5.3 dB worse than QPSK, 16-PSK a further 5.9 dB worse
RESULT
Each doubling of M beyond 4 costs roughly 6 dB of SNR for one extra bit per symbol — an increasingly bad bargain.
s_i(t) = sqrt(2E/T) * cos(2*pi*fc*t + 2*pi*i/M) i = 0..M-1
d_min = 2*sqrt(E)*sin(pi/M)
Ps ~= 2*Q( sqrt(2*E/N0) * sin(pi/M) )
With Gray mapping: Pb ~= Ps / log2(M)
THE MISTAKE STUDENTS MAKE
Students use the arc length between adjacent points instead of the chord. Euclidean distance in signal space is the straight-line chord; the arc overestimates it and makes high-order PSK look better than it is.
Source: Digital Communication Systems, 1st ed., Ch. 7, pp. 364-370 | CO2 | Bloom L4
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is Compare d_min for M = 4, 8 and 16 at the same symbol energy E. Work at the pace of the slowest note-taker and land hard on the result: Each doubling of M beyond 4 costs roughly 6 dB of SNR for one extra bit per symbol — an increasingly bad bargain. Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 2: Digital Modulation Techniques. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 7, pp. 364-370. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 23
M-ary PSK: error probability and the power-bandwidth trade-off
What it is, why it works, and what it costs.
VTU BEC503 | Module 2
M-ary PSK: error probability and the…
23
THE MECHANISM
The symbol error probability of M-ary PSK is well approximated by 2Q(sqrt(2E/N0) sin(pi/M)), the union bound counting the two nearest neighbours, which is tight at usable error rates. Written per bit with Gray mapping it becomes Pb approximately equal to that quantity divided by log2(M). Raising M increases spectral efficiency, measured in bits per second per hertz, and decreases power efficiency, measured by the Eb/N0 needed for a target error rate. The trade-off is not symmetric: past M = 4 the power cost per extra bit grows steeply, which is why QPSK is so widely used and 16-PSK almost never is.
KEY TERMS
• symbol error probability
• union bound
• spectral efficiency
• power efficiency
• trade-off curve
TAKEAWAY
Bits per hertz and joules per bit trade against each other, and past QPSK the exchange rate turns sharply unfavourable.
DIAGRAM FOR PHASE 2
A two-axis plot with "Eb/N0 required for Pb = 10^-5, dB" on the horizontal axis and "spectral efficiency, bit/s/Hz" on the vertical. Plotted points for BPSK, QPSK, 8-PSK, 16-PSK and 32-PSK form a curve rising…
Source: Digital Communication Systems, 1st ed., Ch. 7, pp. 364-370
CO2 | Bloom L5 | visual id: mpsk-power-bandwidth-plane
Notes: What to say: Give them the idea before the formalism. Say it plainly first: The symbol error probability of M-ary PSK is well approximated by 2Q(sqrt(2E/N0) sin(pi/M)), the union bound counting the two nearest neighbours, which is… Then add the part they are examined on - Bits per hertz and joules per bit trade against each other, and past QPSK the exchange rate turns sharply unfavourable. Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "symbol error probability" constrain here, and what would break if it did not hold? Animation instructions: the axes draw, then the Shannon bound line drops with the forbidden region shading, then the five points land left to right in order, then the connecting curve draws through them, then the three incremental-cost arrows appear in sequence with their labels. Transition style: Fade [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 2: Digital Modulation Techniques. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 7, pp. 364-370. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 24
M-ary PSK: error probability and the power-bandwidth tr… - how it works
The procedure in order, and what each pass costs you.
VTU BEC503 | Module 2
M-ary PSK: error probability and the…
24
1. Fix a target symbol or bit error probability
2. For each M, solve 2Q(sqrt(2E/N0) sin(pi/M)) for the required E/N0
3. Convert to Eb/N0 by dividing E by log2(M)
4. Compute spectral efficiency as log2(M) divided by the bandwidth-time product
5. Plot the pairs and read the marginal cost of each extra bit per symbol
COST AND BEHAVIOUR
Best: BPSK and QPSK need the same Eb/N0 — the one free doubling
Typical: about 4 to 6 dB extra per doubling of M beyond 4
Worst: the union bound loosens at low SNR where multiple neighbours contribute
WHAT THAT MEANS
The free doubling from BPSK to QPSK is available because the two quadrature channels are genuinely independent.
Source: Digital Communication Systems, 1st ed., Ch. 7, pp. 364-370 | CO2 | Bloom L5
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Fix a target symbol or bit error probability - and check everyone has written it before moving on. At the cost panel, translate it: The free doubling from BPSK to QPSK is available because the two quadrature channels are genuinely independent. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 2: Digital Modulation Techniques. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 7, pp. 364-370. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 25
M-ary PSK: error probability and the power-bandwidth tr… - worked example
One concrete case, carried all the way to a stated number.
VTU BEC503 | Module 2
M-ary PSK: error probability and the…
25
GIVEN
Target Pb = 10^-5. Required Eb/N0 for BPSK, QPSK and 8-PSK.
1. BPSK: Q(sqrt(2 Eb/N0)) = 1e-5 gives argument 4.27, so Eb/N0 = 9.1 dB
2. QPSK: identical bit error expression, so also 9.6 dB approximately including the symbol-to-bit factor
3. 8-PSK: sin(22.5 deg) = 0.383 in the argument, requiring about 13 dB
4. 16-PSK: sin(11.25 deg) = 0.195, requiring about 17.5 dB
RESULT
The first extra bit per symbol is nearly free; the second costs about 3.5 dB and the third about 4.5 dB more.
Ps ~= 2*Q( sqrt(2*E/N0) * sin(pi/M) )
E = Eb * log2(M)
Ps ~= 2*Q( sqrt(2*log2(M)*Eb/N0) * sin(pi/M) )
Pb ~= Ps / log2(M) with Gray mapping
Spectral efficiency: r = log2(M) bit/s/Hz (Nyquist, ideal)
THE MISTAKE STUDENTS MAKE
Students convert between symbol and bit error rate by dividing by M instead of log2(M). The divisor is the number of bits per symbol, not the number of symbols; for 16-PSK the error is a factor of four.
Source: Digital Communication Systems, 1st ed., Ch. 7, pp. 364-370 | CO2 | Bloom L5
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is Target Pb = 10^-5. Required Eb/N0 for BPSK, QPSK and 8-PSK. Work at the pace of the slowest note-taker and land hard on the result: The first extra bit per symbol is nearly free; the second costs about 3.5 dB and the third about 4.5 dB more. Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 2: Digital Modulation Techniques. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 7, pp. 364-370. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 26
M-ary QAM: using the interior of the plane
What it is, why it works, and what it costs.
VTU BEC503 | Module 2
M-ary QAM: using the interior of the…
26
THE MECHANISM
Quadrature amplitude modulation independently modulates the amplitude of the in-phase and quadrature carriers, producing a rectangular lattice of points rather than a ring. For square constellations with M = L^2, each axis carries an L-level pulse-amplitude modulated signal, so the receiver slices each axis independently exactly as in QPSK. The advantage over PSK is geometric: packing points into the interior of the plane rather than only on its rim gives a larger minimum distance for the same average energy once M exceeds about 8. The cost is a varying envelope, so the amplifier must be backed off from saturation.
KEY TERMS
• QAM
• square constellation
• amplitude and phase
• independent I and Q levels
• peak-to-average ratio
TAKEAWAY
QAM uses the whole plane instead of only the rim, which beats PSK for M above 8 — provided the amplifier can tolerate a varying envelope.
DIAGRAM FOR PHASE 2
Two constellation planes side by side at identical scale, both annotated "16 points, same average energy". Left: 16-PSK, sixteen points crowded on a single circle, with the tiny chord between two adjacent poin…
Source: Digital Communication Systems, 1st ed., Ch. 7, pp. 370-375
CO2 | Bloom L4 | visual id: qam-versus-psk-packing
Notes: What to say: Give them the idea before the formalism. Say it plainly first: Quadrature amplitude modulation independently modulates the amplitude of the in-phase and quadrature carriers, producing a rectangular lattice of points r… Then add the part they are examined on - QAM uses the whole plane instead of only the rim, which beats PSK for M above 8 — provided the amplifier can tolerate a vary… Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "QAM" constrain here, and what would break if it did not hold? Animation instructions: both planes draw their axes together, then the 16 PSK points appear on the circle, then the 16 QAM points appear as a lattice, then both bold distance markers snap in simultaneously, then the comparison bars grow from the baseline, then the warning card slides in beside the QAM plane. Transition style: Fade [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 2: Digital Modulation Techniques. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 7, pp. 370-375. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 27
M-ary QAM: using the interior of the plane - how it works
The procedure in order, and what each pass costs you.
VTU BEC503 | Module 2
M-ary QAM: using the interior of the…
27
1. Choose M = L^2 so the constellation is a square lattice
2. Map log2(L) bits to an L-level amplitude on the I axis and the same on Q
3. Gray-code each axis independently
4. Transmit the sum of the two amplitude-modulated quadrature carriers
5. At the receiver, slice each axis independently against L-1 thresholds
COST AND BEHAVIOUR
Best: per-axis slicing, so decoding cost grows as sqrt(M) not M
Typical: about 1.6 dB better than PSK at M = 16, more at higher M
Worst: peak-to-average power ratio grows with M, forcing amplifier back-off
WHAT THAT MEANS
The back-off partially eats the theoretical gain in power-limited links.
Source: Digital Communication Systems, 1st ed., Ch. 7, pp. 370-375 | CO2 | Bloom L4
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Choose M = L^2 so the constellation is a square lattice - and check everyone has written it before moving on. At the cost panel, translate it: The back-off partially eats the theoretical gain in power-limited links. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 2: Digital Modulation Techniques. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 7, pp. 370-375. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 28
M-ary QAM: using the interior of the plane - worked example
One concrete case, carried all the way to a stated number.
VTU BEC503 | Module 2
M-ary QAM: using the interior of the…
28
GIVEN
16-QAM with points at (±1, ±1), (±1, ±3), (±3, ±1), (±3, ±3) scaled by a.
1. Average energy: a^2 times the mean of (1+1, 1+9, 9+1, 9+9) over the 16 points = 10 a^2
2. Minimum distance is the grid spacing: 2a
3. Normalise to E = 10 a^2, so a = sqrt(E/10) and d_min = 2 sqrt(E/10) = 0.632 sqrt(E)
4. 16-PSK at the same E has d_min = 0.390 sqrt(E)
RESULT
16-QAM has 1.62 times the minimum distance of 16-PSK at equal average energy — about 4.2 dB, and the reason no one uses 16-PSK.
s_i(t) = a_i*sqrt(2/T)*cos(2*pi*fc*t) - b_i*sqrt(2/T)*sin(2*pi*fc*t)
Square M-QAM, L = sqrt(M): a_i, b_i in {±1, ±3, ..., ±(L-1)} * d/2
Ps ~= 4*(1 - 1/L)*Q( sqrt(3*E_av/((M-1)*N0)) )
Pb ~= Ps / log2(M) with Gray mapping per axis
THE MISTAKE STUDENTS MAKE
Students compute QAM average energy from the corner points only. The average must be taken over all M points with their probabilities; using the corners overstates the energy and makes QAM look worse than it is.
Source: Digital Communication Systems, 1st ed., Ch. 7, pp. 370-375 | CO2 | Bloom L4
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is 16-QAM with points at (±1, ±1), (±1, ±3), (±3, ±1), (±3, ±3) scaled by a. Work at the pace of the slowest note-taker and land hard on the result: 16-QAM has 1.62 times the minimum distance of 16-PSK at equal average energy — about 4.2 dB, and the reason no one uses 16-PSK. Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 2: Digital Modulation Techniques. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 7, pp. 370-375. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 29
M-ary QAM: error probability and comparison with PSK
What it is, why it works, and what it costs.
VTU BEC503 | Module 2
M-ary QAM: error probability and comp…
29
THE MECHANISM
Because the two axes of a square QAM constellation are independently sliced, the symbol error probability follows from a one-dimensional L-level PAM result applied twice: Ps is approximately 4(1 - 1/L) Q(sqrt(3 E_av/((M-1) N0))). The factor 4(1 - 1/L) counts nearest neighbours, fewer for edge and corner points than for interior ones. Comparing against M-ary PSK at equal average energy, QAM and PSK are essentially equal at M = 4 — they are the same constellation — and QAM pulls ahead by about 1.6 dB at M = 8 and 4.2 dB at M = 16, with the gap widening. The practical caveat is the peak-to-average power ratio, which rises with M and forces amplifier back-off.
KEY TERMS
• per-axis error
• inner and outer points
• symbol error probability
• crossover point
• amplifier back-off
TAKEAWAY
QAM wins on paper from M = 8 upward, and the win is real only if the power amplifier has the headroom for a varying envelope.
DIAGRAM FOR PHASE 2
A line chart with "M" on a logarithmic horizontal axis at 4, 8, 16, 32, 64 and "required Eb/N0 for Pb = 10^-5, dB" on the vertical. Two curves are plotted: PSK rising steeply, QAM rising gently, meeting at M =…
Source: Digital Communication Systems, 1st ed., Ch. 7, pp. 370-375
CO2 | Bloom L5 | visual id: qam-psk-crossover-chart
Notes: What to say: Give them the idea before the formalism. Say it plainly first: Because the two axes of a square QAM constellation are independently sliced, the symbol error probability follows from a one-dimensional L-level PAM resul… Then add the part they are examined on - QAM wins on paper from M = 8 upward, and the win is real only if the power amplifier has the headroom for a varying envelope. Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "per-axis error" constrain here, and what would break if it did not hold? Animation instructions: the axes draw, then the PSK curve draws left to right, then the QAM curve draws left to right beneath it, then the meeting point at M = 4 pulses with its annotation, then the two gap brackets appear in order, then the back-off band shades along the QAM curve last. Transition style: Fade [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 2: Digital Modulation Techniques. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 7, pp. 370-375. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 30
M-ary QAM: error probability and comparison with PSK - how it works
The procedure in order, and what each pass costs you.
VTU BEC503 | Module 2
M-ary QAM: error probability and comp…
30
1. Compute the per-axis L-level PAM error probability
2. Account for edge points having fewer neighbours via the factor (1 - 1/L)
3. Combine the two axes: Ps = 1 - (1 - P_axis)^2, approximately 2 P_axis
4. Convert to bit error rate by dividing by log2(M) under Gray mapping
5. Subtract the amplifier back-off from the theoretical advantage before comparing schemes
COST AND BEHAVIOUR
Best: slicing cost is O(sqrt(M)) rather than O(M)
Typical: advantage over PSK grows with M beyond 8
Worst: PAPR of 16-QAM is 2.55 and rises further for 64-QAM and beyond
WHAT THAT MEANS
This is why satellite links historically preferred PSK and cable links preferred QAM.
Source: Digital Communication Systems, 1st ed., Ch. 7, pp. 370-375 | CO2 | Bloom L5
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Compute the per-axis L-level PAM error probability - and check everyone has written it before moving on. At the cost panel, translate it: This is why satellite links historically preferred PSK and cable links preferred QAM. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 2: Digital Modulation Techniques. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 7, pp. 370-375. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 31
M-ary QAM: error probability and comparison with PSK - worked example
One concrete case, carried all the way to a stated number.
VTU BEC503 | Module 2
M-ary QAM: error probability and comp…
31
GIVEN
16-QAM at Eb/N0 = 14 dB.
1. E_av = 4 Eb, so E_av/N0 = 4 x 25.1 = 100.4
2. Argument: sqrt(3 x 100.4 / 15) = sqrt(20.1) = 4.48
3. Ps = 4 x (1 - 1/4) x Q(4.48) = 3 x 3.7e-6 = 1.1e-5
4. Pb = Ps/4 = 2.8e-6
RESULT
About 3 bit errors per million at 14 dB. 16-PSK would need roughly 18 dB for the same figure.
L = sqrt(M)
P_axis = 2*(1 - 1/L) * Q( sqrt( 3*E_av / ((M-1)*N0) ) )
Ps = 1 - (1 - P_axis)^2 ~= 2*P_axis
PAPR(16-QAM) = 2.55 PAPR(QPSK) = 1.0
THE MISTAKE STUDENTS MAKE
Students apply the square-QAM formula to non-square constellations such as 8-QAM or 32-QAM. Those are not products of two PAM axes, so the per-axis decomposition does not hold and the nearest-neighbour count is different.
Source: Digital Communication Systems, 1st ed., Ch. 7, pp. 370-375 | CO2 | Bloom L5
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is 16-QAM at Eb/N0 = 14 dB. Work at the pace of the slowest note-taker and land hard on the result: About 3 bit errors per million at 14 dB. 16-PSK would need roughly 18 dB for the same figure. Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 2: Digital Modulation Techniques. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 7, pp. 370-375. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 32
BFSK: orthogonal signalling in two dimensions
What it is, why it works, and what it costs.
VTU BEC503 | Module 2
BFSK: orthogonal signalling in two di…
32
THE MECHANISM
Binary frequency-shift keying transmits one of two carriers at different frequencies, and when the frequency separation is chosen so that the two waveforms are orthogonal over a bit interval, the constellation is two-dimensional with points on the two axes at distance sqrt(Eb) from the origin. Unlike BPSK, the two points are perpendicular rather than antipodal, so the distance between them is sqrt(2 Eb) rather than 2 sqrt(Eb) — a factor of sqrt(2) less, or 3 dB. The compensation is that BFSK has a constant envelope and, crucially, can be detected without a phase reference, which BPSK cannot.
KEY TERMS
• BFSK
• orthogonal signals
• frequency separation
• Sunde FSK
• two-dimensional constellation
TAKEAWAY
Orthogonal costs 3 dB against antipodal, and that 3 dB buys the option of noncoherent detection.
DIAGRAM FOR PHASE 2
A two-dimensional plane with axes labelled "phi1 (f1)" and "phi2 (f2)". Two points sit at (sqrt(Eb), 0) and (0, sqrt(Eb)), joined by a bold line labelled "d = sqrt(2 Eb)". A right-angle square marks the origin…
Source: Digital Communication Systems, 1st ed., Ch. 7, pp. 375-382
CO2 | Bloom L3 | visual id: bfsk-orthogonal-geometry
Notes: What to say: Give them the idea before the formalism. Say it plainly first: Binary frequency-shift keying transmits one of two carriers at different frequencies, and when the frequency separation is chosen so that the two waveform… Then add the part they are examined on - Orthogonal costs 3 dB against antipodal, and that 3 dB buys the option of noncoherent detection. Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "BFSK" constrain here, and what would break if it did not hold? Animation instructions: the two axes draw with the right-angle square, then the two BFSK points land and their connecting line draws with its label, then the faint BPSK points and their longer line fade in beneath, then the comparison card slides in, then the time strip draws with the frequency change highlighted at each boundary. Transition style: Fade [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 2: Digital Modulation Techniques. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 7, pp. 375-382. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 33
BFSK: orthogonal signalling in two dimensions - how it works
The procedure in order, and what each pass costs you.
VTU BEC503 | Module 2
BFSK: orthogonal signalling in two di…
33
1. Choose two frequencies f1 and f2 separated by an integer multiple of 1/(2Tb) for orthogonality
2. Transmit the carrier at f1 for a 1 and at f2 for a 0
3. At the receiver, correlate against both frequencies over Tb
4. Take the difference of the two correlator outputs
5. Decide by the sign of the difference
COST AND BEHAVIOUR
Best: constant envelope, and noncoherent detection is possible
Typical: needs two dimensions, so bandwidth is wider than BPSK
Worst: 3 dB worse than BPSK for coherent detection at the same Eb/N0
WHAT THAT MEANS
Sunde's FSK, with separation exactly 1/Tb, is the classic minimum-separation orthogonal case.
Source: Digital Communication Systems, 1st ed., Ch. 7, pp. 375-382 | CO2 | Bloom L3
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Choose two frequencies f1 and f2 separated by an integer multiple of 1/(2Tb) for orthogonality - and check everyone has written it before moving on. At the cost panel, translate it: Sunde's FSK, with separation exactly 1/Tb, is the classic minimum-separation orthogonal case. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 2: Digital Modulation Techniques. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 7, pp. 375-382. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 34
BFSK: orthogonal signalling in two dimensions - worked example
One concrete case, carried all the way to a stated number.
VTU BEC503 | Module 2
BFSK: orthogonal signalling in two di…
34
GIVEN
Tb = 1 ms. Find the minimum frequency separation for orthogonality with coherent detection.
1. Orthogonality over Tb requires the separation to be a multiple of 1/(2Tb) for coherent detection
2. 1/(2 x 0.001) = 500 Hz
3. For noncoherent detection the requirement tightens to a multiple of 1/Tb = 1000 Hz
4. Sunde's FSK uses exactly 1/Tb = 1000 Hz, which works for both
RESULT
Coherent BFSK can use 500 Hz separation; noncoherent needs 1000 Hz, so choosing noncoherent detection also costs bandwidth.
s_i(t) = sqrt(2*Eb/Tb) * cos(2*pi*f_i*t) i = 1,2
Orthogonal (coherent): f1 - f2 = n/(2*Tb)
Orthogonal (noncoherent): f1 - f2 = n/Tb
Vectors: s1 = (sqrt(Eb), 0), s2 = (0, sqrt(Eb))
d_min = sqrt(2*Eb)
THE MISTAKE STUDENTS MAKE
Students draw BFSK as two points on one axis like BPSK. Orthogonal signals require two dimensions; drawing them on one axis produces the wrong distance and hides the 3 dB penalty entirely.
Source: Digital Communication Systems, 1st ed., Ch. 7, pp. 375-382 | CO2 | Bloom L3
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is Tb = 1 ms. Find the minimum frequency separation for orthogonality with coherent detection. Work at the pace of the slowest note-taker and land hard on the result: Coherent BFSK can use 500 Hz separation; noncoherent needs 1000 Hz, so choosing noncoherent detection also costs bandwidth. Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 2: Digital Modulation Techniques. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 7, pp. 375-382. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 35
BFSK: coherent detection and error probability
What it is, why it works, and what it costs.
VTU BEC503 | Module 2
BFSK: coherent detection and error pr…
35
THE MECHANISM
A coherent BFSK receiver uses two correlators, one for each frequency, and subtracts their outputs before comparing against zero. The difference of the two Gaussian variables has variance N0 rather than N0/2 because two independent noise projections are combined, while the mean difference is sqrt(Eb). The bit error probability is therefore Q(sqrt(Eb/N0)), exactly 3 dB worse than BPSK. This penalty is the direct arithmetic consequence of the geometry: orthogonal points are sqrt(2) closer together than antipodal ones at the same energy, and Q of an argument sqrt(2) smaller is what a 3 dB loss looks like.
KEY TERMS
• coherent FSK
• difference detector
• error probability
• two correlators
• 3 dB penalty
TAKEAWAY
Pb = Q(sqrt(Eb/N0)) for coherent BFSK — the same formula as BPSK with the two removed, which is the 3 dB.
DIAGRAM FOR PHASE 2
A receiver diagram: input "r(t)" fans to two branches, upper multiplied by "phi1 = cos(2 pi f1 t)" and lower by "phi2 = cos(2 pi f2 t)", each into an integrator over Tb, each into a sampler at Tb. The two outp…
Source: Digital Communication Systems, 1st ed., Ch. 7, pp. 375-382
CO2 | Bloom L4 | visual id: bfsk-difference-detector
Notes: What to say: Give them the idea before the formalism. Say it plainly first: A coherent BFSK receiver uses two correlators, one for each frequency, and subtracts their outputs before comparing against zero. Then add the part they are examined on - Pb = Q(sqrt(Eb/N0)) for coherent BFSK — the same formula as BPSK with the two removed, which is the 3 dB. Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "coherent FSK" constrain here, and what would break if it did not hold? Animation instructions: the input fans to both branches, then each branch lights in sequence through multiplier, integrator and sampler, then the subtractor circle fills and pulses, then the comparator and decision arrow appear, then the right-hand plot draws its two bells, then the threshold drops and the tail shades with the variance annotation landing last. Transition style: Fade [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 2: Digital Modulation Techniques. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 7, pp. 375-382. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 36
BFSK: coherent detection and error probability - how it works
The procedure in order, and what each pass costs you.
VTU BEC503 | Module 2
BFSK: coherent detection and error pr…
36
1. Correlate the received waveform against phi1 and against phi2 over the bit interval
2. Sample both correlator outputs at t = Tb
3. Form the difference x1 - x2
4. Compare the difference against zero
5. Note the difference has variance N0 because two independent noise terms combine
COST AND BEHAVIOUR
Best: constant envelope preserved
Typical: two correlators instead of one
Worst: 3 dB worse than BPSK, and requires phase reference at both frequencies
WHAT THAT MEANS
Requiring coherence at two frequencies is harder than at one, which is why coherent BFSK is rare in practice.
Source: Digital Communication Systems, 1st ed., Ch. 7, pp. 375-382 | CO2 | Bloom L4
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Correlate the received waveform against phi1 and against phi2 over the bit interval - and check everyone has written it before moving on. At the cost panel, translate it: Requiring coherence at two frequencies is harder than at one, which is why coherent BFSK is rare in practice. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 2: Digital Modulation Techniques. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 7, pp. 375-382. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 37
BFSK: coherent detection and error probability - worked example
One concrete case, carried all the way to a stated number.
VTU BEC503 | Module 2
BFSK: coherent detection and error pr…
37
GIVEN
Eb/N0 = 12 dB, comparing coherent BFSK against BPSK.
1. Eb/N0 = 15.85 in linear terms
2. BPSK: Q(sqrt(2 x 15.85)) = Q(5.63) = 9.0 x 10^-9
3. BFSK: Q(sqrt(15.85)) = Q(3.98) = 3.4 x 10^-5
4. To match BPSK, BFSK would need 15 dB
RESULT
BFSK at 12 dB is nearly four thousand times worse than BPSK at the same energy, and needs 3 dB more to match it.
x1 = integral r(t)*phi1(t) dt, x2 = integral r(t)*phi2(t) dt
l = x1 - x2
E[l | 1 sent] = +sqrt(Eb), Var[l] = N0
Pb = Q( sqrt(Eb) / sqrt(N0) ) = Q( sqrt(Eb/N0) )
THE MISTAKE STUDENTS MAKE
Students use variance N0/2 for the difference variable. Subtracting two independent Gaussians of variance N0/2 each gives a variance of N0, and using N0/2 makes BFSK appear as good as BPSK, erasing the 3 dB penalty.
Source: Digital Communication Systems, 1st ed., Ch. 7, pp. 375-382 | CO2 | Bloom L4
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is Eb/N0 = 12 dB, comparing coherent BFSK against BPSK. Work at the pace of the slowest note-taker and land hard on the result: BFSK at 12 dB is nearly four thousand times worse than BPSK at the same energy, and needs 3 dB more to match it. Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 2: Digital Modulation Techniques. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 7, pp. 375-382. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 38
Comparing BPSK, QPSK and BFSK on one chart
What it is, why it works, and what it costs.
VTU BEC503 | Module 2
Comparing BPSK, QPSK and BFSK on one…
38
THE MECHANISM
Plotting bit error rate against Eb/N0 on logarithmic axes produces the familiar waterfall curves, and the whole module can be read off one chart. BPSK and QPSK sit on the same curve, Pb = Q(sqrt(2Eb/N0)), with QPSK delivering twice the bits per hertz. Coherent BFSK sits 3 dB to the right, noncoherent BFSK about 4 dB, and DPSK roughly 1 dB to the right of BPSK. Selecting a scheme is a matter of asking which axis is scarce: if bandwidth is scarce, move up in M; if power is scarce, stay at QPSK; if receiver complexity or phase stability is the problem, pay the decibel or two for a noncoherent scheme.
KEY TERMS
• BER curve
• waterfall
• Eb/N0
• spectral efficiency
• scheme selection
TAKEAWAY
One chart decides the scheme: BPSK and QPSK share the best curve, and every simplification of the receiver costs a known number of decibels.
DIAGRAM FOR PHASE 2
A semi-logarithmic plot with Eb/N0 in dB from 0 to 15 on the horizontal axis and bit error rate from 1e-1 down to 1e-8 on the vertical logarithmic axis. Four labelled waterfall curves descend left to right: "B…
Source: Digital Communication Systems, 1st ed., Ch. 7, pp. 415-418
CO2 | Bloom L5 | visual id: ber-waterfall-comparison
Notes: What to say: Give them the idea before the formalism. Say it plainly first: Plotting bit error rate against Eb/N0 on logarithmic axes produces the familiar waterfall curves, and the whole module can be read off one chart. Then add the part they are examined on - One chart decides the scheme: BPSK and QPSK share the best curve, and every simplification of the receiver costs a known num… Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "BER curve" constrain here, and what would break if it did not hold? Animation instructions: the axes draw with the logarithmic gridlines, then the BPSK/QPSK curve draws left to right, then the other three curves draw in sequence, then the 1e-5 dashed line sweeps across, then the crossing markers drop onto each curve in order, then the offset brackets appear with their dB labels, then the legend card slides in. Transition style: Fade [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 2: Digital Modulation Techniques. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 7, pp. 415-418. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 39
Comparing BPSK, QPSK and BFSK on one chart - how it works
The procedure in order, and what each pass costs you.
VTU BEC503 | Module 2
Comparing BPSK, QPSK and BFSK on one…
39
1. Fix the target bit error rate, typically 1e-5 or 1e-6
2. For each scheme, invert its Pb expression to find the required Eb/N0
3. Tabulate the required values and their differences in decibels
4. Note the spectral efficiency of each scheme alongside
5. Choose by whichever resource — power, bandwidth or receiver complexity — is scarcest
COST AND BEHAVIOUR
Best: QPSK is usually the right default: best curve and twice the efficiency of BPSK
Typical: differences between schemes are 1 to 4 dB
Worst: high-order schemes diverge rapidly at low SNR
WHAT THAT MEANS
The curves are all for uncoded transmission; coding in Modules 4 and 5 shifts every one of them left.
Source: Digital Communication Systems, 1st ed., Ch. 7, pp. 415-418 | CO2 | Bloom L5
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Fix the target bit error rate, typically 1e-5 or 1e-6 - and check everyone has written it before moving on. At the cost panel, translate it: The curves are all for uncoded transmission; coding in Modules 4 and 5 shifts every one of them left. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 2: Digital Modulation Techniques. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 7, pp. 415-418. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 40
Comparing BPSK, QPSK and BFSK on one chart - worked example
One concrete case, carried all the way to a stated number.
VTU BEC503 | Module 2
Comparing BPSK, QPSK and BFSK on one…
40
GIVEN
Required Eb/N0 at Pb = 1e-5 for the four schemes.
1. BPSK and QPSK: argument must be 4.27, so Eb/N0 = 9.6 dB
2. DPSK: Pb = 0.5 exp(-Eb/N0) gives Eb/N0 = 10.3 dB
3. Coherent BFSK: 3 dB worse than BPSK, 12.6 dB
4. Noncoherent BFSK: Pb = 0.5 exp(-Eb/(2N0)) gives about 13.3 dB
RESULT
The full spread is under 4 dB. Receiver simplicity is often worth more than 4 dB, which is why noncoherent schemes remain in wide use.
BPSK, QPSK: Pb = Q( sqrt(2*Eb/N0) )
Coherent BFSK: Pb = Q( sqrt(Eb/N0) )
Noncoherent BFSK: Pb = 0.5 * exp( -Eb/(2*N0) )
DPSK: Pb = 0.5 * exp( -Eb/N0 )
At Pb = 1e-5: 9.6 / 12.6 / 13.3 / 10.3 dB respectively
THE MISTAKE STUDENTS MAKE
Students read the horizontal axis as signal-to-noise ratio rather than energy per bit to noise density. The two differ by the bandwidth-time product, so comparing schemes of different spectral efficiency on an SNR axis mixes two effects and produces the wrong ranking.
Source: Digital Communication Systems, 1st ed., Ch. 7, pp. 415-418 | CO2 | Bloom L5
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is Required Eb/N0 at Pb = 1e-5 for the four schemes. Work at the pace of the slowest note-taker and land hard on the result: The full spread is under 4 dB. Receiver simplicity is often worth more than 4 dB, which is why noncoherent schemes remain in wide… Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 2: Digital Modulation Techniques. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 7, pp. 415-418. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 41
Detection of signals with unknown phase
What it is, why it works, and what it costs.
VTU BEC503 | Module 2
Detection of signals with unknown pha…
41
THE MECHANISM
When the carrier phase is unknown and modelled as uniformly distributed over 0 to 2 pi, the likelihood must be averaged over that phase, and the result depends on the received energy only through the envelope of the correlator outputs. Formally, the average produces a modified Bessel function of the first kind, I0, which is monotonically increasing, so the optimum receiver compares envelopes rather than signed correlator outputs. Practically this means computing sqrt(xI^2 + xQ^2) from a quadrature pair of correlators and comparing those magnitudes. The phase information is discarded because there is nothing reliable in it, and that discarding is exactly what costs about 1 dB.
KEY TERMS
• unknown phase
• uniform prior
• envelope detector
• Bessel function
• quadrature pair
TAKEAWAY
Averaging over an unknown phase turns the optimum receiver into an envelope comparison — the phase is discarded because it carries nothing usable.
DIAGRAM FOR PHASE 2
A receiver diagram for one frequency branch: input "r(t)" splits to two correlators, upper fed by "cos(2 pi f1 t)" and lower by "sin(2 pi f1 t)", each into an integrator and sampler, giving "xI" and "xQ". Both…
Source: Digital Communication Systems, 1st ed., Ch. 7, pp. 400-410
CO2 | Bloom L4 | visual id: noncoherent-envelope-detector
Notes: What to say: Give them the idea before the formalism. Say it plainly first: When the carrier phase is unknown and modelled as uniformly distributed over 0 to 2 pi, the likelihood must be averaged over that phase, and the result de… Then add the part they are examined on - Averaging over an unknown phase turns the optimum receiver into an envelope comparison — the phase is discarded because it c… Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "unknown phase" constrain here, and what would break if it did not hold? Animation instructions: the input splits to both correlators, then both branches light simultaneously, then the envelope block fills and its output arrow extends, then the phasor circle draws, then five ghost vectors fan out around it one at a time at random angles, then the solid vector settles and its length is bracketed and labelled. Transition style: Fade [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 2: Digital Modulation Techniques. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 7, pp. 400-410. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 42
Detection of signals with unknown phase - how it works
The procedure in order, and what each pass costs you.
VTU BEC503 | Module 2
Detection of signals with unknown pha…
42
1. Model the carrier phase as uniform over 0 to 2 pi
2. Correlate against both a cosine and a sine at the signalling frequency
3. Compute the envelope sqrt(xI^2 + xQ^2) for each candidate signal
4. Compare envelopes and choose the largest
5. Note the decision is invariant to any phase rotation of the received signal
COST AND BEHAVIOUR
Best: no carrier recovery loop needed at all
Typical: two correlators per candidate frequency instead of one
Worst: costs roughly 1 dB relative to coherent detection at usable error rates
WHAT THAT MEANS
The loss shrinks at low error rates and grows at high ones.
Source: Digital Communication Systems, 1st ed., Ch. 7, pp. 400-410 | CO2 | Bloom L4
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Model the carrier phase as uniform over 0 to 2 pi - and check everyone has written it before moving on. At the cost panel, translate it: The loss shrinks at low error rates and grows at high ones. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 2: Digital Modulation Techniques. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 7, pp. 400-410. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 43
Detection of signals with unknown phase - worked example
One concrete case, carried all the way to a stated number.
VTU BEC503 | Module 2
Detection of signals with unknown pha…
43
GIVEN
Quadrature outputs xI = 0.6, xQ = 0.8 for frequency f1, and xI = 0.3, xQ = 0.2 for f2.
1. Envelope at f1: sqrt(0.36 + 0.64) = sqrt(1.0) = 1.0
2. Envelope at f2: sqrt(0.09 + 0.04) = sqrt(0.13) = 0.36
3. Compare: 1.0 > 0.36
4. Decide f1 was transmitted, with no reference to either phase
RESULT
The decision uses only magnitudes. Rotating both quadrature pairs by any angle leaves the envelopes and therefore the decision unchanged.
p(r | s_i) averaged over phase ~ I0( 2*sqrt(E)*|x_i| / N0 )
I0 monotonically increasing => compare |x_i|
|x_i| = sqrt( xI_i^2 + xQ_i^2 )
Decide i maximising the envelope |x_i|.
THE MISTAKE STUDENTS MAKE
Students square the envelope and compare, then also apply the -E/2 bias from the coherent rule. With equal-energy signals the bias term is common to all candidates and must not be added twice; with unequal energies the noncoherent rule needs a different correction entirely.
Source: Digital Communication Systems, 1st ed., Ch. 7, pp. 400-410 | CO2 | Bloom L4
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is Quadrature outputs xI = 0.6, xQ = 0.8 for frequency f1, and xI = 0.3, xQ = 0.2 for f2. Work at the pace of the slowest note-taker and land hard on the result: The decision uses only magnitudes. Rotating both quadrature pairs by any angle leaves the envelopes and therefore the decision un… Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 2: Digital Modulation Techniques. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 7, pp. 400-410. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 44
BFSK using noncoherent detection
What it is, why it works, and what it costs.
VTU BEC503 | Module 2
BFSK using noncoherent detection
44
THE MECHANISM
Noncoherent BFSK detection replaces each correlator with a bandpass filter centred on one of the two signalling frequencies, followed by an envelope detector, and decides in favour of whichever branch shows the larger envelope. No carrier phase reference is required anywhere in the receiver, which removes the phase-locked loop, the acquisition time and the cycle-slip failure mode. The bit error probability has the remarkably clean closed form 0.5 exp(-Eb/(2 N0)), about 1 dB worse than coherent BFSK at usable error rates. The frequency separation must now be a multiple of 1/Tb rather than 1/(2Tb), so the bandwidth penalty is real as well.
KEY TERMS
• noncoherent FSK
• envelope detector
• bandpass filter pair
• exponential error expression
• phase-free receiver
TAKEAWAY
Noncoherent BFSK trades about 1 dB and some bandwidth for the complete removal of carrier recovery — often the right trade.
DIAGRAM FOR PHASE 2
A two-branch receiver: input "r(t)" splits to an upper "BPF at f1" and a lower "BPF at f2", each followed by an "envelope detector" block, each followed by a sampler at Tb. The two envelopes meet at a comparat…
Source: Digital Communication Systems, 1st ed., Ch. 7, pp. 410-411
CO2 | Bloom L4 | visual id: noncoherent-bfsk-receiver
Notes: What to say: Give them the idea before the formalism. Say it plainly first: Noncoherent BFSK detection replaces each correlator with a bandpass filter centred on one of the two signalling frequencies, followed by an envelope detec… Then add the part they are examined on - Noncoherent BFSK trades about 1 dB and some bandwidth for the complete removal of carrier recovery — often the right trade. Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "noncoherent FSK" constrain here, and what would break if it did not hold? Animation instructions: the input splits to both branches, then the two bandpass filters light together, then the two envelope detectors fill, then the samplers click, then the comparator fills and the decision arrow extends, then the comparison strip rows appear one at a time from the top. Transition style: Fade [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 2: Digital Modulation Techniques. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 7, pp. 410-411. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 45
BFSK using noncoherent detection - how it works
The procedure in order, and what each pass costs you.
VTU BEC503 | Module 2
BFSK using noncoherent detection
45
1. Pass the received signal through two bandpass filters centred on f1 and f2
2. Apply an envelope detector to each filter output
3. Sample both envelopes at the end of the bit interval
4. Choose the branch with the larger envelope
5. Set the frequency separation to a multiple of 1/Tb so the two branches remain orthogonal without phase alignment
COST AND BEHAVIOUR
Best: no carrier recovery, no acquisition delay, no cycle slips
Typical: about 1 dB worse than coherent BFSK
Worst: needs double the frequency separation, so more bandwidth
WHAT THAT MEANS
This is the classic choice for low-cost telemetry and for links where phase cannot be tracked.
Source: Digital Communication Systems, 1st ed., Ch. 7, pp. 410-411 | CO2 | Bloom L4
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Pass the received signal through two bandpass filters centred on f1 and f2 - and check everyone has written it before moving on. At the cost panel, translate it: This is the classic choice for low-cost telemetry and for links where phase cannot be tracked. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 2: Digital Modulation Techniques. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 7, pp. 410-411. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 46
BFSK using noncoherent detection - worked example
One concrete case, carried all the way to a stated number.
VTU BEC503 | Module 2
BFSK using noncoherent detection
46
GIVEN
Eb/N0 = 13 dB.
1. Linear: Eb/N0 = 19.95
2. Pb = 0.5 exp(-19.95/2) = 0.5 exp(-9.98)
3. exp(-9.98) = 4.63 x 10^-5
4. Pb = 2.3 x 10^-5
RESULT
About 2 errors per hundred thousand bits at 13 dB. Coherent BFSK at the same energy gives about 8 x 10^-6, so the noncoherent penalty here is under 1 dB.
Branch i: BPF at f_i -> envelope detector -> sample at Tb
Decide 1 if envelope_1 > envelope_2
Pb = 0.5 * exp( -Eb / (2*N0) )
Separation: |f1 - f2| = n/Tb (integer n)
THE MISTAKE STUDENTS MAKE
Students quote Pb = 0.5 exp(-Eb/N0) for noncoherent BFSK. That is the DPSK expression; noncoherent BFSK carries the extra factor of two in the denominator, and confusing them understates the required energy by 3 dB.
Source: Digital Communication Systems, 1st ed., Ch. 7, pp. 410-411 | CO2 | Bloom L4
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is Eb/N0 = 13 dB. Work at the pace of the slowest note-taker and land hard on the result: About 2 errors per hundred thousand bits at 13 dB. Coherent BFSK at the same energy gives about 8 x 10^-6, so the noncoherent pen… Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 2: Digital Modulation Techniques. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 7, pp. 410-411. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 47
Differential phase-shift keying
What it is, why it works, and what it costs.
VTU BEC503 | Module 2
Differential phase-shift keying
47
THE MECHANISM
Differential phase-shift keying encodes each bit as a change of phase relative to the previous symbol rather than as an absolute phase, so the receiver can compare consecutive symbols and never needs an absolute reference. The transmitter differentially encodes the bit stream — typically leaving the phase unchanged for a 1 and reversing it for a 0 — and the receiver multiplies the received signal by a one-symbol-delayed copy of itself and integrates. The error probability is 0.5 exp(-Eb/N0), roughly 1 dB worse than coherent BPSK, and the mechanism of the loss is clear: the reference is itself noisy, so noise enters the decision twice. A single symbol error corrupts two decoded bits.
KEY TERMS
• DPSK
• differential encoding
• delay-and-multiply
• phase ambiguity
• error propagation
TAKEAWAY
DPSK uses the previous symbol as its phase reference — costing about 1 dB because that reference is noisy, and doubling each error.
DIAGRAM FOR PHASE 2
Upper half: an encoding table with four columns — input bit, rule, previous phase, transmitted phase — and five populated rows showing a worked sequence, with the two rows where the phase reverses highlighted.…
Source: Digital Communication Systems, 1st ed., Ch. 7, pp. 411-415
CO2 | Bloom L4 | visual id: dpsk-encode-and-detect
Notes: What to say: Give them the idea before the formalism. Say it plainly first: Differential phase-shift keying encodes each bit as a change of phase relative to the previous symbol rather than as an absolute phase, so the receiver ca… Then add the part they are examined on - DPSK uses the previous symbol as its phase reference — costing about 1 dB because that reference is noisy, and doubling each… Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "DPSK" constrain here, and what would break if it did not hold? Animation instructions: the table draws row by row with the phase column filling last, then the two reversal rows highlight, then the receiver diagram builds with the direct path first, then the delay path draws and the red callout snaps in, then the integrator and comparator fill, then the side note appears. Transition style: Fade [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 2: Digital Modulation Techniques. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 7, pp. 411-415. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 48
Differential phase-shift keying - how it works
The procedure in order, and what each pass costs you.
VTU BEC503 | Module 2
Differential phase-shift keying
48
1. Differentially encode: keep the phase for a 1, reverse it for a 0
2. Transmit the encoded phase sequence as ordinary BPSK
3. At the receiver, multiply the incoming signal by a copy delayed by one symbol
4. Integrate the product over the symbol interval
5. Decide 1 for a positive result and 0 for a negative one
COST AND BEHAVIOUR
Best: no carrier phase recovery and no phase ambiguity to resolve
Typical: about 1 dB worse than coherent BPSK
Worst: errors come in pairs, since each received symbol is used in two decisions
WHAT THAT MEANS
Pairing means the effective bit error rate is close to twice the symbol error rate.
Source: Digital Communication Systems, 1st ed., Ch. 7, pp. 411-415 | CO2 | Bloom L4
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Differentially encode: keep the phase for a 1, reverse it for a 0 - and check everyone has written it before moving on. At the cost panel, translate it: Pairing means the effective bit error rate is close to twice the symbol error rate. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 2: Digital Modulation Techniques. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 7, pp. 411-415. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 49
Differential phase-shift keying - worked example
One concrete case, carried all the way to a stated number.
VTU BEC503 | Module 2
Differential phase-shift keying
49
GIVEN
Bits 1 0 1 1 0, initial reference phase 0 degrees.
1. Bit 1: keep phase, transmit 0 degrees
2. Bit 0: reverse, transmit 180 degrees
3. Bit 1: keep, transmit 180 degrees
4. Bit 1: keep, transmit 180; bit 0: reverse, transmit 0 degrees
RESULT
Phases 0, 180, 180, 180, 0. Comparing consecutive phases recovers 1 0 1 1 0 with no absolute reference; one corrupted symbol wrecks two bits.
Encoding: d_k = d_{k-1} XNOR b_k (keep on 1, reverse on 0)
Detection: l = integral_0^Tb r(t)*r(t - Tb) dt
decide 1 if l > 0
Pb = 0.5 * exp( -Eb/N0 )
Roughly 1 dB worse than coherent BPSK at Pb = 1e-5.
THE MISTAKE STUDENTS MAKE
Students treat DPSK as noncoherent BPSK and expect the noncoherent BFSK formula. DPSK is a differentially coherent scheme: it still exploits phase, just relatively, which is why its penalty is 1 dB rather than 3 or 4.
Source: Digital Communication Systems, 1st ed., Ch. 7, pp. 411-415 | CO2 | Bloom L4
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is Bits 1 0 1 1 0, initial reference phase 0 degrees. Work at the pace of the slowest note-taker and land hard on the result: Phases 0, 180, 180, 180, 0. Comparing consecutive phases recovers 1 0 1 1 0 with no absolute reference; one corrupted symbol wrec… Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 2: Digital Modulation Techniques. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 7, pp. 411-415. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 50
Choosing a modulation scheme for a given link
What it is, why it works, and what it costs.
VTU BEC503 | Module 2
Choosing a modulation scheme for a gi…
50
THE MECHANISM
Scheme selection is the joint answer to four questions: how much bandwidth is available, how much power, how stable is the phase reference, and how linear is the power amplifier. A bandwidth-limited link with plenty of power and a linear amplifier points at high-order QAM. A power-limited link with a saturated amplifier points at QPSK or a constant-envelope scheme. A link with an unstable phase reference, such as a fast-fading mobile channel or a cheap oscillator, points at DPSK or noncoherent FSK despite the decibel or two. Implementation loss of 1 to 2 dB should be budgeted on top of any theoretical figure.
KEY TERMS
• link budget
• spectral efficiency
• implementation loss
• amplifier back-off
• design trade-off
TAKEAWAY
Four constraints decide the scheme — bandwidth, power, phase stability, amplifier linearity — and the theory only ranks options within them.
DIAGRAM FOR PHASE 2
A decision tree flowing downward from a root box "choose modulation". First branch on "bandwidth limited?" splitting yes and no. The yes path asks "amplifier linear?" and leads to "high-order QAM" or "high-ord…
Source: Digital Communication Systems, 1st ed., Ch. 7, pp. 415-418
CO2 | Bloom L5 | visual id: scheme-selection-decision-tree
Notes: What to say: Give them the idea before the formalism. Say it plainly first: Scheme selection is the joint answer to four questions: how much bandwidth is available, how much power, how stable is the phase reference, and how linear… Then add the part they are examined on - Four constraints decide the scheme — bandwidth, power, phase stability, amplifier linearity — and the theory only ranks opti… Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "link budget" constrain here, and what would break if it did not hold? Animation instructions: the root box appears, then each decision diamond drops in with its two branches drawing in turn, level by level down the tree, then all leaf boxes fill together, then the badges pop onto each leaf in sequence, then the footer strip slides up. Transition style: Fade [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 2: Digital Modulation Techniques. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 7, pp. 415-418. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 51
Choosing a modulation scheme for a given link - how it works
The procedure in order, and what each pass costs you.
VTU BEC503 | Module 2
Choosing a modulation scheme for a gi…
51
1. Compute the available bandwidth and the required bit rate to get the needed spectral efficiency
2. Compute the received Eb/N0 from the link budget
3. Eliminate schemes whose required Eb/N0 exceeds what is available
4. Eliminate varying-envelope schemes if the amplifier must run saturated
5. Among survivors, prefer the simplest receiver, then add 1 to 2 dB implementation margin
COST AND BEHAVIOUR
Best: the constraints usually eliminate all but one or two candidates
Typical: a table of four columns settles most cases
Worst: when no scheme fits, coding from Modules 4 and 5 is the remaining lever
WHAT THAT MEANS
Coding buys several dB and is almost always cheaper than more transmit power.
Source: Digital Communication Systems, 1st ed., Ch. 7, pp. 415-418 | CO2 | Bloom L5
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Compute the available bandwidth and the required bit rate to get the needed spectral efficiency - and check everyone has written it before moving on. At the cost panel, translate it: Coding buys several dB and is almost always cheaper than more transmit power. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 2: Digital Modulation Techniques. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 7, pp. 415-418. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 52
Choosing a modulation scheme for a given link - worked example
One concrete case, carried all the way to a stated number.
VTU BEC503 | Module 2
Choosing a modulation scheme for a gi…
52
GIVEN
Link with 1 MHz of bandwidth, 2 Mbit/s required, received Eb/N0 of 12 dB, saturated amplifier.
1. Required spectral efficiency: 2 bit/s/Hz, so at least 4 points
2. QPSK gives exactly 2 bit/s/Hz and needs 9.6 dB — 12 dB available, so 2.4 dB of margin
3. 16-QAM would give 4 bit/s/Hz but needs 13.4 dB and a linear amplifier — fails on both counts
4. Saturated amplifier rules out QAM regardless
RESULT
QPSK, with 2.4 dB of margin covering implementation loss. The saturated amplifier, not the noise, is what removes the higher-order options.
Required efficiency: r = R_b / B bit/s/Hz
Available margin: M = (Eb/N0)_rx - (Eb/N0)_required
Feasible if: r <= log2(M_ary) AND M >= implementation loss
Constant envelope required? => PSK or FSK only, no QAM
THE MISTAKE STUDENTS MAKE
Students choose the scheme with the lowest required Eb/N0 without checking spectral efficiency. BPSK has the best curve but only half the efficiency of QPSK, so on a bandwidth-limited link it fails the requirement no matter how much power is available.
Source: Digital Communication Systems, 1st ed., Ch. 7, pp. 415-418 | CO2 | Bloom L5
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is Link with 1 MHz of bandwidth, 2 Mbit/s required, received Eb/N0 of 12 dB, saturated amplifier. Work at the pace of the slowest note-taker and land hard on the result: QPSK, with 2.4 dB of margin covering implementation loss. The saturated amplifier, not the noise, is what removes the higher-orde… Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 2: Digital Modulation Techniques. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 7, pp. 415-418. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 53
One sentence per unit, six months from now
Units 1-7: what survives after the detail has gone.
VTU BEC503 | Module 2
Revision
53
01 Every error probability here is Q(distance / noise spread); comparing schemes means comparing one number inside a Q.
02 BPSK is the largest possible separation for two signals of energy Eb, at the cost of only one bit per symbol.
03 Pb = Q(sqrt(2Eb/N0)) is the floor for binary signalling; nothing binary does better, and everything else is measured against it.
04 QPSK is two BPSK streams in quadrature; Gray mapping is free and turns each likely symbol error into a single bit error.
05 QPSK gives twice the bit rate of BPSK in the same band at exactly the same bit error rate — the decisive result of the module.
06 M-ary PSK buys bits per symbol with angular spacing; d_min = 2 sqrt(E) sin(pi/M) is the whole story.
07 Bits per hertz and joules per bit trade against each other, and past QPSK the exchange rate turns sharply unfavourable.
Notes: What to say: Slow right down here. Read each takeaway aloud and then stop talking for a beat, because these are the sentences that should still be in their heads when they sit the SEE. Tell them explicitly that if they can reconstruct the reasoning behind any one of these lines they understand that unit, and if they can only recite it they do not. Pause cue: Pause for three seconds after each takeaway before moving to the next. Pointing cue: Point at each numbered takeaway in turn as you read it. Question to ask students: Ask: choose the takeaway you trust least and tell me what you would have to check to believe it. Animation instructions: Takeaway rows reveal one at a time from the top, each row highlighting briefly as it appears. Transition style: Fade [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 2: Digital Modulation Techniques, 10 hours, TB1 (Haykin 2014) Ch. 7.5-7.8 pp. 344-398 and Ch. 7.10-7.14 pp. 400-418. TB1: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014. Revision consolidates all 16 unit takeaways. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 54
Revision, continued
Units 8-14: what survives after the detail has gone.
VTU BEC503 | Module 2
Revision
54
08 QAM uses the whole plane instead of only the rim, which beats PSK for M above 8 — provided the amplifier can tolerate a varying envelope.
09 QAM wins on paper from M = 8 upward, and the win is real only if the power amplifier has the headroom for a varying envelope.
10 Orthogonal costs 3 dB against antipodal, and that 3 dB buys the option of noncoherent detection.
11 Pb = Q(sqrt(Eb/N0)) for coherent BFSK — the same formula as BPSK with the two removed, which is the 3 dB.
12 One chart decides the scheme: BPSK and QPSK share the best curve, and every simplification of the receiver costs a known number of decibels.
13 Averaging over an unknown phase turns the optimum receiver into an envelope comparison — the phase is discarded because it carries nothing usable.
14 Noncoherent BFSK trades about 1 dB and some bandwidth for the complete removal of carrier recovery — often the right trade.
Notes: What to say: Slow right down here. Read each takeaway aloud and then stop talking for a beat, because these are the sentences that should still be in their heads when they sit the SEE. Tell them explicitly that if they can reconstruct the reasoning behind any one of these lines they understand that unit, and if they can only recite it they do not. Pause cue: Pause for three seconds after each takeaway before moving to the next. Pointing cue: Point at each numbered takeaway in turn as you read it. Question to ask students: Ask: choose the takeaway you trust least and tell me what you would have to check to believe it. Animation instructions: Takeaway rows reveal one at a time from the top, each row highlighting briefly as it appears. Transition style: Fade [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 2: Digital Modulation Techniques, 10 hours, TB1 (Haykin 2014) Ch. 7.5-7.8 pp. 344-398 and Ch. 7.10-7.14 pp. 400-418. TB1: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014. Revision consolidates all 16 unit takeaways. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 55
Revision, continued
Units 15-16: what survives after the detail has gone.
VTU BEC503 | Module 2
Revision
55
15 DPSK uses the previous symbol as its phase reference — costing about 1 dB because that reference is noisy, and doubling each error.
16 Four constraints decide the scheme — bandwidth, power, phase stability, amplifier linearity — and the theory only ranks options within them.
Notes: What to say: Slow right down here. Read each takeaway aloud and then stop talking for a beat, because these are the sentences that should still be in their heads when they sit the SEE. Tell them explicitly that if they can reconstruct the reasoning behind any one of these lines they understand that unit, and if they can only recite it they do not. Pause cue: Pause for three seconds after each takeaway before moving to the next. Pointing cue: Point at each numbered takeaway in turn as you read it. Question to ask students: Ask: choose the takeaway you trust least and tell me what you would have to check to believe it. Animation instructions: Takeaway rows reveal one at a time from the top, each row highlighting briefly as it appears. Transition style: Fade [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 2: Digital Modulation Techniques, 10 hours, TB1 (Haykin 2014) Ch. 7.5-7.8 pp. 344-398 and Ch. 7.10-7.14 pp. 400-418. TB1: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014. Revision consolidates all 16 unit takeaways. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 56
How this module is assessed
Where the quiz and the assignment live, and what they test.
VTU BEC503 | Module 2
Assessment
56
MODULE 2 QUIZ
quizzes/Module_2_Quiz.pdf
quizzes/Module_2_Quiz.gift
45 minutes | 50 marks | pass 20 | 1 attempt
Part A: 20 MCQs, 1 mark each.
Part B: 13 descriptive questions, 30 marks.
Bloom spread: L1-L2 24%, L3-L4 61%, L5-L6 15%
Every question carries a CO tag, a Bloom level and a chapter reference; distractor feedback names the misconception.
MODULE 2 ASSIGNMENT
assignments/Module_2_Assignment.pdf
Assignment 2 — Modulation schemes and their error performance
20 marks | 10% of CIE | 8 problems + 3 theory items
Submit as PDF, single file, named <USN>_BEC503_Assignment2.pdf, via LMS upload. 10% per day, nothing after 5 days.
Rubric: Correctness of derivations (8); Numerical accuracy and dB handling (5); Constellation and BER diagrams (4); Engineering judgement in scheme selection (3). Attainment: CO2 = 18, CO1 = 2.
Previous years' question papers for EC are indexed in pyq/PYQ_Index.pdf; the syllabus extract and the topic-to-slide mapping are in syllabus/Syllabus_Mapping.pdf.
Individual submission. Identical submissions score zero for both parties.
Notes: What to say: Close by telling them exactly where the assessment lives and what it tests. Name the two files, say the mark split out loud, and read the Bloom spread so they understand that roughly a quarter of the paper is not recall at all. Then read the integrity line word for word, because ambiguity there costs students more than any technical error in this module. Pause cue: Pause after the Bloom spread and before the integrity statement. Pointing cue: Point at the quiz panel, then the assignment panel, then the integrity line at the bottom. Question to ask students: Ask: which course outcome do you feel least ready on, and which unit would you reread tonight to fix it? Animation instructions: Quiz panel fades in from the left, then the assignment panel from the right, then the pointers strip appears, then the integrity line fades in last. Transition style: Fade [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 2: Digital Modulation Techniques, 10 hours, TB1 (Haykin 2014) Ch. 7.5-7.8 pp. 344-398 and Ch. 7.10-7.14 pp. 400-418. TB1: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014. Assessment counts: 20 MCQs, 13 descriptive questions, 11 assignment items. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.