## Slide 1
Digital Communication
Module 3 asks: What is the least I can pay to represent a source, and the most I can push through a channel, before the ma…
VTU BEC503 | Module 3
Opening
01
MODULE 3
Information Theory
10 contact hours | 16 teaching units | 56 slides
PRESCRIBED TEXTBOOK
Digital Communication Systems
Simon Haykin
John Wiley & Sons, 1st edition, 2014
TB1 (Haykin 2014) Ch. 5.1-5.10 pp. 207-244
Signal Space & AWGN • Digital Modulation • Information Theory • Block & Cyclic Codes • Convolutional Codes
Surprise measures information → Entropy is average surprise → Codes reach the entropy bound → Channels lose mutual information → Capacity is the hard ceiling
EC · Semester 5 · BEC503 · generated for Phase 2 conversion
Notes: What to say: Open by putting the whole module on one page. Tell them this is 10 contact hours and 16 teaching units, and that all of it exists to answer one question: What is the least I can pay to represent a source, and the most I can push through a channel, before the mathematics says no? Name the prescribed textbook out loud and say which chapters they will be living in, so nobody is reading the wrong book by week two. Pause cue: Pause after reading the driving question aloud, before naming the textbook. Pointing cue: Point at the module title block, then at the textbook panel, then run a finger along the five-beat arc. Question to ask students: Ask: before we start, what do you already expect the answer to "What is the least I can pay to represent a source, and the most I can push through a chan…" to look like? Animation instructions: Module title block fades in first, then the textbook panel slides in from the right, then the five arc beats appear left to right one at a time. Transition style: Fade [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 3: Information Theory, 10 hours, TB1 (Haykin 2014) Ch. 5.1-5.10 pp. 207-244. TB1: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 2
What this module is actually for
One question, five beats, and the scope it does not cover.
VTU BEC503 | Module 3
Overview
02
THE DRIVING QUESTION
What is the least I can pay to represent a source, and the most I can push through a channel, before the mathematics says no?
1
Surprise measures information
2
Entropy is average surprise
3
Codes reach the entropy bound
4
Channels lose mutual information
5
Capacity is the hard ceiling
SCOPE AND PROVENANCE
Built from TB1 Sections 5.1-5.10, which the syllabus names. The module has two halves that mirror each other. The source-coding half asks how few bits a source needs and answers with entropy, achieved by Huffman and Lempel-Ziv. The channel-coding half asks how many bits a channel can carry and answers with capacity, the maximum of mutual information over input distributions. Both are existence results: they say what is possible without saying how, which is exactly the gap that Modules 4 and 5 fill. The Information Capacity Law at the end unifies them and produces the Shannon limit of -1.6 dB, the number every coding scheme is ultimately measured against.
Course outcomes exercised: CO3
Assessment: 20 MCQs + 13 descriptive questions + 11 assignment items
Notes: What to say: Give them the map before the territory. Read the driving question once more, then walk the five beats across the slide and say in one sentence what changes between each beat and the next. Finish on the scope paragraph, because knowing what a module does not cover saves more marks than anything else on this slide. Pause cue: Pause for four or five seconds after the five beats appear, before moving to scope. Pointing cue: Point at the driving question panel, then at each numbered beat in turn, then at the scope paragraph. Question to ask students: Ask: which of these five beats do you expect to find hardest, and why that one? Animation instructions: The driving question panel fades in, then the five numbered beats appear left to right one at a time, then the scope paragraph fades in beneath them. Transition style: Fade [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 3: Information Theory, 10 hours, TB1 (Haykin 2014) Ch. 5.1-5.10 pp. 207-244. TB1: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 3
Every unit against its chapter and pages
Units 1-9 of 16, with the deck slides that teach each one.
VTU BEC503 | Module 3
Syllabus mapping
03
# — Teaching unit — Book chapter and pages — Deck slides — CO / Bloom
01 Information as surprise: the logarithmic measure — Ch. 5, pp. 207-214 — slides 5, 6, 7 — CO3 / L2
02 Entropy: the average information per symbol — Ch. 5, pp. 207-214 — slides 8, 9, 10 — CO3 / L3
03 Properties of entropy and the extension of a source — Ch. 5, pp. 207-214 — slides 11, 12, 13 — CO3 / L4
04 The source coding theorem — Ch. 5, pp. 214-215 — slides 14, 15, 16 — CO3 / L3
05 Prefix codes and the Kraft inequality — Ch. 5, pp. 215-223 — slides 17, 18, 19 — CO3 / L4
06 Huffman coding — Ch. 5, pp. 215-223 — slides 20, 21, 22 — CO3 / L4
07 Lempel-Ziv coding and the case for dictionary methods — Ch. 5, pp. 215-223 — slides 23, 24, 25 — CO3 / L4
08 Code efficiency, redundancy and where compression stops — Ch. 5, pp. 215-223 — slides 26, 27, 28 — CO3 / L4
09 Discrete memoryless channels and the transition matrix — Ch. 5, pp. 223-226 — slides 29, 30, 31 — CO3 / L3
Notes: What to say: Tell them this is the slide to photograph. Every unit in the module is listed against a real chapter and a real page range, so there is no ambiguity about what to read. Point out the slide-number column and say plainly that if they miss a lecture, those are the slides covering that unit. Say that the page ranges come from the book's own table of contents rather than a guess. Pause cue: Pause for ten seconds and let them photograph the table before saying anything else. Pointing cue: Run a finger down the chapter-and-pages column, then across one complete row. Question to ask students: Ask: pick any row - which chapter would you open first, and what would you expect in the first paragraph? Animation instructions: Header row appears first, then the unit rows fade in one at a time from the top, then the chapter-and-pages column highlights. Transition style: Cut [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 3: Information Theory, 10 hours, TB1 (Haykin 2014) Ch. 5.1-5.10 pp. 207-244. TB1: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014. Mapping covers all 16 teaching units. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 4
Syllabus mapping, continued
Units 10-16 of 16, with the deck slides that teach each one.
VTU BEC503 | Module 3
Syllabus mapping
04
# — Teaching unit — Book chapter and pages — Deck slides — CO / Bloom
10 The binary symmetric and binary erasure channels — Ch. 5, pp. 223-226 — slides 32, 33, 34 — CO3 / L4
11 Mutual information: what the output tells you about the input — Ch. 5, pp. 226-230 — slides 35, 36, 37 — CO3 / L4
12 Properties of mutual information — Ch. 5, pp. 226-230 — slides 38, 39, 40 — CO3 / L4
13 Channel capacity — Ch. 5, pp. 230-232 — slides 41, 42, 43 — CO3 / L4
14 The channel coding theorem — Ch. 5, pp. 232-237 — slides 44, 45, 46 — CO3 / L4
15 The Information Capacity Law — Ch. 5, pp. 240-244 — slides 47, 48, 49 — CO3 / L4
16 The bandwidth-power trade-off and the Shannon limit — Ch. 5, pp. 240-244 — slides 50, 51, 52 — CO3 / L5
Notes: What to say: Tell them this is the slide to photograph. Every unit in the module is listed against a real chapter and a real page range, so there is no ambiguity about what to read. Point out the slide-number column and say plainly that if they miss a lecture, those are the slides covering that unit. Say that the page ranges come from the book's own table of contents rather than a guess. Pause cue: Pause for ten seconds and let them photograph the table before saying anything else. Pointing cue: Run a finger down the chapter-and-pages column, then across one complete row. Question to ask students: Ask: pick any row - which chapter would you open first, and what would you expect in the first paragraph? Animation instructions: Header row appears first, then the unit rows fade in one at a time from the top, then the chapter-and-pages column highlights. Transition style: Cut [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 3: Information Theory, 10 hours, TB1 (Haykin 2014) Ch. 5.1-5.10 pp. 207-244. TB1: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014. Mapping covers all 16 teaching units. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 5
Information as surprise: the logarithmic measure
What it is, why it works, and what it costs.
VTU BEC503 | Module 3
Information as surprise: the logarith…
05
THE MECHANISM
The information content of an event of probability p is I = log2(1/p) bits, a quantity that is zero for a certain event and grows without bound as the event becomes rarer. The logarithm is not an arbitrary choice: it is forced by requiring that the information in two independent events add, since probabilities multiply and only the logarithm converts multiplication into addition. Information in this sense is a property of the probability alone, not of the meaning or usefulness of the message, which is why the theory applies equally to speech, images and telemetry. A fair coin flip carries exactly one bit; an event of probability one carries none.
KEY TERMS
• self-information
• surprise
• logarithmic measure
• bit
• additivity
TAKEAWAY
Information is surprise measured logarithmically, and the logarithm is forced by wanting independent events to add.
DIAGRAM FOR PHASE 2
A plot of I = log2(1/p) against probability p from 0 to 1. The curve descends steeply from the upper left, passing through the marked point (0.5, 1 bit) and reaching zero at p = 1, where a filled dot sits labe…
Source: Digital Communication Systems, 1st ed., Ch. 5, pp. 207-214
CO3 | Bloom L2 | visual id: self-information-curve
Notes: What to say: Give them the idea before the formalism. Say it plainly first: The information content of an event of probability p is I = log2(1/p) bits, a quantity that is zero for a certain event and grows without bound as the eve… Then add the part they are examined on - Information is surprise measured logarithmically, and the logarithm is forced by wanting independent events to add. Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "self-information" constrain here, and what would break if it did not hold? Animation instructions: the axes draw, then the curve sweeps in from the left, then the (0.5, 1) marker drops with its label, then the zero point fills, then the asymptote dashes upward, then the additivity panel builds left to right with the equals sign landing last. Transition style: Fade [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 3: Information Theory. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 5, pp. 207-214. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 6
Information as surprise: the logarithmic measure - how it works
The procedure in order, and what each pass costs you.
VTU BEC503 | Module 3
Information as surprise: the logarith…
06
1. Identify the probability p of the event
2. Compute I = log2(1/p) = -log2(p)
3. Read the answer in bits; use natural logarithm for nats or base 10 for hartleys
4. For independent events, add the individual informations
5. Check the two limits: p = 1 gives 0 bits, p approaching 0 gives unbounded bits
COST AND BEHAVIOUR
Best: one logarithm per event
Typical: depends only on the probability, never on the content
Worst: undefined for p = 0, which never occurs in a well-posed source
WHAT THAT MEANS
By convention 0 log 0 is taken as 0, justified by the limit.
Source: Digital Communication Systems, 1st ed., Ch. 5, pp. 207-214 | CO3 | Bloom L2
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Identify the probability p of the event - and check everyone has written it before moving on. At the cost panel, translate it: By convention 0 log 0 is taken as 0, justified by the limit. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 3: Information Theory. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 5, pp. 207-214. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 7
Information as surprise: the logarithmic measure - worked example
One concrete case, carried all the way to a stated number.
VTU BEC503 | Module 3
Information as surprise: the logarith…
07
GIVEN
A source emits A with probability 0.5, B with 0.25, C with 0.125, D with 0.125.
1. I(A) = log2(1/0.5) = 1 bit
2. I(B) = log2(1/0.25) = 2 bits
3. I(C) = I(D) = log2(1/0.125) = 3 bits
4. The sequence AB has information 1 + 2 = 3 bits if the symbols are independent
RESULT
Rare symbols carry more bits. This is precisely why a good code gives short descriptions to common symbols and long ones to rare symbols.
I(x_k) = log2( 1 / p_k ) = -log2( p_k ) bits
Properties:
I(x) = 0 when p = 1
I(x) -> infinity as p -> 0
I(x,y) = I(x)+I(y) for independent x, y
Units: log2 -> bits, ln -> nats, log10 -> hartleys
THE MISTAKE STUDENTS MAKE
Students take information to measure importance or meaning. It measures only improbability: a rare but useless reading carries more information than a common but critical one, and the theory is deliberately indifferent to which.
Source: Digital Communication Systems, 1st ed., Ch. 5, pp. 207-214 | CO3 | Bloom L2
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is A source emits A with probability 0.5, B with 0.25, C with 0.125, D with 0.125. Work at the pace of the slowest note-taker and land hard on the result: Rare symbols carry more bits. This is precisely why a good code gives short descriptions to common symbols and long ones to rare… Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 3: Information Theory. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 5, pp. 207-214. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 8
Entropy: the average information per symbol
What it is, why it works, and what it costs.
VTU BEC503 | Module 3
Entropy: the average information per…
08
THE MECHANISM
The entropy of a discrete memoryless source is H(X) = -sum over k of p_k log2(p_k), the expected value of the self-information over all symbols. It measures the average uncertainty per symbol and, by the source-coding theorem, the average number of bits per symbol any lossless code must use. Entropy depends only on the probability distribution, not on the symbol values, so a source emitting voltages and one emitting letters with the same probabilities have identical entropy. It is maximised when all symbols are equally likely and falls to zero when one symbol has probability one.
KEY TERMS
• entropy
• discrete memoryless source
• expectation
• binary entropy function
• uncertainty
TAKEAWAY
Entropy is average surprise, it depends only on the probabilities, and it is the floor for lossless compression.
DIAGRAM FOR PHASE 2
A plot of H(p) against p from 0 to 1, showing the symmetric cap-shaped binary entropy curve peaking at exactly 1 bit at p = 0.5 and touching zero at both p = 0 and p = 1. The peak is marked with a dot and labe…
Source: Digital Communication Systems, 1st ed., Ch. 5, pp. 207-214
CO3 | Bloom L3 | visual id: binary-entropy-function
Notes: What to say: Give them the idea before the formalism. Say it plainly first: The entropy of a discrete memoryless source is H(X) = -sum over k of p_k log2(p_k), the expected value of the self-information over all symbols. Then add the part they are examined on - Entropy is average surprise, it depends only on the probabilities, and it is the floor for lossless compression. Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "entropy" constrain here, and what would break if it did not hold? Animation instructions: the axes draw, then the curve rises from the left zero, peaks and falls to the right zero in a single sweep, then the peak marker drops with its label, then the two zero markers appear, then the three pie charts fade in left to right with their entropy values counting up beneath each. Transition style: Fade [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 3: Information Theory. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 5, pp. 207-214. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 9
Entropy: the average information per symbol - how it works
The procedure in order, and what each pass costs you.
VTU BEC503 | Module 3
Entropy: the average information per…
09
1. List every symbol and its probability
2. Compute p_k log2(p_k) for each symbol, taking 0 log 0 as 0
3. Sum the products and negate
4. Verify the result lies between 0 and log2(K) for K symbols
5. Check the extremes: uniform gives log2(K), deterministic gives 0
COST AND BEHAVIOUR
Best: zero entropy for a deterministic source
Typical: K logarithms and K multiplications for K symbols
Worst: log2(K) bits when the source is uniform
WHAT THAT MEANS
Real sources are far from uniform, which is what makes compression possible at all.
Source: Digital Communication Systems, 1st ed., Ch. 5, pp. 207-214 | CO3 | Bloom L3
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - List every symbol and its probability - and check everyone has written it before moving on. At the cost panel, translate it: Real sources are far from uniform, which is what makes compression possible at all. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 3: Information Theory. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 5, pp. 207-214. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 10
Entropy: the average information per symbol - worked example
One concrete case, carried all the way to a stated number.
VTU BEC503 | Module 3
Entropy: the average information per…
10
GIVEN
Source with probabilities 0.5, 0.25, 0.125, 0.125.
1. 0.5 x log2(2) = 0.5 x 1 = 0.5
2. 0.25 x log2(4) = 0.25 x 2 = 0.5
3. 0.125 x log2(8) = 0.125 x 3 = 0.375, twice
4. Sum: 0.5 + 0.5 + 0.375 + 0.375 = 1.75 bits per symbol
RESULT
H = 1.75 bits against log2(4) = 2 bits for a uniform four-symbol source. The 0.25 bit of slack is exactly what a compressor can recover.
H(X) = -sum_{k=1}^{K} p_k * log2(p_k) bits/symbol
Bounds: 0 <= H(X) <= log2(K)
H(X) = 0 iff one symbol has probability 1
H(X) = log2(K) iff all symbols are equally likely
Binary: H(p) = -p log2(p) - (1-p) log2(1-p)
THE MISTAKE STUDENTS MAKE
Students compute entropy per message rather than per symbol and then compare it against a per-symbol code length. Entropy as defined here is per source symbol; for a block of n independent symbols the entropy is n H(X).
Source: Digital Communication Systems, 1st ed., Ch. 5, pp. 207-214 | CO3 | Bloom L3
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is Source with probabilities 0.5, 0.25, 0.125, 0.125. Work at the pace of the slowest note-taker and land hard on the result: H = 1.75 bits against log2(4) = 2 bits for a uniform four-symbol source. The 0.25 bit of slack is exactly what a compressor can r… Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 3: Information Theory. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 5, pp. 207-214. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 11
Properties of entropy and the extension of a source
What it is, why it works, and what it costs.
VTU BEC503 | Module 3
Properties of entropy and the extensi…
11
THE MECHANISM
Entropy is bounded between zero and log2(K) for a K-symbol alphabet, reaching the upper bound only when all symbols are equally likely, and it is a concave function of the probability distribution. The nth extension of a discrete memoryless source treats blocks of n symbols as single super-symbols drawn from an alphabet of K^n, and its entropy is exactly n H(X) because the symbols are independent. This matters because coding blocks rather than individual symbols is how practical codes approach the entropy bound: the inefficiency of rounding a code length up to a whole number of bits is amortised over n symbols and shrinks as 1/n.
KEY TERMS
• entropy bounds
• source extension
• block entropy
• concavity
• equiprobable maximum
TAKEAWAY
Coding blocks of n symbols divides the rounding waste by n, which is how real codes creep up on the entropy bound.
DIAGRAM FOR PHASE 2
A bar chart with n on the horizontal axis at values 1, 2, 3, 4 and average code length per source symbol on the vertical. Four bars descend towards a horizontal dashed line labelled "H(X) = 1.75", each bar ann…
Source: Digital Communication Systems, 1st ed., Ch. 5, pp. 207-214
CO3 | Bloom L4 | visual id: source-extension-amortisation
Notes: What to say: Give them the idea before the formalism. Say it plainly first: Entropy is bounded between zero and log2(K) for a K-symbol alphabet, reaching the upper bound only when all symbols are equally likely, and it is a concav… Then add the part they are examined on - Coding blocks of n symbols divides the rounding waste by n, which is how real codes creep up on the entropy bound. Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "entropy bounds" constrain here, and what would break if it did not hold? Animation instructions: the dashed entropy line draws first, then the four bars grow upward from the baseline one at a time with their excess portions shaded, then the grouping strip animates above, boxing symbols into singles, then pairs, then triples, then the caption lands. Transition style: Fade [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 3: Information Theory. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 5, pp. 207-214. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 12
Properties of entropy and the extension of a source - how it works
The procedure in order, and what each pass costs you.
VTU BEC503 | Module 3
Properties of entropy and the extensi…
12
1. Confirm the source is memoryless so that block probabilities are products
2. Form the nth extension with alphabet size K^n
3. Compute the entropy of the extension: it equals n H(X)
4. Design a code for the extension rather than the original alphabet
5. Divide the resulting average length by n to get bits per source symbol
COST AND BEHAVIOUR
Best: n = 1 requires no grouping at all
Typical: excess over entropy falls as 1/n
Worst: alphabet size K^n grows exponentially, so the code table explodes
WHAT THAT MEANS
This exponential blow-up is why arithmetic coding, which avoids explicit tables, displaced block Huffman coding.
Source: Digital Communication Systems, 1st ed., Ch. 5, pp. 207-214 | CO3 | Bloom L4
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Confirm the source is memoryless so that block probabilities are products - and check everyone has written it before moving on. At the cost panel, translate it: This exponential blow-up is why arithmetic coding, which avoids explicit tables, displaced block Huffman coding. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 3: Information Theory. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 5, pp. 207-214. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 13
Properties of entropy and the extension of a source - worked example
One concrete case, carried all the way to a stated number.
VTU BEC503 | Module 3
Properties of entropy and the extensi…
13
GIVEN
Binary source with p = 0.9, so H = 0.469 bits.
1. n = 1: any binary code needs 1 bit per symbol, excess 0.531
2. n = 2: alphabet {AA, AB, BA, BB} with probabilities 0.81, 0.09, 0.09, 0.01
3. A Huffman code on those gives average length about 1.29 bits per pair, or 0.645 per symbol
4. n = 3 brings it down to roughly 0.533 per symbol
RESULT
Excess falls from 0.531 to 0.176 to 0.064 bits per symbol as n goes 1, 2, 3 — converging on the entropy from above, at the price of an alphabet growing 2, 4, 8.
Extension: X^n has alphabet size K^n
H(X^n) = n * H(X) for a memoryless source
Source coding theorem, block form:
H(X) <= L_n / n < H(X) + 1/n
L_n / n -> H(X) as n -> infinity
THE MISTAKE STUDENTS MAKE
Students apply H(X^n) = n H(X) to a source with memory. The relation depends on independence; for a source with memory the block entropy grows more slowly than linearly, which is exactly the redundancy that dictionary coders exploit.
Source: Digital Communication Systems, 1st ed., Ch. 5, pp. 207-214 | CO3 | Bloom L4
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is Binary source with p = 0.9, so H = 0.469 bits. Work at the pace of the slowest note-taker and land hard on the result: Excess falls from 0.531 to 0.176 to 0.064 bits per symbol as n goes 1, 2, 3 — converging on the entropy from above, at the price… Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 3: Information Theory. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 5, pp. 207-214. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 14
The source coding theorem
What it is, why it works, and what it costs.
VTU BEC503 | Module 3
The source coding theorem
14
THE MECHANISM
The Shannon source coding theorem states that for a discrete memoryless source of entropy H(X), the average code length L of any uniquely decodable code satisfies L >= H(X), and codes exist with L less than H(X) + 1. Entropy is therefore both a hard floor and an achievable target, which is what makes it the right definition of information content. The theorem is an existence result: it guarantees a code exists without constructing one, and the gap of up to one bit comes from the need to round code lengths to whole numbers. Coding the nth extension shrinks that gap to 1/n.
KEY TERMS
• source coding theorem
• average code length
• code efficiency
• lower bound
• lossless compression
TAKEAWAY
No lossless code beats entropy, and some code gets within one bit of it — a floor and a ceiling in one theorem.
DIAGRAM FOR PHASE 2
A horizontal number line representing average code length in bits per symbol. A solid vertical barrier stands at H(X) with the region to its left shaded red and labelled "impossible: no uniquely decodable code…
Source: Digital Communication Systems, 1st ed., Ch. 5, pp. 214-215
CO3 | Bloom L3 | visual id: source-coding-bounds
Notes: What to say: Give them the idea before the formalism. Say it plainly first: The Shannon source coding theorem states that for a discrete memoryless source of entropy H(X), the average code length L of any uniquely decodable code s… Then add the part they are examined on - No lossless code beats entropy, and some code gets within one bit of it — a floor and a ceiling in one theorem. Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "source coding theorem" constrain here, and what would break if it did not hold? Animation instructions: the number line draws, then the solid barrier rises at H(X) and the red region fills to its left, then the dashed line appears at H(X)+1, then the green band fills between them, then the Huffman marker drops in, then the arrow extends leftward with its annotation. Transition style: Fade [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 3: Information Theory. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 5, pp. 214-215. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 15
The source coding theorem - how it works
The procedure in order, and what each pass costs you.
VTU BEC503 | Module 3
The source coding theorem
15
1. Compute the source entropy H(X)
2. Design a uniquely decodable code and compute its average length L = sum p_k l_k
3. Verify L >= H(X); a violation means the code is not uniquely decodable
4. Compute efficiency as H(X)/L
5. If efficiency is unsatisfactory, code the nth extension instead
COST AND BEHAVIOUR
Best: efficiency 100% when all probabilities are negative powers of two
Typical: Huffman typically achieves 95% or better on real sources
Worst: a highly skewed binary source can lose over half a bit per symbol at n = 1
WHAT THAT MEANS
That worst case is exactly where arithmetic coding pays for itself.
Source: Digital Communication Systems, 1st ed., Ch. 5, pp. 214-215 | CO3 | Bloom L3
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Compute the source entropy H(X) - and check everyone has written it before moving on. At the cost panel, translate it: That worst case is exactly where arithmetic coding pays for itself. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 3: Information Theory. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 5, pp. 214-215. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 16
The source coding theorem - worked example
One concrete case, carried all the way to a stated number.
VTU BEC503 | Module 3
The source coding theorem
16
GIVEN
Source with probabilities 0.5, 0.25, 0.125, 0.125 and code lengths 1, 2, 3, 3.
1. L = 0.5(1) + 0.25(2) + 0.125(3) + 0.125(3) = 0.5 + 0.5 + 0.375 + 0.375
2. L = 1.75 bits per symbol
3. H(X) = 1.75 bits per symbol, computed earlier
4. Efficiency = 1.75/1.75 = 100%
RESULT
Perfect efficiency, because every probability is a negative power of two so every ideal length log2(1/p_k) is already a whole number.
L = sum_k p_k * l_k average code length
Source coding theorem:
H(X) <= L < H(X) + 1
Efficiency: eta = H(X) / L
Redundancy: 1 - eta
Ideal length: l_k = log2(1/p_k)
THE MISTAKE STUDENTS MAKE
Students find a code with L < H(X) and conclude the theorem is wrong. Such a code is never uniquely decodable — the Kraft inequality fails, so distinct message sequences share the same encoding.
Source: Digital Communication Systems, 1st ed., Ch. 5, pp. 214-215 | CO3 | Bloom L3
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is Source with probabilities 0.5, 0.25, 0.125, 0.125 and code lengths 1, 2, 3, 3. Work at the pace of the slowest note-taker and land hard on the result: Perfect efficiency, because every probability is a negative power of two so every ideal length log2(1/p_k) is already a whole num… Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 3: Information Theory. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 5, pp. 214-215. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 17
Prefix codes and the Kraft inequality
What it is, why it works, and what it costs.
VTU BEC503 | Module 3
Prefix codes and the Kraft inequality
17
THE MECHANISM
A prefix code is one in which no codeword is a prefix of any other, which makes decoding instantaneous: as soon as the received bits match a codeword, that codeword is complete and no lookahead is needed. Prefix codes correspond exactly to binary trees with codewords at the leaves, and a set of lengths l_k admits a prefix code if and only if the Kraft inequality sum of 2^(-l_k) <= 1 holds. The inequality has a direct interpretation: each codeword of length l claims a fraction 2^(-l) of the tree, and the claims cannot exceed the whole tree. Equality means the tree is full, with no wasted branches.
KEY TERMS
• prefix code
• instantaneous decoding
• Kraft inequality
• code tree
• unique decodability
TAKEAWAY
Kraft says code lengths compete for one unit of tree; a prefix code exists exactly when the claims fit.
DIAGRAM FOR PHASE 2
A binary tree drawn downward from a root, with left branches labelled 0 and right branches labelled 1. Four leaves are marked as codewords at depths 1, 2, 3, 3, each with its codeword string beneath. Internal…
Source: Digital Communication Systems, 1st ed., Ch. 5, pp. 215-223
CO3 | Bloom L4 | visual id: prefix-code-tree-budget
Notes: What to say: Give them the idea before the formalism. Say it plainly first: A prefix code is one in which no codeword is a prefix of any other, which makes decoding instantaneous: as soon as the received bits match a codeword, tha… Then add the part they are examined on - Kraft says code lengths compete for one unit of tree; a prefix code exists exactly when the claims fit. Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "prefix code" constrain here, and what would break if it did not hold? Animation instructions: the tree grows level by level from the root, then each leaf fills solid in depth order with its codeword appearing, then the budget bar draws empty, then its segments stack from the bottom one at a time matching the leaf order, then the crossed-out overflow segment appears above the full bar. Transition style: Fade [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 3: Information Theory. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 5, pp. 215-223. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 18
Prefix codes and the Kraft inequality - how it works
The procedure in order, and what each pass costs you.
VTU BEC503 | Module 3
Prefix codes and the Kraft inequality
18
1. List the desired code lengths l_1 .. l_K
2. Compute the Kraft sum: sum over k of 2^(-l_k)
3. If the sum exceeds 1, no prefix code with those lengths exists
4. If the sum is at most 1, assign codewords by walking a binary tree, shortest first
5. Mark each assigned node and all its descendants as unavailable
COST AND BEHAVIOUR
Best: Kraft sum exactly 1 means no wasted tree
Typical: assignment is a single pass over sorted lengths
Worst: a Kraft sum well below 1 signals lengths longer than necessary
WHAT THAT MEANS
Any uniquely decodable code also satisfies Kraft, so prefix codes lose nothing.
Source: Digital Communication Systems, 1st ed., Ch. 5, pp. 215-223 | CO3 | Bloom L4
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - List the desired code lengths l_1 .. l_K - and check everyone has written it before moving on. At the cost panel, translate it: Any uniquely decodable code also satisfies Kraft, so prefix codes lose nothing. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 3: Information Theory. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 5, pp. 215-223. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 19
Prefix codes and the Kraft inequality - worked example
One concrete case, carried all the way to a stated number.
VTU BEC503 | Module 3
Prefix codes and the Kraft inequality
19
GIVEN
Proposed lengths 1, 2, 3, 3.
1. 2^-1 + 2^-2 + 2^-3 + 2^-3
2. = 0.5 + 0.25 + 0.125 + 0.125
3. = 1.0 exactly
4. A prefix code exists and the tree is full: 0, 10, 110, 111
RESULT
Kraft sum is exactly 1, so the code fits perfectly with no spare branches. Adding any fifth codeword is impossible without lengthening an existing one.
Prefix condition: no codeword is a prefix of another
Kraft inequality: sum_k 2^(-l_k) <= 1
Equality => full tree, no unused leaves
Example: lengths 1,2,3,3 -> 0, 10, 110, 111
Kraft sum = 0.5+0.25+0.125+0.125 = 1
THE MISTAKE STUDENTS MAKE
Students treat the Kraft inequality as a test for optimality. It only tests existence: a wildly inefficient code with lengths 5, 5, 5, 5 also satisfies it comfortably while wasting more than three bits per symbol.
Source: Digital Communication Systems, 1st ed., Ch. 5, pp. 215-223 | CO3 | Bloom L4
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is Proposed lengths 1, 2, 3, 3. Work at the pace of the slowest note-taker and land hard on the result: Kraft sum is exactly 1, so the code fits perfectly with no spare branches. Adding any fifth codeword is impossible without length… Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 3: Information Theory. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 5, pp. 215-223. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 20
Huffman coding
What it is, why it works, and what it costs.
VTU BEC503 | Module 3
Huffman coding
20
THE MECHANISM
Huffman coding constructs an optimal prefix code by repeatedly merging the two least probable symbols into a composite symbol whose probability is their sum, until one symbol remains. Reading the resulting binary tree from the root to each leaf yields the codewords, and the construction is provably optimal: no other prefix code has a smaller average length for the same distribution. Its weakness is granularity — code lengths must be whole numbers of bits, so a symbol of probability 0.9 that ideally deserves 0.152 bits still gets a full bit. Ties in the merge order produce different trees with identical average length.
KEY TERMS
• Huffman code
• greedy merge
• optimal prefix code
• code tree construction
• tie breaking
TAKEAWAY
Huffman is optimal among prefix codes, and its only loss is the rounding of ideal lengths to whole bits.
DIAGRAM FOR PHASE 2
A construction diagram flowing bottom to top. Four leaf boxes at the bottom carry probabilities 0.4, 0.3, 0.2, 0.1. The two smallest, 0.2 and 0.1, are joined by lines rising to a node labelled 0.3, with the br…
Source: Digital Communication Systems, 1st ed., Ch. 5, pp. 215-223
CO3 | Bloom L4 | visual id: huffman-merge-tree
Notes: What to say: Give them the idea before the formalism. Say it plainly first: Huffman coding constructs an optimal prefix code by repeatedly merging the two least probable symbols into a composite symbol whose probability is their s… Then add the part they are examined on - Huffman is optimal among prefix codes, and its only loss is the rounding of ideal lengths to whole bits. Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "Huffman code" constrain here, and what would break if it did not hold? Animation instructions: the four leaves appear along the bottom, then merge 1 draws its two rising lines and its node, then merge 2, then merge 3 up to the root, then branch labels 0 and 1 appear along every edge together, then the table fills row by row and the average length and entropy values land last. Transition style: Fade [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 3: Information Theory. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 5, pp. 215-223. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 21
Huffman coding - how it works
The procedure in order, and what each pass costs you.
VTU BEC503 | Module 3
Huffman coding
21
1. List all symbols with their probabilities
2. Merge the two least probable into a node with the sum of their probabilities
3. Insert the merged node back into the list
4. Repeat until a single node of probability 1 remains
5. Label branches 0 and 1 and read codewords from the root down to each leaf
COST AND BEHAVIOUR
Best: O(K log K) with a priority queue
Typical: optimal average length among all prefix codes
Worst: up to one bit per symbol above entropy for skewed sources
WHAT THAT MEANS
Coding the nth extension reduces that excess to 1/n at the cost of a K^n table.
Source: Digital Communication Systems, 1st ed., Ch. 5, pp. 215-223 | CO3 | Bloom L4
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - List all symbols with their probabilities - and check everyone has written it before moving on. At the cost panel, translate it: Coding the nth extension reduces that excess to 1/n at the cost of a K^n table. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 3: Information Theory. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 5, pp. 215-223. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 22
Huffman coding - worked example
One concrete case, carried all the way to a stated number.
VTU BEC503 | Module 3
Huffman coding
22
GIVEN
Probabilities A 0.4, B 0.3, C 0.2, D 0.1.
1. Merge C 0.2 and D 0.1 into CD 0.3
2. Merge B 0.3 and CD 0.3 into BCD 0.6
3. Merge A 0.4 and BCD 0.6 into the root 1.0
4. Codewords: A 0, B 10, C 110, D 111
RESULT
L = 0.4(1) + 0.3(2) + 0.2(3) + 0.1(3) = 1.9 bits against H = 1.846 bits, an efficiency of 97.2%.
while more than one node remains:
take the two smallest probabilities p_i, p_j
create parent with probability p_i + p_j
label the two branches 0 and 1
Codeword(symbol) = branch labels from root to its leaf
Optimal: no prefix code has smaller L for the same p
Bounded: H(X) <= L < H(X) + 1
THE MISTAKE STUDENTS MAKE
Students assign 0 and 1 arbitrarily and then read codewords from leaf to root. The codeword is read root to leaf; reversing it breaks the prefix property in general and produces a code that cannot be decoded.
Source: Digital Communication Systems, 1st ed., Ch. 5, pp. 215-223 | CO3 | Bloom L4
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is Probabilities A 0.4, B 0.3, C 0.2, D 0.1. Work at the pace of the slowest note-taker and land hard on the result: L = 0.4(1) + 0.3(2) + 0.2(3) + 0.1(3) = 1.9 bits against H = 1.846 bits, an efficiency of 97.2%. Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 3: Information Theory. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 5, pp. 215-223. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 23
Lempel-Ziv coding and the case for dictionary methods
What it is, why it works, and what it costs.
VTU BEC503 | Module 3
Lempel-Ziv coding and the case for di…
23
THE MECHANISM
Lempel-Ziv coding builds a dictionary of previously seen phrases as it reads the source, encoding each new phrase as a pointer to the longest matching earlier phrase plus one new symbol. It requires no prior knowledge of the source statistics, which makes it universal: it approaches the entropy rate of any stationary ergodic source as the sequence length grows. Its decisive advantage over Huffman is that it exploits memory — repeated patterns become single pointers regardless of individual symbol probabilities — which is why it underlies gzip, PNG and the compress utility while Huffman appears mostly as a back-end.
KEY TERMS
• Lempel-Ziv
• dictionary coding
• universal code
• source with memory
• adaptive compression
TAKEAWAY
Huffman needs the statistics and ignores memory; Lempel-Ziv learns as it goes and captures repetition, which is where real redundancy lives.
DIAGRAM FOR PHASE 2
A horizontal input string of bits shown as a tape at the top, with a moving parse marker. Beneath, a growing dictionary table with columns index, phrase and encoding, filling row by row as the parse advances.…
Source: Digital Communication Systems, 1st ed., Ch. 5, pp. 215-223
CO3 | Bloom L4 | visual id: lempel-ziv-dictionary-build
Notes: What to say: Give them the idea before the formalism. Say it plainly first: Lempel-Ziv coding builds a dictionary of previously seen phrases as it reads the source, encoding each new phrase as a pointer to the longest matching ear… Then add the part they are examined on - Huffman needs the statistics and ignores memory; Lempel-Ziv learns as it goes and captures repetition, which is where real r… Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "Lempel-Ziv" constrain here, and what would break if it did not hold? Animation instructions: the input tape draws, then the parse marker steps left to right pausing at each phrase boundary, boxing the phrase and adding the matching dictionary row with a connecting arrow, four times in sequence, then the side panel bars slide in from the right one after the other. Transition style: Fade [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 3: Information Theory. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 5, pp. 215-223. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 24
Lempel-Ziv coding and the case for dictionary methods - how it works
The procedure in order, and what each pass costs you.
VTU BEC503 | Module 3
Lempel-Ziv coding and the case for di…
24
1. Initialise the dictionary with the single-symbol phrases
2. Parse the input for the longest phrase already in the dictionary
3. Emit the index of that phrase followed by the next input symbol
4. Add the extended phrase to the dictionary as a new entry
5. Continue until the input is exhausted; the decoder rebuilds the same dictionary
COST AND BEHAVIOUR
Best: highly repetitive data compresses enormously
Typical: approaches the entropy rate for any stationary ergodic source
Worst: random incompressible data expands slightly because of pointer overhead
WHAT THAT MEANS
The decoder needs no transmitted dictionary: it reconstructs the same one from the decoded output.
Source: Digital Communication Systems, 1st ed., Ch. 5, pp. 215-223 | CO3 | Bloom L4
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Initialise the dictionary with the single-symbol phrases - and check everyone has written it before moving on. At the cost panel, translate it: The decoder needs no transmitted dictionary: it reconstructs the same one from the decoded output. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 3: Information Theory. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 5, pp. 215-223. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 25
Lempel-Ziv coding and the case for dictionary methods - worked example
One concrete case, carried all the way to a stated number.
VTU BEC503 | Module 3
Lempel-Ziv coding and the case for di…
25
GIVEN
The sequence 0 0 0 1 0 1 1 1 0 0 1 0.
1. Parse 0, not yet in the dictionary beyond the initial entries: phrase 1 = 0
2. Parse 00, extend phrase 1: phrase 2 = 00, encoded as (1, 0)
3. Parse 1: phrase 3 = 1
4. Parse 01, extend phrase 1 with 1: phrase 4 = 01, encoded as (1, 1)
RESULT
Repeated substrings collapse into short pointers. On this twelve-bit toy input the overhead dominates, but on a megabyte of text the same mechanism typically halves the size.
dictionary = { single symbols }
while input remains:
find longest prefix P of input already in dictionary
let c = next symbol after P
emit ( index(P), c )
dictionary.add( P + c )
Universal: no source statistics required in advance.
THE MISTAKE STUDENTS MAKE
Students expect Lempel-Ziv to beat Huffman on a memoryless source. On a genuinely memoryless source there is no repetition to exploit, so Huffman with known statistics wins; Lempel-Ziv pays pointer overhead for nothing.
Source: Digital Communication Systems, 1st ed., Ch. 5, pp. 215-223 | CO3 | Bloom L4
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is The sequence 0 0 0 1 0 1 1 1 0 0 1 0. Work at the pace of the slowest note-taker and land hard on the result: Repeated substrings collapse into short pointers. On this twelve-bit toy input the overhead dominates, but on a megabyte of text… Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 3: Information Theory. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 5, pp. 215-223. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 26
Code efficiency, redundancy and where compression stops
What it is, why it works, and what it costs.
VTU BEC503 | Module 3
Code efficiency, redundancy and where…
26
THE MECHANISM
Code efficiency is the ratio H(X)/L and redundancy is one minus that, both dimensionless and both bounded by one. A high efficiency means the code is close to the entropy floor, but average length is not the only design criterion: the variance of the code length matters too, because a variable-length code feeding a fixed-rate channel requires a buffer, and the buffer size is driven by the variance rather than the mean. Two Huffman codes can have identical average length and very different variance, which is why the tie-breaking rule in the merge step is not arbitrary in practice.
KEY TERMS
• efficiency
• redundancy
• variance of code length
• buffering
• compression ratio
TAKEAWAY
Efficiency measures the mean; buffer size is set by the variance, so two codes with the same average length are not equally usable.
DIAGRAM FOR PHASE 2
Two Huffman trees drawn side by side, both for the same probability set and both annotated "L = 2.2 bits". The left tree is balanced with lengths 2,2,2,3,3 and the right is skewed with lengths 1,2,3,4,4. Benea…
Source: Digital Communication Systems, 1st ed., Ch. 5, pp. 215-223
CO3 | Bloom L4 | visual id: efficiency-and-variance
Notes: What to say: Give them the idea before the formalism. Say it plainly first: Code efficiency is the ratio H(X)/L and redundancy is one minus that, both dimensionless and both bounded by one. Then add the part they are examined on - Efficiency measures the mean; buffer size is set by the variance, so two codes with the same average length are not equally… Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "efficiency" constrain here, and what would break if it did not hold? Animation instructions: both trees draw simultaneously branch by branch, then the two average-length labels land together, then the two histograms grow beneath, then the two buffer diagrams fill with the right one visibly overflowing further, then the caption appears. Transition style: Fade [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 3: Information Theory. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 5, pp. 215-223. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 27
Code efficiency, redundancy and where compression stops - how it works
The procedure in order, and what each pass costs you.
VTU BEC503 | Module 3
Code efficiency, redundancy and where…
27
1. Compute the average length L and the entropy H(X)
2. Efficiency is H(X)/L; redundancy is 1 minus that
3. Compute the variance of code length: sum p_k (l_k - L)^2
4. Size the transmit buffer from the variance, not the mean
5. Prefer the tie-breaking that minimises variance when average lengths are equal
COST AND BEHAVIOUR
Best: efficiency 1 with zero variance when all lengths are equal and optimal
Typical: real sources reach 90 to 99% efficiency with Huffman
Worst: high variance forces a large buffer and adds latency
WHAT THAT MEANS
Buffer overflow, not compression ratio, is what usually breaks a variable-length link.
Source: Digital Communication Systems, 1st ed., Ch. 5, pp. 215-223 | CO3 | Bloom L4
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Compute the average length L and the entropy H(X) - and check everyone has written it before moving on. At the cost panel, translate it: Buffer overflow, not compression ratio, is what usually breaks a variable-length link. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 3: Information Theory. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 5, pp. 215-223. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 28
Code efficiency, redundancy and where compression stops - worked example
One concrete case, carried all the way to a stated number.
VTU BEC503 | Module 3
Code efficiency, redundancy and where…
28
GIVEN
Code with lengths 1, 2, 3, 3 and probabilities 0.5, 0.25, 0.125, 0.125, so L = 1.75 and H = 1.75.
1. Efficiency = 1.75/1.75 = 100%
2. Variance = 0.5(1-1.75)^2 + 0.25(2-1.75)^2 + 0.125(3-1.75)^2 x 2
3. = 0.5(0.5625) + 0.25(0.0625) + 0.25(1.5625)
4. = 0.281 + 0.016 + 0.391 = 0.688
RESULT
Perfect efficiency but a length variance of 0.688, so the transmit buffer must absorb runs of long codewords even though the average is exactly at the entropy.
Efficiency: eta = H(X) / L
Redundancy: R = 1 - eta
Variance: sigma^2 = sum_k p_k * (l_k - L)^2
Compression ratio = original bits / compressed bits
Buffer sizing is driven by sigma^2, not by L.
THE MISTAKE STUDENTS MAKE
Students report a compression ratio without stating the original representation. Compressing an eight-bit-per-symbol file to two bits gives a ratio of 4, but if the source entropy is 1.9 bits the code is still 5% off optimal — the ratio flatters the code.
Source: Digital Communication Systems, 1st ed., Ch. 5, pp. 215-223 | CO3 | Bloom L4
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is Code with lengths 1, 2, 3, 3 and probabilities 0.5, 0.25, 0.125, 0.125, so L = 1.75 and H = 1.75. Work at the pace of the slowest note-taker and land hard on the result: Perfect efficiency but a length variance of 0.688, so the transmit buffer must absorb runs of long codewords even though the aver… Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 3: Information Theory. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 5, pp. 215-223. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 29
Discrete memoryless channels and the transition matrix
What it is, why it works, and what it costs.
VTU BEC503 | Module 3
Discrete memoryless channels and the…
29
THE MECHANISM
A discrete memoryless channel is specified by an input alphabet, an output alphabet and a matrix of transition probabilities p(y_j | x_k), the probability of observing output j given input k. Memoryless means each output depends only on the current input, not on any previous one, so the matrix fully describes the channel. Every row sums to one because some output must occur. The channel matrix, together with the input distribution chosen by the transmitter, determines everything about the channel, including its capacity — and the split matters, because the matrix is imposed by physics while the input distribution is a design choice.
KEY TERMS
• discrete memoryless channel
• transition probability
• channel matrix
• input alphabet
• output alphabet
TAKEAWAY
The channel matrix is given by nature; the input distribution is yours to choose, and capacity is the best you can do with that one choice.
DIAGRAM FOR PHASE 2
A bipartite diagram with input symbols x1, x2 as filled circles on the left and output symbols y1, y2 as circles on the right. Four arrows connect every input to every output, the two horizontal ones drawn thi…
Source: Digital Communication Systems, 1st ed., Ch. 5, pp. 223-226
CO3 | Bloom L3 | visual id: dmc-transition-graph
Notes: What to say: Give them the idea before the formalism. Say it plainly first: A discrete memoryless channel is specified by an input alphabet, an output alphabet and a matrix of transition probabilities p(y_j | x_k), the probability… Then add the part they are examined on - The channel matrix is given by nature; the input distribution is yours to choose, and capacity is the best you can do with t… Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "discrete memoryless channel" constrain here, and what would break if it did not hold? Animation instructions: the input and output circles appear, then the two thick correct-transition arrows draw with their labels, then the two thin crossover arrows draw in red, then the matrix writes itself row by row, then the row-sum note lands, then the side card slides in with its arrow drawing last. Transition style: Fade [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 3: Information Theory. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 5, pp. 223-226. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 30
Discrete memoryless channels and the transition matrix - how it works
The procedure in order, and what each pass costs you.
VTU BEC503 | Module 3
Discrete memoryless channels and the…
30
1. Enumerate the input alphabet and the output alphabet
2. Fill the matrix entry p(y_j | x_k) for every input-output pair
3. Verify each row sums to one
4. Combine with an input distribution p(x_k) to get joint probabilities
5. Marginalise to obtain the output distribution p(y_j)
COST AND BEHAVIOUR
Best: noiseless channel has an identity matrix
Typical: K x J entries for K inputs and J outputs
Worst: a useless channel has identical rows, making the output independent of the input
WHAT THAT MEANS
Identical rows mean zero mutual information for every input distribution, hence zero capacity.
Source: Digital Communication Systems, 1st ed., Ch. 5, pp. 223-226 | CO3 | Bloom L3
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Enumerate the input alphabet and the output alphabet - and check everyone has written it before moving on. At the cost panel, translate it: Identical rows mean zero mutual information for every input distribution, hence zero capacity. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 3: Information Theory. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 5, pp. 223-226. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 31
Discrete memoryless channels and the transition matrix - worked example
One concrete case, carried all the way to a stated number.
VTU BEC503 | Module 3
Discrete memoryless channels and the…
31
GIVEN
Binary symmetric channel with crossover probability p = 0.1 and equally likely inputs.
1. Matrix rows: [0.9, 0.1] and [0.1, 0.9]
2. Joint probabilities: 0.45, 0.05, 0.05, 0.45
3. Output marginals: p(y=0) = 0.45 + 0.05 = 0.5, p(y=1) = 0.5
4. Outputs are equally likely even though the channel is noisy
RESULT
A uniform input gives a uniform output on a symmetric channel. The output distribution alone reveals nothing about the noise — the mutual information is what does.
Channel: p(y_j | x_k), j = 1..J, k = 1..K
sum_j p(y_j | x_k) = 1 for every k
Joint: p(x_k, y_j) = p(x_k) * p(y_j | x_k)
Marginal: p(y_j) = sum_k p(x_k) * p(y_j | x_k)
BSC: [[1-p, p], [p, 1-p]]
THE MISTAKE STUDENTS MAKE
Students confuse p(y|x) with p(x|y). The channel matrix holds forward probabilities, from input to output; the receiver needs the reverse, which requires Bayes and therefore the input distribution as well.
Source: Digital Communication Systems, 1st ed., Ch. 5, pp. 223-226 | CO3 | Bloom L3
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is Binary symmetric channel with crossover probability p = 0.1 and equally likely inputs. Work at the pace of the slowest note-taker and land hard on the result: A uniform input gives a uniform output on a symmetric channel. The output distribution alone reveals nothing about the noise — th… Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 3: Information Theory. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 5, pp. 223-226. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 32
The binary symmetric and binary erasure channels
What it is, why it works, and what it costs.
VTU BEC503 | Module 3
The binary symmetric and binary erasu…
32
THE MECHANISM
The binary symmetric channel flips each bit independently with probability p, so an error is undetectable at the receiver — a received 1 might be a transmitted 1 or a flipped 0. The binary erasure channel instead replaces each bit with an erasure symbol with probability epsilon, so the receiver always knows which bits it lost. This difference is decisive: knowing where the damage is worth a great deal, and the BEC has capacity 1 - epsilon while the BSC has the much smaller 1 - H(p). At the same probability of disturbance, the erasure channel carries substantially more information.
KEY TERMS
• BSC
• BEC
• crossover probability
• erasure probability
• channel comparison
TAKEAWAY
Knowing which bits are damaged is worth more than the bits themselves; the BEC beats the BSC at the same disturbance probability.
DIAGRAM FOR PHASE 2
Two bipartite channel diagrams side by side. Left, the BSC: two inputs, two outputs, crossing arrows labelled p in red. Right, the BEC: two inputs, three outputs including a middle one drawn as a question mark…
Source: Digital Communication Systems, 1st ed., Ch. 5, pp. 223-226
CO3 | Bloom L4 | visual id: bsc-versus-bec
Notes: What to say: Give them the idea before the formalism. Say it plainly first: The binary symmetric channel flips each bit independently with probability p, so an error is undetectable at the receiver — a received 1 might be a transm… Then add the part they are examined on - Knowing which bits are damaged is worth more than the bits themselves; the BEC beats the BSC at the same disturbance probabi… Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "BSC" constrain here, and what would break if it did not hold? Animation instructions: both diagrams draw their inputs and outputs together, then the BSC crossing arrows appear in red, then the BEC erasure arrows appear in amber with the question-mark node, then the shared plot axes draw, then the BEC line sweeps down, then the BSC curve sweeps down beneath it, then the gap bracket snaps in at p = 0.1. Transition style: Fade [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 3: Information Theory. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 5, pp. 223-226. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 33
The binary symmetric and binary erasure channels - how it works
The procedure in order, and what each pass costs you.
VTU BEC503 | Module 3
The binary symmetric and binary erasu…
33
1. Identify whether the receiver can tell that a symbol was corrupted
2. If corruption is silent, model as a BSC with crossover p
3. If corruption is flagged, model as a BEC with erasure probability epsilon
4. Compute capacity: 1 - H(p) for the BSC, 1 - epsilon for the BEC
5. Prefer a physical layer that flags its failures, since flagged loss is cheaper to code against
COST AND BEHAVIOUR
Best: BEC capacity falls only linearly with the erasure rate
Typical: BSC capacity falls with the binary entropy function, much faster
Worst: BSC at p = 0.5 has zero capacity: the output is independent of the input
WHAT THAT MEANS
A BSC with p = 0.9 is fine — just invert every bit; p = 0.5 is the only truly useless case.
Source: Digital Communication Systems, 1st ed., Ch. 5, pp. 223-226 | CO3 | Bloom L4
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Identify whether the receiver can tell that a symbol was corrupted - and check everyone has written it before moving on. At the cost panel, translate it: A BSC with p = 0.9 is fine — just invert every bit; p = 0.5 is the only truly useless case. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 3: Information Theory. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 5, pp. 223-226. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 34
The binary symmetric and binary erasure channels - worked example
One concrete case, carried all the way to a stated number.
VTU BEC503 | Module 3
The binary symmetric and binary erasu…
34
GIVEN
Compare a BSC with p = 0.1 against a BEC with epsilon = 0.1.
1. H(0.1) = -0.1 log2(0.1) - 0.9 log2(0.9) = 0.332 + 0.137 = 0.469
2. BSC capacity: 1 - 0.469 = 0.531 bits per use
3. BEC capacity: 1 - 0.1 = 0.9 bits per use
4. Ratio: the BEC carries 1.70 times as much
RESULT
At the same 10% disturbance rate the erasure channel carries 70% more information, purely because the receiver knows where the damage is.
BSC: p(y != x) = p
C = 1 - H(p) bits per channel use
H(p) = -p log2 p - (1-p) log2 (1-p)
BEC: p(y = erasure) = epsilon, no bit errors
C = 1 - epsilon
At p = epsilon = 0.1: C_BSC = 0.531, C_BEC = 0.9
THE MISTAKE STUDENTS MAKE
Students say a BSC with p = 0.9 is worse than one with p = 0.5. It is far better: simply invert every received bit and it becomes a BSC with p = 0.1. Capacity is symmetric about p = 0.5, which is the single worst value.
Source: Digital Communication Systems, 1st ed., Ch. 5, pp. 223-226 | CO3 | Bloom L4
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is Compare a BSC with p = 0.1 against a BEC with epsilon = 0.1. Work at the pace of the slowest note-taker and land hard on the result: At the same 10% disturbance rate the erasure channel carries 70% more information, purely because the receiver knows where the da… Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 3: Information Theory. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 5, pp. 223-226. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 35
Mutual information: what the output tells you about the input
What it is, why it works, and what it costs.
VTU BEC503 | Module 3
Mutual information: what the output t…
35
THE MECHANISM
Mutual information I(X;Y) = H(X) - H(X|Y) is the reduction in uncertainty about the input achieved by observing the output. The subtracted term H(X|Y), called the equivocation, is the uncertainty that remains after the observation, and it is exactly the information the channel destroys. Mutual information is symmetric, so it equals H(Y) - H(Y|X) as well, and it is zero precisely when input and output are independent — a channel that tells you nothing. It is never negative: observing the output can never increase your uncertainty about the input, however noisy the channel.
KEY TERMS
• mutual information
• conditional entropy
• equivocation
• uncertainty reduction
• joint entropy
TAKEAWAY
Mutual information is what survives the channel: total uncertainty minus what remains after looking at the output.
DIAGRAM FOR PHASE 2
Two overlapping circles on a plain background, the left labelled H(X) and the right H(Y). The lens-shaped intersection is shaded solid and labelled "I(X;Y)". The left crescent is labelled "H(X|Y), equivocation…
Source: Digital Communication Systems, 1st ed., Ch. 5, pp. 226-230
CO3 | Bloom L4 | visual id: mutual-information-venn
Notes: What to say: Give them the idea before the formalism. Say it plainly first: Mutual information I(X;Y) = H(X) - H(X|Y) is the reduction in uncertainty about the input achieved by observing the output. Then add the part they are examined on - Mutual information is what survives the channel: total uncertainty minus what remains after looking at the output. Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "mutual information" constrain here, and what would break if it did not hold? Animation instructions: the left circle draws, then the right circle draws overlapping it, then the intersection shades and its label lands, then the two crescents are labelled in turn, then the union bracket sweeps beneath, then the two small insets fade in side by side. Transition style: Fade [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 3: Information Theory. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 5, pp. 226-230. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 36
Mutual information: what the output tells you about the… - how it works
The procedure in order, and what each pass costs you.
VTU BEC503 | Module 3
Mutual information: what the output t…
36
1. Compute H(X) from the input distribution
2. Compute the joint distribution p(x,y) from the input and the channel matrix
3. Compute H(X|Y) by averaging the conditional entropies over the output distribution
4. Subtract: I(X;Y) = H(X) - H(X|Y)
5. Cross-check with the symmetric form H(Y) - H(Y|X)
COST AND BEHAVIOUR
Best: noiseless channel gives I = H(X), nothing lost
Typical: requires the full joint distribution
Worst: useless channel gives I = 0 for every input distribution
WHAT THAT MEANS
Mutual information is a function of both the channel and the input distribution; only maximising over inputs gives capacity.
Source: Digital Communication Systems, 1st ed., Ch. 5, pp. 226-230 | CO3 | Bloom L4
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Compute H(X) from the input distribution - and check everyone has written it before moving on. At the cost panel, translate it: Mutual information is a function of both the channel and the input distribution; only maximising over inputs gives capacity. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 3: Information Theory. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 5, pp. 226-230. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 37
Mutual information: what the output tells you about the… - worked example
One concrete case, carried all the way to a stated number.
VTU BEC503 | Module 3
Mutual information: what the output t…
37
GIVEN
BSC with p = 0.1 and equally likely inputs.
1. H(X) = 1 bit since inputs are equiprobable
2. H(Y|X) = H(0.1) = 0.469 bits, the same for either input
3. H(Y) = 1 bit since the output is also equiprobable
4. I(X;Y) = H(Y) - H(Y|X) = 1 - 0.469 = 0.531 bits
RESULT
0.531 bits survive per channel use. The equivocation of 0.469 bits is precisely what channel coding in Module 4 sets out to recover.
I(X;Y) = H(X) - H(X|Y)
= H(Y) - H(Y|X)
= H(X) + H(Y) - H(X,Y)
Properties:
I(X;Y) >= 0
I(X;Y) = 0 iff X and Y are independent
I(X;Y) = I(Y;X)
THE MISTAKE STUDENTS MAKE
Students compute H(X) - H(Y) instead of H(X) - H(X|Y). The first is a difference of two marginal entropies and can be negative, which mutual information never is.
Source: Digital Communication Systems, 1st ed., Ch. 5, pp. 226-230 | CO3 | Bloom L4
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is BSC with p = 0.1 and equally likely inputs. Work at the pace of the slowest note-taker and land hard on the result: 0.531 bits survive per channel use. The equivocation of 0.469 bits is precisely what channel coding in Module 4 sets out to recov… Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 3: Information Theory. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 5, pp. 226-230. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 38
Properties of mutual information
What it is, why it works, and what it costs.
VTU BEC503 | Module 3
Properties of mutual information
38
THE MECHANISM
Mutual information is non-negative, symmetric in its two arguments, and concave in the input distribution for a fixed channel — the last property is what guarantees that maximising it over input distributions has a single global maximum rather than a landscape of local ones. It also obeys the data processing inequality: if X, Y and Z form a Markov chain, then I(X;Z) <= I(X;Y), meaning no amount of post-processing at the receiver can create information that the channel did not deliver. That inequality is the formal reason a clever decoder cannot beat channel capacity, only approach it.
KEY TERMS
• non-negativity
• symmetry
• concavity
• data processing inequality
• independence
TAKEAWAY
Concavity makes capacity computable; the data processing inequality makes it unbeatable by any amount of receiver cleverness.
DIAGRAM FOR PHASE 2
A left-to-right chain of three labelled boxes X, Y, Z joined by two arrows, the first labelled "channel" and the second "any processing". Above the chain, two brackets span the pairs: a wide one from X to Z la…
Source: Digital Communication Systems, 1st ed., Ch. 5, pp. 226-230
CO3 | Bloom L4 | visual id: data-processing-chain
Notes: What to say: Give them the idea before the formalism. Say it plainly first: Mutual information is non-negative, symmetric in its two arguments, and concave in the input distribution for a fixed channel — the last property is what… Then add the part they are examined on - Concavity makes capacity computable; the data processing inequality makes it unbeatable by any amount of receiver cleverness. Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "non-negativity" constrain here, and what would break if it did not hold? Animation instructions: the three boxes appear left to right with their arrows, then the I(X;Y) bracket draws, then the I(X;Z) bracket draws above it, then the inequality sign appears between them and pulses, then the concavity plot axes draw and the curve sweeps up and over, then the peak marker drops with its caption. Transition style: Fade [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 3: Information Theory. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 5, pp. 226-230. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 39
Properties of mutual information - how it works
The procedure in order, and what each pass costs you.
VTU BEC503 | Module 3
Properties of mutual information
39
1. Verify non-negativity: I(X;Y) >= 0 with equality only for independence
2. Verify symmetry: I(X;Y) = I(Y;X)
3. Use concavity in p(x) to justify a single-maximum search for capacity
4. Apply the data processing inequality to any receiver post-processing stage
5. Conclude that no decoder can exceed the mutual information the channel delivers
COST AND BEHAVIOUR
Best: symmetry halves the work in many derivations
Typical: concavity permits standard convex optimisation for capacity
Worst: the maximisation has no closed form for a general asymmetric channel
WHAT THAT MEANS
The Blahut-Arimoto algorithm computes capacity numerically for arbitrary channel matrices.
Source: Digital Communication Systems, 1st ed., Ch. 5, pp. 226-230 | CO3 | Bloom L4
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Verify non-negativity: I(X;Y) >= 0 with equality only for independence - and check everyone has written it before moving on. At the cost panel, translate it: The Blahut-Arimoto algorithm computes capacity numerically for arbitrary channel matrices. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 3: Information Theory. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 5, pp. 226-230. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 40
Properties of mutual information - worked example
One concrete case, carried all the way to a stated number.
VTU BEC503 | Module 3
Properties of mutual information
40
GIVEN
A BSC with p = 0.1 followed by a receiver that simply inverts every bit.
1. I(X;Y) across the channel = 0.531 bits
2. The inversion is a deterministic function, so X -> Y -> Z is a Markov chain
3. Data processing gives I(X;Z) <= 0.531
4. Here inversion is invertible, so equality holds: I(X;Z) = 0.531
RESULT
A reversible operation preserves information exactly; any irreversible one, such as quantising the output more coarsely, strictly loses some.
Non-negativity: I(X;Y) >= 0
Symmetry: I(X;Y) = I(Y;X)
Concavity: I is concave in p(x) for fixed p(y|x)
Data processing: if X -> Y -> Z is a Markov chain
then I(X;Z) <= I(X;Y)
Equality iff the processing is invertible.
THE MISTAKE STUDENTS MAKE
Students apply the data processing inequality in the wrong direction and conclude a better decoder can raise capacity. Post-processing can only preserve or destroy information; capacity is fixed by the channel and the input distribution alone.
Source: Digital Communication Systems, 1st ed., Ch. 5, pp. 226-230 | CO3 | Bloom L4
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is A BSC with p = 0.1 followed by a receiver that simply inverts every bit. Work at the pace of the slowest note-taker and land hard on the result: A reversible operation preserves information exactly; any irreversible one, such as quantising the output more coarsely, strictly… Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 3: Information Theory. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 5, pp. 226-230. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 41
Channel capacity
What it is, why it works, and what it costs.
VTU BEC503 | Module 3
Channel capacity
41
THE MECHANISM
Channel capacity is C = max over p(x) of I(X;Y), the largest mutual information achievable by any choice of input distribution, measured in bits per channel use. The maximisation is over the transmitter design space, since the channel matrix itself is fixed by physics, and concavity guarantees a unique maximum. For symmetric channels the maximising distribution is uniform, which makes the calculation easy; for asymmetric channels it generally is not, and numerical methods are required. Capacity is a property of the channel alone, and it is the ceiling every coding scheme in the remaining modules is trying to approach.
KEY TERMS
• channel capacity
• maximisation over inputs
• bits per channel use
• symmetric channel
• optimal input distribution
TAKEAWAY
Capacity is the best mutual information over all input distributions — a property of the channel, not of any code.
DIAGRAM FOR PHASE 2
A plot of mutual information against the input probability p(x=0) from 0 to 1 for a BSC with p = 0.1. The curve is a symmetric cap peaking at exactly 0.5 with value 0.531, the peak marked with a dot labelled "…
Source: Digital Communication Systems, 1st ed., Ch. 5, pp. 230-232
CO3 | Bloom L4 | visual id: capacity-maximisation
Notes: What to say: Give them the idea before the formalism. Say it plainly first: Channel capacity is C = max over p(x) of I(X;Y), the largest mutual information achievable by any choice of input distribution, measured in bits per chann… Then add the part they are examined on - Capacity is the best mutual information over all input distributions — a property of the channel, not of any code. Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "channel capacity" constrain here, and what would break if it did not hold? Animation instructions: the axes draw, then the symmetric curve sweeps up and over, then its peak marker drops with the label, then the asymmetric curve draws in a second colour, then its off-centre peak marker drops, then the side card slides in with its two lines appearing in order. Transition style: Fade [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 3: Information Theory. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 5, pp. 230-232. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 42
Channel capacity - how it works
The procedure in order, and what each pass costs you.
VTU BEC503 | Module 3
Channel capacity
42
1. Write mutual information as a function of the input distribution
2. Check whether the channel is symmetric
3. If symmetric, take the uniform input distribution and evaluate directly
4. If not, maximise numerically, for example with the Blahut-Arimoto algorithm
5. Report capacity in bits per channel use, and multiply by the symbol rate for bits per second
COST AND BEHAVIOUR
Best: symmetric channels have uniform optimal input and a closed form
Typical: concave maximisation, so a unique global optimum exists
Worst: no closed form for general asymmetric channels
WHAT THAT MEANS
Capacity per second requires multiplying by the symbol rate, which is where bandwidth enters.
Source: Digital Communication Systems, 1st ed., Ch. 5, pp. 230-232 | CO3 | Bloom L4
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Write mutual information as a function of the input distribution - and check everyone has written it before moving on. At the cost panel, translate it: Capacity per second requires multiplying by the symbol rate, which is where bandwidth enters. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 3: Information Theory. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 5, pp. 230-232. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 43
Channel capacity - worked example
One concrete case, carried all the way to a stated number.
VTU BEC503 | Module 3
Channel capacity
43
GIVEN
BSC with p = 0.01, symbol rate 1 Msymbol/s.
1. H(0.01) = -0.01 log2(0.01) - 0.99 log2(0.99) = 0.0664 + 0.0144 = 0.0808
2. C = 1 - 0.0808 = 0.919 bits per channel use
3. At 1 Msymbol/s: 919 kbit/s
4. A 1% error rate therefore costs about 8% of the throughput, not 1%
RESULT
919 kbit/s is the ceiling. Any code achieving less is inefficient; no code achieves more, whatever its complexity.
C = max over p(x) of I(X;Y) bits per channel use
Symmetric channel => uniform p(x) is optimal
BSC: C = 1 - H(p)
BEC: C = 1 - epsilon
Capacity in bits/second = C * symbol rate
THE MISTAKE STUDENTS MAKE
Students state capacity in bits per second without a symbol rate. Capacity as defined is per channel use; converting to bits per second requires the signalling rate, which is set by the bandwidth.
Source: Digital Communication Systems, 1st ed., Ch. 5, pp. 230-232 | CO3 | Bloom L4
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is BSC with p = 0.01, symbol rate 1 Msymbol/s. Work at the pace of the slowest note-taker and land hard on the result: 919 kbit/s is the ceiling. Any code achieving less is inefficient; no code achieves more, whatever its complexity. Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 3: Information Theory. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 5, pp. 230-232. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 44
The channel coding theorem
What it is, why it works, and what it costs.
VTU BEC503 | Module 3
The channel coding theorem
44
THE MECHANISM
The channel coding theorem states that for any code rate R strictly less than capacity C, there exist codes of sufficiently long block length whose probability of error can be made arbitrarily small; and conversely, for R greater than C, the error probability is bounded away from zero no matter what code is used. This is the most consequential result in the subject, because it says reliable communication over an unreliable channel is possible without reducing the rate to zero — which was not obvious and was widely disbelieved before 1948. It is an existence proof by random coding: it shows good codes are plentiful without exhibiting one, which is why the next two modules are needed.
KEY TERMS
• channel coding theorem
• arbitrarily small error
• code rate
• block length
• converse
TAKEAWAY
Below capacity, arbitrarily reliable communication exists; above it, none does. The theorem says codes exist but not which ones.
DIAGRAM FOR PHASE 2
A horizontal rate axis from 0 to beyond C, with a bold vertical threshold line at C. To the left of it the region is tinted green and labelled "R < C: error probability can be driven to zero with long enough b…
Source: Digital Communication Systems, 1st ed., Ch. 5, pp. 232-237
CO3 | Bloom L4 | visual id: coding-theorem-threshold
Notes: What to say: Give them the idea before the formalism. Say it plainly first: The channel coding theorem states that for any code rate R strictly less than capacity C, there exist codes of sufficiently long block length whose probab… Then add the part they are examined on - Below capacity, arbitrarily reliable communication exists; above it, none does. The theorem says codes exist but not which o… Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "channel coding theorem" constrain here, and what would break if it did not hold? Animation instructions: the rate axis draws, then the threshold line rises at C, then the green region fills leftward and the red region rightward, then the three error curves draw in sequence from the fastest-decaying to the flat one, then the caption lands. Transition style: Fade [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 3: Information Theory. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 5, pp. 232-237. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 45
The channel coding theorem - how it works
The procedure in order, and what each pass costs you.
VTU BEC503 | Module 3
The channel coding theorem
45
1. Compute the channel capacity C
2. Choose a code rate R = k/n strictly less than C
3. Increase the block length n until the required error probability is met
4. Accept the increased latency and decoding complexity that longer blocks bring
5. If the required rate exceeds C, reduce the rate or improve the channel — no code will help
COST AND BEHAVIOUR
Best: rates well below capacity converge quickly with modest block length
Typical: error probability falls exponentially in the block length
Worst: rates approaching capacity need very long blocks and heavy decoding
WHAT THAT MEANS
Turbo and LDPC codes reach within a fraction of a dB of capacity with block lengths in the thousands.
Source: Digital Communication Systems, 1st ed., Ch. 5, pp. 232-237 | CO3 | Bloom L4
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Compute the channel capacity C - and check everyone has written it before moving on. At the cost panel, translate it: Turbo and LDPC codes reach within a fraction of a dB of capacity with block lengths in the thousands. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 3: Information Theory. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 5, pp. 232-237. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 46
The channel coding theorem - worked example
One concrete case, carried all the way to a stated number.
VTU BEC503 | Module 3
The channel coding theorem
46
GIVEN
BSC with p = 0.01, so C = 0.919. A designer wants R = 0.95.
1. Check R against C: 0.95 > 0.919
2. The converse applies: error probability is bounded away from zero
3. No block length and no decoder complexity can fix this
4. Options: reduce R below 0.919, or improve the channel to reduce p
RESULT
The design is impossible as stated. Reducing the rate to 0.9 puts it below capacity, at which point long enough codes can make errors as rare as required.
Code rate: R = k/n information bits per transmitted bit
Forward: R < C => exists a code with Pe -> 0 as n -> infinity
Converse: R > C => Pe bounded away from 0 for every code
Random coding argument: almost all long codes are good.
THE MISTAKE STUDENTS MAKE
Students read the theorem as a promise that any specific code will work below capacity. It guarantees that good codes exist, not that a chosen code is one of them — a rate-1/2 repetition code is far below capacity and still poor.
Source: Digital Communication Systems, 1st ed., Ch. 5, pp. 232-237 | CO3 | Bloom L4
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is BSC with p = 0.01, so C = 0.919. A designer wants R = 0.95. Work at the pace of the slowest note-taker and land hard on the result: The design is impossible as stated. Reducing the rate to 0.9 puts it below capacity, at which point long enough codes can make er… Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 3: Information Theory. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 5, pp. 232-237. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 47
The Information Capacity Law
What it is, why it works, and what it costs.
VTU BEC503 | Module 3
The Information Capacity Law
47
THE MECHANISM
The Information Capacity Law states that a band-limited AWGN channel of bandwidth B hertz and signal-to-noise ratio S/N has capacity C = B log2(1 + S/N) bits per second. It ties together the three resources a communication engineer trades between — bandwidth, power and reliability — in a single expression, and it is the continuous-channel counterpart of the discrete capacity results. Capacity grows only logarithmically with power, so doubling the transmit power adds barely one bit per hertz at high SNR, while it grows linearly with bandwidth, which is why spectrum is the more valuable of the two resources.
KEY TERMS
• Shannon-Hartley
• information capacity law
• bandwidth
• signal-to-noise ratio
• band-limited channel
TAKEAWAY
C = B log2(1 + S/N): capacity is linear in bandwidth and only logarithmic in power, which is why spectrum costs more than watts.
DIAGRAM FOR PHASE 2
Two plots side by side sharing a capacity axis. Left: capacity against bandwidth at fixed SNR, a straight line rising from the origin, labelled "linear in B". Right: capacity against SNR in dB at fixed bandwid…
Source: Digital Communication Systems, 1st ed., Ch. 5, pp. 240-244
CO3 | Bloom L4 | visual id: shannon-hartley-surface
Notes: What to say: Give them the idea before the formalism. Say it plainly first: The Information Capacity Law states that a band-limited AWGN channel of bandwidth B hertz and signal-to-noise ratio S/N has capacity C = B log2(1 + S/N) b… Then add the part they are examined on - C = B log2(1 + S/N): capacity is linear in bandwidth and only logarithmic in power, which is why spectrum costs more than wa… Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "Shannon-Hartley" constrain here, and what would break if it did not hold? Animation instructions: both sets of axes draw together, then the left straight line sweeps up from the origin, then the right curve sweeps up and flattens, then the doubling markers appear on each plot in turn with their annotations, then the footer card slides up. Transition style: Fade [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 3: Information Theory. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 5, pp. 240-244. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 48
The Information Capacity Law - how it works
The procedure in order, and what each pass costs you.
VTU BEC503 | Module 3
The Information Capacity Law
48
1. Measure or specify the channel bandwidth B in hertz
2. Compute the signal-to-noise ratio S/N as a linear ratio, not in decibels
3. Evaluate C = B log2(1 + S/N) in bits per second
4. Compare against the required bit rate
5. If short, decide whether more bandwidth or more power is the cheaper remedy
COST AND BEHAVIOUR
Best: unlimited bandwidth still gives a finite capacity of 1.44 S/N0
Typical: one logarithm per evaluation
Worst: high SNR gives sharply diminishing returns on power
WHAT THAT MEANS
The infinite-bandwidth limit is what produces the Shannon limit of -1.6 dB in Eb/N0.
Source: Digital Communication Systems, 1st ed., Ch. 5, pp. 240-244 | CO3 | Bloom L4
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Measure or specify the channel bandwidth B in hertz - and check everyone has written it before moving on. At the cost panel, translate it: The infinite-bandwidth limit is what produces the Shannon limit of -1.6 dB in Eb/N0. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 3: Information Theory. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 5, pp. 240-244. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 49
The Information Capacity Law - worked example
One concrete case, carried all the way to a stated number.
VTU BEC503 | Module 3
The Information Capacity Law
49
GIVEN
A telephone channel with B = 3.1 kHz and SNR = 30 dB.
1. SNR linear: 10^(30/10) = 1000
2. C = 3100 x log2(1001)
3. log2(1001) = 9.97
4. C = 3100 x 9.97 = 30,900 bit/s
RESULT
About 31 kbit/s, which is why 33.6 kbit/s modems sat at the practical limit of the analogue telephone network and no clever modulation could exceed it.
C = B * log2( 1 + S/N ) bits per second
S/N linear, not in dB: S/N = 10^(SNR_dB/10)
With S = Eb*Rb and N = N0*B:
C = B * log2( 1 + (Eb/N0)*(Rb/B) )
Infinite bandwidth limit: C_inf = 1.44 * S/N0
THE MISTAKE STUDENTS MAKE
Students substitute the SNR in decibels directly into the formula. The expression needs the linear power ratio; using 30 instead of 1000 gives 15.4 kbit/s instead of 31 kbit/s.
Source: Digital Communication Systems, 1st ed., Ch. 5, pp. 240-244 | CO3 | Bloom L4
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is A telephone channel with B = 3.1 kHz and SNR = 30 dB. Work at the pace of the slowest note-taker and land hard on the result: About 31 kbit/s, which is why 33.6 kbit/s modems sat at the practical limit of the analogue telephone network and no clever modul… Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 3: Information Theory. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 5, pp. 240-244. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 50
The bandwidth-power trade-off and the Shannon limit
What it is, why it works, and what it costs.
VTU BEC503 | Module 3
The bandwidth-power trade-off and the…
50
THE MECHANISM
Rewriting the capacity law in terms of energy per bit gives a boundary in the plane of spectral efficiency against Eb/N0, and no system can operate to the left of it. As bandwidth grows without limit and spectral efficiency falls towards zero, the required Eb/N0 approaches ln(2), which is -1.59 dB — the Shannon limit, the least energy per bit that can ever suffice on an AWGN channel. Uncoded BPSK needs 9.6 dB for an error rate of 1e-5, so there is over 11 dB of theoretical coding gain available, and modern turbo and LDPC codes claim most of it.
KEY TERMS
• Shannon limit
• bandwidth efficiency
• Eb/N0 minimum
• capacity boundary
• coding gain
TAKEAWAY
The Shannon limit is -1.6 dB; uncoded BPSK sits 11 dB above it, and that gap is exactly what channel coding exists to close.
DIAGRAM FOR PHASE 2
A plot with Eb/N0 in dB on the horizontal axis from -2 to 15 and spectral efficiency in bit/s/Hz on the vertical from 0.1 to 8 on a logarithmic scale. The capacity boundary curve descends from the upper right…
Source: Digital Communication Systems, 1st ed., Ch. 5, pp. 240-244
CO3 | Bloom L5 | visual id: shannon-limit-plane
Notes: What to say: Give them the idea before the formalism. Say it plainly first: Rewriting the capacity law in terms of energy per bit gives a boundary in the plane of spectral efficiency against Eb/N0, and no system can operate to the… Then add the part they are examined on - The Shannon limit is -1.6 dB; uncoded BPSK sits 11 dB above it, and that gap is exactly what channel coding exists to close. Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "Shannon limit" constrain here, and what would break if it did not hold? Animation instructions: the axes draw, then the capacity boundary curve sweeps in from the upper right and flattens onto its asymptote, then the vertical Shannon limit line rises and the red region fills to its left, then the four operating points drop in one at a time, then the coding-gain arrow extends from BPSK to the boundary with its bracket and label last. Transition style: Fade [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 3: Information Theory. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 5, pp. 240-244. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 51
The bandwidth-power trade-off and the Shannon limit - how it works
The procedure in order, and what each pass costs you.
VTU BEC503 | Module 3
The bandwidth-power trade-off and the…
51
1. Express spectral efficiency as r = Rb/B bits per second per hertz
2. Substitute S/N = (Eb/N0)(Rb/B) into the capacity law
3. Solve for the minimum Eb/N0 as (2^r - 1)/r
4. Take the limit as r approaches zero to obtain ln(2) = -1.59 dB
5. Measure any real scheme by its horizontal distance from the boundary
COST AND BEHAVIOUR
Best: the bound is exact and universal for AWGN
Typical: the required Eb/N0 rises steeply for spectral efficiency above 4
Worst: approaching the bound needs enormous block lengths and iterative decoding
WHAT THAT MEANS
Turbo codes reached within 0.5 dB of the bound in 1993, which was the surprise of the decade.
Source: Digital Communication Systems, 1st ed., Ch. 5, pp. 240-244 | CO3 | Bloom L5
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Express spectral efficiency as r = Rb/B bits per second per hertz - and check everyone has written it before moving on. At the cost panel, translate it: Turbo codes reached within 0.5 dB of the bound in 1993, which was the surprise of the decade. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 3: Information Theory. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 5, pp. 240-244. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 52
The bandwidth-power trade-off and the Shannon limit - worked example
One concrete case, carried all the way to a stated number.
VTU BEC503 | Module 3
The bandwidth-power trade-off and the…
52
GIVEN
Required minimum Eb/N0 at spectral efficiencies 4, 1 and approaching 0.
1. r = 4: (2^4 - 1)/4 = 15/4 = 3.75, which is 5.7 dB
2. r = 1: (2^1 - 1)/1 = 1, which is 0 dB
3. r = 0.1: (2^0.1 - 1)/0.1 = 0.718, which is -1.44 dB
4. r approaching 0: the limit is ln(2) = 0.693, which is -1.59 dB
RESULT
Spending bandwidth buys power efficiency all the way down to -1.59 dB and no further. Below that, no bandwidth and no code suffices.
r = Rb/B spectral efficiency, bit/s/Hz
r < log2( 1 + r * Eb/N0 )
=> Eb/N0 > (2^r - 1) / r
As r -> 0: Eb/N0 > ln(2) = 0.693 = -1.59 dB
Uncoded BPSK at 1e-5 needs 9.6 dB: gap = 11.2 dB
THE MISTAKE STUDENTS MAKE
Students quote -1.6 dB as the minimum for any system. It is the limit as spectral efficiency tends to zero, meaning infinite bandwidth per bit. A system at 2 bit/s/Hz faces a minimum of 1.76 dB, not -1.6 dB.
Source: Digital Communication Systems, 1st ed., Ch. 5, pp. 240-244 | CO3 | Bloom L5
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is Required minimum Eb/N0 at spectral efficiencies 4, 1 and approaching 0. Work at the pace of the slowest note-taker and land hard on the result: Spending bandwidth buys power efficiency all the way down to -1.59 dB and no further. Below that, no bandwidth and no code suffic… Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 3: Information Theory. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 5, pp. 240-244. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 53
One sentence per unit, six months from now
Units 1-7: what survives after the detail has gone.
VTU BEC503 | Module 3
Revision
53
01 Information is surprise measured logarithmically, and the logarithm is forced by wanting independent events to add.
02 Entropy is average surprise, it depends only on the probabilities, and it is the floor for lossless compression.
03 Coding blocks of n symbols divides the rounding waste by n, which is how real codes creep up on the entropy bound.
04 No lossless code beats entropy, and some code gets within one bit of it — a floor and a ceiling in one theorem.
05 Kraft says code lengths compete for one unit of tree; a prefix code exists exactly when the claims fit.
06 Huffman is optimal among prefix codes, and its only loss is the rounding of ideal lengths to whole bits.
07 Huffman needs the statistics and ignores memory; Lempel-Ziv learns as it goes and captures repetition, which is where real redundancy lives.
Notes: What to say: Slow right down here. Read each takeaway aloud and then stop talking for a beat, because these are the sentences that should still be in their heads when they sit the SEE. Tell them explicitly that if they can reconstruct the reasoning behind any one of these lines they understand that unit, and if they can only recite it they do not. Pause cue: Pause for three seconds after each takeaway before moving to the next. Pointing cue: Point at each numbered takeaway in turn as you read it. Question to ask students: Ask: choose the takeaway you trust least and tell me what you would have to check to believe it. Animation instructions: Takeaway rows reveal one at a time from the top, each row highlighting briefly as it appears. Transition style: Fade [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 3: Information Theory, 10 hours, TB1 (Haykin 2014) Ch. 5.1-5.10 pp. 207-244. TB1: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014. Revision consolidates all 16 unit takeaways. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 54
Revision, continued
Units 8-14: what survives after the detail has gone.
VTU BEC503 | Module 3
Revision
54
08 Efficiency measures the mean; buffer size is set by the variance, so two codes with the same average length are not equally usable.
09 The channel matrix is given by nature; the input distribution is yours to choose, and capacity is the best you can do with that one choice.
10 Knowing which bits are damaged is worth more than the bits themselves; the BEC beats the BSC at the same disturbance probability.
11 Mutual information is what survives the channel: total uncertainty minus what remains after looking at the output.
12 Concavity makes capacity computable; the data processing inequality makes it unbeatable by any amount of receiver cleverness.
13 Capacity is the best mutual information over all input distributions — a property of the channel, not of any code.
14 Below capacity, arbitrarily reliable communication exists; above it, none does. The theorem says codes exist but not which ones.
Notes: What to say: Slow right down here. Read each takeaway aloud and then stop talking for a beat, because these are the sentences that should still be in their heads when they sit the SEE. Tell them explicitly that if they can reconstruct the reasoning behind any one of these lines they understand that unit, and if they can only recite it they do not. Pause cue: Pause for three seconds after each takeaway before moving to the next. Pointing cue: Point at each numbered takeaway in turn as you read it. Question to ask students: Ask: choose the takeaway you trust least and tell me what you would have to check to believe it. Animation instructions: Takeaway rows reveal one at a time from the top, each row highlighting briefly as it appears. Transition style: Fade [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 3: Information Theory, 10 hours, TB1 (Haykin 2014) Ch. 5.1-5.10 pp. 207-244. TB1: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014. Revision consolidates all 16 unit takeaways. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 55
Revision, continued
Units 15-16: what survives after the detail has gone.
VTU BEC503 | Module 3
Revision
55
15 C = B log2(1 + S/N): capacity is linear in bandwidth and only logarithmic in power, which is why spectrum costs more than watts.
16 The Shannon limit is -1.6 dB; uncoded BPSK sits 11 dB above it, and that gap is exactly what channel coding exists to close.
Notes: What to say: Slow right down here. Read each takeaway aloud and then stop talking for a beat, because these are the sentences that should still be in their heads when they sit the SEE. Tell them explicitly that if they can reconstruct the reasoning behind any one of these lines they understand that unit, and if they can only recite it they do not. Pause cue: Pause for three seconds after each takeaway before moving to the next. Pointing cue: Point at each numbered takeaway in turn as you read it. Question to ask students: Ask: choose the takeaway you trust least and tell me what you would have to check to believe it. Animation instructions: Takeaway rows reveal one at a time from the top, each row highlighting briefly as it appears. Transition style: Fade [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 3: Information Theory, 10 hours, TB1 (Haykin 2014) Ch. 5.1-5.10 pp. 207-244. TB1: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014. Revision consolidates all 16 unit takeaways. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 56
How this module is assessed
Where the quiz and the assignment live, and what they test.
VTU BEC503 | Module 3
Assessment
56
MODULE 3 QUIZ
quizzes/Module_3_Quiz.pdf
quizzes/Module_3_Quiz.gift
45 minutes | 50 marks | pass 20 | 1 attempt
Part A: 20 MCQs, 1 mark each.
Part B: 13 descriptive questions, 30 marks.
Bloom spread: L1-L2 33%, L3-L4 55%, L5-L6 12%
Every question carries a CO tag, a Bloom level and a chapter reference; distractor feedback names the misconception.
MODULE 3 ASSIGNMENT
assignments/Module_3_Assignment.pdf
Assignment 3 — Entropy, source coding and channel capacity
20 marks | 10% of CIE | 8 problems + 3 theory items
Submit as PDF, single file, named <USN>_BEC503_Assignment3.pdf, via LMS upload. 10% per day, nothing after 5 days.
Rubric: Correctness of entropy and capacity calculations (8); Code construction and verification (5); Plots and comparative analysis (4); Interpretation of the fundamental limits (3). Attainment: CO3 = 18, CO4 = 2.
Previous years' question papers for EC are indexed in pyq/PYQ_Index.pdf; the syllabus extract and the topic-to-slide mapping are in syllabus/Syllabus_Mapping.pdf.
Individual submission. Identical submissions score zero for both parties.
Notes: What to say: Close by telling them exactly where the assessment lives and what it tests. Name the two files, say the mark split out loud, and read the Bloom spread so they understand that roughly a quarter of the paper is not recall at all. Then read the integrity line word for word, because ambiguity there costs students more than any technical error in this module. Pause cue: Pause after the Bloom spread and before the integrity statement. Pointing cue: Point at the quiz panel, then the assignment panel, then the integrity line at the bottom. Question to ask students: Ask: which course outcome do you feel least ready on, and which unit would you reread tonight to fix it? Animation instructions: Quiz panel fades in from the left, then the assignment panel from the right, then the pointers strip appears, then the integrity line fades in last. Transition style: Fade [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 3: Information Theory, 10 hours, TB1 (Haykin 2014) Ch. 5.1-5.10 pp. 207-244. TB1: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014. Assessment counts: 20 MCQs, 13 descriptive questions, 11 assignment items. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.