## Slide 1
Digital Communication
Module 4 asks: How do I add redundancy so that the receiver can find and repair errors it cannot even see?
VTU BEC503 | Module 4
Opening
01
MODULE 4
Error Control Coding: Linear Block and Cyclic Codes
10 contact hours | 16 teaching units | 56 slides
PRESCRIBED TEXTBOOK
Digital Communication Systems
Simon Haykin
John Wiley & Sons, 1st edition, 2014
TB1 (Haykin 2014) Ch. 10.1-10.5 pp. 577-605
Signal Space & AWGN • Digital Modulation • Information Theory • Block & Cyclic Codes • Convolutional Codes
Redundancy buys detection → Generator matrix builds codewords → Syndrome exposes the error → Distance sets the guarantee → Polynomials make it cheap
EC · Semester 5 · BEC503 · generated for Phase 2 conversion
Notes: What to say: Open by putting the whole module on one page. Tell them this is 10 contact hours and 16 teaching units, and that all of it exists to answer one question: How do I add redundancy so that the receiver can find and repair errors it cannot even see? Name the prescribed textbook out loud and say which chapters they will be living in, so nobody is reading the wrong book by week two. Pause cue: Pause after reading the driving question aloud, before naming the textbook. Pointing cue: Point at the module title block, then at the textbook panel, then run a finger along the five-beat arc. Question to ask students: Ask: before we start, what do you already expect the answer to "How do I add redundancy so that the receiver can find and repair errors it cannot even se…" to look like? Animation instructions: Module title block fades in first, then the textbook panel slides in from the right, then the five arc beats appear left to right one at a time. Transition style: Fade [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 4: Error Control Coding: Linear Block and Cyclic Codes, 10 hours, TB1 (Haykin 2014) Ch. 10.1-10.5 pp. 577-605. TB1: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 2
What this module is actually for
One question, five beats, and the scope it does not cover.
VTU BEC503 | Module 4
Overview
02
THE DRIVING QUESTION
How do I add redundancy so that the receiver can find and repair errors it cannot even see?
1
Redundancy buys detection
2
Generator matrix builds codewords
3
Syndrome exposes the error
4
Distance sets the guarantee
5
Polynomials make it cheap
SCOPE AND PROVENANCE
Built from TB1 Sections 10.1-10.5, which the syllabus names. The module is the constructive answer to Module 3: capacity said good codes exist, and this is the first family that can actually be built and decoded. The organising idea is linear algebra over GF(2) — codewords form a subspace, the generator matrix is its basis, the parity check matrix annihilates it, and the syndrome is the image of the received word under that annihilator. Everything about detection and correction capability follows from one number, the minimum distance. Cyclic codes then add structure so that matrix multiplication becomes polynomial arithmetic and the encoder collapses to a shift register.
Course outcomes exercised: CO4, CO5
Assessment: 20 MCQs + 13 descriptive questions + 11 assignment items
Notes: What to say: Give them the map before the territory. Read the driving question once more, then walk the five beats across the slide and say in one sentence what changes between each beat and the next. Finish on the scope paragraph, because knowing what a module does not cover saves more marks than anything else on this slide. Pause cue: Pause for four or five seconds after the five beats appear, before moving to scope. Pointing cue: Point at the driving question panel, then at each numbered beat in turn, then at the scope paragraph. Question to ask students: Ask: which of these five beats do you expect to find hardest, and why that one? Animation instructions: The driving question panel fades in, then the five numbered beats appear left to right one at a time, then the scope paragraph fades in beneath them. Transition style: Fade [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 4: Error Control Coding: Linear Block and Cyclic Codes, 10 hours, TB1 (Haykin 2014) Ch. 10.1-10.5 pp. 577-605. TB1: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 3
Every unit against its chapter and pages
Units 1-9 of 16, with the deck slides that teach each one.
VTU BEC503 | Module 4
Syllabus mapping
03
# — Teaching unit — Book chapter and pages — Deck slides — CO / Bloom
01 Forward error correction versus automatic repeat request — Ch. 10, pp. 577-579 — slides 5, 6, 7 — CO4 / L3
02 Linear block codes: the definition and why linearity matters — Ch. 10, pp. 582-586 — slides 8, 9, 10 — CO4 / L3
03 The generator matrix — Ch. 10, pp. 582-586 — slides 11, 12, 13 — CO5 / L3
04 The parity check matrix — Ch. 10, pp. 582-586 — slides 14, 15, 16 — CO5 / L4
05 Systematic form and why encoders prefer it — Ch. 10, pp. 582-586 — slides 17, 18, 19 — CO5 / L3
06 The syndrome and its properties — Ch. 10, pp. 586-590 — slides 20, 21, 22 — CO4 / L4
07 Minimum distance and minimum weight — Ch. 10, pp. 586-590 — slides 23, 24, 25 — CO4 / L4
08 Error detection and correction capability — Ch. 10, pp. 586-590 — slides 26, 27, 28 — CO4 / L4
09 Syndrome decoding and the standard array — Ch. 10, pp. 590-593 — slides 29, 30, 31 — CO5 / L4
Notes: What to say: Tell them this is the slide to photograph. Every unit in the module is listed against a real chapter and a real page range, so there is no ambiguity about what to read. Point out the slide-number column and say plainly that if they miss a lecture, those are the slides covering that unit. Say that the page ranges come from the book's own table of contents rather than a guess. Pause cue: Pause for ten seconds and let them photograph the table before saying anything else. Pointing cue: Run a finger down the chapter-and-pages column, then across one complete row. Question to ask students: Ask: pick any row - which chapter would you open first, and what would you expect in the first paragraph? Animation instructions: Header row appears first, then the unit rows fade in one at a time from the top, then the chapter-and-pages column highlights. Transition style: Cut [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 4: Error Control Coding: Linear Block and Cyclic Codes, 10 hours, TB1 (Haykin 2014) Ch. 10.1-10.5 pp. 577-605. TB1: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014. Mapping covers all 16 teaching units. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 4
Syllabus mapping, continued
Units 10-16 of 16, with the deck slides that teach each one.
VTU BEC503 | Module 4
Syllabus mapping
04
# — Teaching unit — Book chapter and pages — Deck slides — CO / Bloom
10 Hamming codes — Ch. 10, pp. 590-593 — slides 32, 33, 34 — CO5 / L4
11 Cyclic codes: definition and properties — Ch. 10, pp. 593-597 — slides 35, 36, 37 — CO4 / L4
12 The generator polynomial — Ch. 10, pp. 593-597 — slides 38, 39, 40 — CO5 / L4
13 Parity check polynomial and matrix forms — Ch. 10, pp. 597-601 — slides 41, 42, 43 — CO5 / L4
14 Systematic cyclic encoding with a shift register — Ch. 10, pp. 597-601 — slides 44, 45, 46 — CO5 / L5
15 Syndrome computation for cyclic codes and a worked example — Ch. 10, pp. 601-605 — slides 47, 48, 49 — CO5 / L5
16 Cyclic redundancy checks and burst error detection — Ch. 10, pp. 601-605 — slides 50, 51, 52 — CO4 / L5
Notes: What to say: Tell them this is the slide to photograph. Every unit in the module is listed against a real chapter and a real page range, so there is no ambiguity about what to read. Point out the slide-number column and say plainly that if they miss a lecture, those are the slides covering that unit. Say that the page ranges come from the book's own table of contents rather than a guess. Pause cue: Pause for ten seconds and let them photograph the table before saying anything else. Pointing cue: Run a finger down the chapter-and-pages column, then across one complete row. Question to ask students: Ask: pick any row - which chapter would you open first, and what would you expect in the first paragraph? Animation instructions: Header row appears first, then the unit rows fade in one at a time from the top, then the chapter-and-pages column highlights. Transition style: Cut [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 4: Error Control Coding: Linear Block and Cyclic Codes, 10 hours, TB1 (Haykin 2014) Ch. 10.1-10.5 pp. 577-605. TB1: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014. Mapping covers all 16 teaching units. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 5
Forward error correction versus automatic repeat request
What it is, why it works, and what it costs.
VTU BEC503 | Module 4
Forward error correction versus autom…
05
THE MECHANISM
Forward error correction adds redundancy at the transmitter so the receiver can repair errors without asking for a retransmission, while automatic repeat request adds only enough redundancy to detect errors and then requests the block again. FEC costs bandwidth permanently but needs no return path and adds no variable delay; ARQ costs bandwidth only when errors occur but requires a feedback channel and introduces a round-trip delay per failure. The choice is dictated by the link: a deep-space probe with a forty-minute round trip has no realistic ARQ option, while a local network with microsecond latency and rare errors is better served by ARQ. Hybrid schemes correct what they can and request the rest.
KEY TERMS
• FEC
• ARQ
• feedback channel
• latency
• code rate
TAKEAWAY
FEC pays a fixed bandwidth premium to avoid the round trip; ARQ pays a round trip to avoid the premium. Latency decides.
DIAGRAM FOR PHASE 2
Two horizontal timelines stacked. The upper, labelled FEC, shows a continuous stream of blocks flowing left to right with a small permanent shaded portion of each block marked "parity", and a corrupted block b…
Source: Digital Communication Systems, 1st ed., Ch. 10, pp. 577-579
CO4 | Bloom L3 | visual id: fec-versus-arq-timeline
Notes: What to say: Give them the idea before the formalism. Say it plainly first: Forward error correction adds redundancy at the transmitter so the receiver can repair errors without asking for a retransmission, while automatic repeat… Then add the part they are examined on - FEC pays a fixed bandwidth premium to avoid the round trip; ARQ pays a round trip to avoid the premium. Latency decides. Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "FEC" constrain here, and what would break if it did not hold? Animation instructions: the FEC timeline draws left to right with blocks appearing in sequence, then one block reddens and is repaired in place with a tick, then the ARQ timeline draws, then its bad block reddens with a cross, then the feedback arrow loops back and the gap opens visibly before the retransmission arrives, then the comparison card rows fill top to bottom. Transition style: Fade [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 4: Error Control Coding: Linear Block and Cyclic Codes. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 10, pp. 577-579. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 6
Forward error correction versus automatic repeat request - how it works
The procedure in order, and what each pass costs you.
VTU BEC503 | Module 4
Forward error correction versus autom…
06
1. Determine whether a feedback channel exists and its round-trip time
2. Estimate the raw block error rate on the link
3. If the round trip is long or absent, choose FEC
4. If errors are rare and latency is short, choose ARQ
5. For intermediate cases, use hybrid ARQ: correct what the code can, request the rest
COST AND BEHAVIOUR
Best: ARQ on a clean link costs almost no redundancy
Typical: FEC costs (n-k)/n of the bandwidth permanently
Worst: ARQ on a bad link retransmits repeatedly and throughput collapses
WHAT THAT MEANS
ARQ throughput falls off a cliff once the block error rate approaches one.
Source: Digital Communication Systems, 1st ed., Ch. 10, pp. 577-579 | CO4 | Bloom L3
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Determine whether a feedback channel exists and its round-trip time - and check everyone has written it before moving on. At the cost panel, translate it: ARQ throughput falls off a cliff once the block error rate approaches one. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 4: Error Control Coding: Linear Block and Cyclic Codes. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 10, pp. 577-579. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 7
Forward error correction versus automatic repeat request - worked example
One concrete case, carried all the way to a stated number.
VTU BEC503 | Module 4
Forward error correction versus autom…
07
GIVEN
A link with block error rate 0.1 and a round-trip time of 500 ms, carrying 1000-bit blocks.
1. ARQ: average transmissions per block = 1/(1-0.1) = 1.11
2. Bandwidth overhead: 11%, but each failure adds 500 ms of delay
3. Expected delay penalty: 0.1 x 500 ms = 50 ms per block on average
4. FEC at rate 1/2: 100% overhead, zero added delay
RESULT
ARQ wins on bandwidth by a wide margin and loses badly on delay. For a real-time voice link the 50 ms average and unbounded tail rule it out.
Code rate: R = k/n k information bits in n transmitted bits
Overhead: (n - k)/n
ARQ expected transmissions: 1/(1 - Pblock)
ARQ expected delay: Pblock * RTT / (1 - Pblock)
FEC: fixed overhead, zero added delay, no return path
THE MISTAKE STUDENTS MAKE
Students compare FEC and ARQ on bandwidth alone and conclude ARQ always wins on a good link. Delay variance matters as much as mean bandwidth, and for real-time traffic an unbounded retransmission tail is disqualifying however rare.
Source: Digital Communication Systems, 1st ed., Ch. 10, pp. 577-579 | CO4 | Bloom L3
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is A link with block error rate 0.1 and a round-trip time of 500 ms, carrying 1000-bit blocks. Work at the pace of the slowest note-taker and land hard on the result: ARQ wins on bandwidth by a wide margin and loses badly on delay. For a real-time voice link the 50 ms average and unbounded tail… Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 4: Error Control Coding: Linear Block and Cyclic Codes. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 10, pp. 577-579. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 8
Linear block codes: the definition and why linearity matters
What it is, why it works, and what it costs.
VTU BEC503 | Module 4
Linear block codes: the definition an…
08
THE MECHANISM
An (n,k) linear block code maps k information bits to n transmitted bits such that the set of all 2^k codewords is closed under modulo-2 addition: the sum of any two codewords is another codeword. The codewords therefore form a k-dimensional subspace of the n-dimensional vector space over GF(2), and the all-zero word is always a codeword. Linearity is not a cosmetic assumption but the property that makes everything else tractable — it collapses the encoder to a matrix multiplication, makes the minimum distance equal the minimum weight, and lets the decoder work with a syndrome that depends only on the error pattern and not on which codeword was sent.
KEY TERMS
• linear block code
• GF(2)
• subspace
• closure
• code rate
TAKEAWAY
Linearity means codewords form a subspace, and every simplification in this module follows from that single fact.
DIAGRAM FOR PHASE 2
A grid of small squares representing all 2^n binary n-tuples, with a subset highlighted in green representing the 2^k codewords, arranged so their subspace structure is visible. Two green squares are picked ou…
Source: Digital Communication Systems, 1st ed., Ch. 10, pp. 582-586
CO4 | Bloom L3 | visual id: linear-code-subspace
Notes: What to say: Give them the idea before the formalism. Say it plainly first: An (n,k) linear block code maps k information bits to n transmitted bits such that the set of all 2^k codewords is closed under modulo-2 addition: the sum… Then add the part they are examined on - Linearity means codewords form a subspace, and every simplification in this module follows from that single fact. Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "linear block code" constrain here, and what would break if it did not hold? Animation instructions: the full grid fades in grey, then the codeword subset lights green all at once, then the two chosen squares pulse and the plus and arrow draw to their sum which flashes, then the all-zero square is circled, then the three consequence lines appear one at a time. Transition style: Fade [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 4: Error Control Coding: Linear Block and Cyclic Codes. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 10, pp. 582-586. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 9
Linear block codes: the definition and why linearity ma… - how it works
The procedure in order, and what each pass costs you.
VTU BEC503 | Module 4
Linear block codes: the definition an…
09
1. Choose k information bits and n transmitted bits, giving rate k/n
2. Define the code as the set of 2^k linear combinations of k basis codewords
3. Verify closure: the modulo-2 sum of any two codewords is in the set
4. Confirm the all-zero word belongs to the code
5. Note the code is completely specified by any basis, which becomes the generator matrix
COST AND BEHAVIOUR
Best: storage is k basis vectors rather than 2^k codewords
Typical: encoding is a k-by-n matrix multiply over GF(2)
Worst: the number of codewords 2^k is exponential, so exhaustive listing is infeasible
WHAT THAT MEANS
Linearity is what avoids that exponential: everything is done through the basis.
Source: Digital Communication Systems, 1st ed., Ch. 10, pp. 582-586 | CO4 | Bloom L3
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Choose k information bits and n transmitted bits, giving rate k/n - and check everyone has written it before moving on. At the cost panel, translate it: Linearity is what avoids that exponential: everything is done through the basis. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 4: Error Control Coding: Linear Block and Cyclic Codes. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 10, pp. 582-586. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 10
Linear block codes: the definition and why linearity ma… - worked example
One concrete case, carried all the way to a stated number.
VTU BEC503 | Module 4
Linear block codes: the definition an…
10
GIVEN
A (5,2) code with basis codewords 10111 and 01101.
1. Codeword for 00: 00000
2. Codeword for 10: 10111
3. Codeword for 01: 01101
4. Codeword for 11: 10111 XOR 01101 = 11010
RESULT
Four codewords from two basis vectors, and the sum of any two is among them — for example 10111 XOR 11010 = 01101, which is in the code.
Code C is a k-dimensional subspace of GF(2)^n
Closure: c1, c2 in C => c1 XOR c2 in C
Zero word: 0 in C always
Size: |C| = 2^k
Rate: R = k/n
All arithmetic is modulo 2: 1+1 = 0, and subtraction equals addition.
THE MISTAKE STUDENTS MAKE
Students verify closure on a couple of pairs and declare the code linear. Closure must hold for every pair, which is why the code is specified by a basis in the first place — a basis guarantees closure by construction.
Source: Digital Communication Systems, 1st ed., Ch. 10, pp. 582-586 | CO4 | Bloom L3
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is A (5,2) code with basis codewords 10111 and 01101. Work at the pace of the slowest note-taker and land hard on the result: Four codewords from two basis vectors, and the sum of any two is among them — for example 10111 XOR 11010 = 01101, which is in th… Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 4: Error Control Coding: Linear Block and Cyclic Codes. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 10, pp. 582-586. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 11
The generator matrix
What it is, why it works, and what it costs.
VTU BEC503 | Module 4
The generator matrix
11
THE MECHANISM
The generator matrix G is a k-by-n matrix whose rows form a basis for the code, so every codeword is c = mG where m is the k-bit message row vector and all arithmetic is modulo 2. Encoding is therefore one matrix multiplication, and the code is entirely determined by G. Different generator matrices related by row operations produce the same code with a different mapping from messages to codewords, which means G is not unique but the code it generates is. Reducing G to the systematic form [I_k | P] gives a mapping in which the message appears verbatim in the first k positions.
KEY TERMS
• generator matrix
• basis
• row space
• encoding
• row operations
TAKEAWAY
G is a basis in matrix form; encoding is c = mG, and row operations change the mapping without changing the code.
DIAGRAM FOR PHASE 2
A matrix multiplication laid out: a 1-by-k message row vector on the left, a k-by-n generator matrix in the centre with its rows individually tinted, and a 1-by-n codeword on the right, joined by multiplicatio…
Source: Digital Communication Systems, 1st ed., Ch. 10, pp. 582-586
CO5 | Bloom L3 | visual id: generator-matrix-encoding
Notes: What to say: Give them the idea before the formalism. Say it plainly first: The generator matrix G is a k-by-n matrix whose rows form a basis for the code, so every codeword is c = mG where m is the k-bit message row vector and al… Then add the part they are examined on - G is a basis in matrix form; encoding is c = mG, and row operations change the mapping without changing the code. Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "generator matrix" constrain here, and what would break if it did not hold? Animation instructions: the message vector appears, then G draws row by row with each row taking its tint, then the arrows extend from each set message bit to its row and those rows highlight, then the selected rows slide right and stack with XOR symbols, collapsing into the codeword, then the systematic form fades in below with the identity block outlining last. Transition style: Fade [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 4: Error Control Coding: Linear Block and Cyclic Codes. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 10, pp. 582-586. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 12
The generator matrix - how it works
The procedure in order, and what each pass costs you.
VTU BEC503 | Module 4
The generator matrix
12
1. Collect k linearly independent codewords as the rows of G
2. Encode a message m as c = mG with modulo-2 arithmetic
3. Note the codeword is the XOR of the rows selected by the ones in m
4. Apply row operations to reach systematic form [I_k | P] if desired
5. Confirm the code is unchanged: only the message-to-codeword mapping moved
COST AND BEHAVIOUR
Best: systematic form needs only the parity part computed
Typical: k x n multiply-accumulate operations over GF(2)
Worst: a dense non-systematic G requires the full multiplication
WHAT THAT MEANS
In systematic form the first k output bits are copied, so only n-k parity bits need computing.
Source: Digital Communication Systems, 1st ed., Ch. 10, pp. 582-586 | CO5 | Bloom L3
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Collect k linearly independent codewords as the rows of G - and check everyone has written it before moving on. At the cost panel, translate it: In systematic form the first k output bits are copied, so only n-k parity bits need computing. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 4: Error Control Coding: Linear Block and Cyclic Codes. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 10, pp. 582-586. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 13
The generator matrix - worked example
One concrete case, carried all the way to a stated number.
VTU BEC503 | Module 4
The generator matrix
13
GIVEN
G = [[1,0,1,1],[0,1,0,1]] for a (4,2) code. Encode m = 11.
1. Row 1 is selected because the first message bit is 1: 1011
2. Row 2 is selected because the second message bit is 1: 0101
3. XOR them: 1011 XOR 0101 = 1110
4. Check systematic structure: first two bits 11 equal the message
RESULT
Codeword 1110, with the message visible in the first two positions because G is in systematic form.
c = m * G (mod 2)
G is k x n, rank k
Systematic form: G = [ I_k | P ]
=> c = [ m | m*P ] message then parity
Row operations on G change the mapping, not the code.
THE MISTAKE STUDENTS MAKE
Students treat G as unique and conclude two codes are different because their generator matrices differ. Row-equivalent matrices generate the same code; comparing codes means comparing the sets of codewords, not the matrices.
Source: Digital Communication Systems, 1st ed., Ch. 10, pp. 582-586 | CO5 | Bloom L3
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is G = [[1,0,1,1],[0,1,0,1]] for a (4,2) code. Encode m = 11. Work at the pace of the slowest note-taker and land hard on the result: Codeword 1110, with the message visible in the first two positions because G is in systematic form. Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 4: Error Control Coding: Linear Block and Cyclic Codes. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 10, pp. 582-586. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 14
The parity check matrix
What it is, why it works, and what it costs.
VTU BEC503 | Module 4
The parity check matrix
14
THE MECHANISM
The parity check matrix H is an (n-k)-by-n matrix whose null space is the code, so a vector c is a codeword if and only if cH transpose equals zero. Where G builds codewords, H tests them, and the two are related by G H transpose = 0. When G is in the systematic form [I_k | P], the parity check matrix follows immediately as H = [P transpose | I_(n-k)], which is why systematic form is worth reaching. H is the object the decoder actually uses, because the receiver does not know the message but can always apply the test.
KEY TERMS
• parity check matrix
• null space
• orthogonality
• dual code
• systematic relation
TAKEAWAY
G builds, H tests, and G H transpose = 0 ties them together — the decoder only ever needs H.
DIAGRAM FOR PHASE 2
Two matrices shown side by side: G labelled "builds codewords, k x n" with an outgoing arrow to a codeword vector, and H labelled "tests codewords, (n-k) x n" with an incoming arrow from the same vector and an…
Source: Digital Communication Systems, 1st ed., Ch. 10, pp. 582-586
CO5 | Bloom L4 | visual id: g-and-h-duality
Notes: What to say: Give them the idea before the formalism. Say it plainly first: The parity check matrix H is an (n-k)-by-n matrix whose null space is the code, so a vector c is a codeword if and only if cH transpose equals zero. Then add the part they are examined on - G builds, H tests, and G H transpose = 0 ties them together — the decoder only ever needs H. Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "parity check matrix" constrain here, and what would break if it did not hold? Animation instructions: G draws and its arrow produces the codeword, then H draws and the codeword arrow enters it, then the zero result pops out, then the relation box fills and pulses, then the systematic pair fades in below, then the two P blocks tint simultaneously and the transpose arrow curves between them. Transition style: Fade [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 4: Error Control Coding: Linear Block and Cyclic Codes. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 10, pp. 582-586. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 15
The parity check matrix - how it works
The procedure in order, and what each pass costs you.
VTU BEC503 | Module 4
The parity check matrix
15
1. Reduce G to systematic form [I_k | P]
2. Write H as [P transpose | I_(n-k)]
3. Verify G H transpose = 0 over GF(2)
4. Test any received vector r by computing r H transpose
5. A zero result means r is a codeword; a non-zero result means an error is present
COST AND BEHAVIOUR
Best: systematic form gives H by inspection
Typical: (n-k) x n operations to test a received word
Worst: a non-systematic G requires Gaussian elimination first
WHAT THAT MEANS
The rows of H are themselves the generator matrix of the dual code.
Source: Digital Communication Systems, 1st ed., Ch. 10, pp. 582-586 | CO5 | Bloom L4
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Reduce G to systematic form [I_k | P] - and check everyone has written it before moving on. At the cost panel, translate it: The rows of H are themselves the generator matrix of the dual code. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 4: Error Control Coding: Linear Block and Cyclic Codes. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 10, pp. 582-586. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 16
The parity check matrix - worked example
One concrete case, carried all the way to a stated number.
VTU BEC503 | Module 4
The parity check matrix
16
GIVEN
G = [[1,0,1,1],[0,1,0,1]], so P = [[1,1],[0,1]].
1. P transpose = [[1,0],[1,1]]
2. H = [P transpose | I_2] = [[1,0,1,0],[1,1,0,1]]
3. Check with codeword 1110: 1x1 + 1x0 + 1x1 + 0x0 = 0 mod 2
4. Second row: 1x1 + 1x1 + 1x0 + 0x1 = 0 mod 2
RESULT
Both parity checks pass, confirming 1110 is a codeword and that H was constructed correctly.
c is a codeword <=> c * H^T = 0 (mod 2)
G * H^T = 0
Systematic: G = [ I_k | P ]
H = [ P^T | I_(n-k) ]
H is (n-k) x n; its rows generate the dual code.
THE MISTAKE STUDENTS MAKE
Students forget the transpose in P transpose when writing H from G. Without it the dimensions may still appear to work for square P, but G H transpose is not zero and every codeword fails its own parity check.
Source: Digital Communication Systems, 1st ed., Ch. 10, pp. 582-586 | CO5 | Bloom L4
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is G = [[1,0,1,1],[0,1,0,1]], so P = [[1,1],[0,1]]. Work at the pace of the slowest note-taker and land hard on the result: Both parity checks pass, confirming 1110 is a codeword and that H was constructed correctly. Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 4: Error Control Coding: Linear Block and Cyclic Codes. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 10, pp. 582-586. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 17
Systematic form and why encoders prefer it
What it is, why it works, and what it costs.
VTU BEC503 | Module 4
Systematic form and why encoders pref…
17
THE MECHANISM
A code is systematic when the k message bits appear unchanged in fixed positions of the codeword, with the remaining n-k positions holding parity bits computed from them. Every linear block code has a systematic equivalent reachable by row operations on G, and the equivalent has identical distance properties, so nothing is lost by insisting on it. The practical advantages are concrete: the encoder computes only the parity bits rather than the whole codeword, the receiver can read out the message without decoding when the channel is clean, and a decoder failure still leaves a usable if uncertain message.
KEY TERMS
• systematic code
• information positions
• parity positions
• transparent decoding
• implementation cost
TAKEAWAY
Systematic form costs nothing in distance and buys a cheaper encoder plus a message you can read without decoding.
DIAGRAM FOR PHASE 2
A single codeword drawn as a horizontal strip of n cells, the first k tinted green and bracketed "message, copied verbatim", the last n-k tinted blue and bracketed "parity, computed". Arrows rise from the gree…
Source: Digital Communication Systems, 1st ed., Ch. 10, pp. 582-586
CO5 | Bloom L3 | visual id: systematic-codeword-layout
Notes: What to say: Give them the idea before the formalism. Say it plainly first: A code is systematic when the k message bits appear unchanged in fixed positions of the codeword, with the remaining n-k positions holding parity bits com… Then add the part they are examined on - Systematic form costs nothing in distance and buys a cheaper encoder plus a message you can read without decoding. Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "systematic code" constrain here, and what would break if it did not hold? Animation instructions: the strip of n cells draws, then the first k tint green with their bracket, then the last n-k tint blue with theirs, then the arrows rise from the message cells into the XOR network one parity bit at a time and land, then the two cost boxes appear side by side, then the footer note lands. Transition style: Fade [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 4: Error Control Coding: Linear Block and Cyclic Codes. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 10, pp. 582-586. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 18
Systematic form and why encoders prefer it - how it works
The procedure in order, and what each pass costs you.
VTU BEC503 | Module 4
Systematic form and why encoders pref…
18
1. Apply row operations to G until the first k columns form the identity
2. Read off P from the remaining n-k columns
3. Encode by copying the message into the first k positions
4. Compute the parity bits as mP
5. Append the parity bits to complete the codeword
COST AND BEHAVIOUR
Best: only n-k parity bits need computing
Typical: k(n-k) operations rather than kn
Worst: reaching systematic form may require column permutation as well as row operations
WHAT THAT MEANS
A column permutation gives an equivalent code with the same distance, so it is always permitted.
Source: Digital Communication Systems, 1st ed., Ch. 10, pp. 582-586 | CO5 | Bloom L3
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Apply row operations to G until the first k columns form the identity - and check everyone has written it before moving on. At the cost panel, translate it: A column permutation gives an equivalent code with the same distance, so it is always permitted. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 4: Error Control Coding: Linear Block and Cyclic Codes. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 10, pp. 582-586. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 19
Systematic form and why encoders prefer it - worked example
One concrete case, carried all the way to a stated number.
VTU BEC503 | Module 4
Systematic form and why encoders pref…
19
GIVEN
A (7,4) systematic code, message 1011, P = [[1,1,0],[0,1,1],[1,1,1],[1,0,1]].
1. Message occupies positions 1 to 4: 1011
2. Parity bit 1: 1 XOR 0 XOR 1 XOR 1 = 1 (rows selected by the 1s in m, first column of P)
3. Parity bit 2: 1 XOR 0 XOR 1 XOR 0 = 0
4. Parity bit 3: 0 XOR 0 XOR 1 XOR 1 = 0
RESULT
Codeword 1011100. The message is readable directly from the first four bits with no decoding at all.
G = [ I_k | P ]
c = m * G = [ m | m*P ]
message part: c_1..c_k = m
parity part: c_(k+1)..c_n = m * P
Encoder computes only n-k bits.
THE MISTAKE STUDENTS MAKE
Students believe systematic codes are weaker because the message is exposed. Distance properties are unchanged by the row operations that produce systematic form, and error correction has nothing to do with concealment.
Source: Digital Communication Systems, 1st ed., Ch. 10, pp. 582-586 | CO5 | Bloom L3
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is A (7,4) systematic code, message 1011, P = [[1,1,0],[0,1,1],[1,1,1],[1,0,1]]. Work at the pace of the slowest note-taker and land hard on the result: Codeword 1011100. The message is readable directly from the first four bits with no decoding at all. Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 4: Error Control Coding: Linear Block and Cyclic Codes. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 10, pp. 582-586. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 20
The syndrome and its properties
What it is, why it works, and what it costs.
VTU BEC503 | Module 4
The syndrome and its properties
20
THE MECHANISM
The syndrome of a received vector r is s = r H transpose, an (n-k)-bit vector. Writing r = c + e where c is the transmitted codeword and e the error pattern, and using cH transpose = 0, gives s = eH transpose: the syndrome depends only on the error pattern and not at all on which codeword was sent. That single property is what makes syndrome decoding possible, because it reduces a search over 2^k codewords to a lookup over 2^(n-k) syndromes. A zero syndrome means no detectable error; a non-zero syndrome identifies the coset the error lies in, though not the error uniquely.
KEY TERMS
• syndrome
• error pattern
• received vector
• coset
• independence from codeword
TAKEAWAY
s = eH transpose: the syndrome sees the error and is blind to the codeword, which is what shrinks decoding to a small lookup.
DIAGRAM FOR PHASE 2
Three parallel horizontal tracks, each showing a different transmitted codeword c1, c2, c3 with the same error pattern e added by an XOR symbol, producing three different received vectors r1, r2, r3. All three…
Source: Digital Communication Systems, 1st ed., Ch. 10, pp. 586-590
CO4 | Bloom L4 | visual id: syndrome-independence
Notes: What to say: Give them the idea before the formalism. Say it plainly first: The syndrome of a received vector r is s = r H transpose, an (n-k)-bit vector. Then add the part they are examined on - s = eH transpose: the syndrome sees the error and is blind to the codeword, which is what shrinks decoding to a small lookup. Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "syndrome" constrain here, and what would break if it did not hold? Animation instructions: the three tracks draw top to bottom with their codewords, then the error pattern drops onto all three simultaneously via XOR symbols, then the three distinct received vectors appear, then all three arrows converge into the H transpose block, then the single syndrome pops out and is circled, then the size comparison appears with the strike-through drawing last. Transition style: Fade [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 4: Error Control Coding: Linear Block and Cyclic Codes. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 10, pp. 586-590. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 21
The syndrome and its properties - how it works
The procedure in order, and what each pass costs you.
VTU BEC503 | Module 4
The syndrome and its properties
21
1. Receive the vector r of length n
2. Compute s = r H transpose over GF(2)
3. If s is zero, accept r as a codeword
4. If s is non-zero, look up the most likely error pattern with that syndrome
5. Correct by adding the looked-up error pattern to r
COST AND BEHAVIOUR
Best: zero syndrome needs no further work
Typical: (n-k) inner products to compute the syndrome
Worst: 2^(n-k) syndromes to store in the lookup table
WHAT THAT MEANS
The table size is exponential in the number of parity bits, which caps practical block lengths.
Source: Digital Communication Systems, 1st ed., Ch. 10, pp. 586-590 | CO4 | Bloom L4
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Receive the vector r of length n - and check everyone has written it before moving on. At the cost panel, translate it: The table size is exponential in the number of parity bits, which caps practical block lengths. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 4: Error Control Coding: Linear Block and Cyclic Codes. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 10, pp. 586-590. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 22
The syndrome and its properties - worked example
One concrete case, carried all the way to a stated number.
VTU BEC503 | Module 4
The syndrome and its properties
22
GIVEN
H = [[1,0,1,0],[1,1,0,1]], codeword 1110 transmitted, error in position 3 giving r = 1100.
1. s1 = 1x1 + 1x0 + 0x1 + 0x0 = 1
2. s2 = 1x1 + 1x1 + 0x0 + 0x1 = 0
3. Syndrome = 10
4. Compare with column 3 of H, which is [1,0] transpose — a match
RESULT
The syndrome equals the third column of H, correctly identifying position 3 as the error location.
s = r * H^T (n-k)-bit syndrome
r = c + e
s = (c + e) H^T = c H^T + e H^T = 0 + e H^T = e H^T
s = 0 => r is a codeword (possibly an undetected error)
s = column j => single error in position j
THE MISTAKE STUDENTS MAKE
Students conclude a zero syndrome means no errors occurred. It means no detectable error: if the error pattern happens to be a valid codeword, the syndrome is zero and the error passes silently.
Source: Digital Communication Systems, 1st ed., Ch. 10, pp. 586-590 | CO4 | Bloom L4
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is H = [[1,0,1,0],[1,1,0,1]], codeword 1110 transmitted, error in position 3 giving r = 1100. Work at the pace of the slowest note-taker and land hard on the result: The syndrome equals the third column of H, correctly identifying position 3 as the error location. Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 4: Error Control Coding: Linear Block and Cyclic Codes. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 10, pp. 586-590. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 23
Minimum distance and minimum weight
What it is, why it works, and what it costs.
VTU BEC503 | Module 4
Minimum distance and minimum weight
23
THE MECHANISM
The Hamming distance between two codewords is the number of positions in which they differ, and the minimum distance d_min of a code is the smallest such distance over all pairs. For a linear code, the difference of two codewords is itself a codeword, so d_min equals the minimum Hamming weight over all non-zero codewords — a search over 2^k - 1 words instead of over all pairs. This single number determines everything about the code strength: how many errors it can detect, how many it can correct, and whether a given error pattern will be caught or slip through.
KEY TERMS
• Hamming distance
• Hamming weight
• minimum distance
• linearity consequence
• code strength
TAKEAWAY
For a linear code, minimum distance equals minimum weight, and that one number fixes all detection and correction guarantees.
DIAGRAM FOR PHASE 2
Left panel: two codewords written one above the other with differing bit positions highlighted in red and a count beneath labelled "distance 3". Right panel: their XOR shown as a single word with the same thre…
Source: Digital Communication Systems, 1st ed., Ch. 10, pp. 586-590
CO4 | Bloom L4 | visual id: distance-equals-weight
Notes: What to say: Give them the idea before the formalism. Say it plainly first: The Hamming distance between two codewords is the number of positions in which they differ, and the minimum distance d_min of a code is the smallest such… Then add the part they are examined on - For a linear code, minimum distance equals minimum weight, and that one number fixes all detection and correction guarantees. Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "Hamming distance" constrain here, and what would break if it did not hold? Animation instructions: the two codewords appear, then the differing positions light red one at a time, then the distance count lands, then the XOR word forms on the right with its set bits appearing simultaneously, then the equals sign between the panels flashes, then the codeword weight list fills row by row with the minimum highlighting last, then the side card slides in. Transition style: Fade [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 4: Error Control Coding: Linear Block and Cyclic Codes. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 10, pp. 586-590. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 24
Minimum distance and minimum weight - how it works
The procedure in order, and what each pass costs you.
VTU BEC503 | Module 4
Minimum distance and minimum weight
24
1. List all non-zero codewords of the code
2. Compute the Hamming weight of each
3. Take the minimum as d_min
4. Derive detection capability as d_min - 1
5. Derive correction capability as the floor of (d_min - 1)/2
COST AND BEHAVIOUR
Best: weight enumeration over 2^k - 1 words rather than all pairs
Typical: still exponential in k for a general code
Worst: computing d_min for an arbitrary linear code is NP-hard
WHAT THAT MEANS
Structured families such as Hamming and BCH codes have known d_min by construction, which is much of their appeal.
Source: Digital Communication Systems, 1st ed., Ch. 10, pp. 586-590 | CO4 | Bloom L4
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - List all non-zero codewords of the code - and check everyone has written it before moving on. At the cost panel, translate it: Structured families such as Hamming and BCH codes have known d_min by construction, which is much of their appeal. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 4: Error Control Coding: Linear Block and Cyclic Codes. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 10, pp. 586-590. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 25
Minimum distance and minimum weight - worked example
One concrete case, carried all the way to a stated number.
VTU BEC503 | Module 4
Minimum distance and minimum weight
25
GIVEN
The (5,2) code with codewords 00000, 10111, 01101, 11010.
1. Weight of 10111 = 4
2. Weight of 01101 = 3
3. Weight of 11010 = 3
4. Minimum non-zero weight = 3
RESULT
d_min = 3, so the code detects up to 2 errors and corrects 1. Checking all six pairwise distances would give the same answer with three times the work.
d(c1, c2) = number of differing positions
w(c) = number of ones in c
Linear code: d_min = min over non-zero c of w(c)
Detect: up to d_min - 1 errors
Correct: up to t = floor( (d_min - 1)/2 ) errors
THE MISTAKE STUDENTS MAKE
Students compute the minimum weight including the all-zero codeword and obtain d_min = 0. The zero word is always present and must be excluded; the minimum is over non-zero codewords only.
Source: Digital Communication Systems, 1st ed., Ch. 10, pp. 586-590 | CO4 | Bloom L4
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is The (5,2) code with codewords 00000, 10111, 01101, 11010. Work at the pace of the slowest note-taker and land hard on the result: d_min = 3, so the code detects up to 2 errors and corrects 1. Checking all six pairwise distances would give the same answer with… Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 4: Error Control Coding: Linear Block and Cyclic Codes. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 10, pp. 586-590. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 26
Error detection and correction capability
What it is, why it works, and what it costs.
VTU BEC503 | Module 4
Error detection and correction capabi…
26
THE MECHANISM
A code with minimum distance d_min detects any error pattern of up to d_min - 1 errors, because fewer than d_min changes cannot turn one codeword into another. It corrects up to t = floor((d_min - 1)/2) errors, because spheres of radius t around each codeword are disjoint when 2t < d_min, so a received word within t of a codeword is closer to that one than to any other. Detection and correction trade against each other: a code with d_min = 5 can correct two errors, or detect four while correcting none, or correct one while detecting three.
KEY TERMS
• detection capability
• correction capability
• sphere packing
• decoding sphere
• guarantee
TAKEAWAY
d_min buys either detection or correction, and you choose the split — correcting t always costs 2t of the distance budget.
DIAGRAM FOR PHASE 2
Two codeword points drawn in a schematic space, separated by a labelled distance d_min = 5. Around each, a circle of radius t = 2 is drawn and lightly tinted, the two circles clearly disjoint with a visible ga…
Source: Digital Communication Systems, 1st ed., Ch. 10, pp. 586-590
CO4 | Bloom L4 | visual id: decoding-spheres
Notes: What to say: Give them the idea before the formalism. Say it plainly first: A code with minimum distance d_min detects any error pattern of up to d_min - 1 errors, because fewer than d_min changes cannot turn one codeword into ano… Then add the part they are examined on - d_min buys either detection or correction, and you choose the split — correcting t always costs 2t of the distance budget. Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "detection capability" constrain here, and what would break if it did not hold? Animation instructions: the two codeword points appear with the distance bracket between them, then the two spheres inflate around them and the gap is bracketed, then the first received point drops inside a sphere and its correction arrow snaps, then the second point drops in the gap with its question mark, then the slider appears and steps through its three settings. Transition style: Fade [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 4: Error Control Coding: Linear Block and Cyclic Codes. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 10, pp. 586-590. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 27
Error detection and correction capability - how it works
The procedure in order, and what each pass costs you.
VTU BEC503 | Module 4
Error detection and correction capabi…
27
1. Compute d_min for the code
2. For pure detection, the guarantee is d_min - 1 errors
3. For pure correction, compute t = floor((d_min - 1)/2)
4. For a mixed strategy, choose l detections and t corrections with t + l < d_min and l >= t
5. Verify the decoding spheres of radius t remain disjoint
COST AND BEHAVIOUR
Best: odd d_min uses the distance budget fully for correction
Typical: t grows as half of d_min
Worst: even d_min wastes one unit unless a mixed strategy is used
WHAT THAT MEANS
This is why most useful codes are designed with odd minimum distance.
Source: Digital Communication Systems, 1st ed., Ch. 10, pp. 586-590 | CO4 | Bloom L4
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Compute d_min for the code - and check everyone has written it before moving on. At the cost panel, translate it: This is why most useful codes are designed with odd minimum distance. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 4: Error Control Coding: Linear Block and Cyclic Codes. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 10, pp. 586-590. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 28
Error detection and correction capability - worked example
One concrete case, carried all the way to a stated number.
VTU BEC503 | Module 4
Error detection and correction capabi…
28
GIVEN
Codes with d_min = 3, 4 and 5.
1. d_min = 3: detect 2, correct floor(2/2) = 1
2. d_min = 4: detect 3, correct floor(3/2) = 1 — the extra distance buys no extra correction
3. d_min = 5: detect 4, correct floor(4/2) = 2
4. The d_min = 4 code can instead correct 1 and detect 2 simultaneously
RESULT
Going from d_min = 3 to 4 adds detection but no correction. Only odd increments buy correction capability, which is why d_min = 5 is the next useful step.
Detection only: detects up to d_min - 1 errors
Correction only: t = floor( (d_min - 1) / 2 )
Simultaneous: correct t and detect l, with
t + l + 1 <= d_min and l >= t
Spheres of radius t are disjoint iff 2t < d_min.
THE MISTAKE STUDENTS MAKE
Students assume a code corrects every pattern of t or fewer errors and detects everything beyond. Beyond t errors the decoder may silently decode to the wrong codeword, producing a confident wrong answer rather than a detected failure.
Source: Digital Communication Systems, 1st ed., Ch. 10, pp. 586-590 | CO4 | Bloom L4
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is Codes with d_min = 3, 4 and 5. Work at the pace of the slowest note-taker and land hard on the result: Going from d_min = 3 to 4 adds detection but no correction. Only odd increments buy correction capability, which is why d_min = 5… Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 4: Error Control Coding: Linear Block and Cyclic Codes. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 10, pp. 586-590. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 29
Syndrome decoding and the standard array
What it is, why it works, and what it costs.
VTU BEC503 | Module 4
Syndrome decoding and the standard ar…
29
THE MECHANISM
The standard array arranges all 2^n binary n-tuples into 2^(n-k) rows called cosets, each row being a coset of the code obtained by adding a fixed error pattern to every codeword. The minimum-weight member of each coset is its coset leader and is the most likely error pattern for that row, since lower weight means fewer bit flips and therefore higher probability. All members of a coset share the same syndrome, so decoding reduces to computing the syndrome, looking up the coset leader, and adding it to the received word. This is exactly maximum likelihood decoding on a binary symmetric channel, implemented as a table lookup.
KEY TERMS
• standard array
• coset
• coset leader
• syndrome table
• maximum likelihood decoding
TAKEAWAY
Every coset has one syndrome and one most-likely error; decoding is compute-syndrome, look up leader, add.
DIAGRAM FOR PHASE 2
A rectangular table. The top row lists all 2^k codewords starting with the all-zero word in the leftmost column. Each subsequent row is a coset, with its leftmost entry — the coset leader — tinted and its weig…
Source: Digital Communication Systems, 1st ed., Ch. 10, pp. 590-593
CO5 | Bloom L4 | visual id: standard-array-cosets
Notes: What to say: Give them the idea before the formalism. Say it plainly first: The standard array arranges all 2^n binary n-tuples into 2^(n-k) rows called cosets, each row being a coset of the code obtained by adding a fixed error p… Then add the part they are examined on - Every coset has one syndrome and one most-likely error; decoding is compute-syndrome, look up leader, add. Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "standard array" constrain here, and what would break if it did not hold? Animation instructions: the top row of codewords fills left to right, then each coset row fills in turn with its leader tinting, then the syndrome column fills, then three cells in one row highlight and converge on their shared syndrome, then the received word is circled, then the leftward and upward arrows draw in sequence to the decoded codeword. Transition style: Fade [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 4: Error Control Coding: Linear Block and Cyclic Codes. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 10, pp. 590-593. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 30
Syndrome decoding and the standard array - how it works
The procedure in order, and what each pass costs you.
VTU BEC503 | Module 4
Syndrome decoding and the standard ar…
30
1. List all codewords as the first row of the array
2. Choose an unused n-tuple of minimum weight as the next coset leader
3. Fill that row by adding the leader to every codeword
4. Repeat until all 2^n tuples are placed
5. Tabulate each coset leader against its syndrome and decode by lookup
COST AND BEHAVIOUR
Best: lookup is a single table access once built
Typical: table has 2^(n-k) entries
Worst: building the full standard array costs 2^n operations
WHAT THAT MEANS
Only the syndrome-to-leader table need be stored, not the whole array.
Source: Digital Communication Systems, 1st ed., Ch. 10, pp. 590-593 | CO5 | Bloom L4
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - List all codewords as the first row of the array - and check everyone has written it before moving on. At the cost panel, translate it: Only the syndrome-to-leader table need be stored, not the whole array. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 4: Error Control Coding: Linear Block and Cyclic Codes. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 10, pp. 590-593. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 31
Syndrome decoding and the standard array - worked example
One concrete case, carried all the way to a stated number.
VTU BEC503 | Module 4
Syndrome decoding and the standard ar…
31
GIVEN
A (5,2) code, so 2^3 = 8 cosets and 4 codewords per row.
1. Row 0: the four codewords, coset leader 00000, syndrome 000
2. Row 1: leader 00001, syndrome equal to the fifth column of H
3. Rows 2 to 5: the remaining single-error patterns
4. Rows 6 and 7: two-error patterns, since single errors are exhausted
RESULT
Five of the eight cosets have single-error leaders and are corrected reliably; the last two have weight-2 leaders, so only two of the ten possible double errors are corrected.
Coset of e: { c + e : c in C }
All members of a coset share the syndrome s = e H^T
Coset leader = minimum-weight member = most likely error
Decode: s = r H^T -> look up leader e_hat -> c_hat = r + e_hat
THE MISTAKE STUDENTS MAKE
Students choose an arbitrary member of a coset as its leader. The leader must be of minimum weight, since that is what makes the decoder maximum likelihood; any other choice systematically decodes to the wrong codeword.
Source: Digital Communication Systems, 1st ed., Ch. 10, pp. 590-593 | CO5 | Bloom L4
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is A (5,2) code, so 2^3 = 8 cosets and 4 codewords per row. Work at the pace of the slowest note-taker and land hard on the result: Five of the eight cosets have single-error leaders and are corrected reliably; the last two have weight-2 leaders, so only two of… Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 4: Error Control Coding: Linear Block and Cyclic Codes. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 10, pp. 590-593. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 32
Hamming codes
What it is, why it works, and what it costs.
VTU BEC503 | Module 4
Hamming codes
32
THE MECHANISM
A Hamming code is a (2^m - 1, 2^m - 1 - m) code whose parity check matrix has as its columns all 2^m - 1 non-zero binary m-tuples, each appearing exactly once. Because every column is distinct and non-zero, no two columns sum to zero and no single column is zero, so d_min = 3 and the code corrects exactly one error. The construction has an elegant decoding consequence: the syndrome of a single error in position j is precisely column j of H, so if the columns are ordered as binary counting, the syndrome read as a binary number is the error address. Hamming codes are perfect: the decoding spheres of radius one tile the space exactly.
KEY TERMS
• Hamming code
• perfect code
• single error correcting
• column construction
• syndrome as address
TAKEAWAY
Order the columns of H as binary counting and the syndrome literally spells out which bit to flip.
DIAGRAM FOR PHASE 2
The parity check matrix of a (7,4) Hamming code drawn with its seven columns labelled 001, 010, 011, 100, 101, 110, 111 across the top, matching binary counting. Below, a received seven-bit word with one bit h…
Source: Digital Communication Systems, 1st ed., Ch. 10, pp. 590-593
CO5 | Bloom L4 | visual id: hamming-syndrome-address
Notes: What to say: Give them the idea before the formalism. Say it plainly first: A Hamming code is a (2^m - 1, 2^m - 1 - m) code whose parity check matrix has as its columns all 2^m - 1 non-zero binary m-tuples, each appearing exactly… Then add the part they are examined on - Order the columns of H as binary counting and the syndrome literally spells out which bit to flip. Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "Hamming code" constrain here, and what would break if it did not hold? Animation instructions: the matrix draws column by column with the binary labels appearing above each, then the received word appears with the corrupted bit reddening, then the syndrome block computes and 101 pops out, then the bold arrow travels from the syndrome to the matching column and down to the word position, then that bit flips green, then the perfect-code card slides in. Transition style: Fade [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 4: Error Control Coding: Linear Block and Cyclic Codes. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 10, pp. 590-593. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 33
Hamming codes - how it works
The procedure in order, and what each pass costs you.
VTU BEC503 | Module 4
Hamming codes
33
1. Choose m, giving n = 2^m - 1 and k = n - m
2. Build H with all non-zero m-bit columns, ordered as binary counting
3. Derive G from H by rearranging into systematic form if desired
4. Decode by computing the syndrome and reading it as a position index
5. Flip the indicated bit; a zero syndrome means no error
COST AND BEHAVIOUR
Best: decoding is one syndrome computation and one bit flip, no table at all
Typical: rate (2^m - 1 - m)/(2^m - 1) rises towards 1 as m grows
Worst: corrects only one error regardless of block length, so long Hamming codes are fragile
WHAT THAT MEANS
A (255,247) Hamming code has excellent rate and still fails on two errors in 255 bits.
Source: Digital Communication Systems, 1st ed., Ch. 10, pp. 590-593 | CO5 | Bloom L4
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Choose m, giving n = 2^m - 1 and k = n - m - and check everyone has written it before moving on. At the cost panel, translate it: A (255,247) Hamming code has excellent rate and still fails on two errors in 255 bits. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 4: Error Control Coding: Linear Block and Cyclic Codes. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 10, pp. 590-593. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 34
Hamming codes - worked example
One concrete case, carried all the way to a stated number.
VTU BEC503 | Module 4
Hamming codes
34
GIVEN
A (7,4) Hamming code, received word with an error in position 6.
1. Column 6 of H, with binary-counting order, is 110
2. Computing s = rH transpose gives 110
3. Read 110 as the binary number 6
4. Flip bit 6 of the received word
RESULT
The error is located and corrected without any lookup table — the syndrome is the address, which is why Hamming codes appear in memory ECC hardware.
n = 2^m - 1, k = n - m, d_min = 3
H columns = all non-zero m-bit vectors, each once
Syndrome s = column j => error in position j
Order columns as 1,2,...,n in binary => s IS the address
Perfect: 2^k * (1 + n) = 2^n
THE MISTAKE STUDENTS MAKE
Students expect a longer Hamming code to be stronger. Its d_min stays at 3 for every m, so it always corrects exactly one error; a (255,247) code has a far better rate than a (7,4) code and identical, minimal, error-correcting power.
Source: Digital Communication Systems, 1st ed., Ch. 10, pp. 590-593 | CO5 | Bloom L4
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is A (7,4) Hamming code, received word with an error in position 6. Work at the pace of the slowest note-taker and land hard on the result: The error is located and corrected without any lookup table — the syndrome is the address, which is why Hamming codes appear in m… Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 4: Error Control Coding: Linear Block and Cyclic Codes. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 10, pp. 590-593. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 35
Cyclic codes: definition and properties
What it is, why it works, and what it costs.
VTU BEC503 | Module 4
Cyclic codes: definition and properti…
35
THE MECHANISM
A cyclic code is a linear block code with the additional property that any cyclic shift of a codeword is also a codeword. Representing an n-bit word as a polynomial of degree less than n over GF(2), with bit i as the coefficient of x^i, turns a cyclic shift into multiplication by x modulo x^n - 1. The code then becomes an ideal in the ring of polynomials modulo x^n - 1, which is a very strong structural statement: every ideal in that ring is generated by a single polynomial. That is why a cyclic code needs only one generator polynomial rather than a whole matrix.
KEY TERMS
• cyclic code
• cyclic shift
• polynomial representation
• ideal
• structure
TAKEAWAY
Cyclic shift plus linearity means the whole code is generated by one polynomial instead of a k-by-n matrix.
DIAGRAM FOR PHASE 2
A circular arrangement of seven bit cells forming a ring, with the bit values written inside and an arrow indicating a one-position rotation. Beside it, the same word written as a polynomial, and below that th…
Source: Digital Communication Systems, 1st ed., Ch. 10, pp. 593-597
CO4 | Bloom L4 | visual id: cyclic-shift-as-multiplication
Notes: What to say: Give them the idea before the formalism. Say it plainly first: A cyclic code is a linear block code with the additional property that any cyclic shift of a codeword is also a codeword. Then add the part they are examined on - Cyclic shift plus linearity means the whole code is generated by one polynomial instead of a k-by-n matrix. Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "cyclic code" constrain here, and what would break if it did not hold? Animation instructions: the ring of cells draws with its bit values, then the rotation arrow sweeps once around and the bits shift one position with the wrapping bit highlighted as it comes round, then the polynomial form writes itself beside it, then the multiplied form appears below with the modulo note, then the storage comparison card slides in. Transition style: Fade [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 4: Error Control Coding: Linear Block and Cyclic Codes. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 10, pp. 593-597. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 36
Cyclic codes: definition and properties - how it works
The procedure in order, and what each pass costs you.
VTU BEC503 | Module 4
Cyclic codes: definition and properti…
36
1. Represent each codeword as a polynomial c(x) of degree less than n
2. Verify that x c(x) mod (x^n - 1) is also a codeword for every codeword
3. Identify the non-zero codeword of least degree: this is the generator polynomial g(x)
4. Confirm g(x) divides x^n - 1
5. Generate all codewords as multiples of g(x) modulo x^n - 1
COST AND BEHAVIOUR
Best: storage is one polynomial of n-k+1 coefficients
Typical: encoding by polynomial multiplication in a shift register
Worst: the cyclic requirement restricts which (n,k) pairs are achievable
WHAT THAT MEANS
g(x) must divide x^n - 1, which is a genuine constraint on the available code parameters.
Source: Digital Communication Systems, 1st ed., Ch. 10, pp. 593-597 | CO4 | Bloom L4
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Represent each codeword as a polynomial c(x) of degree less than n - and check everyone has written it before moving on. At the cost panel, translate it: g(x) must divide x^n - 1, which is a genuine constraint on the available code parameters. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 4: Error Control Coding: Linear Block and Cyclic Codes. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 10, pp. 593-597. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 37
Cyclic codes: definition and properties - worked example
One concrete case, carried all the way to a stated number.
VTU BEC503 | Module 4
Cyclic codes: definition and properti…
37
GIVEN
The codeword 1011000 of a (7,4) cyclic code.
1. Polynomial: 1 + x^2 + x^3
2. Cyclic shift right by one: 0101100
3. Polynomial: x + x^3 + x^4, which is x times the original
4. No wraparound occurred because the top coefficient was zero
RESULT
The shift corresponds exactly to multiplication by x. Had the highest coefficient been one, the modulo x^7 - 1 reduction would have wrapped it round to the constant term.
c = (c0, c1, ..., c_{n-1}) <-> c(x) = c0 + c1 x + ... + c_{n-1} x^{n-1}
Cyclic shift <-> x * c(x) mod (x^n - 1)
Code is an ideal in GF(2)[x]/(x^n - 1)
=> generated by a single g(x) with g(x) | (x^n - 1)
THE MISTAKE STUDENTS MAKE
Students test the cyclic property on one shift of one codeword. The property must hold for every codeword and every shift, which is guaranteed only when the generator polynomial divides x^n - 1.
Source: Digital Communication Systems, 1st ed., Ch. 10, pp. 593-597 | CO4 | Bloom L4
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is The codeword 1011000 of a (7,4) cyclic code. Work at the pace of the slowest note-taker and land hard on the result: The shift corresponds exactly to multiplication by x. Had the highest coefficient been one, the modulo x^7 - 1 reduction would ha… Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 4: Error Control Coding: Linear Block and Cyclic Codes. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 10, pp. 593-597. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 38
The generator polynomial
What it is, why it works, and what it costs.
VTU BEC503 | Module 4
The generator polynomial
38
THE MECHANISM
The generator polynomial g(x) of an (n,k) cyclic code is the unique monic non-zero codeword polynomial of least degree, and that degree is exactly n-k. Every codeword is a polynomial multiple of g(x), and conversely every multiple of g(x) of degree less than n is a codeword, so the code is completely described by g(x). The generator must divide x^n - 1, which means the available cyclic codes of length n are found by factoring x^n - 1 over GF(2) and taking products of its irreducible factors. Choosing which factors to include is the design decision that fixes both the rate and the minimum distance.
KEY TERMS
• generator polynomial
• degree n-k
• divisor of x^n - 1
• code construction
• factorisation
TAKEAWAY
Factor x^n - 1 and every cyclic code of length n falls out; picking factors picks your rate and your distance together.
DIAGRAM FOR PHASE 2
A factorisation tree with x^7 - 1 at the top branching into three irreducible factors: (x + 1), (x^3 + x + 1) and (x^3 + x^2 + 1). Below, a table lists several products of these factors as candidate generator…
Source: Digital Communication Systems, 1st ed., Ch. 10, pp. 593-597
CO5 | Bloom L4 | visual id: factoring-x7-minus-1
Notes: What to say: Give them the idea before the formalism. Say it plainly first: The generator polynomial g(x) of an (n,k) cyclic code is the unique monic non-zero codeword polynomial of least degree, and that degree is exactly n-k. Then add the part they are examined on - Factor x^n - 1 and every cyclic code of length n falls out; picking factors picks your rate and your distance together. Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "generator polynomial" constrain here, and what would break if it did not hold? Animation instructions: x^7 - 1 appears at the top, then the three factor branches draw downward one at a time, then the table draws its header, then each row fills in turn with its parameters, then the Hamming row highlights and the two factors it uses tint simultaneously with connecting arrows drawing. Transition style: Fade [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 4: Error Control Coding: Linear Block and Cyclic Codes. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 10, pp. 593-597. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 39
The generator polynomial - how it works
The procedure in order, and what each pass costs you.
VTU BEC503 | Module 4
The generator polynomial
39
1. Factor x^n - 1 into irreducible polynomials over GF(2)
2. Choose a subset of factors whose product has degree n-k
3. Take that product as g(x)
4. Generate codewords as m(x) g(x) for all messages m(x) of degree less than k
5. Determine d_min from the structure, or by weight enumeration for small codes
COST AND BEHAVIOUR
Best: factorisations of x^n - 1 are tabulated for common n
Typical: encoding is a polynomial multiply of degree n-k
Worst: choosing factors to maximise d_min is the hard design problem
WHAT THAT MEANS
BCH codes solve exactly this by choosing factors with prescribed roots to guarantee d_min.
Source: Digital Communication Systems, 1st ed., Ch. 10, pp. 593-597 | CO5 | Bloom L4
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Factor x^n - 1 into irreducible polynomials over GF(2) - and check everyone has written it before moving on. At the cost panel, translate it: BCH codes solve exactly this by choosing factors with prescribed roots to guarantee d_min. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 4: Error Control Coding: Linear Block and Cyclic Codes. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 10, pp. 593-597. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 40
The generator polynomial - worked example
One concrete case, carried all the way to a stated number.
VTU BEC503 | Module 4
The generator polynomial
40
GIVEN
n = 7, so factor x^7 - 1 = (x+1)(x^3+x+1)(x^3+x^2+1).
1. Choose g(x) = x^3 + x + 1, of degree 3
2. Then n - k = 3, so k = 4, giving a (7,4) code
3. Encode m = 1011, that is m(x) = 1 + x^2 + x^3
4. c(x) = m(x)g(x) = (1 + x^2 + x^3)(1 + x + x^3)
RESULT
Expanding modulo 2 gives 1 + x + x^2 + x^3 + x^4 + ... — the (7,4) cyclic Hamming code, with d_min = 3.
g(x) monic, least degree, g(x) | (x^n - 1)
deg g(x) = n - k
Codewords: c(x) = m(x) * g(x), deg m(x) < k
n = 7: x^7 - 1 = (x+1)(x^3+x+1)(x^3+x^2+1)
g(x) = x^3+x+1 => (7,4) Hamming
THE MISTAKE STUDENTS MAKE
Students pick a generator polynomial of the right degree without checking that it divides x^n - 1. If it does not, the resulting code is linear but not cyclic, and the shift-register encoder and syndrome circuits built on that assumption fail.
Source: Digital Communication Systems, 1st ed., Ch. 10, pp. 593-597 | CO5 | Bloom L4
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is n = 7, so factor x^7 - 1 = (x+1)(x^3+x+1)(x^3+x^2+1). Work at the pace of the slowest note-taker and land hard on the result: Expanding modulo 2 gives 1 + x + x^2 + x^3 + x^4 + ... — the (7,4) cyclic Hamming code, with d_min = 3. Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 4: Error Control Coding: Linear Block and Cyclic Codes. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 10, pp. 593-597. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 41
Parity check polynomial and matrix forms
What it is, why it works, and what it costs.
VTU BEC503 | Module 4
Parity check polynomial and matrix fo…
41
THE MECHANISM
The parity check polynomial is h(x) = (x^n - 1)/g(x), of degree k, and it plays for cyclic codes the role H plays for general linear codes: c(x)h(x) is congruent to zero modulo x^n - 1 for every codeword. The generator matrix is built by writing the coefficients of g(x) in the first row and cyclically shifting right for each subsequent row, giving a k-by-n matrix. The parity check matrix is built the same way from the reciprocal of h(x), with n-k rows. The two polynomial and matrix descriptions are equivalent, and the polynomial form is preferred for hardware while the matrix form is clearer for analysis.
KEY TERMS
• parity check polynomial
• h(x)
• generator matrix from g(x)
• reciprocal polynomial
• matrix construction
TAKEAWAY
h(x) = (x^n-1)/g(x) is the polynomial parity check; shifting coefficients builds G and H from the two polynomials.
DIAGRAM FOR PHASE 2
Top: the division x^n - 1 divided by g(x) shown producing h(x), all three polynomials written out for a (7,4) example. Middle: a k-by-n generator matrix being built, with g(x) coefficients placed in the first…
Source: Digital Communication Systems, 1st ed., Ch. 10, pp. 597-601
CO5 | Bloom L4 | visual id: g-h-polynomial-matrices
Notes: What to say: Give them the idea before the formalism. Say it plainly first: The parity check polynomial is h(x) = (x^n - 1)/g(x), of degree k, and it plays for cyclic codes the role H plays for general linear codes: c(x)h(x) is co… Then add the part they are examined on - h(x) = (x^n-1)/g(x) is the polynomial parity check; shifting coefficients builds G and H from the two polynomials. Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "parity check polynomial" constrain here, and what would break if it did not hold? Animation instructions: the division writes itself and h(x) pops out, then the generator matrix first row fills with g coefficients, then each subsequent row slides in shifted one place right, forming the diagonal band, then the reciprocal note appears, then the parity check matrix builds the same way row by row. Transition style: Fade [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 4: Error Control Coding: Linear Block and Cyclic Codes. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 10, pp. 597-601. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 42
Parity check polynomial and matrix forms - how it works
The procedure in order, and what each pass costs you.
VTU BEC503 | Module 4
Parity check polynomial and matrix fo…
42
1. Compute h(x) = (x^n - 1)/g(x) by polynomial division over GF(2)
2. Build G by placing g(x) coefficients in row 1 and shifting right for each further row
3. Form the reciprocal of h(x) by reversing its coefficient order
4. Build H the same way from the reciprocal, with n-k rows
5. Verify G H transpose = 0
COST AND BEHAVIOUR
Best: both matrices follow mechanically from two polynomials
Typical: one polynomial division of degree n
Worst: these matrices are not in systematic form and need reduction if that is wanted
WHAT THAT MEANS
Systematic cyclic encoding uses a remainder rather than a product, which keeps the message visible.
Source: Digital Communication Systems, 1st ed., Ch. 10, pp. 597-601 | CO5 | Bloom L4
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Compute h(x) = (x^n - 1)/g(x) by polynomial division over GF(2) - and check everyone has written it before moving on. At the cost panel, translate it: Systematic cyclic encoding uses a remainder rather than a product, which keeps the message visible. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 4: Error Control Coding: Linear Block and Cyclic Codes. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 10, pp. 597-601. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 43
Parity check polynomial and matrix forms - worked example
One concrete case, carried all the way to a stated number.
VTU BEC503 | Module 4
Parity check polynomial and matrix fo…
43
GIVEN
n = 7, g(x) = x^3 + x + 1.
1. h(x) = (x^7 - 1)/(x^3 + x + 1) = x^4 + x^2 + x + 1
2. Degree of h is 4 = k, as required
3. G row 1: coefficients of g, 1101000
4. G rows 2 to 4: 0110100, 0011010, 0001101
RESULT
A 4-by-7 generator matrix with the characteristic diagonal band. The four rows are the four cyclic shifts of g that fit within seven positions.
h(x) = (x^n - 1) / g(x), deg h = k
c(x) * h(x) = 0 mod (x^n - 1) for every codeword
G rows: g(x), x g(x), ..., x^{k-1} g(x)
H rows: built from the reciprocal of h(x)
G * H^T = 0
THE MISTAKE STUDENTS MAKE
Students build H directly from h(x) without reversing the coefficient order. The reciprocal is required, and omitting it produces a matrix that does not annihilate the code.
Source: Digital Communication Systems, 1st ed., Ch. 10, pp. 597-601 | CO5 | Bloom L4
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is n = 7, g(x) = x^3 + x + 1. Work at the pace of the slowest note-taker and land hard on the result: A 4-by-7 generator matrix with the characteristic diagonal band. The four rows are the four cyclic shifts of g that fit within se… Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 4: Error Control Coding: Linear Block and Cyclic Codes. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 10, pp. 597-601. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 44
Systematic cyclic encoding with a shift register
What it is, why it works, and what it costs.
VTU BEC503 | Module 4
Systematic cyclic encoding with a shi…
44
THE MECHANISM
Systematic cyclic encoding multiplies the message polynomial by x^(n-k) to shift it into the high-order positions, divides by g(x), and appends the remainder as the parity bits. The resulting codeword is x^(n-k)m(x) + r(x), which is divisible by g(x) by construction and carries the message unchanged in its top k positions. The hardware is a shift register of n-k stages with feedback taps at the positions of the non-zero coefficients of g(x), which performs the polynomial division as the message bits are clocked in. This is why cyclic codes dominate practice: the encoder is a handful of flip-flops and XOR gates rather than a matrix multiplier.
KEY TERMS
• shift register encoder
• remainder
• systematic cyclic
• feedback taps
• division circuit
TAKEAWAY
Shift the message up, divide by g(x), append the remainder — and the whole operation is n-k flip-flops and a few XOR gates.
DIAGRAM FOR PHASE 2
A shift register of three stages drawn as boxes in a row, with XOR gates inserted between stages at positions matching the non-zero coefficients of g(x) = 1 + x + x^3, and a feedback line running from the outp…
Source: Digital Communication Systems, 1st ed., Ch. 10, pp. 597-601
CO5 | Bloom L5 | visual id: cyclic-shift-register-encoder
Notes: What to say: Give them the idea before the formalism. Say it plainly first: Systematic cyclic encoding multiplies the message polynomial by x^(n-k) to shift it into the high-order positions, divides by g(x), and appends the remain… Then add the part they are examined on - Shift the message up, divide by g(x), append the remainder — and the whole operation is n-k flip-flops and a few XOR gates. Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "shift register encoder" constrain here, and what would break if it did not hold? Animation instructions: the three register stages draw left to right, then the XOR gates drop into their tap positions, then the feedback line sweeps from the output back around to the taps, then the input arrow and switch appear, then the timing table fills row by row as a pulse travels the register once per row, with the last three rows shading as they fill. Transition style: Fade [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 4: Error Control Coding: Linear Block and Cyclic Codes. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 10, pp. 597-601. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 45
Systematic cyclic encoding with a shift register - how it works
The procedure in order, and what each pass costs you.
VTU BEC503 | Module 4
Systematic cyclic encoding with a shi…
45
1. Multiply the message polynomial by x^(n-k)
2. Divide the result by g(x) using polynomial long division over GF(2)
3. Take the remainder r(x), of degree less than n-k
4. Form the codeword as x^(n-k) m(x) + r(x)
5. In hardware, clock the message into a shift register with taps at the coefficients of g(x)
COST AND BEHAVIOUR
Best: n-k flip-flops and at most n-k XOR gates
Typical: n clock cycles per codeword
Worst: the division is inherently serial, so throughput is one bit per clock
WHAT THAT MEANS
Parallel implementations process several bits per clock at the cost of more combinational logic.
Source: Digital Communication Systems, 1st ed., Ch. 10, pp. 597-601 | CO5 | Bloom L5
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Multiply the message polynomial by x^(n-k) - and check everyone has written it before moving on. At the cost panel, translate it: Parallel implementations process several bits per clock at the cost of more combinational logic. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 4: Error Control Coding: Linear Block and Cyclic Codes. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 10, pp. 597-601. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 46
Systematic cyclic encoding with a shift register - worked example
One concrete case, carried all the way to a stated number.
VTU BEC503 | Module 4
Systematic cyclic encoding with a shi…
46
GIVEN
g(x) = x^3 + x + 1, message 1011 so m(x) = 1 + x^2 + x^3, n = 7, k = 4.
1. x^3 m(x) = x^3 + x^5 + x^6
2. Divide by x^3 + x + 1 over GF(2)
3. The remainder is r(x) = 1, that is 100 in coefficient order
4. Codeword = message 1011 followed by parity 100
RESULT
Codeword 1011100, systematic with the message readable in the first four positions and divisible by g(x) by construction.
r(x) = [ x^{n-k} * m(x) ] mod g(x)
c(x) = x^{n-k} * m(x) + r(x)
c(x) is divisible by g(x) by construction.
Hardware: (n-k)-stage shift register, XOR taps at the
non-zero coefficients of g(x), feedback from the output.
THE MISTAKE STUDENTS MAKE
Students add the remainder without first shifting the message by x^(n-k). Without the shift the message and parity overlap in the same positions, the result is not systematic, and it is generally not a codeword either.
Source: Digital Communication Systems, 1st ed., Ch. 10, pp. 597-601 | CO5 | Bloom L5
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is g(x) = x^3 + x + 1, message 1011 so m(x) = 1 + x^2 + x^3, n = 7, k = 4. Work at the pace of the slowest note-taker and land hard on the result: Codeword 1011100, systematic with the message readable in the first four positions and divisible by g(x) by construction. Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 4: Error Control Coding: Linear Block and Cyclic Codes. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 10, pp. 597-601. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 47
Syndrome computation for cyclic codes and a worked example
What it is, why it works, and what it costs.
VTU BEC503 | Module 4
Syndrome computation for cyclic codes…
47
THE MECHANISM
For a cyclic code the syndrome of a received polynomial r(x) is simply its remainder on division by g(x), a computation performed by the same shift register used for encoding. A zero remainder means the received word is a codeword; a non-zero remainder identifies the error pattern up to a coset exactly as in the general linear case. The cyclic structure adds a decisive practical property: because a cyclic shift of the received word produces a predictable shift of the syndrome, one detection circuit can be reused for every error position, which is the basis of the Meggitt decoder. Cyclic codes are also natural burst-error detectors, catching any burst of length n-k or shorter.
KEY TERMS
• syndrome polynomial
• remainder on division
• error detection
• Meggitt decoder
• burst detection
TAKEAWAY
Syndrome equals remainder after division by g(x), and the cyclic structure lets one circuit handle every error position.
DIAGRAM FOR PHASE 2
A worked long division laid out vertically: the received polynomial as the dividend, g(x) as the divisor, the successive subtraction steps shown in XOR form with the bits struck through as they cancel, and the…
Source: Digital Communication Systems, 1st ed., Ch. 10, pp. 601-605
CO5 | Bloom L5 | visual id: cyclic-syndrome-worked
Notes: What to say: Give them the idea before the formalism. Say it plainly first: For a cyclic code the syndrome of a received polynomial r(x) is simply its remainder on division by g(x), a computation performed by the same shift regist… Then add the part they are examined on - Syndrome equals remainder after division by g(x), and the cyclic structure lets one circuit handle every error position. Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "syndrome polynomial" constrain here, and what would break if it did not hold? Animation instructions: the dividend writes itself, then g(x) appears as the divisor, then each subtraction step appears in turn with the cancelling bits striking through, then the remainder box draws and fills, then the shift register appears beside it and its final contents highlight, then the connecting arrow draws between the two identical values, then the footer card slides in. Transition style: Fade [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 4: Error Control Coding: Linear Block and Cyclic Codes. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 10, pp. 601-605. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 48
Syndrome computation for cyclic codes and a worked exam… - how it works
The procedure in order, and what each pass costs you.
VTU BEC503 | Module 4
Syndrome computation for cyclic codes…
48
1. Receive r(x) and divide by g(x) over GF(2)
2. Take the remainder s(x) as the syndrome
3. If s(x) is zero, accept the word
4. If not, use the syndrome to identify the error pattern, shifting cyclically as needed
5. Correct and extract the message from the systematic positions
COST AND BEHAVIOUR
Best: the same shift register serves for both encoding and syndrome computation
Typical: n clock cycles to compute the syndrome
Worst: full correction of multiple errors needs a more elaborate decoder
WHAT THAT MEANS
The Meggitt decoder exploits the cyclic shift property to correct with one detection circuit rather than 2^(n-k) table entries.
Source: Digital Communication Systems, 1st ed., Ch. 10, pp. 601-605 | CO5 | Bloom L5
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Receive r(x) and divide by g(x) over GF(2) - and check everyone has written it before moving on. At the cost panel, translate it: The Meggitt decoder exploits the cyclic shift property to correct with one detection circuit rather than 2^(n-k) table entries. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 4: Error Control Coding: Linear Block and Cyclic Codes. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 10, pp. 601-605. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 49
Syndrome computation for cyclic codes and a worked exam… - worked example
One concrete case, carried all the way to a stated number.
VTU BEC503 | Module 4
Syndrome computation for cyclic codes…
49
GIVEN
g(x) = x^3 + x + 1, transmitted codeword 1011100, an error in position 3 giving r = 1001100.
1. r(x) = 1 + x^3 + x^4
2. Divide by x^3 + x + 1 over GF(2)
3. The remainder is x^2 + x, that is 011
4. Compare against the syndrome table: 011 corresponds to an error at position 3
RESULT
The syndrome 011 locates the error at position 3. Adding the error pattern 0010000 to r recovers 1011100, the transmitted codeword.
s(x) = r(x) mod g(x) degree < n-k
s(x) = 0 => r(x) is a codeword
Cyclic property: syndrome of a shifted r is a predictable
shift of s, so one circuit covers all positions.
Burst detection: any burst of length <= n-k is detected.
THE MISTAKE STUDENTS MAKE
Students divide the received word by h(x) instead of g(x). The syndrome is the remainder on division by the generator polynomial; using the parity check polynomial gives a value that carries no useful error information.
Source: Digital Communication Systems, 1st ed., Ch. 10, pp. 601-605 | CO5 | Bloom L5
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is g(x) = x^3 + x + 1, transmitted codeword 1011100, an error in position 3 giving r = 1001100. Work at the pace of the slowest note-taker and land hard on the result: The syndrome 011 locates the error at position 3. Adding the error pattern 0010000 to r recovers 1011100, the transmitted codewor… Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 4: Error Control Coding: Linear Block and Cyclic Codes. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 10, pp. 601-605. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 50
Cyclic redundancy checks and burst error detection
What it is, why it works, and what it costs.
VTU BEC503 | Module 4
Cyclic redundancy checks and burst er…
50
THE MECHANISM
A cyclic redundancy check is a cyclic code used for detection only: the transmitter appends the remainder of the frame divided by a standard generator polynomial, and the receiver recomputes it and compares. Because the error polynomial of a burst of length l confined to consecutive positions factors as x^i b(x) with b of degree below l, any burst of length n-k or shorter leaves a non-zero remainder and is caught. The residual risk is quantified rather than eliminated: a random error pattern escapes detection with probability about 2^-(n-k), so a 32-bit CRC misses roughly one bad frame in four billion. This is why CRC-32 guards Ethernet frames while forward error correction handles the bit-level noise beneath it.
KEY TERMS
• CRC
• burst error
• detection-only code
• frame check sequence
• undetected error probability
TAKEAWAY
A CRC is a cyclic code spending all its redundancy on detection: every burst up to n-k caught, random patterns missed with probability 2^-(n-k).
DIAGRAM FOR PHASE 2
A frame drawn as a long horizontal strip with a short shaded tail labelled "FCS, 32 bits". Above the frame, a burst of contiguous red error bits spans 20 positions with a bracket labelled "burst length 20 <= n…
Source: Digital Communication Systems, 1st ed., Ch. 10, pp. 601-605
CO4 | Bloom L5 | visual id: crc-frame-and-burst
Notes: What to say: Give them the idea before the formalism. Say it plainly first: A cyclic redundancy check is a cyclic code used for detection only: the transmitter appends the remainder of the frame divided by a standard generator pol… Then add the part they are examined on - A CRC is a cyclic code spending all its redundancy on detection: every burst up to n-k caught, random patterns missed with p… Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "CRC" constrain here, and what would break if it did not hold? Animation instructions: the frame strip draws with its shaded FCS tail, then the contiguous burst reddens across its span and its bracket appears, then the scattered pattern appears below with its probability label, then the division block fills and the two outcome branches light in turn, then the footer generator list appears. Transition style: Fade [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 4: Error Control Coding: Linear Block and Cyclic Codes. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 10, pp. 601-605. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 51
Cyclic redundancy checks and burst error detection - how it works
The procedure in order, and what each pass costs you.
VTU BEC503 | Module 4
Cyclic redundancy checks and burst er…
51
1. Choose a standard generator polynomial of degree n-k, such as CRC-32
2. Append n-k zeros to the frame and divide by g(x)
3. Transmit the frame followed by the remainder as the frame check sequence
4. At the receiver, divide the whole received frame including the FCS by g(x)
5. Accept on a zero remainder and discard the frame otherwise
COST AND BEHAVIOUR
Best: the same shift register as any cyclic encoder, n-k stages
Typical: every burst of length n-k or shorter is detected with certainty
Worst: no correction capability at all: a failed check means discard and retransmit
WHAT THAT MEANS
CRC pairs naturally with ARQ, since detection without correction implies a retransmission request.
Source: Digital Communication Systems, 1st ed., Ch. 10, pp. 601-605 | CO4 | Bloom L5
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Choose a standard generator polynomial of degree n-k, such as CRC-32 - and check everyone has written it before moving on. At the cost panel, translate it: CRC pairs naturally with ARQ, since detection without correction implies a retransmission request. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 4: Error Control Coding: Linear Block and Cyclic Codes. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 10, pp. 601-605. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 52
Cyclic redundancy checks and burst error detection - worked example
One concrete case, carried all the way to a stated number.
VTU BEC503 | Module 4
Cyclic redundancy checks and burst er…
52
GIVEN
CRC-32 protecting a 1500-byte Ethernet frame, link block error rate 1e-6.
1. n - k = 32, so every burst of 32 bits or fewer is detected with certainty
2. Random patterns escape with probability about 2^-32 = 2.3 x 10^-10
3. At 1e-6 frame errors, undetected frames occur at 1e-6 x 2.3e-10
4. That is about 2.3 x 10^-16 per frame
RESULT
Roughly one undetected corrupt frame per 4 x 10^15 frames — at a billion frames a day, about one every eleven thousand years.
FCS = [ x^(n-k) * m(x) ] mod g(x)
Transmit: m(x) followed by FCS
Check: received frame mod g(x) == 0 ?
CRC-16: x^16 + x^15 + x^2 + 1
CRC-CCITT: x^16 + x^12 + x^5 + 1
CRC-32: degree 32, used by Ethernet
Bursts up to n-k always detected.
Random patterns missed with probability ~ 2^-(n-k).
THE MISTAKE STUDENTS MAKE
Students expect a CRC to correct errors because it is a cyclic code. It is deliberately detection-only: all n-k bits of redundancy buy detection strength, and a failed check triggers retransmission rather than repair.
Source: Digital Communication Systems, 1st ed., Ch. 10, pp. 601-605 | CO4 | Bloom L5
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is CRC-32 protecting a 1500-byte Ethernet frame, link block error rate 1e-6. Work at the pace of the slowest note-taker and land hard on the result: Roughly one undetected corrupt frame per 4 x 10^15 frames — at a billion frames a day, about one every eleven thousand years. Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 4: Error Control Coding: Linear Block and Cyclic Codes. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 10, pp. 601-605. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 53
One sentence per unit, six months from now
Units 1-7: what survives after the detail has gone.
VTU BEC503 | Module 4
Revision
53
01 FEC pays a fixed bandwidth premium to avoid the round trip; ARQ pays a round trip to avoid the premium. Latency decides.
02 Linearity means codewords form a subspace, and every simplification in this module follows from that single fact.
03 G is a basis in matrix form; encoding is c = mG, and row operations change the mapping without changing the code.
04 G builds, H tests, and G H transpose = 0 ties them together — the decoder only ever needs H.
05 Systematic form costs nothing in distance and buys a cheaper encoder plus a message you can read without decoding.
06 s = eH transpose: the syndrome sees the error and is blind to the codeword, which is what shrinks decoding to a small lookup.
07 For a linear code, minimum distance equals minimum weight, and that one number fixes all detection and correction guarantees.
Notes: What to say: Slow right down here. Read each takeaway aloud and then stop talking for a beat, because these are the sentences that should still be in their heads when they sit the SEE. Tell them explicitly that if they can reconstruct the reasoning behind any one of these lines they understand that unit, and if they can only recite it they do not. Pause cue: Pause for three seconds after each takeaway before moving to the next. Pointing cue: Point at each numbered takeaway in turn as you read it. Question to ask students: Ask: choose the takeaway you trust least and tell me what you would have to check to believe it. Animation instructions: Takeaway rows reveal one at a time from the top, each row highlighting briefly as it appears. Transition style: Fade [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 4: Error Control Coding: Linear Block and Cyclic Codes, 10 hours, TB1 (Haykin 2014) Ch. 10.1-10.5 pp. 577-605. TB1: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014. Revision consolidates all 16 unit takeaways. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 54
Revision, continued
Units 8-14: what survives after the detail has gone.
VTU BEC503 | Module 4
Revision
54
08 d_min buys either detection or correction, and you choose the split — correcting t always costs 2t of the distance budget.
09 Every coset has one syndrome and one most-likely error; decoding is compute-syndrome, look up leader, add.
10 Order the columns of H as binary counting and the syndrome literally spells out which bit to flip.
11 Cyclic shift plus linearity means the whole code is generated by one polynomial instead of a k-by-n matrix.
12 Factor x^n - 1 and every cyclic code of length n falls out; picking factors picks your rate and your distance together.
13 h(x) = (x^n-1)/g(x) is the polynomial parity check; shifting coefficients builds G and H from the two polynomials.
14 Shift the message up, divide by g(x), append the remainder — and the whole operation is n-k flip-flops and a few XOR gates.
Notes: What to say: Slow right down here. Read each takeaway aloud and then stop talking for a beat, because these are the sentences that should still be in their heads when they sit the SEE. Tell them explicitly that if they can reconstruct the reasoning behind any one of these lines they understand that unit, and if they can only recite it they do not. Pause cue: Pause for three seconds after each takeaway before moving to the next. Pointing cue: Point at each numbered takeaway in turn as you read it. Question to ask students: Ask: choose the takeaway you trust least and tell me what you would have to check to believe it. Animation instructions: Takeaway rows reveal one at a time from the top, each row highlighting briefly as it appears. Transition style: Fade [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 4: Error Control Coding: Linear Block and Cyclic Codes, 10 hours, TB1 (Haykin 2014) Ch. 10.1-10.5 pp. 577-605. TB1: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014. Revision consolidates all 16 unit takeaways. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 55
Revision, continued
Units 15-16: what survives after the detail has gone.
VTU BEC503 | Module 4
Revision
55
15 Syndrome equals remainder after division by g(x), and the cyclic structure lets one circuit handle every error position.
16 A CRC is a cyclic code spending all its redundancy on detection: every burst up to n-k caught, random patterns missed with probability 2^-(n-k).
Notes: What to say: Slow right down here. Read each takeaway aloud and then stop talking for a beat, because these are the sentences that should still be in their heads when they sit the SEE. Tell them explicitly that if they can reconstruct the reasoning behind any one of these lines they understand that unit, and if they can only recite it they do not. Pause cue: Pause for three seconds after each takeaway before moving to the next. Pointing cue: Point at each numbered takeaway in turn as you read it. Question to ask students: Ask: choose the takeaway you trust least and tell me what you would have to check to believe it. Animation instructions: Takeaway rows reveal one at a time from the top, each row highlighting briefly as it appears. Transition style: Fade [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 4: Error Control Coding: Linear Block and Cyclic Codes, 10 hours, TB1 (Haykin 2014) Ch. 10.1-10.5 pp. 577-605. TB1: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014. Revision consolidates all 16 unit takeaways. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 56
How this module is assessed
Where the quiz and the assignment live, and what they test.
VTU BEC503 | Module 4
Assessment
56
MODULE 4 QUIZ
quizzes/Module_4_Quiz.pdf
quizzes/Module_4_Quiz.gift
45 minutes | 50 marks | pass 20 | 1 attempt
Part A: 20 MCQs, 1 mark each.
Part B: 13 descriptive questions, 30 marks.
Bloom spread: L1-L2 21%, L3-L4 64%, L5-L6 15%
Every question carries a CO tag, a Bloom level and a chapter reference; distractor feedback names the misconception.
MODULE 4 ASSIGNMENT
assignments/Module_4_Assignment.pdf
Assignment 4 — Linear block and cyclic code construction
20 marks | 10% of CIE | 8 problems + 3 theory items
Submit as PDF, single file, named <USN>_BEC503_Assignment4.pdf, via LMS upload. 10% per day, nothing after 5 days.
Rubric: Correctness of matrix and polynomial construction (8); GF(2) arithmetic accuracy (5); Circuit design and traces (4); Reasoning about guarantees (3). Attainment: CO4 = 9, CO5 = 11.
Previous years' question papers for EC are indexed in pyq/PYQ_Index.pdf; the syllabus extract and the topic-to-slide mapping are in syllabus/Syllabus_Mapping.pdf.
Individual submission. Identical submissions score zero for both parties.
Notes: What to say: Close by telling them exactly where the assessment lives and what it tests. Name the two files, say the mark split out loud, and read the Bloom spread so they understand that roughly a quarter of the paper is not recall at all. Then read the integrity line word for word, because ambiguity there costs students more than any technical error in this module. Pause cue: Pause after the Bloom spread and before the integrity statement. Pointing cue: Point at the quiz panel, then the assignment panel, then the integrity line at the bottom. Question to ask students: Ask: which course outcome do you feel least ready on, and which unit would you reread tonight to fix it? Animation instructions: Quiz panel fades in from the left, then the assignment panel from the right, then the pointers strip appears, then the integrity line fades in last. Transition style: Fade [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 4: Error Control Coding: Linear Block and Cyclic Codes, 10 hours, TB1 (Haykin 2014) Ch. 10.1-10.5 pp. 577-605. TB1: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014. Assessment counts: 20 MCQs, 13 descriptive questions, 11 assignment items. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.