## Slide 1
Digital Communication
Module 5 asks: How do I code a continuous stream with no block boundaries, and how does the decoder find the best path wit…
VTU BEC503 | Module 5
Opening
01
MODULE 5
Convolutional Codes
10 contact hours | 16 teaching units | 56 slides
PRESCRIBED TEXTBOOK
Digital Communication Systems
Simon Haykin
John Wiley & Sons, 1st edition, 2014
TB1 (Haykin 2014) Ch. 10.6-10.8 pp. 605-623
Signal Space & AWGN • Digital Modulation • Information Theory • Block & Cyclic Codes • Convolutional Codes
Memory replaces block structure → Three pictures, one encoder → Free distance sets the gain → Trellis prunes the search → Viterbi decodes in linear time
EC · Semester 5 · BEC503 · generated for Phase 2 conversion
Notes: What to say: Open by putting the whole module on one page. Tell them this is 10 contact hours and 16 teaching units, and that all of it exists to answer one question: How do I code a continuous stream with no block boundaries, and how does the decoder find the best path without checking every one? Name the prescribed textbook out loud and say which chapters they will be living in, so nobody is reading the wrong book by week two. Pause cue: Pause after reading the driving question aloud, before naming the textbook. Pointing cue: Point at the module title block, then at the textbook panel, then run a finger along the five-beat arc. Question to ask students: Ask: before we start, what do you already expect the answer to "How do I code a continuous stream with no block boundaries, and how does the decoder find…" to look like? Animation instructions: Module title block fades in first, then the textbook panel slides in from the right, then the five arc beats appear left to right one at a time. Transition style: Fade [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 5: Convolutional Codes, 10 hours, TB1 (Haykin 2014) Ch. 10.6-10.8 pp. 605-623. TB1: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 2
What this module is actually for
One question, five beats, and the scope it does not cover.
VTU BEC503 | Module 5
Overview
02
THE DRIVING QUESTION
How do I code a continuous stream with no block boundaries, and how does the decoder find the best path without checking every one?
1
Memory replaces block structure
2
Three pictures, one encoder
3
Free distance sets the gain
4
Trellis prunes the search
5
Viterbi decodes in linear time
SCOPE AND PROVENANCE
Built from TB1 Sections 10.6-10.8, which the syllabus names. The shift from Module 4 is from blocks to streams: a convolutional encoder has memory, so each output depends on several past inputs and there is no block boundary to align to. The same encoder admits three equivalent pictures — tree, trellis and state diagram — and the module spends time on why the trellis is the useful one: it is the only one that does not grow with sequence length, which is precisely what makes the Viterbi algorithm linear rather than exponential. Free distance replaces minimum distance as the figure of merit, and the module closes on hard versus soft decision decoding, where 2 dB is available for the cost of keeping more than one bit from the demodulator.
Course outcomes exercised: CO4, CO5
Assessment: 20 MCQs + 13 descriptive questions + 11 assignment items
Notes: What to say: Give them the map before the territory. Read the driving question once more, then walk the five beats across the slide and say in one sentence what changes between each beat and the next. Finish on the scope paragraph, because knowing what a module does not cover saves more marks than anything else on this slide. Pause cue: Pause for four or five seconds after the five beats appear, before moving to scope. Pointing cue: Point at the driving question panel, then at each numbered beat in turn, then at the scope paragraph. Question to ask students: Ask: which of these five beats do you expect to find hardest, and why that one? Animation instructions: The driving question panel fades in, then the five numbered beats appear left to right one at a time, then the scope paragraph fades in beneath them. Transition style: Fade [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 5: Convolutional Codes, 10 hours, TB1 (Haykin 2014) Ch. 10.6-10.8 pp. 605-623. TB1: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 3
Every unit against its chapter and pages
Units 1-9 of 16, with the deck slides that teach each one.
VTU BEC503 | Module 5
Syllabus mapping
03
# — Teaching unit — Book chapter and pages — Deck slides — CO / Bloom
01 The convolutional encoder: memory instead of blocks — Ch. 10, pp. 605-608 — slides 5, 6, 7 — CO4 / L2
02 Constraint length, rate and generator sequences — Ch. 10, pp. 605-608 — slides 8, 9, 10 — CO4 / L3
03 Impulse response and generator polynomials — Ch. 10, pp. 605-608 — slides 11, 12, 13 — CO5 / L4
04 Time-domain encoding: convolution by hand — Ch. 10, pp. 605-608 — slides 14, 15, 16 — CO5 / L4
05 The code tree and why it does not scale — Ch. 10, pp. 608-613 — slides 17, 18, 19 — CO4 / L3
06 The trellis diagram — Ch. 10, pp. 608-613 — slides 20, 21, 22 — CO5 / L4
07 The state diagram and the transfer function — Ch. 10, pp. 608-613 — slides 23, 24, 25 — CO5 / L5
08 Recursive systematic convolutional codes — Ch. 10, pp. 610-613 — slides 26, 27, 28 — CO4 / L5
09 Free distance and coding gain — Ch. 10, pp. 610-613 — slides 29, 30, 31 — CO4 / L5
Notes: What to say: Tell them this is the slide to photograph. Every unit in the module is listed against a real chapter and a real page range, so there is no ambiguity about what to read. Point out the slide-number column and say plainly that if they miss a lecture, those are the slides covering that unit. Say that the page ranges come from the book's own table of contents rather than a guess. Pause cue: Pause for ten seconds and let them photograph the table before saying anything else. Pointing cue: Run a finger down the chapter-and-pages column, then across one complete row. Question to ask students: Ask: pick any row - which chapter would you open first, and what would you expect in the first paragraph? Animation instructions: Header row appears first, then the unit rows fade in one at a time from the top, then the chapter-and-pages column highlights. Transition style: Cut [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 5: Convolutional Codes, 10 hours, TB1 (Haykin 2014) Ch. 10.6-10.8 pp. 605-623. TB1: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014. Mapping covers all 16 teaching units. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 4
Syllabus mapping, continued
Units 10-16 of 16, with the deck slides that teach each one.
VTU BEC503 | Module 5
Syllabus mapping
04
# — Teaching unit — Book chapter and pages — Deck slides — CO / Bloom
10 Optimum decoding: what the decoder is actually trying to do — Ch. 10, pp. 613-614 — slides 32, 33, 34 — CO4 / L4
11 The Viterbi algorithm: add, compare, select — Ch. 10, pp. 614-618 — slides 35, 36, 37 — CO5 / L4
12 A full Viterbi decoding example — Ch. 10, pp. 618-623 — slides 38, 39, 40 — CO5 / L5
13 Traceback, truncation depth and decoding delay — Ch. 10, pp. 618-623 — slides 41, 42, 43 — CO5 / L5
14 Hard versus soft decision decoding — Ch. 10, pp. 618-623 — slides 44, 45, 46 — CO5 / L5
15 Choosing and deploying a convolutional code — Ch. 10, pp. 618-623 — slides 47, 48, 49 — CO5 / L5
16 Block codes and convolutional codes compared — Ch. 10, pp. 605-623 — slides 50, 51, 52 — CO4 / L5
Notes: What to say: Tell them this is the slide to photograph. Every unit in the module is listed against a real chapter and a real page range, so there is no ambiguity about what to read. Point out the slide-number column and say plainly that if they miss a lecture, those are the slides covering that unit. Say that the page ranges come from the book's own table of contents rather than a guess. Pause cue: Pause for ten seconds and let them photograph the table before saying anything else. Pointing cue: Run a finger down the chapter-and-pages column, then across one complete row. Question to ask students: Ask: pick any row - which chapter would you open first, and what would you expect in the first paragraph? Animation instructions: Header row appears first, then the unit rows fade in one at a time from the top, then the chapter-and-pages column highlights. Transition style: Cut [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 5: Convolutional Codes, 10 hours, TB1 (Haykin 2014) Ch. 10.6-10.8 pp. 605-623. TB1: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014. Mapping covers all 16 teaching units. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 5
The convolutional encoder: memory instead of blocks
What it is, why it works, and what it costs.
VTU BEC503 | Module 5
The convolutional encoder: memory ins…
05
THE MECHANISM
A convolutional encoder is a shift register with modulo-2 adders tapped off its stages: input bits enter one at a time and each produces n output bits that depend on the current input and the M bits already in the register. Unlike a block code, there is no block boundary and no fixed codeword length — the encoder maps a stream to a stream, and its output at any instant depends on recent history. That memory is the source of its strength: an error affecting one output bit is constrained by the encoder structure across several time steps, giving the decoder multiple independent looks at the same information bit.
KEY TERMS
• convolutional encoder
• shift register
• memory
• continuous stream
• modulo-2 adders
TAKEAWAY
A convolutional encoder is a finite state machine on a bit stream; memory, not block length, is what carries the protection.
DIAGRAM FOR PHASE 2
A horizontal shift register of two stages drawn as boxes, with the input arrow entering the first stage from the left. Two modulo-2 adder circles sit above and below the register, each fed by tap lines from th…
Source: Digital Communication Systems, 1st ed., Ch. 10, pp. 605-608
CO4 | Bloom L2 | visual id: convolutional-encoder-structure
Notes: What to say: Give them the idea before the formalism. Say it plainly first: A convolutional encoder is a shift register with modulo-2 adders tapped off its stages: input bits enter one at a time and each produces n output bits tha… Then add the part they are examined on - A convolutional encoder is a finite state machine on a bit stream; memory, not block length, is what carries the protection. Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "convolutional encoder" constrain here, and what would break if it did not hold? Animation instructions: the input arrow and two register boxes draw left to right, then the upper adder appears with its three tap lines drawing in sequence, then the lower adder with its two taps, then the two output lines extend into the commutator which rotates once, then the side card slides in. Transition style: Fade [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 5: Convolutional Codes. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 10, pp. 605-608. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 6
The convolutional encoder: memory instead of blocks - how it works
The procedure in order, and what each pass costs you.
VTU BEC503 | Module 5
The convolutional encoder: memory ins…
06
1. Choose the number of memory stages M and the number of output bits n per input bit
2. Define the tap connections for each of the n modulo-2 adders
3. Shift the input bit into the register
4. Compute each output bit as the XOR of the tapped stages
5. Interleave the n outputs and repeat for the next input bit
COST AND BEHAVIOUR
Best: M flip-flops and a few XOR gates
Typical: rate k/n with 2^M states
Worst: decoding complexity grows as 2^M, so memory is expensive at the receiver
WHAT THAT MEANS
The encoder is trivially cheap; the whole cost sits in the decoder.
Source: Digital Communication Systems, 1st ed., Ch. 10, pp. 605-608 | CO4 | Bloom L2
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Choose the number of memory stages M and the number of output bits n per input bit - and check everyone has written it before moving on. At the cost panel, translate it: The encoder is trivially cheap; the whole cost sits in the decoder. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 5: Convolutional Codes. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 10, pp. 605-608. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 7
The convolutional encoder: memory instead of blocks - worked example
One concrete case, carried all the way to a stated number.
VTU BEC503 | Module 5
The convolutional encoder: memory ins…
07
GIVEN
Rate 1/2, M = 2, generators g1 = 111 and g2 = 101. Input bit 1 into an all-zero register.
1. Register before: 00. Input: 1
2. Output 1 = input XOR s1 XOR s2 = 1 XOR 0 XOR 0 = 1
3. Output 2 = input XOR s2 = 1 XOR 0 = 1
4. Shift: register becomes 10
RESULT
One input bit produced the pair 11 and moved the encoder from state 00 to state 10. Every later output depends on this state.
Rate R = k/n, memory M, constraint length K = M + 1
Output j at time i:
v_j[i] = XOR over taps of u[i - t] for t in g_j
Example: M = 2, g1 = (1,1,1), g2 = (1,0,1)
v1[i] = u[i] + u[i-1] + u[i-2]
v2[i] = u[i] + u[i-2]
Number of states = 2^M
THE MISTAKE STUDENTS MAKE
Students treat the encoder as memoryless and compute each output from the current input alone. The register contents are part of the computation; ignoring them gives a repetition code rather than a convolutional one.
Source: Digital Communication Systems, 1st ed., Ch. 10, pp. 605-608 | CO4 | Bloom L2
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is Rate 1/2, M = 2, generators g1 = 111 and g2 = 101. Input bit 1 into an all-zero register. Work at the pace of the slowest note-taker and land hard on the result: One input bit produced the pair 11 and moved the encoder from state 00 to state 10. Every later output depends on this state. Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 5: Convolutional Codes. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 10, pp. 605-608. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 8
Constraint length, rate and generator sequences
What it is, why it works, and what it costs.
VTU BEC503 | Module 5
Constraint length, rate and generator…
08
THE MECHANISM
The constraint length K = M + 1 is the number of input bits that influence any single output bit, and it is the parameter that governs both the strength of the code and the cost of decoding. The rate R = k/n gives the number of information bits per transmitted bit, most commonly 1/2 or 1/3. The generator sequences specify which register stages feed each adder, usually written in octal: the pair (7,5) octal means 111 and 101 binary, the standard K = 3 rate 1/2 code. Doubling the constraint length roughly doubles the coding gain available while squaring the number of decoder states.
KEY TERMS
• constraint length
• code rate
• generator sequence
• octal notation
• memory order
TAKEAWAY
K sets the strength, and decoder cost is 2^(K-1) — which is why practical constraint lengths stop around 7 to 9.
DIAGRAM FOR PHASE 2
A dual-axis plot with constraint length K from 3 to 10 on the horizontal axis. A left axis carries coding gain in dB with a curve rising and gradually flattening, and a right axis carries the number of decoder…
Source: Digital Communication Systems, 1st ed., Ch. 10, pp. 605-608
CO4 | Bloom L3 | visual id: constraint-length-cost-curve
Notes: What to say: Give them the idea before the formalism. Say it plainly first: The constraint length K = M + 1 is the number of input bits that influence any single output bit, and it is the parameter that governs both the strength o… Then add the part they are examined on - K sets the strength, and decoder cost is 2^(K-1) — which is why practical constraint lengths stop around 7 to 9. Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "constraint length" constrain here, and what would break if it did not hold? Animation instructions: the axes draw with both scales labelled, then the coding-gain curve sweeps up and flattens, then the state-count line climbs steeply, then the practical-range band shades between the two, then the table fills row by row with the (7,5) row highlighting last. Transition style: Fade [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 5: Convolutional Codes. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 10, pp. 605-608. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 9
Constraint length, rate and generator sequences - how it works
The procedure in order, and what each pass costs you.
VTU BEC503 | Module 5
Constraint length, rate and generator…
09
1. Choose the rate k/n from the bandwidth available
2. Choose the constraint length K from the coding gain needed and the decoder budget
3. Look up or search for the generator polynomials maximising free distance for that K and rate
4. Convert the generators to octal for compact specification
5. Confirm the decoder state count 2^(K-1) is affordable
COST AND BEHAVIOUR
Best: K = 3 gives 4 states and about 3.5 dB of gain
Typical: K = 7 gives 64 states and about 5.5 dB
Worst: each increment of K doubles the decoder state count
WHAT THAT MEANS
The K = 7, rate 1/2, (171,133) octal code is the de facto standard in satellite and deep-space links.
Source: Digital Communication Systems, 1st ed., Ch. 10, pp. 605-608 | CO4 | Bloom L3
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Choose the rate k/n from the bandwidth available - and check everyone has written it before moving on. At the cost panel, translate it: The K = 7, rate 1/2, (171,133) octal code is the de facto standard in satellite and deep-space links. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 5: Convolutional Codes. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 10, pp. 605-608. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 10
Constraint length, rate and generator sequences - worked example
One concrete case, carried all the way to a stated number.
VTU BEC503 | Module 5
Constraint length, rate and generator…
10
GIVEN
Generators (7,5) in octal for a rate 1/2 code.
1. 7 octal = 111 binary, so adder 1 taps the input and both register stages
2. 5 octal = 101 binary, so adder 2 taps the input and the second stage only
3. Three taps implies three influencing bits, so K = 3 and M = 2
4. States = 2^(K-1) = 4
RESULT
The (7,5) code has constraint length 3, four states and free distance 5 — the standard textbook example and the one used throughout this module.
Constraint length: K = M + 1
States: 2^(K-1) = 2^M
Rate: R = k/n
Octal generators: (7, 5) -> 111, 101
(171, 133) -> K = 7 standard
Decoder complexity grows as 2^(K-1) per time step.
THE MISTAKE STUDENTS MAKE
Students conflate constraint length with memory order, writing K where M belongs. K = M + 1; using the wrong one gives a state count that is out by a factor of two and a decoder that does not work.
Source: Digital Communication Systems, 1st ed., Ch. 10, pp. 605-608 | CO4 | Bloom L3
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is Generators (7,5) in octal for a rate 1/2 code. Work at the pace of the slowest note-taker and land hard on the result: The (7,5) code has constraint length 3, four states and free distance 5 — the standard textbook example and the one used througho… Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 5: Convolutional Codes. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 10, pp. 605-608. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 11
Impulse response and generator polynomials
What it is, why it works, and what it costs.
VTU BEC503 | Module 5
Impulse response and generator polyno…
11
THE MECHANISM
Feeding a single 1 followed by zeros into the encoder produces each output branch impulse response, and those responses are exactly the generator sequences — which is why the code is called convolutional: the output is the convolution of the input sequence with the generator sequences. Writing the sequences as polynomials in a delay operator D turns that convolution into polynomial multiplication, so the encoder becomes V(D) = U(D) G(D) with all arithmetic over GF(2). This transform-domain view makes the algebra of concatenation and puncturing straightforward and connects convolutional codes to the polynomial machinery already built for cyclic codes.
KEY TERMS
• impulse response
• generator polynomial
• transform domain
• D-transform
• convolution
TAKEAWAY
The generators are the impulse responses, so encoding is convolution — and in the D domain it is just polynomial multiplication.
DIAGRAM FOR PHASE 2
Left: an input strip showing 1 0 0 0 0 entering the encoder, with two output strips beneath showing 1 1 1 0 0 and 1 0 1 0 0, each labelled "impulse response of branch 1" and "branch 2". Centre: an arrow labell…
Source: Digital Communication Systems, 1st ed., Ch. 10, pp. 605-608
CO5 | Bloom L4 | visual id: impulse-response-to-polynomial
Notes: What to say: Give them the idea before the formalism. Say it plainly first: Feeding a single 1 followed by zeros into the encoder produces each output branch impulse response, and those responses are exactly the generator sequence… Then add the part they are examined on - The generators are the impulse responses, so encoding is convolution — and in the D domain it is just polynomial multiplicat… Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "impulse response" constrain here, and what would break if it did not hold? Animation instructions: the impulse input strip appears, then the two output strips fill cell by cell left to right in step, then the read-as-polynomial arrow sweeps right and the two polynomial expressions write themselves, then the matrix equation assembles on the right with the multiplication symbol landing last. Transition style: Fade [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 5: Convolutional Codes. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 10, pp. 605-608. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 12
Impulse response and generator polynomials - how it works
The procedure in order, and what each pass costs you.
VTU BEC503 | Module 5
Impulse response and generator polyno…
12
1. Apply a single 1 followed by zeros to the encoder input
2. Record each output branch sequence: these are the impulse responses
3. Write each as a polynomial in the delay operator D
4. Assemble the generator matrix G(D) with one column per output branch
5. Encode any input as V(D) = U(D) G(D) over GF(2)
COST AND BEHAVIOUR
Best: polynomials have degree at most M
Typical: multiplication of two short polynomials per branch
Worst: the transform view hides the state, so it is less useful for decoding
WHAT THAT MEANS
Encoding is clearer in the D domain; decoding is clearer in the trellis.
Source: Digital Communication Systems, 1st ed., Ch. 10, pp. 605-608 | CO5 | Bloom L4
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Apply a single 1 followed by zeros to the encoder input - and check everyone has written it before moving on. At the cost panel, translate it: Encoding is clearer in the D domain; decoding is clearer in the trellis. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 5: Convolutional Codes. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 10, pp. 605-608. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 13
Impulse response and generator polynomials - worked example
One concrete case, carried all the way to a stated number.
VTU BEC503 | Module 5
Impulse response and generator polyno…
13
GIVEN
Input sequence 1 0 1 with g1(D) = 1 + D + D^2 and g2(D) = 1 + D^2.
1. U(D) = 1 + D^2
2. V1(D) = (1 + D^2)(1 + D + D^2) = 1 + D + D^2 + D^2 + D^3 + D^4 = 1 + D + D^3 + D^4
3. V2(D) = (1 + D^2)(1 + D^2) = 1 + D^2 + D^2 + D^4 = 1 + D^4
4. Interleave: branch 1 gives 11011, branch 2 gives 10001
RESULT
Output pairs 11, 10, 01, 10, 11 over five time steps — note the D^2 terms cancelling in V1, which is modulo-2 arithmetic doing its work.
g1(D) = 1 + D + D^2 (octal 7)
g2(D) = 1 + D^2 (octal 5)
G(D) = [ g1(D) g2(D) ]
V(D) = U(D) * G(D) all arithmetic mod 2
Impulse response of branch j = coefficients of g_j(D)
THE MISTAKE STUDENTS MAKE
Students carry ordinary integer arithmetic into the polynomial multiplication, so D^2 + D^2 becomes 2D^2 rather than 0. Over GF(2) equal terms cancel, and missing that produces outputs the encoder would never emit.
Source: Digital Communication Systems, 1st ed., Ch. 10, pp. 605-608 | CO5 | Bloom L4
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is Input sequence 1 0 1 with g1(D) = 1 + D + D^2 and g2(D) = 1 + D^2. Work at the pace of the slowest note-taker and land hard on the result: Output pairs 11, 10, 01, 10, 11 over five time steps — note the D^2 terms cancelling in V1, which is modulo-2 arithmetic doing it… Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 5: Convolutional Codes. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 10, pp. 605-608. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 14
Time-domain encoding: convolution by hand
What it is, why it works, and what it costs.
VTU BEC503 | Module 5
Time-domain encoding: convolution by…
14
THE MECHANISM
Encoding in the time domain means tracking the register contents step by step: for each input bit, compute the outputs from the current input and state, then shift. Because the encoder has memory, the final M input bits leave the register in a non-zero state unless M zero bits — the tail or flush bits — are appended, which returns the encoder to the all-zero state and lets the decoder finish at a known point. Those tail bits cost rate: an L-bit message with M tail bits at rate 1/n transmits n(L+M) bits, so the effective rate is L/(n(L+M)) rather than 1/n.
KEY TERMS
• time domain
• state sequence
• tail bits
• zero termination
• output interleaving
TAKEAWAY
Track state, compute, shift — and remember the tail bits, which cost real rate on short messages.
DIAGRAM FOR PHASE 2
A table with columns: time step, input bit, state before, output pair, state after. Seven rows are filled for a four-bit message plus two tail bits, the two tail rows tinted amber and labelled "flush to zero s…
Source: Digital Communication Systems, 1st ed., Ch. 10, pp. 605-608
CO5 | Bloom L4 | visual id: time-domain-encoding-table
Notes: What to say: Give them the idea before the formalism. Say it plainly first: Encoding in the time domain means tracking the register contents step by step: for each input bit, compute the outputs from the current input and state, t… Then add the part they are examined on - Track state, compute, shift — and remember the tail bits, which cost real rate on short messages. Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "time domain" constrain here, and what would break if it did not hold? Animation instructions: the table header draws, then each row fills left to right in time order with the state-after cell lighting as it updates, then the two tail rows tint amber as they fill, then the final zero state gets its tick, then the rate strip appears with the effective-rate figure counting up last. Transition style: Fade [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 5: Convolutional Codes. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 10, pp. 605-608. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 15
Time-domain encoding: convolution by hand - how it works
The procedure in order, and what each pass costs you.
VTU BEC503 | Module 5
Time-domain encoding: convolution by…
15
1. Initialise the register to all zeros
2. For each message bit, compute the n outputs from the input and current state
3. Shift the input bit into the register
4. After the last message bit, feed M zeros to flush the register
5. Concatenate all output groups to form the transmitted sequence
COST AND BEHAVIOUR
Best: n XOR operations per input bit
Typical: L + M time steps for an L-bit message
Worst: tail overhead M/(L+M) is severe for short messages
WHAT THAT MEANS
Tail-biting termination avoids the overhead by starting and ending in the same non-zero state.
Source: Digital Communication Systems, 1st ed., Ch. 10, pp. 605-608 | CO5 | Bloom L4
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Initialise the register to all zeros - and check everyone has written it before moving on. At the cost panel, translate it: Tail-biting termination avoids the overhead by starting and ending in the same non-zero state. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 5: Convolutional Codes. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 10, pp. 605-608. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 16
Time-domain encoding: convolution by hand - worked example
One concrete case, carried all the way to a stated number.
VTU BEC503 | Module 5
Time-domain encoding: convolution by…
16
GIVEN
Message 1011, generators (7,5), M = 2, with two tail zeros.
1. Input 1, state 00: outputs 11, state becomes 10
2. Input 0, state 10: outputs 10, state becomes 01
3. Input 1, state 01: outputs 00, state becomes 10
4. Input 1, state 10: outputs 01, state becomes 11; then tails 0, 0 give 01 and 11
RESULT
Transmitted sequence 11 10 00 01 01 11 — twelve bits for four information bits, an effective rate of 1/3 because of the tail.
state = 00
for each input bit u:
v1 = u XOR s1 XOR s2
v2 = u XOR s2
emit (v1, v2)
s2 = s1; s1 = u
After the message, feed M zeros to flush.
Effective rate = L / ( n * (L + M) )
THE MISTAKE STUDENTS MAKE
Students omit the tail bits and leave the encoder in an unknown final state. The decoder then has no fixed endpoint for the trellis, and the final few information bits are decoded with much less protection than the rest.
Source: Digital Communication Systems, 1st ed., Ch. 10, pp. 605-608 | CO5 | Bloom L4
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is Message 1011, generators (7,5), M = 2, with two tail zeros. Work at the pace of the slowest note-taker and land hard on the result: Transmitted sequence 11 10 00 01 01 11 — twelve bits for four information bits, an effective rate of 1/3 because of the tail. Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 5: Convolutional Codes. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 10, pp. 605-608. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 17
The code tree and why it does not scale
What it is, why it works, and what it costs.
VTU BEC503 | Module 5
The code tree and why it does not sca…
17
THE MECHANISM
The code tree draws every possible encoder path as a branching diagram: from each node, the upper branch corresponds to an input 0 and the lower to an input 1, with the output bits labelled on each branch. It is the most literal picture of the encoder and the easiest to read for the first few steps, but it doubles in width at every time step, so after L steps it has 2^L leaves. This makes it useless for anything but illustration. Crucially, the tree becomes repetitive after M steps: nodes at the same depth with the same register contents have identical subtrees, and merging them is exactly what produces the trellis.
KEY TERMS
• code tree
• branch
• path
• exponential growth
• repetition of structure
TAKEAWAY
The tree doubles every step and then starts repeating itself after M steps — merging the repeats is the whole idea of the trellis.
DIAGRAM FOR PHASE 2
A binary tree drawn left to right over four time steps, each branch labelled with its two output bits and marked 0 for upper and 1 for lower. At depth 3, two pairs of nodes are circled and connected by dashed…
Source: Digital Communication Systems, 1st ed., Ch. 10, pp. 608-613
CO4 | Bloom L3 | visual id: code-tree-repetition
Notes: What to say: Give them the idea before the formalism. Say it plainly first: The code tree draws every possible encoder path as a branching diagram: from each node, the upper branch corresponds to an input 0 and the lower to an inp… Then add the part they are examined on - The tree doubles every step and then starts repeating itself after M steps — merging the repeats is the whole idea of the tr… Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "code tree" constrain here, and what would break if it did not hold? Animation instructions: the tree grows depth by depth, each level of branches drawing with its output labels, then the counter increments at each level, then at depth 3 the matching subtrees tint in pairs, then the circles and dashed connectors appear, then the "unusable" annotation lands. Transition style: Fade [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 5: Convolutional Codes. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 10, pp. 608-613. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 18
The code tree and why it does not scale - how it works
The procedure in order, and what each pass costs you.
VTU BEC503 | Module 5
The code tree and why it does not sca…
18
1. Start at the root with the encoder in the all-zero state
2. From each node, draw an upper branch for input 0 and a lower branch for input 1
3. Label each branch with the n output bits it produces
4. Continue to the required depth
5. Observe that beyond depth M, nodes with the same state have identical subtrees
COST AND BEHAVIOUR
Best: clear and readable for the first three or four steps
Typical: 2^L paths after L steps
Worst: completely intractable beyond about ten steps
WHAT THAT MEANS
Its only real value is pedagogical: it makes the merging that produces the trellis obvious.
Source: Digital Communication Systems, 1st ed., Ch. 10, pp. 608-613 | CO4 | Bloom L3
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Start at the root with the encoder in the all-zero state - and check everyone has written it before moving on. At the cost panel, translate it: Its only real value is pedagogical: it makes the merging that produces the trellis obvious. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 5: Convolutional Codes. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 10, pp. 608-613. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 19
The code tree and why it does not scale - worked example
One concrete case, carried all the way to a stated number.
VTU BEC503 | Module 5
The code tree and why it does not sca…
19
GIVEN
The (7,5) code, tree depth 4.
1. Depth 1: 2 nodes
2. Depth 2: 4 nodes
3. Depth 3: 8 nodes, but only 4 distinct states
4. Depth 4: 16 nodes, still only 4 distinct states
RESULT
From depth 3 onward the node count doubles while the state count stays at 4. Every node beyond that is a duplicate of one of four situations, which is exactly the redundancy the trellis removes.
Tree nodes at depth L: 2^L
Distinct encoder states: 2^M
For L > M: 2^L >> 2^M
=> nodes at the same depth with the same state have
identical futures and can be merged.
Merging gives the trellis: width 2^M, constant in L.
THE MISTAKE STUDENTS MAKE
Students try to use the tree for actual decoding of a realistic sequence. With a hundred information bits the tree has 2^100 paths; the trellis has four states at every step and the same information.
Source: Digital Communication Systems, 1st ed., Ch. 10, pp. 608-613 | CO4 | Bloom L3
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is The (7,5) code, tree depth 4. Work at the pace of the slowest note-taker and land hard on the result: From depth 3 onward the node count doubles while the state count stays at 4. Every node beyond that is a duplicate of one of four… Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 5: Convolutional Codes. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 10, pp. 608-613. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 20
The trellis diagram
What it is, why it works, and what it costs.
VTU BEC503 | Module 5
The trellis diagram
20
THE MECHANISM
The trellis is the code tree with equal-state nodes merged, so it has exactly 2^M nodes at every time step regardless of sequence length. Each node has two outgoing branches, for input 0 and input 1, and after the first M steps each node also has two incoming branches. That constant width is the single structural fact that makes efficient decoding possible: the decoder need only keep one surviving path per state rather than one per possible input sequence, so the work per time step is fixed rather than doubling. Every valid encoder output sequence is a path through the trellis, and decoding means finding the path closest to what was received.
KEY TERMS
• trellis
• state node
• branch label
• constant width
• merging paths
TAKEAWAY
Constant width 2^M is everything: it turns an exponential search into a fixed amount of work per time step.
DIAGRAM FOR PHASE 2
A trellis for a four-state code drawn over six time steps: four horizontal rows of nodes labelled 00, 01, 10, 11, with solid branches for input 0 and dashed branches for input 1 connecting each column to the n…
Source: Digital Communication Systems, 1st ed., Ch. 10, pp. 608-613
CO5 | Bloom L4 | visual id: trellis-constant-width
Notes: What to say: Give them the idea before the formalism. Say it plainly first: The trellis is the code tree with equal-state nodes merged, so it has exactly 2^M nodes at every time step regardless of sequence length. Then add the part they are examined on - Constant width 2^M is everything: it turns an exponential search into a fixed amount of work per time step. Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "trellis" constrain here, and what would break if it did not hold? Animation instructions: the four node rows appear as columns of dots, then the branches draw column by column left to right with the first two columns showing the fan-out from the start node, then the output labels appear on the early branches, then the steady-state bracket sweeps across the remaining columns, then the side comparison bars grow, the tree one climbing off the top. Transition style: Fade [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 5: Convolutional Codes. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 10, pp. 608-613. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 21
The trellis diagram - how it works
The procedure in order, and what each pass costs you.
VTU BEC503 | Module 5
The trellis diagram
21
1. Draw 2^M state nodes in a column for each time step
2. From each state, draw a branch to the state reached on input 0 and another for input 1
3. Label each branch with the output bits the encoder emits on that transition
4. Start from the all-zero state and let the trellis fill over the first M steps
5. Terminate by forcing the path back to the all-zero state with tail bits
COST AND BEHAVIOUR
Best: width is fixed at 2^M for any sequence length
Typical: 2^M nodes and 2^(M+1) branches per time step
Worst: width doubles with each increment of constraint length
WHAT THAT MEANS
This is the data structure the Viterbi algorithm walks, and its size is why K stops around 7 to 9.
Source: Digital Communication Systems, 1st ed., Ch. 10, pp. 608-613 | CO5 | Bloom L4
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Draw 2^M state nodes in a column for each time step - and check everyone has written it before moving on. At the cost panel, translate it: This is the data structure the Viterbi algorithm walks, and its size is why K stops around 7 to 9. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 5: Convolutional Codes. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 10, pp. 608-613. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 22
The trellis diagram - worked example
One concrete case, carried all the way to a stated number.
VTU BEC503 | Module 5
The trellis diagram
22
GIVEN
The (7,5) code, states 00, 01, 10, 11.
1. From 00: input 0 gives output 00 to state 00; input 1 gives output 11 to state 10
2. From 10: input 0 gives output 10 to state 01; input 1 gives output 01 to state 11
3. From 01: input 0 gives output 11 to state 00; input 1 gives output 00 to state 10
4. From 11: input 0 gives output 01 to state 01; input 1 gives output 10 to state 11
RESULT
Eight branches, four states, and the pattern repeats identically at every time step — the whole code is described by this one column of transitions.
States: 2^M
Branches per state: 2^k (2 for rate 1/n)
Transition: (state, input) -> (next state, output)
Width is constant in sequence length L.
Work per time step: O(2^M), total O(L * 2^M).
Compare tree: O(2^L).
THE MISTAKE STUDENTS MAKE
Students draw a trellis that widens over time, effectively redrawing the tree. The defining feature is that nodes with the same state at the same time are one node; failing to merge them loses the entire computational benefit.
Source: Digital Communication Systems, 1st ed., Ch. 10, pp. 608-613 | CO5 | Bloom L4
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is The (7,5) code, states 00, 01, 10, 11. Work at the pace of the slowest note-taker and land hard on the result: Eight branches, four states, and the pattern repeats identically at every time step — the whole code is described by this one col… Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 5: Convolutional Codes. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 10, pp. 608-613. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 23
The state diagram and the transfer function
What it is, why it works, and what it costs.
VTU BEC503 | Module 5
The state diagram and the transfer fu…
23
THE MECHANISM
The state diagram collapses the trellis further by removing time altogether: it shows the 2^M states as nodes with labelled transitions between them, so the whole encoder fits in one small graph. Because time is gone, a code sequence becomes a walk through the graph, and the set of all sequences diverging from and returning to the zero state can be enumerated algebraically by a transfer function T(D). Expanding T(D) as a power series gives the number of paths of each Hamming weight, and the exponent of its lowest-order term is the free distance. This is the standard route to computing free distance without searching paths by hand.
KEY TERMS
• state diagram
• transfer function
• path enumeration
• weight enumerator
• self-loop
TAKEAWAY
Drop time and the encoder is one small graph; its transfer function enumerates path weights and hands you the free distance.
DIAGRAM FOR PHASE 2
A four-node state diagram with nodes 00, 01, 10, 11 arranged in a diamond, directed edges labelled with the output weight as a power of D, and a self-loop on the 00 node drawn dashed and greyed with the note "…
Source: Digital Communication Systems, 1st ed., Ch. 10, pp. 608-613
CO5 | Bloom L5 | visual id: state-diagram-transfer-function
Notes: What to say: Give them the idea before the formalism. Say it plainly first: The state diagram collapses the trellis further by removing time altogether: it shows the 2^M states as nodes with labelled transitions between them, so t… Then add the part they are examined on - Drop time and the encoder is one small graph; its transfer function enumerates path weights and hands you the free distance. Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "state diagram" constrain here, and what would break if it did not hold? Animation instructions: the four nodes appear in the diamond, then the directed edges draw one at a time with their D-power labels, then the self-loop dashes in and greys out, then the zero node splits into source and sink sliding apart, then the transfer function writes itself, then the series expansion appears term by term with the first term boxing last. Transition style: Fade [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 5: Convolutional Codes. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 10, pp. 608-613. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 24
The state diagram and the transfer function - how it works
The procedure in order, and what each pass costs you.
VTU BEC503 | Module 5
The state diagram and the transfer fu…
24
1. Draw one node per state with directed edges for each input
2. Label each edge with D raised to the Hamming weight of its output
3. Split the all-zero state into a source and a sink, removing the self-loop
4. Solve the resulting flow-graph equations for the transfer function T(D)
5. Expand T(D) as a power series; the lowest exponent is the free distance
COST AND BEHAVIOUR
Best: four states give a small linear system solvable by hand
Typical: solving 2^M simultaneous equations
Worst: intractable by hand beyond about eight states
WHAT THAT MEANS
Additional variables for input weight and path length give the full augmented transfer function used for bit error bounds.
Source: Digital Communication Systems, 1st ed., Ch. 10, pp. 608-613 | CO5 | Bloom L5
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Draw one node per state with directed edges for each input - and check everyone has written it before moving on. At the cost panel, translate it: Additional variables for input weight and path length give the full augmented transfer function used for bit error bounds. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 5: Convolutional Codes. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 10, pp. 608-613. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 25
The state diagram and the transfer function - worked example
One concrete case, carried all the way to a stated number.
VTU BEC503 | Module 5
The state diagram and the transfer fu…
25
GIVEN
The (7,5) code state diagram.
1. Edges from 00 to 10 carry output 11, weight 2, so label D^2
2. Edges from 10 to 01 carry output 10, weight 1, so label D
3. Edges from 01 to 00 carry output 11, weight 2, so label D^2
4. Solving the flow graph gives T(D) = D^5/(1 - 2D)
RESULT
Expanding: D^5 + 2D^6 + 4D^7 + ... — one path of weight 5, two of weight 6, four of weight 7. The free distance is 5.
Label each edge with D^(weight of its output)
Split the zero state into source and sink.
Solve the flow graph for T(D).
(7,5) code: T(D) = D^5 / (1 - 2D)
= D^5 + 2D^6 + 4D^7 + 8D^8 + ...
d_free = lowest exponent = 5
THE MISTAKE STUDENTS MAKE
Students keep the self-loop on the all-zero state when computing the transfer function. That loop represents staying in the zero state emitting nothing, and leaving it in makes the series diverge without telling you anything about error events.
Source: Digital Communication Systems, 1st ed., Ch. 10, pp. 608-613 | CO5 | Bloom L5
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is The (7,5) code state diagram. Work at the pace of the slowest note-taker and land hard on the result: Expanding: D^5 + 2D^6 + 4D^7 + ... — one path of weight 5, two of weight 6, four of weight 7. The free distance is 5. Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 5: Convolutional Codes. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 10, pp. 608-613. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 26
Recursive systematic convolutional codes
What it is, why it works, and what it costs.
VTU BEC503 | Module 5
Recursive systematic convolutional co…
26
THE MECHANISM
A recursive systematic convolutional encoder feeds one output back into the register input and passes the information bit through unchanged as one of its outputs, so the code is systematic and the encoder has an infinite impulse response. Any non-recursive code has an equivalent RSC form with identical free distance and identical sequence-level distance properties, so nothing is lost. What is gained matters only in context: because a single input 1 produces an output of infinite weight, a low-weight input cannot easily produce a low-weight codeword, which is exactly the property turbo codes exploit when two RSC encoders are combined through an interleaver.
KEY TERMS
• RSC
• feedback
• systematic output
• infinite impulse response
• turbo component
TAKEAWAY
RSC form has the same distance as its non-recursive twin, but a single 1 now rings forever — which is what makes turbo codes work.
DIAGRAM FOR PHASE 2
A shift register with two stages, an XOR at the input fed by a feedback line from the register stages, and two outputs: an upper line taken directly from the input labelled "systematic output, message unchange…
Source: Digital Communication Systems, 1st ed., Ch. 10, pp. 610-613
CO4 | Bloom L5 | visual id: rsc-feedback-encoder
Notes: What to say: Give them the idea before the formalism. Say it plainly first: A recursive systematic convolutional encoder feeds one output back into the register input and passes the information bit through unchanged as one of its… Then add the part they are examined on - RSC form has the same distance as its non-recursive twin, but a single 1 now rings forever — which is what makes turbo codes… Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "RSC" constrain here, and what would break if it did not hold? Animation instructions: the register and its two outputs draw, then the feed-forward taps appear, then the feedback line draws in bold and loops back to the input XOR which flashes, then the two impulse strips fill cell by cell in step, the recursive one continuing past the panel edge with an ellipsis. Transition style: Fade [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 5: Convolutional Codes. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 10, pp. 610-613. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 27
Recursive systematic convolutional codes - how it works
The procedure in order, and what each pass costs you.
VTU BEC503 | Module 5
Recursive systematic convolutional co…
27
1. Take a non-recursive encoder with generators g1 and g2
2. Divide through by one generator to obtain the systematic recursive form
3. Route the information bit directly to one output
4. Feed the other generator output back into the register input through an XOR
5. Verify the free distance is unchanged from the original code
COST AND BEHAVIOUR
Best: same state count and same decoder as the non-recursive form
Typical: one extra XOR in the feedback path
Worst: termination is harder: the tail bits depend on the current state
WHAT THAT MEANS
Terminating an RSC encoder requires state-dependent tail bits rather than plain zeros.
Source: Digital Communication Systems, 1st ed., Ch. 10, pp. 610-613 | CO4 | Bloom L5
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Take a non-recursive encoder with generators g1 and g2 - and check everyone has written it before moving on. At the cost panel, translate it: Terminating an RSC encoder requires state-dependent tail bits rather than plain zeros. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 5: Convolutional Codes. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 10, pp. 610-613. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 28
Recursive systematic convolutional codes - worked example
One concrete case, carried all the way to a stated number.
VTU BEC503 | Module 5
Recursive systematic convolutional co…
28
GIVEN
Non-recursive (7,5) converted to RSC form with g2/g1 feedback.
1. Systematic output: the input bit itself
2. Parity generator becomes g2(D)/g1(D) = (1 + D^2)/(1 + D + D^2)
3. Impulse response of the parity branch: 1, 1, 0, 1, 1, 0, 1, 1, 0, repeating
4. Free distance remains 5, unchanged from the non-recursive form
RESULT
Identical distance properties but an impulse response that never terminates — a weight-1 input now produces an infinite-weight codeword.
Non-recursive: G(D) = [ g1(D) g2(D) ]
Recursive systematic: G(D) = [ 1 g2(D)/g1(D) ]
Same free distance, same trellis, same decoder.
Impulse response is now infinite:
(1 + D^2)/(1 + D + D^2) = 1 + D + D^3 + D^4 + ...
This is why RSC is the building block of turbo codes.
THE MISTAKE STUDENTS MAKE
Students expect RSC codes to outperform their non-recursive equivalents as standalone codes. They do not — the free distance is identical. The advantage appears only in concatenated schemes where low-weight inputs must be prevented from producing low-weight outputs.
Source: Digital Communication Systems, 1st ed., Ch. 10, pp. 610-613 | CO4 | Bloom L5
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is Non-recursive (7,5) converted to RSC form with g2/g1 feedback. Work at the pace of the slowest note-taker and land hard on the result: Identical distance properties but an impulse response that never terminates — a weight-1 input now produces an infinite-weight co… Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 5: Convolutional Codes. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 10, pp. 610-613. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 29
Free distance and coding gain
What it is, why it works, and what it costs.
VTU BEC503 | Module 5
Free distance and coding gain
29
THE MECHANISM
The free distance d_free of a convolutional code is the minimum Hamming weight of any non-zero path that diverges from the all-zero path and later remerges with it. It replaces minimum distance as the figure of merit because there are no blocks, and it governs performance the same way: the asymptotic coding gain in decibels is 10 log10(R d_free) for hard decisions, with an extra 3 dB available for soft decisions. An error event is one such diverge-and-remerge excursion, and at reasonable signal-to-noise ratios almost all errors are minimum-weight events, which is why d_free dominates.
KEY TERMS
• free distance
• error event
• asymptotic coding gain
• path weight
• diverge and remerge
TAKEAWAY
d_free is the weight of the cheapest wrong path that rejoins the right one; coding gain is 10 log10(R d_free).
DIAGRAM FOR PHASE 2
A trellis over eight time steps with the all-zero path drawn as a bold horizontal line along the top row. A second path diverges from it at step 2, wanders through the lower states for three steps, and remerge…
Source: Digital Communication Systems, 1st ed., Ch. 10, pp. 610-613
CO4 | Bloom L5 | visual id: free-distance-error-event
Notes: What to say: Give them the idea before the formalism. Say it plainly first: The free distance d_free of a convolutional code is the minimum Hamming weight of any non-zero path that diverges from the all-zero path and later remerge… Then add the part they are examined on - d_free is the weight of the cheapest wrong path that rejoins the right one; coding gain is 10 log10(R d_free). Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "free distance" constrain here, and what would break if it did not hold? Animation instructions: the trellis grid appears, then the all-zero path draws bold left to right, then the diverging path draws branch by branch with each branch weight label appearing as it is drawn, then the running sum counts up beside it, then the remerge point pulses and the total boxes, then the side card slides in with its two gain figures. Transition style: Fade [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 5: Convolutional Codes. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 10, pp. 610-613. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 30
Free distance and coding gain - how it works
The procedure in order, and what each pass costs you.
VTU BEC503 | Module 5
Free distance and coding gain
30
1. Identify all paths that leave the all-zero state and later return to it
2. Compute the total output weight of each such path
3. Take the minimum as d_free
4. Alternatively, read it off the lowest exponent of the transfer function
5. Compute the asymptotic coding gain as 10 log10(R d_free), adding 3 dB for soft decisions
COST AND BEHAVIOUR
Best: transfer function gives d_free directly for small codes
Typical: d_free grows roughly linearly with constraint length
Worst: exhaustive path search is exponential for large K
WHAT THAT MEANS
Tables of maximum free distance codes for each K and rate are standard and should be used rather than searched.
Source: Digital Communication Systems, 1st ed., Ch. 10, pp. 610-613 | CO4 | Bloom L5
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Identify all paths that leave the all-zero state and later return to it - and check everyone has written it before moving on. At the cost panel, translate it: Tables of maximum free distance codes for each K and rate are standard and should be used rather than searched. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 5: Convolutional Codes. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 10, pp. 610-613. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 31
Free distance and coding gain - worked example
One concrete case, carried all the way to a stated number.
VTU BEC503 | Module 5
Free distance and coding gain
31
GIVEN
Rate 1/2 code with d_free = 5, hard decision decoding.
1. Asymptotic coding gain = 10 log10(R x d_free)
2. = 10 log10(0.5 x 5) = 10 log10(2.5)
3. = 10 x 0.398 = 3.98 dB
4. With soft decision decoding, add approximately 3 dB: about 7 dB
RESULT
About 4 dB of gain hard, 7 dB soft, against uncoded transmission — at the cost of doubling the transmitted bit rate.
d_free = min weight of a path that diverges from and
remerges with the all-zero path
From the transfer function: lowest exponent of T(D)
Asymptotic coding gain (hard): G = 10*log10( R * d_free )
Soft decision adds approximately 3 dB.
(7,5): R = 1/2, d_free = 5 => 3.98 dB hard, ~7 dB soft
THE MISTAKE STUDENTS MAKE
Students compute free distance by comparing two arbitrary codewords. It is defined relative to the all-zero path specifically, and by linearity that loses no generality — but comparing two non-zero paths that never merge gives a meaningless infinite answer.
Source: Digital Communication Systems, 1st ed., Ch. 10, pp. 610-613 | CO4 | Bloom L5
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is Rate 1/2 code with d_free = 5, hard decision decoding. Work at the pace of the slowest note-taker and land hard on the result: About 4 dB of gain hard, 7 dB soft, against uncoded transmission — at the cost of doubling the transmitted bit rate. Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 5: Convolutional Codes. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 10, pp. 610-613. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 32
Optimum decoding: what the decoder is actually trying to do
What it is, why it works, and what it costs.
VTU BEC503 | Module 5
Optimum decoding: what the decoder is…
32
THE MECHANISM
Optimum decoding of a convolutional code means maximum likelihood sequence estimation: choosing the transmitted sequence, among all sequences the encoder could have produced, that maximises the likelihood of the received sequence. On a binary symmetric channel with crossover below one half, this reduces to choosing the trellis path at minimum Hamming distance from the received sequence; on a Gaussian channel with soft outputs, it becomes minimum Euclidean distance. Done naively this is a search over 2^L paths for an L-bit message, which is impossible for any useful L — and the whole content of the Viterbi algorithm is that the trellis structure makes the same answer reachable in linear time.
KEY TERMS
• maximum likelihood sequence estimation
• path metric
• exhaustive search
• decision rule
• optimality
TAKEAWAY
The goal is the closest path through the trellis; the only question is whether you find it in exponential or linear time.
DIAGRAM FOR PHASE 2
Left panel: a fan of many candidate paths drawn faintly over a trellis, with a counter reading "2^L candidates" and a crossed-out clock icon labelled "intractable". Right panel: the same trellis with only one…
Source: Digital Communication Systems, 1st ed., Ch. 10, pp. 613-614
CO4 | Bloom L4 | visual id: mlse-search-space
Notes: What to say: Give them the idea before the formalism. Say it plainly first: Optimum decoding of a convolutional code means maximum likelihood sequence estimation: choosing the transmitted sequence, among all sequences the encoder… Then add the part they are examined on - The goal is the closest path through the trellis; the only question is whether you find it in exponential or linear time. Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "maximum likelihood sequence estimation" constrain here, and what would break if it did not hold? Animation instructions: the left panel fills with dozens of faint paths accumulating rapidly and the counter spins upward, then the crossed-out clock stamps on, then the right panel draws its trellis and the four survivor paths thicken one at a time, then its counter settles and the green clock appears, then the "same answer" bracket draws between the two panels. Transition style: Fade [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 5: Convolutional Codes. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 10, pp. 613-614. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 33
Optimum decoding: what the decoder is actually trying t… - how it works
The procedure in order, and what each pass costs you.
VTU BEC503 | Module 5
Optimum decoding: what the decoder is…
33
1. Enumerate, conceptually, every path through the trellis
2. Compute the distance between each path output sequence and the received sequence
3. Choose the path at minimum distance
4. Map that path back to its input sequence
5. Recognise that steps 1 and 2 are infeasible directly, motivating the Viterbi algorithm
COST AND BEHAVIOUR
Best: optimal by definition — no decoder does better
Typical: naive search is O(2^L)
Worst: completely infeasible beyond about 30 information bits
WHAT THAT MEANS
The optimality is worth keeping in mind: Viterbi is not an approximation, it returns exactly this answer.
Source: Digital Communication Systems, 1st ed., Ch. 10, pp. 613-614 | CO4 | Bloom L4
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Enumerate, conceptually, every path through the trellis - and check everyone has written it before moving on. At the cost panel, translate it: The optimality is worth keeping in mind: Viterbi is not an approximation, it returns exactly this answer. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 5: Convolutional Codes. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 10, pp. 613-614. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 34
Optimum decoding: what the decoder is actually trying t… - worked example
One concrete case, carried all the way to a stated number.
VTU BEC503 | Module 5
Optimum decoding: what the decoder is…
34
GIVEN
A 100-bit message with a rate 1/2 code.
1. Number of candidate paths: 2^100
2. That is approximately 1.27 x 10^30
3. At one billion path evaluations per second, this takes about 4 x 10^13 years
4. The Viterbi algorithm needs 100 x 4 = 400 state updates
RESULT
Exhaustive search needs longer than the age of the universe; Viterbi needs 400 operations. Same answer, and that gap is the entire point of the next three units.
Choose sequence v maximising p(r | v) over all encoder outputs
BSC with p < 0.5: equivalent to minimising Hamming distance
AWGN soft: equivalent to minimising Euclidean distance
Naive: 2^L paths.
Viterbi: L * 2^M operations, same result.
THE MISTAKE STUDENTS MAKE
Students describe the Viterbi algorithm as a suboptimal shortcut. It is exactly maximum likelihood sequence estimation; the saving comes from discarding paths that provably cannot win, not from approximating.
Source: Digital Communication Systems, 1st ed., Ch. 10, pp. 613-614 | CO4 | Bloom L4
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is A 100-bit message with a rate 1/2 code. Work at the pace of the slowest note-taker and land hard on the result: Exhaustive search needs longer than the age of the universe; Viterbi needs 400 operations. Same answer, and that gap is the entir… Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 5: Convolutional Codes. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 10, pp. 613-614. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 35
The Viterbi algorithm: add, compare, select
What it is, why it works, and what it costs.
VTU BEC503 | Module 5
The Viterbi algorithm: add, compare,…
35
THE MECHANISM
The Viterbi algorithm walks the trellis one time step at a time, maintaining for each state the best path reaching it and that path accumulated metric. At each step and for each state it adds the branch metric to the metric of each incoming path, compares the two candidates, and selects the smaller, discarding the loser permanently. Discarding is justified because any path continuing from the loser can be improved by swapping in the winner, so the loser can never be part of the final best path. The work per time step is 2^M add-compare-select operations, independent of how long the sequence is.
KEY TERMS
• Viterbi algorithm
• branch metric
• path metric
• survivor path
• add-compare-select
TAKEAWAY
Add the branch metric, compare the two candidates, select the better, discard the other forever — 2^M times per step.
DIAGRAM FOR PHASE 2
A close-up of one trellis state at one time step. Two incoming branches arrive from the previous column, each labelled with its predecessor path metric and its branch metric, shown feeding two adder blocks. Bo…
Source: Digital Communication Systems, 1st ed., Ch. 10, pp. 614-618
CO5 | Bloom L4 | visual id: add-compare-select-unit
Notes: What to say: Give them the idea before the formalism. Say it plainly first: The Viterbi algorithm walks the trellis one time step at a time, maintaining for each state the best path reaching it and that path accumulated metric. Then add the part they are examined on - Add the branch metric, compare the two candidates, select the better, discard the other forever — 2^M times per step. Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "Viterbi algorithm" constrain here, and what would break if it did not hold? Animation instructions: the two incoming branches draw with their metric labels, then the two adders fill and output their sums, then the comparator fills and pulses, then the selector passes the smaller value forward, then the winning branch thickens while the losing branch greys and gets its strike-through, then the caption appears. Transition style: Fade [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 5: Convolutional Codes. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 10, pp. 614-618. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 36
The Viterbi algorithm: add, compare, select - how it works
The procedure in order, and what each pass costs you.
VTU BEC503 | Module 5
The Viterbi algorithm: add, compare,…
36
1. Initialise the metric of the all-zero state to 0 and all others to infinity
2. For each received group of n bits, compute the branch metric for every branch
3. For each state, add each incoming branch metric to its predecessor path metric
4. Compare the candidates and select the smallest as the new path metric
5. Record the surviving branch and repeat for the next time step
COST AND BEHAVIOUR
Best: 2^M add-compare-select operations per time step
Typical: total work O(L 2^M), linear in sequence length
Worst: memory for L survivor decisions unless truncation is used
WHAT THAT MEANS
The algorithm is inherently sequential across time but fully parallel across states.
Source: Digital Communication Systems, 1st ed., Ch. 10, pp. 614-618 | CO5 | Bloom L4
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Initialise the metric of the all-zero state to 0 and all others to infinity - and check everyone has written it before moving on. At the cost panel, translate it: The algorithm is inherently sequential across time but fully parallel across states. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 5: Convolutional Codes. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 10, pp. 614-618. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 37
The Viterbi algorithm: add, compare, select - worked example
One concrete case, carried all the way to a stated number.
VTU BEC503 | Module 5
The Viterbi algorithm: add, compare,…
37
GIVEN
State 00 at time 3, reached from state 00 with metric 2 and branch metric 1, or from state 01 with metric 1 and branch metric 2.
1. Candidate A: 2 + 1 = 3
2. Candidate B: 1 + 2 = 3
3. Tie — select either, conventionally the lower-numbered predecessor
4. New path metric for state 00 is 3
RESULT
A tie is resolved arbitrarily without loss of optimality, since both paths have identical metrics and either can extend to an optimal sequence.
metric[0][00] = 0, metric[0][other] = infinity
for t = 1..L+M:
for each state s:
for each predecessor p of s:
cand[p] = metric[t-1][p] + branch_metric(p -> s, r_t)
metric[t][s] = min over p of cand[p]
survivor[t][s] = argmin p
Branch metric (hard): Hamming distance between the branch
output and the received n bits.
THE MISTAKE STUDENTS MAKE
Students keep both candidates when the metrics tie, doubling the path count at each tie. One is chosen arbitrarily; since the metrics are equal, either extends to an equally optimal sequence and keeping both gains nothing.
Source: Digital Communication Systems, 1st ed., Ch. 10, pp. 614-618 | CO5 | Bloom L4
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is State 00 at time 3, reached from state 00 with metric 2 and branch metric 1, or from state 01 with metric 1 and branch metric 2. Work at the pace of the slowest note-taker and land hard on the result: A tie is resolved arbitrarily without loss of optimality, since both paths have identical metrics and either can extend to an opt… Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 5: Convolutional Codes. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 10, pp. 614-618. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 38
A full Viterbi decoding example
What it is, why it works, and what it costs.
VTU BEC503 | Module 5
A full Viterbi decoding example
38
THE MECHANISM
Working one complete decode end to end is the only way the algorithm becomes concrete. Taking the (7,5) code, a four-bit message with two tail bits, and a received sequence with one bit corrupted, the decoder computes four path metrics per time step across six steps, keeps four survivors, and traces back from the terminal all-zero state to recover the message. The corrupted bit shows up as a branch metric of one on the correct path, which the accumulated metrics absorb: the correct path finishes with metric 1 while every competitor finishes higher, so the error is corrected rather than merely detected.
KEY TERMS
• worked example
• branch metric
• accumulated metric
• survivor table
• error correction
TAKEAWAY
One corrupted bit leaves the correct path with metric 1 and every rival higher — that gap is what correction looks like numerically.
DIAGRAM FOR PHASE 2
A full four-state trellis over six time steps, every node annotated with its accumulated path metric, survivor branches drawn solid and discarded branches drawn faint grey. The received bit pairs are printed a…
Source: Digital Communication Systems, 1st ed., Ch. 10, pp. 618-623
CO5 | Bloom L5 | visual id: viterbi-worked-trellis
Notes: What to say: Give them the idea before the formalism. Say it plainly first: Working one complete decode end to end is the only way the algorithm becomes concrete. Then add the part they are examined on - One corrupted bit leaves the correct path with metric 1 and every rival higher — that gap is what correction looks like nume… Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "worked example" constrain here, and what would break if it did not hold? Animation instructions: the received sequence prints above with the corrupted pair reddening, then the trellis fills column by column with each node metric appearing and losing branches greying, then the table column fills in step with each trellis column, then at the final column the terminal state pulses, then the traceback path highlights green from right to left, then the decoded bits print beneath. Transition style: Fade [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 5: Convolutional Codes. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 10, pp. 618-623. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 39
A full Viterbi decoding example - how it works
The procedure in order, and what each pass costs you.
VTU BEC503 | Module 5
A full Viterbi decoding example
39
1. Write the received sequence in groups of n bits
2. Compute branch metrics as the Hamming distance to each branch label
3. Run add-compare-select across all states for each time step
4. At the end, select the state with the lowest metric, or the all-zero state if terminated
5. Trace the survivor pointers backwards and read off the input bits
COST AND BEHAVIOUR
Best: error-free reception gives a winning metric of 0
Typical: 24 add-compare-select operations for this example
Worst: metric ties in the final column need a tie-break rule
WHAT THAT MEANS
Terminating with tail bits removes the final ambiguity by forcing a known end state.
Source: Digital Communication Systems, 1st ed., Ch. 10, pp. 618-623 | CO5 | Bloom L5
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Write the received sequence in groups of n bits - and check everyone has written it before moving on. At the cost panel, translate it: Terminating with tail bits removes the final ambiguity by forcing a known end state. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 5: Convolutional Codes. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 10, pp. 618-623. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 40
A full Viterbi decoding example - worked example
One concrete case, carried all the way to a stated number.
VTU BEC503 | Module 5
A full Viterbi decoding example
40
GIVEN
Transmitted 11 10 00 01 01 11 for message 1011; received 11 10 01 01 01 11 with an error in the third pair.
1. Steps 1 and 2 match exactly, so the correct path accumulates metric 0
2. Step 3: received 01 against the correct branch label 00 gives branch metric 1
3. Competing paths at step 3 pick up metrics of 2 or more
4. Steps 4 to 6 match, so the correct path finishes at metric 1
RESULT
Traceback from the terminal 00 state recovers 1011, the original message. The single error is corrected because every alternative path finished with metric 3 or higher.
Received: 11 10 01 01 01 11
Correct: 11 10 00 01 01 11
^ one bit wrong
Correct path metric: 0 + 0 + 1 + 0 + 0 + 0 = 1
Best competitor: 3 or more
Traceback from state 00 at t = 6 -> message 1011
THE MISTAKE STUDENTS MAKE
Students trace back from whichever state has the lowest metric even when tail bits were used. With termination the path must end at the all-zero state; picking a different terminal state gives a sequence the encoder could not have produced.
Source: Digital Communication Systems, 1st ed., Ch. 10, pp. 618-623 | CO5 | Bloom L5
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is Transmitted 11 10 00 01 01 11 for message 1011; received 11 10 01 01 01 11 with an error in the third pair. Work at the pace of the slowest note-taker and land hard on the result: Traceback from the terminal 00 state recovers 1011, the original message. The single error is corrected because every alternative… Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 5: Convolutional Codes. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 10, pp. 618-623. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 41
Traceback, truncation depth and decoding delay
What it is, why it works, and what it costs.
VTU BEC503 | Module 5
Traceback, truncation depth and decod…
41
THE MECHANISM
Storing survivor decisions for an entire sequence before tracing back is impossible for a continuous stream, so practical decoders use a truncation depth: they trace back a fixed number of steps, output the oldest bit, and slide forward. This works because survivor paths almost always merge when traced back far enough, so the oldest bit is the same whichever survivor you start from. A truncation depth of about five times the constraint length makes the probability of a non-merged traceback negligible, and the cost is a fixed decoding delay of that many bit periods plus memory for that many survivor decisions per state.
KEY TERMS
• traceback
• truncation depth
• decoding delay
• survivor memory
• path merging
TAKEAWAY
Trace back about 5K steps, output the oldest bit, slide on — the paths have merged by then, so the answer is the same.
DIAGRAM FOR PHASE 2
A trellis over twelve time steps with four survivor paths drawn from the rightmost column, in four distinct colours, tracing leftward. The four paths are clearly distinct on the right and visibly converge as t…
Source: Digital Communication Systems, 1st ed., Ch. 10, pp. 618-623
CO5 | Bloom L5 | visual id: traceback-merging-depth
Notes: What to say: Give them the idea before the formalism. Say it plainly first: Storing survivor decisions for an entire sequence before tracing back is impossible for a continuous stream, so practical decoders use a truncation depth:… Then add the part they are examined on - Trace back about 5K steps, output the oldest bit, slide on — the paths have merged by then, so the answer is the same. Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "traceback" constrain here, and what would break if it did not hold? Animation instructions: the trellis grid draws, then the four coloured survivor paths trace from right to left simultaneously, converging visibly, then the dashed merge line drops where they become one, then the truncation bracket spans from the right edge to that line, then the output arrow appears at the left end with its label. Transition style: Fade [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 5: Convolutional Codes. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 10, pp. 618-623. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 42
Traceback, truncation depth and decoding delay - how it works
The procedure in order, and what each pass costs you.
VTU BEC503 | Module 5
Traceback, truncation depth and decod…
42
1. Maintain survivor decisions for the last T time steps, where T is the truncation depth
2. At each new time step, trace back T steps from any surviving state
3. Output the information bit at the oldest position reached
4. Discard the survivor decisions for that position and slide the window forward
5. Choose T of at least five times the constraint length
COST AND BEHAVIOUR
Best: memory is 2^M times T decisions, fixed regardless of sequence length
Typical: decoding delay of T bit periods
Worst: too small a T causes occasional non-merged tracebacks and extra errors
WHAT THAT MEANS
T = 5K is the standard rule of thumb and costs a negligible fraction of a decibel.
Source: Digital Communication Systems, 1st ed., Ch. 10, pp. 618-623 | CO5 | Bloom L5
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Maintain survivor decisions for the last T time steps, where T is the truncation depth - and check everyone has written it before moving on. At the cost panel, translate it: T = 5K is the standard rule of thumb and costs a negligible fraction of a decibel. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 5: Convolutional Codes. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 10, pp. 618-623. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 43
Traceback, truncation depth and decoding delay - worked example
One concrete case, carried all the way to a stated number.
VTU BEC503 | Module 5
Traceback, truncation depth and decod…
43
GIVEN
K = 7 code, so M = 6 and 64 states.
1. Truncation depth T = 5K = 35 time steps
2. Survivor memory: 64 states x 35 decisions = 2240 bits
3. Decoding delay: 35 bit periods
4. At 1 Mbit/s that is 35 microseconds
RESULT
2240 bits of survivor memory and 35 microseconds of delay for a K = 7 decoder — modest, and constant no matter how long the transmission runs.
Truncation depth: T ~ 5 * K
Survivor memory: 2^M * T bits
Decoding delay: T bit periods
At each step:
trace back T steps from any state
output the information bit at depth T
slide the window forward one step
Paths have merged by depth T with high probability.
THE MISTAKE STUDENTS MAKE
Students set the truncation depth equal to the constraint length. At that depth the survivor paths have often not merged, so the oldest bit differs between survivors and the decoder introduces errors it would otherwise have corrected.
Source: Digital Communication Systems, 1st ed., Ch. 10, pp. 618-623 | CO5 | Bloom L5
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is K = 7 code, so M = 6 and 64 states. Work at the pace of the slowest note-taker and land hard on the result: 2240 bits of survivor memory and 35 microseconds of delay for a K = 7 decoder — modest, and constant no matter how long the trans… Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 5: Convolutional Codes. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 10, pp. 618-623. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 44
Hard versus soft decision decoding
What it is, why it works, and what it costs.
VTU BEC503 | Module 5
Hard versus soft decision decoding
44
THE MECHANISM
Hard decision decoding takes the demodulator one-bit output and computes Hamming distances; soft decision decoding keeps the demodulator analogue or multi-bit output and computes Euclidean distances, so the decoder knows not only which bit was decided but how confident the decision was. That confidence information is worth about 2 dB of coding gain on an AWGN channel, because a marginal bit no longer carries the same weight as a confident one. Three bits of quantisation recovers nearly all of the available gain, so the practical cost is small: a wider bus from the demodulator and wider adders in the metric computation.
KEY TERMS
• hard decision
• soft decision
• quantisation
• Euclidean metric
• two dB
TAKEAWAY
Keeping three bits instead of one from the demodulator is worth about 2 dB — the cheapest gain in the whole chain.
DIAGRAM FOR PHASE 2
A received-sample axis with the decision threshold at the centre. Above it, hard decision is shown as two regions labelled 0 and 1 with a sample sitting just barely on one side, annotated "counted as certain".…
Source: Digital Communication Systems, 1st ed., Ch. 10, pp. 618-623
CO5 | Bloom L5 | visual id: hard-soft-quantisation
Notes: What to say: Give them the idea before the formalism. Say it plainly first: Hard decision decoding takes the demodulator one-bit output and computes Hamming distances; soft decision decoding keeps the demodulator analogue or multi… Then add the part they are examined on - Keeping three bits instead of one from the demodulator is worth about 2 dB — the cheapest gain in the whole chain. Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "hard decision" constrain here, and what would break if it did not hold? Animation instructions: the axis and threshold draw, then the two hard regions fill and the sample drops in with its label, then the eight soft bands appear beneath and the same sample lands in its band with the doubtful label, then the two BER curves draw right to left, then the 2 dB bracket snaps between them, then the cost strip slides up. Transition style: Fade [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 5: Convolutional Codes. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 10, pp. 618-623. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 45
Hard versus soft decision decoding - how it works
The procedure in order, and what each pass costs you.
VTU BEC503 | Module 5
Hard versus soft decision decoding
45
1. Keep the demodulator output as a multi-bit soft value rather than slicing to one bit
2. Quantise to three bits, which captures nearly all the available gain
3. Compute branch metrics as Euclidean distances or correlations rather than Hamming distances
4. Run the same add-compare-select recursion with these metrics
5. Verify the metric word width is wide enough to avoid overflow, or use modular normalisation
COST AND BEHAVIOUR
Best: about 2 dB of gain for three bits of quantisation
Typical: metric arithmetic widens from a few bits to eight or so
Worst: unquantised soft decisions give marginal extra gain for much more hardware
WHAT THAT MEANS
Going beyond three bits buys under 0.1 dB, which is why three is the industry default.
Source: Digital Communication Systems, 1st ed., Ch. 10, pp. 618-623 | CO5 | Bloom L5
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Keep the demodulator output as a multi-bit soft value rather than slicing to one bit - and check everyone has written it before moving on. At the cost panel, translate it: Going beyond three bits buys under 0.1 dB, which is why three is the industry default. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 5: Convolutional Codes. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 10, pp. 618-623. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 46
Hard versus soft decision decoding - worked example
One concrete case, carried all the way to a stated number.
VTU BEC503 | Module 5
Hard versus soft decision decoding
46
GIVEN
Rate 1/2, K = 7 code at a target bit error rate of 1e-5.
1. Uncoded BPSK requires about 9.6 dB
2. Hard decision Viterbi gives about 4 dB of gain, so 5.6 dB
3. Soft decision adds about 2 dB more, so about 3.6 dB
4. Total coding gain: about 6 dB
RESULT
Six decibels for a decoder of 64 states and a three-bit demodulator bus — which is why this exact configuration flew on Voyager and is still in use.
Hard: branch metric = Hamming distance( branch label, r )
Soft: branch metric = sum over bits of ( r_i - v_i )^2
or equivalently maximise the correlation sum r_i * v_i
Quantisation: 3 bits captures ~2 dB of the available gain
8 bits adds less than 0.1 dB more
Same add-compare-select recursion either way.
THE MISTAKE STUDENTS MAKE
Students expect soft decision decoding to need a different algorithm. The trellis, the survivors and the add-compare-select recursion are identical; only the branch metric computation changes, from Hamming distance to a squared difference or correlation.
Source: Digital Communication Systems, 1st ed., Ch. 10, pp. 618-623 | CO5 | Bloom L5
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is Rate 1/2, K = 7 code at a target bit error rate of 1e-5. Work at the pace of the slowest note-taker and land hard on the result: Six decibels for a decoder of 64 states and a three-bit demodulator bus — which is why this exact configuration flew on Voyager a… Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 5: Convolutional Codes. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 10, pp. 618-623. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 47
Choosing and deploying a convolutional code
What it is, why it works, and what it costs.
VTU BEC503 | Module 5
Choosing and deploying a convolutiona…
47
THE MECHANISM
Deploying a convolutional code means choosing the constraint length against the decoder budget, the rate against the bandwidth, and then adapting both to the channel. Puncturing deletes selected coded bits according to a fixed pattern to raise the rate from 1/2 to 2/3 or 3/4 without changing the encoder or decoder structure, the decoder simply inserting neutral metrics where bits were removed. Interleaving spreads burst errors across many trellis steps so they look like independent errors, which is what the code assumes. Concatenation with an outer Reed-Solomon code mops up the occasional long error event that the Viterbi decoder produces when it does fail.
KEY TERMS
• puncturing
• rate matching
• concatenation
• interleaving
• system design
TAKEAWAY
One encoder covers many rates through puncturing; interleaving makes bursts look random, and an outer code cleans up the rest.
DIAGRAM FOR PHASE 2
A left-to-right system chain: "data" into an "outer Reed-Solomon encoder" block, into an "interleaver" block, into a "convolutional encoder K=7 R=1/2" block, into a "puncturer to R=3/4" block, into "modulator"…
Source: Digital Communication Systems, 1st ed., Ch. 10, pp. 618-623
CO5 | Bloom L5 | visual id: coding-chain-deployment
Notes: What to say: Give them the idea before the formalism. Say it plainly first: Deploying a convolutional code means choosing the constraint length against the decoder budget, the rate against the bandwidth, and then adapting both to… Then add the part they are examined on - One encoder covers many rates through puncturing; interleaving makes bursts look random, and an outer code cleans up the res… Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "puncturing" constrain here, and what would break if it did not hold? Animation instructions: the transmit chain builds block by block left to right, then the channel cloud appears, then the receive chain mirrors back right to left, then the puncture pattern grid appears above with its cells crossing out one at a time, then the burst animation runs above the interleaver, the red errors scattering as they pass through. Transition style: Fade [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 5: Convolutional Codes. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 10, pp. 618-623. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 48
Choosing and deploying a convolutional code - how it works
The procedure in order, and what each pass costs you.
VTU BEC503 | Module 5
Choosing and deploying a convolutiona…
48
1. Choose the constraint length from the decoder budget, typically K = 7
2. Choose the base rate, typically 1/2, and puncture upward if bandwidth is tight
3. Add an interleaver sized to the expected burst length
4. Add an outer Reed-Solomon code if the residual error rate must be very low
5. Budget about 2 dB of the gain to soft decision decoding and verify the total against the link
COST AND BEHAVIOUR
Best: puncturing changes rate with no change to the encoder or decoder hardware
Typical: interleaver depth costs latency proportional to its size
Worst: concatenation adds a second decoder and more delay
WHAT THAT MEANS
The classic concatenated scheme, RS outer plus convolutional inner, was the standard for satellite links for thirty years.
Source: Digital Communication Systems, 1st ed., Ch. 10, pp. 618-623 | CO5 | Bloom L5
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Choose the constraint length from the decoder budget, typically K = 7 - and check everyone has written it before moving on. At the cost panel, translate it: The classic concatenated scheme, RS outer plus convolutional inner, was the standard for satellite links for thirty years. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 5: Convolutional Codes. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 10, pp. 618-623. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 49
Choosing and deploying a convolutional code - worked example
One concrete case, carried all the way to a stated number.
VTU BEC503 | Module 5
Choosing and deploying a convolutiona…
49
GIVEN
A link needing rate 3/4 with a K = 7 base rate 1/2 code.
1. Base code emits 2 coded bits per information bit
2. To reach 3/4, transmit 4 coded bits for every 3 information bits
3. Of the 6 coded bits the base encoder produces from 3 inputs, delete 2 by a fixed pattern
4. The decoder inserts a zero metric contribution at each deleted position
RESULT
Rate 3/4 from the same hardware, at a cost of roughly 1.5 dB of coding gain relative to the unpunctured rate 1/2 code.
Puncturing: delete coded bits by a fixed periodic pattern
R = 1/2 base, pattern period p, delete d bits
New rate = p / (2p - d)
Decoder: insert a neutral (zero) metric at deleted positions.
Typical chain:
RS(255,223) outer -> interleaver -> conv K=7 R=1/2 inner
THE MISTAKE STUDENTS MAKE
Students puncture by deleting bits arbitrarily rather than by a published pattern. Puncture patterns are chosen to maximise the free distance of the resulting higher-rate code, and an arbitrary pattern can cost several decibels for the same rate.
Source: Digital Communication Systems, 1st ed., Ch. 10, pp. 618-623 | CO5 | Bloom L5
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is A link needing rate 3/4 with a K = 7 base rate 1/2 code. Work at the pace of the slowest note-taker and land hard on the result: Rate 3/4 from the same hardware, at a cost of roughly 1.5 dB of coding gain relative to the unpunctured rate 1/2 code. Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 5: Convolutional Codes. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 10, pp. 618-623. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 50
Block codes and convolutional codes compared
What it is, why it works, and what it costs.
VTU BEC503 | Module 5
Block codes and convolutional codes c…
50
THE MECHANISM
Block codes and convolutional codes answer the same question with different structures, and each suits different traffic. Block codes need frame alignment and handle bursts well, since a burst confined to one block is bounded in its effect and Reed-Solomon codes correct symbol errors directly. Convolutional codes need no alignment, suit continuous streams, and reward soft decisions naturally, but a decoder failure produces an error event spanning several trellis steps rather than a single corrupted block. In practice the two are complementary rather than competing, which is exactly why the classic concatenated system uses one of each.
KEY TERMS
• comparison
• block boundary
• burst handling
• decoder complexity
• application fit
TAKEAWAY
Blocks suit framed data and bursts; convolutional suits streams and soft decisions — the standard answer uses both.
DIAGRAM FOR PHASE 2
A two-column comparison table with rows for "frame alignment needed", "burst errors", "soft decision fit", "decoder complexity", "failure mode" and "typical use", the block column and convolutional column fill…
Source: Digital Communication Systems, 1st ed., Ch. 10, pp. 605-623
CO4 | Bloom L5 | visual id: block-vs-convolutional-matrix
Notes: What to say: Give them the idea before the formalism. Say it plainly first: Block codes and convolutional codes answer the same question with different structures, and each suits different traffic. Then add the part they are examined on - Blocks suit framed data and bursts; convolutional suits streams and soft decisions — the standard answer uses both. Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "comparison" constrain here, and what would break if it did not hold? Animation instructions: the table header draws, then each row fills left then right with the favourable cell tinting as it lands, six rows in sequence, then the concatenated diagram draws beneath with its bracket appearing last. Transition style: Fade [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 5: Convolutional Codes. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 10, pp. 605-623. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 51
Block codes and convolutional codes compared - how it works
The procedure in order, and what each pass costs you.
VTU BEC503 | Module 5
Block codes and convolutional codes c…
51
1. Determine whether the data is framed or a continuous stream
2. Determine whether errors arrive in bursts or independently
3. Check whether the demodulator can supply soft outputs
4. Choose block coding for framed, bursty traffic and convolutional for streaming with soft outputs
5. For demanding links, concatenate: convolutional inner, Reed-Solomon outer, with an interleaver between
COST AND BEHAVIOUR
Best: each is near-optimal in its own regime
Typical: concatenation gets most of both advantages
Worst: concatenation costs two decoders and substantial latency
WHAT THAT MEANS
Modern systems increasingly use turbo or LDPC codes, which get closer to capacity than either classical family alone.
Source: Digital Communication Systems, 1st ed., Ch. 10, pp. 605-623 | CO4 | Bloom L5
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Determine whether the data is framed or a continuous stream - and check everyone has written it before moving on. At the cost panel, translate it: Modern systems increasingly use turbo or LDPC codes, which get closer to capacity than either classical family alone. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 5: Convolutional Codes. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 10, pp. 605-623. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 52
Block codes and convolutional codes compared - worked example
One concrete case, carried all the way to a stated number.
VTU BEC503 | Module 5
Block codes and convolutional codes c…
52
GIVEN
A deep-space link with a continuous telemetry stream and occasional solar bursts.
1. Continuous stream, no natural frame boundary: favours convolutional
2. Soft outputs available from the receiver: favours convolutional, worth 2 dB
3. Occasional bursts and a very low residual error requirement: favours an outer block code
4. Viterbi failures produce multi-bit error events, which Reed-Solomon symbols absorb well
RESULT
Convolutional inner with soft decisions, interleaver, Reed-Solomon outer — precisely the Voyager configuration, and for exactly these reasons.
Block: needs framing, bursts bounded per block,
RS corrects symbol errors directly
Convolutional: no framing, continuous, natural soft decision,
failures are multi-bit error events
Concatenated: RS(255,223) outer + conv K=7 R=1/2 inner
interleaver between them
total gain ~ 7-8 dB over uncoded
THE MISTAKE STUDENTS MAKE
Students treat convolutional codes as strictly better because they are newer and have soft decision decoding. A Viterbi failure produces a burst of errors spanning several trellis steps, which is exactly what a block code handles well and a convolutional code does not.
Source: Digital Communication Systems, 1st ed., Ch. 10, pp. 605-623 | CO4 | Bloom L5
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is A deep-space link with a continuous telemetry stream and occasional solar bursts. Work at the pace of the slowest note-taker and land hard on the result: Convolutional inner with soft decisions, interleaver, Reed-Solomon outer — precisely the Voyager configuration, and for exactly t… Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 5: Convolutional Codes. TB1 as listed by the syllabus: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014; Ch. 10, pp. 605-623. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 53
One sentence per unit, six months from now
Units 1-7: what survives after the detail has gone.
VTU BEC503 | Module 5
Revision
53
01 A convolutional encoder is a finite state machine on a bit stream; memory, not block length, is what carries the protection.
02 K sets the strength, and decoder cost is 2^(K-1) — which is why practical constraint lengths stop around 7 to 9.
03 The generators are the impulse responses, so encoding is convolution — and in the D domain it is just polynomial multiplication.
04 Track state, compute, shift — and remember the tail bits, which cost real rate on short messages.
05 The tree doubles every step and then starts repeating itself after M steps — merging the repeats is the whole idea of the trellis.
06 Constant width 2^M is everything: it turns an exponential search into a fixed amount of work per time step.
07 Drop time and the encoder is one small graph; its transfer function enumerates path weights and hands you the free distance.
Notes: What to say: Slow right down here. Read each takeaway aloud and then stop talking for a beat, because these are the sentences that should still be in their heads when they sit the SEE. Tell them explicitly that if they can reconstruct the reasoning behind any one of these lines they understand that unit, and if they can only recite it they do not. Pause cue: Pause for three seconds after each takeaway before moving to the next. Pointing cue: Point at each numbered takeaway in turn as you read it. Question to ask students: Ask: choose the takeaway you trust least and tell me what you would have to check to believe it. Animation instructions: Takeaway rows reveal one at a time from the top, each row highlighting briefly as it appears. Transition style: Fade [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 5: Convolutional Codes, 10 hours, TB1 (Haykin 2014) Ch. 10.6-10.8 pp. 605-623. TB1: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014. Revision consolidates all 16 unit takeaways. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 54
Revision, continued
Units 8-14: what survives after the detail has gone.
VTU BEC503 | Module 5
Revision
54
08 RSC form has the same distance as its non-recursive twin, but a single 1 now rings forever — which is what makes turbo codes work.
09 d_free is the weight of the cheapest wrong path that rejoins the right one; coding gain is 10 log10(R d_free).
10 The goal is the closest path through the trellis; the only question is whether you find it in exponential or linear time.
11 Add the branch metric, compare the two candidates, select the better, discard the other forever — 2^M times per step.
12 One corrupted bit leaves the correct path with metric 1 and every rival higher — that gap is what correction looks like numerically.
13 Trace back about 5K steps, output the oldest bit, slide on — the paths have merged by then, so the answer is the same.
14 Keeping three bits instead of one from the demodulator is worth about 2 dB — the cheapest gain in the whole chain.
Notes: What to say: Slow right down here. Read each takeaway aloud and then stop talking for a beat, because these are the sentences that should still be in their heads when they sit the SEE. Tell them explicitly that if they can reconstruct the reasoning behind any one of these lines they understand that unit, and if they can only recite it they do not. Pause cue: Pause for three seconds after each takeaway before moving to the next. Pointing cue: Point at each numbered takeaway in turn as you read it. Question to ask students: Ask: choose the takeaway you trust least and tell me what you would have to check to believe it. Animation instructions: Takeaway rows reveal one at a time from the top, each row highlighting briefly as it appears. Transition style: Fade [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 5: Convolutional Codes, 10 hours, TB1 (Haykin 2014) Ch. 10.6-10.8 pp. 605-623. TB1: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014. Revision consolidates all 16 unit takeaways. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 55
Revision, continued
Units 15-16: what survives after the detail has gone.
VTU BEC503 | Module 5
Revision
55
15 One encoder covers many rates through puncturing; interleaving makes bursts look random, and an outer code cleans up the rest.
16 Blocks suit framed data and bursts; convolutional suits streams and soft decisions — the standard answer uses both.
Notes: What to say: Slow right down here. Read each takeaway aloud and then stop talking for a beat, because these are the sentences that should still be in their heads when they sit the SEE. Tell them explicitly that if they can reconstruct the reasoning behind any one of these lines they understand that unit, and if they can only recite it they do not. Pause cue: Pause for three seconds after each takeaway before moving to the next. Pointing cue: Point at each numbered takeaway in turn as you read it. Question to ask students: Ask: choose the takeaway you trust least and tell me what you would have to check to believe it. Animation instructions: Takeaway rows reveal one at a time from the top, each row highlighting briefly as it appears. Transition style: Fade [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 5: Convolutional Codes, 10 hours, TB1 (Haykin 2014) Ch. 10.6-10.8 pp. 605-623. TB1: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014. Revision consolidates all 16 unit takeaways. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 56
How this module is assessed
Where the quiz and the assignment live, and what they test.
VTU BEC503 | Module 5
Assessment
56
MODULE 5 QUIZ
quizzes/Module_5_Quiz.pdf
quizzes/Module_5_Quiz.gift
45 minutes | 50 marks | pass 20 | 1 attempt
Part A: 20 MCQs, 1 mark each.
Part B: 13 descriptive questions, 30 marks.
Bloom spread: L1-L2 15%, L3-L4 64%, L5-L6 21%
Every question carries a CO tag, a Bloom level and a chapter reference; distractor feedback names the misconception.
MODULE 5 ASSIGNMENT
assignments/Module_5_Assignment.pdf
Assignment 5 — Convolutional encoding and Viterbi decoding
20 marks | 10% of CIE | 8 problems + 3 theory items
Submit as PDF, single file, named <USN>_BEC503_Assignment5.pdf, via LMS upload. 10% per day, nothing after 5 days.
Rubric: Correctness of encoding and representations (8); Viterbi execution and metric bookkeeping (5); Free distance and coding gain analysis (4); System reasoning (3). Attainment: CO5 = 14, CO4 = 6.
Previous years' question papers for EC are indexed in pyq/PYQ_Index.pdf; the syllabus extract and the topic-to-slide mapping are in syllabus/Syllabus_Mapping.pdf.
Individual submission. Identical submissions score zero for both parties.
Notes: What to say: Close by telling them exactly where the assessment lives and what it tests. Name the two files, say the mark split out loud, and read the Bloom spread so they understand that roughly a quarter of the paper is not recall at all. Then read the integrity line word for word, because ambiguity there costs students more than any technical error in this module. Pause cue: Pause after the Bloom spread and before the integrity statement. Pointing cue: Point at the quiz panel, then the assignment panel, then the integrity line at the bottom. Question to ask students: Ask: which course outcome do you feel least ready on, and which unit would you reread tonight to fix it? Animation instructions: Quiz panel fades in from the left, then the assignment panel from the right, then the pointers strip appears, then the integrity line fades in last. Transition style: Fade [Sources] VTU BEC503 Digital Communication syllabus, 2025 scheme, Module 5: Convolutional Codes, 10 hours, TB1 (Haykin 2014) Ch. 10.6-10.8 pp. 605-623. TB1: Simon Haykin, Digital Communication Systems, John Wiley & Sons, 1st ed., 2014. Assessment counts: 20 MCQs, 13 descriptive questions, 11 assignment items. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.