## Slide 1
Network Analysis
Module 1 asks: Given any linear network, how do I write the smallest set of equations that fully determines it — in DC and…
VTU BEC303 | Module 1
Opening
01
MODULE 1
Basic Concepts — Mesh and Node Analysis
15 contact hours | 16 teaching units | 56 slides
PRESCRIBED TEXTBOOK
Engineering Circuit Analysis
W. H. Hayt, J. E. Kemmerly and S. M. Durbin
McGraw-Hill / Tata McGraw-Hill, 8th edition, 2012
Hayt 8e Ch. 1 (1.1), Ch. 2 (2.3), Ch. 3 (3.2–3.3), Ch. 4 (4.1–4.4), Ch. 5 (5.2, 5.5), Ch. 10 (10.1–10.6), pp. 2–397
Mesh & Nodal Analysis • Network Theorems • Transient Response • Laplace / s-Domain • Two-Port Networks
Circuit models replace physical hardware → Sources supply, elements constrain → Two conservation laws generate equations → Node and mesh pick the variable → Phasors carry it into AC
EC · Semester 3 · BEC303 · generated for Phase 2 conversion
Notes: What to say: Open by putting the whole module on one page. Tell them this is 15 contact hours and 16 teaching units, and that all of it exists to answer one question: Given any linear network, how do I write the smallest set of equations that fully determines it — in DC and in AC? Name the prescribed textbook out loud and say which chapters they will be living in, so nobody is reading the wrong book by week two. Pause cue: Pause after reading the driving question aloud, before naming the textbook. Pointing cue: Point at the module title block, then at the textbook panel, then run a finger along the five-beat arc. Question to ask students: Ask: before we start, what do you already expect the answer to "Given any linear network, how do I write the smallest set of equations that fully determi…" to look like? Animation instructions: Module title block fades in first, then the textbook panel slides in from the right, then the five arc beats appear left to right one at a time. Transition style: Fade [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 1: Basic Concepts — Mesh and Node Analysis, 15 hours, Hayt 8e Ch. 1 (1.1), Ch. 2 (2.3), Ch. 3 (3.2–3.3), Ch. 4 (4.1–4.4), Ch. 5 (5.2, 5.5), Ch. 10 (10.1–10.6), pp. 2–397. TB1: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 2
What this module is actually for
One question, five beats, and the scope it does not cover.
VTU BEC303 | Module 1
Overview
02
THE DRIVING QUESTION
Given any linear network, how do I write the smallest set of equations that fully determines it — in DC and in AC?
1
Circuit models replace physical hardware
2
Sources supply, elements constrain
3
Two conservation laws generate equations
4
Node and mesh pick the variable
5
Phasors carry it into AC
SCOPE AND PROVENANCE
Built from the syllabus-listed Hayt 8e sections. Emphasis is on why nodal and mesh analysis are systematic rather than clever, on the supernode/supermesh repairs that keep them systematic when a source blocks the standard step, and on phasors as the device that makes the identical machinery work for sinusoidal steady state. Delta-wye and source transformation are presented as structure-changing shortcuts used before, not instead of, the systematic method.
Course outcomes exercised: CO1
Assessment: 20 MCQs + 13 descriptive questions + 13 assignment items
Notes: What to say: Give them the map before the territory. Read the driving question once more, then walk the five beats across the slide and say in one sentence what changes between each beat and the next. Finish on the scope paragraph, because knowing what a module does not cover saves more marks than anything else on this slide. Pause cue: Pause for four or five seconds after the five beats appear, before moving to scope. Pointing cue: Point at the driving question panel, then at each numbered beat in turn, then at the scope paragraph. Question to ask students: Ask: which of these five beats do you expect to find hardest, and why that one? Animation instructions: The driving question panel fades in, then the five numbered beats appear left to right one at a time, then the scope paragraph fades in beneath them. Transition style: Fade [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 1: Basic Concepts — Mesh and Node Analysis, 15 hours, Hayt 8e Ch. 1 (1.1), Ch. 2 (2.3), Ch. 3 (3.2–3.3), Ch. 4 (4.1–4.4), Ch. 5 (5.2, 5.5), Ch. 10 (10.1–10.6), pp. 2–397. TB1: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 3
Every unit against its chapter and pages
Units 1-9 of 16, with the deck slides that teach each one.
VTU BEC303 | Module 1
Syllabus mapping
03
# — Teaching unit — Book chapter and pages — Deck slides — CO / Bloom
01 What circuit analysis actually is — Ch. 1, pp. 2-4 — slides 5, 6, 7 — CO1 / L2
02 Sources of electrical energy: independent and dependent — Ch. 2, pp. 17-22 — slides 8, 9, 10 — CO1 / L2
03 Kirchhoff's Current Law — Ch. 3, pp. 40-42 — slides 11, 12, 13 — CO1 / L2
04 Kirchhoff's Voltage Law — Ch. 3, pp. 42-46 — slides 14, 15, 16 — CO1 / L2
05 Nodal analysis: the standard procedure — Ch. 4, pp. 80-89 — slides 17, 18, 19 — CO1 / L3
06 The supernode — Ch. 4, pp. 89-92 — slides 20, 21, 22 — CO1 / L3
07 Mesh analysis: the standard procedure — Ch. 4, pp. 92-98 — slides 23, 24, 25 — CO1 / L3
08 The supermesh — Ch. 4, pp. 98-101 — slides 26, 27, 28 — CO1 / L3
09 Nodal and mesh analysis with dependent sources — Ch. 4, pp. 80-101 — slides 29, 30, 31 — CO1 / L4
Notes: What to say: Tell them this is the slide to photograph. Every unit in the module is listed against a real chapter and a real page range, so there is no ambiguity about what to read. Point out the slide-number column and say plainly that if they miss a lecture, those are the slides covering that unit. Say that the page ranges come from the book's own table of contents rather than a guess. Pause cue: Pause for ten seconds and let them photograph the table before saying anything else. Pointing cue: Run a finger down the chapter-and-pages column, then across one complete row. Question to ask students: Ask: pick any row - which chapter would you open first, and what would you expect in the first paragraph? Animation instructions: Header row appears first, then the unit rows fade in one at a time from the top, then the chapter-and-pages column highlights. Transition style: Cut [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 1: Basic Concepts — Mesh and Node Analysis, 15 hours, Hayt 8e Ch. 1 (1.1), Ch. 2 (2.3), Ch. 3 (3.2–3.3), Ch. 4 (4.1–4.4), Ch. 5 (5.2, 5.5), Ch. 10 (10.1–10.6), pp. 2–397. TB1: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012. Mapping covers all 16 teaching units. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 4
Syllabus mapping, continued
Units 10-16 of 16, with the deck slides that teach each one.
VTU BEC303 | Module 1
Syllabus mapping
04
# — Teaching unit — Book chapter and pages — Deck slides — CO / Bloom
10 Source transformations — Ch. 5, pp. 133-141 — slides 32, 33, 34 — CO1 / L3
11 Delta-wye conversion — Ch. 5, pp. 154-157 — slides 35, 36, 37 — CO1 / L3
12 Characteristics of sinusoids — Ch. 10, pp. 371-374 — slides 38, 39, 40 — CO1 / L2
13 From forced response to the complex forcing function — Ch. 10, pp. 374-383 — slides 41, 42, 43 — CO1 / L3
14 The phasor — Ch. 10, pp. 383-389 — slides 44, 45, 46 — CO1 / L3
15 Impedance and admittance — Ch. 10, pp. 389-394 — slides 47, 48, 49 — CO1 / L3
16 Nodal and mesh analysis of AC networks — Ch. 10, pp. 394-397 — slides 50, 51, 52 — CO1 / L4
Notes: What to say: Tell them this is the slide to photograph. Every unit in the module is listed against a real chapter and a real page range, so there is no ambiguity about what to read. Point out the slide-number column and say plainly that if they miss a lecture, those are the slides covering that unit. Say that the page ranges come from the book's own table of contents rather than a guess. Pause cue: Pause for ten seconds and let them photograph the table before saying anything else. Pointing cue: Run a finger down the chapter-and-pages column, then across one complete row. Question to ask students: Ask: pick any row - which chapter would you open first, and what would you expect in the first paragraph? Animation instructions: Header row appears first, then the unit rows fade in one at a time from the top, then the chapter-and-pages column highlights. Transition style: Cut [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 1: Basic Concepts — Mesh and Node Analysis, 15 hours, Hayt 8e Ch. 1 (1.1), Ch. 2 (2.3), Ch. 3 (3.2–3.3), Ch. 4 (4.1–4.4), Ch. 5 (5.2, 5.5), Ch. 10 (10.1–10.6), pp. 2–397. TB1: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012. Mapping covers all 16 teaching units. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 5
What circuit analysis actually is
What it is, why it works, and what it costs.
VTU BEC303 | Module 1
What circuit analysis actually is
05
THE MECHANISM
Circuit analysis is the practice of replacing physical hardware with a lumped model — ideal elements joined by perfect conductors — and then solving that model exactly. The replacement is legitimate only when the device is small compared with the wavelength of the signals in it, so that voltage and current are meaningful at a terminal rather than varying along the body of the part. What you gain is a finite set of algebraic or differential equations with a unique solution; what you pay is every effect the model deliberately omits — lead inductance, stray capacitance, thermal drift. The method is worth learning because it scales: the same two conservation laws solve a two-resistor divider and a thousand-node integrated circuit.
KEY TERMS
• circuit model
• lumped element
• linearity
• analysis vs design
TAKEAWAY
A circuit diagram is a claim that the hardware behaves like the model; every analysis result inherits that claim.
DIAGRAM FOR PHASE 2
Left half: a photographed-style block labelled "Physical hardware" containing three rounded shapes — resistor body, wire, battery. Right half: a schematic panel labelled "Lumped model" with the standard R symb…
Source: Engineering Circuit Analysis, 8th ed., Ch. 1, pp. 2-4
CO1 | Bloom L2 | visual id: hardware-to-model-map
Notes: What to say: Give them the idea before the formalism. Say it plainly first: Circuit analysis is the practice of replacing physical hardware with a lumped model — ideal elements joined by perfect conductors — and then solving that… Then add the part they are examined on - A circuit diagram is a claim that the hardware behaves like the model; every analysis result inherits that claim. Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "circuit model" constrain here, and what would break if it did not hold? Animation instructions: hardware block fades in, then the crossing arrow draws left to right, then the model panel fades in, then the discarded-effects strip slides up last. Transition style: Fade [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 1: Basic Concepts — Mesh and Node Analysis. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 1, pp. 2-4. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 6
What circuit analysis actually is - how it works
The procedure in order, and what each pass costs you.
VTU BEC303 | Module 1
What circuit analysis actually is
06
1. Identify every physical part and its dominant electrical behaviour
2. Replace each part with its ideal lumped symbol
3. Replace every interconnect with a zero-resistance node
4. Label a reference direction for every unknown current and voltage
5. Write conservation equations and solve
6. Sanity-check the answer against the discarded effects
COST AND BEHAVIOUR
Best: O(n) for a series/parallel ladder
Typical: O(n^3) Gaussian elimination on n unknowns
Worst: O(n^3) with dense coupling
WHAT THAT MEANS
n is the number of unknowns chosen, which is why the choice of node vs mesh variables matters more than the solver.
Source: Engineering Circuit Analysis, 8th ed., Ch. 1, pp. 2-4 | CO1 | Bloom L2
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Identify every physical part and its dominant electrical behaviour - and check everyone has written it before moving on. At the cost panel, translate it: n is the number of unknowns chosen, which is why the choice of node vs mesh variables matters more than the solver. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 1: Basic Concepts — Mesh and Node Analysis. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 1, pp. 2-4. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 7
What circuit analysis actually is - worked example
One concrete case, carried all the way to a stated number.
VTU BEC303 | Module 1
What circuit analysis actually is
07
GIVEN
A 9 V battery with 0.5 Ω internal resistance driving a 100 Ω resistor through 20 cm of copper wire.
1. Wire resistance ≈ 0.01 Ω, small against 100 Ω → model wire as an ideal node
2. Battery becomes 9 V ideal source in series with 0.5 Ω
3. Series loop: I = 9 / (0.5 + 100) = 0.0896 A
4. Load voltage = 0.0896 × 100 = 8.96 V
RESULT
I = 89.6 mA, V_load = 8.96 V; the 0.44 V lost is the modelled internal resistance, not the wire.
V_source = I·(R_internal + R_load)
9 = I·(0.5 + 100)
I = 0.0896 A
THE MISTAKE STUDENTS MAKE
Students treat the schematic as the truth and the hardware as an imperfect copy of it. It is the other way round — the schematic is the approximation, and when a measurement disagrees with the analysis the first suspect is a discarded effect, not arithmetic.
Source: Engineering Circuit Analysis, 8th ed., Ch. 1, pp. 2-4 | CO1 | Bloom L2
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is A 9 V battery with 0.5 Ω internal resistance driving a 100 Ω resistor through 20 cm of copper wire. Work at the pace of the slowest note-taker and land hard on the result: I = 89.6 mA, V_load = 8.96 V; the 0.44 V lost is the modelled internal resistance, not the wire. Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 1: Basic Concepts — Mesh and Node Analysis. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 1, pp. 2-4. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 8
Sources of electrical energy: independent and dependent
What it is, why it works, and what it costs.
VTU BEC303 | Module 1
Sources of electrical energy: indepen…
08
THE MECHANISM
A source is the element that supplies energy to a network rather than constraining it passively. An independent source fixes its voltage or its current at a value that does not depend on anything else in the circuit — an ideal voltage source holds V regardless of current drawn, an ideal current source holds I regardless of voltage across it. A dependent source fixes its output as a multiple of some other voltage or current in the same circuit, giving four types: VCVS, VCCS, CCVS, CCCS. Dependent sources are how transistor and op-amp models get their gain into a linear network, and they are the reason a linear circuit can amplify at all — passive elements alone can only divide.
KEY TERMS
• independent source
• dependent source
• VCVS
• CCCS
• active element
TAKEAWAY
Independent sources set the excitation; dependent sources set the gain, and both must appear before any conservation equation can be written.
DIAGRAM FOR PHASE 2
A 2×3 grid. Top row, two cells: "Independent voltage source" showing a circle with + / − and the caption "V fixed, I free", and "Independent current source" showing a circle with an arrow and "I fixed, V free"…
Source: Engineering Circuit Analysis, 8th ed., Ch. 2, pp. 17-22
CO1 | Bloom L2 | visual id: source-taxonomy-grid
Notes: What to say: Give them the idea before the formalism. Say it plainly first: A source is the element that supplies energy to a network rather than constraining it passively. Then add the part they are examined on - Independent sources set the excitation; dependent sources set the gain, and both must appear before any conservation equatio… Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "independent source" constrain here, and what would break if it did not hold? Animation instructions: the divider draws first, then the two independent cells fade in together, then the four dependent diamonds pop in clockwise from top-left, then each gain symbol fades in last. Transition style: Fade [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 1: Basic Concepts — Mesh and Node Analysis. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 2, pp. 17-22. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 9
Sources of electrical energy: independent and dependent - how it works
The procedure in order, and what each pass costs you.
VTU BEC303 | Module 1
Sources of electrical energy: indepen…
09
1. Scan the schematic for circle symbols — these are independent sources
2. Scan for diamond symbols — these are dependent sources
3. For each diamond, find and label its controlling variable elsewhere in the circuit
4. Note that a controlling variable is an extra unknown unless it can be written in terms of chosen variables
5. Never short an ideal voltage source or open an ideal current source when simplifying
COST AND BEHAVIOUR
Best: no extra unknowns when the controlling variable is already a chosen node voltage
Typical: one constraint equation per dependent source
Worst: one extra unknown and one constraint per dependent source
WHAT THAT MEANS
Dependent sources never increase the order of the system, only the bookkeeping.
Source: Engineering Circuit Analysis, 8th ed., Ch. 2, pp. 17-22 | CO1 | Bloom L2
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Scan the schematic for circle symbols — these are independent sources - and check everyone has written it before moving on. At the cost panel, translate it: Dependent sources never increase the order of the system, only the bookkeeping. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 1: Basic Concepts — Mesh and Node Analysis. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 2, pp. 17-22. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 10
Sources of electrical energy: independent and dependent - worked example
One concrete case, carried all the way to a stated number.
VTU BEC303 | Module 1
Sources of electrical energy: indepen…
10
GIVEN
A 12 V independent source in series with 4 kΩ feeding a node, where a VCVS of value 3·v_x sits in the return path and v_x is the drop across the 4 kΩ.
1. Let the loop current be I; v_x = 4000·I
2. KVL round the loop: 12 − 4000·I − 3·v_x = 0
3. Substitute the control law: 12 − 4000·I − 12000·I = 0
4. I = 12 / 16000 = 0.75 mA
RESULT
I = 0.75 mA and v_x = 3 V; the dependent source contributes 9 V of opposition even though it supplies no independent energy.
v_x = 4kΩ · I
12 − 4000I − 3(4000I) = 0
I = 0.75 mA, v_x = 3 V
THE MISTAKE STUDENTS MAKE
Students kill a dependent source along with the independent ones when applying superposition or finding a Thévenin resistance. Dependent sources stay live — only independent sources are zeroed — because a dependent source carries the circuit's gain, not its excitation.
Source: Engineering Circuit Analysis, 8th ed., Ch. 2, pp. 17-22 | CO1 | Bloom L2
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is A 12 V independent source in series with 4 kΩ feeding a node, where a VCVS of value 3·v_x sits in the return path and v_x is the drop acros… Work at the pace of the slowest note-taker and land hard on the result: I = 0.75 mA and v_x = 3 V; the dependent source contributes 9 V of opposition even though it supplies no independent energy. Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 1: Basic Concepts — Mesh and Node Analysis. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 2, pp. 17-22. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 11
Kirchhoff's Current Law
What it is, why it works, and what it costs.
VTU BEC303 | Module 1
Kirchhoff's Current Law
11
THE MECHANISM
KCL states that the algebraic sum of currents entering any node is zero at every instant. It is charge conservation applied to a point that can store no charge: a node in a lumped model has no capacitance to ground, so whatever arrives must leave. The law is not restricted to single nodes — it holds for any closed boundary drawn around a group of nodes, which is exactly what later licenses the supernode. KCL is instantaneous and independent of element type, so it applies unchanged to resistors, capacitors, dependent sources and nonlinear devices.
KEY TERMS
• node
• KCL
• charge conservation
• supernode boundary
• Gaussian surface
TAKEAWAY
KCL is a statement about a boundary, not about a dot on the page — draw the boundary wherever it makes the algebra smallest.
DIAGRAM FOR PHASE 2
Centre: a node dot with five branches radiating outward, three arrows pointing in labelled i1, i2, i3 and two pointing out labelled i4, i5. Beneath, the equation i1 + i2 + i3 = i4 + i5. A dashed closed curve i…
Source: Engineering Circuit Analysis, 8th ed., Ch. 3, pp. 40-42
CO1 | Bloom L2 | visual id: kcl-boundary-bubble
Notes: What to say: Give them the idea before the formalism. Say it plainly first: KCL states that the algebraic sum of currents entering any node is zero at every instant. Then add the part they are examined on - KCL is a statement about a boundary, not about a dot on the page — draw the boundary wherever it makes the algebra smallest. Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "node" constrain here, and what would break if it did not hold? Animation instructions: node and its five arrows draw in one by one, then the first equation types in, then the dashed boundary draws around the two-node cluster, then the interior branch dims to grey to show it cancels, then the second equation appears. Transition style: Fade [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 1: Basic Concepts — Mesh and Node Analysis. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 3, pp. 40-42. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 12
Kirchhoff's Current Law - how it works
The procedure in order, and what each pass costs you.
VTU BEC303 | Module 1
Kirchhoff's Current Law
12
1. Choose a node or draw a closed boundary around several nodes
2. Assign a sign convention — entering positive is conventional
3. List every branch that crosses the boundary
4. Write each crossing current in terms of the chosen unknowns
5. Set the algebraic sum to zero
6. Ignore every branch entirely inside the boundary
COST AND BEHAVIOUR
Best: trivial at a two-branch node — the currents are simply equal
Typical: one usable equation per node minus one
Worst: N−1 independent equations for N nodes
WHAT THAT MEANS
The Nth KCL equation is always a linear combination of the others, so writing it adds nothing.
Source: Engineering Circuit Analysis, 8th ed., Ch. 3, pp. 40-42 | CO1 | Bloom L2
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Choose a node or draw a closed boundary around several nodes - and check everyone has written it before moving on. At the cost panel, translate it: The Nth KCL equation is always a linear combination of the others, so writing it adds nothing. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 1: Basic Concepts — Mesh and Node Analysis. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 3, pp. 40-42. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 13
Kirchhoff's Current Law - worked example
One concrete case, carried all the way to a stated number.
VTU BEC303 | Module 1
Kirchhoff's Current Law
13
GIVEN
A node fed by 5 A and 3 A, with two exit branches, one carrying 6 A and one unknown.
1. Entering: 5 + 3 = 8 A
2. Leaving: 6 + i_x
3. KCL: 8 − 6 − i_x = 0
4. i_x = 2 A
RESULT
i_x = 2 A leaving the node; a negative answer would simply have meant the assumed arrow was backwards.
Σ i_in = Σ i_out
5 + 3 = 6 + i_x
i_x = 2 A
THE MISTAKE STUDENTS MAKE
Students redraw arrows when an answer comes out negative. A negative current is a correct answer expressed against an assumed reference — changing the arrow midway through invalidates every other equation that used it.
Source: Engineering Circuit Analysis, 8th ed., Ch. 3, pp. 40-42 | CO1 | Bloom L2
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is A node fed by 5 A and 3 A, with two exit branches, one carrying 6 A and one unknown. Work at the pace of the slowest note-taker and land hard on the result: i_x = 2 A leaving the node; a negative answer would simply have meant the assumed arrow was backwards. Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 1: Basic Concepts — Mesh and Node Analysis. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 3, pp. 40-42. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 14
Kirchhoff's Voltage Law
What it is, why it works, and what it costs.
VTU BEC303 | Module 1
Kirchhoff's Voltage Law
14
THE MECHANISM
KVL states that the algebraic sum of voltages around any closed loop is zero. It is energy conservation for a unit charge: carry one coulomb all the way round a loop and return it to its starting point, and the net work done on it must be zero because potential is a single-valued function of position. The law holds for any closed path, whether or not that path follows real wires, and it holds instantaneously for any element. In a planar circuit the natural choice of loops is the set of meshes — loops enclosing no other loop — because those give exactly the independent equations needed and no redundant ones.
KEY TERMS
• loop
• mesh
• KVL
• energy conservation
• reference polarity
TAKEAWAY
KVL works because potential is single-valued; the loop you choose is free, but choosing meshes guarantees independence.
DIAGRAM FOR PHASE 2
A rectangular loop with four elements on its sides: a source on the left marked + above −, and three resistors on the top, right and bottom with + / − polarities marked. A small walking marker travels clockwis…
Source: Engineering Circuit Analysis, 8th ed., Ch. 3, pp. 42-46
CO1 | Bloom L2 | visual id: kvl-loop-walk
Notes: What to say: Give them the idea before the formalism. Say it plainly first: KVL states that the algebraic sum of voltages around any closed loop is zero. Then add the part they are examined on - KVL works because potential is single-valued; the loop you choose is free, but choosing meshes guarantees independence. Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "loop" constrain here, and what would break if it did not hold? Animation instructions: the loop rectangle draws, then the four polarity pairs fade in, then the walking marker animates clockwise one element at a time with its term appearing in sync, then the completed equation highlights. Transition style: Fade [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 1: Basic Concepts — Mesh and Node Analysis. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 3, pp. 42-46. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 15
Kirchhoff's Voltage Law - how it works
The procedure in order, and what each pass costs you.
VTU BEC303 | Module 1
Kirchhoff's Voltage Law
15
1. Pick a closed loop and a direction to traverse it
2. Mark a reference polarity on every element in the loop
3. Start anywhere and walk the loop in the chosen direction
4. Add the element voltage when you enter at + and subtract when you enter at −
5. Set the total to zero
6. Repeat for each mesh to get an independent set
COST AND BEHAVIOUR
Best: a single-loop circuit needs exactly one equation
Typical: B − N + 1 independent loop equations for B branches and N nodes
Worst: B − N + 1, the number of meshes in a planar network
WHAT THAT MEANS
Any additional loop equation is a sum of mesh equations and carries no new information.
Source: Engineering Circuit Analysis, 8th ed., Ch. 3, pp. 42-46 | CO1 | Bloom L2
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Pick a closed loop and a direction to traverse it - and check everyone has written it before moving on. At the cost panel, translate it: Any additional loop equation is a sum of mesh equations and carries no new information. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 1: Basic Concepts — Mesh and Node Analysis. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 3, pp. 42-46. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 16
Kirchhoff's Voltage Law - worked example
One concrete case, carried all the way to a stated number.
VTU BEC303 | Module 1
Kirchhoff's Voltage Law
16
GIVEN
A 20 V source driving 2 kΩ and 3 kΩ in series.
1. Assume clockwise current I
2. KVL: −20 + 2000·I + 3000·I = 0
3. I = 20 / 5000 = 4 mA
4. v_2k = 8 V, v_3k = 12 V
RESULT
I = 4 mA with 8 V and 12 V across the two resistors, summing back to the 20 V source as KVL requires.
−20 + 2000I + 3000I = 0
I = 4 mA
v = (8 V, 12 V), Σv = 20 V ✓
THE MISTAKE STUDENTS MAKE
Students apply KVL only around paths made of real wire and conclude it cannot be used across an open switch or a capacitor gap. KVL applies to any closed path in a lumped model, including one that jumps an open circuit, where the term is simply the unknown open-circuit voltage.
Source: Engineering Circuit Analysis, 8th ed., Ch. 3, pp. 42-46 | CO1 | Bloom L2
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is A 20 V source driving 2 kΩ and 3 kΩ in series. Work at the pace of the slowest note-taker and land hard on the result: I = 4 mA with 8 V and 12 V across the two resistors, summing back to the 20 V source as KVL requires. Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 1: Basic Concepts — Mesh and Node Analysis. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 3, pp. 42-46. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 17
Nodal analysis: the standard procedure
What it is, why it works, and what it costs.
VTU BEC303 | Module 1
Nodal analysis: the standard procedure
17
THE MECHANISM
Nodal analysis chooses node voltages as the unknowns and generates one KCL equation per non-reference node. Choosing voltages rather than branch currents halves the bookkeeping because every element current can be written directly from the two node voltages at its ends and its own conductance. One node is declared the reference and assigned zero volts; this is a free choice that removes an arbitrary constant, not a physical statement about earth. The resulting system is a conductance matrix that is symmetric and diagonally dominant for a purely resistive network with independent sources only, which is why it always has a unique solution.
KEY TERMS
• reference node
• node voltage
• conductance matrix
• ground
TAKEAWAY
Nodal analysis trades a large number of branch currents for a small number of node voltages, and the count of equations is fixed before you look at a single element.
DIAGRAM FOR PHASE 2
Left: a three-node circuit with the bottom node hatched and labelled "reference, 0 V", and the two upper nodes circled and labelled v1 and v2, with conductances G1, G2, G3 drawn between them and a current sour…
Source: Engineering Circuit Analysis, 8th ed., Ch. 4, pp. 80-89
CO1 | Bloom L3 | visual id: nodal-matrix-build
Notes: What to say: Give them the idea before the formalism. Say it plainly first: Nodal analysis chooses node voltages as the unknowns and generates one KCL equation per non-reference node. Then add the part they are examined on - Nodal analysis trades a large number of branch currents for a small number of node voltages, and the count of equations is f… Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "reference node" constrain here, and what would break if it did not hold? Animation instructions: circuit fades in, reference node hatching appears, then v1 is highlighted and its KCL terms fly across to populate matrix row 1, then v2 highlights and populates row 2, then the symmetry of the off-diagonal pair is marked with a two-headed arrow. Transition style: Fade [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 1: Basic Concepts — Mesh and Node Analysis. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 4, pp. 80-89. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 18
Nodal analysis: the standard procedure - how it works
The procedure in order, and what each pass costs you.
VTU BEC303 | Module 1
Nodal analysis: the standard procedure
18
1. Count nodes N; choose the node with most connections as reference
2. Label the remaining N−1 node voltages
3. Write KCL at each labelled node
4. Express every branch current as (v_near − v_far)·G
5. Move known source currents to the right-hand side
6. Solve the N−1 simultaneous equations
COST AND BEHAVIOUR
Best: O(1) when one node voltage is fixed directly by a grounded source
Typical: O((N−1)^3) elimination
Worst: O((N−1)^3) for a densely connected network
WHAT THAT MEANS
Prefer nodal when the circuit has many voltage-defined branches and few loops.
Source: Engineering Circuit Analysis, 8th ed., Ch. 4, pp. 80-89 | CO1 | Bloom L3
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Count nodes N; choose the node with most connections as reference - and check everyone has written it before moving on. At the cost panel, translate it: Prefer nodal when the circuit has many voltage-defined branches and few loops. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 1: Basic Concepts — Mesh and Node Analysis. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 4, pp. 80-89. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 19
Nodal analysis: the standard procedure - worked example
One concrete case, carried all the way to a stated number.
VTU BEC303 | Module 1
Nodal analysis: the standard procedure
19
GIVEN
A 6 mA source into node v1, with 2 kΩ from v1 to ground, 1 kΩ from v1 to v2 and 3 kΩ from v2 to ground.
1. Node v1: v1/2000 + (v1 − v2)/1000 = 0.006
2. Node v2: (v2 − v1)/1000 + v2/3000 = 0
3. From node 2: v1 = v2·(1 + 1/3) = 1.3333·v2
4. Substitute: 1.3333v2/2000 + 0.3333v2/1000 = 0.006 → v2 = 6 V, v1 = 8 V
RESULT
v1 = 8 V and v2 = 6 V; the 1 kΩ carries 2 mA, which checks against the 2 mA leaving v2 through the 3 kΩ.
[ 1/2k + 1/1k −1/1k ] [v1] [6 mA]
[ −1/1k 1/1k + 1/3k ] [v2] = [ 0 ]
v1 = 8 V, v2 = 6 V
THE MISTAKE STUDENTS MAKE
Students write the current through a resistor as v_node/R even when the far end is not at ground. The term is always (v_near − v_far)/R; dropping the far node silently grounds an element that was never grounded.
Source: Engineering Circuit Analysis, 8th ed., Ch. 4, pp. 80-89 | CO1 | Bloom L3
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is A 6 mA source into node v1, with 2 kΩ from v1 to ground, 1 kΩ from v1 to v2 and 3 kΩ from v2 to ground. Work at the pace of the slowest note-taker and land hard on the result: v1 = 8 V and v2 = 6 V; the 1 kΩ carries 2 mA, which checks against the 2 mA leaving v2 through the 3 kΩ. Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 1: Basic Concepts — Mesh and Node Analysis. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 4, pp. 80-89. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 20
The supernode
What it is, why it works, and what it costs.
VTU BEC303 | Module 1
The supernode
20
THE MECHANISM
A supernode is the repair for a voltage source that sits between two non-reference nodes, where neither node voltage is directly known and no current expression exists for the source branch. The fix is to draw a closed boundary enclosing both nodes and the source, and apply KCL to that boundary — legitimate because KCL holds for any boundary, and the unknown source current is now internal and cancels. That gives one equation for two unknowns, so the missing second equation comes from the source itself: the constraint v_a − v_b equals the source value. The cost is that the tidy symmetric conductance matrix is lost, since one row is now a constraint rather than a KCL statement.
KEY TERMS
• supernode
• floating source
• constraint equation
• boundary KCL
TAKEAWAY
A floating voltage source removes a KCL equation and hands back a constraint equation; the equation count never changes.
DIAGRAM FOR PHASE 2
A four-node circuit with a voltage source V_s connected directly between nodes v2 and v3, neither of which is the reference. A dashed rounded rectangle is drawn enclosing v2, v3 and V_s together. Arrows for th…
Source: Engineering Circuit Analysis, 8th ed., Ch. 4, pp. 89-92
CO1 | Bloom L3 | visual id: supernode-bubble
Notes: What to say: Give them the idea before the formalism. Say it plainly first: A supernode is the repair for a voltage source that sits between two non-reference nodes, where neither node voltage is directly known and no current expr… Then add the part they are examined on - A floating voltage source removes a KCL equation and hands back a constraint equation; the equation count never changes. Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "supernode" constrain here, and what would break if it did not hold? Animation instructions: circuit fades in, the source between v2 and v3 flashes red as "no current expression", the dashed bubble draws around it, the internal current greys out, then the boundary KCL strip appears, then the constraint strip appears. Transition style: Fade [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 1: Basic Concepts — Mesh and Node Analysis. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 4, pp. 89-92. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 21
The supernode - how it works
The procedure in order, and what each pass costs you.
VTU BEC303 | Module 1
The supernode
21
1. Locate every voltage source not connected to the reference node
2. Enclose each such source and its two nodes in a supernode boundary
3. Write one KCL equation for the whole boundary, ignoring internal branches
4. Write the constraint equation from the source value and polarity
5. Write ordinary KCL at all remaining non-reference nodes
6. Solve the combined system
COST AND BEHAVIOUR
Best: no supernodes needed when every source has one end grounded
Typical: one supernode per floating source, equation count unchanged
Worst: supernodes chained when sources share nodes, forming one large boundary
WHAT THAT MEANS
Matrix symmetry is lost but the solution cost is unchanged.
Source: Engineering Circuit Analysis, 8th ed., Ch. 4, pp. 89-92 | CO1 | Bloom L3
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Locate every voltage source not connected to the reference node - and check everyone has written it before moving on. At the cost panel, translate it: Matrix symmetry is lost but the solution cost is unchanged. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 1: Basic Concepts — Mesh and Node Analysis. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 4, pp. 89-92. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 22
The supernode - worked example
One concrete case, carried all the way to a stated number.
VTU BEC303 | Module 1
The supernode
22
GIVEN
Nodes v1 and v2 bridged by a floating 10 V source (+ at v1), with 5 kΩ from v1 to ground, 10 kΩ from v2 to ground, and 2 mA injected into v1.
1. Supernode boundary encloses v1, v2 and the 10 V source
2. Boundary KCL: v1/5000 + v2/10000 = 0.002
3. Constraint: v1 − v2 = 10
4. Substitute v1 = v2 + 10: (v2+10)/5000 + v2/10000 = 0.002
RESULT
v1 = 10 V, v2 = 0 V; the source delivers 2 mA into the 5 kΩ and nothing through the 10 kΩ.
boundary KCL: v1/5k + v2/10k = 2 mA
constraint : v1 − v2 = 10
⇒ v1 = 10 V, v2 = 0 V
THE MISTAKE STUDENTS MAKE
Students write KCL separately at each node of the supernode and invent a symbol for the source current, then forget to eliminate it. The whole point of the boundary is that the source current never has to be named.
Source: Engineering Circuit Analysis, 8th ed., Ch. 4, pp. 89-92 | CO1 | Bloom L3
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is Nodes v1 and v2 bridged by a floating 10 V source (+ at v1), with 5 kΩ from v1 to ground, 10 kΩ from v2 to ground, and 2 mA injected into v… Work at the pace of the slowest note-taker and land hard on the result: v1 = 10 V, v2 = 0 V; the source delivers 2 mA into the 5 kΩ and nothing through the 10 kΩ. Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 1: Basic Concepts — Mesh and Node Analysis. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 4, pp. 89-92. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 23
Mesh analysis: the standard procedure
What it is, why it works, and what it costs.
VTU BEC303 | Module 1
Mesh analysis: the standard procedure
23
THE MECHANISM
Mesh analysis chooses circulating mesh currents as unknowns and writes one KVL equation per mesh. A mesh current is a mathematical device, not a measurable quantity: the physical branch current in an element shared by two meshes is the difference of the two mesh currents. The method requires a planar circuit — one that can be drawn without crossing wires — because only then do the meshes form a complete independent set. For a network of independent voltage sources and resistors the result is a symmetric resistance matrix whose diagonal is the total resistance around each mesh and whose off-diagonal entries are the negated shared resistances.
KEY TERMS
• mesh
• mesh current
• planar circuit
• resistance matrix
TAKEAWAY
Mesh currents are fictitious circulating variables; only their differences across shared branches are physically real.
DIAGRAM FOR PHASE 2
A two-mesh ladder circuit drawn as two adjacent rectangles sharing a vertical middle branch containing R2. A blue circular arrow labelled i1 loops clockwise inside the left rectangle, a green circular arrow la…
Source: Engineering Circuit Analysis, 8th ed., Ch. 4, pp. 92-98
CO1 | Bloom L3 | visual id: mesh-current-overlap
Notes: What to say: Give them the idea before the formalism. Say it plainly first: Mesh analysis chooses circulating mesh currents as unknowns and writes one KVL equation per mesh. Then add the part they are examined on - Mesh currents are fictitious circulating variables; only their differences across shared branches are physically real. Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "mesh" constrain here, and what would break if it did not hold? Animation instructions: the ladder draws, then the blue loop animates around mesh 1, then the green loop animates around mesh 2, then the shared branch highlights and the difference annotation appears, then the matrix builds row by row. Transition style: Fade [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 1: Basic Concepts — Mesh and Node Analysis. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 4, pp. 92-98. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 24
Mesh analysis: the standard procedure - how it works
The procedure in order, and what each pass costs you.
VTU BEC303 | Module 1
Mesh analysis: the standard procedure
24
1. Confirm the circuit is planar and identify each mesh
2. Assign a circulating current to every mesh, all in the same direction
3. Write KVL around each mesh
4. For a shared element use the difference of the two mesh currents
5. Collect terms into a resistance matrix
6. Solve, then convert mesh currents into branch currents
COST AND BEHAVIOUR
Best: O(1) for a single-mesh circuit
Typical: O(M^3) for M meshes
Worst: O(M^3), M = B − N + 1
WHAT THAT MEANS
Prefer mesh analysis when voltage sources dominate and the mesh count is below the node count.
Source: Engineering Circuit Analysis, 8th ed., Ch. 4, pp. 92-98 | CO1 | Bloom L3
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Confirm the circuit is planar and identify each mesh - and check everyone has written it before moving on. At the cost panel, translate it: Prefer mesh analysis when voltage sources dominate and the mesh count is below the node count. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 1: Basic Concepts — Mesh and Node Analysis. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 4, pp. 92-98. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 25
Mesh analysis: the standard procedure - worked example
One concrete case, carried all the way to a stated number.
VTU BEC303 | Module 1
Mesh analysis: the standard procedure
25
GIVEN
Two meshes: 10 V source and 1 kΩ in mesh 1, 2 kΩ shared, 3 kΩ in mesh 2 with no source.
1. Mesh 1: −10 + 1000·i1 + 2000·(i1 − i2) = 0
2. Mesh 2: 2000·(i2 − i1) + 3000·i2 = 0
3. From mesh 2: 5000·i2 = 2000·i1 → i2 = 0.4·i1
4. Mesh 1: 3000i1 − 2000(0.4i1) = 10 → 2200·i1 = 10 → i1 = 4.545 mA, i2 = 1.818 mA
RESULT
i1 = 4.545 mA, i2 = 1.818 mA, and the shared 2 kΩ actually carries i1 − i2 = 2.727 mA.
[ 1k+2k −2k ] [i1] [10]
[ −2k 2k+3k ] [i2] = [ 0]
i1 = 4.545 mA, i2 = 1.818 mA
THE MISTAKE STUDENTS MAKE
Students report the mesh current as the current in a shared branch. In a shared element the reading on an ammeter would be i1 − i2; quoting i1 alone overstates the current in every branch the two meshes have in common.
Source: Engineering Circuit Analysis, 8th ed., Ch. 4, pp. 92-98 | CO1 | Bloom L3
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is Two meshes: 10 V source and 1 kΩ in mesh 1, 2 kΩ shared, 3 kΩ in mesh 2 with no source. Work at the pace of the slowest note-taker and land hard on the result: i1 = 4.545 mA, i2 = 1.818 mA, and the shared 2 kΩ actually carries i1 − i2 = 2.727 mA. Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 1: Basic Concepts — Mesh and Node Analysis. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 4, pp. 92-98. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 26
The supermesh
What it is, why it works, and what it costs.
VTU BEC303 | Module 1
The supermesh
26
THE MECHANISM
A supermesh is the mesh-analysis counterpart of the supernode, used when a current source sits on a branch shared by two meshes and therefore has an unknown and unexpressible voltage across it. The repair is to avoid traversing that branch: merge the two meshes into one larger loop and write KVL around the outside of the merged region only. The missing equation is supplied by the source itself, whose value fixes the difference between the two mesh currents. A current source on the outer boundary of a single mesh needs no supermesh at all — it simply sets that mesh current directly and removes an unknown.
KEY TERMS
• supermesh
• shared current source
• merged loop
• constraint equation
TAKEAWAY
You cannot write KVL across a current source, so route the loop around it and recover the lost equation from the source value.
DIAGRAM FOR PHASE 2
Two adjacent mesh rectangles sharing a vertical branch that contains a current source I_s drawn as a circle with an arrow. The shared branch flashes and is annotated "v across source unknown". The internal div…
Source: Engineering Circuit Analysis, 8th ed., Ch. 4, pp. 98-101
CO1 | Bloom L3 | visual id: supermesh-merge
Notes: What to say: Give them the idea before the formalism. Say it plainly first: A supermesh is the mesh-analysis counterpart of the supernode, used when a current source sits on a branch shared by two meshes and therefore has an unkno… Then add the part they are examined on - You cannot write KVL across a current source, so route the loop around it and recover the lost equation from the source valu… Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "supermesh" constrain here, and what would break if it did not hold? Animation instructions: both meshes fade in, the shared source flashes amber, the dividing branch dissolves to dotted grey, the outer loop traces around the perimeter, then the two equation strips appear in order. Transition style: Fade [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 1: Basic Concepts — Mesh and Node Analysis. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 4, pp. 98-101. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 27
The supermesh - how it works
The procedure in order, and what each pass costs you.
VTU BEC303 | Module 1
The supermesh
27
1. Find current sources on branches shared between two meshes
2. Merge those two meshes and discard the shared branch from the traversal path
3. Write one KVL equation around the merged outer path
4. Write the constraint relating the two mesh currents to the source value
5. Write ordinary KVL for all unmerged meshes
6. Solve the combined system
COST AND BEHAVIOUR
Best: source on an outer branch fixes a mesh current directly, reducing unknowns by one
Typical: one supermesh per shared current source, equation count unchanged
Worst: chained supermeshes when sources share meshes
WHAT THAT MEANS
Like the supernode, symmetry is lost but the order of the system is not.
Source: Engineering Circuit Analysis, 8th ed., Ch. 4, pp. 98-101 | CO1 | Bloom L3
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Find current sources on branches shared between two meshes - and check everyone has written it before moving on. At the cost panel, translate it: Like the supernode, symmetry is lost but the order of the system is not. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 1: Basic Concepts — Mesh and Node Analysis. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 4, pp. 98-101. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 28
The supermesh - worked example
One concrete case, carried all the way to a stated number.
VTU BEC303 | Module 1
The supermesh
28
GIVEN
Two meshes sharing a 3 mA source; mesh 1 has a 12 V source and 2 kΩ, mesh 2 has 4 kΩ.
1. Constraint from the shared source: i1 − i2 = 0.003
2. Supermesh KVL round the outside: −12 + 2000·i1 + 4000·i2 = 0
3. Substitute i1 = i2 + 0.003: −12 + 2000i2 + 6 + 4000i2 = 0
4. 6000·i2 = 6 → i2 = 1 mA, i1 = 4 mA
RESULT
i1 = 4 mA, i2 = 1 mA, and the voltage across the current source can now be recovered afterwards from either mesh equation.
constraint : i1 − i2 = 3 mA
supermesh : −12 + 2k·i1 + 4k·i2 = 0
⇒ i1 = 4 mA, i2 = 1 mA
THE MISTAKE STUDENTS MAKE
Students include the shared branch in the supermesh KVL walk, adding an unknown source voltage they then cannot eliminate. The merged path must go around the source, never through it.
Source: Engineering Circuit Analysis, 8th ed., Ch. 4, pp. 98-101 | CO1 | Bloom L3
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is Two meshes sharing a 3 mA source; mesh 1 has a 12 V source and 2 kΩ, mesh 2 has 4 kΩ. Work at the pace of the slowest note-taker and land hard on the result: i1 = 4 mA, i2 = 1 mA, and the voltage across the current source can now be recovered afterwards from either mesh equation. Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 1: Basic Concepts — Mesh and Node Analysis. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 4, pp. 98-101. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 29
Nodal and mesh analysis with dependent sources
What it is, why it works, and what it costs.
VTU BEC303 | Module 1
Nodal and mesh analysis with dependen…
29
THE MECHANISM
Adding a dependent source changes nothing structural about nodal or mesh analysis — the same KCL or KVL equations are written — but it introduces a controlling variable that must be expressed in terms of the chosen unknowns. If the controlling quantity happens to be a node voltage or a mesh current, substitution is immediate. If it is some other branch voltage or current, one auxiliary equation is written to relate it to the chosen variables and then eliminated. The practical consequence is that the coefficient matrix loses its symmetry, because a dependent source contributes a term to one row that has no matching term in the mirrored position.
KEY TERMS
• controlling variable
• auxiliary equation
• asymmetric matrix
• gain constraint
TAKEAWAY
Dependent sources cost one auxiliary equation each and destroy matrix symmetry, but never change how many unknowns you started with.
DIAGRAM FOR PHASE 2
Three panels left to right joined by arrows. Panel 1 "Write KCL as usual" shows a node equation containing the symbol 4·i_x highlighted amber. Panel 2 "Express the control" shows i_x = (v1 − v2)/R with the sam…
Source: Engineering Circuit Analysis, 8th ed., Ch. 4, pp. 80-101
CO1 | Bloom L4 | visual id: dependent-substitution-chain
Notes: What to say: Give them the idea before the formalism. Say it plainly first: Adding a dependent source changes nothing structural about nodal or mesh analysis — the same KCL or KVL equations are written — but it introduces a contro… Then add the part they are examined on - Dependent sources cost one auxiliary equation each and destroy matrix symmetry, but never change how many unknowns you start… Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "controlling variable" constrain here, and what would break if it did not hold? Animation instructions: panel 1 fades in, arrow draws, panel 2 fades in, the amber terms pulse simultaneously in both panels, arrow draws, panel 3 fades in, then the red symmetry box appears last. Transition style: Fade [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 1: Basic Concepts — Mesh and Node Analysis. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 4, pp. 80-101. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 30
Nodal and mesh analysis with dependent sources - how it works
The procedure in order, and what each pass costs you.
VTU BEC303 | Module 1
Nodal and mesh analysis with dependen…
30
1. Write the nodal or mesh equations exactly as if all sources were independent
2. Identify each controlling variable by name
3. Write one auxiliary equation per controlling variable in terms of the chosen unknowns
4. Substitute to eliminate the controlling variables
5. Collect coefficients and solve
6. Expect an asymmetric matrix and do not treat that as an error
COST AND BEHAVIOUR
Best: zero extra work when the control is already a chosen unknown
Typical: one substitution per dependent source
Worst: one auxiliary equation per dependent source plus loss of symmetry
WHAT THAT MEANS
Symmetry loss removes some numerical shortcuts but not solvability.
Source: Engineering Circuit Analysis, 8th ed., Ch. 4, pp. 80-101 | CO1 | Bloom L4
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Write the nodal or mesh equations exactly as if all sources were independent - and check everyone has written it before moving on. At the cost panel, translate it: Symmetry loss removes some numerical shortcuts but not solvability. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 1: Basic Concepts — Mesh and Node Analysis. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 4, pp. 80-101. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 31
Nodal and mesh analysis with dependent sources - worked example
One concrete case, carried all the way to a stated number.
VTU BEC303 | Module 1
Nodal and mesh analysis with dependen…
31
GIVEN
Node v1 fed by 5 mA, with 1 kΩ from v1 to ground and a VCCS of 2·v1 mA drawn from v1 to ground.
1. KCL at v1: v1/1000 + 0.002·v1 = 0.005
2. Controlling variable is already v1, so no auxiliary equation is needed
3. Combine: v1·(0.001 + 0.002) = 0.005
4. v1 = 0.005 / 0.003 = 1.667 V
RESULT
v1 = 1.667 V; the dependent source behaves here like an extra 500 Ω to ground, which is what a VCCS across its own control always does.
v1/1k + 2e-3·v1 = 5 mA
v1·(1e-3 + 2e-3) = 5e-3
v1 = 1.667 V (VCCS ≡ 500 Ω here)
THE MISTAKE STUDENTS MAKE
Students set a dependent source to zero when they are told to "turn off the sources". Only independent sources are deactivated; a dependent source is part of the network's structure, and zeroing it changes the circuit into a different one.
Source: Engineering Circuit Analysis, 8th ed., Ch. 4, pp. 80-101 | CO1 | Bloom L4
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is Node v1 fed by 5 mA, with 1 kΩ from v1 to ground and a VCCS of 2·v1 mA drawn from v1 to ground. Work at the pace of the slowest note-taker and land hard on the result: v1 = 1.667 V; the dependent source behaves here like an extra 500 Ω to ground, which is what a VCCS across its own control always… Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 1: Basic Concepts — Mesh and Node Analysis. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 4, pp. 80-101. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 32
Source transformations
What it is, why it works, and what it costs.
VTU BEC303 | Module 1
Source transformations
32
THE MECHANISM
A source transformation converts a voltage source V_s in series with R into a current source V_s/R in parallel with the same R, and back again. The two are equivalent only at their external terminals: any load sees identical voltage and current from either arrangement, but the internal power dissipated in R differs, so the transformation may not be used to compute source efficiency. Its real value is procedural — each conversion can merge a source into a series or parallel group that was previously blocked, collapsing a multi-element network step by step until a single loop remains. Ideal sources cannot be transformed, because the transformation divides by or multiplies by R.
KEY TERMS
• practical source
• source transformation
• terminal equivalence
• series-parallel reduction
TAKEAWAY
Source transformation is terminal equivalence only — the outside world cannot tell the difference, but the inside of the source can.
DIAGRAM FOR PHASE 2
Two circuit fragments side by side, separated by a double-headed arrow labelled "V_s = I_s·R". Left fragment: a voltage source symbol in series with R, terminals a and b on the right edge. Right fragment: a cu…
Source: Engineering Circuit Analysis, 8th ed., Ch. 5, pp. 133-141
CO1 | Bloom L3 | visual id: source-transform-seesaw
Notes: What to say: Give them the idea before the formalism. Say it plainly first: A source transformation converts a voltage source V_s in series with R into a current source V_s/R in parallel with the same R, and back again. Then add the part they are examined on - Source transformation is terminal equivalence only — the outside world cannot tell the difference, but the inside of the sou… Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "practical source" constrain here, and what would break if it did not hold? Animation instructions: left fragment draws, right fragment draws, the double arrow animates between them, then the two identical readings light up green simultaneously, then the red warning panel slides in last. Transition style: Fade [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 1: Basic Concepts — Mesh and Node Analysis. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 5, pp. 133-141. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 33
Source transformations - how it works
The procedure in order, and what each pass costs you.
VTU BEC303 | Module 1
Source transformations
33
1. Find a voltage source in series with a resistance, or a current source in parallel with one
2. Compute the equivalent using V_s = I_s·R
3. Redraw with the converted source and the same R
4. Merge any now-adjacent series or parallel elements
5. Repeat until the network reduces to a single loop or node pair
6. Never transform an ideal source with no series or parallel resistance
COST AND BEHAVIOUR
Best: one transformation collapses a two-source network to one loop
Typical: k transformations for k source-resistor pairs, O(k) work
Worst: no benefit when every source is ideal or the topology blocks merging
WHAT THAT MEANS
Purely a preprocessing step — it never changes the answer, only the effort.
Source: Engineering Circuit Analysis, 8th ed., Ch. 5, pp. 133-141 | CO1 | Bloom L3
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Find a voltage source in series with a resistance, or a current source in parallel with one - and check everyone has written it before moving on. At the cost panel, translate it: Purely a preprocessing step — it never changes the answer, only the effort. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 1: Basic Concepts — Mesh and Node Analysis. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 5, pp. 133-141. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 34
Source transformations - worked example
One concrete case, carried all the way to a stated number.
VTU BEC303 | Module 1
Source transformations
34
GIVEN
A 12 V source in series with 4 kΩ, feeding a 2 kΩ load to ground.
1. Transform: I_s = 12/4000 = 3 mA in parallel with 4 kΩ
2. The 4 kΩ and the 2 kΩ load are now in parallel: 1.333 kΩ
3. V_load = 3 mA × 1.333 kΩ = 4 V
4. Check with a plain divider on the original: 12 × 2/(2+4) = 4 V
RESULT
V_load = 4 V by both routes; note the transformed source dissipates a different internal power than the original, though the load cannot tell.
V_s = I_s·R ⇒ 12 V + 4k ≡ 3 mA ∥ 4k
V_load = 3 mA · (4k ∥ 2k) = 3 mA · 1.333k = 4 V
THE MISTAKE STUDENTS MAKE
Students transform a source and then answer a question about the power delivered by the source. Only the terminal behaviour is preserved; the internal dissipation changes, so any internal quantity must be computed on the original circuit.
Source: Engineering Circuit Analysis, 8th ed., Ch. 5, pp. 133-141 | CO1 | Bloom L3
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is A 12 V source in series with 4 kΩ, feeding a 2 kΩ load to ground. Work at the pace of the slowest note-taker and land hard on the result: V_load = 4 V by both routes; note the transformed source dissipates a different internal power than the original, though the load… Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 1: Basic Concepts — Mesh and Node Analysis. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 5, pp. 133-141. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 35
Delta-wye conversion
What it is, why it works, and what it costs.
VTU BEC303 | Module 1
Delta-wye conversion
35
THE MECHANISM
Delta-wye conversion replaces a three-terminal resistive mesh with an electrically equivalent three-terminal star, or the reverse. It exists because some networks — the classic bridge — contain no two resistors that are purely in series or purely in parallel, so series-parallel reduction stalls completely. Converting one delta into a wye breaks the deadlock and makes the rest of the network collapse by ordinary reduction. Each wye resistance is the product of the two adjacent delta resistances divided by the sum of all three; the reverse formula divides the sum of pairwise products by the opposite wye resistance. The equivalence holds at the three terminals only, and both networks must be purely passive for it to apply.
KEY TERMS
• delta (Δ)
• wye (Y)
• bridge network
• three-terminal equivalence
TAKEAWAY
Delta-wye is the tool for exactly one situation — when series-parallel reduction has run out of moves.
DIAGRAM FOR PHASE 2
Centre: three labelled terminals a, b, c arranged as a triangle. Inside the triangle, on the left state, three resistors R_ab, R_bc, R_ca form the delta along the triangle edges. A morph arrow labelled "R_a =…
Source: Engineering Circuit Analysis, 8th ed., Ch. 5, pp. 154-157
CO1 | Bloom L3 | visual id: delta-wye-morph
Notes: What to say: Give them the idea before the formalism. Say it plainly first: Delta-wye conversion replaces a three-terminal resistive mesh with an electrically equivalent three-terminal star, or the reverse. Then add the part they are examined on - Delta-wye is the tool for exactly one situation — when series-parallel reduction has run out of moves. Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "delta (Δ)" constrain here, and what would break if it did not hold? Animation instructions: terminals appear, delta edges draw, then each delta resistor slides inward and re-forms as a wye spoke one at a time, then the Δ→Y formula box types in, then the bridge badge flips red to green last. Transition style: Fade [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 1: Basic Concepts — Mesh and Node Analysis. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 5, pp. 154-157. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 36
Delta-wye conversion - how it works
The procedure in order, and what each pass costs you.
VTU BEC303 | Module 1
Delta-wye conversion
36
1. Confirm no two elements are in simple series or parallel
2. Pick a three-terminal delta or wye sub-network
3. Apply R_a = R_ab·R_ca / (R_ab + R_bc + R_ca) for each wye branch
4. Redraw the whole network with the converted sub-network
5. Reduce the rest by ordinary series and parallel combination
6. Convert back only if the original terminal labels are needed
COST AND BEHAVIOUR
Best: one conversion unblocks a bridge entirely
Typical: three divisions per conversion, O(1)
Worst: repeated conversions on a ladder of bridges
WHAT THAT MEANS
Cheap arithmetic; the skill is recognising when it is the only move left.
Source: Engineering Circuit Analysis, 8th ed., Ch. 5, pp. 154-157 | CO1 | Bloom L3
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Confirm no two elements are in simple series or parallel - and check everyone has written it before moving on. At the cost panel, translate it: Cheap arithmetic; the skill is recognising when it is the only move left. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 1: Basic Concepts — Mesh and Node Analysis. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 5, pp. 154-157. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 37
Delta-wye conversion - worked example
One concrete case, carried all the way to a stated number.
VTU BEC303 | Module 1
Delta-wye conversion
37
GIVEN
A delta with R_ab = 30 Ω, R_bc = 60 Ω, R_ca = 30 Ω.
1. Sum = 30 + 60 + 30 = 120 Ω
2. R_a = (30 × 30)/120 = 7.5 Ω
3. R_b = (30 × 60)/120 = 15 Ω
4. R_c = (60 × 30)/120 = 15 Ω
RESULT
Wye of 7.5 Ω, 15 Ω and 15 Ω; terminal a has the smallest spoke because it sits between the two smallest delta arms.
R_a = R_ab·R_ca / (R_ab+R_bc+R_ca) = 30·30/120 = 7.5 Ω
R_b = R_ab·R_bc / Σ = 15 Ω
R_c = R_bc·R_ca / Σ = 15 Ω
THE MISTAKE STUDENTS MAKE
Students pair each wye resistance with the delta resistance directly opposite it. The Δ→Y numerator uses the two delta arms that touch that terminal, not the one facing it — getting this backwards produces a plausible-looking but wrong set of three values.
Source: Engineering Circuit Analysis, 8th ed., Ch. 5, pp. 154-157 | CO1 | Bloom L3
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is A delta with R_ab = 30 Ω, R_bc = 60 Ω, R_ca = 30 Ω. Work at the pace of the slowest note-taker and land hard on the result: Wye of 7.5 Ω, 15 Ω and 15 Ω; terminal a has the smallest spoke because it sits between the two smallest delta arms. Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 1: Basic Concepts — Mesh and Node Analysis. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 5, pp. 154-157. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 38
Characteristics of sinusoids
What it is, why it works, and what it costs.
VTU BEC303 | Module 1
Characteristics of sinusoids
38
THE MECHANISM
A sinusoid v(t) = V_m·cos(ωt + φ) is fixed by three numbers: amplitude V_m, angular frequency ω in radians per second, and phase φ. Sinusoids matter in circuit analysis for a structural reason, not an aesthetic one — they are the only waveform whose shape survives differentiation and integration, so a linear circuit driven by a sinusoid produces a sinusoid at the same frequency in every branch, with only amplitude and phase changing. Comparing two sinusoids is only meaningful when both are written in the same form, conventionally cosine with positive amplitude; a sine must be converted using sin(x) = cos(x − 90°) before any lead or lag can be read off.
KEY TERMS
• amplitude
• angular frequency
• phase angle
• lead and lag
• period
TAKEAWAY
In a linear circuit the frequency never changes — only amplitude and phase do, and that is what makes phasors possible.
DIAGRAM FOR PHASE 2
A single cosine wave drawn across the panel with three callouts: a vertical double arrow at the crest labelled V_m, a horizontal double arrow between two crests labelled T = 2π/ω, and a short horizontal offset…
Source: Engineering Circuit Analysis, 8th ed., Ch. 10, pp. 371-374
CO1 | Bloom L2 | visual id: sinusoid-three-parameters
Notes: What to say: Give them the idea before the formalism. Say it plainly first: A sinusoid v(t) = V_m·cos(ωt + φ) is fixed by three numbers: amplitude V_m, angular frequency ω in radians per second, and phase φ. Then add the part they are examined on - In a linear circuit the frequency never changes — only amplitude and phase do, and that is what makes phasors possible. Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "amplitude" constrain here, and what would break if it did not hold? Animation instructions: reference cosine draws left to right, then V_m arrow appears, then the period arrow appears, then the shifted wave draws and the φ offset arrow appears, then the conversion strip fades in. Transition style: Fade [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 1: Basic Concepts — Mesh and Node Analysis. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 10, pp. 371-374. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 39
Characteristics of sinusoids - how it works
The procedure in order, and what each pass costs you.
VTU BEC303 | Module 1
Characteristics of sinusoids
39
1. Write every sinusoid as V_m·cos(ωt + φ) with V_m positive
2. Convert sines using sin(x) = cos(x − 90°)
3. Flip a negative amplitude using −cos(x) = cos(x ± 180°)
4. Confirm both signals share the same ω before comparing
5. Subtract phases: a larger φ leads
COST AND BEHAVIOUR
Best: O(1) when both waveforms are already cosines
Typical: one or two identity substitutions
Worst: multiple conversions for mixed sine/negative forms
WHAT THAT MEANS
All arithmetic; errors here are sign errors, not algebra errors.
Source: Engineering Circuit Analysis, 8th ed., Ch. 10, pp. 371-374 | CO1 | Bloom L2
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Write every sinusoid as V_m·cos(ωt + φ) with V_m positive - and check everyone has written it before moving on. At the cost panel, translate it: All arithmetic; errors here are sign errors, not algebra errors. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 1: Basic Concepts — Mesh and Node Analysis. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 10, pp. 371-374. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 40
Characteristics of sinusoids - worked example
One concrete case, carried all the way to a stated number.
VTU BEC303 | Module 1
Characteristics of sinusoids
40
GIVEN
v1 = 5·sin(377t + 30°) and v2 = 4·cos(377t − 20°).
1. Convert v1: 5·sin(377t + 30°) = 5·cos(377t + 30° − 90°) = 5·cos(377t − 60°)
2. Both now cosine at ω = 377 rad/s
3. Phase of v1 = −60°, phase of v2 = −20°
4. Difference = −60 − (−20) = −40°
RESULT
v1 lags v2 by 40°; without the sine-to-cosine conversion the naive comparison 30° vs −20° would have wrongly said v1 leads by 50°.
sin(x) = cos(x − 90°)
5 sin(377t+30°) = 5 cos(377t−60°)
Δφ = −60° − (−20°) = −40° → v1 lags v2 by 40°
THE MISTAKE STUDENTS MAKE
Students compare a sine against a cosine directly and report the phase difference straight from the written angles. Mixed forms must be reduced to one convention first, or the answer is off by exactly 90°.
Source: Engineering Circuit Analysis, 8th ed., Ch. 10, pp. 371-374 | CO1 | Bloom L2
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is v1 = 5·sin(377t + 30°) and v2 = 4·cos(377t − 20°). Work at the pace of the slowest note-taker and land hard on the result: v1 lags v2 by 40°; without the sine-to-cosine conversion the naive comparison 30° vs −20° would have wrongly said v1 leads by 50°. Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 1: Basic Concepts — Mesh and Node Analysis. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 10, pp. 371-374. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 41
From forced response to the complex forcing function
What it is, why it works, and what it costs.
VTU BEC303 | Module 1
From forced response to the complex f…
41
THE MECHANISM
Driving an RL or RC circuit with a sinusoid and solving the differential equation directly produces the right answer but demands laborious trigonometric collection of sine and cosine terms. The complex forcing function replaces the real drive V_m·cos(ωt) with V_m·e^(j(ωt+φ)), solves the now far simpler equation, and takes the real part at the end. This is legitimate because the circuit is linear: a complex source is just a real source plus j times a second real source in quadrature, and superposition guarantees the real part of the response belongs to the real part of the drive. Every e^(jωt) factor then appears in every term and cancels, which is what leaves behind the purely algebraic phasor equation.
KEY TERMS
• forced response
• steady state
• complex forcing function
• Euler's identity
• superposition of real and imaginary
TAKEAWAY
Complex forcing is not an approximation — it solves two real problems at once and you keep the half you asked for.
DIAGRAM FOR PHASE 2
A flowchart shaped like a detour. Top-left node "Real sinusoid V_m cos(ωt+φ)" has a straight downward arrow labelled "hard: trig collection" to a bottom node "Real answer", drawn thin and dashed. A parallel ro…
Source: Engineering Circuit Analysis, 8th ed., Ch. 10, pp. 374-383
CO1 | Bloom L3 | visual id: complex-forcing-detour
Notes: What to say: Give them the idea before the formalism. Say it plainly first: Driving an RL or RC circuit with a sinusoid and solving the differential equation directly produces the right answer but demands laborious trigonometric c… Then add the part they are examined on - Complex forcing is not an approximation — it solves two real problems at once and you keep the half you asked for. Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "forced response" constrain here, and what would break if it did not hold? Animation instructions: the top node appears, the thin dashed direct route draws and greys out, then the three solid detour nodes appear left to right, then the returning Re{ } arrow draws, then the Euler box fades in. Transition style: Fade [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 1: Basic Concepts — Mesh and Node Analysis. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 10, pp. 374-383. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 42
From forced response to the complex forcing function - how it works
The procedure in order, and what each pass costs you.
VTU BEC303 | Module 1
From forced response to the complex f…
42
1. Replace the real sinusoidal source with its complex exponential form
2. Write the differential equation for the circuit
3. Assume a response of the form A·e^(jωt) and substitute
4. Cancel the common e^(jωt) factor from every term
5. Solve the remaining algebraic equation for the complex amplitude
6. Take the real part to recover the physical response
COST AND BEHAVIOUR
Best: first-order circuit — one algebraic division
Typical: one complex division per unknown
Worst: equivalent to the real method for a single element, gains grow with circuit size
WHAT THAT MEANS
The saving is in avoided trigonometry, not in asymptotic order.
Source: Engineering Circuit Analysis, 8th ed., Ch. 10, pp. 374-383 | CO1 | Bloom L3
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Replace the real sinusoidal source with its complex exponential form - and check everyone has written it before moving on. At the cost panel, translate it: The saving is in avoided trigonometry, not in asymptotic order. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 1: Basic Concepts — Mesh and Node Analysis. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 10, pp. 374-383. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 43
From forced response to the complex forcing function - worked example
One concrete case, carried all the way to a stated number.
VTU BEC303 | Module 1
From forced response to the complex f…
43
GIVEN
A series RL circuit, R = 3 Ω, L = 4 mH, driven by 10·cos(1000t) V.
1. Complex drive: 10·e^(j1000t)
2. Equation: 3·i + 0.004·di/dt = 10·e^(j1000t)
3. Assume i = I·e^(j1000t): (3 + j4)·I = 10
4. I = 10/(3 + j4) = 2∠−53.13° A
RESULT
i(t) = 2·cos(1000t − 53.13°) A; the current lags by 53.13° because the inductive term contributed the +j4.
3i + 0.004 di/dt = 10 e^{j1000t}
(3 + j4)I = 10
I = 2∠−53.13° ⇒ i(t) = 2cos(1000t − 53.13°) A
THE MISTAKE STUDENTS MAKE
Students forget to take the real part and quote a complex number as the time-domain current. The complex result is an intermediate; only Re{I·e^(jωt)} is a physical waveform.
Source: Engineering Circuit Analysis, 8th ed., Ch. 10, pp. 374-383 | CO1 | Bloom L3
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is A series RL circuit, R = 3 Ω, L = 4 mH, driven by 10·cos(1000t) V. Work at the pace of the slowest note-taker and land hard on the result: i(t) = 2·cos(1000t − 53.13°) A; the current lags by 53.13° because the inductive term contributed the +j4. Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 1: Basic Concepts — Mesh and Node Analysis. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 10, pp. 374-383. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 44
The phasor
What it is, why it works, and what it costs.
VTU BEC303 | Module 1
The phasor
44
THE MECHANISM
A phasor is the complex amplitude that survives after the common e^(jωt) factor has been cancelled: V_m·cos(ωt + φ) transforms to V = V_m∠φ. It carries amplitude and phase and deliberately discards frequency, which is safe precisely because a linear circuit cannot change frequency. Phasor addition corresponds to adding time-domain waveforms, which is why rectangular form is used for sums and differences; multiplication and division correspond to scaling and shifting, which is why polar form is used for impedance arithmetic. The transformation is exact and reversible, but it applies only to steady state — the transient part of the response is invisible in phasor form.
KEY TERMS
• phasor
• polar form
• rectangular form
• time-domain transform pair
TAKEAWAY
A phasor is a full description of a sinusoid at a known frequency, and nothing at all about how the circuit got there.
DIAGRAM FOR PHASE 2
Left: a complex plane with a single arrow of length V_m at angle φ from the real axis, labelled V = V_m∠φ, with dotted projections onto the real and imaginary axes labelled V_m cos φ and V_m sin φ. Right: the…
Source: Engineering Circuit Analysis, 8th ed., Ch. 10, pp. 383-389
CO1 | Bloom L3 | visual id: phasor-rotating-arrow
Notes: What to say: Give them the idea before the formalism. Say it plainly first: A phasor is the complex amplitude that survives after the common e^(jωt) factor has been cancelled: V_m·cos(ωt + φ) transforms to V = V_m∠φ. Then add the part they are examined on - A phasor is a full description of a sinusoid at a known frequency, and nothing at all about how the circuit got there. Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "phasor" constrain here, and what would break if it did not hold? Animation instructions: axes draw, then the arrow sweeps out from the origin to angle φ, then the two dotted projections drop, then the waveform draws right, then the tie line connects, then the conversion strip appears. Transition style: Fade [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 1: Basic Concepts — Mesh and Node Analysis. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 10, pp. 383-389. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 45
The phasor - how it works
The procedure in order, and what each pass costs you.
VTU BEC303 | Module 1
The phasor
45
1. Write the source as a cosine with positive amplitude
2. Read off V_m and φ
3. Write the phasor V = V_m∠φ
4. Use rectangular form for addition and subtraction
5. Use polar form for multiplication and division
6. Convert back by multiplying by e^(jωt) and taking the real part
COST AND BEHAVIOUR
Best: O(1) transform per source
Typical: O(1) per element, with polar/rectangular conversions as needed
Worst: repeated conversion overhead in mixed-operation problems
WHAT THAT MEANS
Choosing the wrong form is the main source of arithmetic cost.
Source: Engineering Circuit Analysis, 8th ed., Ch. 10, pp. 383-389 | CO1 | Bloom L3
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Write the source as a cosine with positive amplitude - and check everyone has written it before moving on. At the cost panel, translate it: Choosing the wrong form is the main source of arithmetic cost. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 1: Basic Concepts — Mesh and Node Analysis. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 10, pp. 383-389. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 46
The phasor - worked example
One concrete case, carried all the way to a stated number.
VTU BEC303 | Module 1
The phasor
46
GIVEN
Add v1 = 30·cos(ωt + 30°) and v2 = 40·cos(ωt − 60°).
1. V1 = 30∠30° = 25.98 + j15.00
2. V2 = 40∠−60° = 20.00 − j34.64
3. Sum = 45.98 − j19.64
4. Magnitude = 50.0, angle = −23.13°
RESULT
v1 + v2 = 50·cos(ωt − 23.13°) V; note the amplitudes 30 and 40 combine to 50 exactly because the two phasors happen to be 90° apart.
30∠30° = 25.98 + j15.00
40∠−60° = 20.00 − j34.64
Σ = 45.98 − j19.64 = 50∠−23.13°
THE MISTAKE STUDENTS MAKE
Students add phasor magnitudes and average the angles. Addition is only valid in rectangular form; 30∠30° + 40∠−60° is 50∠−23.13°, not 70 at some intermediate angle.
Source: Engineering Circuit Analysis, 8th ed., Ch. 10, pp. 383-389 | CO1 | Bloom L3
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is Add v1 = 30·cos(ωt + 30°) and v2 = 40·cos(ωt − 60°). Work at the pace of the slowest note-taker and land hard on the result: v1 + v2 = 50·cos(ωt − 23.13°) V; note the amplitudes 30 and 40 combine to 50 exactly because the two phasors happen to be 90° apa… Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 1: Basic Concepts — Mesh and Node Analysis. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 10, pp. 383-389. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 47
Impedance and admittance
What it is, why it works, and what it costs.
VTU BEC303 | Module 1
Impedance and admittance
47
THE MECHANISM
Impedance is the ratio of phasor voltage to phasor current, Z = V/I, measured in ohms and generally complex: Z = R + jX, where R is resistance and X is reactance. A resistor contributes R with no phase shift, an inductor contributes jωL which grows with frequency, and a capacitor contributes 1/(jωC) = −j/(ωC) which shrinks with frequency. Because impedance is defined as a ratio of phasors, impedances in series add and impedances in parallel combine reciprocally — exactly like resistances — which is the real payoff: every DC technique already learned transfers to AC unchanged. Admittance Y = 1/Z = G + jB is simply the more convenient form for parallel combinations.
KEY TERMS
• impedance Z
• admittance Y
• reactance
• susceptance
• frequency dependence
TAKEAWAY
Impedance makes AC analysis identical to DC analysis with complex numbers, at the price of redoing the whole calculation at each new frequency.
DIAGRAM FOR PHASE 2
Left: an impedance triangle in the complex plane with horizontal leg R, vertical leg X, hypotenuse |Z| and angle θ marked at the origin. Right: three small element panels stacked — resistor with "Z = R, flat l…
Source: Engineering Circuit Analysis, 8th ed., Ch. 10, pp. 389-394
CO1 | Bloom L3 | visual id: impedance-triangle-sweep
Notes: What to say: Give them the idea before the formalism. Say it plainly first: Impedance is the ratio of phasor voltage to phasor current, Z = V/I, measured in ohms and generally complex: Z = R + jX, where R is resistance and X is re… Then add the part they are examined on - Impedance makes AC analysis identical to DC analysis with complex numbers, at the price of redoing the whole calculation at… Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "impedance Z" constrain here, and what would break if it did not hold? Animation instructions: triangle draws R first then X then hypotenuse, θ arc appears, then the three element panels slide in from the right in order, then the frequency slider animates once from low to high with the triangle deforming in sync. Transition style: Fade [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 1: Basic Concepts — Mesh and Node Analysis. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 10, pp. 389-394. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 48
Impedance and admittance - how it works
The procedure in order, and what each pass costs you.
VTU BEC303 | Module 1
Impedance and admittance
48
1. Fix the operating frequency ω
2. Replace each R by Z = R
3. Replace each L by Z = jωL
4. Replace each C by Z = 1/(jωC)
5. Combine in series and parallel exactly as with resistances
6. Recompute everything from scratch if ω changes
COST AND BEHAVIOUR
Best: O(n) for a pure series or parallel chain
Typical: same cost as the equivalent DC problem, with complex arithmetic
Worst: full recomputation per frequency point in a sweep
WHAT THAT MEANS
A frequency sweep of k points costs k independent solutions — this is why the Laplace method in Module 4 exists.
Source: Engineering Circuit Analysis, 8th ed., Ch. 10, pp. 389-394 | CO1 | Bloom L3
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Fix the operating frequency ω - and check everyone has written it before moving on. At the cost panel, translate it: A frequency sweep of k points costs k independent solutions — this is why the Laplace method in Module 4 exists. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 1: Basic Concepts — Mesh and Node Analysis. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 10, pp. 389-394. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 49
Impedance and admittance - worked example
One concrete case, carried all the way to a stated number.
VTU BEC303 | Module 1
Impedance and admittance
49
GIVEN
R = 100 Ω in series with L = 50 mH at ω = 2000 rad/s, driven by 10∠0° V.
1. Z_L = j·2000·0.05 = j100 Ω
2. Z_total = 100 + j100 = 141.4∠45° Ω
3. I = 10∠0° / 141.4∠45° = 0.0707∠−45° A
4. V_L = I·Z_L = 0.0707∠−45° × 100∠90° = 7.07∠45° V
RESULT
I = 70.7∠−45° mA and V_L = 7.07∠45° V; the resistor and inductor voltages are each 7.07 V yet sum to 10 V, because they are 90° apart.
Z_L = jωL = j100 Ω
Z = 100 + j100 = 141.4∠45°
I = 10∠0° / 141.4∠45° = 70.7∠−45° mA
THE MISTAKE STUDENTS MAKE
Students add the magnitudes of series impedances: |100| + |100| = 200 Ω. Impedances add as complex numbers, giving 141.4 Ω here — a 41% error that then propagates into every current and power figure.
Source: Engineering Circuit Analysis, 8th ed., Ch. 10, pp. 389-394 | CO1 | Bloom L3
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is R = 100 Ω in series with L = 50 mH at ω = 2000 rad/s, driven by 10∠0° V. Work at the pace of the slowest note-taker and land hard on the result: I = 70.7∠−45° mA and V_L = 7.07∠45° V; the resistor and inductor voltages are each 7.07 V yet sum to 10 V, because they are 90° a… Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 1: Basic Concepts — Mesh and Node Analysis. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 10, pp. 389-394. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 50
Nodal and mesh analysis of AC networks
What it is, why it works, and what it costs.
VTU BEC303 | Module 1
Nodal and mesh analysis of AC networks
50
THE MECHANISM
Once every source is a phasor and every element an impedance, nodal and mesh analysis proceed without a single change of rule. KCL and KVL hold for phasors because they hold instantaneously and the transform is linear, so the same equations are assembled — only now the coefficient matrix is complex. Supernodes and supermeshes are formed for exactly the same reasons as in DC, and dependent sources are handled with the same auxiliary equations. The only genuinely new burden is arithmetic: solving a 2×2 complex system by hand is roughly four times the work of the real case, which is why systematic elimination rather than ad-hoc substitution becomes worth the discipline.
KEY TERMS
• phasor nodal analysis
• complex conductance matrix
• AC mesh analysis
• steady-state solution
TAKEAWAY
AC analysis introduces no new circuit theory at all — it introduces complex arithmetic into theory you already have.
DIAGRAM FOR PHASE 2
A split panel with a vertical seam. Left half shows a DC two-node circuit with resistor values and a real 2×2 conductance matrix beneath. Right half shows the identical topology with impedance labels Z1, Z2, Z…
Source: Engineering Circuit Analysis, 8th ed., Ch. 10, pp. 394-397
CO1 | Bloom L4 | visual id: dc-to-ac-overlay
Notes: What to say: Give them the idea before the formalism. Say it plainly first: Once every source is a phasor and every element an impedance, nodal and mesh analysis proceed without a single change of rule. Then add the part they are examined on - AC analysis introduces no new circuit theory at all — it introduces complex arithmetic into theory you already have. Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "phasor nodal analysis" constrain here, and what would break if it did not hold? Animation instructions: the left DC half fades in with its matrix, then the seam draws downward, then the right half fades in element by element mirroring the left, then the three green ticks pop in top to bottom. Transition style: Fade [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 1: Basic Concepts — Mesh and Node Analysis. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 10, pp. 394-397. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 51
Nodal and mesh analysis of AC networks - how it works
The procedure in order, and what each pass costs you.
VTU BEC303 | Module 1
Nodal and mesh analysis of AC networks
51
1. Convert all sources to phasors at the common frequency
2. Convert all elements to impedances at that frequency
3. Apply nodal or mesh analysis exactly as in DC
4. Form supernodes or supermeshes where sources demand it
5. Solve the complex simultaneous equations
6. Convert the phasor answers back to time-domain waveforms
COST AND BEHAVIOUR
Best: O(1) for a single-node phasor divider
Typical: O(n^3) complex operations, about 4× the real-arithmetic cost
Worst: O(n^3) per frequency point in a sweep
WHAT THAT MEANS
Use nodal when parallel branches dominate, mesh when series loops dominate — the rule is unchanged from DC.
Source: Engineering Circuit Analysis, 8th ed., Ch. 10, pp. 394-397 | CO1 | Bloom L4
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Convert all sources to phasors at the common frequency - and check everyone has written it before moving on. At the cost panel, translate it: Use nodal when parallel branches dominate, mesh when series loops dominate — the rule is unchanged from DC. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 1: Basic Concepts — Mesh and Node Analysis. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 10, pp. 394-397. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 52
Nodal and mesh analysis of AC networks - worked example
One concrete case, carried all the way to a stated number.
VTU BEC303 | Module 1
Nodal and mesh analysis of AC networks
52
GIVEN
Source 10∠0° V through Z1 = 5 Ω to node v, with Z2 = −j10 Ω from v to ground.
1. KCL at v: (v − 10∠0°)/5 + v/(−j10) = 0
2. Multiply through: (v − 10)·(−j10) + v·5 = 0 after clearing denominators
3. Collect: v·(1/5 + j0.1) = 2
4. v = 2 / (0.2 + j0.1) = 8.944∠−26.57° V
RESULT
v = 8.944∠−26.57° V, i.e. v(t) = 8.944·cos(ωt − 26.57°); the capacitive branch pulls the node phase negative.
(v − 10)/5 + v/(−j10) = 0
v(0.2 + j0.1) = 2
v = 8.944∠−26.57° V
THE MISTAKE STUDENTS MAKE
Students mix a source given in volts RMS with element values solved in peak amplitude and never state which convention they used. Fix one convention at the start of the problem; a silent switch scales every power result by a factor of two.
Source: Engineering Circuit Analysis, 8th ed., Ch. 10, pp. 394-397 | CO1 | Bloom L4
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is Source 10∠0° V through Z1 = 5 Ω to node v, with Z2 = −j10 Ω from v to ground. Work at the pace of the slowest note-taker and land hard on the result: v = 8.944∠−26.57° V, i.e. v(t) = 8.944·cos(ωt − 26.57°); the capacitive branch pulls the node phase negative. Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 1: Basic Concepts — Mesh and Node Analysis. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 10, pp. 394-397. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 53
One sentence per unit, six months from now
Units 1-7: what survives after the detail has gone.
VTU BEC303 | Module 1
Revision
53
01 A circuit diagram is a claim that the hardware behaves like the model; every analysis result inherits that claim.
02 Independent sources set the excitation; dependent sources set the gain, and both must appear before any conservation equation can be written.
03 KCL is a statement about a boundary, not about a dot on the page — draw the boundary wherever it makes the algebra smallest.
04 KVL works because potential is single-valued; the loop you choose is free, but choosing meshes guarantees independence.
05 Nodal analysis trades a large number of branch currents for a small number of node voltages, and the count of equations is fixed before you look at a single element.
06 A floating voltage source removes a KCL equation and hands back a constraint equation; the equation count never changes.
07 Mesh currents are fictitious circulating variables; only their differences across shared branches are physically real.
Notes: What to say: Slow right down here. Read each takeaway aloud and then stop talking for a beat, because these are the sentences that should still be in their heads when they sit the SEE. Tell them explicitly that if they can reconstruct the reasoning behind any one of these lines they understand that unit, and if they can only recite it they do not. Pause cue: Pause for three seconds after each takeaway before moving to the next. Pointing cue: Point at each numbered takeaway in turn as you read it. Question to ask students: Ask: choose the takeaway you trust least and tell me what you would have to check to believe it. Animation instructions: Takeaway rows reveal one at a time from the top, each row highlighting briefly as it appears. Transition style: Fade [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 1: Basic Concepts — Mesh and Node Analysis, 15 hours, Hayt 8e Ch. 1 (1.1), Ch. 2 (2.3), Ch. 3 (3.2–3.3), Ch. 4 (4.1–4.4), Ch. 5 (5.2, 5.5), Ch. 10 (10.1–10.6), pp. 2–397. TB1: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012. Revision consolidates all 16 unit takeaways. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 54
Revision, continued
Units 8-14: what survives after the detail has gone.
VTU BEC303 | Module 1
Revision
54
08 You cannot write KVL across a current source, so route the loop around it and recover the lost equation from the source value.
09 Dependent sources cost one auxiliary equation each and destroy matrix symmetry, but never change how many unknowns you started with.
10 Source transformation is terminal equivalence only — the outside world cannot tell the difference, but the inside of the source can.
11 Delta-wye is the tool for exactly one situation — when series-parallel reduction has run out of moves.
12 In a linear circuit the frequency never changes — only amplitude and phase do, and that is what makes phasors possible.
13 Complex forcing is not an approximation — it solves two real problems at once and you keep the half you asked for.
14 A phasor is a full description of a sinusoid at a known frequency, and nothing at all about how the circuit got there.
Notes: What to say: Slow right down here. Read each takeaway aloud and then stop talking for a beat, because these are the sentences that should still be in their heads when they sit the SEE. Tell them explicitly that if they can reconstruct the reasoning behind any one of these lines they understand that unit, and if they can only recite it they do not. Pause cue: Pause for three seconds after each takeaway before moving to the next. Pointing cue: Point at each numbered takeaway in turn as you read it. Question to ask students: Ask: choose the takeaway you trust least and tell me what you would have to check to believe it. Animation instructions: Takeaway rows reveal one at a time from the top, each row highlighting briefly as it appears. Transition style: Fade [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 1: Basic Concepts — Mesh and Node Analysis, 15 hours, Hayt 8e Ch. 1 (1.1), Ch. 2 (2.3), Ch. 3 (3.2–3.3), Ch. 4 (4.1–4.4), Ch. 5 (5.2, 5.5), Ch. 10 (10.1–10.6), pp. 2–397. TB1: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012. Revision consolidates all 16 unit takeaways. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 55
Revision, continued
Units 15-16: what survives after the detail has gone.
VTU BEC303 | Module 1
Revision
55
15 Impedance makes AC analysis identical to DC analysis with complex numbers, at the price of redoing the whole calculation at each new frequency.
16 AC analysis introduces no new circuit theory at all — it introduces complex arithmetic into theory you already have.
Notes: What to say: Slow right down here. Read each takeaway aloud and then stop talking for a beat, because these are the sentences that should still be in their heads when they sit the SEE. Tell them explicitly that if they can reconstruct the reasoning behind any one of these lines they understand that unit, and if they can only recite it they do not. Pause cue: Pause for three seconds after each takeaway before moving to the next. Pointing cue: Point at each numbered takeaway in turn as you read it. Question to ask students: Ask: choose the takeaway you trust least and tell me what you would have to check to believe it. Animation instructions: Takeaway rows reveal one at a time from the top, each row highlighting briefly as it appears. Transition style: Fade [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 1: Basic Concepts — Mesh and Node Analysis, 15 hours, Hayt 8e Ch. 1 (1.1), Ch. 2 (2.3), Ch. 3 (3.2–3.3), Ch. 4 (4.1–4.4), Ch. 5 (5.2, 5.5), Ch. 10 (10.1–10.6), pp. 2–397. TB1: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012. Revision consolidates all 16 unit takeaways. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 56
How this module is assessed
Where the quiz and the assignment live, and what they test.
VTU BEC303 | Module 1
Assessment
56
MODULE 1 QUIZ
quizzes/Module_1_Quiz.pdf
quizzes/Module_1_Quiz.gift
45 minutes | 50 marks | pass 20 | 1 attempt
Part A: 20 MCQs, 1 mark each.
Part B: 13 descriptive questions, 30 marks.
Bloom spread: L1-L2 52%, L3-L4 48%, L5-L6 0%
Every question carries a CO tag, a Bloom level and a chapter reference; distractor feedback names the misconception.
MODULE 1 ASSIGNMENT
assignments/Module_1_Assignment.pdf
Assignment 1 — Systematic analysis of DC and AC networks
20 marks | 10% of CIE | 10 problems + 3 theory items
Submit as PDF, single file, named <USN>_BEC303_Assignment1.pdf, via LMS upload. 10% per day, nothing after 5 days.
Rubric: Correctness of equations and solution (8); Method selection and justification (5); Handling of special cases (supernode, supermesh, dependent sources) (4); Presentation, units and phasor conventions (3). Attainment: CO1 = 20.
Previous years' question papers for EC are indexed in pyq/PYQ_Index.pdf; the syllabus extract and the topic-to-slide mapping are in syllabus/Syllabus_Mapping.pdf.
Individual submission. Identical submissions score zero for both parties.
Notes: What to say: Close by telling them exactly where the assessment lives and what it tests. Name the two files, say the mark split out loud, and read the Bloom spread so they understand that roughly a quarter of the paper is not recall at all. Then read the integrity line word for word, because ambiguity there costs students more than any technical error in this module. Pause cue: Pause after the Bloom spread and before the integrity statement. Pointing cue: Point at the quiz panel, then the assignment panel, then the integrity line at the bottom. Question to ask students: Ask: which course outcome do you feel least ready on, and which unit would you reread tonight to fix it? Animation instructions: Quiz panel fades in from the left, then the assignment panel from the right, then the pointers strip appears, then the integrity line fades in last. Transition style: Fade [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 1: Basic Concepts — Mesh and Node Analysis, 15 hours, Hayt 8e Ch. 1 (1.1), Ch. 2 (2.3), Ch. 3 (3.2–3.3), Ch. 4 (4.1–4.4), Ch. 5 (5.2, 5.5), Ch. 10 (10.1–10.6), pp. 2–397. TB1: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012. Assessment counts: 20 MCQs, 13 descriptive questions, 13 assignment items. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.