## Slide 1
Network Analysis
Module 2 asks: When I do not need every branch current, which theorem gets me the one answer I want with the least work —…
VTU BEC303 | Module 2
Opening
01
MODULE 2
Network Theorems for DC and AC Circuits
13 contact hours | 16 teaching units | 56 slides
PRESCRIBED TEXTBOOK
Engineering Circuit Analysis
W. H. Hayt, J. E. Kemmerly and S. M. Durbin
McGraw-Hill / Tata McGraw-Hill, 8th edition, 2012
Hayt 8e Ch. 5 (5.1, 5.3, 5.4), Ch. 10 (10.7), pp. 123–154 and 397–406; reciprocity from syllabus TB2 (Channa Venkatesh & Ganesh Rao) §4.9
Mesh & Nodal Analysis • Network Theorems • Transient Response • Laplace / s-Domain • Two-Port Networks
Linearity licenses every theorem → Split the problem by source → Ports behave symmetrically → Collapse a network to two numbers → Match the load, pay the efficiency
EC · Semester 3 · BEC303 · generated for Phase 2 conversion
Notes: What to say: Open by putting the whole module on one page. Tell them this is 13 contact hours and 16 teaching units, and that all of it exists to answer one question: When I do not need every branch current, which theorem gets me the one answer I want with the least work — and when does the shortcut stop being valid? Name the prescribed textbook out loud and say which chapters they will be living in, so nobody is reading the wrong book by week two. Pause cue: Pause after reading the driving question aloud, before naming the textbook. Pointing cue: Point at the module title block, then at the textbook panel, then run a finger along the five-beat arc. Question to ask students: Ask: before we start, what do you already expect the answer to "When I do not need every branch current, which theorem gets me the one answer I want with…" to look like? Animation instructions: Module title block fades in first, then the textbook panel slides in from the right, then the five arc beats appear left to right one at a time. Transition style: Fade [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 2: Network Theorems for DC and AC Circuits, 13 hours, Hayt 8e Ch. 5 (5.1, 5.3, 5.4), Ch. 10 (10.7), pp. 123–154 and 397–406; reciprocity from syllabus TB2 (Channa Venkatesh & Ganesh Rao) §4.9. TB1: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 2
What this module is actually for
One question, five beats, and the scope it does not cover.
VTU BEC303 | Module 2
Overview
02
THE DRIVING QUESTION
When I do not need every branch current, which theorem gets me the one answer I want with the least work — and when does the shortcut stop being valid?
1
Linearity licenses every theorem
2
Split the problem by source
3
Ports behave symmetrically
4
Collapse a network to two numbers
5
Match the load, pay the efficiency
SCOPE AND PROVENANCE
Built from the syllabus-listed Hayt 8e sections plus the syllabus-listed TB2 section for reciprocity. Emphasis throughout is on the validity boundary of each theorem rather than its mechanics: superposition is exact for voltage and current and wrong for power; Thévenin requires linearity inside the port but nothing of the load; reciprocity fails the moment a dependent source appears. The maximum power transfer case study is developed as an engineering trade-off — maximum power is not maximum efficiency.
Course outcomes exercised: CO2
Assessment: 20 MCQs + 13 descriptive questions + 13 assignment items
Notes: What to say: Give them the map before the territory. Read the driving question once more, then walk the five beats across the slide and say in one sentence what changes between each beat and the next. Finish on the scope paragraph, because knowing what a module does not cover saves more marks than anything else on this slide. Pause cue: Pause for four or five seconds after the five beats appear, before moving to scope. Pointing cue: Point at the driving question panel, then at each numbered beat in turn, then at the scope paragraph. Question to ask students: Ask: which of these five beats do you expect to find hardest, and why that one? Animation instructions: The driving question panel fades in, then the five numbered beats appear left to right one at a time, then the scope paragraph fades in beneath them. Transition style: Fade [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 2: Network Theorems for DC and AC Circuits, 13 hours, Hayt 8e Ch. 5 (5.1, 5.3, 5.4), Ch. 10 (10.7), pp. 123–154 and 397–406; reciprocity from syllabus TB2 (Channa Venkatesh & Ganesh Rao) §4.9. TB1: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 3
Every unit against its chapter and pages
Units 1-9 of 16, with the deck slides that teach each one.
VTU BEC303 | Module 2
Syllabus mapping
03
# — Teaching unit — Book chapter and pages — Deck slides — CO / Bloom
01 Linearity: the property every theorem rests on — Ch. 5, pp. 123-133 — slides 5, 6, 7 — CO2 / L2
02 The superposition theorem — Ch. 5, pp. 123-133 — slides 8, 9, 10 — CO2 / L3
03 Deactivating sources correctly — Ch. 5, pp. 123-133 — slides 11, 12, 13 — CO2 / L2
04 Superposition with sources at different frequencies — Ch. 5, pp. 123-133 — slides 14, 15, 16 — CO2 / L4
05 Why superposition fails for power — Ch. 5, pp. 123-133 — slides 17, 18, 19 — CO2 / L4
06 The reciprocity theorem — TB2 §4.9 — slides 20, 21, 22 — CO2 / L2
07 Conditions for reciprocity — TB2 §4.9 — slides 23, 24, 25 — CO2 / L3
08 Reciprocal and non-reciprocal circuits — TB2 §4.9 — slides 26, 27, 28 — CO2 / L4
09 Thévenin's theorem — Ch. 5, pp. 141-152 — slides 29, 30, 31 — CO2 / L3
Notes: What to say: Tell them this is the slide to photograph. Every unit in the module is listed against a real chapter and a real page range, so there is no ambiguity about what to read. Point out the slide-number column and say plainly that if they miss a lecture, those are the slides covering that unit. Say that the page ranges come from the book's own table of contents rather than a guess. Pause cue: Pause for ten seconds and let them photograph the table before saying anything else. Pointing cue: Run a finger down the chapter-and-pages column, then across one complete row. Question to ask students: Ask: pick any row - which chapter would you open first, and what would you expect in the first paragraph? Animation instructions: Header row appears first, then the unit rows fade in one at a time from the top, then the chapter-and-pages column highlights. Transition style: Cut [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 2: Network Theorems for DC and AC Circuits, 13 hours, Hayt 8e Ch. 5 (5.1, 5.3, 5.4), Ch. 10 (10.7), pp. 123–154 and 397–406; reciprocity from syllabus TB2 (Channa Venkatesh & Ganesh Rao) §4.9. TB1: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012. Mapping covers all 16 teaching units. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 4
Syllabus mapping, continued
Units 10-16 of 16, with the deck slides that teach each one.
VTU BEC303 | Module 2
Syllabus mapping
04
# — Teaching unit — Book chapter and pages — Deck slides — CO / Bloom
10 Finding R_th: three methods and when each applies — Ch. 5, pp. 141-152 — slides 32, 33, 34 — CO2 / L4
11 Norton's theorem and Thévenin–Norton duality — Ch. 5, pp. 141-152 — slides 35, 36, 37 — CO2 / L3
12 The maximum power transfer theorem — Ch. 5, pp. 152-154 — slides 38, 39, 40 — CO2 / L4
13 Case study: maximum power transfer in electronic systems design — Ch. 5, pp. 152-154 — slides 41, 42, 43 — CO2 / L5
14 Network theorems in the phasor domain — Ch. 10, pp. 397-406 — slides 44, 45, 46 — CO2 / L4
15 Choosing between theorems: a decision procedure — Ch. 5, pp. 123-154 — slides 47, 48, 49 — CO2 / L5
16 Verifying a theorem result — Ch. 5, pp. 141-152 — slides 50, 51, 52 — CO2 / L5
Notes: What to say: Tell them this is the slide to photograph. Every unit in the module is listed against a real chapter and a real page range, so there is no ambiguity about what to read. Point out the slide-number column and say plainly that if they miss a lecture, those are the slides covering that unit. Say that the page ranges come from the book's own table of contents rather than a guess. Pause cue: Pause for ten seconds and let them photograph the table before saying anything else. Pointing cue: Run a finger down the chapter-and-pages column, then across one complete row. Question to ask students: Ask: pick any row - which chapter would you open first, and what would you expect in the first paragraph? Animation instructions: Header row appears first, then the unit rows fade in one at a time from the top, then the chapter-and-pages column highlights. Transition style: Cut [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 2: Network Theorems for DC and AC Circuits, 13 hours, Hayt 8e Ch. 5 (5.1, 5.3, 5.4), Ch. 10 (10.7), pp. 123–154 and 397–406; reciprocity from syllabus TB2 (Channa Venkatesh & Ganesh Rao) §4.9. TB1: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012. Mapping covers all 16 teaching units. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 5
Linearity: the property every theorem rests on
What it is, why it works, and what it costs.
VTU BEC303 | Module 2
Linearity: the property every theorem…
05
THE MECHANISM
A circuit is linear when its response obeys two properties together: homogeneity, meaning scaling every source by k scales every response by k, and additivity, meaning the response to a sum of sources is the sum of the individual responses. Resistors, inductors, capacitors and all four dependent source types are linear elements; diodes, transistors outside their small-signal region and any element with a square or product law are not. Every theorem in this module is a corollary of these two properties, which is why none of them may be applied to a circuit containing a genuinely nonlinear element. Power is the standard counterexample: p = i²R is quadratic in the response, so power never inherits linearity even in a fully linear circuit.
KEY TERMS
• homogeneity
• additivity
• linear element
• linear circuit
TAKEAWAY
Linearity is not a convenience assumption — it is the single hypothesis that makes superposition, Thévenin and reciprocity true at all.
DIAGRAM FOR PHASE 2
Two stone-pillar shapes side by side supporting a horizontal lintel. Left pillar is labelled "Homogeneity: k·source → k·response" with a small graph beneath showing a straight line through the origin. Right pi…
Source: Engineering Circuit Analysis, 8th ed., Ch. 5, pp. 123-133
CO2 | Bloom L2 | visual id: linearity-two-pillars
Notes: What to say: Give them the idea before the formalism. Say it plainly first: A circuit is linear when its response obeys two properties together: homogeneity, meaning scaling every source by k scales every response by k, and additi… Then add the part they are examined on - Linearity is not a convenience assumption — it is the single hypothesis that makes superposition, Thévenin and reciprocity t… Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "homogeneity" constrain here, and what would break if it did not hold? Animation instructions: left pillar rises, right pillar rises, then the lintel slides across on top, then the theorem names appear one by one along it, then the cracked power block drops in last with the red X. Transition style: Fade [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 2: Network Theorems for DC and AC Circuits. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 5, pp. 123-133. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 6
Linearity: the property every theorem rests on - how it works
The procedure in order, and what each pass costs you.
VTU BEC303 | Module 2
Linearity: the property every theorem…
06
1. Check every element against the linear list before invoking any theorem
2. Test homogeneity: does doubling all sources double the answer?
3. Test additivity: does the answer decompose across sources?
4. Classify dependent sources as linear — they are
5. Refuse to apply any theorem if a diode or saturating device is inside the region of interest
6. Remember that a linear circuit still has nonlinear power
COST AND BEHAVIOUR
Best: O(1) — inspection of the element list
Typical: O(n) over n elements
Worst: O(n) plus a judgement call on small-signal validity
WHAT THAT MEANS
The check is cheap; skipping it is what makes later work worthless.
Source: Engineering Circuit Analysis, 8th ed., Ch. 5, pp. 123-133 | CO2 | Bloom L2
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Check every element against the linear list before invoking any theorem - and check everyone has written it before moving on. At the cost panel, translate it: The check is cheap; skipping it is what makes later work worthless. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 2: Network Theorems for DC and AC Circuits. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 5, pp. 123-133. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 7
Linearity: the property every theorem rests on - worked example
One concrete case, carried all the way to a stated number.
VTU BEC303 | Module 2
Linearity: the property every theorem…
07
GIVEN
A resistive divider gives 4 V at the output from a 12 V source. The source is raised to 30 V.
1. Circuit is purely resistive, therefore linear
2. Homogeneity: scale factor k = 30/12 = 2.5
3. New output = 2.5 × 4 = 10 V
4. Power in the load, however, scales by k² = 6.25, not 2.5
RESULT
Output rises to 10 V but load power rises 6.25-fold — the clearest demonstration that voltage is linear and power is not.
v_out(k·V_s) = k·v_out(V_s) (linear)
p_out(k·V_s) = k²·p_out(V_s) (NOT linear)
k = 2.5 ⇒ v: 4→10 V, p: ×6.25
THE MISTAKE STUDENTS MAKE
Students assume that because a circuit is called linear, everything computed from it is linear. Voltage and current are; power, energy and RMS values are quadratic and must always be computed from the final total response.
Source: Engineering Circuit Analysis, 8th ed., Ch. 5, pp. 123-133 | CO2 | Bloom L2
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is A resistive divider gives 4 V at the output from a 12 V source. The source is raised to 30 V. Work at the pace of the slowest note-taker and land hard on the result: Output rises to 10 V but load power rises 6.25-fold — the clearest demonstration that voltage is linear and power is not. Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 2: Network Theorems for DC and AC Circuits. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 5, pp. 123-133. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 8
The superposition theorem
What it is, why it works, and what it costs.
VTU BEC303 | Module 2
The superposition theorem
08
THE MECHANISM
Superposition states that in a linear circuit the current or voltage at any point is the algebraic sum of the responses produced by each independent source acting alone, with all other independent sources deactivated. Its value is not speed — for a two-source circuit it is usually slower than nodal analysis — but insight: it isolates which source is responsible for how much of an output, which is exactly what is needed when diagnosing an unwanted offset or identifying the dominant noise contributor. It also lets a circuit with sources at different frequencies be solved at all, since each frequency must be handled in its own phasor domain and only the time-domain results can be added.
KEY TERMS
• superposition
• partial response
• one source at a time
• algebraic sum
TAKEAWAY
Superposition is a diagnostic tool first and a solving method second — use it when you need to know which source caused what.
DIAGRAM FOR PHASE 2
A single circuit at the top containing two independent sources, V_s and I_s, and a load marked with output v_o. Two arrows fan downward to two copies of the circuit: the left copy keeps V_s live and shows I_s…
Source: Engineering Circuit Analysis, 8th ed., Ch. 5, pp. 123-133
CO2 | Bloom L3 | visual id: superposition-split-merge
Notes: What to say: Give them the idea before the formalism. Say it plainly first: Superposition states that in a linear circuit the current or voltage at any point is the algebraic sum of the responses produced by each independent sourc… Then add the part they are examined on - Superposition is a diagnostic tool first and a solving method second — use it when you need to know which source caused what. Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "superposition" constrain here, and what would break if it did not hold? Animation instructions: the top circuit fades in, the two fan-out arrows draw simultaneously, the left copy appears with the source deactivation animating, then the right copy the same way, then both converge arrows draw into the summation box which highlights green. Transition style: Fade [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 2: Network Theorems for DC and AC Circuits. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 5, pp. 123-133. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 9
The superposition theorem - how it works
The procedure in order, and what each pass costs you.
VTU BEC303 | Module 2
The superposition theorem
09
1. Confirm the circuit is linear
2. Select one independent source and deactivate all the others
3. Replace deactivated voltage sources by shorts and current sources by opens
4. Leave every dependent source active
5. Solve for the partial response, keeping its sign
6. Repeat for every independent source and add the partial responses algebraically
COST AND BEHAVIOUR
Best: two sources, one trivial sub-circuit each
Typical: k sub-circuit solutions for k independent sources
Worst: k full network solutions, i.e. k times the cost of a single nodal analysis
WHAT THAT MEANS
Always slower than direct analysis; the payoff is attribution, not speed.
Source: Engineering Circuit Analysis, 8th ed., Ch. 5, pp. 123-133 | CO2 | Bloom L3
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Confirm the circuit is linear - and check everyone has written it before moving on. At the cost panel, translate it: Always slower than direct analysis; the payoff is attribution, not speed. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 2: Network Theorems for DC and AC Circuits. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 5, pp. 123-133. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 10
The superposition theorem - worked example
One concrete case, carried all the way to a stated number.
VTU BEC303 | Module 2
The superposition theorem
10
GIVEN
A 10 V source in series with 2 kΩ and a 3 mA source both feeding a common 6 kΩ load to ground.
1. Source 1 alone: open the 3 mA source; v′ = 10 × 6/(2+6) = 7.5 V
2. Source 2 alone: short the 10 V source; the 2 kΩ and 6 kΩ are now in parallel = 1.5 kΩ
3. v″ = 3 mA × 1.5 kΩ = 4.5 V
4. Total: v = 7.5 + 4.5 = 12 V
RESULT
v = 12 V, of which the voltage source contributes 7.5 V and the current source 4.5 V — an attribution that a single nodal solve would not reveal.
v' = 10·6k/(2k+6k) = 7.5 V
v'' = 3 mA·(2k ∥ 6k) = 3 mA·1.5k = 4.5 V
v = 7.5 + 4.5 = 12 V
THE MISTAKE STUDENTS MAKE
Students add the partial responses as magnitudes and lose the sign. A partial response that opposes the others must be subtracted; superposition is an algebraic sum, and a source that fights the output is precisely the case the method exists to expose.
Source: Engineering Circuit Analysis, 8th ed., Ch. 5, pp. 123-133 | CO2 | Bloom L3
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is A 10 V source in series with 2 kΩ and a 3 mA source both feeding a common 6 kΩ load to ground. Work at the pace of the slowest note-taker and land hard on the result: v = 12 V, of which the voltage source contributes 7.5 V and the current source 4.5 V — an attribution that a single nodal solve w… Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 2: Network Theorems for DC and AC Circuits. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 5, pp. 123-133. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 11
Deactivating sources correctly
What it is, why it works, and what it costs.
VTU BEC303 | Module 2
Deactivating sources correctly
11
THE MECHANISM
Deactivating an independent voltage source means setting its terminal voltage to zero, which is a short circuit; deactivating an independent current source means setting its current to zero, which is an open circuit. The resistance associated with a practical source is not part of the source and always stays in the circuit — a 10 V source with 2 Ω internal resistance deactivates to a plain 2 Ω, not to nothing. Dependent sources are never deactivated because their value is determined by the circuit rather than imposed on it; removing one changes the network topology and produces the wrong answer for every subsequent step.
KEY TERMS
• zeroing a source
• short circuit
• open circuit
• practical vs ideal source
TAKEAWAY
Zeroing a source removes its excitation, never its resistance, and never applies to a dependent source.
DIAGRAM FOR PHASE 2
A three-row lookup table drawn as cards. Row 1: "Independent voltage source" with a before-symbol (circle, +/−) and an after-symbol (plain wire), joined by an arrow labelled "V = 0 ⇒ short". Row 2: "Independen…
Source: Engineering Circuit Analysis, 8th ed., Ch. 5, pp. 123-133
CO2 | Bloom L2 | visual id: deactivation-lookup
Notes: What to say: Give them the idea before the formalism. Say it plainly first: Deactivating an independent voltage source means setting its terminal voltage to zero, which is a short circuit; deactivating an independent current sourc… Then add the part they are examined on - Zeroing a source removes its excitation, never its resistance, and never applies to a dependent source. Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "zeroing a source" constrain here, and what would break if it did not hold? Animation instructions: rows appear top to bottom, each with the symbol morphing from before to after; then the green tick lands on row 3; then the amber side panel slides in last. Transition style: Fade [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 2: Network Theorems for DC and AC Circuits. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 5, pp. 123-133. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 12
Deactivating sources correctly - how it works
The procedure in order, and what each pass costs you.
VTU BEC303 | Module 2
Deactivating sources correctly
12
1. List every source and label it independent or dependent
2. Replace each deactivated independent voltage source with a wire
3. Replace each deactivated independent current source with a gap
4. Keep every series or parallel resistance associated with a practical source
5. Leave all dependent sources exactly as drawn
6. Redraw the simplified network before solving
COST AND BEHAVIOUR
Best: O(1) per source
Typical: O(k) for k sources per sub-circuit
Worst: O(k) plus a redraw that may change the series-parallel structure entirely
WHAT THAT MEANS
The redraw is where most arithmetic errors enter — do it explicitly.
Source: Engineering Circuit Analysis, 8th ed., Ch. 5, pp. 123-133 | CO2 | Bloom L2
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - List every source and label it independent or dependent - and check everyone has written it before moving on. At the cost panel, translate it: The redraw is where most arithmetic errors enter — do it explicitly. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 2: Network Theorems for DC and AC Circuits. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 5, pp. 123-133. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 13
Deactivating sources correctly - worked example
One concrete case, carried all the way to a stated number.
VTU BEC303 | Module 2
Deactivating sources correctly
13
GIVEN
A practical source of 10 V with 2 Ω internal resistance, in a circuit with a second 5 A ideal source, is to be deactivated for a superposition step.
1. The 10 V ideal part becomes a short circuit
2. The 2 Ω internal resistance remains in place
3. The branch is now simply a 2 Ω path
4. The 5 A source stays live for this step
RESULT
The branch reduces to 2 Ω, not to an open or a plain wire — deleting the 2 Ω would change the parallel combination and every downstream current.
10 V ⊕ 2 Ω --deactivate--> 2 Ω
(not a wire, not an open)
THE MISTAKE STUDENTS MAKE
Students remove the entire practical source branch, resistance included. The internal resistance belongs to the network, not to the excitation, and dropping it typically changes the equivalent resistance by tens of percent.
Source: Engineering Circuit Analysis, 8th ed., Ch. 5, pp. 123-133 | CO2 | Bloom L2
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is A practical source of 10 V with 2 Ω internal resistance, in a circuit with a second 5 A ideal source, is to be deactivated for a superposit… Work at the pace of the slowest note-taker and land hard on the result: The branch reduces to 2 Ω, not to an open or a plain wire — deleting the 2 Ω would change the parallel combination and every down… Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 2: Network Theorems for DC and AC Circuits. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 5, pp. 123-133. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 14
Superposition with sources at different frequencies
What it is, why it works, and what it costs.
VTU BEC303 | Module 2
Superposition with sources at differe…
14
THE MECHANISM
When a circuit is driven by sources at different frequencies, no single phasor domain can hold them, because impedance itself is a function of ω. Superposition is then not merely convenient but mandatory: each source is solved in its own phasor domain with impedances evaluated at that source's frequency, the partial answers are converted back to the time domain, and only then are they added. A DC source is handled as the ω = 0 case, where an inductor becomes a short and a capacitor an open. Adding the phasors directly is meaningless, since two phasors at different frequencies have no fixed relative phase.
KEY TERMS
• multi-frequency excitation
• per-frequency phasor domain
• time-domain recombination
• DC plus AC
TAKEAWAY
Different frequencies may only be combined in the time domain — phasors from different ω values are not addable at all.
DIAGRAM FOR PHASE 2
Three horizontal lanes stacked. Lane 1 labelled "ω = 0 (DC)" shows L as a wire and C as a gap, ending in a box "v₀(t) = const". Lane 2 labelled "ω = 377" shows impedance values jωL and 1/jωC computed at 377, e…
Source: Engineering Circuit Analysis, 8th ed., Ch. 5, pp. 123-133
CO2 | Bloom L4 | visual id: multi-frequency-lanes
Notes: What to say: Give them the idea before the formalism. Say it plainly first: When a circuit is driven by sources at different frequencies, no single phasor domain can hold them, because impedance itself is a function of ω. Then add the part they are examined on - Different frequencies may only be combined in the time domain — phasors from different ω values are not addable at all. Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "multi-frequency excitation" constrain here, and what would break if it did not hold? Animation instructions: lanes appear top to bottom, each computing left to right, then the three arrows converge into the sum node, then the red crossed shortcut appears last. Transition style: Fade [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 2: Network Theorems for DC and AC Circuits. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 5, pp. 123-133. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 15
Superposition with sources at different frequencies - how it works
The procedure in order, and what each pass costs you.
VTU BEC303 | Module 2
Superposition with sources at differe…
15
1. Group the sources by frequency
2. For each distinct frequency, deactivate all sources of other frequencies
3. Evaluate every impedance at that frequency
4. Solve the phasor circuit and convert the answer to the time domain
5. Handle DC as ω = 0 with L shorted and C opened
6. Add all time-domain partial responses
COST AND BEHAVIOUR
Best: two frequencies, two simple solves
Typical: one full solve per distinct frequency
Worst: m solves for m frequencies, each O(n^3)
WHAT THAT MEANS
Cost grows with the number of distinct frequencies, not the number of sources.
Source: Engineering Circuit Analysis, 8th ed., Ch. 5, pp. 123-133 | CO2 | Bloom L4
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Group the sources by frequency - and check everyone has written it before moving on. At the cost panel, translate it: Cost grows with the number of distinct frequencies, not the number of sources. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 2: Network Theorems for DC and AC Circuits. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 5, pp. 123-133. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 16
Superposition with sources at different frequencies - worked example
One concrete case, carried all the way to a stated number.
VTU BEC303 | Module 2
Superposition with sources at differe…
16
GIVEN
A series R = 1 kΩ, C = 1 µF branch driven by 5 V DC plus 10·cos(1000t) V.
1. DC step: capacitor is open, so no DC current flows and the full 5 V appears across C
2. AC step: Z_C = 1/(j·1000·1e−6) = −j1000 Ω, Z_total = 1000 − j1000 = 1414∠−45° Ω
3. I = 10∠0°/1414∠−45° = 7.07∠45° mA, V_C = I × 1000∠−90° = 7.07∠−45° V
4. Add in the time domain: v_C(t) = 5 + 7.07·cos(1000t − 45°) V
RESULT
v_C(t) = 5 + 7.07·cos(1000t − 45°) V — a DC level with an AC ripple riding on it, which no single phasor could have represented.
DC (ω=0): C open ⇒ V_C,dc = 5 V
AC (ω=1000): Z_C = −j1000, V_C,ac = 7.07∠−45° V
v_C(t) = 5 + 7.07 cos(1000t − 45°) V
THE MISTAKE STUDENTS MAKE
Students add a DC value to a phasor magnitude and quote a single number. A DC level and a sinusoid are different functions of time; the only correct combination is a time-domain sum, which is why the answer has two terms and not one.
Source: Engineering Circuit Analysis, 8th ed., Ch. 5, pp. 123-133 | CO2 | Bloom L4
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is A series R = 1 kΩ, C = 1 µF branch driven by 5 V DC plus 10·cos(1000t) V. Work at the pace of the slowest note-taker and land hard on the result: v_C(t) = 5 + 7.07·cos(1000t − 45°) V — a DC level with an AC ripple riding on it, which no single phasor could have represented. Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 2: Network Theorems for DC and AC Circuits. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 5, pp. 123-133. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 17
Why superposition fails for power
What it is, why it works, and what it costs.
VTU BEC303 | Module 2
Why superposition fails for power
17
THE MECHANISM
Power is a quadratic function of the response, p = i²R, so expanding the square of a sum produces a cross term: (i₁ + i₂)²R = i₁²R + i₂²R + 2i₁i₂R. The first two terms are what superposition of powers would predict; the third is the interaction term that superposition of powers silently discards. The error is not small — if the two partial currents are equal, the true power is four times one partial power while the naive sum gives two, a 100 % error. The correct procedure is always to superpose currents or voltages first, obtain the total response, and only then compute power from that total.
KEY TERMS
• quadratic response
• cross term
• power superposition fallacy
• total response first
TAKEAWAY
Superpose the response, then square; never square, then superpose.
DIAGRAM FOR PHASE 2
Centre: a large algebraic expansion typeset in three coloured chunks — (i₁ + i₂)²R expanding to i₁²R (blue) + i₂²R (green) + 2i₁i₂R (red). Beneath, two result bars side by side: a short bar labelled "naive Σp…
Source: Engineering Circuit Analysis, 8th ed., Ch. 5, pp. 123-133
CO2 | Bloom L4 | visual id: power-cross-term
Notes: What to say: Give them the idea before the formalism. Say it plainly first: Power is a quadratic function of the response, p = i²R, so expanding the square of a sum produces a cross term: (i₁ + i₂)²R = i₁²R + i₂²R + 2i₁i₂R. Then add the part they are examined on - Superpose the response, then square; never square, then superpose. Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "quadratic response" constrain here, and what would break if it did not hold? Animation instructions: the expansion types in chunk by chunk with the red cross term appearing last and pulsing, then the naive bar grows, then the true bar grows with the red segment stacking visibly on top, then the error badge pops in. Transition style: Fade [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 2: Network Theorems for DC and AC Circuits. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 5, pp. 123-133. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 18
Why superposition fails for power - how it works
The procedure in order, and what each pass costs you.
VTU BEC303 | Module 2
Why superposition fails for power
18
1. Use superposition to find the total current or voltage
2. Stop — do not compute any partial powers
3. Square the total response
4. Multiply by R, or use v·i for the total quantities
5. If partial powers were computed, discard them
COST AND BEHAVIOUR
Best: no extra cost — power is one multiplication after the total is known
Typical: same as a standard superposition solve plus one squaring
Worst: unbounded error if the rule is violated
WHAT THAT MEANS
The only situation where partial powers happen to add is when the partial responses are orthogonal, e.g. at different frequencies over a full period.
Source: Engineering Circuit Analysis, 8th ed., Ch. 5, pp. 123-133 | CO2 | Bloom L4
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Use superposition to find the total current or voltage - and check everyone has written it before moving on. At the cost panel, translate it: The only situation where partial powers happen to add is when the partial responses are orthogonal, e.g. at different frequencies over a fu… Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 2: Network Theorems for DC and AC Circuits. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 5, pp. 123-133. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 19
Why superposition fails for power - worked example
One concrete case, carried all the way to a stated number.
VTU BEC303 | Module 2
Why superposition fails for power
19
GIVEN
Two sources each produce 2 mA through a shared 1 kΩ resistor.
1. Naive: p₁ = (0.002)² × 1000 = 4 mW, p₂ = 4 mW, naive sum = 8 mW
2. Correct: i_total = 2 + 2 = 4 mA
3. p = (0.004)² × 1000 = 16 mW
4. Cross term = 2 × 0.002 × 0.002 × 1000 = 8 mW, the exact shortfall
RESULT
True power is 16 mW against a naive 8 mW — the discarded cross term was equal to the entire naive answer.
(i₁+i₂)²R = i₁²R + i₂²R + 2i₁i₂R
naive : 4 + 4 = 8 mW
true : (4 mA)²·1k = 16 mW (cross term = 8 mW)
THE MISTAKE STUDENTS MAKE
Students apply superposition to power because it worked for current in the same problem five minutes earlier. The theorem is a statement about linear responses only, and power is the one quantity in a linear circuit that is not a linear response.
Source: Engineering Circuit Analysis, 8th ed., Ch. 5, pp. 123-133 | CO2 | Bloom L4
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is Two sources each produce 2 mA through a shared 1 kΩ resistor. Work at the pace of the slowest note-taker and land hard on the result: True power is 16 mW against a naive 8 mW — the discarded cross term was equal to the entire naive answer. Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 2: Network Theorems for DC and AC Circuits. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 5, pp. 123-133. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 20
The reciprocity theorem
What it is, why it works, and what it costs.
VTU BEC303 | Module 2
The reciprocity theorem
20
THE MECHANISM
Reciprocity states that in a linear, passive, bilateral network with a single source, interchanging the positions of the excitation and the response leaves the ratio between them unchanged. Put concretely, if a voltage source in branch A produces a current I in branch B, then moving that same source to branch B produces exactly the same current I in branch A. The ratio excitation/response is called the transfer resistance or transfer impedance, and reciprocity is the statement that this quantity is symmetric between any two branches. It is what allows a measurement made at one accessible port to predict behaviour at an inaccessible one, and it is the network-theory ancestor of the symmetry of the z and y matrices met in Module 5.
KEY TERMS
• reciprocity
• excitation-response interchange
• transfer resistance
• bilateral network
TAKEAWAY
Reciprocity says a passive bilateral network cannot tell which of two ports you are pushing on.
DIAGRAM FOR PHASE 2
Two identical network boxes stacked vertically, each with branch A on the left edge and branch B on the right edge. In the upper box a source symbol sits in branch A and an ammeter reading "I = 2 mA" sits in b…
Source: Network Analysis - A Simplified Approach (TB2, not supplied) - TB2 §4.9
CO2 | Bloom L2 | visual id: reciprocity-swap
Notes: What to say: Give them the idea before the formalism. Say it plainly first: Reciprocity states that in a linear, passive, bilateral network with a single source, interchanging the positions of the excitation and the response leave… Then add the part they are examined on - Reciprocity says a passive bilateral network cannot tell which of two ports you are pushing on. Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "reciprocity" constrain here, and what would break if it did not hold? Animation instructions: the upper box draws with its source and meter, the reading appears, the curved swap arrow sweeps down, the lower box draws with the swapped placement, its reading appears, then the green equals sign flashes between the two readings. Transition style: Fade [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 2: Network Theorems for DC and AC Circuits. Assigned by the syllabus to TB2: K. Channa Venkatesh and D. Ganesh Rao, Network Analysis - A Simplified Approach, Cengage India, 2nd ed., 2012; TB2 §4.9. TB2 was NOT supplied in this environment, so this unit is aligned to the verbatim syllabus headings, cites only the chapter the syllabus gives, and claims no page numbers.

## Slide 21
The reciprocity theorem - how it works
The procedure in order, and what each pass costs you.
VTU BEC303 | Module 2
The reciprocity theorem
21
1. Confirm the network is linear, passive and bilateral
2. Confirm there is exactly one independent source
3. Record the excitation in branch A and the response in branch B
4. Move the source to branch B, preserving its value and polarity convention
5. Measure or compute the response now appearing in branch A
6. Confirm the two ratios are equal
COST AND BEHAVIOUR
Best: one solve replaces two when reciprocity can be invoked
Typical: halves the work for a two-configuration problem
Worst: no benefit if any hypothesis fails
WHAT THAT MEANS
The theorem is a shortcut and a verification check in equal measure.
Source: Network Analysis - A Simplified Approach (TB2, not supplied) - TB2 §4.9 | CO2 | Bloom L2
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Confirm the network is linear, passive and bilateral - and check everyone has written it before moving on. At the cost panel, translate it: The theorem is a shortcut and a verification check in equal measure. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 2: Network Theorems for DC and AC Circuits. Assigned by the syllabus to TB2: K. Channa Venkatesh and D. Ganesh Rao, Network Analysis - A Simplified Approach, Cengage India, 2nd ed., 2012; TB2 §4.9. TB2 was NOT supplied in this environment, so this unit is aligned to the verbatim syllabus headings, cites only the chapter the syllabus gives, and claims no page numbers.

## Slide 22
The reciprocity theorem - worked example
One concrete case, carried all the way to a stated number.
VTU BEC303 | Module 2
The reciprocity theorem
22
GIVEN
A 20 V source in branch A of a passive ladder produces 4 mA in branch B.
1. Transfer resistance = 20 / 0.004 = 5000 Ω
2. Move the 20 V source to branch B
3. Reciprocity asserts the transfer resistance is unchanged
4. Current now in branch A = 20 / 5000 = 4 mA
RESULT
The same 4 mA appears in branch A, without solving the network a second time.
R_transfer = V_A / I_B = 20 / 4 mA = 5 kΩ
swap ⇒ I_A = V_B / R_transfer = 20 / 5 kΩ = 4 mA
THE MISTAKE STUDENTS MAKE
Students apply reciprocity to a circuit that contains a transistor small-signal model. That model contains a dependent source, which makes the network non-bilateral, and the swapped measurement will not match — this is exactly why amplifiers have an input and an output rather than two interchangeable ports.
Source: Network Analysis - A Simplified Approach (TB2, not supplied) - TB2 §4.9 | CO2 | Bloom L2
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is A 20 V source in branch A of a passive ladder produces 4 mA in branch B. Work at the pace of the slowest note-taker and land hard on the result: The same 4 mA appears in branch A, without solving the network a second time. Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 2: Network Theorems for DC and AC Circuits. Assigned by the syllabus to TB2: K. Channa Venkatesh and D. Ganesh Rao, Network Analysis - A Simplified Approach, Cengage India, 2nd ed., 2012; TB2 §4.9. TB2 was NOT supplied in this environment, so this unit is aligned to the verbatim syllabus headings, cites only the chapter the syllabus gives, and claims no page numbers.

## Slide 23
Conditions for reciprocity
What it is, why it works, and what it costs.
VTU BEC303 | Module 2
Conditions for reciprocity
23
THE MECHANISM
Reciprocity holds only under four conditions taken together. The network must be linear; it must be passive, containing no independent or dependent sources other than the single excitation being moved; every element must be bilateral, meaning it presents the same behaviour to current in either direction; and all initial conditions must be zero, so that no stored energy contributes a second, unmoved excitation. Resistors, inductors, capacitors and ideal transformers are bilateral. Dependent sources, diodes, gyrators and any device with a preferred direction are not. If any single condition fails the theorem gives no guarantee, and in practice the swapped measurement differs sharply rather than slightly.
KEY TERMS
• bilateral element
• passivity
• single excitation
• initial conditions zero
TAKEAWAY
Four conditions, all required — and the one students forget is that dependent sources destroy bilaterality.
DIAGRAM FOR PHASE 2
A vertical gate made of four horizontal bars, each a condition: "Linear", "Passive — single excitation only", "Bilateral elements", "Zero initial conditions". A test circuit token travels downward and must pas…
Source: Network Analysis - A Simplified Approach (TB2, not supplied) - TB2 §4.9
CO2 | Bloom L3 | visual id: reciprocity-checklist-gate
Notes: What to say: Give them the idea before the formalism. Say it plainly first: Reciprocity holds only under four conditions taken together. Then add the part they are examined on - Four conditions, all required — and the one students forget is that dependent sources destroy bilaterality. Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "bilateral element" constrain here, and what would break if it did not hold? Animation instructions: the four bars stack in from the left, the green token descends passing each bar which turns green in turn, then the bottom badge lights, then the red token and its stopped state fade in beside it. Transition style: Fade [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 2: Network Theorems for DC and AC Circuits. Assigned by the syllabus to TB2: K. Channa Venkatesh and D. Ganesh Rao, Network Analysis - A Simplified Approach, Cengage India, 2nd ed., 2012; TB2 §4.9. TB2 was NOT supplied in this environment, so this unit is aligned to the verbatim syllabus headings, cites only the chapter the syllabus gives, and claims no page numbers.

## Slide 24
Conditions for reciprocity - how it works
The procedure in order, and what each pass costs you.
VTU BEC303 | Module 2
Conditions for reciprocity
24
1. Check linearity of every element
2. Check that no source other than the excitation is present
3. Check each element for bilateral behaviour
4. Check that all capacitor voltages and inductor currents start at zero
5. Only then invoke reciprocity
6. If any check fails, solve the swapped configuration explicitly
COST AND BEHAVIOUR
Best: O(n) inspection
Typical: O(n) over n elements
Worst: O(n) plus an explicit second solve when the check fails
WHAT THAT MEANS
The check costs far less than a wrong answer built on it.
Source: Network Analysis - A Simplified Approach (TB2, not supplied) - TB2 §4.9 | CO2 | Bloom L3
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Check linearity of every element - and check everyone has written it before moving on. At the cost panel, translate it: The check costs far less than a wrong answer built on it. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 2: Network Theorems for DC and AC Circuits. Assigned by the syllabus to TB2: K. Channa Venkatesh and D. Ganesh Rao, Network Analysis - A Simplified Approach, Cengage India, 2nd ed., 2012; TB2 §4.9. TB2 was NOT supplied in this environment, so this unit is aligned to the verbatim syllabus headings, cites only the chapter the syllabus gives, and claims no page numbers.

## Slide 25
Conditions for reciprocity - worked example
One concrete case, carried all the way to a stated number.
VTU BEC303 | Module 2
Conditions for reciprocity
25
GIVEN
A network of resistors and one ideal transformer, with a single 12 V source and no stored energy.
1. Linear — resistors and ideal transformers are linear: pass
2. Passive apart from the single excitation: pass
3. Bilateral — an ideal transformer transmits equally in both directions: pass
4. Zero initial conditions — purely resistive plus transformer, no stored energy: pass
RESULT
All four conditions hold, so the excitation and response may be interchanged without re-solving the network.
linear ∧ passive ∧ bilateral ∧ IC = 0
⇒ V_A/I_B = V_B/I_A
THE MISTAKE STUDENTS MAKE
Students check only for linearity, since that is the condition the other theorems in this module emphasise. Superposition and Thévenin survive dependent sources; reciprocity does not, and that difference is the whole point of stating four conditions instead of one.
Source: Network Analysis - A Simplified Approach (TB2, not supplied) - TB2 §4.9 | CO2 | Bloom L3
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is A network of resistors and one ideal transformer, with a single 12 V source and no stored energy. Work at the pace of the slowest note-taker and land hard on the result: All four conditions hold, so the excitation and response may be interchanged without re-solving the network. Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 2: Network Theorems for DC and AC Circuits. Assigned by the syllabus to TB2: K. Channa Venkatesh and D. Ganesh Rao, Network Analysis - A Simplified Approach, Cengage India, 2nd ed., 2012; TB2 §4.9. TB2 was NOT supplied in this environment, so this unit is aligned to the verbatim syllabus headings, cites only the chapter the syllabus gives, and claims no page numbers.

## Slide 26
Reciprocal and non-reciprocal circuits
What it is, why it works, and what it costs.
VTU BEC303 | Module 2
Reciprocal and non-reciprocal circuits
26
THE MECHANISM
A purely resistive ladder, an LC filter and a passive transformer-coupled network are reciprocal: interchange source and meter and the reading is unchanged. A transistor amplifier, an op-amp stage, a gyrator and a microwave isolator are non-reciprocal, because each contains a dependent source or a directionally biased medium that transmits differently forwards and backwards. The distinction is engineering-critical rather than academic: non-reciprocity is exactly what makes one-way signal flow possible, so an amplifier does not amplify backwards and an isolator protects a source from a reflected wave. Reciprocity is therefore a property to be exploited in passive design and deliberately broken in active design.
KEY TERMS
• reciprocal network
• non-reciprocal network
• gyrator
• isolator
• amplifier asymmetry
TAKEAWAY
Reciprocity is a feature of passive networks and a bug in anything meant to have an input and an output.
DIAGRAM FOR PHASE 2
Two panels side by side with a dividing line. Left panel headed "Reciprocal" contains three thumbnails — a resistive ladder, an LC filter, a transformer — each with a symmetric double-headed arrow across it an…
Source: Network Analysis - A Simplified Approach (TB2, not supplied) - TB2 §4.9
CO2 | Bloom L4 | visual id: reciprocal-vs-not-panels
Notes: What to say: Give them the idea before the formalism. Say it plainly first: A purely resistive ladder, an LC filter and a passive transformer-coupled network are reciprocal: interchange source and meter and the reading is unchange… Then add the part they are examined on - Reciprocity is a feature of passive networks and a bug in anything meant to have an input and an output. Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "reciprocal network" constrain here, and what would break if it did not hold? Animation instructions: the divider draws, left thumbnails appear top to bottom with their double arrows animating both ways, then right thumbnails appear with their arrows animating forward only and the reverse attempt bouncing back, then the caption strip slides up. Transition style: Fade [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 2: Network Theorems for DC and AC Circuits. Assigned by the syllabus to TB2: K. Channa Venkatesh and D. Ganesh Rao, Network Analysis - A Simplified Approach, Cengage India, 2nd ed., 2012; TB2 §4.9. TB2 was NOT supplied in this environment, so this unit is aligned to the verbatim syllabus headings, cites only the chapter the syllabus gives, and claims no page numbers.

## Slide 27
Reciprocal and non-reciprocal circuits - how it works
The procedure in order, and what each pass costs you.
VTU BEC303 | Module 2
Reciprocal and non-reciprocal circuits
27
1. Identify whether the network contains any dependent source
2. Identify any element with a directional medium or bias
3. Classify as reciprocal only if neither is present
4. For reciprocal networks, exploit symmetry to halve the analysis
5. For non-reciprocal networks, analyse each direction separately
6. Expect z and y matrices to be symmetric only in the reciprocal case
COST AND BEHAVIOUR
Best: inspection, O(1) for a small network
Typical: O(n) element scan
Worst: O(n) plus two full solves for a non-reciprocal network
WHAT THAT MEANS
This classification is what Module 5 will reuse when testing z₁₂ = z₂₁.
Source: Network Analysis - A Simplified Approach (TB2, not supplied) - TB2 §4.9 | CO2 | Bloom L4
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Identify whether the network contains any dependent source - and check everyone has written it before moving on. At the cost panel, translate it: This classification is what Module 5 will reuse when testing z₁₂ = z₂₁. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 2: Network Theorems for DC and AC Circuits. Assigned by the syllabus to TB2: K. Channa Venkatesh and D. Ganesh Rao, Network Analysis - A Simplified Approach, Cengage India, 2nd ed., 2012; TB2 §4.9. TB2 was NOT supplied in this environment, so this unit is aligned to the verbatim syllabus headings, cites only the chapter the syllabus gives, and claims no page numbers.

## Slide 28
Reciprocal and non-reciprocal circuits - worked example
One concrete case, carried all the way to a stated number.
VTU BEC303 | Module 2
Reciprocal and non-reciprocal circuits
28
GIVEN
A common-emitter amplifier modelled as r_π with a current-controlled current source β·i_b driving R_C.
1. Forward: a signal at the base produces β·i_b through R_C — substantial gain
2. Reverse: a signal applied at the collector finds no path that controls i_b
3. The dependent source transmits in one direction only
4. Swapped excitation and response give completely different readings
RESULT
The network is non-reciprocal, and that asymmetry is precisely what makes it useful as an amplifier rather than a filter.
forward : i_c = β·i_b (gain)
reverse : i_b ≠ f(i_c) (no path)
⇒ z₁₂ ≠ z₂₁ — non-reciprocal
THE MISTAKE STUDENTS MAKE
Students describe a network as non-reciprocal because it is asymmetric in layout. Physical asymmetry is irrelevant; an unbalanced but purely passive ladder is perfectly reciprocal. Only dependent sources and directional media break it.
Source: Network Analysis - A Simplified Approach (TB2, not supplied) - TB2 §4.9 | CO2 | Bloom L4
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is A common-emitter amplifier modelled as r_π with a current-controlled current source β·i_b driving R_C. Work at the pace of the slowest note-taker and land hard on the result: The network is non-reciprocal, and that asymmetry is precisely what makes it useful as an amplifier rather than a filter. Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 2: Network Theorems for DC and AC Circuits. Assigned by the syllabus to TB2: K. Channa Venkatesh and D. Ganesh Rao, Network Analysis - A Simplified Approach, Cengage India, 2nd ed., 2012; TB2 §4.9. TB2 was NOT supplied in this environment, so this unit is aligned to the verbatim syllabus headings, cites only the chapter the syllabus gives, and claims no page numbers.

## Slide 29
Thévenin's theorem
What it is, why it works, and what it costs.
VTU BEC303 | Module 2
Thévenin's theorem
29
THE MECHANISM
Thévenin's theorem states that any linear two-terminal network may be replaced, as far as anything connected to those two terminals can tell, by a single voltage source V_th in series with a single resistance R_th. The theorem's power comes from what it does not require: the load may be nonlinear, time-varying, or completely unknown, because the linearity hypothesis applies only inside the port. This is what makes it the standard tool for repeated-load problems — compute the equivalent once, then sweep the load as many times as needed with a two-element circuit instead of the full network. The equivalent is exact at the terminals and says nothing whatever about internal currents or internal power.
KEY TERMS
• Thévenin equivalent
• port
• V_th
• R_th
• load independence
TAKEAWAY
Thévenin collapses everything behind a port into two numbers, and those two numbers are valid for any load you care to attach.
DIAGRAM FOR PHASE 2
Left: a complicated network drawn as a cloud containing several sources and resistors, with two terminals a and b protruding on the right and a load box R_L attached. A large arrow labelled "collapse" points r…
Source: Engineering Circuit Analysis, 8th ed., Ch. 5, pp. 141-152
CO2 | Bloom L3 | visual id: thevenin-collapse
Notes: What to say: Give them the idea before the formalism. Say it plainly first: Thévenin's theorem states that any linear two-terminal network may be replaced, as far as anything connected to those two terminals can tell, by a single… Then add the part they are examined on - Thévenin collapses everything behind a port into two numbers, and those two numbers are valid for any load you care to attac… Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "Thévenin equivalent" constrain here, and what would break if it did not hold? Animation instructions: the cloud network fades in with the load, the collapse arrow sweeps right while the cloud shrinks into the two-element form, then the two meter readings light up and the green equals sign appears, then the two captions fade in. Transition style: Fade [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 2: Network Theorems for DC and AC Circuits. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 5, pp. 141-152. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 30
Thévenin's theorem - how it works
The procedure in order, and what each pass costs you.
VTU BEC303 | Module 2
Thévenin's theorem
30
1. Identify the two terminals that define the port
2. Detach the load at those terminals
3. Find the open-circuit voltage across the terminals — this is V_th
4. Find the resistance looking back into the terminals — this is R_th
5. Redraw as V_th in series with R_th
6. Reattach the load and solve the two-element circuit
COST AND BEHAVIOUR
Best: O(1) when the network is a simple divider
Typical: two solves — one for V_th, one for R_th
Worst: two full network solves, then O(1) per load value
WHAT THAT MEANS
Break-even against direct analysis occurs at about three different load values.
Source: Engineering Circuit Analysis, 8th ed., Ch. 5, pp. 141-152 | CO2 | Bloom L3
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Identify the two terminals that define the port - and check everyone has written it before moving on. At the cost panel, translate it: Break-even against direct analysis occurs at about three different load values. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 2: Network Theorems for DC and AC Circuits. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 5, pp. 141-152. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 31
Thévenin's theorem - worked example
One concrete case, carried all the way to a stated number.
VTU BEC303 | Module 2
Thévenin's theorem
31
GIVEN
A 12 V source in series with 4 kΩ, with 6 kΩ to ground, and the port taken across the 6 kΩ.
1. Remove the load; V_th = 12 × 6/(4+6) = 7.2 V
2. Deactivate the 12 V source (short it)
3. Looking back: 4 kΩ ∥ 6 kΩ = 2.4 kΩ = R_th
4. Equivalent: 7.2 V in series with 2.4 kΩ
RESULT
V_th = 7.2 V, R_th = 2.4 kΩ; attaching a 2.4 kΩ load now gives 3.6 V in one line instead of re-solving the divider.
V_th = 12·6k/(4k+6k) = 7.2 V
R_th = 4k ∥ 6k = 2.4 kΩ
with R_L = 2.4k: v = 7.2/2 = 3.6 V
THE MISTAKE STUDENTS MAKE
Students compute V_th with the load still connected. The Thévenin voltage is by definition the open-circuit voltage; leaving the load in place loads the divider and produces a value that is always too low.
Source: Engineering Circuit Analysis, 8th ed., Ch. 5, pp. 141-152 | CO2 | Bloom L3
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is A 12 V source in series with 4 kΩ, with 6 kΩ to ground, and the port taken across the 6 kΩ. Work at the pace of the slowest note-taker and land hard on the result: V_th = 7.2 V, R_th = 2.4 kΩ; attaching a 2.4 kΩ load now gives 3.6 V in one line instead of re-solving the divider. Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 2: Network Theorems for DC and AC Circuits. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 5, pp. 141-152. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 32
Finding R_th: three methods and when each applies
What it is, why it works, and what it costs.
VTU BEC303 | Module 2
Finding R_th: three methods and when…
32
THE MECHANISM
There are three ways to find R_th and the choice is dictated by what the network contains. If the network has only independent sources, deactivate them all and reduce the remaining resistive network by series-parallel and delta-wye — the fastest route. If dependent sources are present, deactivation is not permitted, so instead apply a 1 V test source across the dead port, compute the resulting current, and take R_th = 1/I; this works in every case. The third method takes the ratio of open-circuit voltage to short-circuit current, R_th = V_oc/I_sc, which is convenient when both quantities are being computed anyway but fails when V_oc and I_sc are both zero. Networks with dependent sources can legitimately yield a negative R_th, which is a real effect and not an arithmetic error.
KEY TERMS
• look-back resistance
• test source method
• open-circuit/short-circuit method
• negative resistance
TAKEAWAY
No dependent sources means look back and reduce; dependent sources means apply a test source — there is no third option that is always safe.
DIAGRAM FOR PHASE 2
A decision diamond at the top reading "Dependent sources present?" with two branches. The "No" branch leads to a box "Deactivate all sources, reduce network" with a small series-parallel thumbnail. The "Yes" b…
Source: Engineering Circuit Analysis, 8th ed., Ch. 5, pp. 141-152
CO2 | Bloom L4 | visual id: rth-three-routes
Notes: What to say: Give them the idea before the formalism. Say it plainly first: There are three ways to find R_th and the choice is dictated by what the network contains. Then add the part they are examined on - No dependent sources means look back and reduce; dependent sources means apply a test source — there is no third option that… Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "look-back resistance" constrain here, and what would break if it did not hold? Animation instructions: the diamond appears, the No branch draws left with its box, the Yes branch draws right with its box, then the dotted lines and the shared V_oc/I_sc box appear, then the amber negative-resistance badge pops in. Transition style: Fade [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 2: Network Theorems for DC and AC Circuits. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 5, pp. 141-152. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 33
Finding R_th: three methods and when each applies - how it works
The procedure in order, and what each pass costs you.
VTU BEC303 | Module 2
Finding R_th: three methods and when…
33
1. Detach the load and inspect the network for dependent sources
2. If none, deactivate every independent source and reduce the resistive network
3. If any, leave all sources as drawn, deactivate only independent ones, and apply a 1 V test source at the port
4. Compute the test current and take R_th = V_test / I_test
5. Alternatively compute V_oc and I_sc and take their ratio
6. Accept a negative R_th as a genuine result when dependent sources are present
COST AND BEHAVIOUR
Best: O(n) series-parallel reduction with independent sources only
Typical: one extra network solve for the test-source method
Worst: two solves for the V_oc/I_sc route
WHAT THAT MEANS
The test-source method is the only one that never fails, which is why it is the fallback.
Source: Engineering Circuit Analysis, 8th ed., Ch. 5, pp. 141-152 | CO2 | Bloom L4
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Detach the load and inspect the network for dependent sources - and check everyone has written it before moving on. At the cost panel, translate it: The test-source method is the only one that never fails, which is why it is the fallback. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 2: Network Theorems for DC and AC Circuits. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 5, pp. 141-152. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 34
Finding R_th: three methods and when each applies - worked example
One concrete case, carried all the way to a stated number.
VTU BEC303 | Module 2
Finding R_th: three methods and when…
34
GIVEN
A port with a 2 kΩ resistor and a CCVS of 3000·i_x in series, where i_x is the port current itself.
1. Dependent source present, so deactivation is not allowed
2. Apply a 1 V test source: 1 = 2000·i_x + 3000·i_x
3. i_x = 1/5000 = 0.2 mA
4. R_th = 1 / 0.0002 = 5000 Ω
RESULT
R_th = 5 kΩ, not the 2 kΩ a naive deactivation would have given — the dependent source contributed 3 kΩ of apparent resistance.
apply V_test = 1 V
1 = 2000·i + 3000·i ⇒ i = 0.2 mA
R_th = V_test/i = 5 kΩ (not 2 kΩ)
THE MISTAKE STUDENTS MAKE
Students deactivate dependent sources to make the look-back reduction work. In the worked example that shortcut gives 2 kΩ against a true 5 kΩ — a 60 % error, and the maximum-power load derived from it would be badly wrong.
Source: Engineering Circuit Analysis, 8th ed., Ch. 5, pp. 141-152 | CO2 | Bloom L4
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is A port with a 2 kΩ resistor and a CCVS of 3000·i_x in series, where i_x is the port current itself. Work at the pace of the slowest note-taker and land hard on the result: R_th = 5 kΩ, not the 2 kΩ a naive deactivation would have given — the dependent source contributed 3 kΩ of apparent resistance. Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 2: Network Theorems for DC and AC Circuits. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 5, pp. 141-152. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 35
Norton's theorem and Thévenin–Norton duality
What it is, why it works, and what it costs.
VTU BEC303 | Module 2
Norton's theorem and Thévenin–Norton…
35
THE MECHANISM
Norton's theorem is the current-source dual of Thévenin's: any linear two-terminal network may be replaced by a current source I_N in parallel with a resistance R_N, where I_N is the short-circuit current at the port and R_N equals R_th. The two equivalents are related by exactly the source transformation of Module 1, V_th = I_N·R_th, so either can be derived from the other in one line. Which to use is a matter of the load topology rather than principle — a Thévenin form suits a load in series, a Norton form suits a load in parallel with other branches. Both are exact at the terminals and both are silent about anything inside.
KEY TERMS
• Norton equivalent
• I_N
• short-circuit current
• duality
• equivalence transformation
TAKEAWAY
Thévenin and Norton are the same two facts about a port written in two different notations; choose the one that matches the load.
DIAGRAM FOR PHASE 2
A central vertical axis with the Thévenin form on the left — V_th in series with R_th, terminals a-b — and the Norton form on the right — I_N in parallel with R_N, terminals a-b. A double-headed horizontal arr…
Source: Engineering Circuit Analysis, 8th ed., Ch. 5, pp. 141-152
CO2 | Bloom L3 | visual id: thevenin-norton-duality
Notes: What to say: Give them the idea before the formalism. Say it plainly first: Norton's theorem is the current-source dual of Thévenin's: any linear two-terminal network may be replaced by a current source I_N in parallel with a resi… Then add the part they are examined on - Thévenin and Norton are the same two facts about a port written in two different notations; choose the one that matches the… Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "Norton equivalent" constrain here, and what would break if it did not hold? Animation instructions: Thévenin form draws, Norton form draws, the double arrow animates between them, the two measurement badges drop in, then the two load thumbnails slide up with their green preference arrows. Transition style: Fade [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 2: Network Theorems for DC and AC Circuits. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 5, pp. 141-152. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 36
Norton's theorem and Thévenin–Norton duality - how it works
The procedure in order, and what each pass costs you.
VTU BEC303 | Module 2
Norton's theorem and Thévenin–Norton…
36
1. Detach the load at the port
2. Short the terminals and compute the short-circuit current — this is I_N
3. Compute R_th by the appropriate method; R_N equals it
4. Draw I_N in parallel with R_N
5. Convert to Thévenin form when needed using V_th = I_N·R_th
6. Reattach the load and solve
COST AND BEHAVIOUR
Best: O(1) conversion when the other equivalent is already known
Typical: two solves, identical in cost to the Thévenin route
Worst: two full network solves
WHAT THAT MEANS
Never compute both from scratch — derive the second from the first.
Source: Engineering Circuit Analysis, 8th ed., Ch. 5, pp. 141-152 | CO2 | Bloom L3
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Detach the load at the port - and check everyone has written it before moving on. At the cost panel, translate it: Never compute both from scratch — derive the second from the first. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 2: Network Theorems for DC and AC Circuits. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 5, pp. 141-152. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 37
Norton's theorem and Thévenin–Norton duality - worked example
One concrete case, carried all the way to a stated number.
VTU BEC303 | Module 2
Norton's theorem and Thévenin–Norton…
37
GIVEN
A port whose Thévenin equivalent is 7.2 V in series with 2.4 kΩ.
1. I_N = V_th / R_th = 7.2 / 2400 = 3 mA
2. R_N = R_th = 2.4 kΩ
3. Norton form: 3 mA in parallel with 2.4 kΩ
4. Check with a 2.4 kΩ load: current divides equally, load current = 1.5 mA, load voltage = 3.6 V
RESULT
Norton form is 3 mA ∥ 2.4 kΩ, and it reproduces the 3.6 V load voltage found from the Thévenin form, as it must.
I_N = V_th/R_th = 7.2/2.4k = 3 mA
R_N = R_th = 2.4 kΩ
check R_L = 2.4k ⇒ I_L = 1.5 mA, v = 3.6 V ✓
THE MISTAKE STUDENTS MAKE
Students compute I_N by dividing V_th by the load resistance instead of by R_th. I_N is the short-circuit current at the port, a property of the network alone, and it must not involve the load in any way.
Source: Engineering Circuit Analysis, 8th ed., Ch. 5, pp. 141-152 | CO2 | Bloom L3
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is A port whose Thévenin equivalent is 7.2 V in series with 2.4 kΩ. Work at the pace of the slowest note-taker and land hard on the result: Norton form is 3 mA ∥ 2.4 kΩ, and it reproduces the 3.6 V load voltage found from the Thévenin form, as it must. Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 2: Network Theorems for DC and AC Circuits. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 5, pp. 141-152. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 38
The maximum power transfer theorem
What it is, why it works, and what it costs.
VTU BEC303 | Module 2
The maximum power transfer theorem
38
THE MECHANISM
Maximum power is delivered to a load when the load resistance equals the Thévenin resistance of the source network. The derivation is a single differentiation: p = V_th²·R_L/(R_th + R_L)², and setting dp/dR_L = 0 gives R_L = R_th, at which point p_max = V_th²/(4R_th). Two consequences are routinely missed. First, the optimum is flat — a load mismatched by a factor of two still delivers about 89 % of the maximum, which is why exact matching is rarely worth expensive components. Second, at the match exactly half the total power is dissipated inside the source, so efficiency is 50 %, and any design that values efficiency over delivered power must deliberately mismatch.
KEY TERMS
• matched load
• R_L = R_th
• power maximum
• flat optimum
• efficiency
TAKEAWAY
Matching maximises delivered power and caps efficiency at 50 % — those are two different design goals and you may only have one.
DIAGRAM FOR PHASE 2
A curve of delivered power p against the ratio R_L/R_th on a logarithmic horizontal axis from 0.1 to 10. The curve rises to a broad rounded peak at ratio 1, marked with a vertical dashed line and the label p_m…
Source: Engineering Circuit Analysis, 8th ed., Ch. 5, pp. 152-154
CO2 | Bloom L4 | visual id: max-power-curve
Notes: What to say: Give them the idea before the formalism. Say it plainly first: Maximum power is delivered to a load when the load resistance equals the Thévenin resistance of the source network. Then add the part they are examined on - Matching maximises delivered power and caps efficiency at 50 % — those are two different design goals and you may only have… Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "matched load" constrain here, and what would break if it did not hold? Animation instructions: axes draw, the power curve traces left to right, the peak dashed line drops, the two flatness bands shade in simultaneously, then the efficiency curve traces as a dashed line, then the 50% crossing callout appears last. Transition style: Fade [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 2: Network Theorems for DC and AC Circuits. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 5, pp. 152-154. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 39
The maximum power transfer theorem - how it works
The procedure in order, and what each pass costs you.
VTU BEC303 | Module 2
The maximum power transfer theorem
39
1. Find the Thévenin equivalent of the network feeding the load
2. Set R_L = R_th for maximum delivered power
3. Compute p_max = V_th² / (4·R_th)
4. Check the efficiency: it is 50 % at the match, by construction
5. If efficiency matters more than delivered power, choose R_L ≫ R_th instead
6. For AC, match the complex conjugate: Z_L = Z_th*
COST AND BEHAVIOUR
Best: O(1) once the Thévenin equivalent is known
Typical: cost of one Thévenin reduction plus one division
Worst: full network reduction first
WHAT THAT MEANS
The flatness of the optimum means a 2:1 component tolerance costs about 11 % of peak power.
Source: Engineering Circuit Analysis, 8th ed., Ch. 5, pp. 152-154 | CO2 | Bloom L4
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Find the Thévenin equivalent of the network feeding the load - and check everyone has written it before moving on. At the cost panel, translate it: The flatness of the optimum means a 2:1 component tolerance costs about 11 % of peak power. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 2: Network Theorems for DC and AC Circuits. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 5, pp. 152-154. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 40
The maximum power transfer theorem - worked example
One concrete case, carried all the way to a stated number.
VTU BEC303 | Module 2
The maximum power transfer theorem
40
GIVEN
A source network with V_th = 12 V and R_th = 50 Ω.
1. Matched load: R_L = 50 Ω
2. p_max = 12² / (4 × 50) = 144/200 = 0.72 W
3. Source dissipation at the match = also 0.72 W, so efficiency = 50 %
4. Mismatch check at R_L = 100 Ω: p = 144 × 100/150² = 0.64 W, i.e. 89 % of peak
RESULT
p_max = 0.72 W at R_L = 50 Ω; doubling the load to 100 Ω still delivers 0.64 W but raises efficiency to 67 %.
p(R_L) = V_th²·R_L/(R_th+R_L)²
dp/dR_L = 0 ⇒ R_L = R_th
p_max = 12²/(4·50) = 0.72 W, η = 50%
THE MISTAKE STUDENTS MAKE
Students describe the matched condition as the most efficient operating point. It is the opposite — it is the point at which the source wastes as much power as it delivers, and power utilities deliberately operate at R_L ≫ R_th for exactly that reason.
Source: Engineering Circuit Analysis, 8th ed., Ch. 5, pp. 152-154 | CO2 | Bloom L4
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is A source network with V_th = 12 V and R_th = 50 Ω. Work at the pace of the slowest note-taker and land hard on the result: p_max = 0.72 W at R_L = 50 Ω; doubling the load to 100 Ω still delivers 0.64 W but raises efficiency to 67 %. Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 2: Network Theorems for DC and AC Circuits. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 5, pp. 152-154. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 41
Case study: maximum power transfer in electronic systems design
What it is, why it works, and what it costs.
VTU BEC303 | Module 2
Case study: maximum power transfer in…
41
THE MECHANISM
Real designs choose between three matching regimes according to what is scarce. In RF and transmission-line systems the load is matched to 50 Ω not for maximum power but to eliminate reflections, because a mismatch sends energy back down the line and corrupts the signal. In audio power stages the amplifier output impedance is deliberately made far smaller than the loudspeaker impedance, giving a high damping factor and good efficiency rather than maximum transferred power. In sensor front ends the amplifier input impedance is made far larger than the source impedance so that the measured voltage is not loaded down. Maximum power transfer is therefore the right criterion in only a minority of designs — typically small-signal antenna and transducer interfaces where the available signal power is the scarce resource.
KEY TERMS
• impedance matching
• audio power amplifier
• RF 50 Ω system
• signal integrity
• conjugate match
TAKEAWAY
Match for power when signal power is scarce, match for reflection when the line is long, and mismatch deliberately everywhere else.
DIAGRAM FOR PHASE 2
Three vertical panels. Panel 1 "RF / transmission line": a source, a length of line drawn as parallel rails, and a 50 Ω termination, with a reflected wave arrow shown bouncing back in red when the termination…
Source: Engineering Circuit Analysis, 8th ed., Ch. 5, pp. 152-154
CO2 | Bloom L5 | visual id: matching-regimes-triptych
Notes: What to say: Give them the idea before the formalism. Say it plainly first: Real designs choose between three matching regimes according to what is scarce. Then add the part they are examined on - Match for power when signal power is scarce, match for reflection when the line is long, and mismatch deliberately everywher… Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "impedance matching" constrain here, and what would break if it did not hold? Animation instructions: panels appear left to right; in panel 1 the red reflection animates then the green matched case replaces it; panel 2 and 3 fade in with their annotations; then the footer strip types in left to right. Transition style: Fade [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 2: Network Theorems for DC and AC Circuits. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 5, pp. 152-154. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 42
Case study: maximum power transfer in electronic system… - how it works
The procedure in order, and what each pass costs you.
VTU BEC303 | Module 2
Case study: maximum power transfer in…
42
1. Identify the scarce resource: signal power, efficiency, or signal fidelity
2. If signal power is scarce, conjugate match Z_L = Z_th*
3. If the interconnect is electrically long, match to the line impedance to prevent reflection
4. If efficiency or damping matters, make R_out ≪ R_L
5. If voltage fidelity matters, make R_in ≫ R_source
6. State the chosen criterion explicitly in the design documentation
COST AND BEHAVIOUR
Best: one matching network for a single frequency
Typical: a matching network per band of interest
Worst: broadband matching, which trades bandwidth against match quality
WHAT THAT MEANS
Matching is inherently frequency-dependent; a match at one frequency is a mismatch at another.
Source: Engineering Circuit Analysis, 8th ed., Ch. 5, pp. 152-154 | CO2 | Bloom L5
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Identify the scarce resource: signal power, efficiency, or signal fidelity - and check everyone has written it before moving on. At the cost panel, translate it: Matching is inherently frequency-dependent; a match at one frequency is a mismatch at another. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 2: Network Theorems for DC and AC Circuits. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 5, pp. 152-154. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 43
Case study: maximum power transfer in electronic system… - worked example
One concrete case, carried all the way to a stated number.
VTU BEC303 | Module 2
Case study: maximum power transfer in…
43
GIVEN
An antenna with source impedance 50 + j30 Ω feeding a receiver front end.
1. Signal power from an antenna is the scarce resource, so match for maximum power
2. Conjugate match requires Z_L = 50 − j30 Ω
3. The −j30 cancels the antenna reactance, leaving a purely resistive 100 Ω loop
4. Delivered power = |V_th|²/(4 × 50), the maximum available
RESULT
A 50 − j30 Ω input presents the conjugate match and extracts the maximum available signal power; a plain 50 Ω resistive input would lose power to the uncancelled reactance.
Z_th = 50 + j30 Ω
Z_L = Z_th* = 50 − j30 Ω
loop = 100 Ω purely real ⇒ p = |V_th|²/(4·50)
THE MISTAKE STUDENTS MAKE
Students match the magnitude of the impedance instead of taking the complex conjugate. Setting |Z_L| = |Z_th| leaves the reactances adding rather than cancelling, and the delivered power falls well short of the available maximum.
Source: Engineering Circuit Analysis, 8th ed., Ch. 5, pp. 152-154 | CO2 | Bloom L5
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is An antenna with source impedance 50 + j30 Ω feeding a receiver front end. Work at the pace of the slowest note-taker and land hard on the result: A 50 − j30 Ω input presents the conjugate match and extracts the maximum available signal power; a plain 50 Ω resistive input wou… Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 2: Network Theorems for DC and AC Circuits. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 5, pp. 152-154. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 44
Network theorems in the phasor domain
What it is, why it works, and what it costs.
VTU BEC303 | Module 2
Network theorems in the phasor domain
44
THE MECHANISM
Every theorem in this module transfers to sinusoidal steady state by a single substitution: resistance becomes impedance and real arithmetic becomes complex arithmetic. Superposition applies to phasors at a common frequency and to time-domain waveforms across frequencies. Thévenin yields V_th as a phasor and Z_th as a complex impedance, found by the same three methods as before. Source transformation becomes V_th = I_N·Z_th. The single genuine modification is maximum power transfer, where the optimum is the conjugate Z_L = Z_th* rather than Z_L = Z_th, because the load reactance must cancel the source reactance before the resistive match can do its work.
KEY TERMS
• phasor superposition
• Thévenin impedance Z_th
• complex source transformation
• AC theorem transfer
TAKEAWAY
All the DC theorems survive into AC unchanged except maximum power transfer, which becomes a conjugate match.
DIAGRAM FOR PHASE 2
A bridge spanning two banks. Left bank labelled "DC" carries four tiles: Superposition, Thévenin, Norton, Max power. Right bank labelled "AC (phasor)" carries four matching tiles. Three of the four pairs are j…
Source: Engineering Circuit Analysis, 8th ed., Ch. 10, pp. 397-406
CO2 | Bloom L4 | visual id: theorem-transfer-bridge
Notes: What to say: Give them the idea before the formalism. Say it plainly first: Every theorem in this module transfers to sinusoidal steady state by a single substitution: resistance becomes impedance and real arithmetic becomes compl… Then add the part they are examined on - All the DC theorems survive into AC unchanged except maximum power transfer, which becomes a conjugate match. Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "phasor superposition" constrain here, and what would break if it did not hold? Animation instructions: the two banks draw, the four DC tiles appear, then each green span extends left to right revealing its AC tile, then the amber conjugate span extends last and pulses, then the legend fades in. Transition style: Fade [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 2: Network Theorems for DC and AC Circuits. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 10, pp. 397-406. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 45
Network theorems in the phasor domain - how it works
The procedure in order, and what each pass costs you.
VTU BEC303 | Module 2
Network theorems in the phasor domain
45
1. Convert every source to a phasor and every element to an impedance
2. Apply the required theorem with resistance replaced by impedance
3. For superposition across different frequencies, recombine only in the time domain
4. For Thévenin, compute V_th as a phasor and Z_th by test source or look-back
5. For maximum power, use the conjugate Z_L = Z_th*
6. Convert the final phasor answers back to the time domain
COST AND BEHAVIOUR
Best: identical structure to the DC case
Typical: about four times the arithmetic of the real case
Worst: one full solve per frequency in a multi-frequency problem
WHAT THAT MEANS
No new theory is introduced; all the additional cost is complex arithmetic.
Source: Engineering Circuit Analysis, 8th ed., Ch. 10, pp. 397-406 | CO2 | Bloom L4
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Convert every source to a phasor and every element to an impedance - and check everyone has written it before moving on. At the cost panel, translate it: No new theory is introduced; all the additional cost is complex arithmetic. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 2: Network Theorems for DC and AC Circuits. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 10, pp. 397-406. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 46
Network theorems in the phasor domain - worked example
One concrete case, carried all the way to a stated number.
VTU BEC303 | Module 2
Network theorems in the phasor domain
46
GIVEN
A source 20∠0° V with Z_th = 30 + j40 Ω, delivering to a load chosen for maximum power.
1. Conjugate match: Z_L = 30 − j40 Ω
2. Loop impedance = 60 + j0 = 60 Ω purely resistive
3. I = 20∠0°/60 = 0.3333∠0° A
4. p_L = |I|²·Re{Z_L} = 0.1111 × 30 = 3.33 W, matching V_th²/(4·R_th) = 400/120 = 3.33 W
RESULT
Maximum delivered power is 3.33 W with Z_L = 30 − j40 Ω; the two independent routes to the same number confirm the conjugate rule.
Z_L = Z_th* = 30 − j40 Ω
I = 20∠0°/(60) = 0.333 A
p = |I|²·30 = 3.33 W = |V_th|²/(4·30) ✓
THE MISTAKE STUDENTS MAKE
Students carry the DC rule R_L = R_th straight into AC and set Z_L = Z_th. That leaves the total loop reactance at 2X instead of zero, and the delivered power drops well below the achievable maximum.
Source: Engineering Circuit Analysis, 8th ed., Ch. 10, pp. 397-406 | CO2 | Bloom L4
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is A source 20∠0° V with Z_th = 30 + j40 Ω, delivering to a load chosen for maximum power. Work at the pace of the slowest note-taker and land hard on the result: Maximum delivered power is 3.33 W with Z_L = 30 − j40 Ω; the two independent routes to the same number confirm the conjugate rule. Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 2: Network Theorems for DC and AC Circuits. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 10, pp. 397-406. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 47
Choosing between theorems: a decision procedure
What it is, why it works, and what it costs.
VTU BEC303 | Module 2
Choosing between theorems: a decision…
47
THE MECHANISM
The theorems are not interchangeable and choosing badly costs more work than it saves. Use Thévenin or Norton when one load is going to be varied repeatedly, because the equivalent is computed once and reused. Use superposition when the question asks which source is responsible for an observed output, or when sources operate at different frequencies and no other method applies. Use reciprocity to halve the work when a passive network is to be measured or driven from two different ports. Use straightforward nodal or mesh analysis when all branch quantities are wanted at once, since every theorem here gives a single answer at a single point and would have to be repeated for every other branch.
KEY TERMS
• method selection
• repeated load
• attribution
• equation economy
TAKEAWAY
Pick the theorem by what the question asks for, not by what is easiest to recall.
DIAGRAM FOR PHASE 2
A decision tree flowing top to bottom. Root: "What does the question ask?". Four branches: "One load, many values" → leaf "Thévenin / Norton"; "Which source caused this?" → leaf "Superposition"; "Different fre…
Source: Engineering Circuit Analysis, 8th ed., Ch. 5, pp. 123-154
CO2 | Bloom L5 | visual id: theorem-decision-tree
Notes: What to say: Give them the idea before the formalism. Say it plainly first: The theorems are not interchangeable and choosing badly costs more work than it saves. Then add the part they are examined on - Pick the theorem by what the question asks for, not by what is easiest to recall. Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "method selection" constrain here, and what would break if it did not hold? Animation instructions: the root appears, then each branch draws in turn with its leaf fading in, then all five cost badges appear together at the end. Transition style: Fade [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 2: Network Theorems for DC and AC Circuits. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 5, pp. 123-154. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 48
Choosing between theorems: a decision procedure - how it works
The procedure in order, and what each pass costs you.
VTU BEC303 | Module 2
Choosing between theorems: a decision…
48
1. Read the question and identify the single quantity actually required
2. If a load will be swept, build a Thévenin or Norton equivalent
3. If attribution across sources is wanted, use superposition
4. If sources differ in frequency, superposition is mandatory
5. If the network is passive and two ports are involved, consider reciprocity
6. If every branch quantity is wanted, use nodal or mesh analysis directly
COST AND BEHAVIOUR
Best: 1 solve with the right choice
Typical: 2 solves for an equivalent-based route
Worst: k solves when superposition is applied to a k-source problem that only needed one nodal analysis
WHAT THAT MEANS
The worst case is entirely self-inflicted and is the most common exam time loss.
Source: Engineering Circuit Analysis, 8th ed., Ch. 5, pp. 123-154 | CO2 | Bloom L5
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Read the question and identify the single quantity actually required - and check everyone has written it before moving on. At the cost panel, translate it: The worst case is entirely self-inflicted and is the most common exam time loss. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 2: Network Theorems for DC and AC Circuits. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 5, pp. 123-154. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 49
Choosing between theorems: a decision procedure - worked example
One concrete case, carried all the way to a stated number.
VTU BEC303 | Module 2
Choosing between theorems: a decision…
49
GIVEN
A question asks for the power in a load resistor as the load is stepped through 1 kΩ, 2 kΩ and 5 kΩ.
1. A load is being swept, so an equivalent is the right tool
2. Compute V_th and R_th once: two network solves
3. Each load value now costs one divider calculation
4. Total: 2 solves plus 3 trivial evaluations, against 3 full network solves the direct way
RESULT
The Thévenin route is cheaper from the second load value onward, and the margin widens with every additional value requested.
direct : 3 full solves
Thévenin : 2 solves + 3 dividers
break-even at 3 load values
THE MISTAKE STUDENTS MAKE
Students reach for superposition on every multi-source problem because it is the theorem they learned first. If the question wants all the branch currents, superposition requires a full solve per source and then a recombination per branch — several times the work of one nodal analysis.
Source: Engineering Circuit Analysis, 8th ed., Ch. 5, pp. 123-154 | CO2 | Bloom L5
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is A question asks for the power in a load resistor as the load is stepped through 1 kΩ, 2 kΩ and 5 kΩ. Work at the pace of the slowest note-taker and land hard on the result: The Thévenin route is cheaper from the second load value onward, and the margin widens with every additional value requested. Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 2: Network Theorems for DC and AC Circuits. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 5, pp. 123-154. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 50
Verifying a theorem result
What it is, why it works, and what it costs.
VTU BEC303 | Module 2
Verifying a theorem result
50
THE MECHANISM
Every theorem result should be checked, because the failure modes of these methods are silent — a wrong R_th produces a plausible number rather than an obvious contradiction. Three cheap checks catch most errors. A power balance confirms that the total power supplied by the sources equals the total dissipated, computed from the final total responses rather than any partial ones. A limiting case substitutes an extreme load: an open circuit must give V_th at the terminals and a short must give I_N. An independent recomputation by a different route — nodal analysis for a result obtained by Thévenin — is the most expensive check and the most conclusive.
KEY TERMS
• sanity check
• power balance
• limiting case
• independent recomputation
TAKEAWAY
A theorem result that has not been checked against a limiting case is a guess with arithmetic attached.
DIAGRAM FOR PHASE 2
Three check cards arranged in a row, each with a magnifier icon. Card 1 "Power balance": a small bar chart with a supplied bar and a dissipated bar of equal height, joined by an equals sign. Card 2 "Limiting c…
Source: Engineering Circuit Analysis, 8th ed., Ch. 5, pp. 141-152
CO2 | Bloom L5 | visual id: verification-three-checks
Notes: What to say: Give them the idea before the formalism. Say it plainly first: Every theorem result should be checked, because the failure modes of these methods are silent — a wrong R_th produces a plausible number rather than an ob… Then add the part they are examined on - A theorem result that has not been checked against a limiting case is a guess with arithmetic attached. Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "sanity check" constrain here, and what would break if it did not hold? Animation instructions: the three cards flip in left to right, each internal tick or equals sign lighting green after the card settles, then the cost strip slides up. Transition style: Fade [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 2: Network Theorems for DC and AC Circuits. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 5, pp. 141-152. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 51
Verifying a theorem result - how it works
The procedure in order, and what each pass costs you.
VTU BEC303 | Module 2
Verifying a theorem result
51
1. Compute the total response first, never from partial responses
2. Sum the power supplied by all sources and the power dissipated in all resistors
3. Confirm the two sums agree within rounding
4. Substitute an open-circuit load and confirm the terminal voltage equals V_th
5. Substitute a short-circuit load and confirm the current equals I_N
6. If time allows, recompute by an unrelated method
COST AND BEHAVIOUR
Best: O(1) for a limiting-case check
Typical: O(n) for a power balance over n elements
Worst: a second full solve for an independent recomputation
WHAT THAT MEANS
The limiting-case check costs almost nothing and catches the majority of R_th errors.
Source: Engineering Circuit Analysis, 8th ed., Ch. 5, pp. 141-152 | CO2 | Bloom L5
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Compute the total response first, never from partial responses - and check everyone has written it before moving on. At the cost panel, translate it: The limiting-case check costs almost nothing and catches the majority of R_th errors. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 2: Network Theorems for DC and AC Circuits. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 5, pp. 141-152. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 52
Verifying a theorem result - worked example
One concrete case, carried all the way to a stated number.
VTU BEC303 | Module 2
Verifying a theorem result
52
GIVEN
A claimed equivalent of V_th = 7.2 V, R_th = 2.4 kΩ for the divider of an earlier unit.
1. Open-circuit check: equivalent gives 7.2 V; original divider gives 12 × 6/10 = 7.2 V — agrees
2. Short-circuit check: equivalent gives 7.2/2400 = 3 mA
3. Original with terminals shorted: the 6 kΩ is bypassed, so I = 12/4000 = 3 mA — agrees
4. Both limiting cases match, so V_th and R_th are jointly confirmed
RESULT
Both limits agree, which pins down both parameters — a single limiting case would have confirmed only one of them.
open : 7.2 V vs 12·6k/10k = 7.2 V ✓
short: 7.2/2.4k = 3 mA vs 12/4k = 3 mA ✓
THE MISTAKE STUDENTS MAKE
Students check only the open-circuit case, which verifies V_th but leaves R_th completely untested. Two limiting cases are needed because the equivalent has two parameters.
Source: Engineering Circuit Analysis, 8th ed., Ch. 5, pp. 141-152 | CO2 | Bloom L5
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is A claimed equivalent of V_th = 7.2 V, R_th = 2.4 kΩ for the divider of an earlier unit. Work at the pace of the slowest note-taker and land hard on the result: Both limits agree, which pins down both parameters — a single limiting case would have confirmed only one of them. Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 2: Network Theorems for DC and AC Circuits. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 5, pp. 141-152. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 53
One sentence per unit, six months from now
Units 1-7: what survives after the detail has gone.
VTU BEC303 | Module 2
Revision
53
01 Linearity is not a convenience assumption — it is the single hypothesis that makes superposition, Thévenin and reciprocity true at all.
02 Superposition is a diagnostic tool first and a solving method second — use it when you need to know which source caused what.
03 Zeroing a source removes its excitation, never its resistance, and never applies to a dependent source.
04 Different frequencies may only be combined in the time domain — phasors from different ω values are not addable at all.
05 Superpose the response, then square; never square, then superpose.
06 Reciprocity says a passive bilateral network cannot tell which of two ports you are pushing on.
07 Four conditions, all required — and the one students forget is that dependent sources destroy bilaterality.
Notes: What to say: Slow right down here. Read each takeaway aloud and then stop talking for a beat, because these are the sentences that should still be in their heads when they sit the SEE. Tell them explicitly that if they can reconstruct the reasoning behind any one of these lines they understand that unit, and if they can only recite it they do not. Pause cue: Pause for three seconds after each takeaway before moving to the next. Pointing cue: Point at each numbered takeaway in turn as you read it. Question to ask students: Ask: choose the takeaway you trust least and tell me what you would have to check to believe it. Animation instructions: Takeaway rows reveal one at a time from the top, each row highlighting briefly as it appears. Transition style: Fade [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 2: Network Theorems for DC and AC Circuits, 13 hours, Hayt 8e Ch. 5 (5.1, 5.3, 5.4), Ch. 10 (10.7), pp. 123–154 and 397–406; reciprocity from syllabus TB2 (Channa Venkatesh & Ganesh Rao) §4.9. TB1: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012. Revision consolidates all 16 unit takeaways. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 54
Revision, continued
Units 8-14: what survives after the detail has gone.
VTU BEC303 | Module 2
Revision
54
08 Reciprocity is a feature of passive networks and a bug in anything meant to have an input and an output.
09 Thévenin collapses everything behind a port into two numbers, and those two numbers are valid for any load you care to attach.
10 No dependent sources means look back and reduce; dependent sources means apply a test source — there is no third option that is always safe.
11 Thévenin and Norton are the same two facts about a port written in two different notations; choose the one that matches the load.
12 Matching maximises delivered power and caps efficiency at 50 % — those are two different design goals and you may only have one.
13 Match for power when signal power is scarce, match for reflection when the line is long, and mismatch deliberately everywhere else.
14 All the DC theorems survive into AC unchanged except maximum power transfer, which becomes a conjugate match.
Notes: What to say: Slow right down here. Read each takeaway aloud and then stop talking for a beat, because these are the sentences that should still be in their heads when they sit the SEE. Tell them explicitly that if they can reconstruct the reasoning behind any one of these lines they understand that unit, and if they can only recite it they do not. Pause cue: Pause for three seconds after each takeaway before moving to the next. Pointing cue: Point at each numbered takeaway in turn as you read it. Question to ask students: Ask: choose the takeaway you trust least and tell me what you would have to check to believe it. Animation instructions: Takeaway rows reveal one at a time from the top, each row highlighting briefly as it appears. Transition style: Fade [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 2: Network Theorems for DC and AC Circuits, 13 hours, Hayt 8e Ch. 5 (5.1, 5.3, 5.4), Ch. 10 (10.7), pp. 123–154 and 397–406; reciprocity from syllabus TB2 (Channa Venkatesh & Ganesh Rao) §4.9. TB1: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012. Revision consolidates all 16 unit takeaways. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 55
Revision, continued
Units 15-16: what survives after the detail has gone.
VTU BEC303 | Module 2
Revision
55
15 Pick the theorem by what the question asks for, not by what is easiest to recall.
16 A theorem result that has not been checked against a limiting case is a guess with arithmetic attached.
Notes: What to say: Slow right down here. Read each takeaway aloud and then stop talking for a beat, because these are the sentences that should still be in their heads when they sit the SEE. Tell them explicitly that if they can reconstruct the reasoning behind any one of these lines they understand that unit, and if they can only recite it they do not. Pause cue: Pause for three seconds after each takeaway before moving to the next. Pointing cue: Point at each numbered takeaway in turn as you read it. Question to ask students: Ask: choose the takeaway you trust least and tell me what you would have to check to believe it. Animation instructions: Takeaway rows reveal one at a time from the top, each row highlighting briefly as it appears. Transition style: Fade [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 2: Network Theorems for DC and AC Circuits, 13 hours, Hayt 8e Ch. 5 (5.1, 5.3, 5.4), Ch. 10 (10.7), pp. 123–154 and 397–406; reciprocity from syllabus TB2 (Channa Venkatesh & Ganesh Rao) §4.9. TB1: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012. Revision consolidates all 16 unit takeaways. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 56
How this module is assessed
Where the quiz and the assignment live, and what they test.
VTU BEC303 | Module 2
Assessment
56
MODULE 2 QUIZ
quizzes/Module_2_Quiz.pdf
quizzes/Module_2_Quiz.gift
45 minutes | 50 marks | pass 20 | 1 attempt
Part A: 20 MCQs, 1 mark each.
Part B: 13 descriptive questions, 30 marks.
Bloom spread: L1-L2 24%, L3-L4 61%, L5-L6 15%
Every question carries a CO tag, a Bloom level and a chapter reference; distractor feedback names the misconception.
MODULE 2 ASSIGNMENT
assignments/Module_2_Assignment.pdf
Assignment 2 — Applying and bounding the network theorems
20 marks | 10% of CIE | 10 problems + 3 theory items
Submit as PDF, single file, named <USN>_BEC303_Assignment2.pdf, via LMS upload. 10% per day, nothing after 5 days.
Rubric: Correct application of theorems (7); Treatment of validity limits (5); Verification and cross-checking (4); Engineering judgement in the design question (4). Attainment: CO2 = 20.
Previous years' question papers for EC are indexed in pyq/PYQ_Index.pdf; the syllabus extract and the topic-to-slide mapping are in syllabus/Syllabus_Mapping.pdf.
Individual submission. Identical submissions score zero for both parties.
Notes: What to say: Close by telling them exactly where the assessment lives and what it tests. Name the two files, say the mark split out loud, and read the Bloom spread so they understand that roughly a quarter of the paper is not recall at all. Then read the integrity line word for word, because ambiguity there costs students more than any technical error in this module. Pause cue: Pause after the Bloom spread and before the integrity statement. Pointing cue: Point at the quiz panel, then the assignment panel, then the integrity line at the bottom. Question to ask students: Ask: which course outcome do you feel least ready on, and which unit would you reread tonight to fix it? Animation instructions: Quiz panel fades in from the left, then the assignment panel from the right, then the pointers strip appears, then the integrity line fades in last. Transition style: Fade [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 2: Network Theorems for DC and AC Circuits, 13 hours, Hayt 8e Ch. 5 (5.1, 5.3, 5.4), Ch. 10 (10.7), pp. 123–154 and 397–406; reciprocity from syllabus TB2 (Channa Venkatesh & Ganesh Rao) §4.9. TB1: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012. Assessment counts: 20 MCQs, 13 descriptive questions, 13 assignment items. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.