## Slide 1
Network Analysis
Module 3 asks: A switch closes. What does every voltage and current in the circuit do between that instant and settling —…
VTU BEC303 | Module 3
Opening
01
MODULE 3
Transient Behavior and Initial Conditions
14 contact hours | 16 teaching units | 56 slides
PRESCRIBED TEXTBOOK
Engineering Circuit Analysis
W. H. Hayt, J. E. Kemmerly and S. M. Durbin
McGraw-Hill / Tata McGraw-Hill, 8th edition, 2012
Hayt 8e Ch. 7 (7.1, 7.2, 7.7), Ch. 8 (8.1–8.9), Ch. 9 (9.1–9.7), Ch. 10 (10.1–10.7), pp. 217–247, 261–361 and 371–406
Mesh & Nodal Analysis • Network Theorems • Transient Response • Laplace / s-Domain • Two-Port Networks
Storage elements resist instant change → Two continuity rules fix t=0+ → One time constant sets the pace → Second order adds damping choice → Natural plus forced equals complete
EC · Semester 3 · BEC303 · generated for Phase 2 conversion
Notes: What to say: Open by putting the whole module on one page. Tell them this is 14 contact hours and 16 teaching units, and that all of it exists to answer one question: A switch closes. What does every voltage and current in the circuit do between that instant and settling — and how much of it can I write down without solving anything? Name the prescribed textbook out loud and say which chapters they will be living in, so nobody is reading the wrong book by week two. Pause cue: Pause after reading the driving question aloud, before naming the textbook. Pointing cue: Point at the module title block, then at the textbook panel, then run a finger along the five-beat arc. Question to ask students: Ask: before we start, what do you already expect the answer to "A switch closes. What does every voltage and current in the circuit do between that insta…" to look like? Animation instructions: Module title block fades in first, then the textbook panel slides in from the right, then the five arc beats appear left to right one at a time. Transition style: Fade [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 3: Transient Behavior and Initial Conditions, 14 hours, Hayt 8e Ch. 7 (7.1, 7.2, 7.7), Ch. 8 (8.1–8.9), Ch. 9 (9.1–9.7), Ch. 10 (10.1–10.7), pp. 217–247, 261–361 and 371–406. TB1: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 2
What this module is actually for
One question, five beats, and the scope it does not cover.
VTU BEC303 | Module 3
Overview
02
THE DRIVING QUESTION
A switch closes. What does every voltage and current in the circuit do between that instant and settling — and how much of it can I write down without solving anything?
1
Storage elements resist instant change
2
Two continuity rules fix t=0+
3
One time constant sets the pace
4
Second order adds damping choice
5
Natural plus forced equals complete
SCOPE AND PROVENANCE
Built from the syllabus-listed Hayt 8e sections. The organising idea is that the two continuity rules — inductor current and capacitor voltage cannot jump — plus the DC limits at t = ∞ give three of the four things needed for any first-order answer without solving a differential equation at all. Second-order circuits are then presented as the same programme with a damping classification in front of it. Sequentially switched circuits are included because they are where students discover that the final condition of one interval is the initial condition of the next.
Course outcomes exercised: CO3
Assessment: 20 MCQs + 13 descriptive questions + 13 assignment items
Notes: What to say: Give them the map before the territory. Read the driving question once more, then walk the five beats across the slide and say in one sentence what changes between each beat and the next. Finish on the scope paragraph, because knowing what a module does not cover saves more marks than anything else on this slide. Pause cue: Pause for four or five seconds after the five beats appear, before moving to scope. Pointing cue: Point at the driving question panel, then at each numbered beat in turn, then at the scope paragraph. Question to ask students: Ask: which of these five beats do you expect to find hardest, and why that one? Animation instructions: The driving question panel fades in, then the five numbered beats appear left to right one at a time, then the scope paragraph fades in beneath them. Transition style: Fade [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 3: Transient Behavior and Initial Conditions, 14 hours, Hayt 8e Ch. 7 (7.1, 7.2, 7.7), Ch. 8 (8.1–8.9), Ch. 9 (9.1–9.7), Ch. 10 (10.1–10.7), pp. 217–247, 261–361 and 371–406. TB1: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 3
Every unit against its chapter and pages
Units 1-9 of 16, with the deck slides that teach each one.
VTU BEC303 | Module 3
Syllabus mapping
03
# — Teaching unit — Book chapter and pages — Deck slides — CO / Bloom
01 The capacitor: v-i relation, energy and continuity — Ch. 7, pp. 217-225 — slides 5, 6, 7 — CO3 / L2
02 The inductor: v-i relation, energy and continuity — Ch. 7, pp. 225-235 — slides 8, 9, 10 — CO3 / L2
03 Representing elements under switching — Ch. 7, pp. 217-247 — slides 11, 12, 13 — CO3 / L3
04 Evaluating initial conditions at t = 0+ — Ch. 8, pp. 261-268 — slides 14, 15, 16 — CO3 / L3
05 Evaluating final conditions at t = ∞ — Ch. 8, pp. 275-282 — slides 17, 18, 19 — CO3 / L3
06 The source-free RL circuit and the time constant — Ch. 8, pp. 261-268 — slides 20, 21, 22 — CO3 / L3
07 Properties of the exponential response — Ch. 8, pp. 268-272 — slides 23, 24, 25 — CO3 / L3
08 The source-free RC circuit — Ch. 8, pp. 272-275 — slides 26, 27, 28 — CO3 / L3
09 The unit-step function and switched sources — Ch. 8, pp. 282-286 — slides 29, 30, 31 — CO3 / L3
Notes: What to say: Tell them this is the slide to photograph. Every unit in the module is listed against a real chapter and a real page range, so there is no ambiguity about what to read. Point out the slide-number column and say plainly that if they miss a lecture, those are the slides covering that unit. Say that the page ranges come from the book's own table of contents rather than a guess. Pause cue: Pause for ten seconds and let them photograph the table before saying anything else. Pointing cue: Run a finger down the chapter-and-pages column, then across one complete row. Question to ask students: Ask: pick any row - which chapter would you open first, and what would you expect in the first paragraph? Animation instructions: Header row appears first, then the unit rows fade in one at a time from the top, then the chapter-and-pages column highlights. Transition style: Cut [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 3: Transient Behavior and Initial Conditions, 14 hours, Hayt 8e Ch. 7 (7.1, 7.2, 7.7), Ch. 8 (8.1–8.9), Ch. 9 (9.1–9.7), Ch. 10 (10.1–10.7), pp. 217–247, 261–361 and 371–406. TB1: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012. Mapping covers all 16 teaching units. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 4
Syllabus mapping, continued
Units 10-16 of 16, with the deck slides that teach each one.
VTU BEC303 | Module 3
Syllabus mapping
04
# — Teaching unit — Book chapter and pages — Deck slides — CO / Bloom
10 Driven RL circuits: natural and forced response — Ch. 8, pp. 286-295 — slides 32, 33, 34 — CO3 / L4
11 Driven RC circuits and the power-ON delay case study — Ch. 8, pp. 295-300 — slides 35, 36, 37 — CO3 / L5
12 Sequentially switched circuits — Ch. 8, pp. 300-306 — slides 38, 39, 40 — CO3 / L4
13 The source-free parallel RLC and damping classification — Ch. 9, pp. 321-334 — slides 41, 42, 43 — CO3 / L4
14 Critically damped and underdamped responses — Ch. 9, pp. 334-345 — slides 44, 45, 46 — CO3 / L4
15 The source-free series RLC and the complete second-order response — Ch. 9, pp. 345-359 — slides 47, 48, 49 — CO3 / L4
16 Transients under AC excitation and the lossless LC circuit — Ch. 9, pp. 359-361 — slides 50, 51, 52 — CO3 / L5
Notes: What to say: Tell them this is the slide to photograph. Every unit in the module is listed against a real chapter and a real page range, so there is no ambiguity about what to read. Point out the slide-number column and say plainly that if they miss a lecture, those are the slides covering that unit. Say that the page ranges come from the book's own table of contents rather than a guess. Pause cue: Pause for ten seconds and let them photograph the table before saying anything else. Pointing cue: Run a finger down the chapter-and-pages column, then across one complete row. Question to ask students: Ask: pick any row - which chapter would you open first, and what would you expect in the first paragraph? Animation instructions: Header row appears first, then the unit rows fade in one at a time from the top, then the chapter-and-pages column highlights. Transition style: Cut [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 3: Transient Behavior and Initial Conditions, 14 hours, Hayt 8e Ch. 7 (7.1, 7.2, 7.7), Ch. 8 (8.1–8.9), Ch. 9 (9.1–9.7), Ch. 10 (10.1–10.7), pp. 217–247, 261–361 and 371–406. TB1: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012. Mapping covers all 16 teaching units. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 5
The capacitor: v-i relation, energy and continuity
What it is, why it works, and what it costs.
VTU BEC303 | Module 3
The capacitor: v-i relation, energy a…
05
THE MECHANISM
A capacitor relates current to the rate of change of its voltage, i = C·dv/dt, which means current flows only while the voltage is changing. Integrating gives v(t) = v(0) + (1/C)∫i dt, so the capacitor voltage is the accumulated history of its current and therefore cannot jump — a discontinuity in v would demand infinite current. Its stored energy is w = ½Cv², always non-negative, so the capacitor returns energy but never dissipates it. In DC steady state dv/dt is zero, so the current is zero and the capacitor behaves as an open circuit, which is the fact that supplies half of every final-condition calculation.
KEY TERMS
• capacitance
• i = C·dv/dt
• stored energy
• voltage continuity
• DC open circuit
TAKEAWAY
Capacitor voltage is continuous because a jump would need infinite current — that single fact fixes the t = 0+ value.
DIAGRAM FOR PHASE 2
Left: a capacitor symbol with the relation i = C·dv/dt printed beside it and an arrow showing current only while a small v-versus-t ramp is rising. Centre: two stacked waveform panels — the upper shows a smoot…
Source: Engineering Circuit Analysis, 8th ed., Ch. 7, pp. 217-225
CO3 | Bloom L2 | visual id: capacitor-continuity-panel
Notes: What to say: Give them the idea before the formalism. Say it plainly first: A capacitor relates current to the rate of change of its voltage, i = C·dv/dt, which means current flows only while the voltage is changing. Then add the part they are examined on - Capacitor voltage is continuous because a jump would need infinite current — that single fact fixes the t = 0+ value. Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "capacitance" constrain here, and what would break if it did not hold? Animation instructions: the symbol and relation fade in, the v(t) curve draws through the dashed switching line, then i(t) draws showing its step, then the red impossible-jump inset appears, then the two right-hand badges drop in. Transition style: Fade [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 3: Transient Behavior and Initial Conditions. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 7, pp. 217-225. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 6
The capacitor: v-i relation, energy and continuity - how it works
The procedure in order, and what each pass costs you.
VTU BEC303 | Module 3
The capacitor: v-i relation, energy a…
06
1. Write i = C·dv/dt for every capacitor
2. At any switching instant, carry v(0−) forward to v(0+) unchanged
3. Allow the capacitor current to step discontinuously
4. In DC steady state, replace the capacitor by an open circuit
5. Compute stored energy as ½Cv² from the voltage, never from the current
COST AND BEHAVIOUR
Best: O(1) — the continuity rule needs no computation
Typical: one integration per interval
Worst: one integration per switching interval in a sequentially switched circuit
WHAT THAT MEANS
The continuity rule is free information and should always be extracted before any equation is written.
Source: Engineering Circuit Analysis, 8th ed., Ch. 7, pp. 217-225 | CO3 | Bloom L2
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Write i = C·dv/dt for every capacitor - and check everyone has written it before moving on. At the cost panel, translate it: The continuity rule is free information and should always be extracted before any equation is written. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 3: Transient Behavior and Initial Conditions. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 7, pp. 217-225. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 7
The capacitor: v-i relation, energy and continuity - worked example
One concrete case, carried all the way to a stated number.
VTU BEC303 | Module 3
The capacitor: v-i relation, energy a…
07
GIVEN
A 10 µF capacitor charged to 5 V is suddenly connected across a 1 kΩ resistor at t = 0.
1. v(0−) = 5 V, so by continuity v(0+) = 5 V
2. The resistor now sees 5 V, so i(0+) = 5/1000 = 5 mA
3. Before the switch, i(0−) = 0
4. Stored energy at t = 0: w = ½ × 10e−6 × 25 = 125 µJ
RESULT
Voltage is continuous at 5 V while current jumps from 0 to 5 mA — exactly the asymmetry the element definition predicts.
i = C dv/dt, v(t) = v(0) + (1/C)∫i dt
v(0+) = v(0−) = 5 V
i(0+) = 5/1k = 5 mA (jumps), w = ½Cv² = 125 µJ
THE MISTAKE STUDENTS MAKE
Students assume the capacitor current is also continuous, by analogy with the voltage. Only the voltage is constrained; the current is free to step, and in a switched circuit it almost always does.
Source: Engineering Circuit Analysis, 8th ed., Ch. 7, pp. 217-225 | CO3 | Bloom L2
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is A 10 µF capacitor charged to 5 V is suddenly connected across a 1 kΩ resistor at t = 0. Work at the pace of the slowest note-taker and land hard on the result: Voltage is continuous at 5 V while current jumps from 0 to 5 mA — exactly the asymmetry the element definition predicts. Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 3: Transient Behavior and Initial Conditions. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 7, pp. 217-225. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 8
The inductor: v-i relation, energy and continuity
What it is, why it works, and what it costs.
VTU BEC303 | Module 3
The inductor: v-i relation, energy an…
08
THE MECHANISM
An inductor relates voltage to the rate of change of its current, v = L·di/dt, so voltage appears only while the current is changing. Integrating gives i(t) = i(0) + (1/L)∫v dt, so the inductor current is the accumulated history of its voltage and cannot jump — a discontinuity would demand infinite voltage, which is precisely why opening an inductive circuit produces an arc. Stored energy is w = ½Li², again non-negative and recoverable. In DC steady state di/dt is zero, so no voltage appears and the inductor behaves as a short circuit, supplying the other half of every final-condition calculation.
KEY TERMS
• inductance
• v = L·di/dt
• flux linkage
• current continuity
• DC short circuit
TAKEAWAY
Inductor current is continuous because a jump would need infinite voltage — and the arc across an opening switch is that physics made visible.
DIAGRAM FOR PHASE 2
Left: an inductor coil symbol with v = L·di/dt printed beside it. Centre: two stacked waveform panels — the upper shows a continuous i(t) through a vertical dashed switching line at t = 0, the lower shows v(t)…
Source: Engineering Circuit Analysis, 8th ed., Ch. 7, pp. 225-235
CO3 | Bloom L2 | visual id: inductor-continuity-panel
Notes: What to say: Give them the idea before the formalism. Say it plainly first: An inductor relates voltage to the rate of change of its current, v = L·di/dt, so voltage appears only while the current is changing. Then add the part they are examined on - Inductor current is continuous because a jump would need infinite voltage — and the arc across an opening switch is that phy… Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "inductance" constrain here, and what would break if it did not hold? Animation instructions: symbol and relation fade in, i(t) draws through the dashed line, v(t) draws showing its step, then the switch-arc inset flashes, then the two badges drop in. Transition style: Fade [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 3: Transient Behavior and Initial Conditions. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 7, pp. 225-235. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 9
The inductor: v-i relation, energy and continuity - how it works
The procedure in order, and what each pass costs you.
VTU BEC303 | Module 3
The inductor: v-i relation, energy an…
09
1. Write v = L·di/dt for every inductor
2. At any switching instant, carry i(0−) forward to i(0+) unchanged
3. Allow the inductor voltage to step discontinuously
4. In DC steady state, replace the inductor by a short circuit
5. Provide a freewheeling path before opening any inductive branch
COST AND BEHAVIOUR
Best: O(1) for the continuity rule
Typical: one integration per interval
Worst: one per switching interval
WHAT THAT MEANS
The arc problem is an engineering consequence, not a modelling artefact — real designs add a diode.
Source: Engineering Circuit Analysis, 8th ed., Ch. 7, pp. 225-235 | CO3 | Bloom L2
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Write v = L·di/dt for every inductor - and check everyone has written it before moving on. At the cost panel, translate it: The arc problem is an engineering consequence, not a modelling artefact — real designs add a diode. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 3: Transient Behavior and Initial Conditions. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 7, pp. 225-235. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 10
The inductor: v-i relation, energy and continuity - worked example
One concrete case, carried all the way to a stated number.
VTU BEC303 | Module 3
The inductor: v-i relation, energy an…
10
GIVEN
A 2 H inductor carrying 3 A in a DC loop is suddenly switched to a 100 Ω resistor at t = 0.
1. i(0−) = 3 A, so by continuity i(0+) = 3 A
2. The resistor must carry that same 3 A immediately
3. v(0+) = 3 × 100 = 300 V across the resistor
4. Stored energy: w = ½ × 2 × 9 = 9 J
RESULT
The current is continuous at 3 A but the voltage jumps to 300 V — three times the original supply would typically be, which is why inductive switching destroys unprotected contacts.
v = L di/dt, i(t) = i(0) + (1/L)∫v dt
i(0+) = i(0−) = 3 A
v(0+) = 3·100 = 300 V (jumps), w = ½Li² = 9 J
THE MISTAKE STUDENTS MAKE
Students treat an inductor as an open circuit immediately after switching because "no current has had time to build up". The opposite is true: whatever current was flowing keeps flowing, and the inductor acts momentarily as a current source of value i(0−).
Source: Engineering Circuit Analysis, 8th ed., Ch. 7, pp. 225-235 | CO3 | Bloom L2
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is A 2 H inductor carrying 3 A in a DC loop is suddenly switched to a 100 Ω resistor at t = 0. Work at the pace of the slowest note-taker and land hard on the result: The current is continuous at 3 A but the voltage jumps to 300 V — three times the original supply would typically be, which is wh… Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 3: Transient Behavior and Initial Conditions. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 7, pp. 225-235. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 11
Representing elements under switching
What it is, why it works, and what it costs.
VTU BEC303 | Module 3
Representing elements under switching
11
THE MECHANISM
Switching analysis is made routine by replacing each storage element with a resistive equivalent valid at the instant in question. At t = 0+, a capacitor with initial voltage V₀ is drawn as an ideal voltage source of V₀ — a short if V₀ = 0 — and an inductor with initial current I₀ is drawn as an ideal current source of I₀ — an open if I₀ = 0. At t = ∞ under DC excitation, the capacitor becomes an open circuit and the inductor a short. Each replacement turns a differential-equation problem into a purely resistive one that can be solved by the Module 1 methods, which is why initial and final conditions can be found without ever writing the differential equation. Circuit simulators encode exactly these models internally.
KEY TERMS
• equivalent at t=0+
• equivalent at t=∞
• initial-condition source
• simulation model
TAKEAWAY
Two resistive snapshots — one at t = 0+ and one at t = ∞ — give you the endpoints of every transient for free.
DIAGRAM FOR PHASE 2
A two-column, two-row grid. Column headers: "t = 0+" and "t = ∞ (DC)". Row 1 "Capacitor": left cell shows a battery symbol labelled V₀ with a note "short if V₀ = 0", right cell shows a break in the wire labell…
Source: Engineering Circuit Analysis, 8th ed., Ch. 7, pp. 217-247
CO3 | Bloom L3 | visual id: switching-equivalents-table
Notes: What to say: Give them the idea before the formalism. Say it plainly first: Switching analysis is made routine by replacing each storage element with a resistive equivalent valid at the instant in question. Then add the part they are examined on - Two resistive snapshots — one at t = 0+ and one at t = ∞ — give you the endpoints of every transient for free. Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "equivalent at t=0+" constrain here, and what would break if it did not hold? Animation instructions: the grid outline draws, the four cells populate row by row, then the three circuit snapshots appear left to right with the substitution animating in each. Transition style: Fade [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 3: Transient Behavior and Initial Conditions. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 7, pp. 217-247. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 12
Representing elements under switching - how it works
The procedure in order, and what each pass costs you.
VTU BEC303 | Module 3
Representing elements under switching
12
1. Solve the circuit for t < 0 in DC steady state to obtain v_C(0−) and i_L(0−)
2. Apply continuity to get v_C(0+) and i_L(0+)
3. Redraw at t = 0+ with capacitors as V₀ sources and inductors as I₀ sources
4. Solve that resistive circuit for every other initial value
5. Redraw at t = ∞ with capacitors open and inductors short
6. Solve that resistive circuit for every final value
COST AND BEHAVIOUR
Best: two trivial resistive solves
Typical: three resistive solves — before, at 0+, and at ∞
Worst: three solves per switching interval
WHAT THAT MEANS
Far cheaper than solving the differential equation, and it supplies the boundary conditions the equation would need anyway.
Source: Engineering Circuit Analysis, 8th ed., Ch. 7, pp. 217-247 | CO3 | Bloom L3
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Solve the circuit for t < 0 in DC steady state to obtain v_C(0−) and i_L(0−) - and check everyone has written it before moving on. At the cost panel, translate it: Far cheaper than solving the differential equation, and it supplies the boundary conditions the equation would need anyway. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 3: Transient Behavior and Initial Conditions. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 7, pp. 217-247. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 13
Representing elements under switching - worked example
One concrete case, carried all the way to a stated number.
VTU BEC303 | Module 3
Representing elements under switching
13
GIVEN
A 12 V source, 4 kΩ in series, and a 1 µF capacitor to ground; the switch closes at t = 0 with the capacitor initially uncharged.
1. t < 0: capacitor uncharged, so v_C(0−) = 0
2. t = 0+: capacitor replaced by a short, so v_C(0+) = 0 and i(0+) = 12/4000 = 3 mA
3. t = ∞: capacitor replaced by an open, so i(∞) = 0
4. v_C(∞) = 12 V since no current means no drop across the 4 kΩ
RESULT
Current falls from 3 mA to 0 while the capacitor voltage rises from 0 to 12 V — both endpoints obtained without a differential equation.
t=0+ : C → short (V₀=0) ⇒ i = 12/4k = 3 mA
t=∞ : C → open ⇒ i = 0, v_C = 12 V
THE MISTAKE STUDENTS MAKE
Students apply the t = ∞ equivalents at t = 0+, opening the capacitor immediately after the switch closes. That gives zero initial current, which is exactly backwards — an uncharged capacitor is a short at the first instant, not an open.
Source: Engineering Circuit Analysis, 8th ed., Ch. 7, pp. 217-247 | CO3 | Bloom L3
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is A 12 V source, 4 kΩ in series, and a 1 µF capacitor to ground; the switch closes at t = 0 with the capacitor initially uncharged. Work at the pace of the slowest note-taker and land hard on the result: Current falls from 3 mA to 0 while the capacitor voltage rises from 0 to 12 V — both endpoints obtained without a differential eq… Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 3: Transient Behavior and Initial Conditions. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 7, pp. 217-247. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 14
Evaluating initial conditions at t = 0+
What it is, why it works, and what it costs.
VTU BEC303 | Module 3
Evaluating initial conditions at t =…
14
THE MECHANISM
The full initial-condition procedure has three stages. First, solve the circuit at t = 0− in DC steady state to find v_C(0−) and i_L(0−) — these are the only two quantities that carry across the switching instant. Second, apply continuity to get v_C(0+) and i_L(0+). Third, redraw at t = 0+ with the storage elements replaced by their initial-condition sources and solve the resulting resistive circuit for every other quantity, all of which may have jumped. For a second-order problem a fourth stage is needed: the derivatives at 0+ are obtained from the element laws themselves, i_C(0+)/C giving dv_C/dt and v_L(0+)/L giving di_L/dt.
KEY TERMS
• t = 0−
• t = 0+
• continuity rules
• derivative initial conditions
TAKEAWAY
Only two quantities survive the switch; everything else at t = 0+ is computed from them by ordinary resistive analysis.
DIAGRAM FOR PHASE 2
A four-stage horizontal pipeline with arrows. Stage 1 box "t = 0− DC solve" outputs two tokens labelled v_C(0−) and i_L(0−). Stage 2 box "continuity" passes only those two tokens through a narrow gate, with al…
Source: Engineering Circuit Analysis, 8th ed., Ch. 8, pp. 261-268
CO3 | Bloom L3 | visual id: initial-conditions-pipeline
Notes: What to say: Give them the idea before the formalism. Say it plainly first: The full initial-condition procedure has three stages. Then add the part they are examined on - Only two quantities survive the switch; everything else at t = 0+ is computed from them by ordinary resistive analysis. Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "t = 0−" constrain here, and what would break if it did not hold? Animation instructions: stages light up left to right; at stage 2 the two surviving tokens pass through while the rejected ones visibly bounce; stage 3 fans out its outputs; stage 4 appears last. Transition style: Fade [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 3: Transient Behavior and Initial Conditions. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 8, pp. 261-268. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 15
Evaluating initial conditions at t = 0+ - how it works
The procedure in order, and what each pass costs you.
VTU BEC303 | Module 3
Evaluating initial conditions at t =…
15
1. Redraw the circuit as it stood for t < 0 and solve it in DC steady state
2. Record v_C(0−) for every capacitor and i_L(0−) for every inductor
3. Set v_C(0+) = v_C(0−) and i_L(0+) = i_L(0−)
4. Redraw at t = 0+ with the new switch position and initial-condition sources
5. Solve that resistive circuit for all remaining voltages and currents
6. If second order, compute the derivatives from i_C(0+)/C and v_L(0+)/L
COST AND BEHAVIOUR
Best: two resistive solves
Typical: two solves plus two derivative evaluations
Worst: a solve per storage element in a chained network
WHAT THAT MEANS
Each stage is purely resistive, so the total cost is far below a direct differential solution.
Source: Engineering Circuit Analysis, 8th ed., Ch. 8, pp. 261-268 | CO3 | Bloom L3
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Redraw the circuit as it stood for t < 0 and solve it in DC steady state - and check everyone has written it before moving on. At the cost panel, translate it: Each stage is purely resistive, so the total cost is far below a direct differential solution. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 3: Transient Behavior and Initial Conditions. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 8, pp. 261-268. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 16
Evaluating initial conditions at t = 0+ - worked example
One concrete case, carried all the way to a stated number.
VTU BEC303 | Module 3
Evaluating initial conditions at t =…
16
GIVEN
A 20 V source with 5 Ω and a 2 H inductor in series has been closed for a long time; at t = 0 a 15 Ω resistor is switched in series with the inductor.
1. t = 0−: inductor is a short in DC, so i_L(0−) = 20/5 = 4 A
2. Continuity: i_L(0+) = 4 A
3. t = 0+: the loop now has 5 + 15 = 20 Ω carrying 4 A
4. KVL: v_L(0+) = 20 − 4 × 20 = −60 V, so di_L/dt(0+) = −60/2 = −30 A/s
RESULT
The current holds at 4 A but the inductor voltage jumps to −60 V and the current begins falling at 30 A/s.
i_L(0−) = 20/5 = 4 A ⇒ i_L(0+) = 4 A
v_L(0+) = 20 − 4(20) = −60 V
di_L/dt(0+) = v_L(0+)/L = −30 A/s
THE MISTAKE STUDENTS MAKE
Students carry a resistor current or a node voltage across the switching instant along with the state variables. Only capacitor voltage and inductor current are continuous; every other quantity must be recomputed at t = 0+ from the new topology.
Source: Engineering Circuit Analysis, 8th ed., Ch. 8, pp. 261-268 | CO3 | Bloom L3
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is A 20 V source with 5 Ω and a 2 H inductor in series has been closed for a long time; at t = 0 a 15 Ω resistor is switched in series with th… Work at the pace of the slowest note-taker and land hard on the result: The current holds at 4 A but the inductor voltage jumps to −60 V and the current begins falling at 30 A/s. Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 3: Transient Behavior and Initial Conditions. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 8, pp. 261-268. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 17
Evaluating final conditions at t = ∞
What it is, why it works, and what it costs.
VTU BEC303 | Module 3
Evaluating final conditions at t = ∞
17
THE MECHANISM
Final conditions describe the circuit once all transients have decayed, which for a DC excitation means every derivative is zero. Capacitors become open circuits, inductors become short circuits, and what remains is a purely resistive network solved by ordinary means. For a sinusoidal excitation the final condition is not a constant but an AC steady state, found by phasor analysis at the source frequency — the transient decays and leaves the forced sinusoidal response behind. The distinction matters because students trained only on DC switching will wrongly report a final value of zero for a circuit that settles into a continuing oscillation.
KEY TERMS
• steady state
• DC final value
• AC steady state
• settled response
TAKEAWAY
Final condition means the transient has died, not that the circuit has stopped — under AC excitation the steady state is itself a waveform.
DIAGRAM FOR PHASE 2
Two stacked time plots sharing a common time axis with a shaded "transient" band on the left third. Upper plot "DC excitation": the response rises and flattens to a horizontal line labelled "constant final val…
Source: Engineering Circuit Analysis, 8th ed., Ch. 8, pp. 275-282
CO3 | Bloom L3 | visual id: final-condition-two-cases
Notes: What to say: Give them the idea before the formalism. Say it plainly first: Final conditions describe the circuit once all transients have decayed, which for a DC excitation means every derivative is zero. Then add the part they are examined on - Final condition means the transient has died, not that the circuit has stopped — under AC excitation the steady state is its… Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "steady state" constrain here, and what would break if it did not hold? Animation instructions: the shared axis draws, the DC curve traces and flattens with its inset appearing, then the AC curve traces and settles into oscillation with its inset appearing, then the 5τ line drops last. Transition style: Fade [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 3: Transient Behavior and Initial Conditions. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 8, pp. 275-282. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 18
Evaluating final conditions at t = ∞ - how it works
The procedure in order, and what each pass costs you.
VTU BEC303 | Module 3
Evaluating final conditions at t = ∞
18
1. Confirm the excitation type — DC, AC, or none
2. For DC, replace capacitors by opens and inductors by shorts
3. Solve the remaining resistive network for all final values
4. For AC, convert to impedances at the source frequency
5. Solve the phasor circuit for the steady-state waveform
6. For a source-free circuit, the final value of every quantity is zero
COST AND BEHAVIOUR
Best: one resistive solve for DC
Typical: one resistive or one phasor solve
Worst: one phasor solve per frequency present
WHAT THAT MEANS
Always cheaper than integrating the transient forward in time.
Source: Engineering Circuit Analysis, 8th ed., Ch. 8, pp. 275-282 | CO3 | Bloom L3
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Confirm the excitation type — DC, AC, or none - and check everyone has written it before moving on. At the cost panel, translate it: Always cheaper than integrating the transient forward in time. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 3: Transient Behavior and Initial Conditions. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 8, pp. 275-282. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 19
Evaluating final conditions at t = ∞ - worked example
One concrete case, carried all the way to a stated number.
VTU BEC303 | Module 3
Evaluating final conditions at t = ∞
19
GIVEN
A 12 V source with 4 kΩ and a capacitor to ground; then the same circuit driven by 12·cos(1000t) V with C = 1 µF.
1. DC case: C is open, so i(∞) = 0 and v_C(∞) = 12 V
2. AC case: Z_C = 1/(j·1000·1e−6) = −j1000 Ω
3. Z_total = 4000 − j1000 = 4123∠−14.04° Ω
4. V_C = 12∠0° × 1000∠−90°/4123∠−14.04° = 2.91∠−75.96° V
RESULT
The DC case settles at a constant 12 V; the AC case settles into a continuing 2.91 V sinusoid lagging by 75.96°.
DC : C open ⇒ v_C(∞) = 12 V
AC : Z_C = −j1000, v_C(t) = 2.91 cos(1000t − 75.96°) V
THE MISTAKE STUDENTS MAKE
Students report "final value = 0" for any circuit whose transient decays. Zero is correct only for a source-free circuit; a driven circuit settles into whatever its forced response is, which under AC excitation is a sinusoid of constant amplitude.
Source: Engineering Circuit Analysis, 8th ed., Ch. 8, pp. 275-282 | CO3 | Bloom L3
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is A 12 V source with 4 kΩ and a capacitor to ground; then the same circuit driven by 12·cos(1000t) V with C = 1 µF. Work at the pace of the slowest note-taker and land hard on the result: The DC case settles at a constant 12 V; the AC case settles into a continuing 2.91 V sinusoid lagging by 75.96°. Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 3: Transient Behavior and Initial Conditions. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 8, pp. 275-282. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 20
The source-free RL circuit and the time constant
What it is, why it works, and what it costs.
VTU BEC303 | Module 3
The source-free RL circuit and the ti…
20
THE MECHANISM
With its source removed, an RL loop obeys L·di/dt + R·i = 0, whose solution is i(t) = i(0)·e^(−Rt/L). The quantity τ = L/R has units of seconds and is the time constant: it is the time for the current to fall to 1/e, about 36.8 %, of its initial value. The entire response is fixed by two numbers — the initial current and τ — and nothing else about the circuit matters. Physically the inductor's stored energy ½Li² is being dissipated in R, so a larger R drains it faster and a larger L stores more and lasts longer.
KEY TERMS
• natural response
• time constant τ = L/R
• exponential decay
• initial energy
TAKEAWAY
Two numbers, i(0) and τ = L/R, determine the entire source-free RL response for all time.
DIAGRAM FOR PHASE 2
A decaying exponential curve of i(t) from i(0) to zero. Vertical dashed lines at t = τ, 2τ, 3τ, 4τ, 5τ, each meeting the curve at a dot annotated with the remaining percentage: 36.8 %, 13.5 %, 5.0 %, 1.8 %, 0.…
Source: Engineering Circuit Analysis, 8th ed., Ch. 8, pp. 261-268
CO3 | Bloom L3 | visual id: rl-decay-tau
Notes: What to say: Give them the idea before the formalism. Say it plainly first: With its source removed, an RL loop obeys L·di/dt + R·i = 0, whose solution is i(t) = i(0)·e^(−Rt/L). Then add the part they are examined on - Two numbers, i(0) and τ = L/R, determine the entire source-free RL response for all time. Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "natural response" constrain here, and what would break if it did not hold? Animation instructions: the curve draws left to right, then the five dashed lines drop in sequence with their percentage labels, then the initial tangent sweeps down to the axis, then the side box with the two comparison curves fades in. Transition style: Fade [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 3: Transient Behavior and Initial Conditions. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 8, pp. 261-268. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 21
The source-free RL circuit and the time constant - how it works
The procedure in order, and what each pass costs you.
VTU BEC303 | Module 3
The source-free RL circuit and the ti…
21
1. Find i_L(0−) from the DC steady state before switching
2. Apply continuity: i(0+) = i(0−)
3. Identify the resistance R seen by the inductor after switching
4. Compute τ = L/R
5. Write i(t) = i(0)·e^(−t/τ)
6. Obtain any other quantity from this current by Ohm's law or v = L·di/dt
COST AND BEHAVIOUR
Best: O(1) once R and i(0) are known
Typical: one resistive solve for R plus one for i(0)
Worst: a Thévenin reduction to find the R seen by the inductor
WHAT THAT MEANS
Settling to within 1 % takes about 5τ, which is the standard engineering rule.
Source: Engineering Circuit Analysis, 8th ed., Ch. 8, pp. 261-268 | CO3 | Bloom L3
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Find i_L(0−) from the DC steady state before switching - and check everyone has written it before moving on. At the cost panel, translate it: Settling to within 1 % takes about 5τ, which is the standard engineering rule. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 3: Transient Behavior and Initial Conditions. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 8, pp. 261-268. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 22
The source-free RL circuit and the time constant - worked example
One concrete case, carried all the way to a stated number.
VTU BEC303 | Module 3
The source-free RL circuit and the ti…
22
GIVEN
L = 2 H carrying 4 A at t = 0, discharging through a total of 20 Ω.
1. τ = L/R = 2/20 = 0.1 s
2. i(t) = 4·e^(−t/0.1) = 4·e^(−10t) A
3. At t = 0.1 s: i = 4 × 0.368 = 1.47 A
4. At t = 0.5 s = 5τ: i = 4 × 0.0067 = 27 mA, i.e. 0.7 % remaining
RESULT
The current falls from 4 A to 27 mA in half a second, and the 5τ rule correctly predicts that the circuit is essentially settled by then.
τ = L/R = 2/20 = 0.1 s
i(t) = 4 e^{−10t} A
i(τ) = 1.47 A, i(5τ) = 27 mA
THE MISTAKE STUDENTS MAKE
Students use the resistance that was in the circuit before switching. τ depends on the resistance the inductor sees after switching, which is frequently a different network entirely — and getting it wrong scales the whole time axis.
Source: Engineering Circuit Analysis, 8th ed., Ch. 8, pp. 261-268 | CO3 | Bloom L3
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is L = 2 H carrying 4 A at t = 0, discharging through a total of 20 Ω. Work at the pace of the slowest note-taker and land hard on the result: The current falls from 4 A to 27 mA in half a second, and the 5τ rule correctly predicts that the circuit is essentially settled… Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 3: Transient Behavior and Initial Conditions. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 8, pp. 261-268. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 23
Properties of the exponential response
What it is, why it works, and what it costs.
VTU BEC303 | Module 3
Properties of the exponential response
23
THE MECHANISM
The exponential e^(−t/τ) has three properties worth knowing by heart. Its initial tangent reaches zero at exactly t = τ, which gives a graphical way to read a time constant off an oscilloscope trace. It falls to 36.8 %, 13.5 %, 5 %, 1.8 % and 0.7 % at one through five time constants, so 5τ is the conventional settling criterion. And it is memoryless in the sense that the fractional decay over any interval depends only on the interval length, not on where that interval starts — the current always falls to 36.8 % of whatever it was, one time constant later. Plotted on a logarithmic vertical axis the decay becomes a straight line whose slope is −1/τ, which is how time constants are extracted from measured data.
KEY TERMS
• 1/e rule
• initial slope
• 5τ settling
• memoryless decay
• semilog straight line
TAKEAWAY
The decay has no memory of where it started — every τ removes the same fraction, which is why a semilog plot straightens it.
DIAGRAM FOR PHASE 2
Three linked panels. Panel 1 "Initial tangent": the decay curve with a straight tangent from the start point meeting the axis at τ. Panel 2 "Memoryless": the same curve with two equal-width shaded intervals at…
Source: Engineering Circuit Analysis, 8th ed., Ch. 8, pp. 268-272
CO3 | Bloom L3 | visual id: exponential-properties-triple
Notes: What to say: Give them the idea before the formalism. Say it plainly first: The exponential e^(−t/τ) has three properties worth knowing by heart. Then add the part they are examined on - The decay has no memory of where it started — every τ removes the same fraction, which is why a semilog plot straightens it. Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "1/e rule" constrain here, and what would break if it did not hold? Animation instructions: panel 1 draws its curve then its tangent; panel 2 highlights the two intervals in turn and then the double arrow connects them; panel 3 morphs the curve into the straight line and the slope annotation appears. Transition style: Fade [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 3: Transient Behavior and Initial Conditions. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 8, pp. 268-272. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 24
Properties of the exponential response - how it works
The procedure in order, and what each pass costs you.
VTU BEC303 | Module 3
Properties of the exponential response
24
1. Read the initial value from the trace
2. Draw the tangent at t = 0 and find where it meets the axis — that is τ
3. Alternatively find the time to fall to 36.8 % of the initial value
4. Alternatively plot on a logarithmic axis and take the slope as −1/τ
5. Use 5τ as the settling time for a 1 % criterion
COST AND BEHAVIOUR
Best: O(1) graphical reading
Typical: O(n) least-squares fit on a semilog plot for n samples
Worst: O(n) with noise rejection
WHAT THAT MEANS
The semilog fit is the robust method when measurement noise is present.
Source: Engineering Circuit Analysis, 8th ed., Ch. 8, pp. 268-272 | CO3 | Bloom L3
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Read the initial value from the trace - and check everyone has written it before moving on. At the cost panel, translate it: The semilog fit is the robust method when measurement noise is present. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 3: Transient Behavior and Initial Conditions. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 8, pp. 268-272. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 25
Properties of the exponential response - worked example
One concrete case, carried all the way to a stated number.
VTU BEC303 | Module 3
Properties of the exponential response
25
GIVEN
A measured decay falls from 10 V to 3.68 V in 4 ms.
1. 3.68/10 = 0.368, which is exactly 1/e
2. Therefore 4 ms is one time constant, τ = 4 ms
3. Settling to 1 % requires about 5τ = 20 ms
4. Value after 8 ms (2τ) = 10 × 0.135 = 1.35 V
RESULT
τ = 4 ms and the circuit is settled by 20 ms — both read directly off the trace without knowing R or C at all.
v(τ)/v(0) = 1/e = 0.368
4 ms → τ = 4 ms
settle ≈ 5τ = 20 ms, v(2τ) = 1.35 V
THE MISTAKE STUDENTS MAKE
Students describe the response as finishing at 5τ. It never reaches zero exactly; 5τ is a 0.7 % convention, and in a precision circuit — a 12-bit converter, say — settling to half an LSB requires closer to 9τ.
Source: Engineering Circuit Analysis, 8th ed., Ch. 8, pp. 268-272 | CO3 | Bloom L3
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is A measured decay falls from 10 V to 3.68 V in 4 ms. Work at the pace of the slowest note-taker and land hard on the result: τ = 4 ms and the circuit is settled by 20 ms — both read directly off the trace without knowing R or C at all. Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 3: Transient Behavior and Initial Conditions. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 8, pp. 268-272. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 26
The source-free RC circuit
What it is, why it works, and what it costs.
VTU BEC303 | Module 3
The source-free RC circuit
26
THE MECHANISM
A charged capacitor discharging through a resistor obeys RC·dv/dt + v = 0, giving v(t) = v(0)·e^(−t/RC) with time constant τ = RC. The structure is the exact dual of the RL case: where the inductor kept its current and needed a small R to last, the capacitor keeps its voltage and needs a large R to last. All the exponential properties carry across unchanged. The total energy dissipated over all time equals the energy initially stored, ½Cv(0)², regardless of the value of R — R sets how fast the energy leaves, never how much.
KEY TERMS
• τ = RC
• capacitor discharge
• duality with RL
• energy dissipation
TAKEAWAY
RC and RL are duals: swap v for i and R for 1/R and every result maps across.
DIAGRAM FOR PHASE 2
A vertical mirror line down the centre. Left side "RC": a capacitor discharging through R, with the equation RC·dv/dt + v = 0, τ = RC, and a decaying v(t) curve. Right side "RL": an inductor decaying through R…
Source: Engineering Circuit Analysis, 8th ed., Ch. 8, pp. 272-275
CO3 | Bloom L3 | visual id: rc-rl-duality-mirror
Notes: What to say: Give them the idea before the formalism. Say it plainly first: A charged capacitor discharging through a resistor obeys RC·dv/dt + v = 0, giving v(t) = v(0)·e^(−t/RC) with time constant τ = RC. Then add the part they are examined on - RC and RL are duals: swap v for i and R for 1/R and every result maps across. Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "τ = RC" constrain here, and what would break if it did not hold? Animation instructions: the mirror line draws, the left side builds top to bottom, then each right-side item appears as its tie line sweeps across, then the footer note fades in. Transition style: Fade [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 3: Transient Behavior and Initial Conditions. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 8, pp. 272-275. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 27
The source-free RC circuit - how it works
The procedure in order, and what each pass costs you.
VTU BEC303 | Module 3
The source-free RC circuit
27
1. Find v_C(0−) from the DC steady state before switching
2. Apply continuity: v(0+) = v(0−)
3. Identify the resistance R the capacitor sees after switching
4. Compute τ = RC
5. Write v(t) = v(0)·e^(−t/τ)
6. Obtain the current from i = −C·dv/dt or from v/R
COST AND BEHAVIOUR
Best: O(1) once R and v(0) are known
Typical: one resistive solve for R
Worst: a Thévenin reduction seen from the capacitor terminals
WHAT THAT MEANS
Identical cost structure to the RL case by duality.
Source: Engineering Circuit Analysis, 8th ed., Ch. 8, pp. 272-275 | CO3 | Bloom L3
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Find v_C(0−) from the DC steady state before switching - and check everyone has written it before moving on. At the cost panel, translate it: Identical cost structure to the RL case by duality. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 3: Transient Behavior and Initial Conditions. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 8, pp. 272-275. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 28
The source-free RC circuit - worked example
One concrete case, carried all the way to a stated number.
VTU BEC303 | Module 3
The source-free RC circuit
28
GIVEN
A 10 µF capacitor charged to 5 V discharges through 1 kΩ.
1. τ = RC = 1000 × 10e−6 = 10 ms
2. v(t) = 5·e^(−t/0.01) V
3. i(t) = v/R = 5e^(−100t)/1000 = 5·e^(−100t) mA
4. Energy dissipated over all time = ½ × 10e−6 × 25 = 125 µJ
RESULT
τ = 10 ms, initial current 5 mA, and the full 125 µJ ends up in the resistor no matter what value R takes.
τ = RC = 1k · 10µ = 10 ms
v(t) = 5 e^{−100t} V, i(t) = 5 e^{−100t} mA
∫p dt = ½Cv(0)² = 125 µJ
THE MISTAKE STUDENTS MAKE
Students expect a larger resistor to dissipate more total energy because it has more resistance. The total is fixed by the stored energy alone; a larger R simply spreads the same joules over a longer time at lower power.
Source: Engineering Circuit Analysis, 8th ed., Ch. 8, pp. 272-275 | CO3 | Bloom L3
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is A 10 µF capacitor charged to 5 V discharges through 1 kΩ. Work at the pace of the slowest note-taker and land hard on the result: τ = 10 ms, initial current 5 mA, and the full 125 µJ ends up in the resistor no matter what value R takes. Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 3: Transient Behavior and Initial Conditions. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 8, pp. 272-275. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 29
The unit-step function and switched sources
What it is, why it works, and what it costs.
VTU BEC303 | Module 3
The unit-step function and switched s…
29
THE MECHANISM
The unit step u(t) is zero for t < 0 and one for t > 0, and it exists so that a switching event can be written into an equation instead of described in words. A source that turns on at t = 0 is written V·u(t); one that turns on at t = t₀ is V·u(t − t₀). A rectangular pulse of width T is the difference of two steps, u(t) − u(t − T), which lets a pulse response be obtained by superposition of two step responses rather than by piecewise integration. The step is also the integral of the impulse and the derivative of the ramp, which places it in the middle of the singularity-function family used throughout Module 4.
KEY TERMS
• unit step u(t)
• delayed step
• pulse as a difference of steps
• switch equivalence
TAKEAWAY
The step turns a switch into algebra, and any pulse is just two steps with opposite signs.
DIAGRAM FOR PHASE 2
Three stacked time plots sharing an axis. Plot 1: u(t), a clean rising step at t = 0 held at 1. Plot 2: −u(t − T), a falling step at t = T held at −1, drawn in a second colour. Plot 3: their sum, a rectangular…
Source: Engineering Circuit Analysis, 8th ed., Ch. 8, pp. 282-286
CO3 | Bloom L3 | visual id: step-pulse-construction
Notes: What to say: Give them the idea before the formalism. Say it plainly first: The unit step u(t) is zero for t < 0 and one for t > 0, and it exists so that a switching event can be written into an equation instead of described in wo… Then add the part they are examined on - The step turns a switch into algebra, and any pulse is just two steps with opposite signs. Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "unit step u(t)" constrain here, and what would break if it did not hold? Animation instructions: plot 1 draws, plot 2 draws in its own colour, then the two are shown sliding together to form plot 3 which fills in as a shaded rectangle, then the switch-to-expression arrows appear on the right. Transition style: Fade [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 3: Transient Behavior and Initial Conditions. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 8, pp. 282-286. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 30
The unit-step function and switched sources - how it works
The procedure in order, and what each pass costs you.
VTU BEC303 | Module 3
The unit-step function and switched s…
30
1. Write each switch closure as a step at the appropriate time
2. Write a source active only between t₁ and t₂ as u(t − t₁) − u(t − t₂)
3. For a pulse response, find the step response first
4. Superpose a delayed and negated copy of the step response
5. Check that the constructed waveform is zero where the physical source is off
COST AND BEHAVIOUR
Best: one step response reused twice for a pulse
Typical: one step response per distinct switching level
Worst: k step responses for a k-level staircase input
WHAT THAT MEANS
Superposition of steps is far cheaper than piecewise integration across intervals.
Source: Engineering Circuit Analysis, 8th ed., Ch. 8, pp. 282-286 | CO3 | Bloom L3
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Write each switch closure as a step at the appropriate time - and check everyone has written it before moving on. At the cost panel, translate it: Superposition of steps is far cheaper than piecewise integration across intervals. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 3: Transient Behavior and Initial Conditions. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 8, pp. 282-286. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 31
The unit-step function and switched sources - worked example
One concrete case, carried all the way to a stated number.
VTU BEC303 | Module 3
The unit-step function and switched s…
31
GIVEN
A 5 V pulse of width 3 ms applied to an RC circuit with τ = 1 ms, initially uncharged.
1. Input written as 5[u(t) − u(t − 0.003)]
2. Step response: v(t) = 5(1 − e^(−t/0.001)) for the rising step
3. At t = 3 ms = 3τ the capacitor has reached 5(1 − 0.0498) = 4.75 V
4. After 3 ms the second step applies: v(t) = 4.75·e^(−(t−0.003)/0.001)
RESULT
The capacitor charges to 4.75 V during the pulse and then decays from that value — obtained entirely by superposing two step responses.
v_in = 5[u(t) − u(t−3ms)]
0 < t < 3ms : v = 5(1 − e^{−t/τ}) ⇒ v(3ms) = 4.75 V
t > 3ms : v = 4.75 e^{−(t−3ms)/τ}
THE MISTAKE STUDENTS MAKE
Students restart the second interval from the full 5 V rather than from the 4.75 V actually reached. The final condition of one interval is the initial condition of the next, and a pulse shorter than about 5τ never reaches the full value.
Source: Engineering Circuit Analysis, 8th ed., Ch. 8, pp. 282-286 | CO3 | Bloom L3
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is A 5 V pulse of width 3 ms applied to an RC circuit with τ = 1 ms, initially uncharged. Work at the pace of the slowest note-taker and land hard on the result: The capacitor charges to 4.75 V during the pulse and then decays from that value — obtained entirely by superposing two step resp… Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 3: Transient Behavior and Initial Conditions. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 8, pp. 282-286. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 32
Driven RL circuits: natural and forced response
What it is, why it works, and what it costs.
VTU BEC303 | Module 3
Driven RL circuits: natural and force…
32
THE MECHANISM
The complete response of a driven first-order circuit is the sum of two parts. The natural response is the source-free solution, an exponential of the form A·e^(−t/τ) whose shape is set by the circuit and whose amplitude A is set by the initial condition. The forced response is whatever the circuit settles into under the continuing excitation, a constant for a DC drive and a sinusoid for an AC drive. Only after both parts have been written is the initial condition applied, to fix A — applying it to the natural response alone is the single most common error, because at t = 0+ the forced response is generally not zero and contributes to the total.
KEY TERMS
• natural response
• forced response
• complete response
• superposition of responses
TAKEAWAY
Write the whole response first, then apply the initial condition to the total — never to the natural part alone.
DIAGRAM FOR PHASE 2
Three time plots stacked vertically with a plus sign between the first two and an equals sign before the third. Plot 1 "Natural: A·e^(−t/τ)" shows a decaying exponential starting at A. Plot 2 "Forced: i(∞)" sh…
Source: Engineering Circuit Analysis, 8th ed., Ch. 8, pp. 286-295
CO3 | Bloom L4 | visual id: natural-plus-forced-stack
Notes: What to say: Give them the idea before the formalism. Say it plainly first: The complete response of a driven first-order circuit is the sum of two parts. Then add the part they are examined on - Write the whole response first, then apply the initial condition to the total — never to the natural part alone. Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "natural response" constrain here, and what would break if it did not hold? Animation instructions: plots 1 and 2 draw, the plus and equals signs appear, plot 3 draws as a visible point-by-point sum of the two above, then the green callout lands on plot 3 and the red crossed callout appears on plot 1. Transition style: Fade [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 3: Transient Behavior and Initial Conditions. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 8, pp. 286-295. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 33
Driven RL circuits: natural and forced response - how it works
The procedure in order, and what each pass costs you.
VTU BEC303 | Module 3
Driven RL circuits: natural and force…
33
1. Find the final value i(∞) — this is the forced response for a DC drive
2. Find τ from the resistance seen by the inductor after switching
3. Write i(t) = i(∞) + A·e^(−t/τ)
4. Find i(0+) from the continuity rule
5. Set t = 0 in the complete expression and solve for A = i(0+) − i(∞)
6. Substitute A back to obtain the final answer
COST AND BEHAVIOUR
Best: O(1) using the shortcut formula
Typical: two resistive solves plus one algebraic step
Worst: a phasor solve for the forced part under AC excitation
WHAT THAT MEANS
The general first-order formula x(t) = x(∞) + [x(0+) − x(∞)]·e^(−t/τ) covers every DC-driven case.
Source: Engineering Circuit Analysis, 8th ed., Ch. 8, pp. 286-295 | CO3 | Bloom L4
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Find the final value i(∞) — this is the forced response for a DC drive - and check everyone has written it before moving on. At the cost panel, translate it: The general first-order formula x(t) = x(∞) + [x(0+) − x(∞)]·e^(−t/τ) covers every DC-driven case. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 3: Transient Behavior and Initial Conditions. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 8, pp. 286-295. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 34
Driven RL circuits: natural and forced response - worked example
One concrete case, carried all the way to a stated number.
VTU BEC303 | Module 3
Driven RL circuits: natural and force…
34
GIVEN
A 20 V source switched onto a series 5 Ω and 2 H at t = 0, with zero initial current.
1. Forced: i(∞) = 20/5 = 4 A
2. τ = L/R = 2/5 = 0.4 s
3. i(t) = 4 + A·e^(−t/0.4)
4. i(0+) = 0 ⇒ 0 = 4 + A ⇒ A = −4
RESULT
i(t) = 4(1 − e^(−2.5t)) A, rising from zero to 4 A with the current at one time constant being 2.53 A.
x(t) = x(∞) + [x(0+) − x(∞)]·e^{−t/τ}
i(t) = 4 + (0 − 4)e^{−t/0.4} = 4(1 − e^{−2.5t}) A
THE MISTAKE STUDENTS MAKE
Students set the natural response amplitude equal to the initial value, writing i(t) = 4 + 0·e^(−t/τ) when i(0) = 0. A is the difference between the initial and final values, not the initial value itself.
Source: Engineering Circuit Analysis, 8th ed., Ch. 8, pp. 286-295 | CO3 | Bloom L4
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is A 20 V source switched onto a series 5 Ω and 2 H at t = 0, with zero initial current. Work at the pace of the slowest note-taker and land hard on the result: i(t) = 4(1 − e^(−2.5t)) A, rising from zero to 4 A with the current at one time constant being 2.53 A. Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 3: Transient Behavior and Initial Conditions. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 8, pp. 286-295. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 35
Driven RC circuits and the power-ON delay case study
What it is, why it works, and what it costs.
VTU BEC303 | Module 3
Driven RC circuits and the power-ON d…
35
THE MECHANISM
A driven RC circuit charges as v(t) = v(∞) + [v(0+) − v(∞)]·e^(−t/RC), the same general form as the RL case. Its most common engineering use is as a deliberate delay: a comparator or logic input has a threshold V_th, and the RC charges toward the supply until it crosses that threshold, at which point the indicator turns on. Solving the charging equation for time gives t_delay = −RC·ln(1 − V_th/V_supply), which shows that the delay scales linearly with RC and depends only logarithmically on the threshold ratio. The design consequence is that supply tolerance and threshold tolerance both shift the delay, so a precision delay needs either a tight threshold or a different technique altogether.
KEY TERMS
• charging curve
• threshold crossing
• delay design
• indicator circuit
TAKEAWAY
An RC delay is set by RC and a logarithm of the threshold ratio, which makes it cheap, adjustable and only moderately precise.
DIAGRAM FOR PHASE 2
A charging curve rising from 0 toward a horizontal asymptote labelled V_supply. A horizontal dashed line at V_th crosses the curve, and a vertical dashed line drops from the crossing to the time axis labelled…
Source: Engineering Circuit Analysis, 8th ed., Ch. 8, pp. 295-300
CO3 | Bloom L5 | visual id: rc-delay-threshold
Notes: What to say: Give them the idea before the formalism. Say it plainly first: A driven RC circuit charges as v(t) = v(∞) + [v(0+) − v(∞)]·e^(−t/RC), the same general form as the RL case. Then add the part they are examined on - An RC delay is set by RC and a logarithm of the threshold ratio, which makes it cheap, adjustable and only moderately precis… Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "charging curve" constrain here, and what would break if it did not hold? Animation instructions: the curve draws toward its asymptote, the threshold line slides in, the crossing point flashes, the vertical delay line drops, the LED lights, then the formula and sensitivity table fade in. Transition style: Fade [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 3: Transient Behavior and Initial Conditions. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 8, pp. 295-300. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 36
Driven RC circuits and the power-ON delay case study - how it works
The procedure in order, and what each pass costs you.
VTU BEC303 | Module 3
Driven RC circuits and the power-ON d…
36
1. Identify the supply voltage and the input threshold
2. Choose the capacitor first, from available values and leakage limits
3. Compute the required RC from t_delay = −RC·ln(1 − V_th/V_supply)
4. Solve for R and choose the nearest standard value
5. Recompute the actual delay with the chosen R and C
6. Check the delay spread over the supply and threshold tolerances
COST AND BEHAVIOUR
Best: O(1) — one logarithm
Typical: one design pass plus one tolerance check
Worst: iteration when standard component values shift the delay outside specification
WHAT THAT MEANS
Tolerance stack-up, not the algebra, is what makes this a design problem.
Source: Engineering Circuit Analysis, 8th ed., Ch. 8, pp. 295-300 | CO3 | Bloom L5
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Identify the supply voltage and the input threshold - and check everyone has written it before moving on. At the cost panel, translate it: Tolerance stack-up, not the algebra, is what makes this a design problem. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 3: Transient Behavior and Initial Conditions. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 8, pp. 295-300. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 37
Driven RC circuits and the power-ON delay case study - worked example
One concrete case, carried all the way to a stated number.
VTU BEC303 | Module 3
Driven RC circuits and the power-ON d…
37
GIVEN
A 5 V supply, a logic threshold of 2.5 V, and a required delay of 100 ms.
1. V_th/V_supply = 0.5, so ln(1 − 0.5) = −0.693
2. t = 0.693·RC ⇒ RC = 0.1/0.693 = 0.1443 s
3. Choose C = 10 µF, giving R = 0.1443/10e−6 = 14.43 kΩ
4. Nearest standard 5 % value is 15 kΩ, giving an actual delay of 0.693 × 15000 × 10e−6 = 104 ms
RESULT
R = 15 kΩ with C = 10 µF gives 104 ms against a 100 ms target — a 4 % error from component rounding alone, before tolerance is considered.
t = −RC·ln(1 − V_th/V_s)
0.1 = 0.693·RC ⇒ RC = 144.3 ms
C = 10 µF ⇒ R = 14.43 kΩ → use 15 kΩ (t = 104 ms)
THE MISTAKE STUDENTS MAKE
Students use t = RC as the delay, assuming the threshold sits at 63 % of the supply. That is true only for one specific threshold ratio; at a 50 % threshold the delay is 0.693·RC, a 31 % difference.
Source: Engineering Circuit Analysis, 8th ed., Ch. 8, pp. 295-300 | CO3 | Bloom L5
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is A 5 V supply, a logic threshold of 2.5 V, and a required delay of 100 ms. Work at the pace of the slowest note-taker and land hard on the result: R = 15 kΩ with C = 10 µF gives 104 ms against a 100 ms target — a 4 % error from component rounding alone, before tolerance is co… Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 3: Transient Behavior and Initial Conditions. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 8, pp. 295-300. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 38
Sequentially switched circuits
What it is, why it works, and what it costs.
VTU BEC303 | Module 3
Sequentially switched circuits
38
THE MECHANISM
When a circuit is switched more than once, each interval is solved as a separate first-order problem, and the final value reached in one interval becomes the initial condition of the next. The critical case is incomplete settling: if an interval is shorter than about 5τ the response does not reach its asymptote, and carrying the asymptotic value forward instead of the actual value corrupts every subsequent interval. Each interval may also have its own time constant, because the resistance seen by the storage element changes with the switch position. The general approach is therefore bookkeeping rather than new theory, but the bookkeeping is where the errors live.
KEY TERMS
• multiple switching instants
• interval chaining
• incomplete settling
• piecewise response
TAKEAWAY
Each interval hands its actual end value — not its asymptote — to the next as an initial condition.
DIAGRAM FOR PHASE 2
A single time axis divided into three shaded intervals by two vertical switching lines at t₁ and t₂. The response curve is drawn piecewise, with each segment starting exactly where the previous one ended, and…
Source: Engineering Circuit Analysis, 8th ed., Ch. 8, pp. 300-306
CO3 | Bloom L4 | visual id: sequential-intervals-chain
Notes: What to say: Give them the idea before the formalism. Say it plainly first: When a circuit is switched more than once, each interval is solved as a separate first-order problem, and the final value reached in one interval becomes… Then add the part they are examined on - Each interval hands its actual end value — not its asymptote — to the next as an initial condition. Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "multiple switching instants" constrain here, and what would break if it did not hold? Animation instructions: interval 1 curve draws, the red ghost asymptote appears then dims, the green handover dot flashes, interval 2 draws from that dot, the same for interval 3, then the three circuit thumbnails appear beneath. Transition style: Fade [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 3: Transient Behavior and Initial Conditions. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 8, pp. 300-306. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 39
Sequentially switched circuits - how it works
The procedure in order, and what each pass costs you.
VTU BEC303 | Module 3
Sequentially switched circuits
39
1. Divide the timeline at every switching instant
2. For the first interval, find the initial condition from the pre-switch steady state
3. Determine τ for that interval from the resistance then in circuit
4. Compute the response and evaluate it at the end of the interval
5. Use that value as the initial condition for the next interval
6. Repeat, recomputing τ whenever the topology changes
COST AND BEHAVIOUR
Best: O(k) for k intervals with the same τ
Typical: O(k) with a resistive solve per interval
Worst: O(k) solves plus O(k) evaluations for k switchings
WHAT THAT MEANS
Cost is linear in the number of intervals; the risk is that one carried-forward error propagates through all of them.
Source: Engineering Circuit Analysis, 8th ed., Ch. 8, pp. 300-306 | CO3 | Bloom L4
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Divide the timeline at every switching instant - and check everyone has written it before moving on. At the cost panel, translate it: Cost is linear in the number of intervals; the risk is that one carried-forward error propagates through all of them. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 3: Transient Behavior and Initial Conditions. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 8, pp. 300-306. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 40
Sequentially switched circuits - worked example
One concrete case, carried all the way to a stated number.
VTU BEC303 | Module 3
Sequentially switched circuits
40
GIVEN
An RC circuit with τ = 1 ms charges from 0 toward 10 V for 2 ms, then the source is removed and it discharges through the same R.
1. Interval 1: v(t) = 10(1 − e^(−t/0.001))
2. At t = 2 ms = 2τ: v = 10(1 − 0.1353) = 8.65 V, not 10 V
3. Interval 2 initial condition: v(0+) = 8.65 V
4. Interval 2: v(t) = 8.65·e^(−(t−0.002)/0.001)
RESULT
The discharge starts from 8.65 V; assuming a full 10 V would overstate every subsequent value by 16 %.
interval 1: v = 10(1 − e^{−t/τ}), v(2τ) = 8.65 V
interval 2: v = 8.65 e^{−(t−2τ)/τ}
(using 10 V here → 16% error)
THE MISTAKE STUDENTS MAKE
Students assume each interval starts fresh from the supply value or from zero. The handover value is whatever the previous interval actually reached, and for intervals shorter than 5τ that is never the asymptote.
Source: Engineering Circuit Analysis, 8th ed., Ch. 8, pp. 300-306 | CO3 | Bloom L4
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is An RC circuit with τ = 1 ms charges from 0 toward 10 V for 2 ms, then the source is removed and it discharges through the same R. Work at the pace of the slowest note-taker and land hard on the result: The discharge starts from 8.65 V; assuming a full 10 V would overstate every subsequent value by 16 %. Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 3: Transient Behavior and Initial Conditions. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 8, pp. 300-306. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 41
The source-free parallel RLC and damping classification
What it is, why it works, and what it costs.
VTU BEC303 | Module 3
The source-free parallel RLC and damp…
41
THE MECHANISM
A parallel RLC circuit with no source obeys a second-order differential equation whose characteristic roots are s = −α ± √(α² − ω₀²), where α = 1/(2RC) is the neper frequency and ω₀ = 1/√(LC) is the resonant frequency. The discriminant decides everything: α > ω₀ gives two real roots and an overdamped response that decays without oscillating; α = ω₀ gives a repeated root and the critically damped response, the fastest possible without overshoot; α < ω₀ gives complex roots and an underdamped response that rings at ω_d = √(ω₀² − α²). Nothing else about the circuit changes the shape of the response — the three cases are exhaustive.
KEY TERMS
• second order
• neper frequency α
• resonant frequency ω₀
• characteristic equation
• damping ratio
TAKEAWAY
Compare α with ω₀ before writing anything else; that one comparison determines the entire form of the answer.
DIAGRAM FOR PHASE 2
Top: a number line with ω₀ marked at the centre and α varying along it, with three labelled zones — "α > ω₀ overdamped", "α = ω₀ critically damped", "α < ω₀ underdamped". Below, three time plots side by side,…
Source: Engineering Circuit Analysis, 8th ed., Ch. 9, pp. 321-334
CO3 | Bloom L4 | visual id: damping-three-cases
Notes: What to say: Give them the idea before the formalism. Say it plainly first: A parallel RLC circuit with no source obeys a second-order differential equation whose characteristic roots are s = −α ± √(α² − ω₀²), where α = 1/(2RC) is… Then add the part they are examined on - Compare α with ω₀ before writing anything else; that one comparison determines the entire form of the answer. Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "second order" constrain here, and what would break if it did not hold? Animation instructions: the number line draws with its three zones shading in turn, then each of the three plots draws left to right, then the three root forms type in beneath. Transition style: Fade [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 3: Transient Behavior and Initial Conditions. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 9, pp. 321-334. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 42
The source-free parallel RLC and damping classification - how it works
The procedure in order, and what each pass costs you.
VTU BEC303 | Module 3
The source-free parallel RLC and damp…
42
1. Compute α = 1/(2RC) for a parallel circuit
2. Compute ω₀ = 1/√(LC)
3. Compare α with ω₀ to classify the response
4. Write the appropriate solution form for that case
5. Find the two constants from v(0+) and dv/dt(0+)
6. Check that the result decays for all positive R
COST AND BEHAVIOUR
Best: O(1) classification from two formulas
Typical: classification plus a 2×2 solve for the constants
Worst: a full initial-condition pipeline to obtain the derivative at 0+
WHAT THAT MEANS
The classification costs two square roots and saves choosing the wrong solution form entirely.
Source: Engineering Circuit Analysis, 8th ed., Ch. 9, pp. 321-334 | CO3 | Bloom L4
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Compute α = 1/(2RC) for a parallel circuit - and check everyone has written it before moving on. At the cost panel, translate it: The classification costs two square roots and saves choosing the wrong solution form entirely. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 3: Transient Behavior and Initial Conditions. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 9, pp. 321-334. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 43
The source-free parallel RLC and damping classification - worked example
One concrete case, carried all the way to a stated number.
VTU BEC303 | Module 3
The source-free parallel RLC and damp…
43
GIVEN
A parallel RLC with R = 500 Ω, L = 10 mH, C = 1 µF, source-free.
1. α = 1/(2RC) = 1/(2 × 500 × 1e−6) = 1000 s⁻¹
2. ω₀ = 1/√(LC) = 1/√(1e−2 × 1e−6) = 10000 rad/s
3. α < ω₀, so the response is underdamped
4. ω_d = √(10000² − 1000²) = 9950 rad/s
RESULT
Underdamped, ringing at 9950 rad/s inside a decaying envelope e^(−1000t) — so about ten oscillations before the envelope falls to 37 %.
α = 1/(2RC) = 1000 s⁻¹, ω₀ = 1/√(LC) = 10000 rad/s
α < ω₀ ⇒ underdamped, ω_d = √(ω₀²−α²) = 9950 rad/s
THE MISTAKE STUDENTS MAKE
Students use the series formula α = R/(2L) for a parallel circuit. The two expressions are duals and give wildly different numbers for the same components, which flips the damping classification and produces a solution of the wrong shape.
Source: Engineering Circuit Analysis, 8th ed., Ch. 9, pp. 321-334 | CO3 | Bloom L4
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is A parallel RLC with R = 500 Ω, L = 10 mH, C = 1 µF, source-free. Work at the pace of the slowest note-taker and land hard on the result: Underdamped, ringing at 9950 rad/s inside a decaying envelope e^(−1000t) — so about ten oscillations before the envelope falls to… Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 3: Transient Behavior and Initial Conditions. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 9, pp. 321-334. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 44
Critically damped and underdamped responses
What it is, why it works, and what it costs.
VTU BEC303 | Module 3
Critically damped and underdamped res…
44
THE MECHANISM
When α = ω₀ the characteristic equation has a repeated root and the solution takes the special form (A₁ + A₂t)·e^(−αt); the extra factor of t is required because two independent solutions are needed and e^(−αt) alone supplies only one. This is the fastest decay achievable without overshoot, which is why servo and instrumentation designers aim for it. When α < ω₀ the roots are complex and the solution is e^(−αt)(B₁cos ω_d t + B₂sin ω_d t), an oscillation at the damped frequency ω_d = √(ω₀² − α²) inside an exponential envelope. Overshoot grows as α falls, and in the limit α → 0 the circuit becomes a lossless oscillator that never settles.
KEY TERMS
• repeated root
• t·e^(−αt) term
• damped natural frequency
• envelope
• overshoot
TAKEAWAY
Critical damping is the fastest settling without overshoot — and the repeated root is why it needs a t·e^(−αt) term.
DIAGRAM FOR PHASE 2
A single set of axes carrying three overlaid step responses normalised to the same final value: an overdamped curve in grey rising slowly, a critically damped curve in green reaching the final value fastest wi…
Source: Engineering Circuit Analysis, 8th ed., Ch. 9, pp. 334-345
CO3 | Bloom L4 | visual id: critical-vs-underdamped-overlay
Notes: What to say: Give them the idea before the formalism. Say it plainly first: When α = ω₀ the characteristic equation has a repeated root and the solution takes the special form (A₁ + A₂t)·e^(−αt); the extra factor of t is required… Then add the part they are examined on - Critical damping is the fastest settling without overshoot — and the repeated root is why it needs a t·e^(−αt) term. Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "repeated root" constrain here, and what would break if it did not hold? Animation instructions: grey curve draws, green curve draws and its settling marker drops, blue curve draws with its overshoot peak flashing and the envelope appearing as dashes, then the side box slides in with the highlight landing last. Transition style: Fade [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 3: Transient Behavior and Initial Conditions. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 9, pp. 334-345. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 45
Critically damped and underdamped responses - how it works
The procedure in order, and what each pass costs you.
VTU BEC303 | Module 3
Critically damped and underdamped res…
45
1. Classify the response by comparing α and ω₀
2. For the critically damped case write (A₁ + A₂t)·e^(−αt)
3. For the underdamped case compute ω_d and write e^(−αt)(B₁cos ω_d t + B₂sin ω_d t)
4. Apply the value at t = 0+ to get the first constant
5. Apply the derivative at t = 0+ to get the second
6. Sanity-check that the response decays and has the expected number of oscillations
COST AND BEHAVIOUR
Best: O(1) once the two initial conditions are known
Typical: a 2×2 linear solve for the constants
Worst: a full initial-condition pipeline to obtain the derivative
WHAT THAT MEANS
Forgetting the t factor in the critical case produces a solution that cannot satisfy two independent initial conditions.
Source: Engineering Circuit Analysis, 8th ed., Ch. 9, pp. 334-345 | CO3 | Bloom L4
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Classify the response by comparing α and ω₀ - and check everyone has written it before moving on. At the cost panel, translate it: Forgetting the t factor in the critical case produces a solution that cannot satisfy two independent initial conditions. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 3: Transient Behavior and Initial Conditions. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 9, pp. 334-345. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 46
Critically damped and underdamped responses - worked example
One concrete case, carried all the way to a stated number.
VTU BEC303 | Module 3
Critically damped and underdamped res…
46
GIVEN
A critically damped circuit with α = 1000 s⁻¹, v(0+) = 10 V and dv/dt(0+) = 0.
1. Form: v(t) = (A₁ + A₂t)·e^(−1000t)
2. At t = 0: A₁ = 10
3. Differentiate: dv/dt = A₂e^(−αt) − α(A₁ + A₂t)e^(−αt)
4. At t = 0: 0 = A₂ − 1000 × 10 ⇒ A₂ = 10000
RESULT
v(t) = (10 + 10000t)·e^(−1000t) V — the response initially rises slightly before decaying, which the simple exponential form could never have represented.
v(t) = (A₁ + A₂t)e^{−αt}
v(0)=10 ⇒ A₁=10
v̇(0)=0 ⇒ A₂ = αA₁ = 10000
v(t) = (10 + 10000t)e^{−1000t} V
THE MISTAKE STUDENTS MAKE
Students omit the t factor and write A·e^(−αt) for the critically damped case. With only one constant the solution cannot match both the initial value and the initial derivative, and the answer will silently satisfy only one of them.
Source: Engineering Circuit Analysis, 8th ed., Ch. 9, pp. 334-345 | CO3 | Bloom L4
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is A critically damped circuit with α = 1000 s⁻¹, v(0+) = 10 V and dv/dt(0+) = 0. Work at the pace of the slowest note-taker and land hard on the result: v(t) = (10 + 10000t)·e^(−1000t) V — the response initially rises slightly before decaying, which the simple exponential form coul… Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 3: Transient Behavior and Initial Conditions. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 9, pp. 334-345. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 47
The source-free series RLC and the complete second-order response
What it is, why it works, and what it costs.
VTU BEC303 | Module 3
The source-free series RLC and the co…
47
THE MECHANISM
The series RLC is the dual of the parallel case: α = R/(2L) rather than 1/(2RC), while ω₀ = 1/√(LC) is unchanged. Everything else — the three damping cases, the solution forms, the role of ω_d — transfers directly. Note the reversal: increasing R damps a series circuit more but a parallel circuit less, because in series the resistance is in the current path while in parallel it is a bypass. The complete driven response is the forced response plus the natural response, exactly as in the first-order case, and the two natural-response constants are found by applying both the value and the derivative at t = 0+ to the complete expression, not to the natural part alone.
KEY TERMS
• series α = R/2L
• duality
• complete response
• forced plus natural
• two initial conditions
TAKEAWAY
Series and parallel RLC differ only in α — but the direction in which R damps them is opposite, and that trips people constantly.
DIAGRAM FOR PHASE 2
Left panel "Series RLC": R, L and C in a loop, with α = R/(2L) printed and an arrow labelled "R ↑ ⇒ more damping" pointing toward a flatter response curve. Right panel "Parallel RLC": R, L and C across a commo…
Source: Engineering Circuit Analysis, 8th ed., Ch. 9, pp. 345-359
CO3 | Bloom L4 | visual id: series-parallel-alpha-contrast
Notes: What to say: Give them the idea before the formalism. Say it plainly first: The series RLC is the dual of the parallel case: α = R/(2L) rather than 1/(2RC), while ω₀ = 1/√(LC) is unchanged. Then add the part they are examined on - Series and parallel RLC differ only in α — but the direction in which R damps them is opposite, and that trips people consta… Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "series α = R/2L" constrain here, and what would break if it did not hold? Animation instructions: left panel draws with its formula and its arrow sweeping to the flat curve, right panel draws with its arrow sweeping to the ringing curve, then the central warning badge flashes, then the shared strip slides up. Transition style: Fade [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 3: Transient Behavior and Initial Conditions. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 9, pp. 345-359. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 48
The source-free series RLC and the complete second-orde… - how it works
The procedure in order, and what each pass costs you.
VTU BEC303 | Module 3
The source-free series RLC and the co…
48
1. Identify the topology as series or parallel
2. Use α = R/(2L) for series, α = 1/(2RC) for parallel
3. Compute ω₀ = 1/√(LC) and classify the damping
4. Write the forced response from the DC or AC final condition
5. Add the appropriate natural-response form with two unknown constants
6. Apply x(0+) and dx/dt(0+) to the complete expression to find both constants
COST AND BEHAVIOUR
Best: O(1) classification plus a 2×2 solve
Typical: one initial-condition pipeline plus a 2×2 solve
Worst: a phasor solve for the forced part under AC excitation
WHAT THAT MEANS
Two initial conditions are always required for a second-order circuit — one is never enough.
Source: Engineering Circuit Analysis, 8th ed., Ch. 9, pp. 345-359 | CO3 | Bloom L4
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Identify the topology as series or parallel - and check everyone has written it before moving on. At the cost panel, translate it: Two initial conditions are always required for a second-order circuit — one is never enough. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 3: Transient Behavior and Initial Conditions. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 9, pp. 345-359. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 49
The source-free series RLC and the complete second-orde… - worked example
One concrete case, carried all the way to a stated number.
VTU BEC303 | Module 3
The source-free series RLC and the co…
49
GIVEN
A series RLC with R = 40 Ω, L = 10 mH, C = 1 µF, driven by a 10 V step with zero initial conditions.
1. α = R/(2L) = 40/0.02 = 2000 s⁻¹
2. ω₀ = 1/√(1e−2 × 1e−6) = 10000 rad/s, so α < ω₀: underdamped
3. ω_d = √(10000² − 2000²) = 9798 rad/s
4. Forced: v_C(∞) = 10 V; complete: v_C = 10 + e^(−2000t)(B₁cos ω_d t + B₂sin ω_d t)
RESULT
Underdamped with ω_d = 9798 rad/s; applying v_C(0+) = 0 gives B₁ = −10, and the zero initial current then fixes B₂.
series: α = R/2L = 2000 s⁻¹, ω₀ = 10000 rad/s
underdamped, ω_d = 9798 rad/s
v_C = 10 + e^{−2000t}(B₁cos ω_d t + B₂sin ω_d t), B₁ = −10
THE MISTAKE STUDENTS MAKE
Students apply only the initial value and leave the second constant undetermined, or guess it as zero. A second-order circuit needs two independent initial conditions, and the second one comes from the element law: i_C(0+)/C for a capacitor voltage or v_L(0+)/L for an inductor current.
Source: Engineering Circuit Analysis, 8th ed., Ch. 9, pp. 345-359 | CO3 | Bloom L4
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is A series RLC with R = 40 Ω, L = 10 mH, C = 1 µF, driven by a 10 V step with zero initial conditions. Work at the pace of the slowest note-taker and land hard on the result: Underdamped with ω_d = 9798 rad/s; applying v_C(0+) = 0 gives B₁ = −10, and the zero initial current then fixes B₂. Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 3: Transient Behavior and Initial Conditions. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 9, pp. 345-359. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 50
Transients under AC excitation and the lossless LC circuit
What it is, why it works, and what it costs.
VTU BEC303 | Module 3
Transients under AC excitation and th…
50
THE MECHANISM
When a sinusoidal source is switched onto a reactive circuit, the complete response is again natural plus forced, but the forced part is now a sinusoid obtained by phasor analysis at the source frequency rather than a constant. The natural part decays as before, so the total shows a decaying offset riding on a steady sinusoid. The size of that offset depends on the switching angle: closing an inductive circuit at a voltage zero produces the largest transient because the forced current at that instant is at its peak and the natural response must cancel a large mismatch, which is why transformer inrush is worst at a zero crossing. The lossless LC circuit is the limiting case R = 0, where α = 0 and the natural response never decays at all.
KEY TERMS
• AC transient
• switching angle
• phasor forced response
• lossless oscillation
• worst-case inrush
TAKEAWAY
Under AC excitation the transient is a decaying offset on a steady sinusoid, and its size is set by when in the cycle you switched.
DIAGRAM FOR PHASE 2
Two side-by-side time plots of current after switching an inductive circuit onto an AC supply. Left plot "switch at voltage peak": the current starts near its steady-state value and the response is almost imme…
Source: Engineering Circuit Analysis, 8th ed., Ch. 9, pp. 359-361
CO3 | Bloom L5 | visual id: ac-switching-angle
Notes: What to say: Give them the idea before the formalism. Say it plainly first: When a sinusoidal source is switched onto a reactive circuit, the complete response is again natural plus forced, but the forced part is now a sinusoid ob… Then add the part they are examined on - Under AC excitation the transient is a decaying offset on a steady sinusoid, and its size is set by when in the cycle you sw… Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "AC transient" constrain here, and what would break if it did not hold? Animation instructions: left plot draws with its small offset, right plot draws with the large offset envelope appearing first and the one-sided waveform filling in under it, the 2× marker flashes, then the lossless strip fades in. Transition style: Fade [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 3: Transient Behavior and Initial Conditions. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 9, pp. 359-361. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 51
Transients under AC excitation and the lossless LC circ… - how it works
The procedure in order, and what each pass costs you.
VTU BEC303 | Module 3
Transients under AC excitation and th…
51
1. Find the forced response by phasor analysis at the source frequency
2. Convert the forced phasor back to a time-domain sinusoid
3. Write the natural response form with unknown constants and the circuit τ or α
4. Apply the continuity rules at the switching instant to the complete expression
5. Solve for the constants, noting that they depend on the switching angle
6. For R = 0, recognise that the natural term persists indefinitely
COST AND BEHAVIOUR
Best: one phasor solve plus one algebraic step
Typical: a phasor solve plus a first- or second-order constant fit
Worst: a second-order fit with two switching-angle-dependent constants
WHAT THAT MEANS
Worst-case design requires evaluating the switching angle that maximises the offset, not an arbitrary one.
Source: Engineering Circuit Analysis, 8th ed., Ch. 9, pp. 359-361 | CO3 | Bloom L5
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Find the forced response by phasor analysis at the source frequency - and check everyone has written it before moving on. At the cost panel, translate it: Worst-case design requires evaluating the switching angle that maximises the offset, not an arbitrary one. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 3: Transient Behavior and Initial Conditions. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 9, pp. 359-361. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 52
Transients under AC excitation and the lossless LC circ… - worked example
One concrete case, carried all the way to a stated number.
VTU BEC303 | Module 3
Transients under AC excitation and th…
52
GIVEN
A series R = 10 Ω, L = 20 mH switched onto 100·cos(377t) V at the instant the voltage is zero.
1. Z = 10 + j377 × 0.02 = 10 + j7.54 = 12.52∠37.0° Ω
2. Forced: i_ss(t) = (100/12.52)·cos(377t − 37.0°) = 7.99·cos(377t − 37.0°) A
3. Switching at a voltage zero means 377t = −90°, at which i_ss = 7.99·cos(−127°) = −4.81 A
4. Continuity requires i(0+) = 0, so the natural term must be +4.81 A, decaying with τ = L/R = 2 ms
RESULT
i(t) = 7.99·cos(377t − 37°) + 4.81·e^(−t/0.002) A — a substantial one-sided offset that dies away in about 10 ms.
Z = 10 + j7.54 = 12.52∠37°
i_ss = 7.99 cos(377t − 37°) A
i(0+) = 0 ⇒ natural = +4.81 A, τ = L/R = 2 ms
THE MISTAKE STUDENTS MAKE
Students assume the AC transient is negligible because "the circuit reaches steady state quickly". The offset can nearly double the first peak, which is exactly the case protective fuses and inrush limiters are sized for.
Source: Engineering Circuit Analysis, 8th ed., Ch. 9, pp. 359-361 | CO3 | Bloom L5
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is A series R = 10 Ω, L = 20 mH switched onto 100·cos(377t) V at the instant the voltage is zero. Work at the pace of the slowest note-taker and land hard on the result: i(t) = 7.99·cos(377t − 37°) + 4.81·e^(−t/0.002) A — a substantial one-sided offset that dies away in about 10 ms. Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 3: Transient Behavior and Initial Conditions. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 9, pp. 359-361. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 53
One sentence per unit, six months from now
Units 1-7: what survives after the detail has gone.
VTU BEC303 | Module 3
Revision
53
01 Capacitor voltage is continuous because a jump would need infinite current — that single fact fixes the t = 0+ value.
02 Inductor current is continuous because a jump would need infinite voltage — and the arc across an opening switch is that physics made visible.
03 Two resistive snapshots — one at t = 0+ and one at t = ∞ — give you the endpoints of every transient for free.
04 Only two quantities survive the switch; everything else at t = 0+ is computed from them by ordinary resistive analysis.
05 Final condition means the transient has died, not that the circuit has stopped — under AC excitation the steady state is itself a waveform.
06 Two numbers, i(0) and τ = L/R, determine the entire source-free RL response for all time.
07 The decay has no memory of where it started — every τ removes the same fraction, which is why a semilog plot straightens it.
Notes: What to say: Slow right down here. Read each takeaway aloud and then stop talking for a beat, because these are the sentences that should still be in their heads when they sit the SEE. Tell them explicitly that if they can reconstruct the reasoning behind any one of these lines they understand that unit, and if they can only recite it they do not. Pause cue: Pause for three seconds after each takeaway before moving to the next. Pointing cue: Point at each numbered takeaway in turn as you read it. Question to ask students: Ask: choose the takeaway you trust least and tell me what you would have to check to believe it. Animation instructions: Takeaway rows reveal one at a time from the top, each row highlighting briefly as it appears. Transition style: Fade [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 3: Transient Behavior and Initial Conditions, 14 hours, Hayt 8e Ch. 7 (7.1, 7.2, 7.7), Ch. 8 (8.1–8.9), Ch. 9 (9.1–9.7), Ch. 10 (10.1–10.7), pp. 217–247, 261–361 and 371–406. TB1: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012. Revision consolidates all 16 unit takeaways. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 54
Revision, continued
Units 8-14: what survives after the detail has gone.
VTU BEC303 | Module 3
Revision
54
08 RC and RL are duals: swap v for i and R for 1/R and every result maps across.
09 The step turns a switch into algebra, and any pulse is just two steps with opposite signs.
10 Write the whole response first, then apply the initial condition to the total — never to the natural part alone.
11 An RC delay is set by RC and a logarithm of the threshold ratio, which makes it cheap, adjustable and only moderately precise.
12 Each interval hands its actual end value — not its asymptote — to the next as an initial condition.
13 Compare α with ω₀ before writing anything else; that one comparison determines the entire form of the answer.
14 Critical damping is the fastest settling without overshoot — and the repeated root is why it needs a t·e^(−αt) term.
Notes: What to say: Slow right down here. Read each takeaway aloud and then stop talking for a beat, because these are the sentences that should still be in their heads when they sit the SEE. Tell them explicitly that if they can reconstruct the reasoning behind any one of these lines they understand that unit, and if they can only recite it they do not. Pause cue: Pause for three seconds after each takeaway before moving to the next. Pointing cue: Point at each numbered takeaway in turn as you read it. Question to ask students: Ask: choose the takeaway you trust least and tell me what you would have to check to believe it. Animation instructions: Takeaway rows reveal one at a time from the top, each row highlighting briefly as it appears. Transition style: Fade [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 3: Transient Behavior and Initial Conditions, 14 hours, Hayt 8e Ch. 7 (7.1, 7.2, 7.7), Ch. 8 (8.1–8.9), Ch. 9 (9.1–9.7), Ch. 10 (10.1–10.7), pp. 217–247, 261–361 and 371–406. TB1: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012. Revision consolidates all 16 unit takeaways. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 55
Revision, continued
Units 15-16: what survives after the detail has gone.
VTU BEC303 | Module 3
Revision
55
15 Series and parallel RLC differ only in α — but the direction in which R damps them is opposite, and that trips people constantly.
16 Under AC excitation the transient is a decaying offset on a steady sinusoid, and its size is set by when in the cycle you switched.
Notes: What to say: Slow right down here. Read each takeaway aloud and then stop talking for a beat, because these are the sentences that should still be in their heads when they sit the SEE. Tell them explicitly that if they can reconstruct the reasoning behind any one of these lines they understand that unit, and if they can only recite it they do not. Pause cue: Pause for three seconds after each takeaway before moving to the next. Pointing cue: Point at each numbered takeaway in turn as you read it. Question to ask students: Ask: choose the takeaway you trust least and tell me what you would have to check to believe it. Animation instructions: Takeaway rows reveal one at a time from the top, each row highlighting briefly as it appears. Transition style: Fade [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 3: Transient Behavior and Initial Conditions, 14 hours, Hayt 8e Ch. 7 (7.1, 7.2, 7.7), Ch. 8 (8.1–8.9), Ch. 9 (9.1–9.7), Ch. 10 (10.1–10.7), pp. 217–247, 261–361 and 371–406. TB1: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012. Revision consolidates all 16 unit takeaways. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 56
How this module is assessed
Where the quiz and the assignment live, and what they test.
VTU BEC303 | Module 3
Assessment
56
MODULE 3 QUIZ
quizzes/Module_3_Quiz.pdf
quizzes/Module_3_Quiz.gift
45 minutes | 50 marks | pass 20 | 1 attempt
Part A: 20 MCQs, 1 mark each.
Part B: 13 descriptive questions, 30 marks.
Bloom spread: L1-L2 33%, L3-L4 58%, L5-L6 9%
Every question carries a CO tag, a Bloom level and a chapter reference; distractor feedback names the misconception.
MODULE 3 ASSIGNMENT
assignments/Module_3_Assignment.pdf
Assignment 3 — Initial conditions, time constants and second-order response
20 marks | 10% of CIE | 10 problems + 3 theory items
Submit as PDF, single file, named <USN>_BEC303_Assignment3.pdf, via LMS upload. 10% per day, nothing after 5 days.
Rubric: Correct initial and final conditions (6); Time constants and response forms (6); Sequential and AC switching analysis (4); Verification, plots and engineering commentary (4). Attainment: CO3 = 20.
Previous years' question papers for EC are indexed in pyq/PYQ_Index.pdf; the syllabus extract and the topic-to-slide mapping are in syllabus/Syllabus_Mapping.pdf.
Individual submission. Identical submissions score zero for both parties.
Notes: What to say: Close by telling them exactly where the assessment lives and what it tests. Name the two files, say the mark split out loud, and read the Bloom spread so they understand that roughly a quarter of the paper is not recall at all. Then read the integrity line word for word, because ambiguity there costs students more than any technical error in this module. Pause cue: Pause after the Bloom spread and before the integrity statement. Pointing cue: Point at the quiz panel, then the assignment panel, then the integrity line at the bottom. Question to ask students: Ask: which course outcome do you feel least ready on, and which unit would you reread tonight to fix it? Animation instructions: Quiz panel fades in from the left, then the assignment panel from the right, then the pointers strip appears, then the integrity line fades in last. Transition style: Fade [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 3: Transient Behavior and Initial Conditions, 14 hours, Hayt 8e Ch. 7 (7.1, 7.2, 7.7), Ch. 8 (8.1–8.9), Ch. 9 (9.1–9.7), Ch. 10 (10.1–10.7), pp. 217–247, 261–361 and 371–406. TB1: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012. Assessment counts: 20 MCQs, 13 descriptive questions, 13 assignment items. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.