## Slide 1
Network Analysis
Module 4 asks: Can I replace calculus with algebra — solve the whole transient, initial conditions included, without ever…
VTU BEC303 | Module 4
Opening
01
MODULE 4
Laplace Transformation and Applications
14 contact hours | 16 teaching units | 56 slides
PRESCRIBED TEXTBOOK
Engineering Circuit Analysis
W. H. Hayt, J. E. Kemmerly and S. M. Durbin
McGraw-Hill / Tata McGraw-Hill, 8th edition, 2012
Hayt 8e Ch. 14 (14.3–14.7), Ch. 15 (15.1–15.8), pp. 540–564 and 571–610; waveform and network synthesis from syllabus TB2 §6.8
Mesh & Nodal Analysis • Network Theorems • Transient Response • Laplace / s-Domain • Two-Port Networks
Transform turns calculus algebraic → Initial conditions become sources → Impedance generalises to s → Poles predict the response shape → Synthesis runs the map backwards
EC · Semester 3 · BEC303 · generated for Phase 2 conversion
Notes: What to say: Open by putting the whole module on one page. Tell them this is 14 contact hours and 16 teaching units, and that all of it exists to answer one question: Can I replace calculus with algebra — solve the whole transient, initial conditions included, without ever writing a differential equation? Name the prescribed textbook out loud and say which chapters they will be living in, so nobody is reading the wrong book by week two. Pause cue: Pause after reading the driving question aloud, before naming the textbook. Pointing cue: Point at the module title block, then at the textbook panel, then run a finger along the five-beat arc. Question to ask students: Ask: before we start, what do you already expect the answer to "Can I replace calculus with algebra — solve the whole transient, initial conditions inclu…" to look like? Animation instructions: Module title block fades in first, then the textbook panel slides in from the right, then the five arc beats appear left to right one at a time. Transition style: Fade [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 4: Laplace Transformation and Applications, 14 hours, Hayt 8e Ch. 14 (14.3–14.7), Ch. 15 (15.1–15.8), pp. 540–564 and 571–610; waveform and network synthesis from syllabus TB2 §6.8. TB1: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 2
What this module is actually for
One question, five beats, and the scope it does not cover.
VTU BEC303 | Module 4
Overview
02
THE DRIVING QUESTION
Can I replace calculus with algebra — solve the whole transient, initial conditions included, without ever writing a differential equation?
1
Transform turns calculus algebraic
2
Initial conditions become sources
3
Impedance generalises to s
4
Poles predict the response shape
5
Synthesis runs the map backwards
SCOPE AND PROVENANCE
Built from the syllabus-listed Hayt 8e sections plus the syllabus-listed TB2 section for waveform and network synthesis. The through-line is that the s-domain does in one pass what Module 3 did in several: the natural and forced responses, the initial conditions and the steady state all emerge from one algebraic solution. Pole locations are introduced early and used repeatedly, so that by the case study students can read settling time and bandwidth off a pole position without computing a response at all.
Course outcomes exercised: CO4
Assessment: 20 MCQs + 13 descriptive questions + 13 assignment items
Notes: What to say: Give them the map before the territory. Read the driving question once more, then walk the five beats across the slide and say in one sentence what changes between each beat and the next. Finish on the scope paragraph, because knowing what a module does not cover saves more marks than anything else on this slide. Pause cue: Pause for four or five seconds after the five beats appear, before moving to scope. Pointing cue: Point at the driving question panel, then at each numbered beat in turn, then at the scope paragraph. Question to ask students: Ask: which of these five beats do you expect to find hardest, and why that one? Animation instructions: The driving question panel fades in, then the five numbered beats appear left to right one at a time, then the scope paragraph fades in beneath them. Transition style: Fade [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 4: Laplace Transformation and Applications, 14 hours, Hayt 8e Ch. 14 (14.3–14.7), Ch. 15 (15.1–15.8), pp. 540–564 and 571–610; waveform and network synthesis from syllabus TB2 §6.8. TB1: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 3
Every unit against its chapter and pages
Units 1-9 of 16, with the deck slides that teach each one.
VTU BEC303 | Module 4
Syllabus mapping
03
# — Teaching unit — Book chapter and pages — Deck slides — CO / Bloom
01 Definition of the Laplace transform — Ch. 14, pp. 540-543 — slides 5, 6, 7 — CO4 / L2
02 Transforms of simple time functions — Ch. 14, pp. 543-546 — slides 8, 9, 10 — CO4 / L2
03 Inverse transform by partial fractions — Ch. 14, pp. 546-553 — slides 11, 12, 13 — CO4 / L3
04 Basic theorems: linearity, shifting, differentiation and integration — Ch. 14, pp. 553-561 — slides 14, 15, 16 — CO4 / L3
05 Initial-value and final-value theorems — Ch. 14, pp. 561-564 — slides 17, 18, 19 — CO4 / L4
06 Z(s) and Y(s): impedance in the s-domain — Ch. 15, pp. 571-578 — slides 20, 21, 22 — CO4 / L3
07 Initial conditions as sources in the s-domain — Ch. 15, pp. 571-578 — slides 23, 24, 25 — CO4 / L4
08 Nodal and mesh analysis in the s-domain — Ch. 15, pp. 578-585 — slides 26, 27, 28 — CO4 / L4
09 Thévenin, Norton and superposition in the s-domain — Ch. 15, pp. 585-588 — slides 29, 30, 31 — CO4 / L4
Notes: What to say: Tell them this is the slide to photograph. Every unit in the module is listed against a real chapter and a real page range, so there is no ambiguity about what to read. Point out the slide-number column and say plainly that if they miss a lecture, those are the slides covering that unit. Say that the page ranges come from the book's own table of contents rather than a guess. Pause cue: Pause for ten seconds and let them photograph the table before saying anything else. Pointing cue: Run a finger down the chapter-and-pages column, then across one complete row. Question to ask students: Ask: pick any row - which chapter would you open first, and what would you expect in the first paragraph? Animation instructions: Header row appears first, then the unit rows fade in one at a time from the top, then the chapter-and-pages column highlights. Transition style: Cut [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 4: Laplace Transformation and Applications, 14 hours, Hayt 8e Ch. 14 (14.3–14.7), Ch. 15 (15.1–15.8), pp. 540–564 and 571–610; waveform and network synthesis from syllabus TB2 §6.8. TB1: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012. Mapping covers all 16 teaching units. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 4
Syllabus mapping, continued
Units 10-16 of 16, with the deck slides that teach each one.
VTU BEC303 | Module 4
Syllabus mapping
04
# — Teaching unit — Book chapter and pages — Deck slides — CO / Bloom
10 Transfer functions, poles and zeros — Ch. 15, pp. 588-589 — slides 32, 33, 34 — CO4 / L4
11 Step, ramp and impulse responses — Ch. 14, pp. 543-546 — slides 35, 36, 37 — CO4 / L4
12 Waveform synthesis — TB2 §6.8 — slides 38, 39, 40 — CO4 / L4
13 Convolution — Ch. 15, pp. 589-598 — slides 41, 42, 43 — CO4 / L5
14 The complex-frequency plane and the first-order filter pole case study — Ch. 15, pp. 598-602 — slides 44, 45, 46 — CO4 / L5
15 Natural response and the s-plane — Ch. 15, pp. 602-606 — slides 47, 48, 49 — CO4 / L5
16 Network synthesis: realising a specified H(s) — Ch. 15, pp. 606-610 — slides 50, 51, 52 — CO4 / L5
Notes: What to say: Tell them this is the slide to photograph. Every unit in the module is listed against a real chapter and a real page range, so there is no ambiguity about what to read. Point out the slide-number column and say plainly that if they miss a lecture, those are the slides covering that unit. Say that the page ranges come from the book's own table of contents rather than a guess. Pause cue: Pause for ten seconds and let them photograph the table before saying anything else. Pointing cue: Run a finger down the chapter-and-pages column, then across one complete row. Question to ask students: Ask: pick any row - which chapter would you open first, and what would you expect in the first paragraph? Animation instructions: Header row appears first, then the unit rows fade in one at a time from the top, then the chapter-and-pages column highlights. Transition style: Cut [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 4: Laplace Transformation and Applications, 14 hours, Hayt 8e Ch. 14 (14.3–14.7), Ch. 15 (15.1–15.8), pp. 540–564 and 571–610; waveform and network synthesis from syllabus TB2 §6.8. TB1: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012. Mapping covers all 16 teaching units. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 5
Definition of the Laplace transform
What it is, why it works, and what it costs.
VTU BEC303 | Module 4
Definition of the Laplace transform
05
THE MECHANISM
The one-sided Laplace transform is F(s) = ∫₀^∞ f(t)·e^(−st) dt, where s = σ + jω is a complex frequency. The decaying kernel e^(−σt) is what makes the integral converge for functions that grow, which is why the Laplace transform handles ramps and growing exponentials that the Fourier transform cannot. The lower limit is taken at 0− so that an impulse at the origin is fully captured and so that initial conditions enter the algebra automatically. The transform is linear and one-to-one on its region of convergence, which is what allows an answer found in the s-domain to be carried back uniquely to the time domain.
KEY TERMS
• one-sided transform
• complex frequency s
• region of convergence
• kernel e^(−st)
TAKEAWAY
The e^(−σt) kernel buys convergence, and taking the lower limit at 0− is what lets initial conditions ride into the algebra.
DIAGRAM FOR PHASE 2
Centre: the integral F(s) = ∫₀^∞ f(t)e^(−st)dt typeset large, with three callout arrows. Arrow 1 points at the lower limit and reads "0−: captures impulses and initial conditions". Arrow 2 points at e^(−st) an…
Source: Engineering Circuit Analysis, 8th ed., Ch. 14, pp. 540-543
CO4 | Bloom L2 | visual id: laplace-integral-anatomy
Notes: What to say: Give them the idea before the formalism. Say it plainly first: The one-sided Laplace transform is F(s) = ∫₀^∞ f(t)·e^(−st) dt, where s = σ + jω is a complex frequency. Then add the part they are examined on - The e^(−σt) kernel buys convergence, and taking the lower limit at 0− is what lets initial conditions ride into the algebra. Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "one-sided transform" constrain here, and what would break if it did not hold? Animation instructions: the integral types in, then arrow 1 and its label, then arrow 2 with its convergence inset animating the product, then arrow 3 with the s-plane and the ROC shading in last. Transition style: Fade [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 4: Laplace Transformation and Applications. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 14, pp. 540-543. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 6
Definition of the Laplace transform - how it works
The procedure in order, and what each pass costs you.
VTU BEC303 | Module 4
Definition of the Laplace transform
06
1. Write the time function, valid for t ≥ 0
2. Multiply by the kernel e^(−st)
3. Integrate from 0− to ∞
4. Identify the values of σ for which the integral converges
5. Report F(s) together with its region of convergence
6. Use a table rather than the integral for standard functions
COST AND BEHAVIOUR
Best: O(1) by table lookup
Typical: one integration by parts
Worst: repeated integration by parts for t^n terms
WHAT THAT MEANS
In circuit work the integral is almost never evaluated directly; the table plus the theorems do the work.
Source: Engineering Circuit Analysis, 8th ed., Ch. 14, pp. 540-543 | CO4 | Bloom L2
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Write the time function, valid for t ≥ 0 - and check everyone has written it before moving on. At the cost panel, translate it: In circuit work the integral is almost never evaluated directly; the table plus the theorems do the work. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 4: Laplace Transformation and Applications. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 14, pp. 540-543. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 7
Definition of the Laplace transform - worked example
One concrete case, carried all the way to a stated number.
VTU BEC303 | Module 4
Definition of the Laplace transform
07
GIVEN
f(t) = e^(−at)·u(t).
1. F(s) = ∫₀^∞ e^(−at)·e^(−st) dt
2. Combine exponents: ∫₀^∞ e^(−(s+a)t) dt
3. Integrate: [−e^(−(s+a)t)/(s+a)]₀^∞
4. For Re{s} > −a the upper limit vanishes, leaving 1/(s + a)
RESULT
F(s) = 1/(s + a) with a region of convergence Re{s} > −a; the pole at s = −a is exactly the decay rate of the original function.
F(s) = ∫₀⁻^∞ f(t)e^{−st}dt
f(t) = e^{−at}u(t) ⇒ F(s) = 1/(s+a), Re{s} > −a
THE MISTAKE STUDENTS MAKE
Students take the lower limit at 0+ out of habit. At 0+ an impulse at the origin is excluded and the differentiation theorem loses its f(0−) term, which is precisely the term that carries the initial condition.
Source: Engineering Circuit Analysis, 8th ed., Ch. 14, pp. 540-543 | CO4 | Bloom L2
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is f(t) = e^(−at)·u(t). Work at the pace of the slowest note-taker and land hard on the result: F(s) = 1/(s + a) with a region of convergence Re{s} > −a; the pole at s = −a is exactly the decay rate of the original function. Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 4: Laplace Transformation and Applications. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 14, pp. 540-543. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 8
Transforms of simple time functions
What it is, why it works, and what it costs.
VTU BEC303 | Module 4
Transforms of simple time functions
08
THE MECHANISM
A small table covers almost every circuit problem. The impulse transforms to 1, the step to 1/s, the ramp to 1/s², t^n to n!/s^(n+1), the exponential e^(−at) to 1/(s + a), the sinusoid sin ωt to ω/(s² + ω²) and cos ωt to s/(s² + ω²). The pattern is worth noticing rather than memorising blindly: each integration in time adds a factor of 1/s, which is why the step, ramp and parabola form a 1/s, 1/s², 1/s³ sequence. Multiplying a time function by e^(−at) shifts every s in its transform to s + a, which turns the plain sinusoid pair into the damped sinusoid pair used for underdamped responses.
KEY TERMS
• impulse δ(t)
• step u(t)
• ramp t·u(t)
• exponential
• damped sinusoid
TAKEAWAY
Integrating in time divides by s, and damping in time shifts s — two patterns that generate most of the table.
DIAGRAM FOR PHASE 2
Left column: five time-domain sketches stacked — impulse spike, unit step, ramp, decaying exponential, damped sinusoid. Right column: their transforms 1, 1/s, 1/s², 1/(s+a), ω/((s+a)²+ω²). Between the first th…
Source: Engineering Circuit Analysis, 8th ed., Ch. 14, pp. 543-546
CO4 | Bloom L2 | visual id: transform-table-ladder
Notes: What to say: Give them the idea before the formalism. Say it plainly first: A small table covers almost every circuit problem. Then add the part they are examined on - Integrating in time divides by s, and damping in time shifts s — two patterns that generate most of the table. Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "impulse δ(t)" constrain here, and what would break if it did not hold? Animation instructions: the five time sketches draw top to bottom, then each transform appears beside its sketch, then the vertical integration arrow sweeps down the first three, then the s-shift arrow animates across the last pair. Transition style: Fade [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 4: Laplace Transformation and Applications. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 14, pp. 543-546. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 9
Transforms of simple time functions - how it works
The procedure in order, and what each pass costs you.
VTU BEC303 | Module 4
Transforms of simple time functions
09
1. Express the time function as a sum of standard forms
2. Look up each standard transform
3. Apply linearity to combine them
4. Use the s-shift rule for any factor of e^(−at)
5. Use the 1/s rule for any integration in time
6. Check the result against a known limiting case
COST AND BEHAVIOUR
Best: O(1) single lookup
Typical: O(k) for a k-term sum
Worst: O(k) plus repeated shift applications
WHAT THAT MEANS
Decomposition into standard forms is the whole skill; the lookups are trivial.
Source: Engineering Circuit Analysis, 8th ed., Ch. 14, pp. 543-546 | CO4 | Bloom L2
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Express the time function as a sum of standard forms - and check everyone has written it before moving on. At the cost panel, translate it: Decomposition into standard forms is the whole skill; the lookups are trivial. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 4: Laplace Transformation and Applications. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 14, pp. 543-546. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 10
Transforms of simple time functions - worked example
One concrete case, carried all the way to a stated number.
VTU BEC303 | Module 4
Transforms of simple time functions
10
GIVEN
f(t) = 3 − 2e^(−5t) + 4t, for t ≥ 0.
1. Constant 3 is 3·u(t), transforming to 3/s
2. −2e^(−5t) transforms to −2/(s + 5)
3. 4t transforms to 4/s²
4. By linearity F(s) = 3/s − 2/(s + 5) + 4/s²
RESULT
F(s) = 3/s − 2/(s+5) + 4/s², with poles at s = 0 (double) and s = −5, matching the ramp and the decay in the original.
u(t) → 1/s, t·u(t) → 1/s², e^{−at} → 1/(s+a)
f = 3 − 2e^{−5t} + 4t ⇒ F(s) = 3/s − 2/(s+5) + 4/s²
THE MISTAKE STUDENTS MAKE
Students transform a constant as if it existed for all time and write 3 → 3. The one-sided transform assumes the function starts at t = 0, so a constant is really a step and transforms to 3/s.
Source: Engineering Circuit Analysis, 8th ed., Ch. 14, pp. 543-546 | CO4 | Bloom L2
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is f(t) = 3 − 2e^(−5t) + 4t, for t ≥ 0. Work at the pace of the slowest note-taker and land hard on the result: F(s) = 3/s − 2/(s+5) + 4/s², with poles at s = 0 (double) and s = −5, matching the ramp and the decay in the original. Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 4: Laplace Transformation and Applications. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 14, pp. 543-546. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 11
Inverse transform by partial fractions
What it is, why it works, and what it costs.
VTU BEC303 | Module 4
Inverse transform by partial fractions
11
THE MECHANISM
An s-domain answer is normally a ratio of polynomials, and the inverse transform is obtained by splitting that ratio into terms that appear in the table. For distinct real poles each term is a residue over (s − p), and the residue is found by covering up that factor and evaluating the rest at s = p. Repeated poles need an extra term per repetition, with the highest-power residue found by the cover-up rule and the lower ones by differentiation. Complex poles always come in conjugate pairs for a real circuit, and the cleanest route is to keep the pair together as a quadratic and match it to the damped sine and cosine forms rather than expanding into complex residues.
KEY TERMS
• partial fraction expansion
• distinct poles
• repeated poles
• complex pole pair
• residue
TAKEAWAY
Every inverse transform in circuit work is table lookup plus bookkeeping — the bookkeeping is partial fractions.
DIAGRAM FOR PHASE 2
A single rational function F(s) = N(s)/D(s) enters a splitter box on the left. Three output pipes emerge on the right, each labelled by pole type. Pipe 1 "distinct real" outputs K/(s − p) with a cover-up hand…
Source: Engineering Circuit Analysis, 8th ed., Ch. 14, pp. 546-553
CO4 | Bloom L3 | visual id: partial-fraction-splitter
Notes: What to say: Give them the idea before the formalism. Say it plainly first: An s-domain answer is normally a ratio of polynomials, and the inverse transform is obtained by splitting that ratio into terms that appear in the table. Then add the part they are examined on - Every inverse transform in circuit work is table lookup plus bookkeeping — the bookkeeping is partial fractions. Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "partial fraction expansion" constrain here, and what would break if it did not hold? Animation instructions: F(s) slides into the splitter, the three pipes extend in turn with their expressions typing in, then each pipe's time-domain sketch draws at the far right. Transition style: Fade [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 4: Laplace Transformation and Applications. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 14, pp. 546-553. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 12
Inverse transform by partial fractions - how it works
The procedure in order, and what each pass costs you.
VTU BEC303 | Module 4
Inverse transform by partial fractions
12
1. Factor the denominator to locate every pole
2. Confirm the numerator degree is lower than the denominator; divide out first if not
3. Write one term per distinct pole and one extra term per repetition
4. Find each residue by the cover-up rule, using differentiation for repeated poles
5. Keep complex conjugate pairs as a real quadratic
6. Look up each term and sum the time functions
COST AND BEHAVIOUR
Best: O(n) for n distinct real poles
Typical: O(n) cover-up evaluations
Worst: O(m²) derivative evaluations for a pole of multiplicity m
WHAT THAT MEANS
Improper fractions must be reduced by long division first, or the impulse term is lost.
Source: Engineering Circuit Analysis, 8th ed., Ch. 14, pp. 546-553 | CO4 | Bloom L3
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Factor the denominator to locate every pole - and check everyone has written it before moving on. At the cost panel, translate it: Improper fractions must be reduced by long division first, or the impulse term is lost. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 4: Laplace Transformation and Applications. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 14, pp. 546-553. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 13
Inverse transform by partial fractions - worked example
One concrete case, carried all the way to a stated number.
VTU BEC303 | Module 4
Inverse transform by partial fractions
13
GIVEN
F(s) = (s + 4)/(s(s + 2)).
1. Write F(s) = A/s + B/(s + 2)
2. Cover up s and evaluate at s = 0: A = (0 + 4)/(0 + 2) = 2
3. Cover up (s + 2) and evaluate at s = −2: B = (−2 + 4)/(−2) = −1
4. F(s) = 2/s − 1/(s + 2)
RESULT
f(t) = 2 − e^(−2t) for t ≥ 0; the check f(0) = 1 matches the initial-value theorem applied to the original F(s).
F(s) = (s+4)/(s(s+2)) = A/s + B/(s+2)
A = (s+4)/(s+2)|_{s=0} = 2, B = (s+4)/s|_{s=−2} = −1
f(t) = 2 − e^{−2t}
THE MISTAKE STUDENTS MAKE
Students expand a fraction whose numerator degree equals or exceeds the denominator degree without dividing first. The quotient contributes a constant that inverse-transforms to an impulse, and skipping it silently deletes a real part of the response.
Source: Engineering Circuit Analysis, 8th ed., Ch. 14, pp. 546-553 | CO4 | Bloom L3
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is F(s) = (s + 4)/(s(s + 2)). Work at the pace of the slowest note-taker and land hard on the result: f(t) = 2 − e^(−2t) for t ≥ 0; the check f(0) = 1 matches the initial-value theorem applied to the original F(s). Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 4: Laplace Transformation and Applications. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 14, pp. 546-553. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 14
Basic theorems: linearity, shifting, differentiation and integration
What it is, why it works, and what it costs.
VTU BEC303 | Module 4
Basic theorems: linearity, shifting,…
14
THE MECHANISM
Five theorems do almost all the work. Linearity lets a sum be transformed term by term. The time-shift theorem says f(t − a)·u(t − a) transforms to e^(−as)·F(s), which is how delayed pulses are handled. The frequency-shift theorem says e^(−at)f(t) transforms to F(s + a), which generates every damped form. The differentiation theorem, df/dt → s·F(s) − f(0−), is the crucial one for circuits: it converts a derivative into multiplication by s and deposits the initial condition directly into the algebra. The integration theorem, ∫f dt → F(s)/s, does the reverse and generates the capacitor and inductor s-domain models.
KEY TERMS
• linearity
• time shift
• frequency shift
• differentiation theorem
• integration theorem
TAKEAWAY
The differentiation theorem is why the s-domain handles initial conditions for free — the f(0−) term is the initial condition.
DIAGRAM FOR PHASE 2
A console panel with five labelled slots arranged vertically. Slot 1 "Linearity": a·f + b·g ↔ a·F + b·G. Slot 2 "Time shift": f(t−a)u(t−a) ↔ e^(−as)F(s), with a small waveform sliding right and an e^(−as) tag…
Source: Engineering Circuit Analysis, 8th ed., Ch. 14, pp. 553-561
CO4 | Bloom L3 | visual id: five-theorems-console
Notes: What to say: Give them the idea before the formalism. Say it plainly first: Five theorems do almost all the work. Then add the part they are examined on - The differentiation theorem is why the s-domain handles initial conditions for free — the f(0−) term is the initial conditio… Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "linearity" constrain here, and what would break if it did not hold? Animation instructions: slots light up top to bottom, each with its small animation — the waveform sliding for slot 2, the envelope wrapping for slot 3 — and the green box on slot 4 pulsing twice at the end. Transition style: Fade [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 4: Laplace Transformation and Applications. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 14, pp. 553-561. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 15
Basic theorems: linearity, shifting, differentiation an… - how it works
The procedure in order, and what each pass costs you.
VTU BEC303 | Module 4
Basic theorems: linearity, shifting,…
15
1. Decompose the expression into standard functions and operations
2. Apply linearity to split sums
3. Apply the time-shift theorem to any delayed term
4. Apply the frequency-shift theorem to any e^(−at) factor
5. Replace each derivative using s·F(s) − f(0−)
6. Replace each integral using F(s)/s
COST AND BEHAVIOUR
Best: O(1) per theorem application
Typical: O(k) for k terms
Worst: O(k·m) for m-fold derivatives
WHAT THAT MEANS
For an mth derivative, m initial-condition terms appear, which is exactly the number a differential equation of that order needs.
Source: Engineering Circuit Analysis, 8th ed., Ch. 14, pp. 553-561 | CO4 | Bloom L3
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Decompose the expression into standard functions and operations - and check everyone has written it before moving on. At the cost panel, translate it: For an mth derivative, m initial-condition terms appear, which is exactly the number a differential equation of that order needs. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 4: Laplace Transformation and Applications. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 14, pp. 553-561. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 16
Basic theorems: linearity, shifting, differentiation an… - worked example
One concrete case, carried all the way to a stated number.
VTU BEC303 | Module 4
Basic theorems: linearity, shifting,…
16
GIVEN
Transform the equation 2·di/dt + 6i = 12·u(t), with i(0−) = 3 A.
1. Apply the differentiation theorem: 2[sI(s) − 3] + 6I(s) = 12/s
2. Expand: 2sI(s) − 6 + 6I(s) = 12/s
3. Collect: I(s)(2s + 6) = 12/s + 6
4. I(s) = (12 + 6s)/(s(2s + 6)) = (6s + 12)/(2s(s + 3))
RESULT
I(s) = (3s + 6)/(s(s + 3)); the initial condition of 3 A entered as the −6 term without any separate boundary-condition step.
2 di/dt + 6i = 12u(t), i(0−) = 3
2[sI − 3] + 6I = 12/s
I(s) = (3s + 6)/(s(s+3))
THE MISTAKE STUDENTS MAKE
Students drop the f(0−) term in the differentiation theorem and then add the initial condition separately at the end. The whole advantage of the method is that the term is already there; adding it twice, or not at all, is the standard way to get a wrong transient.
Source: Engineering Circuit Analysis, 8th ed., Ch. 14, pp. 553-561 | CO4 | Bloom L3
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is Transform the equation 2·di/dt + 6i = 12·u(t), with i(0−) = 3 A. Work at the pace of the slowest note-taker and land hard on the result: I(s) = (3s + 6)/(s(s + 3)); the initial condition of 3 A entered as the −6 term without any separate boundary-condition step. Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 4: Laplace Transformation and Applications. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 14, pp. 553-561. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 17
Initial-value and final-value theorems
What it is, why it works, and what it costs.
VTU BEC303 | Module 4
Initial-value and final-value theorems
17
THE MECHANISM
The initial-value theorem states f(0+) = lim(s→∞) s·F(s), and the final-value theorem states f(∞) = lim(s→0) s·F(s). Both let an endpoint be read off the s-domain answer without inverting it, which makes them the cheapest possible check on a partial-fraction expansion. The final-value theorem carries an essential condition: every pole of s·F(s) must lie strictly in the left half plane. If a pole sits on the imaginary axis the function oscillates forever and has no final value, and if a pole lies in the right half plane the function grows without bound — in both cases the theorem will still return a finite number, and that number is meaningless.
KEY TERMS
• initial-value theorem
• final-value theorem
• validity condition
• sanity check
TAKEAWAY
Both theorems are free checks, but the final-value theorem lies confidently when a pole is not strictly in the left half plane.
DIAGRAM FOR PHASE 2
Two circular gauge dials side by side. Left gauge "Initial value" has its needle driven by the expression lim(s→∞) sF(s) printed beneath, with a small time plot showing the t = 0+ point highlighted. Right gaug…
Source: Engineering Circuit Analysis, 8th ed., Ch. 14, pp. 561-564
CO4 | Bloom L4 | visual id: value-theorems-gauges
Notes: What to say: Give them the idea before the formalism. Say it plainly first: The initial-value theorem states f(0+) = lim(s→∞) s·F(s), and the final-value theorem states f(∞) = lim(s→0) s·F(s). Then add the part they are examined on - Both theorems are free checks, but the final-value theorem lies confidently when a pole is not strictly in the left half pla… Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "initial-value theorem" constrain here, and what would break if it did not hold? Animation instructions: left gauge needle sweeps to its reading with its time plot, then the right gauge sweeps, then the red banner slides up and the s-plane inset shades in three stages: green LHP, red axis, red RHP. Transition style: Fade [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 4: Laplace Transformation and Applications. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 14, pp. 561-564. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 18
Initial-value and final-value theorems - how it works
The procedure in order, and what each pass costs you.
VTU BEC303 | Module 4
Initial-value and final-value theorems
18
1. Form s·F(s)
2. For the initial value, take the limit as s → ∞
3. Before using the final-value theorem, factor s·F(s) and locate every pole
4. Confirm every pole has a strictly negative real part
5. If so, take the limit as s → 0
6. If not, report that no final value exists
COST AND BEHAVIOUR
Best: O(1) limit evaluation
Typical: O(1) plus a pole check
Worst: factoring the denominator to verify pole locations
WHAT THAT MEANS
The pole check is the only part with any cost, and skipping it is what makes the theorem dangerous.
Source: Engineering Circuit Analysis, 8th ed., Ch. 14, pp. 561-564 | CO4 | Bloom L4
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Form s·F(s) - and check everyone has written it before moving on. At the cost panel, translate it: The pole check is the only part with any cost, and skipping it is what makes the theorem dangerous. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 4: Laplace Transformation and Applications. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 14, pp. 561-564. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 19
Initial-value and final-value theorems - worked example
One concrete case, carried all the way to a stated number.
VTU BEC303 | Module 4
Initial-value and final-value theorems
19
GIVEN
F(s) = (3s + 6)/(s(s + 3)) from the previous unit.
1. s·F(s) = (3s + 6)/(s + 3)
2. Initial value: as s → ∞, this tends to 3 — matching i(0−) = 3 A
3. Poles of s·F(s): only s = −3, strictly in the left half plane, so the theorem applies
4. Final value: as s → 0, this tends to 6/3 = 2 A
RESULT
The current starts at 3 A and settles at 2 A, both read directly from F(s) without any inverse transform.
sF(s) = (3s+6)/(s+3)
f(0+) = lim_{s→∞} = 3 A
poles of sF(s): s = −3 (LHP) ✓ ⇒ f(∞) = 6/3 = 2 A
THE MISTAKE STUDENTS MAKE
Students apply the final-value theorem to a purely oscillatory response, where s·F(s) has poles on the jω axis. The limit returns zero, which looks like a settled circuit, when in fact the response oscillates undiminished forever.
Source: Engineering Circuit Analysis, 8th ed., Ch. 14, pp. 561-564 | CO4 | Bloom L4
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is F(s) = (3s + 6)/(s(s + 3)) from the previous unit. Work at the pace of the slowest note-taker and land hard on the result: The current starts at 3 A and settles at 2 A, both read directly from F(s) without any inverse transform. Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 4: Laplace Transformation and Applications. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 14, pp. 561-564. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 20
Z(s) and Y(s): impedance in the s-domain
What it is, why it works, and what it costs.
VTU BEC303 | Module 4
Z(s) and Y(s): impedance in the s-dom…
20
THE MECHANISM
Applying the differentiation and integration theorems to the element laws gives the s-domain impedances directly: a resistor is R, an inductor is sL and a capacitor is 1/(sC). These generalise the phasor impedances of Module 1, which are recovered by setting s = jω, and they generalise them usefully — because s carries both a decay rate σ and a frequency ω, the s-domain impedance describes transient and steady-state behaviour at once. With these substitutions, series and parallel combination rules, voltage and current division, and every Module 1 and Module 2 technique apply unchanged, now operating on rational functions of s rather than on numbers.
KEY TERMS
• generalised impedance
• sL
• 1/sC
• driving-point impedance
• operational impedance
TAKEAWAY
Replace R, L and C by R, sL and 1/sC and every DC technique you own becomes a full transient solver.
DIAGRAM FOR PHASE 2
A three-column table. Column 1 "Element": resistor, inductor, capacitor symbols. Column 2 "Phasor (s = jω)": R, jωL, 1/(jωC). Column 3 "s-domain": R, sL, 1/(sC). An arrow spans columns 2 to 3 labelled "jω → s:…
Source: Engineering Circuit Analysis, 8th ed., Ch. 15, pp. 571-578
CO4 | Bloom L3 | visual id: impedance-generalisation-ladder
Notes: What to say: Give them the idea before the formalism. Say it plainly first: Applying the differentiation and integration theorems to the element laws gives the s-domain impedances directly: a resistor is R, an inductor is sL and a… Then add the part they are examined on - Replace R, L and C by R, sL and 1/sC and every DC technique you own becomes a full transient solver. Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "generalised impedance" constrain here, and what would break if it did not hold? Animation instructions: table rows fill in left to right, then the generalisation arrow sweeps from column 2 to column 3, then the s-plane point appears with its projections, then the two mini circuits fade in. Transition style: Fade [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 4: Laplace Transformation and Applications. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 15, pp. 571-578. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 21
Z(s) and Y(s): impedance in the s-domain - how it works
The procedure in order, and what each pass costs you.
VTU BEC303 | Module 4
Z(s) and Y(s): impedance in the s-dom…
21
1. Replace every resistor by R
2. Replace every inductor by sL
3. Replace every capacitor by 1/(sC)
4. Transform every source using the transform table
5. Apply series, parallel, division, nodal or mesh exactly as in DC
6. Solve for the required quantity as a rational function of s
COST AND BEHAVIOUR
Best: O(n) for a series or parallel chain
Typical: same structure as the DC problem, with polynomial arithmetic
Worst: polynomial division and factoring dominate for large networks
WHAT THAT MEANS
The cost moves from repeated numeric solves to a single symbolic one.
Source: Engineering Circuit Analysis, 8th ed., Ch. 15, pp. 571-578 | CO4 | Bloom L3
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Replace every resistor by R - and check everyone has written it before moving on. At the cost panel, translate it: The cost moves from repeated numeric solves to a single symbolic one. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 4: Laplace Transformation and Applications. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 15, pp. 571-578. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 22
Z(s) and Y(s): impedance in the s-domain - worked example
One concrete case, carried all the way to a stated number.
VTU BEC303 | Module 4
Z(s) and Y(s): impedance in the s-dom…
22
GIVEN
A series R = 1 kΩ and C = 1 µF driven by a 10 V step, capacitor initially uncharged.
1. Z(s) = 1000 + 1/(1e−6·s) = 1000 + 1e6/s
2. Source: 10/s
3. I(s) = (10/s)/(1000 + 1e6/s) = 10/(1000s + 1e6) = 0.01/(s + 1000)
4. Inverse transform: i(t) = 0.01·e^(−1000t) A
RESULT
i(t) = 10·e^(−1000t) mA, with the pole at s = −1000 corresponding exactly to τ = RC = 1 ms.
Z(s) = R + 1/sC = 1000 + 10⁶/s
I(s) = (10/s)/Z(s) = 0.01/(s+1000)
i(t) = 10 e^{−1000t} mA (pole −1000 ⇔ τ = 1 ms)
THE MISTAKE STUDENTS MAKE
Students write the capacitor impedance as sC by analogy with the inductor. The capacitor law integrates, so its impedance divides by s — writing sC makes a capacitor behave like an inductor and inverts the entire frequency response.
Source: Engineering Circuit Analysis, 8th ed., Ch. 15, pp. 571-578 | CO4 | Bloom L3
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is A series R = 1 kΩ and C = 1 µF driven by a 10 V step, capacitor initially uncharged. Work at the pace of the slowest note-taker and land hard on the result: i(t) = 10·e^(−1000t) mA, with the pole at s = −1000 corresponding exactly to τ = RC = 1 ms. Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 4: Laplace Transformation and Applications. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 15, pp. 571-578. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 23
Initial conditions as sources in the s-domain
What it is, why it works, and what it costs.
VTU BEC303 | Module 4
Initial conditions as sources in the…
23
THE MECHANISM
The initial-condition terms produced by the differentiation theorem can be drawn as sources rather than carried as algebra. An inductor with initial current i(0−) becomes an impedance sL in series with a voltage source of value L·i(0−), or equivalently sL in parallel with a current source i(0−)/s. A capacitor with initial voltage v(0−) becomes 1/(sC) in series with a voltage source v(0−)/s, or in parallel with a current source C·v(0−). Once these models are in place the network is a pure impedance network with sources, and a single algebraic solve produces the complete response — natural and forced together — with no separate initial-condition stage at all.
KEY TERMS
• initial-condition generator
• L·i(0−) source
• v(0−)/s source
• equivalent model
TAKEAWAY
Initial conditions become sources, so the s-domain circuit needs one solve where the time domain needed three.
DIAGRAM FOR PHASE 2
A two-row, two-column grid of element models. Row 1 "Inductor, i(0−)": left cell shows sL in series with a battery symbol labelled L·i(0−); right cell shows sL in parallel with a current-source symbol labelled…
Source: Engineering Circuit Analysis, 8th ed., Ch. 15, pp. 571-578
CO4 | Bloom L4 | visual id: initial-condition-source-models
Notes: What to say: Give them the idea before the formalism. Say it plainly first: The initial-condition terms produced by the differentiation theorem can be drawn as sources rather than carried as algebra. Then add the part they are examined on - Initial conditions become sources, so the s-domain circuit needs one solve where the time domain needed three. Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "initial-condition generator" constrain here, and what would break if it did not hold? Animation instructions: the grid outline draws, the four cells populate row by row with the source symbols snapping into place, then the column divider label appears, then the banner slides up. Transition style: Fade [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 4: Laplace Transformation and Applications. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 15, pp. 571-578. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 24
Initial conditions as sources in the s-domain - how it works
The procedure in order, and what each pass costs you.
VTU BEC303 | Module 4
Initial conditions as sources in the…
24
1. Find v_C(0−) and i_L(0−) from the pre-switching steady state
2. Replace each inductor by sL in series with L·i(0−)
3. Replace each capacitor by 1/(sC) in series with v(0−)/s
4. Check the polarity of each initial-condition source against the assumed reference direction
5. Solve the resulting impedance network algebraically
6. Inverse transform the result
COST AND BEHAVIOUR
Best: one algebraic solve
Typical: one solve plus one partial-fraction expansion
Worst: a high-order partial fraction with repeated poles
WHAT THAT MEANS
Replaces the three-stage time-domain pipeline with a single pass.
Source: Engineering Circuit Analysis, 8th ed., Ch. 15, pp. 571-578 | CO4 | Bloom L4
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Find v_C(0−) and i_L(0−) from the pre-switching steady state - and check everyone has written it before moving on. At the cost panel, translate it: Replaces the three-stage time-domain pipeline with a single pass. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 4: Laplace Transformation and Applications. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 15, pp. 571-578. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 25
Initial conditions as sources in the s-domain - worked example
One concrete case, carried all the way to a stated number.
VTU BEC303 | Module 4
Initial conditions as sources in the…
25
GIVEN
An inductor L = 2 H carrying 3 A at t = 0−, in series with 6 Ω and a 12 V step.
1. Inductor model: 2s in series with a source of L·i(0−) = 6 V, aiding the current
2. Loop: I(s) = (12/s + 6)/(2s + 6)
3. Simplify: I(s) = (12 + 6s)/(s(2s + 6)) = (6s + 12)/(2s(s + 3)) = (3s + 6)/(s(s+3))
4. Partial fractions: 2/s + 1/(s + 3)
RESULT
i(t) = 2 + e^(−3t) A, starting at 3 A and settling at 2 A — both endpoints matching the value theorems applied earlier.
L model: sL in series with L·i(0−) = 6 V
I(s) = (12/s + 6)/(2s + 6) = 2/s + 1/(s+3)
i(t) = 2 + e^{−3t} A
THE MISTAKE STUDENTS MAKE
Students give the initial-condition source the wrong polarity, so the transient adds where it should subtract. The check is immediate: evaluate the result at t = 0 and confirm it reproduces the known initial current or voltage.
Source: Engineering Circuit Analysis, 8th ed., Ch. 15, pp. 571-578 | CO4 | Bloom L4
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is An inductor L = 2 H carrying 3 A at t = 0−, in series with 6 Ω and a 12 V step. Work at the pace of the slowest note-taker and land hard on the result: i(t) = 2 + e^(−3t) A, starting at 3 A and settling at 2 A — both endpoints matching the value theorems applied earlier. Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 4: Laplace Transformation and Applications. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 15, pp. 571-578. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 26
Nodal and mesh analysis in the s-domain
What it is, why it works, and what it costs.
VTU BEC303 | Module 4
Nodal and mesh analysis in the s-doma…
26
THE MECHANISM
Nodal and mesh analysis proceed in the s-domain exactly as in DC, with conductances replaced by admittances Y(s) and resistances by impedances Z(s). The coefficient matrix now contains rational functions of s rather than numbers, so the elimination is symbolic and the answer emerges as a ratio of polynomials. Supernodes and supermeshes are formed for the same reasons and dependent sources handled the same way. The single algebraic solution contains the complete response — natural, forced, and initial-condition contributions all folded together — which is the decisive advantage over the time-domain method, where each of those had to be found separately and then combined.
KEY TERMS
• s-domain nodal analysis
• polynomial matrix
• symbolic solve
• complete response
TAKEAWAY
One symbolic nodal solve in s replaces the whole natural-plus-forced-plus-initial-condition assembly.
DIAGRAM FOR PHASE 2
Left: a two-node circuit drawn with s-domain element labels — R, sL, 1/(sC) — and an initial-condition source attached to the inductor. Right: a 2×2 matrix whose entries are rational expressions in s, beside a…
Source: Engineering Circuit Analysis, 8th ed., Ch. 15, pp. 578-585
CO4 | Bloom L4 | visual id: s-domain-nodal-matrix
Notes: What to say: Give them the idea before the formalism. Say it plainly first: Nodal and mesh analysis proceed in the s-domain exactly as in DC, with conductances replaced by admittances Y(s) and resistances by impedances Z(s). Then add the part they are examined on - One symbolic nodal solve in s replaces the whole natural-plus-forced-plus-initial-condition assembly. Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "s-domain nodal analysis" constrain here, and what would break if it did not hold? Animation instructions: circuit fades in, matrix entries populate one by one, the green initial-condition terms land in the right-hand vector last, then V(s) appears, then the decomposition strip peels into its three labelled parts. Transition style: Fade [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 4: Laplace Transformation and Applications. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 15, pp. 578-585. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 27
Nodal and mesh analysis in the s-domain - how it works
The procedure in order, and what each pass costs you.
VTU BEC303 | Module 4
Nodal and mesh analysis in the s-doma…
27
1. Transform every source and replace every element by its s-domain impedance
2. Insert initial-condition sources for every energised inductor and capacitor
3. Choose a reference node and write KCL with admittances, or write KVL with impedances
4. Form supernodes or supermeshes where required
5. Solve the symbolic system for the required quantity
6. Expand by partial fractions and inverse transform
COST AND BEHAVIOUR
Best: O(1) for a single-node divider
Typical: O(n^3) symbolic elimination on polynomials
Worst: polynomial degree growth makes symbolic elimination markedly more expensive than the numeric case
WHAT THAT MEANS
Prefer reducing the network before solving; polynomial arithmetic punishes unnecessary nodes.
Source: Engineering Circuit Analysis, 8th ed., Ch. 15, pp. 578-585 | CO4 | Bloom L4
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Transform every source and replace every element by its s-domain impedance - and check everyone has written it before moving on. At the cost panel, translate it: Prefer reducing the network before solving; polynomial arithmetic punishes unnecessary nodes. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 4: Laplace Transformation and Applications. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 15, pp. 578-585. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 28
Nodal and mesh analysis in the s-domain - worked example
One concrete case, carried all the way to a stated number.
VTU BEC303 | Module 4
Nodal and mesh analysis in the s-doma…
28
GIVEN
A 10/s V source through R = 2 Ω to a node with L = 1 H to ground, inductor initially unenergised.
1. Node admittances: 1/2 from the source side, 1/s from the inductor
2. KCL: (V − 10/s)/2 + V/s = 0
3. Multiply by 2s: s·V − 10 + 2V = 0
4. V(s) = 10/(s + 2)
RESULT
v(t) = 10·e^(−2t) V; a single symbolic solve produced the complete transient with no separate initial-condition step.
(V − 10/s)/2 + V/s = 0
sV − 10 + 2V = 0
V(s) = 10/(s+2) ⇒ v(t) = 10 e^{−2t} V
THE MISTAKE STUDENTS MAKE
Students clear denominators carelessly and lose a factor of s, which shifts a pole to the wrong place. Since the pole locations are the entire transient behaviour, an algebra slip here changes the answer qualitatively rather than slightly.
Source: Engineering Circuit Analysis, 8th ed., Ch. 15, pp. 578-585 | CO4 | Bloom L4
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is A 10/s V source through R = 2 Ω to a node with L = 1 H to ground, inductor initially unenergised. Work at the pace of the slowest note-taker and land hard on the result: v(t) = 10·e^(−2t) V; a single symbolic solve produced the complete transient with no separate initial-condition step. Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 4: Laplace Transformation and Applications. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 15, pp. 578-585. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 29
Thévenin, Norton and superposition in the s-domain
What it is, why it works, and what it costs.
VTU BEC303 | Module 4
Thévenin, Norton and superposition in…
29
THE MECHANISM
Every theorem from Module 2 transfers into the s-domain with resistance replaced by Z(s). A Thévenin equivalent now consists of V_th(s), a rational function, in series with Z_th(s), also rational; this is powerful because a load can then be swept in the s-domain and each case inverse-transformed separately. Superposition applies to transforms directly, so a circuit with several sources and several energised elements can be decomposed by contribution — and unlike the time domain, sources at different frequencies need no special treatment, because each simply contributes its own transform to the same algebraic sum. Source transformation becomes V_th(s) = I_N(s)·Z_th(s).
KEY TERMS
• Z_th(s)
• s-domain equivalent
• superposition of transforms
• source transformation in s
TAKEAWAY
In the s-domain, sources at different frequencies stop being a special case — they are just different rational terms.
DIAGRAM FOR PHASE 2
Three stacked rows, each showing a DC form on the left and its s-domain counterpart on the right, joined by an arrow labelled "R → Z(s)". Row 1: Thévenin, V_th with R_th becoming V_th(s) with Z_th(s), both dra…
Source: Engineering Circuit Analysis, 8th ed., Ch. 15, pp. 585-588
CO4 | Bloom L4 | visual id: s-domain-theorem-carry
Notes: What to say: Give them the idea before the formalism. Say it plainly first: Every theorem from Module 2 transfers into the s-domain with resistance replaced by Z(s). Then add the part they are examined on - In the s-domain, sources at different frequencies stop being a special case — they are just different rational terms. Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "Z_th(s)" constrain here, and what would break if it did not hold? Animation instructions: each row's DC form appears, the arrow sweeps right, the s-domain form appears; after row 3 completes, the green badge pops in and pulses. Transition style: Fade [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 4: Laplace Transformation and Applications. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 15, pp. 585-588. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 30
Thévenin, Norton and superposition in the s-domain - how it works
The procedure in order, and what each pass costs you.
VTU BEC303 | Module 4
Thévenin, Norton and superposition in…
30
1. Transform the network into the s-domain including initial-condition sources
2. Detach the load at the port of interest
3. Compute V_th(s) as the open-circuit transform
4. Compute Z_th(s) by look-back or by a test source, as in Module 2
5. Reattach the load and solve the two-element s-domain circuit
6. Inverse transform the result
COST AND BEHAVIOUR
Best: one reduction reused across every load
Typical: two symbolic solves
Worst: two symbolic solves with high-degree polynomials
WHAT THAT MEANS
The payoff is larger than in DC, because each avoided solve is a symbolic one.
Source: Engineering Circuit Analysis, 8th ed., Ch. 15, pp. 585-588 | CO4 | Bloom L4
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Transform the network into the s-domain including initial-condition sources - and check everyone has written it before moving on. At the cost panel, translate it: The payoff is larger than in DC, because each avoided solve is a symbolic one. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 4: Laplace Transformation and Applications. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 15, pp. 585-588. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 31
Thévenin, Norton and superposition in the s-domain - worked example
One concrete case, carried all the way to a stated number.
VTU BEC303 | Module 4
Thévenin, Norton and superposition in…
31
GIVEN
A 10/s source in series with 1 Ω and 1 H; find the s-domain Thévenin equivalent at the inductor terminals.
1. Remove the inductor; V_th(s) = 10/s, since no current flows through the 1 Ω
2. Deactivate the source: Z_th(s) = 1 Ω
3. Equivalent: 10/s in series with 1 Ω
4. Reattach the inductor: I(s) = (10/s)/(1 + s) = 10/(s(s+1))
RESULT
I(s) = 10/(s(s+1)), which inverts to i(t) = 10(1 − e^(−t)) A — the familiar rising exponential, obtained through a two-element equivalent.
V_th(s) = 10/s, Z_th(s) = 1 Ω
I(s) = (10/s)/(1+s) = 10/(s(s+1))
i(t) = 10(1 − e^{−t}) A
THE MISTAKE STUDENTS MAKE
Students forget that Z_th(s) must include the impedance contributions of any energised storage element, while its initial-condition source belongs to V_th(s). Mixing the two puts an initial condition into the impedance, which is dimensionally wrong and produces a spurious pole.
Source: Engineering Circuit Analysis, 8th ed., Ch. 15, pp. 585-588 | CO4 | Bloom L4
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is A 10/s source in series with 1 Ω and 1 H; find the s-domain Thévenin equivalent at the inductor terminals. Work at the pace of the slowest note-taker and land hard on the result: I(s) = 10/(s(s+1)), which inverts to i(t) = 10(1 − e^(−t)) A — the familiar rising exponential, obtained through a two-element eq… Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 4: Laplace Transformation and Applications. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 15, pp. 585-588. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 32
Transfer functions, poles and zeros
What it is, why it works, and what it costs.
VTU BEC303 | Module 4
Transfer functions, poles and zeros
32
THE MECHANISM
The transfer function H(s) is the ratio of an output transform to an input transform with all initial conditions set to zero, H(s) = Y(s)/X(s). It is a property of the network alone, independent of the excitation, which is what makes it the compact description of a circuit's behaviour. Its zeros are the roots of the numerator — frequencies the network blocks completely — and its poles are the roots of the denominator, which are the natural frequencies of the circuit and are identical to the roots of the characteristic equation met in Module 3. Because the poles determine the natural response and the zeros shape the forced response, a pole-zero plot conveys the circuit's dynamic behaviour at a glance.
KEY TERMS
• transfer function H(s)
• pole
• zero
• zero-state response
• characteristic equation
TAKEAWAY
Poles are the circuit's natural frequencies and zeros are what it blocks — together they are the circuit, independent of any input.
DIAGRAM FOR PHASE 2
Left: an s-plane with the real axis σ and imaginary axis jω. Two crosses mark a complex conjugate pole pair in the left half plane and a circle marks a zero on the real axis. Dotted construction lines show the…
Source: Engineering Circuit Analysis, 8th ed., Ch. 15, pp. 588-589
CO4 | Bloom L4 | visual id: pole-zero-map-to-response
Notes: What to say: Give them the idea before the formalism. Say it plainly first: The transfer function H(s) is the ratio of an output transform to an input transform with all initial conditions set to zero, H(s) = Y(s)/X(s). Then add the part they are examined on - Poles are the circuit's natural frequencies and zeros are what it blocks — together they are the circuit, independent of any… Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "transfer function H(s)" constrain here, and what would break if it did not hold? Animation instructions: axes draw, the pole crosses appear, the zero circle appears, then the α and ω_d construction lines extend, then the time response draws, then the two curved mapping arrows sweep across from pole to envelope and from pole to ringing period. Transition style: Fade [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 4: Laplace Transformation and Applications. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 15, pp. 588-589. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 33
Transfer functions, poles and zeros - how it works
The procedure in order, and what each pass costs you.
VTU BEC303 | Module 4
Transfer functions, poles and zeros
33
1. Set all initial conditions to zero
2. Transform the network into the s-domain
3. Compute the required output transform in terms of the input transform
4. Form the ratio H(s) = Y(s)/X(s)
5. Factor the numerator for zeros and the denominator for poles
6. Plot them on the s-plane and read the response character from their positions
COST AND BEHAVIOUR
Best: O(1) for a first-order divider
Typical: one symbolic solve plus a factoring step
Worst: root finding on a high-degree polynomial
WHAT THAT MEANS
The pole-zero plot is the cheapest complete summary of a linear circuit that exists.
Source: Engineering Circuit Analysis, 8th ed., Ch. 15, pp. 588-589 | CO4 | Bloom L4
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Set all initial conditions to zero - and check everyone has written it before moving on. At the cost panel, translate it: The pole-zero plot is the cheapest complete summary of a linear circuit that exists. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 4: Laplace Transformation and Applications. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 15, pp. 588-589. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 34
Transfer functions, poles and zeros - worked example
One concrete case, carried all the way to a stated number.
VTU BEC303 | Module 4
Transfer functions, poles and zeros
34
GIVEN
A series RC low-pass with R = 1 kΩ, C = 1 µF, output taken across C.
1. H(s) = (1/sC)/(R + 1/sC)
2. Multiply numerator and denominator by sC: H(s) = 1/(1 + sRC)
3. Substitute values: H(s) = 1/(1 + 0.001s) = 1000/(s + 1000)
4. One pole at s = −1000, no finite zeros
RESULT
H(s) = 1000/(s + 1000): a single pole at −1000 rad/s, which is simultaneously the reciprocal of τ and the −3 dB cutoff frequency.
H(s) = (1/sC)/(R + 1/sC) = 1/(1 + sRC)
= 1000/(s + 1000)
pole at s = −1000 rad/s, no finite zeros
THE MISTAKE STUDENTS MAKE
Students compute a transfer function with initial conditions still present. H(s) is defined for the zero-state response only; leaving an initial-condition source in place makes the ratio depend on the initial energy, so it is no longer a property of the network.
Source: Engineering Circuit Analysis, 8th ed., Ch. 15, pp. 588-589 | CO4 | Bloom L4
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is A series RC low-pass with R = 1 kΩ, C = 1 µF, output taken across C. Work at the pace of the slowest note-taker and land hard on the result: H(s) = 1000/(s + 1000): a single pole at −1000 rad/s, which is simultaneously the reciprocal of τ and the −3 dB cutoff frequency. Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 4: Laplace Transformation and Applications. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 15, pp. 588-589. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 35
Step, ramp and impulse responses
What it is, why it works, and what it costs.
VTU BEC303 | Module 4
Step, ramp and impulse responses
35
THE MECHANISM
The three standard responses are related by integration, because their inputs are. Since the step is the integral of the impulse and the ramp is the integral of the step, the step response is the integral of the impulse response and the ramp response is the integral of the step response. In the s-domain this is transparent: the impulse response transform is H(s) itself, the step response is H(s)/s and the ramp response is H(s)/s². The impulse response therefore characterises the system completely, and the other two follow without any further circuit analysis — which is why measuring or computing one of the three is enough.
KEY TERMS
• impulse response h(t)
• step response
• ramp response
• integration relationship
TAKEAWAY
Impulse, step and ramp responses are one function integrated repeatedly — compute one and the others follow by dividing by s.
DIAGRAM FOR PHASE 2
A three-stage chain running left to right. Stage 1: input δ(t) drawn as a spike, feeding a block H(s), producing an impulse response h(t) that decays. Stage 2: input u(t) as a step, same block, producing the s…
Source: Engineering Circuit Analysis, 8th ed., Ch. 14, pp. 543-546
CO4 | Bloom L4 | visual id: three-responses-integration-chain
Notes: What to say: Give them the idea before the formalism. Say it plainly first: The three standard responses are related by integration, because their inputs are. Then add the part they are examined on - Impulse, step and ramp responses are one function integrated repeatedly — compute one and the others follow by dividing by s. Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "impulse response h(t)" constrain here, and what would break if it did not hold? Animation instructions: stage 1 builds — spike, block, decaying response — then the integration arrow sweeps to stage 2 which builds, then again to stage 3; finally the three transforms type in along the bottom. Transition style: Fade [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 4: Laplace Transformation and Applications. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 14, pp. 543-546. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 36
Step, ramp and impulse responses - how it works
The procedure in order, and what each pass costs you.
VTU BEC303 | Module 4
Step, ramp and impulse responses
36
1. Obtain H(s) for the circuit with zero initial conditions
2. For the impulse response, inverse transform H(s) directly
3. For the step response, inverse transform H(s)/s
4. For the ramp response, inverse transform H(s)/s²
5. Alternatively integrate a known response in the time domain
6. Check each against the initial- and final-value theorems
COST AND BEHAVIOUR
Best: O(1) once H(s) is factored
Typical: one partial-fraction expansion per response
Worst: repeated poles at the origin for the ramp response
WHAT THAT MEANS
The ramp introduces a double pole at the origin, which needs the repeated-pole expansion rule.
Source: Engineering Circuit Analysis, 8th ed., Ch. 14, pp. 543-546 | CO4 | Bloom L4
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Obtain H(s) for the circuit with zero initial conditions - and check everyone has written it before moving on. At the cost panel, translate it: The ramp introduces a double pole at the origin, which needs the repeated-pole expansion rule. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 4: Laplace Transformation and Applications. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 14, pp. 543-546. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 37
Step, ramp and impulse responses - worked example
One concrete case, carried all the way to a stated number.
VTU BEC303 | Module 4
Step, ramp and impulse responses
37
GIVEN
H(s) = 1000/(s + 1000) from the RC low-pass.
1. Impulse response: h(t) = 1000·e^(−1000t)
2. Step response transform: 1000/(s(s + 1000)) = 1/s − 1/(s + 1000)
3. Step response: 1 − e^(−1000t)
4. Check: the derivative of the step response is 1000·e^(−1000t) = h(t)
RESULT
Impulse response 1000e^(−1000t) and step response 1 − e^(−1000t), each the derivative and integral of the other as required.
h(t) = L⁻¹{H(s)} = 1000 e^{−1000t}
step: L⁻¹{H(s)/s} = 1 − e^{−1000t}
d/dt[step] = h(t) ✓
THE MISTAKE STUDENTS MAKE
Students treat the impulse response as physically measurable by applying a very short pulse of unit height. The impulse has unit area, not unit height, so a 1 µs test pulse must have an amplitude of 10⁶ to approximate it — otherwise the measured response is scaled down by the pulse width.
Source: Engineering Circuit Analysis, 8th ed., Ch. 14, pp. 543-546 | CO4 | Bloom L4
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is H(s) = 1000/(s + 1000) from the RC low-pass. Work at the pace of the slowest note-taker and land hard on the result: Impulse response 1000e^(−1000t) and step response 1 − e^(−1000t), each the derivative and integral of the other as required. Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 4: Laplace Transformation and Applications. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 14, pp. 543-546. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 38
Waveform synthesis
What it is, why it works, and what it costs.
VTU BEC303 | Module 4
Waveform synthesis
38
THE MECHANISM
Waveform synthesis is the practice of writing an arbitrary piecewise-linear waveform as a sum of shifted steps, ramps and impulses, so that its transform can be written down term by term instead of integrated piecewise. A step creates a jump, a ramp creates a change of slope, and an impulse creates a spike; since any piecewise-linear signal is fully described by its jumps and slope changes, these three blocks are sufficient. The method is to walk along the waveform and add a block wherever a discontinuity or a slope change occurs, using the difference between the new and old values or slopes as the block's coefficient. The transform then follows by applying the time-shift theorem to each block.
KEY TERMS
• piecewise waveform
• building blocks
• shifted steps and ramps
• synthesis by superposition
TAKEAWAY
Add a step at every jump and a ramp at every slope change, and the transform writes itself.
DIAGRAM FOR PHASE 2
Top: a target trapezoidal pulse rising linearly from 0 to A over 0 to t₁, flat to t₂, then falling to 0 by t₃. Below it, four component waveforms stacked, each in its own colour: a ramp starting at 0 with slop…
Source: Network Analysis - A Simplified Approach (TB2, not supplied) - TB2 §6.8
CO4 | Bloom L4 | visual id: waveform-synthesis-decomposition
Notes: What to say: Give them the idea before the formalism. Say it plainly first: Waveform synthesis is the practice of writing an arbitrary piecewise-linear waveform as a sum of shifted steps, ramps and impulses, so that its transform… Then add the part they are examined on - Add a step at every jump and a ramp at every slope change, and the transform writes itself. Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "piecewise waveform" constrain here, and what would break if it did not hold? Animation instructions: the target waveform draws, then each component appears in turn with its marker flashing on the target, then the components visibly stack and sum to reproduce the target, then the transform expression types in. Transition style: Fade [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 4: Laplace Transformation and Applications. Assigned by the syllabus to TB2: K. Channa Venkatesh and D. Ganesh Rao, Network Analysis - A Simplified Approach, Cengage India, 2nd ed., 2012; TB2 §6.8. TB2 was NOT supplied in this environment, so this unit is aligned to the verbatim syllabus headings, cites only the chapter the syllabus gives, and claims no page numbers.

## Slide 39
Waveform synthesis - how it works
The procedure in order, and what each pass costs you.
VTU BEC303 | Module 4
Waveform synthesis
39
1. Sketch the waveform and mark every jump and every slope change
2. At each jump of height ΔV, add ΔV·u(t − t_k)
3. At each slope change of Δm, add Δm·(t − t_k)·u(t − t_k)
4. Confirm the assembled sum reproduces the original at several test times
5. Apply the time-shift theorem to each term
6. Sum the transforms
COST AND BEHAVIOUR
Best: two blocks for a rectangular pulse
Typical: one block per breakpoint
Worst: O(k) blocks for k breakpoints
WHAT THAT MEANS
A waveform that is not piecewise linear needs a different decomposition entirely.
Source: Network Analysis - A Simplified Approach (TB2, not supplied) - TB2 §6.8 | CO4 | Bloom L4
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Sketch the waveform and mark every jump and every slope change - and check everyone has written it before moving on. At the cost panel, translate it: A waveform that is not piecewise linear needs a different decomposition entirely. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 4: Laplace Transformation and Applications. Assigned by the syllabus to TB2: K. Channa Venkatesh and D. Ganesh Rao, Network Analysis - A Simplified Approach, Cengage India, 2nd ed., 2012; TB2 §6.8. TB2 was NOT supplied in this environment, so this unit is aligned to the verbatim syllabus headings, cites only the chapter the syllabus gives, and claims no page numbers.

## Slide 40
Waveform synthesis - worked example
One concrete case, carried all the way to a stated number.
VTU BEC303 | Module 4
Waveform synthesis
40
GIVEN
A triangular pulse rising from 0 to 1 over 0 ≤ t ≤ 1 and falling back to 0 over 1 ≤ t ≤ 2.
1. Slope +1 starts at t = 0: add t·u(t)
2. Slope changes from +1 to −1 at t = 1, a change of −2: add −2(t−1)·u(t−1)
3. Slope changes from −1 to 0 at t = 2, a change of +1: add (t−2)·u(t−2)
4. Transform: 1/s² − 2e^(−s)/s² + e^(−2s)/s²
RESULT
F(s) = (1 − 2e^(−s) + e^(−2s))/s² = (1 − e^(−s))²/s², a compact form that would be tedious to obtain by direct integration.
f(t) = t·u(t) − 2(t−1)u(t−1) + (t−2)u(t−2)
F(s) = (1 − 2e^{−s} + e^{−2s})/s² = (1 − e^{−s})²/s²
THE MISTAKE STUDENTS MAKE
Students use the new slope as the coefficient of each ramp instead of the change in slope. For the triangular pulse that gives −1 at t = 1 instead of −2, producing a waveform that flattens rather than descending.
Source: Network Analysis - A Simplified Approach (TB2, not supplied) - TB2 §6.8 | CO4 | Bloom L4
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is A triangular pulse rising from 0 to 1 over 0 ≤ t ≤ 1 and falling back to 0 over 1 ≤ t ≤ 2. Work at the pace of the slowest note-taker and land hard on the result: F(s) = (1 − 2e^(−s) + e^(−2s))/s² = (1 − e^(−s))²/s², a compact form that would be tedious to obtain by direct integration. Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 4: Laplace Transformation and Applications. Assigned by the syllabus to TB2: K. Channa Venkatesh and D. Ganesh Rao, Network Analysis - A Simplified Approach, Cengage India, 2nd ed., 2012; TB2 §6.8. TB2 was NOT supplied in this environment, so this unit is aligned to the verbatim syllabus headings, cites only the chapter the syllabus gives, and claims no page numbers.

## Slide 41
Convolution
What it is, why it works, and what it costs.
VTU BEC303 | Module 4
Convolution
41
THE MECHANISM
Convolution is the time-domain operation corresponding to multiplication in the s-domain: if Y(s) = H(s)·X(s) then y(t) = ∫₀^t h(τ)·x(t − τ) dτ. Physically it says the output at any instant is the accumulated effect of every past input sample, each weighted by how much of its impulse response survives to the present — which is why the impulse response fully characterises a linear time-invariant circuit. In practice the s-domain route is almost always easier, and convolution is used when the impulse response is known only as measured data rather than as a formula, or when the input is not analytically transformable.
KEY TERMS
• convolution integral
• flip and slide
• multiplication in s
• zero-state response
TAKEAWAY
Convolution is what multiplication in s means physically — the present output is a weighted memory of past inputs.
DIAGRAM FOR PHASE 2
A three-track animation panel. Track 1 shows the input x(τ) as a rectangular pulse fixed in place. Track 2 shows h(t − τ), the impulse response flipped left-right and sliding rightward as t increases, drawn in…
Source: Engineering Circuit Analysis, 8th ed., Ch. 15, pp. 589-598
CO4 | Bloom L5 | visual id: convolution-flip-slide
Notes: What to say: Give them the idea before the formalism. Say it plainly first: Convolution is the time-domain operation corresponding to multiplication in the s-domain: if Y(s) = H(s)·X(s) then y(t) = ∫₀^t h(τ)·x(t − τ) dτ. Then add the part they are examined on - Convolution is what multiplication in s means physically — the present output is a weighted memory of past inputs. Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "convolution integral" constrain here, and what would break if it did not hold? Animation instructions: track 1 draws, track 2 appears flipped at the far left, then slides right in steps with the overlap shading and the arrow plotting a new point on track 3 at each step, then the side note appears once the output curve is complete. Transition style: Fade [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 4: Laplace Transformation and Applications. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 15, pp. 589-598. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 42
Convolution - how it works
The procedure in order, and what each pass costs you.
VTU BEC303 | Module 4
Convolution
42
1. Obtain the impulse response h(t)
2. Flip it in time to get h(−τ) and shift by t to get h(t − τ)
3. Multiply pointwise by x(τ)
4. Integrate the product from 0 to t
5. Repeat for each value of t to build the output
6. Prefer Y(s) = H(s)·X(s) whenever both transforms exist
COST AND BEHAVIOUR
Best: O(1) via s-domain multiplication
Typical: O(n²) for a direct numerical convolution of n samples
Worst: O(n²) without transform methods
WHAT THAT MEANS
The s-domain route converts an O(n²) integral into a polynomial multiplication, which is the entire point.
Source: Engineering Circuit Analysis, 8th ed., Ch. 15, pp. 589-598 | CO4 | Bloom L5
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Obtain the impulse response h(t) - and check everyone has written it before moving on. At the cost panel, translate it: The s-domain route converts an O(n²) integral into a polynomial multiplication, which is the entire point. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 4: Laplace Transformation and Applications. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 15, pp. 589-598. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 43
Convolution - worked example
One concrete case, carried all the way to a stated number.
VTU BEC303 | Module 4
Convolution
43
GIVEN
h(t) = e^(−t)·u(t) convolved with x(t) = u(t).
1. y(t) = ∫₀^t e^(−τ)·1 dτ
2. Integrate: [−e^(−τ)]₀^t
3. y(t) = 1 − e^(−t)
4. Check in the s-domain: H(s)X(s) = [1/(s+1)]·[1/s] = 1/s − 1/(s+1), which inverts to the same thing
RESULT
y(t) = 1 − e^(−t), confirmed by both routes — and the s-domain route took one line against three.
y(t) = ∫₀^t h(τ)x(t−τ)dτ = ∫₀^t e^{−τ}dτ = 1 − e^{−t}
s-domain: H(s)X(s) = 1/(s(s+1)) ⇒ same
THE MISTAKE STUDENTS MAKE
Students forget to flip one of the functions and compute a correlation instead of a convolution. For a symmetric h(t) the two agree and the error hides; for an asymmetric one — which every causal impulse response is — the answer is wrong.
Source: Engineering Circuit Analysis, 8th ed., Ch. 15, pp. 589-598 | CO4 | Bloom L5
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is h(t) = e^(−t)·u(t) convolved with x(t) = u(t). Work at the pace of the slowest note-taker and land hard on the result: y(t) = 1 − e^(−t), confirmed by both routes — and the s-domain route took one line against three. Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 4: Laplace Transformation and Applications. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 15, pp. 589-598. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 44
The complex-frequency plane and the first-order filter pole case study
What it is, why it works, and what it costs.
VTU BEC303 | Module 4
The complex-frequency plane and the f…
44
THE MECHANISM
A pole position on the s-plane encodes both the transient and the frequency behaviour of a circuit, and the first-order low-pass filter is the clearest demonstration. Its single pole at s = −1/RC sits on the negative real axis; the distance from the origin is simultaneously the reciprocal of the time constant and the −3 dB cutoff in radians per second. Moving the pole further from the origin widens the bandwidth and shortens the settling time in exactly the same proportion, so the product of bandwidth and rise time is a constant — approximately 0.35 when bandwidth is in hertz and rise time in seconds. This is the reason a fast circuit must be a wideband circuit, and why one cannot be improved without the other.
KEY TERMS
• s-plane geometry
• cutoff frequency
• bandwidth
• settling time
• pole-bandwidth link
TAKEAWAY
Pole distance from the origin is bandwidth and is also the reciprocal of settling time — the two are the same number seen twice.
DIAGRAM FOR PHASE 2
Centre: an s-plane with a single pole marked by a cross on the negative real axis at −1/RC, with a double-headed arrow from the origin to the pole labelled "1/RC". Two panels branch off. The upper-right panel…
Source: Engineering Circuit Analysis, 8th ed., Ch. 15, pp. 598-602
CO4 | Bloom L5 | visual id: pole-distance-dual-reading
Notes: What to say: Give them the idea before the formalism. Say it plainly first: A pole position on the s-plane encodes both the transient and the frequency behaviour of a circuit, and the first-order low-pass filter is the clearest de… Then add the part they are examined on - Pole distance from the origin is bandwidth and is also the reciprocal of settling time — the two are the same number seen tw… Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "s-plane geometry" constrain here, and what would break if it did not hold? Animation instructions: s-plane and pole draw, the distance arrow extends, the upper panel builds with its −3 dB marker, the lower panel builds with its rise-time marker, the connecting strip types in, then the ghosted far pole slides in and both panels visibly stretch and compress in sync. Transition style: Fade [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 4: Laplace Transformation and Applications. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 15, pp. 598-602. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 45
The complex-frequency plane and the first-order filter… - how it works
The procedure in order, and what each pass costs you.
VTU BEC303 | Module 4
The complex-frequency plane and the f…
45
1. Find the transfer function of the first-order network
2. Locate the pole at s = −1/RC
3. Read the −3 dB cutoff directly as ω_c = 1/RC rad/s
4. Convert to hertz as f_c = 1/(2πRC)
5. Read the time constant as τ = RC and the 10–90 % rise time as 2.2·τ
6. Verify that f_c × t_rise ≈ 0.35
COST AND BEHAVIOUR
Best: O(1) — one pole location gives every parameter
Typical: O(1) plus unit conversions
Worst: a dominant-pole approximation for higher-order networks
WHAT THAT MEANS
For higher-order filters the same reading applies approximately to the dominant pole.
Source: Engineering Circuit Analysis, 8th ed., Ch. 15, pp. 598-602 | CO4 | Bloom L5
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Find the transfer function of the first-order network - and check everyone has written it before moving on. At the cost panel, translate it: For higher-order filters the same reading applies approximately to the dominant pole. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 4: Laplace Transformation and Applications. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 15, pp. 598-602. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 46
The complex-frequency plane and the first-order filter… - worked example
One concrete case, carried all the way to a stated number.
VTU BEC303 | Module 4
The complex-frequency plane and the f…
46
GIVEN
An RC low-pass with R = 1 kΩ and C = 1 µF.
1. Pole at s = −1/RC = −1000 rad/s
2. Cutoff: ω_c = 1000 rad/s, so f_c = 1000/(2π) = 159.2 Hz
3. Time constant τ = 1 ms, so 10–90 % rise time = 2.2 ms
4. Check: 159.2 × 0.0022 = 0.35
RESULT
f_c = 159.2 Hz and t_rise = 2.2 ms, and their product is 0.35 exactly as the relationship predicts.
pole at −1/RC = −1000 rad/s
f_c = 1/(2πRC) = 159.2 Hz
t_rise = 2.2·RC = 2.2 ms, f_c·t_rise = 0.35 ✓
THE MISTAKE STUDENTS MAKE
Students quote the cutoff in rad/s where hertz is meant, or the reverse, producing a factor of 2π error. The pole location is naturally in rad/s; every specification in a datasheet is in hertz, and the conversion must be explicit.
Source: Engineering Circuit Analysis, 8th ed., Ch. 15, pp. 598-602 | CO4 | Bloom L5
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is An RC low-pass with R = 1 kΩ and C = 1 µF. Work at the pace of the slowest note-taker and land hard on the result: f_c = 159.2 Hz and t_rise = 2.2 ms, and their product is 0.35 exactly as the relationship predicts. Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 4: Laplace Transformation and Applications. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 15, pp. 598-602. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 47
Natural response and the s-plane
What it is, why it works, and what it costs.
VTU BEC303 | Module 4
Natural response and the s-plane
47
THE MECHANISM
The poles of a network function are its natural frequencies, and their positions on the s-plane classify the natural response completely. A pole on the negative real axis gives a pure decaying exponential whose rate is the distance from the origin. A complex conjugate pair in the left half plane gives a damped oscillation whose ringing frequency is the imaginary part and whose envelope decay is the real part; the angle from the negative real axis therefore sets the damping ratio. A pole on the jω axis gives an undamped oscillation and a pole in the right half plane gives exponential growth, so a passive network — which can never be unstable — always has its poles in the closed left half plane.
KEY TERMS
• natural frequencies
• left half plane
• stability
• jω axis poles
• damping from pole angle
TAKEAWAY
Real part sets how fast it dies, imaginary part sets how fast it rings, and anything not in the left half plane does not settle.
DIAGRAM FOR PHASE 2
A large s-plane divided into regions, each carrying a small inset time-response sketch pinned at a representative pole location. Far left on the real axis: a fast-decaying exponential. Nearer the origin on the…
Source: Engineering Circuit Analysis, 8th ed., Ch. 15, pp. 602-606
CO4 | Bloom L5 | visual id: s-plane-response-atlas
Notes: What to say: Give them the idea before the formalism. Say it plainly first: The poles of a network function are its natural frequencies, and their positions on the s-plane classify the natural response completely. Then add the part they are examined on - Real part sets how fast it dies, imaginary part sets how fast it rings, and anything not in the left half plane does not set… Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "natural frequencies" constrain here, and what would break if it did not hold? Animation instructions: axes draw, then each region's pole marker and its inset sketch appear in order from far-left to right-half-plane, with the amber and red tags landing last, then the radial damping-ratio lines sweep in. Transition style: Fade [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 4: Laplace Transformation and Applications. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 15, pp. 602-606. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 48
Natural response and the s-plane - how it works
The procedure in order, and what each pass costs you.
VTU BEC303 | Module 4
Natural response and the s-plane
48
1. Find the denominator of the network function
2. Factor it to obtain every pole
3. Plot the poles on the s-plane
4. Read the decay rate from each pole's real part
5. Read the ringing frequency from each pole's imaginary part
6. Identify the dominant pole as the one closest to the jω axis
COST AND BEHAVIOUR
Best: O(1) for a first-order network
Typical: root finding on the denominator
Worst: numerical root finding for high-order polynomials
WHAT THAT MEANS
The pole closest to the jω axis dominates the long-term response and often justifies a first-order approximation.
Source: Engineering Circuit Analysis, 8th ed., Ch. 15, pp. 602-606 | CO4 | Bloom L5
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Find the denominator of the network function - and check everyone has written it before moving on. At the cost panel, translate it: The pole closest to the jω axis dominates the long-term response and often justifies a first-order approximation. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 4: Laplace Transformation and Applications. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 15, pp. 602-606. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 49
Natural response and the s-plane - worked example
One concrete case, carried all the way to a stated number.
VTU BEC303 | Module 4
Natural response and the s-plane
49
GIVEN
A network with poles at s = −2000 and s = −100 ± j400.
1. The pole at −2000 decays with a 0.5 ms time constant — fast
2. The complex pair decays with a 10 ms time constant and rings at 400 rad/s
3. The complex pair is closest to the jω axis, so it dominates
4. Damping ratio of the pair = 100/√(100² + 400²) = 0.243
RESULT
The response is dominated by a lightly damped 400 rad/s ringing lasting about 50 ms, with the fast −2000 pole contributing only a brief initial transient.
poles: −2000, −100 ± j400
τ_fast = 0.5 ms, τ_dom = 10 ms, ω_d = 400 rad/s
ζ = α/√(α²+ω_d²) = 100/412 = 0.243
THE MISTAKE STUDENTS MAKE
Students assume the pole with the largest magnitude dominates. It is the opposite: the pole nearest the jω axis has the slowest decay and therefore persists longest, so it governs settling time.
Source: Engineering Circuit Analysis, 8th ed., Ch. 15, pp. 602-606 | CO4 | Bloom L5
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is A network with poles at s = −2000 and s = −100 ± j400. Work at the pace of the slowest note-taker and land hard on the result: The response is dominated by a lightly damped 400 rad/s ringing lasting about 50 ms, with the fast −2000 pole contributing only a… Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 4: Laplace Transformation and Applications. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 15, pp. 602-606. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 50
Network synthesis: realising a specified H(s)
What it is, why it works, and what it costs.
VTU BEC303 | Module 4
Network synthesis: realising a specif…
50
THE MECHANISM
Synthesis runs the analysis map backwards: given a desired H(s), find a network that produces it. Not every rational function is realisable with passive components — a driving-point impedance must be a positive real function, meaning it has no right-half-plane poles or zeros and a non-negative real part for Re{s} ≥ 0. For a voltage-ratio transfer function the constraints are looser but the numerator degree must not exceed the denominator degree in a passive network. The practical method for simple cases is to recognise the target as a cascade or ladder of known first-order sections and match coefficients, checking at the end that the loading between sections has been accounted for, since unbuffered sections do not simply multiply.
KEY TERMS
• synthesis
• realisability
• positive real function
• ladder realisation
• voltage ratio
TAKEAWAY
Synthesis is analysis reversed plus a realisability test — and the trap is that cascaded passive sections load each other.
DIAGRAM FOR PHASE 2
A horizontal two-lane track. The upper lane, labelled "Analysis", runs left to right from a circuit thumbnail to an H(s) expression, with a solid arrow. The lower lane, labelled "Synthesis", runs right to left…
Source: Engineering Circuit Analysis, 8th ed., Ch. 15, pp. 606-610
CO4 | Bloom L5 | visual id: synthesis-reverse-map
Notes: What to say: Give them the idea before the formalism. Say it plainly first: Synthesis runs the analysis map backwards: given a desired H(s), find a network that produces it. Then add the part they are examined on - Synthesis is analysis reversed plus a realisability test — and the trap is that cascaded passive sections load each other. Keep the key terms visible; they are the vocabulary every later slide assumes. Pause cue: Pause once the mechanism paragraph is fully revealed, before the takeaway appears. Pointing cue: Point at the mechanism panel, then at each key term in turn, then at the takeaway box. Question to ask students: Ask: in your own words, what does "synthesis" constrain here, and what would break if it did not hold? Animation instructions: the analysis lane animates left to right, then the synthesis lane animates right to left and pauses at the realisability gate which flashes, then the unbuffered cascade appears with its red warning, then the buffered version appears with its green tick. Transition style: Fade [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 4: Laplace Transformation and Applications. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 15, pp. 606-610. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 51
Network synthesis: realising a specified H(s) - how it works
The procedure in order, and what each pass costs you.
VTU BEC303 | Module 4
Network synthesis: realising a specif…
51
1. Write the target H(s) in factored form
2. Check realisability: no right-half-plane poles, numerator degree not exceeding denominator degree
3. Identify first- and second-order sections in the factorisation
4. Choose a topology for each section and match coefficients to component values
5. Account for inter-section loading, or insert buffers
6. Verify the realised H(s) by analysing the completed circuit
COST AND BEHAVIOUR
Best: O(1) for a single first-order section
Typical: one section per pole pair
Worst: iterative component adjustment when loading cannot be avoided
WHAT THAT MEANS
The verification step is not optional — loading errors are invisible until the circuit is analysed forward again.
Source: Engineering Circuit Analysis, 8th ed., Ch. 15, pp. 606-610 | CO4 | Bloom L5
Notes: What to say: Walk the procedure out loud, one line at a time, and refuse to jump ahead. Start with step one - Write the target H(s) in factored form - and check everyone has written it before moving on. At the cost panel, translate it: The verification step is not optional — loading errors are invisible until the circuit is analysed forward again. Pause cue: Pause after step three and ask for a show of hands before continuing. Pointing cue: Point at each numbered step as you read it, then move across to the cost panel on the right. Question to ask students: Ask: which of these steps would you skip first if you were short of time, and exactly what would that cost you? Animation instructions: Procedure steps reveal one at a time from the top, then the cost panel fades in on the right, then the interpretation box slides up beneath it. Transition style: Push [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 4: Laplace Transformation and Applications. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 15, pp. 606-610. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 52
Network synthesis: realising a specified H(s) - worked example
One concrete case, carried all the way to a stated number.
VTU BEC303 | Module 4
Network synthesis: realising a specif…
52
GIVEN
Realise H(s) = 1000/(s + 1000) as a passive RC network.
1. Recognise the standard first-order low-pass form 1/(1 + sRC) with 1/RC = 1000
2. Choose C = 1 µF, then R = 1/(1000 × 1e−6) = 1 kΩ
3. Realise as a series R with the output taken across C
4. Verify by forward analysis: H(s) = (1/sC)/(R + 1/sC) = 1000/(s + 1000) ✓
RESULT
R = 1 kΩ with C = 1 µF realises the target exactly, and forward analysis confirms it — but cascading a second identical section would not give H(s)² because the first section would be loaded.
target H(s) = 1000/(s+1000) ≡ 1/(1 + sRC), 1/RC = 1000
C = 1 µF ⇒ R = 1 kΩ
verify: (1/sC)/(R + 1/sC) = 1000/(s+1000) ✓
THE MISTAKE STUDENTS MAKE
Students cascade two identical RC sections expecting H(s)². The second section draws current from the first, changing its effective load, so the realised response has different pole locations and a shallower roll-off than intended.
Source: Engineering Circuit Analysis, 8th ed., Ch. 15, pp. 606-610 | CO4 | Bloom L5
Notes: What to say: Do this on the board in real time rather than reading it off the slide. The case is Realise H(s) = 1000/(s + 1000) as a passive RC network. Work at the pace of the slowest note-taker and land hard on the result: R = 1 kΩ with C = 1 µF realises the target exactly, and forward analysis confirms it — but cascading a second identical section w… Then spend a minute on the mistake box. Pause cue: Pause before revealing the result and ask the room to predict it. Pointing cue: Point at the given panel, then at each numbered step, then at the result box, then at the mistake panel. Question to ask students: Ask: if I changed one number in this case, which step would change first, and would the conclusion survive? Animation instructions: Given panel appears, then the numbered steps reveal one at a time, then the result box fades in, then the expression panel appears on the right, then the mistake panel outlines in last. Transition style: Cut [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 4: Laplace Transformation and Applications. TB1 as listed by the syllabus: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012; Ch. 15, pp. 606-610. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 53
One sentence per unit, six months from now
Units 1-7: what survives after the detail has gone.
VTU BEC303 | Module 4
Revision
53
01 The e^(−σt) kernel buys convergence, and taking the lower limit at 0− is what lets initial conditions ride into the algebra.
02 Integrating in time divides by s, and damping in time shifts s — two patterns that generate most of the table.
03 Every inverse transform in circuit work is table lookup plus bookkeeping — the bookkeeping is partial fractions.
04 The differentiation theorem is why the s-domain handles initial conditions for free — the f(0−) term is the initial condition.
05 Both theorems are free checks, but the final-value theorem lies confidently when a pole is not strictly in the left half plane.
06 Replace R, L and C by R, sL and 1/sC and every DC technique you own becomes a full transient solver.
07 Initial conditions become sources, so the s-domain circuit needs one solve where the time domain needed three.
Notes: What to say: Slow right down here. Read each takeaway aloud and then stop talking for a beat, because these are the sentences that should still be in their heads when they sit the SEE. Tell them explicitly that if they can reconstruct the reasoning behind any one of these lines they understand that unit, and if they can only recite it they do not. Pause cue: Pause for three seconds after each takeaway before moving to the next. Pointing cue: Point at each numbered takeaway in turn as you read it. Question to ask students: Ask: choose the takeaway you trust least and tell me what you would have to check to believe it. Animation instructions: Takeaway rows reveal one at a time from the top, each row highlighting briefly as it appears. Transition style: Fade [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 4: Laplace Transformation and Applications, 14 hours, Hayt 8e Ch. 14 (14.3–14.7), Ch. 15 (15.1–15.8), pp. 540–564 and 571–610; waveform and network synthesis from syllabus TB2 §6.8. TB1: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012. Revision consolidates all 16 unit takeaways. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 54
Revision, continued
Units 8-14: what survives after the detail has gone.
VTU BEC303 | Module 4
Revision
54
08 One symbolic nodal solve in s replaces the whole natural-plus-forced-plus-initial-condition assembly.
09 In the s-domain, sources at different frequencies stop being a special case — they are just different rational terms.
10 Poles are the circuit's natural frequencies and zeros are what it blocks — together they are the circuit, independent of any input.
11 Impulse, step and ramp responses are one function integrated repeatedly — compute one and the others follow by dividing by s.
12 Add a step at every jump and a ramp at every slope change, and the transform writes itself.
13 Convolution is what multiplication in s means physically — the present output is a weighted memory of past inputs.
14 Pole distance from the origin is bandwidth and is also the reciprocal of settling time — the two are the same number seen twice.
Notes: What to say: Slow right down here. Read each takeaway aloud and then stop talking for a beat, because these are the sentences that should still be in their heads when they sit the SEE. Tell them explicitly that if they can reconstruct the reasoning behind any one of these lines they understand that unit, and if they can only recite it they do not. Pause cue: Pause for three seconds after each takeaway before moving to the next. Pointing cue: Point at each numbered takeaway in turn as you read it. Question to ask students: Ask: choose the takeaway you trust least and tell me what you would have to check to believe it. Animation instructions: Takeaway rows reveal one at a time from the top, each row highlighting briefly as it appears. Transition style: Fade [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 4: Laplace Transformation and Applications, 14 hours, Hayt 8e Ch. 14 (14.3–14.7), Ch. 15 (15.1–15.8), pp. 540–564 and 571–610; waveform and network synthesis from syllabus TB2 §6.8. TB1: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012. Revision consolidates all 16 unit takeaways. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 55
Revision, continued
Units 15-16: what survives after the detail has gone.
VTU BEC303 | Module 4
Revision
55
15 Real part sets how fast it dies, imaginary part sets how fast it rings, and anything not in the left half plane does not settle.
16 Synthesis is analysis reversed plus a realisability test — and the trap is that cascaded passive sections load each other.
Notes: What to say: Slow right down here. Read each takeaway aloud and then stop talking for a beat, because these are the sentences that should still be in their heads when they sit the SEE. Tell them explicitly that if they can reconstruct the reasoning behind any one of these lines they understand that unit, and if they can only recite it they do not. Pause cue: Pause for three seconds after each takeaway before moving to the next. Pointing cue: Point at each numbered takeaway in turn as you read it. Question to ask students: Ask: choose the takeaway you trust least and tell me what you would have to check to believe it. Animation instructions: Takeaway rows reveal one at a time from the top, each row highlighting briefly as it appears. Transition style: Fade [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 4: Laplace Transformation and Applications, 14 hours, Hayt 8e Ch. 14 (14.3–14.7), Ch. 15 (15.1–15.8), pp. 540–564 and 571–610; waveform and network synthesis from syllabus TB2 §6.8. TB1: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012. Revision consolidates all 16 unit takeaways. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.

## Slide 56
How this module is assessed
Where the quiz and the assignment live, and what they test.
VTU BEC303 | Module 4
Assessment
56
MODULE 4 QUIZ
quizzes/Module_4_Quiz.pdf
quizzes/Module_4_Quiz.gift
45 minutes | 50 marks | pass 20 | 1 attempt
Part A: 20 MCQs, 1 mark each.
Part B: 13 descriptive questions, 30 marks.
Bloom spread: L1-L2 21%, L3-L4 52%, L5-L6 27%
Every question carries a CO tag, a Bloom level and a chapter reference; distractor feedback names the misconception.
MODULE 4 ASSIGNMENT
assignments/Module_4_Assignment.pdf
Assignment 4 — s-domain analysis, transfer functions and synthesis
20 marks | 10% of CIE | 10 problems + 3 theory items
Submit as PDF, single file, named <USN>_BEC303_Assignment4.pdf, via LMS upload. 10% per day, nothing after 5 days.
Rubric: Transform and inverse-transform technique (6); s-domain network modelling (5); Pole-zero interpretation (5); Synthesis and verification (4). Attainment: CO4 = 20.
Previous years' question papers for EC are indexed in pyq/PYQ_Index.pdf; the syllabus extract and the topic-to-slide mapping are in syllabus/Syllabus_Mapping.pdf.
Individual submission. Identical submissions score zero for both parties.
Notes: What to say: Close by telling them exactly where the assessment lives and what it tests. Name the two files, say the mark split out loud, and read the Bloom spread so they understand that roughly a quarter of the paper is not recall at all. Then read the integrity line word for word, because ambiguity there costs students more than any technical error in this module. Pause cue: Pause after the Bloom spread and before the integrity statement. Pointing cue: Point at the quiz panel, then the assignment panel, then the integrity line at the bottom. Question to ask students: Ask: which course outcome do you feel least ready on, and which unit would you reread tonight to fix it? Animation instructions: Quiz panel fades in from the left, then the assignment panel from the right, then the pointers strip appears, then the integrity line fades in last. Transition style: Fade [Sources] VTU BEC303 Network Analysis syllabus, 2025 scheme, Module 4: Laplace Transformation and Applications, 14 hours, Hayt 8e Ch. 14 (14.3–14.7), Ch. 15 (15.1–15.8), pp. 540–564 and 571–610; waveform and network synthesis from syllabus TB2 §6.8. TB1: W. H. Hayt, J. E. Kemmerly and S. M. Durbin, Engineering Circuit Analysis, McGraw-Hill / Tata McGraw-Hill, 8th ed., 2012. Assessment counts: 20 MCQs, 13 descriptive questions, 13 assignment items. TB1 PDF was machine-extractable, so page ranges come from the book's own table of contents.